| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, 5-8 DECEMBER 2005 |  | ET DR&/Doc. 5.1(1) ITEM: 5.1 (29.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

Proposed Observation Reporting Practices for TDCF

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The migration to BUFR/CREX necessitates the writing of a new set of regulations for reporting TAC data in BUFR or CREX. Annex to this document demonstrates an attempt to express the new reporting practices.

________________________________________________________________

ACTION PROPOSED

The team is invited to comment on the document, in particular on the suggested  approach to producing regulations for reporting TAC data in BUFR or CREX, based on a the regulations found in the Manual on Codes, Volume I.1.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] ET DR&C / Doc. 5.1(1), Kuala Lumpur, 21 – 26  June 2004

[3] Final Report, ET DR&C, Kuala Lumpur, 21 – 26  June 2004

1.  Background

The Manual on Codes, Volume I.1, contains more regulations related to reporting practices than formatting rules. The Volume I.2, on the contrary defines formatting systems, and practically no reporting regulations. The Volume I.1 links reporting practices to the alphanumeric coding format. The migration to BUFR/CREX will push producers and users (human decoders) of BUFR/CREX codes to consider Volume I.2, rather than Volume I.1. It is necessary to re-write the regulations on reporting practices connected with the traditional alphanumeric codes (TAC), and produce a new set of regulations for reporting TAC data in BUFR or CREX.

The ETDR&C meetings in 2002 and 2003 agreed on the difficulty of this task. The Team recommended this activity to be performed under the responsibility of the WMO Secretariat and Dr Cliff Dey as a consultant developed a set of regulations for observations disconnecting the reporting practices from the coding in traditional format.

At the ET DR&C meeting (Kuala Lumpur, 21 – 26 June 2004), Doc. 5.1(1) was submitted by the WMO Secretariat. This document contained a set of regulations for reporting SYNOP data according to a BUFR template; however, the system of regulation numbering of the traditional code was kept.

2. Proposal for producing regulations for reporting TAC data in TDCF

The Annex to this document contains a set of regulations for reporting SYNOP data in BUFR/CREX. The original text, prepared by Dr Dey, is written in black; the subsequent additions and modifications are written in blue and marked by side bars.

The following problems are to be solved and clarified:

2.1 System of numbering of the regulations for reporting TAC data in TDCF

The regulations in the Annex are specified by the same numbers as the corresponding regulations in SYNOP. However, the order of elements in the BUFR template for SYNOP data differs significantly from the order of elements in the traditional SYNOP. Consequently, the regulation numbers in the Annex are not increasing which would make their usage rather difficult. Therefore, it is proposed to create a new system for numbering of the regulations, e.g.

B/C1 – Regulations for reporting SYNOP data in BUFR/CREX,

B/C2 – Regulations for reporting SYNOP MOBIL data in BUFR/CREX,

B/C3 – Regulations for reporting SHIP data in BUFR/CREX, etc.

The numbers of the regulations for each type of data could be then numbered in the increasing order in compliance with a standard BUFR template recommended for the data type. For reference, the number of the corresponding TAC regulation might be included at the end of the regulation, written in italics.

2.2 Additional elements

The BUFR templates defined for TAC data contain not only the elements reported in the corresponding traditional codes, but also other important information. The regulations for reporting TAC data in BUFR/CREX should address also these additional entries (e.g. horizontal and vertical coordinates of the observation site, position of sensors and significance qualifiers, vertical significance).

2.3 Units

With each element introduced within the regulations, the unit and the required precision should be specified. If different units are used in BUFR and CREX, the unit in which the element value is reported in CREX should be also mentioned.

2.4 Reference to descriptor numbers in the regulations

Prevailing part of the text in the Annex does not refer to the sequence descriptor numbers used in the BUFR template for SYNOP data, and SYNOP symbolic letters are used only exceptionally in the text of the regulations. However, reporting clouds with bases below station level is described using BUFR sequence descriptors and SYNOP groups and symbolic letters. Explicit reference to the sequence descriptor numbers in the regulations would practically exclude the proclaimed flexibility of TDCF. On the other hand, supplementing each described element with its B-Table number might be helpful (up to now, the B-Table numbers have been added only in part of the text).

2.5 Description of entries of Section 1

The meeting is invited to consider the need of description of the entries of Section 1 within the Reporting practices or at least some of them e.g. data category and subcategory or datum/time entries in Section 1. The time of observation reported in the Data section may differ significantly from the “most typical” time in Section 1 (standard time corresponding with YYGGgg in the abbreviated telecommunication header), e.g. in case of reporting PILOT and TEMP data in TDCF.

2.6 Miscellaneous explanatory additions

# The text of the Reporting practices may require inclusion of explanary notes, e.g.

# Based on the suggestion from the JMA, the description of temperature elements has been supplemented by notes explaining why temperature data should be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree.

# Reporting practices should primarily refer to the procedures relevant for producing of the data in TDCF at the observing site. However, collecting of the data in TAC and converting them into TDCF in the centre has to be considered and the Reporting practices should adequatly cover this issue.

# ANNEX

B/C1 – Regulations for reporting SYNOP data in BUFR/CREX

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM FIXED LAND STATIONS SUITABLE FOR SYNOP OBSERVATION DATA

| 3 01 090 |  |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 004 | 0 01 001 | WMO block number II | Numeric, 0 |
|  |  | 0 01 002 | WMO station number iii | Numeric, 0 |
|  |  | 0 01 015 | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 031 | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  | 0 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  | Pressure (standard level) a3 | Pa, –1 |
|  | 0 10 009 |  | Geopotential height of the standard level hhh | gpm, 0 |
| 3 02 035 |  |  | Basic synoptic “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 033 | 0 07 032 | Height of sensor above local ground (for visibility measurement) | m, 2 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  |  |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | Cloud top description Ct | Code table, 0 |
|  |  |  | Direction of cloud drift gr. 56DLDMDH |  |
| 3 02 047 | 1 02 003 |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | Vertical significance = 7 (low cloud) = 8 (middle cloud) = 9 (high cloud) | Code table, 0 |
|  | 0 20 054 |  | True direction from which clouds are moving DL, DM, DH | Degree true, 0 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Direction and elevation of cloud gr. 57CDaeC |  |
| 3 02 048 | 0 05 021 |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  | State of ground, snow depth, ground minimum temperature |  |
| 3 02 037 | 0 20 062 |  | State of ground (with or without snow) E or E’ | Code table, 0 |
|  | 0 13 013 |  | Total snow depth sss | m, 2 |
|  | 0 12 113 |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, 2 |
| 3 02 043 |  |  | Basic synoptic “period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Sunshine data (from 1 hour and 24 hour period) |  |
|  | 1 01 002 |  | Replicate 1 descriptors 2 times |  |
|  | 3 02 039 | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 14 031 | Total sunshine SS and SSS | Minute, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 041 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 042 | 0 07 032 | Height of sensor above local ground (for wind measurement) | m, 2 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Evaporation data |  |
| 3 02 044 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 02 004 |  | Type of instrument for evaporation or crop type for evapotranspiration iE | Code table, 0 |
|  | 0 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1 |
|  |  |  | Radiation data (from 1 hour and 24 hour period) |  |
| 1 01 002 |  |  | Replicate next descriptor 2 times |  |
| 3 02 045 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified 553SS 4FFFF or 553SS 5FFFF, 55SSS 4F24F24F24F24 or 55SSS 5F24F24F24F24 | J m-2, -3 |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified 553SS 6FFFF, 55SSS 6F24F24F24F24 | J m-2, -3 |
|  | 0 14 016 |  | Net radiation, integrated over period specified 553SS 0FFFF or 553SS 1FFFF, 55SSS 0F24F24F24F24 or 55SSS 1F24F24F24F24 | J m-2, -4 |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified 553SS 2FFFF, 55SSS 2F24F24F24F24 | J m-2, -4 |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified 553SS 3FFFF, 55SSS 3F24F24F24F24 | J m-2, -4 |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified 55408 4FFFF, 55508 5F24F24F24F24 | J m-2, -4 |
| 3 02 046 |  |  | Temperature change group 54g0sndT |  |
|  | 0 04 024 |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | Time period or displacement (see Note 3) | Hour, 0 |
|  | 0 12 049 |  | Temperature change over period specified sndT | K, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)        	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)          To construct the required time range, descriptor 004024 has to be included two times.

Regulations:

B/C1.1  Section 1 of TDCF

B/C1.1.1  Entries required in Section 1 of BUFR

The following entries shall be included in BUFR Section 1:

- BUFR master table,

- identification of originating/generating centre,

- identification of originating/generating sub-centre,

- update sequence number,

- identification of inclusion of optional section,

- data category (= 000 for SYNOP data),

- international data sub-category (see Note below),

- local data subcategory,

- version number of master table,

- version number of local tables,

- year (year of the century up to BUFR edition 3),

- month (standard time),

- day (standard time = YY in the abbreviated telecom. header),

- hour (standard time = GG in the abbreviated telecom. header),

- minute (standard time = 00).

Note:

If required, the international data sub-category shall be included for SYNOP data as

= 002 at main synoptic times 00, 06, 12, 18 UTC,

= 001 at intermediate times 03, 09, 15, 21 UTC,

= 000 at observation times 01, 02, 04, 05, 07, 08, 10, 11, 13, 14, 16, 17, 19, 20, 22 and 23 UTC.

B/C1.1.2  Entries required in Section 1 of CREX

The following entries shall be included in CREX Section 1:

- CREX master table,

- CREX edition number,

- CREX table version number,

- version number of BUFR master table (1),

- version number of local tables (1),

- data category (= 000 for SYNOP data),

- international data sub-category (1), (2),

- identification of originating/generating centre (1),

- identification of originating/generating sub-centre (1),

- update sequence number (1),

- number of subsets (1),

- year ( standard time) (1),

- month (standard time) (1),

- day (standard time) (1),

- hour (standard time) (1),

- minute (standard time = 00) (1).

Notes:

- Inclusion of these entries is required starting with CREX edition 2.

- If inclusion of international data sub-category is required, Note under B/C 1.1.1 applies.

B/C1.2 Fixed station identification, time, horizontal and vertical coordinates

B/C1.2.1 Fixed station identification

WMO block number station (0 01 001) and WMO station number (0 01 002) shall be always reported.

B/C1.2.2 Time of observation

Year (0 04 001), month (0 04 002), day (0 04 003), hour (0 04 004) and minute (0 04 005) of the actual time of observation shall be reported.

Note:

If the actual time of observation differs by 10 minutes or less from the standard time reported in Section 1, the standard time may be reported instead of the actual time of observation. [12.2.6]

B/C1.2.3 Horizontal and vertical coordinates

Latitude (0 05 001) and longitude (0 06 001) of the station shall be reported in degrees with precision in 10-5 of a degree.

Height of station ground above mean sea level (0 07 030) and height of barometer above mean sea level (0 07 031) shall be reported in meters with precision in tenths of a meter.

B/C 1.3 Pressure data

B/C 1.3.1 Pressure at the station level, in tenths of a hectopascal

Pressure at the station level (0 10 004), i.e. at the level defined by 0 07 031 (height of barometer above mean sea level), shall be reported in pascals (with precision in tens of a pascal).

B/C 1.3.1.1

The station pressure shall be included in reports for global exchange from land stations, together with either the mean sea level pressure or, in accordance with Regulation B/C 1.3.5.1, with the geopotential height of a standard pressure level [12.2.4].

Note :

Inclusion of the station pressure at other times is left to the decision of individual Members.

B/C 1.3.2 Pressure at reduced to mean sea level in tenths of a hectopascal

Pressure reduced to mean sea level (0 10 051) shall be reported in pascals (with precision in tens of a pascal).

B/C 1.3.2.1

Whenever air pressure at mean sea level can be computed with reasonable

accuracy, this pressure shall be reported [12.2.3.4.1].

Notes:

- For a station situated in a region of normal synoptic network density, the pressure at mean sea level is considered not to be computed with reasonable accuracy when it introduces a deformation into the analysis of the horizontal pressure field which is purely local and recurring.

- For a station lying in a data-sparse area of the synoptic network, reasonable accuracy will be obtained when using a reduction method which has proved to be satisfactory in a region of normal network density and under similar geographic conditions.

B/C 1.3.3 Three-hour pressure change and characteristic of pressure tendency

12.2.3.5.1	Amount of pressure, either positive, zero or negative, expressed in tenths of a hectopascal in pascals (with precision in tens of a pascal) at station level, during the three hours preceding the time of observation.

Unless specified otherwise by regional decision, pressure tendency shall be included whenever the three-hourly pressure tendency is available.

12.2.3.5.2	The characteristic of pressure tendency (Code table 010063) over the past three hours shall, whenever possible, be determined on the basis of pressure samplet at equi-spaced intervals not exceeding one hour.

Note :

Algorithms for selecting the appropriate code figure are included in publication WMO–No.8, Guide to Meteorological Instruments and Methods of Observation.

12.2.3.5.3	Where it is not possible to apply the algorithms specified in Regulation 12.2.3.5.2 in reports from automatic weather stations, the characteristic of pressure tendency shall be reported as 2 when the tendency is positive, as 7 when the tendency is negative, and as 4 when the atmospheric pressure is the same as three hours before.

B/C 1.3.4  24-hour pressure change:

12.4.8		            Surface pressure change

Amount of surface pressure change during the past 24 hours,

either positive, zero  or negative,  in tenths of a hectopascal

expressed in pascals (with precision in tens of a pascal) at station level, during 24 hours preceding the time of observation.

B/C 1.3.5  Geopotential height of the standard level, in geopotential meters:

12.2.3.4.2	By regional decision, a high-level station which cannot give pressure at mean sea level to a satisfactory degree of accuracy shall report both the station-level pressure and the geopotential height of an agreed standard isobaric surface. The standard isobaric level is specified by the preceding entry, i.e. by 0 07 004 (Pressure).

Note :	The level chosen for each station is indicated in Volume A of publication WMO – No. 9.

Basic synoptic “instantaneous” data

Temperature and humidity data

Height of sensor above local ground (for temperature and humidity measurement), in meters (with precision in hundredths of a meter)

This datum represents the actual height of temperature and humidity sensors above ground at the point where the sensors are located.

Dry-bulb air temperature, in degrees Kelvin (with precision in hundredths of a degree Celsius Kelvin); if produced in CREX, in degrees Celsius (with precision in hundredths of a degree Celsius)

Note:

Temperature data shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values.

12.2.3.2	When data are not available as a result of a temporary instrument failure, automatic weather stations programmed to transmit this quantity shall include it in their reports as a missing value  this quality shall be included as a missing value.

Dew-point temperature, in degrees Kelvin (with precision in hundredths of a degree Celsius Kelvin); if produced in CREX, in degrees Celsius (with precision in hundredths of a degree Celsius)

Note:

Dew-point temperature data shall be reported with precision in hundredths of a degree even if they are available with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values.

        - When data is not available as a result of a temporary instrument failure, automatic weather stations programmed to transmit this quantity shall include it in their reports as a missing value  this quality shall be included as a missing value.

Relative humidity, in units of a percent

Both dew point and relative humidity shall be transmitted when available.

Visibility data

Height of sensor above local ground (for visibility measurement), in meters (with precision in hundredths of a meter)

If reported this datum represents the actual height of visibility sensor above ground at the point where the sensor is located. If visibility is estimated by a human observer, average height of observer’s eyes above ground shall be reported.

Horizontal visibility at surface in meters (with precision in tens of meters)

12.2.1.3.1		When the horizontal visibility is not the same in different directions, the shortest distance shall be given for visibility.

Precipitation past 24 hours

Height of sensor above local ground (for precipitation measurement), in meters (with precision in hundredths of a meter)

This datum represents the actual height of the rain gauge rim above ground at the point where the rain gauge is located.

Total amount of precipitation during the 24-hour period ending at the time of observation in kilograms per square meter (with precision in tenths of a kilogram per square meter).

12.4.1	Total amount of precipitation during the 24-hour period ending at the time of observation.  The precipitation over the past 24 hours shall be included (not missing) at least once a day at one appropriate time of the main standard times (0000, 0600, 1200, 1800 UTC).

12.2.5.4	Precipitation, when it can be and has to be reported, shall be reported as 0.0 kgm-2 coded 0 even  if no precipitation were observed during the referenced period. Trace shall be reported as - 0.1 kgm-2

.

Cloud data

Total cloud cover, in units of a percent:

Total cloud cover shall embrace the total fraction of the celestial dome covered by clouds irrespective of their genus.

12.2.2.2.1	Total cloud cover shall be reported as actually seen by the observer during the observation.

12.2.2.2.2	Altocumulus perlucidus or Stratocumulus perlucidus (“mackerel sky”) shall be reported using 90%  as 99% or less  (unless overlying clouds appear to cover the whole sky) since breaks are always present in this cloud form even if it extends over the whole celestial dome.

12.2.2.2.3	Total cloud cover shall be reported as zero when blue sky or stars are seen through existing fog or other analogous phenomena without any trace of cloud being seen.

12.2.2.2.4	When clouds are observed through fog or analogous phenomena, their amount shall be evaluated and reported as if these phenomena were non-existent.

12.2.2.2.5	Total cloud cover shall not include the amount resulting from rapidly dissipating condensation trails.

12.2.2.2.6	Persistent condensation trails and cloud masses which have obviously developed from condensation trails shall be reported as cloud, using the appropriate code figure.

Vertical significance – Code table 008002

To be written

Cloud amount of low or middle clouds (Nh) – Code table 020011

Amount of all the low clouds (clouds of the genera Stratocumulus, Stratus, Cumulus, and Cumulonimbus) present or, if no low clouds are present, the amount of all the middle clouds (clouds of the genera Altocumulus, Altostratus, and Nimbostratus) present.

12.2.7.2.1	(a)	If there are low clouds then the total amount of all low clouds, as actually seen by the observer during the observation shall be reported for the cloud amount.

(b)	If there are no low clouds but there are middle clouds, then the total amount of the middle clouds shall be reported for the cloud amount.

(c)	If there are no low clouds and there are no middle clouds but there are high clouds (clouds of the genera Cirrus, Cirrocumulus, and Cirrostratus), then the cloud amount shall be reported as zero.

12.2.7.2.2	Altocumulus perlucidus or Stratocumulus perlucidus (“mackerel sky”) shall be reported using 90%  code figure 7or less since breaks are always present in this cloud form even if it extends over the whole celestial dome.

12.2.7.2.3	When the clouds reported for cloud amount are observed through fog or an analogous phenomenon, the cloud amount shall be reported as if these phenomena were not present.

12.2.7.2.4	If the clouds reported for cloud amount include contrails, then the cloud amount shall include the amount of persistent contrails.  Rapidly dissipating contrails shall not be included in the value for the cloud amount.

Height of base of lowest cloud in meters (with precision in tens of a meter)

Height above surface of the base of the lowest cloud seen.

12.2.1.2	When the station is in fog, a sandstorm or in blowing snow but the sky is discernable, the base of the lowest cloud shall refer to the base of the lowest cloud observed, if any.  When, under the above conditions, the sky is not discernible, the base of the lowest cloud shall be reported as missing. When no cloud are reported (Total cloud cover  = 0) the value shall be reported as “missing”.

Note 1:	The term « height above surface »  shall be considered as being the height above the official aerodrome elevation or above station elevation at a non-aerodrome station.

Cloud type of low, middle and high clouds

12.2.7.3	The reporting of type of low, middle and high clouds (CL, CM, and CH clouds) shall be as specified in publication WMO-NO. 407 – International Cloud Atlas, Volume I.

Individual cloud layers or masses

Vertical significance – Code table 008002

To be written

Cloud amount, type and height of base (Ns, genus C, and height hshs)

12.4.10.1	Amount of individual cloud layer or mass, genus of cloud layer or mass, and height of base of individual cloud layer or mass.  The number of individual cloud layers or masses shall in the absence of Cumulonimbus clouds not exceed three.  Cumulonimbus clouds, when observed, shall always be reported, so that the total number of individual cloud layers or masses can be four.  The selection of layers (or masses) to be reported shall be made in accordance with the following criteria :

(a)	The lowest individual layer (or mass) of any amount (cloud amount at least one octa or less, but not zero) ;

(b)	The next higher individual layer (or mass) the amount of which is greater than two octas;

(c)	The next higher individual layer (or mass) the amount of which is greater than four octas;

(d)	Cumulonimbus clouds, whenever observed and not reported under (a), (b) and (c) above.

12.4.10.2	The order of reporting the individual cloud layers or masses shall always be from lower to higher levels.

12.4.10.3		In determining cloud amounts to be reported for individual layers or masses, the observer shall estimate, by taking into consideration the evolution of the sky, the cloud amounts of each individual layer or mass at the different levels, as if no

other clouds existed.

12.4.10.4		When the sky is clear, cloud amount, genus, and height shall

not be reported.

12.4.10.5	If, notwithstanding the existence of fog, sandstorm, duststorm, blowing snow or other obscuring phenomena, the sky is discernible, the partially obscuring phenomena shall be disregarded.  If, under the above conditions, the sky is not discernible, the cloud genus shall be reported as missing and the cloud height shall be replaced by vertical visibility.

Note:  The vertical visibility is defined as the vertical visual range into an obscuring medium.

12.4.10.6	Cloud heights are the « height above surface ».  This shall be considered as being the height above the official aerodrome elevation or above station level at a non-aerodrome station.

If two or more types of cloud occur with their bases at the same level and this level is one to be reported in accordance with Regulation 12.4.10.1, the selection for cloud genus and amount shall be made with the following criteria :

(a)	If these types do not include Cumulonimbus then cloud genus shall refer to the cloud type that represents the greatest amount, or if there are two or more types of cloud all having the same amount, the highest applicable code figure for cloud genus shall be reported.  Cloud amount shall refer to the total amount of cloud whose bases are all at the same level ;

(b)	If these types do include Cumulonimbus then one group shall be used to describe only this type with cloud genus reported as Cumulominbus and the cloud amount as the amount of the Cumulonimbus.  If the total amount of the remaining type(s) of cloud (excluding Cumulonimbus) whose bases are all at the same level is greater than that required by Regulation 12.4.10.1, then another group shall be reported with genus being selected in accordance with (a)  and amount referring to the total amount of the remaining cloud (excluding Cumulonimbus).

12.4.10.7		Regulations 12.2.2.2.3 to 12.2.2.2.6, inclusive shall apply.

Clouds with bases below station level

This part is not consistent with the system used in the rest of the text:

Reporting of clouds with bases below station level is described using a mixture of BUFR sequence descriptors and SYNOP groups and symbolic letters.

Inclusion of these data shall be determined by national decision.

12.5.2	Clouds with tops below station level shall be reported only by these descriptors sequence 3 02 036, and any co-existent clouds with bases above station level shall be reported in Sequences 3 02 004 and 3 02 005.

12.5.3	Low clouds with bases below and tops above station level shall be reported in both Sequences 3 02 004, 3 02 005 and 3 02 036, provided that the station is out of cloud sufficiently frequently to enable the various features to be recognized.  In this case :

- Nh  shall correspond with N’  and CL with C’ while h shall be coded as missing or having a negative value if the base of cloud is observed;

- If the upper surface of clouds with tops above station level can be observed, it shall be reported with H’H’;

(c)	Other low clouds present with tops below station level shall be reported in a second N’C’H’H’Ct  cloud group;

12.5.3.1	Each cloud group reported in Sequence 3 02 036 shall have the following parameters:

(a)     Vertical significance

(b)	Amount of cloud whose base is below the level of the station;

(c)	Genus of cloud whose base is below the level of the station;

(d)	Altitude of the upper surface of clouds below the level of the station;

(e)	Description of the top of cloud whose base is below the

level of the station.

12.5.4		If the station is in almost continuous cloud, Sequence 3 02 036 shall be omitted all parameters shall be reported as missing.

12.5.5		When two or more cloud layers with their bases below station level occur at different levels, two or more cloud groups shall be reported in Sequence 3 02 036.

12.5.6		Rapidly dissipating condensation trails shall not be reported in Sequence 3 02 036.

12.5.7	However, the top of persistent condensation trails and cloud masses which have obviously developed from condensation trails shall be reported in Sequence 3 02 036.

12.5.8	Regulations 12.2.2.2.1 to 12.2.2.2.6, inclusive shall apply.

12.5.9	Spaces occupied by mountains emerging from the cloud layers shall be counted as occupied by clouds

Direction of cloud drift

12.4.7.5                      True direction, in degrees, from which the low, middle, or high

clouds are moving.

Note :		This information is required from land stations

mainly in the tropics.

Direction and elevation of cloud

      - True direction, in degrees, from which orographic clouds or

clouds with vertical development are seen, and elevation angle, in degrees, of the top of the cloud with specified genus (Code table 0 20 012).

Note :		This information is required from land stations

mainly in the tropics.

State of ground, snow depth, ground minimum temperature

State of ground (with or without snow), Code table 0 20 062.

Total snow depth, in meters (with precision in hundredths of a meter).

When total snow depth has to be reported, it is reported as 0.00 m if no snow, ice and other forms of solid precipitation on the ground are observed at the time of observation.  A snow depth of - 0.01 m shall indicate a little (less than 0.005 m) snow. A snow depth of – 0.02 shall indicate “snow cover not continuous).

12.4.6.1	The measurement shall include snow, ice and all other forms of solid precipitation on the ground at the time of observation.

12.4.6.2		When the depth is not uniform, the average depth over a representative area shall be reported.

Ground minimum temperature, in degrees Kelvin (with precision in hundredths of a degree Kelvin); if produced in CREX, in degrees Celsius (with precision in hundredths of a degree Celsius)

The period of time covered by ground minimum temperature and the synoptic hour at which this temperature is reported shall be determined by regional decision.

Note:

Ground minimum temperature data shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values.

Basic synoptic “period” data

Present and past weather

12.2.6.1	Present weather (Code table 0 20 003) and past weather (Code tables 0 20 004 and 0 20 005) shall be included in an observation by a manually operated station after a period of closure or at start up, when past weather conditions for the period applicable to the report are unknown.   Otherwise, it shall only be included if present or past weather phenomena of significance, or both, were observed. Present weather reported as missing shall indicate that present conditions are unknown. Past weather reported as missing shall indicate that previous conditions are unknown. This regulation shall also apply to automatic reporting stations with the facility to report present and past weather.

      - Code figures 0, 1, 2, 3 and 100 for present weather and code figures 0, 1, 2 and 10 for past weather shall be considered to represent phenomena without significance.

12.2.6.3	Present and past weather shall be reported if available (observation made), regardless of their significance.  omitted if both present and past weather were:

- Not available (no observation made); or

- An observation was made but observed phenomena were not of significance

If data are produced and collected in TAC and present weather and past weather is omitted (no significant phenomenon to report), code figure 508 shall be used for present weather in BUFR or CREX.

Present weather from a manned weather station:

12.2.6.4.1	If more than one form of weather is observed, the highest applicable code figure from the range <00 to 99> shall be selected for present weather. Other weather may be reported and repeated as necessary. Code figure 17 shall have precedence over code figures 20 – 49. Other weather may be reported using additional entries 0 20 021 to 0 20 026.

12.2.6.4.2	In coding 01, 02, or 03, there is no limitation on the magnitude of the change of the cloud amount.  Code figures 00, 01, and 02 can each be used when the sky is clear at the time of observation.  In this case, the following interpretation of the specifications shall apply:

- 00 is used when the preceding conditions are not known

- 01 is used when the clouds have dissolved during the past hour

- 02 is used when the sky has been continuously clear during the past hour

12.2.6.4.3	When the phenomena is not predominantly water droplets, the appropriate code figure shall be selected without regard to visibility,

12.2.6.4.4	The code figure 05 shall be used when the obstruction to vision consists predominantly of lithometeors.

12.2.6.4.5	National instructions shall be used to indicate the specifications for code figures 07 and 09.

12.2.6.4.6	The visibility restrictions on code figure 10 shall be 1000 metres or more.  The specification refers only to water droplets and ice crystals.

12.2.6.4.7	For code figures 11 or 12 to be reported, the apparent visibility shall be less than 1000 metres.

12.2.6.4.8	For code figure 18, the following criteria for reporting squalls shall be used :

- When wind speed is measured : A sudden increase of wind speed of at least eight metres per second (16 knots), the speed rising to 11 metre per second (22 knots) or more and lasting for at lest one minute ;

- When the Beaufort scale is used for estimating wind speed : A sudden increase of wind speed by at least three stages of the Beaufort scale, the speed rising to force 6 or more and lasting for at least one minute.

12.2.6.4.9	Code figures 20 – 29 shall never be used when precipitation is observed at the time of observation.

12.2.6.4.10	For code figure 28, visibility shall have been less than 1000 metres.

Note :	The specification refers only to visibility restrictions which occurred as a result of water droplets or ice crystals.

12.2.6.4.11	For synoptic coding purposes, a thunderstorm shall be regarded as being at the station from the time thunder is first heard, whether or not lightning is seen or precipitation is occurring at the station.  A thunderstorm shall be reported if thunder is heard within the normal observational period preceding the time of the report.  A thunderstorm shall  be regarded as having ceased at the time thunder is lst heard and the cessation is confirmed if thunder is not heard for 10 – 15 minutes after this time.

        - The necessary uniformity in reporting code figures 36, 37, 38, and 39 which may be desirable within certain regions shall be obtained by means of national instructions.

        - A visibility restriction « less than 1000 metres » shall be applied to code figures 42 – 49.  In the case of code figures 40 or 41, the apparent visibility in the fog or ice fog patch or bank shall be less than 1000 metres.  Code figures 40 – 47 shall be used when the obstructions to vision consist predominantly of water droplets or ice crystals, and 48 or 49 when the obstructions consist predominantly of water droplets.

        - When referring to precipitation, the phrase « at the station » in the code table shall mean « at the point where the observation is normally taken ».

        - The precipitation shall be encoded as intermittent if it has been discontinuous during the preceding hour, without presenting the character of a shower.

        - The intensity of precipitation shall be determined by the intensity at the time of the observation.

        - Code figures 80 – 89 shall be used only when the precipitation is of the shower type and takes place at the time of the observation.

Note :	Showers are produced by convective clouds.  They are characterized by their abrupt beginning and end and by the generally rapid and sometimes great variations in the intensity of the precipitation.  Drops and solid particles falling in a shower are generally larger than those falling in non-showery precipitation.  Between showers openings may be observed unless stratiform clouds fill the intervals between the cumuliform clouds.

        - In reporting code figure 98, the observer shall be allowed considerable latitude in determining whether precipitation is or is not occurring, if it is not actually visible.

Present weather from an automatic weather station:

        - The highest applicable code figure shall be selected.

        - In coding code figures 101, 102, and 103, there is no limitation on the magnitude of the change of the cloud amount.  Code figures 100, 101, and 102 can each be used when the sky is clear at the time of observation.  In this case, the following interpretation of the specifications shall apply:

- Code figure 100 is used when the preceding conditions are not known ;

- Code figure 101 is used when the clouds have dissolved during the past hour ;

- Code figure 102 is used when the sky has been continuously clear during the past hour.

        - When the phenomenon is not predominantly water droplets, the appropriate code figure shall be selected without regard to the visibility.

        - The code figures 104 and 105 shall be used when the obstruction to vision consists predominantly of lithometeors.

        - The visibility restriction on code figure 110 shall be 1000 metres or more.  The specification refers only to water droplets and ice crystals.

        - For code figure 118, the following criteria for reporting squalls shall be used :

A sudden increase of wind speed of at least eight metres per second (16 knots), the speed rising to 11 metres per second (22 knots) or more and lasting for at least one minute.

        - Code figures 120 – 126 shall never be used when precipitation is observed at the time of observation.

        - For code figure 120, visibility shall have been less than 1000 metres.

Note :	The specification refers only to visibility restrictions which occurred as a result of water droplets or ice crystals.

        - For synoptic coding purposes, a thunderstorm shall be regarded as being at the station from the time thunder is first detected, whether or not lightning is detected or precipitation is occurring at the station.  A thunderstorm shall be reported in present weather if thunder is detected within the normal observational period preceding the time of the report.  A thunderstorm shall be regarded as having ceased at the time thunder is last detected and the cessation is confirmed if thunder is not detected for 10 – 15 minutes after this time.

        - A visibility restriction « less than 1000 metres » shall be applied to code figures 130 – 135.

        - The precipitation shall be encoded as intermittent if it has been discontinuous during the preceding hour, without presenting the character of a shower.

        - The intensity of predipitation shall be determined by the intensity at the time of observation.

        - Code figures 180 – 189  shall be used only when the precipitation is intermittent or of the shower type and takes place at the time of observation.

Note :	Showers are produced by convective clouds.  They are characterized by their abrupt beginning and end and by the generally rapid and sometimes great variations in the intensity of the precipitaiton.  Drops and solid particles falling in a shower are generally larger than those falling in non-showery precipitaiton.  Between showers openings may be observed ujnless stratiform couds fill the intervals between the cumuliform clouds.

Past weather reported from a manned weather station:

        - The period (in hours) covered by past weather (1) and past weather (2) shall be:

- Six hours for observations at 0000, 0600, 1200, and 1800 UTC;

- Three hours for observations at 0300, 0900, 1500, and 2100 UTC;

- Two hours for intermediate observations if taken every two hours.

- One hour for intermediate observations if taken every hour.

12.2.6.6.2	The code figures for past weather (1) and past weather (2) shall be selected in such a way that past and present weather together give as complete a description as possible of the weather in the time interval concerned.  For example, if the type of weather undergoes a complete change during the time interval concerned, the code figures selected for past weather (1) and past weather (2) shall describe the weather prevailing before the type of weather indicated by present weather began.

12.2.6.6.3	When the past weather (1) and past weather (2) are used in hourly reports other than those covered by Regulation 12.2.12.6.1 (a) and (b), they cover a short period of time and Regulation 12.2.12.6.2 shall apply.

        - If, using Regulation 12.2.12.6.2, more than one code figure may be given to past weather (1), the highest figure shall be reported for past weather (1) and the second highest code figure shall be reported for past weather (2).

        - If the weather during the period has not changed so that only one code figure may be selected for past weather, then that code figure shall be reported for both past weather (1) and past weather (2).

Past weather from an automatic weather station:

        - The period (in hours) covered by past weather (1) and past weather (2) shall be:

- Six hours for observations at 0000, 0600, 1200, and 1800 UTC;

- Three hours for observations at 0300, 0900, 1500, and 2100 UTC;

- Two hours for intermediate observations if taken every two hours.

- One hour for intermediate observations if taken every hour.

        - The code figures for past weather (1) and past weather (2) shall be selected so that the maximum capability of the automatic station to discern past weather is utilized, and so that past and present weather together give as complete a description as possible of the weather in the time interval concerned.

        - In cases where the automatic station is capable only of discerning very basic weather conditions, the lower code figures representing basic and generic phenomena may be used.  If the automatic station has higher discrimination capabilities, the higher code figures representing more detailed explanation of the phenomena shall be used.  For each basic type of phenomenon, the highest code figure within the discrimination capability of the automatic station shall be reported.

        - If the type of weather during the time interval concerned undergoes complete and discernible changes, the code figures selected for past weather (1) and past weather (2) shall describe the weather prevailing before the type of weather indicated by present weather began.  The highest figure shall be reported for past weather (1) and the second highest code figure shall be reported for past weather (2).

        - If a discernible change in weather has not occurred during the period, so that only one code figure may be selected for the past weather, then that code figure shall be reported for both past weather (1) and past weather (2).  For example, rain during the entire period shall be reported as code figure 14 for both past weather (1) and past weather (2) in the case of an automatic station incapable of differentiating types of precipitation, or code figure 16 for both past weather (1) and past weather (2) in the case of a station with the higher discrimination capability.

Sunshine data

Period of reference for sunshine duration (in hours).

Duration of sunshine over the previous hour and over the previous 24 hours may be reported.

Duration of sunshine (in minutes).

The duration of sunshine over the previous hour shall be reported by national decision.

12.4.7.4.2	The duration of sunshine over the previous 24 hours shall, by regional decision, be reported at all stations capable of doing so and included at either 0000 UTC, 0600 UTC, 1200 UTC or 1800 UTC.  When the duration of sunshine is reported, it is accompanied by the absolute value of the amount of solar or terrestrial radiation, as appropriate, in joules per square centimetre over the previous 24 hours at either 0000 UTC, 0600 UTC, 1200 UTC, or 1800 UTC.

#### Precipitation measurement

Height of sensor above local ground (for precipitation measurement), in meters (with precision in hundredths of a meter)

This datum represents the actual height of the rain gauge rim above ground at the point where the rain gauge is located.

Period of reference for amount of precipitation, ending at the time of observation (in hours) shall be determined by regional decision.

Amount of precipitation which has fallen during the period of reference, and duration of period of reference for amount of precipitation, ending at the time of the report.

Total amount of precipitation, in kilograms per square meter (with precision in tenths of a kilograms per square meter) which has fallen during the period of reference for amount of precipitation.

      - Precipitation, when it can be and has to be reported, shall be  coded 0

reported as 0.0 kgm-2 even if no precipitation were observed during

the referenced  period. Trace shall be reported as  - 0.1 kgm-2.

Extreme temperature data

Height of sensor above local ground (for temperature measurement), in meters (with precision in hundredths of a meter)

This datum represents the actual height of temperature sensor(s) above ground at the point where the sensors are located.

Period of reference for extreme temperatures (in hours) shall be determined by regional decision.

12.4.4	Maximum and minimum temperature, in tenths of a degree Celsius in degrees Kelvin (with precision in hundredths of a degree Kelvin); if produced in CREX, in degrees Celsius (with precision in hundredths of a degree Celsius).  The period of time covered by the maximum and minimum temperature and the synoptic hour at which these temperatures are reported shall be determined by regional decision.

Note:

Extreme temperature data shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values.

### Wind data

Height of sensor above local ground (for wind measurement), in meters (with precision in hundredths of a meter)

This datum represents the actual height of the sensor above ground at the point where the sensor is located.

12.2.2.3.1	Wind direction is the true direction, in tens of degrees, from which the wind is blowing (or will blow) and wind speed, in either metres per second (with precision in tenths of meters per second) or knots.  The mean direction and speed of the wind over the 10-minute period immediately preceding the observation shall be reported.  However, when the 10-minute period includes a discontinuity in the wind characteristics, only data obtained after the discontinuity shall be used for reporting the mean values, and hence the period in these circumstances shall be correspondingly reduced.

12.2.2.3.2	In the absence of wind instruments, the wind speed shall be estimated on the basis of the Beaufort wind scale.  The Beaufort number obtained by estimation is converted into metres per second by use of the wind speed equivalent columns on the Beaufort scale, and this speed is reported for wind speed.

Period of reference for wind gust direction and speed (in hours) shall be determined by regional or national decision.

If it is reported, maximum wind gust direction in degrees true and maximum wind gust speed in metres per second (with precision in tenths of meters per second).

###### Evaporation data

12.4.7.2.2	Amount of either evaporation or evapotranspiration, in kilograms per square meter (with precision in tenths of a kilogram per square meter), during the preceding 24 hours, and indicator of type of instrument for evaporation measurement or the type of crops, at either 0000 UTC, 0600 UTC, or 1200 UTC.

###### Radiation data

Period of reference for radiation data (in hours).

Radiation over the previous hour and over the previous 24 hours may be reported.

Amount of radiation, in joules per square metre (with precision in thousandths of a joule per square metre for radiation type (1) and (2); with precision in ten-thousandths of a joule per square metre for radiation types (3) to (6)).

12.4.7.4.3 	The radiation data may take one or more of the following forms:

(1)	Long-wave radiation (using the proper sign to specify

downward or upward long-wave radiation);

(2)	Short-wave radiation;

(3)	Net radiation (using the proper sign to specify positive

or negative net radiation);

(4)	Global solar radiation;

(5)	Diffuse solar radiation;

(6)	Direct solar radiation.

The above regulation covers SYNOP regulation 12.4.7.4.3 as well as 12.4.7.4.4.

###### Temperature change

Period of reference for temperature change (in hours)

12.4.4.1		The temperature change data during the period covered by

past weather(1) and past weather(2). The temperature change

(see Code table 0822) is for the period of time, in hours,

between the time of the observation and the time of the

occurrence of temperature change. To construct the required

period, time period or displacement has to be included twice;

the first one corresponding to period covered by past weather

(1) and past weather (2), the second one specified by the time

of the occurrence of temperature change.

Note :

The period is the number of whole hours, disregarding the minutes.  For example, if the time of occurrence is 45 minutes after the time of the observation, the time period is considered to be zero hours.  If the time of occurrence is 1 hour or more, but less than 2 hours after the observation, the time period go shall be considered to be 1 hour, etc.

Temperature change in degrees (Kelvin or Celsius)

12.4.7.2		For a change of temperature to  be reported, the change shall

be equal to or more than 5o C and occur in less than 30

minutes during the period covered by past weather (1) and

past weather (2).

Note :

The reporting of this information is restricted by regional or national decision to islands or other widely separated stations.