| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, 5-8 DECEMBER 2005 |  | CT MTDCF/Doc. 5.4(1)REV1 ITEM: 5.4 (22.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

Review of templates for Traditional Alphanumeric Codes (TAC) in TDCF

and proposal for new Common Sequences

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains templates recommended

for representation of TAC data in BUFR or CREX

and proposed sequence descriptors.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to review and discuss the content of the document.

References:

[1] BUFR/CREX Templates to Transmit in Table Driven Code Forms, WMO, March 2005.

[2] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[3] Final Report, ET DR&C, Prague, 22-26 April 2002

[4] Final Report, ET DR&C, Kuala Lumpur, 21 – 26  June 2004.

[5] Aircraft Meteorological Data Relay (AMDAR), Reference Manual, WMO-No. 958, 2003.

[6] Draft Final Report, CT MTDCF, Geneva, 1 - 4 November 2005.

Introduction

This document contains templates for representation of TAC data in BUFR or CREX, i.e. not all templates shown in [1] are included here. Strictly speaking, the templates presented below are BUFR templates; if used for CREX, relevant modifications have to be introduced.

- BUFR/CREX templates for common code data

BUFR/CREX templates for:

  - Synoptic reports from fixed land stations suitable for SYNOP observation data..........................page 4

  - Synoptic reports from mobile land stations suitable for SYNOP MOBIL observation data..........page 7

  - Wind vertical profiles suitable for PILOT, PILOT SHIP and PILOT MOBIL observation data

(with pressure as the vertical coordinate)	page 8

  - Wind vertical profiles suitable for PILOT, PILOT SHIP and PILOT MOBIL observation data

(with height as the vertical coordinate)...	... page 10

  - P, T, U and wind vertical profiles suitable for TEMP, TEMP SHIP and TEMP MOBIL

observation data.........................................................................................................................page 11

  - P, T, U and wind vertical profiles from drop soundings suitable for TEMP DROP observation

data............................................................................................................................................page 13

  - CLIMAT data..............................................................................................................................page 14

  - CLIMAT TEMP and CLIMAT TEMP SHIP data..........................................................................page 19

- BUFR/CREX templates for maritime code data

BUFR/CREX templates for:

  - Synoptic reports from sea stations suitable for SHIP observation data.....................................page 20

  - Synoptic reports from sea stations suitable for SHIP observation data from VOS stations......page 23

  - Wind vertical profiles suitable for PILOT SHIP observation data (with pressure as the vertical

coordinate)	page 26

  - Wind vertical profiles suitable for PILOT SHIP observation data (with height as the vertical coordinate)	 page 26

  - P, T, U and wind vertical profiles suitable for TEMP SHIP observation data.............................page 26

  - CLIMAT SHIP data... ................................................................................................................page 27

  - CLIMAT TEMP SHIP data.........................................................................................................page 28

  - BUOY, TESAC and BATHY data..............................................................................................page 29

- BUOY

- Sub-surface profiling floats

- XBT/XCTD

  - TRACKOB data.........................................................................................................................page 33

- BUFR/CREX templates for aviation code data

BUFR/CREX templates for:

3.1 METAR/SPECI data...................................................................................................................page 34

3.2 TAF (not yet included)................................................................................................................page 36

3.3 Single level AMDAR data........................................................................................................... page 37

- Standard AMDAR reports

- Single level AMDAR data

- Single level AMDAR data (a more complex template)

3.4 Aircraft ascent/descent profile suitable for AMDAR profile data	page 39

- BUFR/CREX templates for satellite observations

BUFR/CREX templates for:

4.1 SAREP data (Part A: Information on tropical cyclone).............................................................. page 40

- BUFR/CREX templates for miscellaneous codes

BUFR/CREX templates for:

5.1 RADOB data (Part A: Information on tropical cyclone).............................................................. page 41

BUFR templates presented in this document should provide facilities for representation of data reported in the Traditional Alphanumeric Codes described in the international part of Manual on Codes, WMO-No. 306, Volume I.1. Successful migration to Table Driven Code Forms will require also the coverage of regional and national reporting practices that are published in Manual on Codes, WMO-No. 306, Volume II. If required, the global template for the particular data types may be supplemented by relevant additions, reflecting the reporting regional or national practices as discussed in ET DR&C/Doc. 5.2(1) and ET DR&C/Doc. 5.3(1), respectively.

BUFR templates for vertical profile data and templates for aircraft ascent/descent profile data have already regulatory status as so-called "common sequence numbers" was approved by CBS. For most of the other templates, following their validation, sequence descriptors for BUFR Table D are proposed in this document (see throughout the text of the document and in the Annex).

The first version of this document was submitted to the first meeting of CT on Migration to TDCF, held in Geneva from 1 to 4 November 2005, as CT MTDCF/Doc. 5.1(1). Besides some editorial changes in the text, a BUFR template for SAREP data (Part A: Information on tropical cyclone), developed and validated by JMA, has been added following the meeting. Another substantial modification has been done in paragraph 1.3 (Wind vertical profiles suitable for PILOT, PILOT SHIP and PILOT MOBIL observation data with pressure as the vertical coordinate). As noted by Mr. W. Qu (Australia), reporting maximum wind data with height as the vertical coordinate, while the complete vertical wind profile is reported with pressure as the vertical coordinate, would require producing two bulletins: one for the complete vertical wind profile using common sequence 3 09 050 and the other for maximum wind data using 3 09 051. To avoid this undesirable procedure, the meeting of CT MTDCF recommended to represent the maximum wind data by a relevant addition to the original template [6]. The ET DR&C meeting is invited to discuss the approach suggested in Notes (4a)  and (4b) in paragraph 1.3 and to provide relevant recommendation.

1.   BUFR/CREX templates for common code data

  - BUFR template for synoptic reports from fixed land stations suitable for SYNOP

observation data

During the recent validation process a typo has been corrected within 3 02 043 (Basic synoptic “period” data) as marked below. Sequence descriptor numbers written in blue in this template, have not yet been included in Manual on Codes, WMO-No. 306, I.2 (November 2005).

It is proposed to represent this template by a single descriptor 3 07 080.

3 07 080:

| 3 01 090 |  |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 004 | 0 01 001 | WMO block number II | Numeric, 0 |
|  |  | 0 01 002 | WMO station number iii | Numeric, 0 |
|  |  | 0 01 015 | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 031 |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  | 0 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  | Pressure (standard level) a3 | Pa, –1 |
|  | 0 10 009 |  | Geopotential height of the standard level hhh | gpm, 0 |
| 3 02 035 |  |  | Basic synoptic “instantaneous” data |  |
|  | 3 02 032 |  | Temperature and humidity data |  |
|  |  | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  | 3 02 033 |  | Visibility data |  |
|  |  | 0 07 032 | Height of sensor above local ground (for visibility measurement) | m, 2 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 3 02 034 |  | Precipitation past 24 hours |  |
|  |  | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
| 3 02 036 |  |  | Clouds with bases below station level |  |
|  | 1 05 000 |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | Cloud top description Ct | Code table, 0 |
| 3 02 047 |  |  | Direction of cloud drift gr. 56DLDMDH |  |
|  | 1 02 003 |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | Vertical significance = 7 (low cloud) = 8 (middle cloud) = 9 (high cloud) | Code table, 0 |
|  | 0 20 054 |  | True direction from which clouds are moving DL, DM, DH | Degree true, 0 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
| 3 02 048 |  |  | Direction and elevation of cloud gr. 57CDaeC |  |
|  | 0 05 021 |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
| 3 02 037 |  |  | State of ground, snow depth, ground minimum temperature |  |
|  | 0 20 062 |  | State of ground (with or without snow) E or E’ | Code table, 0 |
|  | 0 13 013 |  | Total snow depth sss | m, 2 |
|  | 0 12 113 |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, 2 |
| 3 02 043 |  |  | Basic synoptic “period” data |  |
|  | 3 02 038 |  | Present and past weather |  |
|  |  | 0 20 003 | Present weather ww or wawa | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 or Wa1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 or Wa2 | Code table, 0 |
|  |  |  | Sunshine data (from 1 hour and 24 hour period) |  |
|  | 1 01 002 |  | Replicate 1 descriptor 2 times |  |
|  | 3 02 039 | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 14 031 | Total sunshine SS and SSS | Minute, 0 |
|  | 3 02 040 |  | Precipitation measurement |  |
|  |  | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  | 3 02 041 |  | Extreme temperature data |  |
|  |  | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  | 3 02 042 |  | Wind data |  |
|  |  | 0 07 032 | Height of sensor above local ground (for wind measurement) | m, 2 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 3 02 044 |  |  | Evaporation data |  |
|  | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 02 004 |  | Type of instrument for evaporation or crop type for evapotranspiration iE | Code table, 0 |
|  | 0 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1 |
|  |  |  | Radiation data (from 1 hour and 24 hour period) |  |
| 1 01 002 |  |  | Replicate next descriptor 2 times |  |
| 3 02 045 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified 553SS 4FFFF or 553SS 5FFFF, 55SSS 4F24F24F24F24 or 55SSS 5F24F24F24F24 | J m-2, -3 |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified 553SS 6FFFF, 55SSS 6F24F24F24F24 | J m-2, -3 |
|  | 0 14 016 |  | Net radiation, integrated over period specified 553SS 0FFFF or 553SS 1FFFF, 55SSS 0F24F24F24F24 or 55SSS 1F24F24F24F24 | J m-2, -4 |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified 553SS 2FFFF, 55SSS 2F24F24F24F24 | J m-2, -4 |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified 553SS 3FFFF, 55SSS 3F24F24F24F24 | J m-2, -4 |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified 55408 4FFFF, 55508 5F24F24F24F24 | J m-2, -4 |
| 3 02 046 |  |  | Temperature change group 54g0sndT |  |
|  | 0 04 024 |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | Time period or displacement (see Note 3) | Hour, 0 |
|  | 0 12 049 |  | Temperature change over period specified sndT | K, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)        	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)           To construct the required time range, descriptor 004024 has to be included two times.

  - BUFR template for synoptic reports from mobile land stations suitable for SYNOP

MOBIL observation data

BUFR template for SYNOP MOBIL is similar to the BUFR template for SYNOP.  The only difference between them is in the very first sequence descriptor; in case of representation of SYNOP MOBIL data, the station identification, time, horizontal and vertical coordinates is provided by a sequence descriptor 3 01 092 (not yet been included in Manual on Codes, WMO-No. 306, I.2 (November 2005)).

It is proposed to represent this template by a single descriptor 3 07 090.

3 07 090:

| 3 01 092 |  |  | Mobile surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 0 01 011 |  | Mobile land station identifier D….D | CCITT IA5, 0 |
|  | 0 01 003 |  | WMO Region number A1 | Code table, 0 |
|  | 0 02 001 |  | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) LaLaLa | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) LoLoLoLo | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  | 0 33 024 |  | Station elevation quality mark im | Code table, 0 |

The rest of the template is identical with the BUFR template for SYNOP data, including the Notes below the template for SYNOP data.

  - BUFR template for wind vertical profiles suitable for PILOT, PILOT SHIP and PILOT

MOBIL observation data (with pressure as the vertical coordinate)

3 09 050

| 3 01 110 |  | Identification of launch site and instrumentation for wind measurements |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Wind data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 050 |  | Wind data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 051 |  | Wind shear data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

(2) Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds)

(3) Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

The ET DR&C meeting is invited to discuss the approach suggested in the Note (4a) that is based on recommendation of the CT MTDCF and also the alternative proposal expressed in the Note (4b). If PILOT data are collected in TAC and converted into BUFR in the national centre, the significant levels are reported using pressure as a vertical coordinate in the TAC message. If needed, however, the height approximates to the standard isobaric surfaces may be applied when the TAC data are converted into BUFR. Significant and fixed regional levels may be reported with either pressure or height as the vertical coordinate, but only one coordinate should be used for the significant and fixed regional levels in the coded TAC report  (Regulation 32.3.1.4). The maximum wind data and wind shear data may also be reported with either pressure or height as the vertical coordinate. Reporting the maximum wind data with height while the whole profile is reported with pressure should not take place in practice as the maximum wind levels are selected from the list of the significant levels (reported with pressure as the vertical coordinate). The Regulations of FM 32 PILOT, however, do not exclude this situation explicitly. Therefore, it is proposed to add the following Note (4b), if any:

(4a)  If maximum wind data and/or wind shear data are reported with height as the vertical coordinate while the whole vertical wind profile is reported with pressure as the vertical coordinate, the sequence 3 09 050 is supplemented by <1 01 000, 0 31 001, 3 03 052> to represent the maximum wind data and by <1 01 000, 0 31 001, 3 03 053> to represent the wind shear data.

(4b)  If maximum wind data and/or wind shear data are reported with height as the vertical coordinate in Parts A or C of  Pilot report, while the whole vertical wind profile is reported with pressure as the vertical coordinate, the data may be converted into BUFR using sequence 3 09 050, because the maximum wind data are as significant levels also included in Parts B or D (being identified by pressure as the vertical coordinate).

  - BUFR template for wind vertical profiles suitable for PILOT, PILOT SHIP and PILOT

MOBIL observation data (with height as the vertical coordinate)

3 09 051

| 3 01 110 |  | Identification of launch site and instrumentation for wind measurements |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Wind data at heights |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 052 |  | Wind data at a height level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at heights |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 053 |  | Wind shear data at a height level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

(2) Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds)

(3) Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

1.5  BUFR template for P, T, U and wind vertical profiles suitable for TEMP, TEMP SHIP

and TEMP MOBIL observation data

3 09 052

| 3 01 111 |  | Identification of launch site and instrumentation |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
| 3 02 049 |  | Cloud information reported with vertical soundings |  |
|  | 0 08 002 | Vertical significance | Code table |
|  | 0 20 011 | Cloud amount (of low or middle clouds Nh) | Code table |
|  | 0 20 013 | Height of base of cloud (h) | m, scale –1 |
|  | 0 20 012 | Cloud type (low clouds CL) | Code table |
|  | 0 20 012 | Cloud type (middle clouds CM) | Code table |
|  | 0 20 012 | Cloud type (high clouds CH) | Code table |
|  | 0 08 002 | Vertical significance ( = missing value) | Code table |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Temperature, dew-point, wind at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 054 |  | Temperature, dew-point, wind at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 10 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 051 |  | Wind shear data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

(2) Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds)

(3) Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

1.6  BUFR template for P, T, U and wind vertical profiles from drop soundings suitable

for TEMP DROP observation data

3 09 053

| 3 01 112 |  | Identification of launch point and instrumentation of dropsonde |  |
| --- | --- | --- | --- |
|  | 0 01 006 | Aircraft identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark | Code table |
|  |  | Temperature, dew-point, wind at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 054 |  | Temperature, dew-point, wind at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 10 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 051 |  | Wind shear data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

(2) Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds)

(3) Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.

Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch

site.

1.7  BUFR template for CLIMAT data

It is proposed to represent the complete template for CLIMAT data by a descriptor 3 07 073 that would be composed of 3 07 071 and 3 07 072 for representation of CLIMAT data of the actual month and for monthly normals (data of CLIMAT Section 2), respectively.

3 07 073 = 3 07 071 + 3 07 072

| 3 07 071 |  | Data of the month (data of CLIMAT Sections 0, 1, 3 and 4) |  |
| --- | --- | --- | --- |
| 3 01 090 |  | Surface station identification; time, horizontal and vertical co-ordinates 3 01 090 = 3 01 004 + 3 01 011 + 3 01 012 + 3 01 021 + 0 07 030 + 0 07 031 |  |
| 3 01 004 |  | Surface station identification |  |
|  | 0 01 001 | WMO block number | Numeric |
|  | 0 01 002 | WMO station number | Numeric |
|  | 0 01 015 | Station or site name | CCITT IA5 |
|  | 0 02 001 | Type of station | Code table |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day ( = 1) (1) | Day |
| 3 01 012 | 0 04 004 | Hour ( = 0) (1) | Hour |
|  | 0 04 005 | Minute ( = 0) (1) | Minute |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, scale 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, scale 5 |
| 0 07 030 |  | Height of station ground above msl | m, scale 1 |
| 0 07 031 |  | Height of barometer above msl | m, scale 1 |
| 0 04 023 |  | Time period ( = number of days in the month) | Day |
|  |  | Monthly mean values of pressure, temperature, extreme temperatures and vapour pressure |  |
| 0 08 023 |  | First order statistics = 4; mean value | Code table |
| 0 10 004 |  | _________ Pressure ( = PoPoPoPo – s.1, gr. 1 in CLIMAT) | Pa, scale –1 |
| 0 10 051 |  | ______ Pressure reduced to msl ( = PPPP - s.1, gr. 2 ) | Pa, scale –1 |
| 0 07 004 |  | Pressure (standard level) (for lowland stations = missing value) | Pa, scale –1 |
| 0 10 009 |  | Geopotential height of the standard level _____ ( = PPPP - s.1, gr. 2 ) (for lowland stations = missing value) | gpm |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature _____ ( = snTTT - s.1, gr. 3 ) | K, scale 2 |
| 0 02 051 |  | Indicator to specify observing method for extreme temperatures ( = iy - s. 4, gr. 7 ) | Code table |
| 0 04 051 |  | Principal time of daily reading of maximum temperature ( = GxGx - s. 4, gr. 7) | Hour |
| 0 12 118 |  | Maximum temperature at height specified, past 24 hours ( = snTxTxTx - s. 1, gr. 4) | K, scale 2 |
| 0 04 052 |  | Principal time of daily reading of minimum temperature ( = GnGn - s.4, gr. 7) | Hour |
| 0 12 119 |  | Minimum temperature at height specified, past 24 hours ( = snTnTnTn - s.1, gr. 4) | K, scale 2 |
| 0 13 004 |  | ____ Vapour pressure ( = eee - s.1, gr. 5 ) | Pa, scale -1 |
| 0 08 023 |  | First order statistics ( = 63; missing value) | Code table |
| 0 12 151 |  | Standard deviation of daily mean temperature ( = ststst - s.1, gr. 3) | K, scale 2 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
| 1 02 005 |  | Replicate 2 descriptors 5 times |  |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic = 1 (pressure) = 2 (temperature) = 4 (vapour pressure) = 7 (maximum temperature) = 8 (minimum temperature) | Code table |
| 0 08 020 |  | Total number of missing entities (days) = mpmp - s.1, gr. 8 (pressure) = mTmT - s.1, gr. 8 (temperature) = meme - s.1, gr. 9 (vapour pressure) = mTx - s.1, gr. 8 (maximum temperature) = mTn - s.1, gr. 8 (minimum temperature) | Numeric |
|  |  | Sunshine duration |  |
| 0 14 032 |  | Total sunshine ( = S1S1S1 - s.1, gr. 7) | Hour |
| 0 14 033 |  | Total sunshine ( = pspsps - s.1, gr. 7) | % |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic = 6 (sunshine duration) | Code table |
| 0 08 020 |  | Total number of missing entities (days) = mSmS - s.1, gr. 9 | Numeric |
|  |  | Number of days of occurrence |  |
| 1 02 018 |  | Replicate 2 descriptors 18 times |  |
| 0 08 052 |  | Conditions for which number of days of occurrence follows = 0 (wind ≥ 10 m/s) = 1 (wind ≥ 20 m/s) = 2 (wind ≥ 30 m/s) = 3 (max. T <273.15 K) = 4 (max. T ≥ 298.15 K) = 5 (max. T ≥ 303.15 K) = 6 (max. T ≥ 308.15 K) = 7 (max. T ≥ 313.15 K) = 8 (min. T < 273.15 K) = 16 (sss > 0.00 m) = 17 (sss > 0.01 m ) = 18 (sss > 0.10 m) = 19 (sss > 0.50 m ) = 20 (horizontal visibility < 50 m) = 21 (horizontal visibility < 100 m) = 22 (horizontal visibility < 1000 m) = 23 (hail) = 24 ( thunderstorm) | Code table |
| 0 08 022 |  | Total number (of days) = f10f10 - s.3 gr.8 (wind ≥10 m/s) = f20f20 - s.3 gr.8 (wind ≥ 20 m/s) = f30f30 - s.3 gr.8 (wind ≥ 30 m/s) = Tx0Tx0 - s.3 gr.2 (Tx < 273.15 K) = T25T25 - s.3 gr.0 (Tx ≥ 298.15 K) = T30T30 - s.3 gr.0 (Tx ≥ 303.15 K) = T35T35 - s.3 gr.1 (Tx ≥ 308.15 K) = T40T40 - s.3 gr.1 (Tx ≥ 313.15 K) = Tn0Tn0 - s.3 gr.2 (Tn < 273.15 K) = s0s0 - s.3 gr.6 (sss > 0.00 m) = s1s1 - s.3 gr.6 (sss > 0.01 m ) = s10s10 - s.3 gr.7 (sss > 0.10 m) = s50s50 - s.3 gr.7 (sss > 0.50 m ) = V1V1 - s.3 gr.9 (h. v. < 50 m) = V2V2 - s.3 gr.9 (h. v. < 100 m) = V3V3 - s.3 gr.9 (h. v. < 1000 m) = DgrDgr - s.4 gr.6 (hail) = DtsDts - s.4 gr.6 ( thunderstorm) | Numeric |
|  |  | Occurrence of extreme values of temperature and wind speed |  |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier = 0 (on 1 day only) = 1 (on 2 or more days) | Code table |
| 0 04 003 |  | Day ( = yxyx - s. 4 gr. 0) | Day |
| 0 12 152 |  | Highest daily mean temperature ( = snTxdTxdTxd - s. 4 gr. 0) | K, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier = 0 (on 1 day only) = 1 (on 2 or more days) | Code table |
| 0 04 003 |  | Day ( = ynyn - s. 4 gr. 1) | Day |
| 0 12 153 |  | Lowest daily mean temperature ( = snTndTndTnd - s. 4 gr. 1) | K, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier = 0 (on 1 day only) = 1 (on 2 or more days) | Code table |
| 0 04 003 |  | Day ( = yaxyax - s. 4 gr. 2) | Day |
| 0 08 023 |  | First order statistics ( = 2; maximum value) | Code table |
| 0 12 101 |  | Temperature/dry-bulb temperature ( = snTaxTaxTax - s. 4 gr. 2) | K, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier = 0 (on 1 day only) = 1 (on 2 or more days) | Code table |
| 0 04 003 |  | Day ( = yanyan - s. 4 gr. 3) | Day |
| 0 08 023 |  | First order statistics (= 3; minimum value) | Code table |
| 0 12 101 |  | Temperature/dry-bulb temperature ( =sn TanTanTan - s. 4 gr. 3) | K, scale 2 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 02 002 |  | Type of instrumentation for wind measurement | Flag table |
| 0 08 053 |  | Day of occurrence qualifier = 0 (on 1 day only) = 1 (on 2 or more days) | Code table |
| 0 04 003 |  | Day ( = yfxyfx - s. 4 gr. 5) | Day |
| 0 11 046 |  | Maximum instantaneous wind speed ( = fxfxfx - s. 4 gr. 5) | ms-1, scale 1 |
| 0 08 053 |  | Day of occurrence qualifier (set to missing = 3 to cancel the previous value) | Code table |
|  |  | Precipitation |  |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 023 |  | Time period (= number of days in the month) (2) | Day |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 13 060 |  | Total accumulated precipitation (= R1R1R1R1 –s.1 gr. 6) | kg m-2, scale 1 |
| 0 13 051 |  | Frequency group; precipitation ( = Rd - s.1 gr. 6) | Code table |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm ( = nrnr - s.1 gr. 6) | Numeric |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic = 5 (precipitation) | Code table |
| 0 08 020 |  | Total number of missing entities (days) = mRmR - s.1, gr. 9 | Numeric |
|  |  | Number of days of occurrence |  |
| 1 02 006 |  | Replicate 2 descriptors 6 times |  |
| 0 08 052 |  | Conditions for which number of days of occurrence follows = 10 (precipitation ≥ 1.0 kg m-2) = 11 (precipitation ≥ 5.0 kg m-2) = 12 (precipitation ≥ 10.0 kg m-2) = 13 (precipitation ≥ 50.0 kg m-2) = 14 (precipitation ≥ 100.0 kg m-2) = 15 (precipitation ≥ 150.0 kg m-2) | Code table |
| 0 08 022 |  | Total number (of days) = R1R1 - s.3 gr.3 (precipitation ≥ 1.0 kg m-2) = R5R5 - s.3 gr.3 (precipitation ≥ 5.0 kg m-2) = R10R10 - s.3 gr.4 (precipitation ≥ 10.0 kg m-2) = R50R50 - s.3 gr.4 (precipitation ≥ 50.0 kg m-2) = R100R100 - s.3 gr.5 (precipitation ≥ 100.0 kg m-2) = R150R150 - s.3 gr.5 (precipitation ≥ 150.0 kg m-2) | Numeric |
|  |  | Occurrence of extreme precipitation |  |
| 0 08 053 |  | Day of occurrence qualifier = 0 (on 1 day only) = 1 (on 2 or more days) | Code table |
| 0 04 003 |  | Day ( = yryr - s. 4 gr. 4) | Day |
| 0 13 052 |  | Highest daily amount of precipitation ( = RxRxRx - s. 4 gr. 4) | kg m-2, scale 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
| 3 07 072 |  | NORMALS (data of CLIMAT Section 2) |  |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (1) | Day |
| 0 04 004 |  | Hour (= 0) (1) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of monthly mean pressure, temperatures, vapour pressure and of standard deviation |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 004 |  | _________ Pressure ( = PoPoPoPo - s.2, gr. 1) | Pa, scale –1 |
| 0 10 051 |  | ______ Pressure reduced to msl ( = PPPP - s.2, gr. 2 ) | Pa, scale –1 |
| 0 07 004 |  | Pressure (standard level) | Pa, scale –1 |
| 0 10 009 |  | Geopotential height of the standard level _____ ( = PPPP - s.2, gr. 2 ) | gpm |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature _____ ( = snTTT - s.2, gr. 3 ) | K, scale 2 |
| 0 02 051 |  | Indicator to specify observing method for extreme temperatures = 2 ( = iy - s. 4, gr. 7 ) | Code table |
| 0 04 051 |  | Principal time of daily reading of maximum temperature ( = GxGx - s. 4, gr. 7) | Hour |
| 0 12 118 |  | Maximum temperature at height specified, past 24 h. _______ ( = snTxTxTx - s. 2, gr. 4) | K, scale 2 |
| 0 04 052 |  | Principal time of daily reading of minimum temperature ( = GnGn - s.4, gr. 7) | Hour |
| 0 12 119 |  | Minimum temperature at height specified, past 24 h. ______ ( = snTnTnTn - s.2, gr. 4) | K, scale 2 |
| 0 13 004 |  | ____ Vapour pressure ( = eee - s.2, gr. 5) | Pa, scale -1 |
| 0 12 151 |  | Standard deviation of daily mean temperature _____ ( = ststst - s.2, gr. 3) | K, scale 2 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
|  |  | Normal of sunshine duration |  |
| 0 14 032 |  | Total sunshine ( = S1S1S1 - s.2, gr. 7) | Hour |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of precipitation |  |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 13 060 |  | Total accumulated precipitation (= R1R1R1R1- s.2 gr. 6) | kg m-2, scale 1 |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm ( = nrnr - s.2 gr. 6) | Numeric |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 1 02 008 |  | Replicate 2 descriptors 8 times |  |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic = 1 (pressure), = 2 (temperature), = 3 (extreme temperatures),(4) = 4 (vapour pressure), = 5 (precipitation), = 6 (sunshine duration) = 7 (maximum temperature), (4) = 8 (minimum temperature), (4) | Code table |
| 0 08 020 |  | Total number of missing entities (years) = ypyp - s.2, gr. 8 (pressure) = yTyT - s.2, gr. 8 (temperature) = yTxyTx - s.2, gr. 8 (extreme temperatures)(4) = yeye - s.2, gr. 9 (vapour pressure) = yRyR - s.2, gr. 9 (precipitation) = ySyS - s.2, gr. 9 (sunshine duration) = maximum temperature (4) = minimum temperature (4) | Numeric |

Notes:

- The time identification refers to the beginning of the one-month period.

- In case of precipitation measurements, the one-month period begins at 06 UTC on the first day of the month and ends at 06 UTC on the first day of the following month.

- If the height of the sensor was changed during the period specified, the value shall be that which   existed for the greater part of the period.

- The number of missing years within the reference period from the calculation of normal for mean extreme air temperature should be given, if available, for both the calculation of normal maximum temperature and for the calculation of normal minimum temperature in addition to the number of missing years for the extreme air temperatures reported under 0 08 020 preceded by 0 08 050 in which Figure 3 is used.

1.8  BUFR template for CLIMAT TEMP and CLIMAT TEMP SHIP data

It is proposed to represent this template by a single descriptor 3 09 054.

3 09 054:

| 3 01 001 | 0 01 001 | WMO block number | Numeric |
| --- | --- | --- | --- |
|  | 0 01 002 | WMO station number | Numeric |
| 0 01 011 |  | Ship's call sign | CCITT IA5 |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day (= 1) (1) | Day |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour |
|  | 0 04 005 | Minute (= 0) (1) | Minute |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 07 007 |  | Height release of sonde above mean sea level | m |
| 0 04 023 |  | Time period (= number of days in the month) | Day |
| 0 04 059 |  | Times of observations used to compute the reported mean values | Flag table |
| 1 15 000 |  | Delayed replication of 15 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 10 009 |  | Geopotential height | gpm |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 12 103 |  | Dew-point temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 32; vector mean) | Code table |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 11 019 |  | Steadiness of wind | % |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 2; temperature) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 9; wind) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |

Note:

The time identification refers to the beginning of the one-month period.

2.  BUFR/CREX templates for maritime code data

2. 1  BUFR template for synoptic reports from sea stations suitable for SHIP observation

data

Editorial modification has been done within 3 02 052 (Temperature and humidity data) as marked below. Sequence descriptor numbers written in blue in this template, have not yet been included in Manual on Codes, WMO-No. 306, I.2 (November 2005).

It is proposed to represent this template by a single descriptor 3 08 007.

3 08 007:

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 001 | 0 10 004 |  | Pressure P0P0P0P0 | Pa, –1 |
|  | 0 10 051 |  | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  | 0 10 061 |  | 3-hour pressure change ppp | Pa, –1 |
|  | 0 10 063 |  | Characteristic of pressure tendency a | Code table, 0 |
| 3 02 054 |  |  | SHIP “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
| 3 02 055 | 0 20 031 |  | Ice deposit (thickness) EsEs | m, 2 |
|  | 0 20 032 |  | Rate of ice accretion Rs | Code table, 0 |
|  | 0 20 033 |  | Cause of ice accretion Is | Flag table, 0 |
|  | 0 20 034 |  | Sea ice concentration ci | Code table, 0 |
|  | 0 20 035 |  | Amount and type of ice bi | Code table, 0 |
|  | 0 20 036 |  | Ice situation zi | Code table, 0 |
|  | 0 20 037 |  | Ice development Si | Code table, 0 |
|  | 0 20 038 |  | Bearing of ice edge Di | Degree true, 0 |
| 3 02 057 |  |  | SHIP marine data |  |
|  |  |  | Sea/water temperature |  |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 060 |  |  | SHIP“period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 059 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)        	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)           0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4)         0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5)          If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

2. 2  BUFR template for synoptic reports from sea stations suitable for SHIP observation

data from VOS stations

This template is a modified version of the BUFR template in paragraph 2.1. Delayed replications have been used extensively to reduce the volume of an individual message, which is a crucial aspect for transmission from VOS stations. It is proposed to represent the entire template by a single descriptor   3 08 008 from Category 8 – Surface report sequences (sea).

Sequence descriptor numbers written in blue in this template, have not yet been included in Manual on Codes, WMO-No. 306, I.2 (November 2005).

3 08 008  =  3 01 093  +  3 02 062   +  3 02 063

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 062 |  |  | SHIP “instantaneous” data from VOS |  |
|  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  | 0 08 002 |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 055 | 0 20 031 | Ice deposit (thickness) EsEs | m, 2 |
|  |  | 0 20 032 | Rate of ice accretion Rs | Code table, 0 |
|  |  | 0 20 033 | Cause of ice accretion Is | Flag table, 0 |
|  |  | 0 20 034 | Sea ice concentration ci | Code table, 0 |
|  |  | 0 20 035 | Amount and type of ice bi | Code table, 0 |
|  |  | 0 20 036 | Ice situation zi | Code table, 0 |
|  |  | 0 20 037 | Ice development Si | Code table, 0 |
|  |  | 0 20 038 | Bearing of ice edge Di | Degree true, 0 |
|  |  |  | Sea/water temperature |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 063 |  |  | SHIP“period” data from VOS |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 064 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  |  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1) Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2) Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3) 0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4) 0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5) If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

2.3  BUFR template for wind vertical profiles suitable for PILOT SHIP observation data

(with pressure as the vertical coordinate)

BUFR template for PILOT SHIP data (with pressure as the vertical coordinate) is identical with the BUFR template for PILOT and PILOT MOBIL data, displayed in paragraph 1.3.

2.4  BUFR template for wind vertical profiles suitable for PILOT SHIP observation data

(with height as the vertical coordinate)

BUFR template for PILOT SHIP data (with height as the vertical coordinate) is identical with the BUFR template for PILOT and PILOT MOBIL data, displayed in paragraph 1.4.

2.5  BUFR template for P, T, U and wind vertical profiles suitable for TEMP SHIP

observation data

BUFR template for TEMP SHIP data is identical with the BUFR template for TEMP and TEMP MOBIL data, displayed in paragraph 1.5.

2.6  BUFR template for CLIMAT SHIP data

It is proposed to represent the complete template for CLIMAT SHIP data by a descriptor 3 08 013 that would be composed of 3 08 011 and 3 08 012 for representation of CLIMAT SHIP data of the actual month and for monthly normals  (data of CLIMAT SHIP Section 2), respectively.

3 08 013 = 3 08 011 + 3 08 012

| 3 08 011 |  | Data of the month (data of CLIMAT SHIP Section 1) |  |
| --- | --- | --- | --- |
| 0 01 011 |  | Ship's call sign | CCITT IA5 |
| 0 02 001 |  | Type of station | Code table |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day (= 1) (1) | Day |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour |
|  | 0 04 005 | Minute (= 0) (1) | Minute |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 07 030 |  | Height of station platform above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 04 023 |  | Time period (= number of days in the month) | Day |
|  |  | Monthly mean values of pressure, temperature, vapour pressure and sea/water temperature |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 051 |  | Pressure reduced to mean sea level | Pa, scale –1 |
| 0 07 032 |  | Height of sensor above marine deck platform (for temperature measurement) | m, scale 2 |
| 0 07 033 |  | Height of sensor above water surface (for temperature measurement) | m, scale 1 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 13 004 |  | Vapour pressure | Pa, scale -1 |
| 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, scale 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, scale 1 |
| 0 22 043 |  | Sea/water temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
|  |  | Precipitation |  |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 023 |  | Time period (= number of days in the month) (2) | Day |
| 0 07 032 |  | Height of sensor above marine deck platform | m, scale 2 |
| 0 13 060 |  | Total accumulated precipitation | kg m-2, scale 1 |
| 0 13 051 |  | Frequency group; precipitation | Code table |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm | Numeric |
| 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, scale 2 |
| 3 08 012 |  | NORMALS (data of CLIMAT SHIP Section 2) |  |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (1) | Day |
| 0 04 004 |  | Hour (= 0) (1) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of monthly mean pressure, temperature, vapour pressure and sea/water temperature |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 051 |  | Pressure reduced to mean sea level | Pa, scale –1 |
| 0 07 032 |  | Height of sensor above marine deck platform (for temperature measurement) | m, scale 2 |
| 0 07 033 |  | Height of sensor above water surface (for temperature measurement) | m, scale 1 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 13 004 |  | Vapour pressure | Pa, scale -1 |
| 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value | m, scale 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, scale 1 |
| 0 22 043 |  | Sea/water temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of precipitation |  |
| 0 07 032 |  | Height of sensor above marine deck platform (for precipitation measurement) | m, scale 2 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 13 060 |  | Total accumulated precipitation | kg m-2, scale 1 |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm | Numeric |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |

Notes:

- The time identification refers to the beginning  of the one-month period.

- In case of precipitation measurements, the one-month period begins at 06 UTC on the first day of the month and ends at 06 UTC on the first day of the following month.

- If the height of the sensor was changed during the period specified, the value shall be that which existed for the greater part of the period.

2.7  BUFR template for CLIMAT TEMP SHIP data

BUFR template for CLIMAT TEMP SHIP data is identical with the BUFR template for CLIMAT TEMP data, displayed in paragraph 1.8.

2.8  BUFR templates for BUOY, TESAC and BATHY data

BUFR template for BUOY data

It is proposed to represent this template by a descriptor 3 08 005.

3 08 005:

001003 - WMO region

001020 - WMO region sub-area

001005 - Buoy/platform identifier

002001 - Type of station

002036 - Buoy type

002149 - Type of data buoy

301011 - Date

301012 - Time

008021 - Time significance (= 26 (time of last known position))

301011 - Date

301012 - Time

008021 - Time significance (set to missing to cancel the previous value)

301021 - Latitude and longitude (high accuracy)

027004 - Alternate latitude (high accuracy)

028004 - Alternate longitude (high accuracy)

007030 - Height of station above MSL

001051 - Platform Transmitter ID (CCITT IA5)

002148 - Data collection and/or Location system

001012 - Platform drift direction

001014 - Platform drift speed

002040 - Method of removing platform direction and speed from current

033022 - Quality of buoy satellite transmission

033023 - Quality of buoy location

033027 - Location quality class (range of radius of 66% confidence)

022063 - Total water depth

302021 - Waves

302022 - Wind waves

302023 - Swell waves

008081 - Type of equipment (observing platform)

025026 - Battery voltage

008081 - Type of equipment (transmitter)

025026 - Battery voltage

008081 - Type of equipment (receiver)

025026 - Battery voltage

008081 - Type of equipment (set to missing to cancel the previous value)

002034 - Drogue type

022060 - Lagrangian drifter drogue status

007070 - Drogue depth

002190 - Lagrangian drifter submergence

025086 - Depth correction indicator

002035 - Cable length

002168 - Hydrostatic pressure of lower end of cable

020031 - Ice deposit (thickness)

002038 - Method of water temperature and/or salinity measurement

306004 - Digitization, depth/salinity method, depths/salinities/temperatures

002030 - Method of current measurement

306005 - Time/duration of current measurement, depths/directions/speeds

007031 - Height of barometer above MSL

008081 - Type of equipment (sensor)

012064 - Instrument temperature

302001 - Pressure and pressure change

008081 - Type of equipment (set to missing to cancel the previous value)

007032 - Height of sensor above marine deck platform (for temp.&hum. measurement)

007033 - Height of sensor above water surface (for temp.&hum. measurement)

012101 - Dry-bulb temperature (scale 2)

012103 - Dew-point temperature (scale 2)

013003 - Relative humidity

007032 - Height of sensor above marine deck platform (for wind measurement)

007033 - Height of sensor above water surface (for wind measurement)

008082 - Modification of sensor height to another value

007033 - Height of sensor above water surface (here height of anemometer to which it is modified)

002169 - Anemometer type

002002 - Type of instrumentation for wind measurement

008021 - Time significance (= 2 (time averaged))

004025 - Time period in minutes

011001 - Wind direction

011002 - Wind speed

008021 - Time significance (set to missing to cancel the previous value)

004025 - Time period in minutes

011043 - Maximum wind gust direction

011041 - Maximum wind gust speed

008082 - Modification of sensor height to another value (set to missing to reset previous value)

007033 - Height of sensor above water surface (set to missing to cancel previous value)

007032 - Height of sensor above marine deck platform (for precipitation measurement)

004024 - Time period in hours

013011 - Total precipitation

007032 - Height of sensor above marine deck platform (set to missing to cancel the previous value)

008021 - Time significance (= 3 (accumulated))

004024 - Time period in hours

014021 - Global radiation, integrated over period specified

008021 - Time significance (set to missing to cancel the previous value)

025028 – Operator or manufacturer defined parameter (#1)

025028 – Operator or manufacturer defined parameter (#2)

025028 – Operator or manufacturer defined parameter (#3)

BUFR template for sub-surface profiling floats suitable for representation of TESAC data

It is proposed to represent this template by a descriptor 3 15 003.

3 15 003:

001003 - WMO region

001020 - WMO region sub-area

001005 - Buoy/platform identifier

001085 - Observing platform manufacturers model

001086 - Observing platform manufacturers serial number

002036 - Buoy type

002149 - Type of data buoy

301011 - Date

301012 - Time

301021 - Latitude and longitude (high accuracy)

007030 - Height of station above MSL

002040 - Method of removing platform direction and speed from current

022067 - Instrument type for water temperature profile measurement

022068 - Water temperature profile recorder type

102004 - Replication 4 times of next 2 descriptors

008080 - Qualifier for quality flag (total water pressure profile)

033050 - Global GTSPP quality flag (for total water pressure profile as qualified above)

008080 - Qualifier for quality flag (total water temperature profile)

033050 - Global GTSPP quality flag (for total water temperature profile as qualified above)

008080 - Qualifier for quality flag (total water salinity profile)

033050 - Global GTSPP quality flag (for total water salinity profile as qualified above)

008080 - Qualifier for quality flag (total water conductivity profile)

033050 - Global GTSPP quality flag (for total water conductivity profile as qualified above)

022055 - Float cycle number

022056 - Direction of profile

022063 - Total depth of water

302021 - Waves

002032 - Indicator for digitization

002033 - Method of salinity/depth measurement

103000 - Delayed replication of 3 descriptors

031001 - Delayed descriptor replication factor

007062 - Depth below sea surface

022045 - Subsurface sea temperature (scale 3)

022064 - Salinity (scale 3)

002030 - Method of current measurement

306005 - Time/duration of current measurement, depths/directions/speeds

Note:	A supplementary descriptor for a unique observation identifier may be added later after definition in coordination with DBCP/SOOP.

BUFR template for XBT/XCTD suitable for representation of BATHY and TESAC data

It is proposed to represent this template by a descriptor 3 15 004.

3 15 004:

001003 - WMO region

001020 - WMO region sub-area

001005 - Buoy/platform identifier

001011 - Ship call sign

001019 - Ship name

001080 - Ship line number according to SOOP

005036 - Ship transect number according to SOOP

001036 - Agency in charge of operating the observing platform

301011 - Date

301012 - Time

301021 - Latitude and longitude (high accuracy)

007030 - Height of station platform above MSL

002040 - Method of removing platform direction and speed from current

022067 - Instrument type for water temperature profile measurement

022068 - Water temperature profile recorder type

008080 - Qualifier for quality flag (total water pressure profile)

033050 - Global GTSPP quality flag (for total water pressure profile as qualified above)

008080 - Qualifier for quality flag (total water temperature profile)

033050 - Global GTSPP quality flag (for total water temperature profile as qualified above)

008080 - Qualifier for quality flag (total water salinity profile)

033050 - Global GTSPP quality flag (for total water salinity profile as qualified above)

008080 - Qualifier for quality flag (total water conductivity profile)

033050 - Global GTSPP quality flag (for total water conductivity profile as qualified above)

025100 - XBT/XCTD fall rate equation coefficient a

025101 - XBT/XCTD fall rate equation coefficient b

022063 - Total depth of water

302021 - Waves

306004 - Sea temperature and salinity profile

002030 - Method of current measurement

306005 - Time/duration of current measurement, depths/directions/speeds

007032 - Height of thermometer above station platform

012101 - Dry-bulb temperature (scale 2)

012103 - Dew-point temperature (scale 2)

007032 - Height of anemometer above station platform

011001 - Wind direction

011002 - Wind speed

Note:	A supplementary descriptor for a unique observation identifier may be added later after definition in coordination with DBCP/SOOP.

2.9  BUFR template for TRACKOB data

BUFR TEMPLATE FOR TRACKOB

It is proposed to represent this template by a descriptor 3 08 015.

3 08 015:

| Table reference | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
| 0 01 011 |  | Ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 72 |
| 1 13 000 |  | Delayed replication of 13 descriptors |  |  |  |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |
| 3 01 011 | 0 04 001 | Year | Year | 0 | 0 | 12 |
|  | 0 04 002 | Month | Month | 0 | 0 | 4 |
|  | 0 04 003 | Day | Day | 0 | 0 | 6 |
| 3 01 012 | 0 04 004 | Hour | Hour | 0 | 0 | 5 |
|  | 0 04 005 | Minute | Minute | 0 | 0 | 6 |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree | 5 | –9000000 | 25 |
|  | 0 06 001 | Longitude (high accuracy) | Degree | 5 | –18000000 | 26 |
| 0 04 080 | NEW | Averaging period for following value | Code table | 0 | 0 | 4 |
| 0 22 049 | NEW | Sea surface temperature | K | 2 | 0 | 15 |
| 0 04 080 | NEW | Averaging period for following value | Code table | 0 | 0 | 4 |
| 0 22 059 | NEW | Sea surface salinity | Part per thousand | 2 | 0 | 14 |
| 0 04 080 | NEW | Averaging period for following value | Code table | 0 | 0 | 4 |
| 0 22 005 | NEW | Direction of sea surface current | Degree true | 0 | 0 | 9 |
| 0 02 042 | NEW | Indicator for sea surface current speed | Code table | 0 | 0 | 2 |
| 0 22 032 | NEW | Speed of sea surface current | ms-1 | 2 | 0 | 13 |
| 0 02 042 | NEW | Indicator for sea surface current speed (cancel) | Code table | 0 | 0 | 2 |
| 0 04 080 | NEW | Averaging period for following value (cancel) | Code table | 0 | 0 | 4 |

3.   BUFR/CREX templates for aviation codes

3.1  BUFR template for METAR/SPECI data

BUFR sequences for data of METAR/SPECI that are available in Manual on Codes, WMO-No. 306, Volume I.2, were developed many years ago and suitable to represent the existing METAR/SPECI code form valid at that time. Since then, however, several changes to the code form and its regulations have been introduced, e.g. NIL, COR, reporting of State of the runway, prevailing visibility. Consequently, name of the sequence descriptor 307021 -Total sequence for representation of METAR/SPECI code in BUFR – does not correspond with the current complete extent of the code. The plan for future activities of ET DR&C [4] contained a recommendation for reviewing templates for METAR/SPECI (and TAF) data.

BUFR sequences for data of METAR/SPECI in Manual on Codes, WMO-No. 306, Volume I.2:

|  |  |  |  |  |  | (Total sequence for representation of METAR/SPECI code in BUFR) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 07 | 021 | 3 | 07 | 011 | Main part of data |  |
|  |  |  | 3 | 07 | 012 | DvVVVV |  |
|  |  |  | 3 | 07 | 013 | DRDRVRVRVRVR |  |
|  |  |  | 3 | 07 | 014 | W´w´ |  |
|  |  |  | 3 | 07 | 015 | Clouds group(s) |  |
|  |  |  | 3 | 07 | 016 | REw´w´ |  |
|  |  |  | 3 | 07 | 017 | Wind shear on runway(s) |  |
|  |  |  | 3 | 07 | 018 | Trend-type landing forecast |  |
|  |  |  | 3 | 07 | 015 | Clouds group(s) |  |

|  |  |  |  |  |  | (Main part of data for representation of METAR/SPECI code in BUFR) |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 | 07 | 011 | 0 | 01 | 063 | ICAO location indicator | CCCC |
|  |  |  | 0 | 02 | 001 | Type of station | (AUTO) |
|  |  |  | 3 | 01 | 011 | Year, month, day (YY) |  |
|  |  |  | 3 | 01 | 012 | GG, gg |  |
|  |  |  | 3 | 01 | 024 | Latitude-longitude (coarse accuracy), height of station |  |
|  |  |  | 0 | 07 | 006 | Height above station (= height of an anemometer) |  |
|  |  |  | 0 | 11 | 001 | Wind direction | ddd |
|  |  |  | 0 | 11 | 016 | Extreme counterclockwise wind direction of a variable wind | dndndn |
|  |  |  | 0 | 11 | 017 | Extreme clockwise wind direction of a variable wind | dxdxdx |
|  |  |  | 0 | 11 | 002 | Wind speed | ff |
|  |  |  | 0 | 11 | 041 | Maximum wind speed (gusts) | fmfm |
|  |  |  | 0 | 07 | 006 | Height above station (= height of a thermometer) |  |
|  |  |  | 0 | 12 | 001 | Temperature | T´T´ |
|  |  |  | 0 | 12 | 003 | Dew-point temperature | T´dT´d |
|  |  |  | 0 | 10 | 052 | Altimeter setting (QNH) | PHPHPHPH |
|  |  |  | 0 | 20 | 009 | General Weather Indicator TAF/METAR |  |
|  |  |  |  |  |  | (DvVVVV) |  |
| 3 | 07 | 012 | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 3) |  |
|  |  |  | 0 | 08 | 023 | First order statistics |  |
|  |  |  | 0 | 05 | 021 | Direction of visibility observed | Dv |
|  |  |  | 0 | 20 | 001 | Horizontal visibility | VVVV |
|  |  |  |  |  |  | (DRDRVRVRVRVR) |  |
| 3 | 07 | 013 | 1 | 06 | 000 | Delayed replication of 6 descriptors |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 4) |  |
|  |  |  | 0 | 01 | 064 | Runway designator | DRDR |
|  |  |  | 0 | 08 | 014 | Qualification for runway visual range |  |
|  |  |  | 0 | 20 | 061 | Runway visual range | VRVRVRVR |
|  |  |  | 0 | 08 | 014 | Qualification for runway visual range |  |
|  |  |  | 0 | 20 | 061 | Runway visual range | VRVRVRVR |
|  |  |  | 0 | 20 | 018 | Tendency of runway visual range | i |
|  |  |  |  |  |  | (w´w´) |  |
| 3 | 07 | 014 | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 3) |  |
|  |  |  | 0 | 20 | 019 | Significant present weather | w´w´ |
|  |  |  |  |  |  | (Clouds group(s)) |  |
| 3 | 07 | 015 | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication |  |
|  |  |  | 3 | 02 | 005 | (NsNsNs, CC, hshshs) |  |
|  |  |  | 0 | 20 | 002 | Vertical visibility | VVhshshs |
|  |  |  |  |  |  | (REw´w´) |  |
| 3 | 07 | 016 | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 3) |  |
|  |  |  | 0 | 20 | 020 | Significant recent weather phenomena | REw´w´ |
|  |  |  |  |  |  | (Wind shear on runways(s)) |  |
| 3 | 07 | 017 | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication |  |
|  |  |  | 0 | 11 | 070 | Runway designator of the runway affected by wind shear (including ALL) | WS RWYDRDR |
|  |  |  |  |  |  | (Trend-type landing forecast) |  |
| 3 | 07 | 018 | 0 | 08 | 016 | Change qualifier of a trend-type | TTTTT |
|  |  |  |  |  |  | Forecast or an aerodrome forecast |  |
|  |  |  | 1 | 02 | 000 | Delayed replication of 2 descriptors |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 2) |  |
|  |  |  | 0 | 08 | 017 | Qualifier of the time when the forecast | TT |
|  |  |  |  |  |  | Change is expected (FM, TL, AT) |  |
|  |  |  | 3 | 01 | 012 | GG, gg |  |
|  |  |  | 1 | 04 | 000 | Delayed replication of 4 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 1) |  |
|  |  |  | 0 | 07 | 006 | Height above station |  |
|  |  |  | 0 | 11 | 001 | Wind direction | ddd |
|  |  |  | 0 | 11 | 002 | Wind speed | ff |
|  |  |  | 0 | 11 | 041 | Maximum wind speed (gusts) | fmfm |
|  |  |  | 0 | 20 | 009 | General Weather Indicator |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 1) |  |
|  |  |  | 0 | 20 | 001 | Horizontal visibility | VVVV |
|  |  |  | 3 | 07 | 014 | W´w´ |  |
|  |  |  |  |  |  | (Short METAR/SPECI) |  |
| 3 | 07 | 020 | 3 | 07 | 011 | Main part of data |  |
|  |  |  | 3 | 07 | 014 | W´w´ |  |
|  |  |  | 3 | 07 | 016 | REw´w´ |  |

Alternative representation of data in sequences 307011 and  307018:

In compliance with the general policy to use temperature descriptors with higher accuracy (scale 2) and in 2001 newly introduced vertical coordinate descriptors 3 07 030, 3 07 031 and 3 07 032 in  BUFR/CREX templates, an alternative way of representation of data in sequences 307011 and 307018 was suggested:

Instead of sequence 307011, use the following new sequence:

001063 - ICAO location indicator

002001 - Type of station

301011 - Year, month, and day

301012 - Hour and minute

301023 - Latitude and longitude (coarse accuracy)

007031 - Height of barometer above MSL

007032 - Height of anemometer above ground

011001 - Wind direction

011016 - Extreme counterclockwise wind direction of a variable wind

011017 - Extreme clockwise wind direction of a variable wind

011002 - Wind speed

011041 - Maximum wind speed (gusts)

007032 - Height of thermometer above ground

012101 - Temperature (scale 2)

012103 - Dewpoint temperature (scale 2)

010052 - Altimeter setting (QNH)

020009 - General Weather Indicator (TAF/METAR)

Instead of sequence 307018, use the following new sequence:

008016 - Change qualifier of a trend-type or aerodrome forecast

102000 - Delayed replication of 2 descriptors

031001 - Number of replications (up to 2)

008017 - Qualifier of the time when the forecast change is expected (FM,TL,AT)

301012 - Hour and minute

104000 - Delayed replication of 4 descriptors

031001 - Number of replications (up to 1)

007032 - Height of anemometer above ground

011001 - Wind direction

011002 - Wind speed

011041 - Maximum wind speed (gusts)

020009 - General Weather Indicator

101000 - Delayed replication of 1 descriptor

031001 - Number of replications (up to 1)

020001 - Horizontal visibility

307014 - Significant present weather sequence

3.2  BUFR template for TAF

A draft template for representation of TAF data in BUFR/CREX has been developed. The ET DR&C recommended  to review and update this template [4].

3.3  BUFR template for single level AMDAR data

There are three BUFR templates for AMDAR data in this paragraph:

- a template for standard AMDAR reports [2],

- a template for AMDAR data [1], [3],

- a more complex template for AMDAR data [1], [3], [4].

Besides that, sequences 3 11 001 and 3 11 002 are recommended as an example of AMDAR descriptors in [5] - Aircraft Meteorological Data Relay (AMDAR), Reference Manual, WMO-No. 958.

BUFR template for standard AMDAR reports

|  |  |  |  |  |  | (Standard AMDAR reports) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 11 | 005 | 0 | 01 | 008 | Aircraft identification |
|  |  |  | 0 | 01 | 023 | Sequence number |
|  |  |  | 3 | 01 | 021 | Latitude and longitude |
|  |  |  | 3 | 01 | 011 | Year, month and day |
|  |  |  | 3 | 01 | 013 | Hour, minute and second |
|  |  |  | 0 | 07 | 010 | Flight level |
|  |  |  | 0 | 08 | 009 | Detailed phase of flight |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |
|  |  |  | 0 | 11 | 031 | Degree of turbulence |
|  |  |  | 0 | 11 | 036 | Derived equivalent vertical gust speed |
|  |  |  | 0 | 12 | 101 | Temperature/dry-bulb temperature |
|  |  |  | 0 | 33 | 025 | ACARS interpolated values |

BUFR template for single level AMDAR data

It is proposed to delete this template from the list of templates for representation of TAC in TDCF

001006 - Aircraft identifier

002061 - Aircraft navigational system

301011 - Year, month, and day

301013 - Hour, minute, and second

301021 - Latitude and longitude (high accuracy)

008004 - Phase of aircraft flight

007010 - Height or altitude (flight level)

002062 - Type of aircraft data relay system

002005 - Precision of temperature observation

012101 - Temperature/dry-bulb temperature (scale 2)

012103 - Dew-point temperature (scale 2)

013003 - Relative humidity

011001 - Wind direction

011002 - Wind speed

011031 - Degree of turbulence

011036 - Maximum derived equivalent vertical gust speed

Note:

New descriptors may need to be defined for reporting, the flight level value defined within Section 3 of FM 42 AMDAR, and such descriptor(s) should then be added to the above template.  Note that this is not the same as the altitude value within Section 2, which is itself stored as 007010 in the above template.

BUFR template for single level AMDAR data (a more complex template)

It is proposed to represent this template by a descriptor 3 11 010.

3 11 010:

| 3 | 11 | 005 | 0 | 01 | 008 | Aircraft identification (1) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 0 | 01 | 023 | Sequence number (2) |
|  |  |  | 3 | 01 | 021 | Latitude and longitude |
|  |  |  | 3 | 01 | 011 | Year, month and day |
|  |  |  | 3 | 01 | 013 | Hour, minute and second |
|  |  |  | 0 | 07 | 010 | Flight level (4) |
|  |  |  | 0 | 08 | 009 | Detailed phase of flight (3) |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |
|  |  |  | 0 | 11 | 031 | Degree of turbulence |
|  |  |  | 0 | 11 | 036 | Derived equivalent vertical gust speed |
|  |  |  | 0 | 12 | 101 | Temperature/dry-bulb temperature |
|  |  |  | 0 | 33 | 025 | ACARS interpolated values |
| 0 | 08 | 004 |  |  |  | Phase of flight |
| 0 | 02 | 064 |  |  |  | Wind quality/roll angle |
| 0 | 13 | 003 |  |  |  | Relative humidity |
| 0 | 12 | 103 |  |  |  | Dew-point temperature |
| 0 | 13 | 002 |  |  |  | Mixing ratio |
| 1 | 02 | 000 |  |  |  | Delayed replication of two descriptors |
| 0 | 31 | 001 |  |  |  | Delayed descriptor replication factor (5) |
| 0 | 11 | 075 |  |  |  | Intensity (EDR) |
| 0 | 11 | 076 |  |  |  | Peak (EDR) |
| 0 | 11 | 037 |  |  |  | Turbulence index (EDR) |
| 0 | 11 | 039 |  |  |  | Extended time of occurrence of peak EDR (6) |
| 0 | 11 | 077 |  |  |  | EDR reporting interval (7) |
| 0 | 20 | 042 |  |  |  | Ice/no ice |
| 0 | 20 | 043 |  |  |  | Peak liquid water content (8) |
| 0 | 20 | 044 |  |  |  | Average liquid water content (8) |
| 0 | 20 | 045 |  |  |  | Supercooled water droplet conditions (8) |

Notes:

1.	Aircraft identifier  0 01 008 can cope with ASDAR, ADS and other AMDAR identities.  ADS reports use a 24-bit ICAO airframe identifier, equating to an 8-character BCD number.

- The sequence number is a simple observation count to be included in the downlinked message.  It should be reset at 0000 UTC each day and is especially useful for quality control, data management and archiving purposes.

- This phase of flight table is expanded to indicate wind quality from roll angle (or roll and pitch combined) and also to indicate the method of ascent and descent observation interval selection either by time or pressure increments.

- Flight level is defined relative to the ICAO standard sea level pressure and is readily converted to static air pressure using standard formulae.  Once converted, the original resolution (either 100ft or 10ft) is lost, hence it is desirable to disseminate the element in the received form.  The descriptor shown is designed to deal with high-resolution flight level data.

- Some aircraft report up to 10 pairs of EDR values per observation.  The corresponding times and position could be found by interpolation from the previous report.

- 0 11 039 allows observation intervals up to one hour.  0 11 038 allows up to 15 minutes only whereas observation intervals of 30 minutes or more are commonly used.

- The EDR observing interval and associated averaging time differs according to individual observing schedule and cannot be assumed to be identical to the observation interval for the main elements.  It is desirable to include this information in the coded data.

- A special automatic icing report, including these elements, is expected to become available from some aircraft and a downlink code has been published.

3.4  BUFR templates for aircraft ascent/descent profile suitable for AMDAR profile data

| BUFR/CREX template for aircraft ascent/descent profile without Lat. Long. reported at each level |
| --- |
| Element | BUFR descriptor (BUFR Table B/D) | Notes | CREX descriptor |
| Descriptor defining the complete template | 3 11 008 |  | D 11 008 |
| Aircraft identification | 0 01 008 |  | B 01 008 |
| Year, month, day | 3 01 011 | Date/Time and position of first level in profile | D 01 011 |
| Hour, Min, second | 3 01 013 |  | D 01 013 |
| Latitude, Longitude | 3 01 021 |  | D 01 021 |
| Phase of flight | 0 08 004 | Ascent or descent profile | B 08 004 |
| Delayed replication of one descriptor | 1 01 000 |  | R 01 000 |
| Delayed descriptor replication factor | 0 31 001 | Number of levels following |  |
| Aircraft ascent/descent profile data for one level (as below) | 3 11 006 |  | D 11 006 |
| Flight level | 0 07 010 |  | B 07 010 |
| Wind direction | 0 11 001 |  | B 11 001 |
| Wind speed | 0 11 002 |  | B 11 002 |
| Roll angle quality | 0 02 064 |  | B 02 064 |
| Temperature/dry-bulb temperature | 0 12 101 |  | B 12 101 |
| Dew-point temperature | 0 12 103 |  | B 12 103 |
| BUFR/CREX template for aircraft ascent/descent profile with lat. long given for each level |
| Descriptor defining the complete template | 3 11 009 |  | D 11 009 |
| Aircraft identification | 0 01 008 |  | B 01 008 |
| Year, month, day | 3 01 011 | Date/Time and position of first level in profile | D 01 011 |
| Hour, Min, second | 3 01 013 |  | D 01 013 |
| Latitude, Longitude | 3 01 021 |  | D 01 021 |
| Phase of flight | 0 08 004 | Ascent or descent profile | B 08 004 |
| Delayed replication of one descriptor | 1 01 000 |  | R 01 000 |
| Delayed descriptor replication factor | 0 31 001 | Number of levels following |  |
| Aircraft ascent/descent profile data for one level with lat. long. indicated | 3 11 007 |  | D 11 007 |
| Flight level | 0 07 010 |  | B 07 010 |
| Latitude, Longitude | 3 01 021 |  | D 01 021 |
| Wind direction | 0 11 001 |  | B 11 001 |
| Wind speed | 0 11 002 |  | B 11 002 |
| Roll angle quality | 0 02 064 |  | B 02 064 |
| Temperature/dry-bulb temperature | 0 12 101 |  | B 12 101 |
| Dew-point temperature | 0 12 103 |  | B 12 103 |

4.   BUFR/CREX templates for satellite observations

4.1  BUFR template for SAREP data (Part A: Information on tropical cyclone)

It is proposed to represent this template by a descriptor 3 16 030:

| Table reference | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
|  |  | (Station identification and time) |  |  |  |  |
| 3 01 005 NEW | 0 01 035 | Originating centre | Common code table C-11 | 0 | 0 | 16 |
|  | 0 01 034 | Identification of originating/generating sub-centre | Common code table C-12 | 0 | 0 | 8 |
| 3 01 011 | 0 04 001 | Year | Year | 0 | 0 | 12 |
|  | 0 04 002 | Month | Month | 0 | 0 | 4 |
|  | 0 04 003 | Day | Day | 0 | 0 | 6 |
| 3 01 012 | 0 04 004 | Hour | Hour | 0 | 0 | 5 |
|  | 0 04 005 | Minute | Minute | 0 | 0 | 6 |
|  |  | (Satellite information) |  |  |  |  |
| 0 01 007 |  | Satellite identifier | Code table | 0 | 0 | 10 |
| 0 25 150 | NEW | Satellite intensity analysis method of tropical cyclone | Code table | 0 | 0 | 4 |
|  |  | (Tropical cyclone information) |  |  |  |  |
| 1 22 000 |  | Delayed replication of 22 descriptors |  |  |  |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric | 0 | 0 | 8 |
| 0 01 027 |  | WMO long storm name | CCITT IA5 | 0 | 0 | 80 |
| 0 19 150 | NEW | Typhoon International Common Number (Typhoon Committee) | CCITT IA5 | 0 | 0 | 32 |
| 0 19 106 | NEW | Identification number of tropical cyclone | Numeric | 0 | 0 | 7 |
| 0 08 005 |  | Meteorological attribute significance (=1) | Code table | 0 | 0 | 4 |
| 0 05 002 |  | Latitude (coarse accuracy) | Degree | 2 | –9000 | 15 |
| 0 06 002 |  | Longitude (coarse accuracy) | Degree | 2 | –18000 | 16 |
| 0 08 005 |  | Meteorological attribute significance (set to missing to cancel the previous value) | Code table | 0 | 0 | 4 |
| 0 19 107 | NEW | Time interval of the tropical cyclone analysis | Code table | 0 | 0 | 4 |
| 0 19 005 |  | Direction of motion of feature | Degree true | 0 | 0 | 9 |
| 0 19 006 |  | Speed of motion of feature | m s–1 | 2 | 0 | 14 |
| 0 19 108 | NEW | Accuracy of geographical position of the tropical cyclone | Code table | 0 | 0 | 3 |
| 0 19 109 | NEW | Mean diameter of the overcast cloud of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 110 | NEW | Apparent 24-hour change in intensity of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 111 | NEW | Current Intensity (CI) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 112 | NEW | Data tropical (DT) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 113 | NEW | Cloud pattern type of the DT-number | Code table | 0 | 0 | 4 |
| 0 19 114 | NEW | Model Expected tropical (MET) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 115 | NEW | Trend of the past 24-hour change (+: Developed, -: Weakened) | Numeric | 1 | -30 | 6 |
| 0 19 116 | NEW | Pattern tropical (PT) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 117 | NEW | Cloud picture type of the PT-number | Code table | 0 | 0 | 3 |
| 0 19 118 | NEW | Final tropical (T) number of the tropical cyclone | Numeric | 1 | 0 | 7 |
| 0 19 119 | NEW | Type of the final T-number | Code table | 0 | 0 | 3 |

5.   BUFR/CREX templates for miscellaneous codes

5.1  BUFR template for RADOB data (Part A: Information on tropical cyclone)

It is proposed to represent this template by a descriptor 3 16 032.

3 16 032:

| Table reference | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
|  |  | Station identification and time |  |  |  |  |
| 3 01 001 | 0 01 001 | WMO block number | Numeric | 0 | 0 | 7 |
|  | 0 01 002 | WMO station number | Numeric | 0 | 0 | 10 |
| 3 01 011 | 0 04 001 | Year | Year | 0 | 0 | 12 |
|  | 0 04 002 | Month | Month | 0 | 0 | 4 |
|  | 0 04 003 | Day | Day | 0 | 0 | 6 |
| 3 01 012 | 0 04 004 | Hour | Hour | 0 | 0 | 5 |
|  | 0 04 005 | Minute | Minute | 0 | 0 | 6 |
|  |  | Radar information |  |  |  |  |
| 0 02 160 | NEW | Wave length of the radar | Code table | 0 | 0 | 4 |
|  |  | Tropical Cyclone |  |  |  |  |
| 0 08 005 |  | Meteorological attribute significance (=1) | Code table | 0 | 0 | 4 |
| 0 05 002 |  | Latitude (coarse accuracy) | Degree | 2 | –9000 | 15 |
| 0 06 002 |  | Longitude (coarse accuracy) | Degree | 2 | –18000 | 16 |
| 0 08 005 |  | Meteorological attribute significance (set to missing to cancel the previous value) | Code table | 0 | 0 | 4 |
| 0 19 100 | NEW | Time interval over which the movement of the centre or the eye of the tropical cyclone has been calculated | Code table | 0 | 0 | 4 |
| 0 19 005 |  | Direction of motion of feature | Degree true | 0 | 0 | 9 |
| 0 19 006 |  | Speed of motion of feature | m s–1 | 2 | 0 | 14 |
| 0 19 101 | NEW | Accuracy of the position of the centre or the eye of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 102 | NEW | Shape and definition of the eye of the tropical cyclone | Code table | 0 | 0 | 3 |
| 0 19 103 | NEW | Diameter or length of major axis of the eye of the tropical cyclone | Code table | 0 | 0 | 4 |
| 0 19 104 | NEW | Change in character of the eye during the 30 minutes preceding the time of observation | Code table | 0 | 0 | 4 |
| 0 19 105 | NEW | Distance between the end of the observed outermost spiral band and the centre of the tropical cyclone | Code table | 0 | 0 | 4 |

ANNEX

Proposed common sequences:

| 3 07 073 |  | Sequence for representation of CLIMAT data |
| --- | --- | --- |
|  | 3 07 071 | Data of the month (suitable for representation of CLIMAT data, Section 0, 1, 3 and 4) |
|  | 3 07 072 | Normals (suitable for representation of CLIMAT data, Section 2) |
| 3 07 080 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data |
| 3 07 090 |  | Sequence for representation of synoptic reports from a mobile station suitable for SYNOP MOBIL type data |
| 3 08 005 | ? | Sequence for representation of BUOY data |
| 3 08 007 |  | Sequence for representation of synoptic reports from a sea station suitable for SHIP data |
| 3 08 008 |  | Sequence for representation of synoptic reports from a sea station suitable for SHIP data from VOS stations |
| 3 08 013 |  | Sequence for representation of CLIMAT SHIP data |
|  | 3 08 011 | Data of the month (suitable for representation of CLIMAT SHIP data, Section 1) |
|  | 3 08 012 | Normals (suitable for representation of CLIMAT SHIP data, Section 2) |
| 3 08 015 |  | Sequence for representation of TRACKOB data |
| 3 09 054 |  | Sequence for representation of CLIMAT TEMP and CLIMAT TEMP SHIP data |
| 3 11 010 |  | Sequence for representation of single level AMDAR data |
| 3 15 003 |  | Sequence for sub-surface profiling floats suitable for representation of TESAC data |
| 3 15 004 |  | Sequence for XBT/XCTD suitable for representation of BATHY/TESAC data |
| 3 16 030 |  | Sequence for representation SAREP data (Part A: Information on tropical cyclone) |
| 3 16 032 |  | Sequence for representation of RADOB data (Part A: Information on tropical cyclone) |

Note:

It is proposed to delete 3 07 070 (Sequence for representation of synoptic reports from a sea station suitable for SHIP data from VOS stations) from the list of validated common sequences as it was replaced by  3 08 008 from a more properly chosen category 08 (Surface report sequences (sea)).