| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, 5-8 DECEMBER 2005 |  | CT MTDCF/Doc. 5.4(2) ITEM: 5.4 (16.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

Proposed BUFR template for buoy wave data

Submitted by the Data Buoy Cooperation Panel (DBCP)

________________________________________________________________

Summary and Purpose of Document

The document contains a template recommended for representation of buoy wave data.

________________________________________________________________

ACTION PROPOSED

CBS ET/DRC is invited to discuss the proposed template, possibly suggest changes, and eventually to adopt it for pre-operational use.

Proposed BUFR template for buoy wave data

Submitted by the Data Buoy Cooperation Panel (DBCP)

DISCUSSION

At its 20th session, the Data Buoy Cooperation Panel (DBCP) expressed concern that there was no BUFR template defined for wave data reported from buoys.

The Technical Coordinator of the DBCP and Météo France had worked during the DBCP intersessional period to draft a new template for buoy data. The latter had been discussed and agreed upon by the DBCP at its 21st session, Buenos Aires,  17-21 October 2005, and the Technical Coordinator was asked to submit it to the CBS Expert Team on Data Representation and Codes for discussion, possible amendment and adoption.

There is the need for a buoy wave template because there are a number of directional and non-directional wave buoys deployed that report their data in real time. FM-65-XI Ext. WAVEOB format (annex B) is usually being used for GTS distribution of the data.

Also, Puertos Del Estado, Spain (PDE, http://www.puertos.es/externo/clima/Rayo/indexeng.html) had deployed a moored buoy network around the Iberic Peninsula both in the Atlantic Ocean and the Mediterranean Sea. Many of these buoys do measure and report directional wave data. PDE had designed and developed in cooperation with Instituto Nacional de Meteorología español (INM) a Spanish version of a BUFR template for wave buoy data that meets their needs (annex C). However, while the latter contains useful descriptors and satisfies many user needs, it contains minor inconsistencies and is not entirely satisfactory as a standard and for global use (encoding practices, lack of required descriptors).

New BUFR template for buoy wave data herewith proposed would:

- Meet PDE needs and users of PDE wave data;

- Include additional descriptors corresponding to fields that appear in WAVEOB format but did not appear in the PDE template;

- Remain compatible with the BUFR template for buoy data that was adopted by the CBS Expert Team on data representation and codes at its Arusha meeting, 17-21 February 2003 and which is now being used operationally by Service Argos for GTS distribution of buoy data in BUFR. Compatibility is ensured by just adding new required descriptors at the end of the existing template.

Proposed draft BUFR template is described in annex A.

CBS ET/DRC is invited to discuss the proposed template, possibly suggest changes, and eventually to adopt it for pre-operational use.

Proposed BUFR Template for buoy and wave data

(draft)

Proposed template is listed in the table 1 below. Descriptors number 1 to 84 in the table correspond to the existing BUFR template for buoy data (i.e. the “Arusha” template).

Descriptors used are from BUFR Master table 0, version 11. No local table is being used.

- Are indicated in red descriptors that are presently being used for BUFR encoding of PDE buoy data

- Are indicated in blue descriptors that are similar to those being used for BUFR encoding of PDE buoy data (i.e. another way to code the same information is proposed)

- Are indicated in green, information which will have to be encoded for PDE buoys if the information is available (i.e. will be useful or required by users)

- New proposed descriptors for BUFR template for buoy data are indicated in bold and italic. They correspond to descriptors 85 and after.

Implication for PDE buoys:

- Buoy WMO identification number to be coded and divided in 3 descriptors instead of 1 (i.e. 001003, 001020, and 001005).

- Buoy position to be coded in high accuracy instead of coarse accuracy.

- Air pressure reduced to sea level (MSLP) must be computed and encoded.

- Sensor height with regard to platform deck and average sea level will have to be encoded for air temperature and wind; wind is assumed to be corrected to 10m so this will have to be indicated in the reports (i.e. 008082 coded 1, and 007033 coded for 10m).

- Fields for which information is not available will be coded with “missing”.

- Section 1 of existing PDE BUFR reports was not encoded according to existing regulations:

  - Local table version should be coded 0 (not 1) as all descriptors being used are formal WMO descriptors (i.e. no PDE local descriptors are being used).

  - Current B§UFR table version is 11 (not 1)

  - Year should be coded as following: YYYY coded (YYYY-100*(Century-1)), e.g. 2005 coded 05.

Table 1: Proposed new template for buoy data, including directional and non-directional wave data

| # | Descriptor | Name | Expanded descriptors | Comment, encoding |
| --- | --- | --- | --- | --- |
| 1 | 001003 | WMO region | 001003 | First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO region sub-area | 001020 | Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 002001 | Type of station | 002001 | 1=Manned station |
| 5 | 002036 | Buoy type | 002036 | 1=Fixed buoy |
| 6 | 002149 | Type of data buoy | 002149 | 16=unspecified moored buoy 24=Omnidirectional waverider 25=Directional waverider |
| 7 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | Date of observation |
| 8 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | Time of observation |
| 9 | 008021 | Time significance | 008021 | Value = 26 (time of last known position) |
| 10 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | Date of last known position coded here; coded missing for fixed station |
| 11 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | Time of last known position coded here; coded missing for fixed station |
| 12 | 008021 | Time significance | 008021 | Value = “missing” |
| 13 | 301021 | Latitude and longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Coarse accuracy descriptors (005002 and 006002 respectively) were used with PDE buoys |
| 14 | 027004 | Alternate latitude (high accuracy) | 027004 | Coded if Argos is used for location; otherwise coded missing |
| 15 | 028004 | Alternate longitude (high accuracy) | 028004 | Coded if Argos is used for location; otherwise coded missing |
| 16 | 007030 | Height of station above MSL | 007030 |  |
| 17 | 001051 | Platform Transmitter ID (CCITT IA5) | 001051 | If Argos is used, Argos ID number; |
| 18 | 002148 | Data collection and/or Location system | 002148 | 1=Argos 2=GPS Coded missing if none |
| 19 | 001012 | Platform drift direction | 001012 | Coded missing for moored buoys |
| 20 | 001014 | Platform drift speed | 001014 | Coded missing for moored buoys |
| 21 | 002040 | Method of removing platform direction and speed from current | 002040 | Coded missing for moored buoys |
| 22 | 033022 | Quality of buoy satellite transmission | 033022 | 0=Good 1=Dubious 3=missing |
| 23 | 033023 | Quality of buoy location | 033023 | 0=Reliable 1=Last known position 2=Dubious 3=missinh |
| 24 | 033027 | Location quality class (range of radius of 66% confidence) | 033027 | 0: >= 1500m 1: 500m to 1500m |
| 25 | 022063 | Total water depth | 022063 | Mooring depth; otherwise coded missing |
| 26 | 302021 | Waves | 022001 (direction of waves) 022011 (period of waves) 022021 (height of waves) |  |
| 27 | 302022 | Wind waves | 022002 (direction wind wv) 022012 (period wind wv) 022022 (height wind wv) |  |
| 28 | 302023 | Swell waves | 022003 (direction swell wv) 022013 (period swell wv) 022023 (height swell wv) |  |
| 29 | 008081 | Type of equipment (observing platform) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=3: Equipment = “platform” |
| 30 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Platform battery voltage |
| 31 | 008081 | Type of equipment (transmitter) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=1: Equipment = “transmitter” |
| 32 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Transmitter battery voltage |
| 33 | 008081 | Type of equipment (receiver) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=2: Equipment = “receiver” |
| 34 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Receiver battery voltage |
| 35 | 008081 | Type of equipment – value Missing = cancel | 008081 | 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value = “missing” |
| 36 | 002034 | Drogue type | 002034 | Coded missing for moored buoys |
| 37 | 022060 | Lagrangian drifter drogue status | 022060 | (New descriptor, scale=0, ref=0, bits=3) 0=detached 1=attached 3=missing Coded missing for moored buoys |
| 38 | 007070 | Drogue depth | 007070 | Coded missing for moored buoys |
| 39 | 002190 | Lagrangian drifter submergence | 002190 | Coded missing for moored buoys |
| 40 | 025086 | Depth correction indicator for sub-surface measurements along cable | 025086 | 0=depths are not corrected 1=depths are corrected 3=missing |
| 41 | 002035 | Cable length | 002035 | Depth of hydrostatic pressure sensor at bottom of cable |
| 42 | 002168 | Hydrostatic pressure of lower end of cable | 002168 |  |
| 43 | 020031 | Ice deposit (thickness) | 020031 | Ice thickness |
| 44 | 002038 | Method of temperature and/or velocity measurement | 002038 | e.g. 2=hull contact sensor 8=thermistor chain |
| 45 | 306004 | Digitization, depth/salinity method, depths/salinities/temperatures | 002032 (indicator for digit) 002033 (method sal/depth) 103000 (delayed repl 3 desc) 031001 (replication factor) 007062 (depth) 022043 (sea temperature) 022062 (salinity) | Replication factor indicates number of (depth, temp., salinity) data points that are encoded |
| 46 | 002030 | Method of current measurement | 002030 |  |
| 47 | 306005 | Time/duration of current measurement, depths/directions/speeds | 002031 (method current) 103000 (delayed repl 3 desc) 031001 (replicationfactor) 007062 (depth) 022004 (direction current) 022031 (speed current) | Replication factor indicates number of (pepth, dir, speed) data points that are encoded |
| 48 | 007031 | Height of barometer above MSL | 007031 |  |
| 49 | 008081 | Type of equipment (sensor) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=0: Equipment = “sensor” |
| 50 | 012064 | Instrument temperature | 012064 | Temperature of air pressure sensor |
| 51 | 302001 | Pressure and pressure change | 010004 (pressure at station) 010051 (MSLP) 010061 (3-hour tendency) 010063 (tend. Characteristic) | Mean Seal Level Pressure to be computed based upon pressure at station level and sensor height |
| 52 | 008081 | Type of equipment – value missing = cancel | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value = “missing” |
| 53 | 007032 | Height of sensor above marine deck platform (for temp.&hum. measurement) | 007032 | Height of thermometer above marine desck |
| 54 | 007033 | Height of sensor above water surface (for temp.&hum. measurement) | 007033 | Height of thermometer (assumed should be coded with value = 2 metres for PDE buoys) |
| 55 | 012101 | Dry-bulb temperature (scale 2) | 012101 | Dry-bulb temperature at 2m (012004) was used for PDE buoys |
| 56 | 012103 | Dew-point temperature (scale 2) | 012103 |  |
| 57 | 013003 | Relative humidity | 013003 |  |
| 58 | 007032 | Height of sensor above marine deck platform (for wind measurement) | 007032 | Real height of anemometer above marine deck |
| 59 | 007033 | Height of sensor above water surface (for wind measurement) | 007033 | Real height of anemometer above average water surface |
| 60 | 008082 | Artificial correction of sensor height to another value | 008082 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor height is not corrected 1=sensor height is artificially corrected 7=missing Assumed should be coded to value 1 for PDE buoys |
| 61 | 007033 | Height of sensor above water surface (here height of anemometer to which it is artificially corrected) | 007033 | Here height of anemometer to which it is artificially corrected Assumed should be coded with value = 10 metres for PDE buoys |
| 62 | 002169 | Anemometer type | 002169 | e.g. 0=rotor 1=propeller rotor |
| 63 | 002002 | Type of instrumentation for wind measurement | 002002 |  |
| 64 | 008021 | Time significance | 008021 | Value = 2 (time averaged) |
| 65 | 004025 | Time period in minutes | 004025 | Value for averaging period (e.g. 10 minutes) |
| 66 | 011001 | Wind direction | 011001 | Wind direction at 10m (011011) was used with PDE buoys |
| 67 | 011002 | Wind speed | 011002 | Wind speed at 10m (011012) was used with PDE buoys |
| 68 | 008021 | Time significance | 008021 | Value = 23 (monitoring period) |
| 69 | 004025 | Time period in minutes | 004025 | Period during which gust is being monitored prior to observation time |
| 70 | 011043 | Maximum wind gust direction | 011043 |  |
| 71 | 011041 | Maximum wind gust speed | 011041 |  |
| 72 | 008082 | Artificial correction of sensor height to another value (set to missing to reset previous value) | 008082 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor height is not corrected 1=sensor height is artificially corrected 7=missing Here coded with value = “missing” |
| 73 | 007033 | Height of sensor above water surface (set to missing to cancel previous value) | 007033 | Value=”missing”: Redefine height to previous level |
| 74 | 007032 | Height of sensor above marine deck platform (for precipitation measurement) | 007032 | Here height of precipitations |
| 75 | 004024 | Time period in hours | 004024 | Period during which precipitation is being monitored prior to observation time |
| 76 | 013011 | Total precipitation | 013011 | Total precipitation during monitoring period |
| 77 | 007032 | Height of sensor above marine deck platform (set to missing to cancel the previous value) | 007032 | Value = “missing” |
| 78 | 008021 | Time significance | 008021 | Value = 3 (accumulated) |
| 79 | 004024 | Time period in hours | 004024 | Period during which global radiation is being accumulated prior to observation time |
| 80 | 014021 | Global radiation, integrated over period specified | 014021 |  |
| 81 | 008021 | Time significance | 008021 | Value = “missing” |
| 82 | 025028 | Operator or manufacturer defined parameter (#1) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 1 |
| 83 | 025028 | Operator or manufacturer defined parameter (#2) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 2 |
| 84 | 025028 | Operator or manufacturer defined parameter (#3) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 3 |
| 85 | 022073 | Maximum wave height | 022073 |  |
| 86 | 022070 | Significant wave height | 022070 | HsHsHsHs in WAVEOB section 0 |
| 87 | 022074 | Average wave period | 022074 | PaPaPaPa in WAVEOB section 0 |
| 88 | 022076 | Direction from which dominant waves are coming | 022076 | dddd in WAVEOB section 0 |
| 89 | 022077 | Directional spread of dominant waves | 022077 | dsds in WAVEOB section 0 |
| 90 | 022071 | Spectral peak wave period | 022071 | PpPpPpPp in WAVEOB section 0 |
| 91 | 022078 | Duration of wave record | 022078 | D’D’D’D’ in WAVEOB section 1 |
| 92 | 022082 | Maximum non-directional spectral wave density | 022082 | CmCmCm in WAVEOB section 2 |
| 93 | 022084 | Band containing maximum non-directional spectral wave density | 022084 | nmnm in WAVEOB section 2 |
| 94 | 025043 | Wave sampling interval (time) | 025043 | SSSS in WAVEOB (Ia=0) |
| 95 | 025044 | Wave sampling interval (space) | 025044 | SSSS in WAVEOB (Ia=1) |
| 96 | 112000 | Delayed replication of 12 descriptors | 112000 | Replication for frequency bands. PDE buoys did not used delayed replication |
| 97 | 031001 | Replication factor | 031001 | Delayed replication therefore added. Replication factor = Number of frequency bands |
| 98 | 022080 | Waveband central frequency | 022080 | fnfnfn in WAVEOB section 1 |
| 99 | 201134 | Add 6 bits to data width | 201134 |  |
| 100 | 022096 | Spectral band width | 022096 | Here coded with 10 bits as descriptor requires 4 bits and we have 6 bits added due to previous operation descriptor |
| 101 | 201000 | Reset data width to normal | 201000 |  |
| 102 | 022090 | Non-directional spectral estimate by wave frequency | 022090 | AnAnAn in WAVEOB (Ib=0) section 5 |
| 103 | 022086 | Mean direction from which waves are coming | 022086 | da1da1 in WAVEOB section 4 |
| 104 | 022087 | Principal direction from which waves are coming | 022087 | da2da2 in WAVEOB section 4 |
| 105 | 022095 | Directional spread of individual waves | 022095 |  |
| 106 | 022085 | Spectral wave density ratio | 022085 | cncn in WAVEOB section 2 |
| 107 | 022088 | First normalized polar coordinate from Fourier coefficients | 022088 | r1r1 in WAVEOB section 4 |
| 108 | 022089 | Second normalized polar coordinate from Fourier coefficients | 022089 | r2r2 in WAVEOB section 4 |
| 109 | 022092 | Directional spectral estimate by wave frequency | 022092 | AnAnAn in WAVEOB (Ib=1) section 5 |

WAVEOB code (WMO code form FM 65-XI Ext. WAVEOB)

Wave spectrum observation from a sea station (e.g. buoy) or remote platform (aircraft or satellite).

Note: This is neither an official description of WMO GTS code forms, nor a detailed one.  For formal WMO regulations and details, see the WMO Manual on Codes, Volume 1, International Codes, WMO No 306.

In the following code descriptions,

(i)	Code fields are indicated in bold

(ii)	Each symbolic letter represents a character to encode (e.g. da1 represents one character)

(iii)	Fields are separated by one space ASCII character (i.e. ASCII code 32).

(iv)	Sections are separated by the following sequence of ASCII characters: Carriage Return, Carriage Return, Line Feed (i.e. ASCII codes 13,13,10)

(v)	Optional elements are indicated in parentheses ()

(vi)	Underlined&bold fields are constant fields or constant part of the message (e.g. 888)

1) Description of the FM 65-XI Ext. WAVEOB code:

Section 0 is mandatory, all other sections are optional. However, if one of sections 2 to 5 is present, section 1 must be included.

Section 0:	MMXX 	(D....D or A1bwnbnbnb or I6I6I6//)

YYMMJ	GGgg/

(IIiii or (QcLaLaLaLa	LoLoLoLoLo))

00IaImIp	1hhhh	2HSHSHSHS

3PpPpPpPp	(4HmHmHmHm)	(5PaPaPaPa)

(6HseHseHseHse)	(7PspPspPspPsp)	(8PsaPsaPsaPsa)

(9dddddsds)

Section 1:	(111BTBT	SSSS/	D'D'D'D'/

BB//		1f1f1f1x	1fdfdfdx	…

BB//		nfnfnfnx	nfdfdfdx)

Section 2:	(2222x	CmCmCmnmnm

1c1c1c2c2	3c3c3c4c4 … n-1cn-1cn-1cncn (or ncncn//))

Section 3:	(3333x	CsmCsmCsmnsmnsm

1cs1cs1cs2cs2	3cs3cs3cs4cs4	n-1csn-1csn-1csncsn (or ncsncsn//))

Section 4:	(4444	1da1da1da2da2	1r1r1r2r2	2da1da1da2da2	2r1r1r2r2 …

nda1da1da2da2	nr1r1r2r2 )

Section 5:	(5555Ib	1A1A1A1x	(1d1d1dsds)	1A2A2A2x	(2d2d2dsds) …

nAnAnAnx	(ndndndsds))

Each WAVEOB report should be terminated with character '='.

Explanation of fields:

Section 0

MiMiXjXj	Here coded with 4 letter “MMXX”

D....D	Ship’s call sign (ship observation only)

A1bwnbnbnb	WMO Number (WMO region, sub-area, buoy number) (sea station or remote platform, e.g. wave buoy)

I6I6I6	Satellite numeric indicator (Common code table C-5) (satellite observation only)

YYMMJ	Observation date (day of month, month, year of decade)

GGgg	Observation time (hours, minutes)

IIiii	Block number and station number (fixed sea station only)

Qc	Quadrant of the globe (1:NE, 3:SE, 5:SW, 7:NW) (sea station or remote platform)

LaLaLaLa	Latitude (degrees and minutes) (sea station or remote platform, e.g. wave buoy)

LoLoLoLoLo	Longitude (degrees and minutes) (se station or remote platform, e.g. wave buoy)

Ia	Indicator for frequency or wave number (code table 1731): 0=frequency (Hz); 1=wave number (m-1)

Im	Indicator for method of calculation of sprectral data (code table 1744): 1=Longuet-Higgins (1964); 2=Longuet Higgins (F3 method); 3=Maximum probability method; 4=Maximum entropy method.

Ip	Indocator for type of platform (code table 1747): 0=sea station; 1=buoy; 2=aeronef; 3=satellite

hhhh	Water depth (m)

HSHSHSHS	Significant wave height (cm)

PpPpPpPp	Spectral peak period derived from heave sensor

HmHmHmHm	Altitude of the level of maximum wind (1/10 of geopotential metres)

PaPaPaPa	Average wave period (1/10 s)

HseHseHseHse  	Estimate of significant wave height from slope sensor (cm)

PspPspPspPsp 	spectral peak period derived from slope sensors (1/10s) or spectral peak wave length (m)

PsaPsaPsaPsa 	Average period derived from slope sensors (1/10s) or average wave length (m)

dddd 	True direction, in units of 4 degrees, from which dominant wave is coming (code table 880) (00: 358°-2°, 01: 2°-6°, 02: 6°-10°, 89: 354°-358°)

dsds 	Directional spread, in whole degrees, of the dominant wave

Section 1

BTBT	Total number of bands described

SSSS	Sampling interval (1/10s or m)

D'D'D'D'	Duration of record of waves (s) or length of record of waves (1/10m)

BB	Number of bands described by the following two groups; BB=00 to indicate that each of the following groups represents only one central frequency or central wave number.

fnfnfnx	Centre frequency or centre wave number (x is used for exponent, see below; decimal point is supposed to be placed at left, e.g. 3004 => 0.300 10-1)

fdfdfdx	Increment to be added to previous centre frequency or previous wave number to obtain the next centre frequency or next wave number (x used for exponent, see below; decimal point is supposed to be placed at left, e.g. 3004 => 0.300 10-1).

Section 2

x	Exponent to be applied (code table 4800): exponent = 10(x-5)

CmCmCm	Maximum non-directional spectral density derived from heave sensors, in m2 Hz-1 for frequencies and m3 for wave numbers

nmnm	Number of the band in which the maximum non-directional spectral density determined by heave sensor lies

cncn 	The ratio of the spectral density derived from heave sensors for a given band, to the maximum spectral density given by CmCmCm. A code value of 00 may indicate either zero, or that the band contains the maximum spectral density. Since the band containing the maximum value will have been identified, it will be obvious which meaning should be assigned.

Section 3

CsmCsmCsm	Maximum non-directional spectral density derived from slope sensors, in m2 Hz-1 for frequencies and m3 for wave numbers

nsmnsm	Number of the band in which the maximum non-directional spectral density determined by slope sensor lies

csncsn	The ratio of the spectral density derived from slope sensors for a given band, to the maximum spectral density given by CsmCsmCsm. A code value of 00 may indicate either zero, or that the band contains the maximum spectral density. Since the band containing the maximum value will have been identified, it will be obvious which meaning should be assigned.

Section 4

da1da1	Mean direction, in units of 4 degrees, from which waves are coming for the band indicated, relative to true north (code table 880). A value of 99 indicates the energy for that band is below a given threshold.

da2da2	Principal direction, in units of 4 degrees, from which waves are coming for the band indicated, relative to true north (code table 880). A value of 99 indicates the energy for that band is below a given threshold.

r1r1	First normalized polar coordinate derived from Fourier coefficients

r2r2	Second normalized polar coordinate derived from Fourier coefficients.

Section 5

Ib	Indicator for directional or non-directional spectral wave data (code table 1732). 0: non-directional data; 1= directional data.

AnAnAn	Spectral estimations of nth frequency band or wave number (x used for exponent, see above)

dndn	True direction (rounded of to the nearest 5°), in tens of degrees, from which wind is blowing at specified levels starting with sea surface level.

dsds	Directional spread, in whole degrees, of the dominant wave. The value of the directional thread is normally less than one radian (about 57°).

Template presently being used to encode PDE buoy data in BUFR

DATA DESCRIPTORS (UNEXPANDED)

1  001005

2  002001

3  004001

4  004002

5  004003

6  004004

7  004005

8  005002

9  006002

10  010004

11  011011

12  011012

13  012004

14  022070

15  022074

16  022076

17  022071

18  002031

19  107014

20  022080

21  201134

22  022096

23  201000

24  022090

25  022086

26  022095

27  000000

28  000000

29  000000

30  000000

31  000000

32  000000

33  000000

34  000000

35  000000

36  000000

37  000000

38  000000

39  000000

40  000000

41  000000

42  000000

43  000000

44  000000

45  000000

46  000000

47  000000

48  000000

49  000000

50  000000

51  000000

52  000000

53  000000

54  000000

55  000000

56  000000

57  000000

58  000000

59  000000

60  000000

61  000000

62  000000

63  000000

64  000000

65  000000

66  000000

67  000000

68  000000

69  000000

70  000000

71  000000

72  000000

73  000000

74  000000

75  000000

76  000000

77  000000

78  000000

79  000000

80  000000

81  000000

82  000000

83  000000

84  000000

85  000000

86  000000

87  000000

88  000000

DATA DESCRIPTORS (EXPANDED)

1  001005  Buoy/platform identifier

2  002001  Type of station

3  004001  Year

4  004002  Month

5  004003  Day

6  004004  Hour

7  004005  Minute

8  005002  Latitude (coarse accuracy)

9  006002  Longitude (coarse accuracy)

10  010004  Pressure

11  011011  Wind direction at 10 m

12  011012  Wind speed at 10 m

13  012004  Dry-bulb temperature at 2 m

14  022070  Significant wave height

15  022074  Average wave period

16  022076  Direction from which dominant waves are coming

17  022071  Spectral peak wave period

18  002031  Duration and time of current measurement

19  022080  Waveband central frequency

20  022096  Spectral band width

21  022090  Non-directional spectral estimate by wave frequency

22  022086  Mean direction from which waves are coming

23  022095  Directional spread of individual waves

24  022080  Waveband central frequency

25  022096  Spectral band width

26  022090  Non-directional spectral estimate by wave frequency

27  022086  Mean direction from which waves are coming

28  022095  Directional spread of individual waves

29  022080  Waveband central frequency

30  022096  Spectral band width

31  022090  Non-directional spectral estimate by wave frequency

32  022086  Mean direction from which waves are coming

33  022095  Directional spread of individual waves

34  022080  Waveband central frequency

35  022096  Spectral band width

36  022090  Non-directional spectral estimate by wave frequency

37  022086  Mean direction from which waves are coming

38  022095  Directional spread of individual waves

39  022080  Waveband central frequency

40  022096  Spectral band width

41  022090  Non-directional spectral estimate by wave frequency

42  022086  Mean direction from which waves are coming

43  022095  Directional spread of individual waves

44  022080  Waveband central frequency

45  022096  Spectral band width

46  022090  Non-directional spectral estimate by wave frequency

47  022086  Mean direction from which waves are coming

48  022095  Directional spread of individual waves

49  022080  Waveband central frequency

50  022096  Spectral band width

51  022090  Non-directional spectral estimate by wave frequency

52  022086  Mean direction from which waves are coming

53  022095  Directional spread of individual waves

54  022080  Waveband central frequency

55  022096  Spectral band width

56  022090  Non-directional spectral estimate by wave frequency

57  022086  Mean direction from which waves are coming

58  022095  Directional spread of individual waves

59  022080  Waveband central frequency

60  022096  Spectral band width

61  022090  Non-directional spectral estimate by wave frequency

62  022086  Mean direction from which waves are coming

63  022095  Directional spread of individual waves

64  022080  Waveband central frequency

65  022096  Spectral band width

66  022090  Non-directional spectral estimate by wave frequency

67  022086  Mean direction from which waves are coming

68  022095  Directional spread of individual waves

69  022080  Waveband central frequency

70  022096  Spectral band width

71  022090  Non-directional spectral estimate by wave frequency

72  022086  Mean direction from which waves are coming

73  022095  Directional spread of individual waves

74  022080  Waveband central frequency

75  022096  Spectral band width

76  022090  Non-directional spectral estimate by wave frequency

77  022086  Mean direction from which waves are coming

78  022095  Directional spread of individual waves

79  022080  Waveband central frequency

80  022096  Spectral band width

81  022090  Non-directional spectral estimate by wave frequency

82  022086  Mean direction from which waves are coming

83  022095  Directional spread of individual waves

84  022080  Waveband central frequency

85  022096  Spectral band width

86  022090  Non-directional spectral estimate by wave frequency

87  022086  Mean direction from which waves are coming

88  022095  Directional spread of individual waves

Example of decoded data:

1 Buoy/platform i     0.6202400000E+05 NUMERIC

2 Type of station     0.0000000000E+00 CODE TABLE

3 Year                0.2005000000E+04 Year

4 Month               0.4000000000E+01 Month

5 Day                 0.1600000000E+02 Day

6 Hour                0.2300000000E+02 Hour

7 Minute              0.0000000000E+00 Minute

8 Latitude (coars     0.4363999939E+02 Degree

9 Longitude (coar    -0.3039999962E+01 Degree

10 Pressure            0.1016000000E+06 Pa

11 Wind direction      0.2760000000E+03 Degree true

12 Wind speed at 1     0.6099999905E+01 m s-1

13 Dry-bulb temper     0.2842999878E+03 K

14 Significant wav     0.2460000038E+01 m

15 Average wave pe     0.6099999905E+01 s

16 Direction from      0.3260000000E+03 Degree true

17 Spectral peak w     0.8600000381E+01 s

18 Duration and ti     0.3000000000E+01 CODE TABLE

19 Waveband centra     0.6899999827E-01 Hz

20 Spectral band w     0.1799999923E-01 s-1

21 Non-directional     0.9000000358E-01 m2 s

22 Mean direction      0.2870000000E+03 Degree true

23 Directional spr     0.5800000000E+02 Degree

24 Waveband centra     0.8100000024E-01 Hz

25 Spectral band w     0.4999999888E-02 s-1

26 Non-directional     0.5799999833E+00 m2 s

27 Mean direction      0.2810000000E+03 Degree true

28 Directional spr     0.5800000000E+02 Degree

29 Waveband centra     0.8699999750E-01 Hz

30 Spectral band w     0.8000000380E-02 s-1

31 Non-directional     0.7500000000E+00 m2 s

32 Mean direction      0.2810000000E+03 Degree true

33 Directional spr     0.5000000000E+02 Degree

34 Waveband centra     0.9300000221E-01 Hz

35 Spectral band w     0.3000000026E-02 s-1

36 Non-directional     0.4769999981E+01 m2 s

37 Mean direction      0.3040000000E+03 Degree true

38 Directional spr     0.4200000000E+02 Degree

39 Waveband centra     0.9899999946E-01 Hz

40 Spectral band w     0.9999999776E-02 s-1

41 Non-directional     0.2519999981E+01 m2 s

42 Mean direction      0.3040000000E+03 Degree true

43 Directional spr     0.4200000000E+02 Degree

44 Waveband centra     0.1089999974E+00 Hz

45 Spectral band w     0.9999999776E-02 s-1

46 Non-directional     0.5030000210E+01 m2 s

47 Mean direction      0.3090000000E+03 Degree true

48 Directional spr     0.5000000000E+02 Degree

49 Waveband centra     0.1159999967E+00 Hz

50 Spectral band w     0.4999999888E-02 s-1

51 Non-directional     0.9239999771E+01 m2 s

52 Mean direction      0.3090000000E+03 Degree true

53 Directional spr     0.5800000000E+02 Degree

54 Waveband centra     0.1239999980E+00 Hz

55 Spectral band w     0.9999999776E-02 s-1

56 Non-directional     0.5030000210E+01 m2 s

57 Mean direction      0.3260000000E+03 Degree true

58 Directional spr     0.3600000000E+02 Degree

59 Waveband centra     0.1379999965E+00 Hz

60 Spectral band w     0.1799999923E-01 s-1

61 Non-directional     0.2710000038E+01 m2 s

62 Mean direction      0.3260000000E+03 Degree true

63 Directional spr     0.5000000000E+02 Degree

64 Waveband centra     0.1580000073E+00 Hz

65 Spectral band w     0.2199999988E-01 s-1

66 Non-directional     0.2240000010E+01 m2 s

67 Mean direction      0.3260000000E+03 Degree true

68 Directional spr     0.5000000000E+02 Degree

69 Waveband centra     0.1889999956E+00 Hz

70 Spectral band w     0.3999999911E-01 s-1

71 Non-directional     0.1250000000E+01 m2 s

72 Mean direction      0.3150000000E+03 Degree true

73 Directional spr     0.5000000000E+02 Degree

74 Waveband centra     0.2380000055E+00 Hz

75 Spectral band w     0.5900000036E-01 s-1

76 Non-directional     0.4199999869E+00 m2 s

77 Mean direction      0.3090000000E+03 Degree true

78 Directional spr     0.5800000000E+02 Degree

79 Waveband centra     0.2930000126E+00 Hz

80 Spectral band w     0.5000000075E-01 s-1

81 Non-directional     0.2500000000E+00 m2 s

82 Mean direction      0.3090000000E+03 Degree true

83 Directional spr     0.5800000000E+02 Degree

84 Waveband centra     0.4090000093E+00 Hz

85 Spectral band w     0.1819999963E+00 s-1

86 Non-directional     0.7000000030E-01 m2 s

87 Mean direction      0.2980000000E+03 Degree true

88 Directional spr     0.5800000000E+02 Degree

_____________