| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, 5-8 DECEMBER 2005 |  | CT MTDCF/Doc. 5.4(3) ITEM: 5.4 (2.XII.2005) ENGLISH ONLY |
| --- | --- | --- |

Proposed BUFR template for Radiosonde data

Submitted by the Secretariat following information from UKMO

________________________________________________________________

Summary and Purpose of Document

The document contains a template wished for representation of radiosonde data by UKMO.

________________________________________________________________

ACTION PROPOSED

CBS ET/DRC is invited to discuss the proposed template, possibly suggest changes, and make an adjusted recommendation for radiosonde templates.

## Background

This document was handled to the Secretariat by Mr John Marsh, Vice-President of the CIMO Commission.  The concern of UKMO is the need to put metadata at the beginning of the report.  At least a minmum set of metadata should be agreed internationally for the beginning of the report.  At the end of the report other metadata could be included at the discrepancy of the producer.

The need to replace dew point temperature by relative humidity was expressed.  This value is more accurate than the due point, which is a calculated value.

Proposed version 1.0 (Met Office 23/11/05)

High Resolution Radiosonde BUFR (Land, Ship or Mobile)

| Table Reference | Element Name | Type & Byte Size (Bits) | Comments |
| --- | --- | --- | --- |
|  | Identification of launch site and instrumentation. |  |  |
| 0 | 01 | 001 | WMO Block Number | Numeric | 7 |  |
| 0 | 01 | 002 | WMO Station Number | Numeric | 10 |  |
| 0 | 01 | 011 | Ship or mobile land station identifier | CCITT IA5 | 72 |  |
| 0 | 02 | 011 | Radiosonde Type | Code table | 8 | Code table might need updating |
| 0 | 02 | 013 | Solar and Infrared radiation correction | Code table | 4 | Code table might need updating |
| 0 | 02 | 014 | Tracking technique/status of system used | Code table | 7 | Code table might need updating |
| 0 | 02 | 003 | Type of measuring equipment used | Code table | 4 | Code table might need updating |
| 0 | 25 | 061 | Software identification number | CCITT IA5 | 96 | Text descriptor |
| 0 | 01 | 082 | Radiosonde ascension number | Numeric | 14 |  |
| 0 | 01 | 081 | Radiosonde serial number | CCITT IA5 | 160 |  |
| 0 | 02 | 067 | Radiosonde operating frequency | Hz, Scale-5 | 15 | Frequency at Launch |
| 0 | 02 | 095 | Type of pressure sensor | Code table | 5 |  |
| 0 | 02 | 096 | Type of temperature sensor | Code table | 5 |  |
| 0 | 02 | 097 | Type of humidity sensor | Code table | 5 |  |
| 0 | 02 | 081 | Type of balloon | Code table | 5 |  |
| 0 | 02 | 082 | Weight of balloon | Kg, scale 3 | 12 |  |
| 0 | 02 | 084 | Type of gas used in balloon | Code table | 4 |  |
| ? | ?? | ??? | Geopotential height calculation | Code table | 4 | 1 – from pressure 2 – from GPS Height |
|  |  |  | Date/time of launch |  |  |  |
| 0 | 08 | 021 | Time significance | Code table | 5 | Nominal hour? |
| 0 | 04 | 001 | Year | Year | 12 |  |
| 0 | 04 | 002 | Month 3 01 011 | Month | 4 |  |
| 0 | 04 | 003 | Day | Day | 6 |  |
| 0 | 04 | 004 | Hour | Hour | 5 |  |
| 0 | 04 | 005 | Minute 3 01 013 | Minute | 6 |  |
| 0 | 04 | 006 | Second | Second | 6 |  |
|  |  |  | Horizontal and vertical coordinates of launch site. |  |  |  |
| 0 | 05 | 001 | Latitude (High Accuracy) | Degree | 25 |  |
| 0 | 06 | 001 | Longitude (High Accuracy) | Degree | 26 |  |
| 0 | 07 | 030 | Height of station above MSL | M, scale 1 | 17 |  |
| 0 | 07 | 031 | Height of barometer above MSL | M, scale 1 | 17 |  |
| 0 | 07 | 007 | Height of radiosonde release above MSL | M | 15 |  |
|  |  |  | Surface information reported with vertical sounding |  |  |  |
| 0 | 08 | 002 | Vertical significance (surface obs) | Flag | 6 |  |
| 0 | 10 | 004 | Pressure | Pa, scale -1 | 14 | Need to change scale? |
| 0 | 12 | 101 | Temperature (dry bulb) | K, scale 2 | 16 |  |
| 0 | 13 | 003 | Relative humidity | %, scale 0 | 7 |  |
| 0 | 11 | 001 | Wind Direction | Deg,scale 0 | 9 |  |
| 0 | 11 | 002 | Wind Speed | m/s, scale 1 | 12 |  |
| 0 | 08 | 002 | Vertical significance | Flag | 6 | Cloud Ob |
| 0 | 20 | 011 | Cloud amount ( low or middle Nh) | Code table | 4 |  |
| 0 | 20 | 013 | Height of base of cloud (h) | m, scale -1 | 11 |  |
| 0 | 20 | 012 | Cloud Type (Low) | Code table | 6 |  |
| 0 | 20 | 012 | Cloud Type (Medium) | Code table | 6 |  |
| 0 | 20 | 012 | Cloud Type (High) | Code table | 6 |  |
| 0 | 08 | 002 | Vertical significance (missing values) | Flag | 6 |  |
|  |  |  | Present weather? |  |  |  |
| 0 | 22 | 043 | Sea/water temp (ship stations) | K, scale 2 | 15 |  |
|  |  |  | Vertical sounding data |  |  | *Repeated section* |
| 1 | 01 | 000 | Delayed replication of 1 descriptor |  |  |  |
| 0 | 31 | 002 | Extended delayed descriptor replication factor | Numeric | 16 |  |
| 0 | 04 | 086 | Long time period or displacement (since launch time) | Second | 15 |  |
| 0 | 08 | 042 | Extended vertical sounding significance | Flag table | 18 |  |
| 0 | 10 | 009 | Geopotential height | gpm, scale0 | 17 |  |
| 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) | Degree, Scale 5 | 25 | Displacement or actual? Is resolution too much 5 decimal places? |
| 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) | Degree, Scale 5 | 26 |  |
| 0 | 12 | 101 | Temperature/dry bulb | K, scale 2 | 12 |  |
| 0 | 13 | 003 | Relative Humidity | %, scale 0 | 7 |  |
| 0 | 11 | 001 | Wind direction | Degree true | 9 |  |
| 0 | 11 | 002 | Wind Speed | m/s, scale 1 | 12 |  |

Table showing estimated BUFR message size based on above template:

(Note a typical TEMP message, ABCD, is approx. 3kbytes

|  | Header | Data | Total |
| --- | --- | --- | --- |
| 120 minute @ 1 sec. | 92 bytes | 113400 bytes | ~ 114 Kbytes |
| 120 minute @ 2 sec. | 92 bytes | 56700 bytes | ~ 57 Kbytes |
| 120 minute @ 10 sec. | 92 bytes | 11340 bytes | ~ 12 Kbytes |
| 120 minute @ 30 sec. | 92 bytes | 3780 bytes | ~ 4 Kbytes |
| 120 minute @ 60 sec. | 92 bytes | 1890 bytes | ~ 2 Kbytes |

Issues that need further discussion and agreement:

- Do we need pressure and geopotential height in repeated section?

- Should Relative Humidity be in tenths of %? (Note adding 1 decimal place adds 5 bits each repetition, approx 3 Kbytes @ 2 second resolution)

- Should we include information on the surface observation equipment?

- List of additional metadata needs to be reviewed?

- Is it possible to vary the time resolution used to code the BUFR message, using a higher resolution in the boundary layer?

- Currently we send TEMP parts A & B once the sounding has passed through 100hPa, with C & D being sent at the end of the flight. Is this still a requirement? If yes, how will this work with the BUFR message.