| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES MUSCAT, OMAN, 5 - 8 DECEMBER 2005 |  | ET DR&C/Doc. 5.5(1) (30.XI.2005) ENGLISH ONLY |
| --- | --- | --- |

## Proposed templates for encoding TAF and METAR and SPECI in BUFR

Submitted by Charles Sanders

________________________________________________________________

Summary and Purpose of Document

This document notes that the current table D descriptors do not allow all possible aviation aerodrome forecasts to be encoded, New descriptors are proposed for this purpose, together with suggested TAF and METAR templates.

________________________________________________________________

ACTION PROPOSED

The ET DR&C meeting is requested to consider the proposals.

- TAF template

New table D and table B descriptors are listed below. Many alternatives are possible, including

  - Specifying the height above ground of the forecast winds and temperature

  - Not using sequence descriptors for the forecast maximum and minimum temperatures

  - Not providing a single sequence descriptor for the entire forecast, but recommending a template consisting of the proposed contents of 3 07 fff

  - Adding the additional time significance entries in to the code table for an existing time significance descriptor instead of creating a new one.

  - Adding the forecast status entries to, or merging them with, an existing or proposed descriptor, such as the SIGMET status descriptor.

| F X Y | Reference | Element/Sequence name | TAF code group(s) |
| --- | --- | --- | --- |
|  |  | (Aerodrome forecast identification and time interval) |  |
| 3 07 aaa | 0 01 063 | ICAO location identifier | CCCC |
|  | 0 08 ddd | Time significance – Issue time |  |
|  | 3 01 011 | Year, Month, Day | YY |
|  | 3 01 012 | Hour, Minute | GGgg |
|  | 0 08 eee | Status of forecast | COR CNL AMD NIL |
|  | 3 01 011 | Year, Month, Day (start of forecast) | Y1Y1 |
|  | 3 01 012 | Hour, Minute | G1G1 |
|  | 3 01 011 | Year, Month, Day (end of forecast) | Y2Y2 |
|  | 3 01 012 | Hour, Minute | G2G2 |
|  | 3 01 024 | Latitude, Longitude, Height of station |  |
|  |  | (Forecast weather at an aerodrome) |  |
| 3 07 bbb | 0 11 001 | Wind direction | ddd |
|  | 0 11 002 | Wind speed | ff |
|  | 0 11 041 | Maximum wind speed (gusts) | fmfm |
|  | 0 20 009 | General weather indicator | CAVOK NSW NSC SKC |
|  | 3 07 014 | Weather | w’w’ |
|  | 3 07 015 | Cloud layer(s) | NsNsNshshshs |
|  |  | (Change indicator and forecast changes) |  |
| 3 07 ccc | 0 xx ggg | Probability of following event | C2C2 |
|  | 0 08 016 | Change qualifier for an aerodrome forecast | TTTTTT |
|  | 3 01 012 | Start of time change | GG GGgg |
|  | 3 01 012 | End of time change | GeGe |
|  | 3 07 bbb | Forecast conditions during or after change |  |
|  |  | (Forecast of maximum temperature) |  |
| 3 07 ddd | 0 08 ddd | Time significance (Time of maximum temperature) |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 12 111 | Maximum temperature | TFTF |
|  |  | (Forecast of minimum temperature) |  |
| 3 07 eee | 0 08 ddd | Time significance (Time of minimum temperature) |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 12 111 | Minimum temperature | TFTF |
|  |  | (Aerodrome forecast) |  |
| 3 07 fff | 3 07 aaa | Identification and time interval |  |
|  | 3 07 bbb | Forecast |  |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication factor |  |
|  | 3 07 ccc | Forecast change |  |
|  | 3 07 ddd | Maximum temperature forecast |  |
|  | 3 07 eee | Minimum temperature forecast |  |

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Reference | Width | Unit | Scale | Width |
| 0 08 ddd | Time significance (Aviation forecast) | Code table | 0 | 0 | 6 | Code table | 0 | 2 |
| 0 08 eee | Status of forecast | Code table | 0 | 0 | 4 | Code table | 0 | 1 |

| 0 08 ddd |
| --- |
| Time significance (Aviation forecast) |
| Code figure |  |
| 0 | Issue time of forecast |
| 1 | Forecast time of extreme temperature |
| 2…62 | Reserved |
| 63 | Missing |
| 0 08 eee |
| Status of forecast |
| 0 | Normal forecast |
| 1 | Correction to a previously issued forecast (COR) |
| 2 | Amendment to a previously issued forecast (AMD) |
| 3 | Correction to a previously issued amended forecast (COR AMD) ** Is this allowed ? |
| 4 | Cancellation of a previously issued forecast (CNL) |
| 5 | No forecast available (NIL) |
| 6-14 | Reserved |
| 15 | Missing |

2.  METAR and SPECI

The existing table D entries are mostly satisfactory, but the treatment of trend forecasts is incorrect. The sequence for the full METAR/SPECI, 3 07 021, allows for only one change while up to three are permitted in the TAC and the ICAO template. In addition, the forecast clouds are not included as part of the trend forecast sequence 3 08 018 but are separate.

For many of the new table B descriptors, there are two possibilities, either using a code table as the METAR and SPECI alphanumeric codes do, or using the corresponding physical values. For example, the depth of runway deposits can be reported using a code table equivalent to code table 1079, or it can be converted to metres.

However, there is no specification of whether the report is routine (METAR) or non-routine (SPECI) in the table D sequences, nor whether or not this is a correction to a previous erroneous report. If these are included, then 3 07 011 and 3 07 020 will also need to be replaced with new sequences.

| F X Y | Reference | Element/Sequence name | METAR/ SPECI Code group(s) |
| --- | --- | --- | --- |
|  |  | (Trend type forecast, replacing 3 07 018) |  |
| 3 07 kkk | 0 08 016 | Change qualifier for trend type forecast | TTTTT NOSIG |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replications (0, 1 or 2) |  |
|  | 0 08 017 | Qualifier for time of forecast change | TT |
|  | 3 01 012 | Time of change | GGgg |
|  | 1 04 000 | Delayed replication of four descriptors |  |
|  | 0 31 000 | Short delayed replication count (0 or 1) |  |
|  | 0 07 006 | Height above station (10m) |  |
|  | 0 11 001 | Wind direction | Ddd |
|  | 0 11 012 | Wind speed | Ff |
|  | 0 11 041 | Maximum wind speed (gust) | fmfm |
|  | 0 20 009 | General weather indicator | CAVOK NSW NSC SKC |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 000 | Short delayed replication count (0 or 1) |  |
|  | 0 20 001 | Horizontal visibility | VVVV |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 015 | Clouds | NsNsNshshshs |
|  |  | (Sea conditions WTsTs/SS’) |  |
| 3 07 lll | 1 02 000 | Delayed replication of 2 descriptors |  |
|  | 0 31 000 | Short delayed replication factor (0 or 1) |  |
|  | 0 22 043 | Sea/water temperature | TsTs |
|  | 0 22 021 | Height of waves | S’ |
|  |  | (Runway state RRRRERERCReReRBRBR) |  |
| 3 07 mmm | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 01 064 | Runway designator | RRRR |
|  | 0 xx vvv | General condition of runway | CLRD// SNOCLO |
|  | 0 xx www | Runway deposits | ER |
|  | 0 xx xxx | Runway contamination | CR |
|  | 0 xx yyy | Depth of runway deposits | eReR |
|  | 0 xx zzz | Runway friction coefficient | BRBR |
|  |  | (Full METAR/SPECI, replacing 3 07 021) |  |
| 3 07 nnn | 3 07 011 | Main part of METAR/SPECI data |  |
|  | 3 07 012 | Visibility | VVVVDv |
|  | 3 07 013 | Runway visual range | RDRDRVRVRVRVR |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 015 | Clouds | NsNsNshshshs |
|  | 3 07 016 | Recent weather phenomena | REw’w’ |
|  | 3 07 017 | Runway shear | WS RWYDRDR |
|  | 3 07 lll | Sea conditions | WTsTs/SS’ |
|  | 3 07 mmm | Runway state | RRRRERCReReRBRBR |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication count (0 to 3 normally) |  |
|  | 3 07 kkk | Trend type forecast |  |

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Reference | Width | Unit | Scale | Width |
| 0 xx vvv | General condition of runway | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 xx www | Runway deposits | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 xx xxx | Runway contamination | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 xx xxx | Runway contamination | % | 0 | 0 | 7 | % | 0 | 3 |
| 0 xx yyy | Depth of runway deposits | m | 3 | 0 | 12 | M | 0 | 4 |
| 0 xx zzz | Runway friction coefficient | Code table | 0 | 0 | 7 | Code table | 0 | 2 |
| 0 xx zzz | Runway friction coefficient | Numeric | 2 | 0 | 7 | 2 | 0 | 2 |

| 0 xx vvv |
| --- |
| General condition of runway |
| Code figure |  |
| 0 | Cleared (CLRD//) |
| 1 | All runways closed (SNOCLO) |
| 2…14 | Reserved |
| 15 | Missing or not applicable |
|  | 0 xx www |
|  | Runway contamination |
| Code figure |  |
| 0 | Clear and dry |
| 1 | Damp |
| 2 | Wet with water patches |
| 3 | Rime and frost covered (generally less than 0.001m) |
| 4 | Dry snow |
| 5 | Wet snow |
| 6 | Slush |
| 7 | Ice |
| 8 | Compacted or rolled snow |
| 9 | Frozen ruts or ridges |
| 10-14 | Reserved |
| 15 | Missing or not reported |
|  | 0 xx xxx |
|  | Runway contamination |
| Code figure |  |
| 0 | Reserved |
| 1 | Less than 10% of runway covered |
| 2 | 11% to 25% of runway covered |
| 3-4 | Reserved |
| 5 | 25% to 50% of runway covered |
| 6-8 | Reserved |
| 9 | 51% to 100% of runway covered |
| 10-14 | Reserved |
| 15 | Missing or not reported |
|  | 0 xx zzz |
|  | Friction co-efficient |
| 0 | 0.00 |
| 01 | 0.01 |
| 02…88 | 0.02…0.88 |
| 89 | 0.80 |
| 90 | 0.90 |
| 91 | Braking action poor |
| 92 | Braking action medium to poor |
| 93 | Braking action medium |
| 94 | Braking action medium to good |
| 95 | Braking action good |
| 96-98 | Reserved |
| 99 | Unreliable |
| 100-126 | Reserved |
| 127 | Missing, not reported, or runway not operational. |