| WORLD METEOROLOGICAL ORGANIZATION _________________________ IMPLEMENTATION COORDINATION MEETING ON THE IMPROVED MAIN TELECOMMUNICATION NETWORK (CLOUD I) WASHINGTON, 27-29 NOVEMBER 2007 |  | ICM-IMTN/Doc. 2.2 (3) (20.XI.2007) Agenda item 2 ENGLISH only |
| --- | --- | --- |

STATUS OF RTH MELBOURNE

(Submitted by RTH Melbourne)

Summary and purpose of document This document includes the report on the status of implementation of telecommunication systems and circuits at RTH Melbourne.

1.  International Links

Melbourne has GTS connections to Tokyo, Exeter and Washington. However, in support of Region V and other areas, Melbourne is also connected to several other centres. The international connections include:-

- Tokyo (Japan) - International frame relay (32kbps PVC)

- Exeter (UK) - International frame relay (64kbps PVC)

- Washington (USA) - International frame relay (16kbps PVC)

- New Delhi (India) - via Internet

- Wellington (New Zealand) - via Internet

- Singapore - International frame relay (8kbps PVC)

- Jakarta (Indonesia) - International frame relay (4kbps PVC)

- Noumea (New Caledonia) - International frame relay

- Nadi (Fiji) - International frame relay (8kbps PVC)

- Port Moresby (PNG) - via Internet

- Honiara (Solomon Islands) - via Internet

- Port Vila (Vanuatu) - via Internet

- Kuala Lumpur (Malaysia) - via Internet

- Moscow (Russia) - via Internet

- Beijing (China) - via Internet

- Male (Maldives) - via Internet

- Kuwait – via Internet

Melbourne Frame Relay access for Tokyo, Exeter, Washington, Singapore and Jakarta is 256kbps.

An alternative 256kbps Frame Relay access is provided in Brisbane, with shadow PVCs to Tokyo, Exeter, Washington and Singapore.

BT Frame Relay Network

GTS and Other International Data Links

2. International Data Exchange with RTH Melbourne

Data exchange between RTH Melbourne and other centres:-

|  | Traffic Volume per Day (MB) |
| --- | --- |
| Centre | From Melbourne to Centre |  | From Centre to Melbourne |
|  | Alpha-numeric | Binary | Charts | Other |  | Alpha-numeric | Binary | Charts | Other |
| Tokyo (Japan) | 5 | 60 | 0.7 | 40 |  | 45 | 85 | 3 | 35 |
| Exeter (UK) | 4.5 | 4 | 0.3 | 200 (non GTS) |  | 8 | 150 | 3 | 400 (non GTS) |
| Washington (USA) | 4 | 0.5 |  |  |  | 50 | 200 | 5 |  |
| New Delhi (India) | 8 |  |  |  |  | 0.8 |  |  |  |
| Wellington (New Zealand) | 20 | 200 | 15 |  |  | 0.2 |  | 0.7 |  |
| Singapore | 7.5 | 160 | 3 |  |  | 0.4 |  |  | 6.5 |
| Jakarta (Indonesia) | 5 | 9 | 17 |  |  | 0.15 |  |  |  |
| Noumea (New Caledonia) | 25 |  |  |  |  | 0.6 |  |  |  |
| Nadi (Fiji) | 8 | 14 |  |  |  | 0.1 |  |  |  |
| Port Moresby (PNG) | Not operational |  |  |
| Honiara (Solomon Islands) | Not operational |  |  |
| Port Vila (Vanuatu) | 0.6 | 35 |  |  |  | 0.02 |  |  |  |
| Kuala Lumpur (Malaysia) | 9 | 7 | 0.6 | 25 |  | 0.05 |  |  |  |
| Moscow (Russia) | 5 |  |  |  |  | 13 |  |  |  |
| Beijing (China) | 2 | 0.1 |  |  |  | 300 |  |  |  |
| Male (Maldives) | 6 |  |  |  |  | 0.03 |  |  |  |
| Kuwait |  |  |  |  |  | 0.8 |  |  | 65 |
| ECMWF |  |  |  |  |  |  |  |  | 800 |
| Canada |  |  |  |  |  |  |  |  | 150 |
| Germany |  |  |  |  |  |  |  |  | 5 |

3. Bureau of Meteorology’s Position Regarding Cloud I and Cloud II

In a recent WMO survey for WIS implementation, the Bureau of Meteorology in Australia nominated itself as interested in being a Global Information System Centre (GISC).

However, as the Bureau also supports a number of centres in Region V and other regions, the cost of providing this service is one of many major considerations. The Bureau will need to carefully assessing the infrastructure, storage, communications, support and financial implications as the requirements and services become clearer.

The Bureau of Meteorology believes that with the introduction of WIS there is a need to have a single private network (ie. a singler cloud) between centres to allow the “any to any” connectivity required by WIS. It is understood that the GISCs will not necessarily store all of the data, but rather the metadata and directory information. The Bureau is also keenly interested in how the smaller centres might be included in the cloud.