| WORLD METEOROLOGICAL ORGANIZATION _________________________ REGIONAL ASSOCIATION II IMPLEMENTATION-CO-ORDINATION MEETING ON WIS AND GTS IN RA II Khabarovsk, 10-12 September 2007 | RA II/ICM-GTS Doc. 2, 1 (7.VIIII.2007) ____________ ITEM 2.1 ENGLISH only |
| --- | --- |

STATUS OF IMPLEMENTATION AT RTH BANGKOK

(Submitted by Kumpol Luengpetgnarm, RTH Bangkok)

Summary and purpose of document This document provides information on the status of Implementation of systems, circuits and future plan at RTH Bangkok.

CURRENT STATUS OF IMPLEMENTATION AT RTH BANGKOK

The new Message Switching System (MSS) and the Real-time Meteorologicall Databank of  RTH Bangkok  started fully operation in November 2006. Subsequently, considering TCP/IP strategy and guide on the use of TCP/IP on the GTS.  All low speed GTS circuits have been planed to upgrade by using cost-effective protocol  in very near future. The current status of implementation at RTH Bangkok is as follow :

| Circuits | Speed | Protocol | Exchange data type |
| --- | --- | --- | --- |
| Bangkok-Tokyo | CIR:BK 16/16 TK Port: BK=128 Kbps TK=192 Kbps | TCP/IP Socket | Message (A/N, Binary) |
| Bangkok-Beijing | 9.6 Kbps | X.25 PVC | Message (A/N) |
| Bangkok-New Delhi | 200 bps | Asynchronous | Message (A/N) |
| Bangkok-Kuala Lumpur | CIR:BK 16/16 KL Port: BK=128 Kbps KL= 64 Kbps | TCP/IP Socket | Message (A/N, Binary) |
| Bangkok-Hanoi | 1.2 Kbps | Asynchronous | Message (A/N) |
| Bangkok-Vientiane | 64 Kbps | TCP/IP Socket FTP | Message (A/N, Binary) |
| Bangkok-Jeddah | 75 bps | Asynchronous | Message (A/N) |
| Bangkok-Singapore | 2.4 Kbps | X.25 PVC | Message (A/N,Bibary) |
| Bangkok-Yangon | 50 bps | Asynchronous | Message (A/N) |
| Bangkok-Phnom Penh | Internet | VPN via Internet | Message(A/N,Binary) |

Future development at RTH Bangkok

According  to WMO plan  for making the GTS fulling operation in all Ocean rim countries to support the TWS, RTH Bangkok plans to upgrade the following inter-regional and regionall circuits to cost-effective connections such as TCP/IP  protocol.

| Circuits | Speed | Protocol | Remarks |
| --- | --- | --- | --- |
| Bangkok-New Delhi | 64 Kbps | TCP/IP Socket | Target: Before the end of 2007 |
| Bangkok-Beijing | 64 Kbps | TCP/IP Socket | Target: Before the end of 2007 |
| Bangkok-Yangon | Internet | VPN via Internet | Target : in October 2007 |
| Bangkok-Jeddah | 64 Kbps | TCP/IP Socket | Target: within early 2008 |

GTS facilities at RTH Bangkok

RTH Bangkok has installed a new message switching system to replace the old one that operated since 1995, in order to increase the higher performance and capacity to meet the requirement for RTHs and NMCs.  The current new systems handle the use of all protocols of data transmission recommended by WMO standard procedure. The new system included various protocols such as:

- Asynchronous

- X.25

- TCP/IP Frame Relay, IP-VPN

- FTP

- Using E-mail via internet

The draft diagram for RTH Bangkok network is as follow:

TCP/IP Connections at RTH Bangkok

RTH Bangkok also considered the concept of an improved RMTN using modern cost-effective data-communication network services. But sometimes the design of the improved RMTN could be based on the implementation of several networks grouping RTHs and NMCs as appropriate.   However the cost-effective data network services such as TCP/IP, IP-VPN services  should be available and provided more for GTS connections in the region II.

----------------------------------------------