| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc. 2.3 (1) (22.VI.2010) ------------------------- ITEM 2.3 ENGLISH ONLY |
| --- | --- | --- |

### Encoding Wave spectra in GRIB Edition 2

# Submitted by Thomas Bruns, Sibylle Krebber (DWD)

________________________________________________________________

# Summary and Purpose of Document

This document contains a proposal for the addition of a new GRIB2 template for "Analysis or Forecast of Wave Parameters at the Sea Surface at a point in time", the substitution of Product Definition Template 4.50 with "Analysis or Forecast of Wave Parameters at the Sea Surface", a new code table and new code table entries.

_________________________________________________________________

# ACTION PROPOSED

# The meeting is requested to review the document and approve

the contents for validation.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

### Background and discussion

The issue of how to encode wave spectra in GRIB Edition 2 was discussed in 2008 between ECMWF and DWD wave experts and a template was proposed for the "Analysis or forecast of a multi component parameter or matrix element at a point in time". However, the proposal of the list of parameter was withdrawn because it seemed to be not very seminal and it was decided to discuss and consider this issue again.

The following proposals are an outcome of further discussion and careful consideration of the wave experts within DWD.

These proposals are put up for discussion to get a general accepted regulation how to encode wave data in GRIB2.

#### Proposals

# Product Definition Template 4.50

# Change

# Product Definition Template 4.50:    Analysis or forecast of a multi component parameter or matrix element at a point in time  - for validation

# in

# Product Definition Template 4.50:    Analysis or forecast of spectral ocean wave energy at a given direction and frequency at a point in time.

| Octet | Contents |
| --- | --- |
| 10 | Parameter category (see Code Table 4.1). |
| 11 | Parameter number (see Code Table 4.2). |
| 12 | Type of Ocean Wave Spectral Partitioning (see Code Table 4.225). |
| 13 | Type of generating process (see Code Table 4.3) |
| 14 | Background generating process identifier (defined by originating centre) |
| 15 | Analysis or forecast generating processes identifier (defined by originating centre) |
| 16-17 | Hours of observational data cutoff after reference time (see Note 1) |
| 18 | Minutes of observational data cutoff after reference time |
| 19 | Indicator of unit of time range (see Code Table 4.4) |
| 20-23 | Forecast time in units defined by octet 18 |
| 24 | First dimension physical significance (Code Table 5.3) (see Note 2) |
| 25 | Second dimension physical significance (Code Table 5.3) (see Note 2) |
| 26-29 | First dimension coordinate value (IEEE 32-bit floating-point value) |
| 30-33 | Second dimension coordinate value (IEEE 32-bit floating-point value) |
| 34-35 | First dimension (rows) of the complete matrix (see Note 3) |
| 36-37 | Second dimension (columns) of the complete matrix (see Note 3) |

Note:

(1)   Hours greater than 65534 will be coded as 65534.

(2)  According to Code Table 5.3, the physical significance values are 1 (Direction Degrees true) and 2 (Frequency (s-1).

(3) The dimensions define the number of GRIBs needed for reconstruction of a complete matrix (e.g. wave spectrum) at one or more grid points. In case of 1-dim-spectra, the second dimension must be set to 1 and the second dimension physical significance must be set to 255 (missing).

# New Product Definition Template for Wave Parameters

# Product Definition Template 4.52:  Analysis or Forecast of Wave Parameters at the Sea Surface at a point in time

| Octet | Contents |
| --- | --- |
| 10 | Parameter category (see Code Table 4.1). |
| 11 | Parameter number (see Code Table 4.2). |
| 12 | Type of Ocean Wave Spectral Partitioning (see Code Table 4.225). |
| 13 | Type of generating process (see Code Table 4.3) |
| 14 | Background generating process identifier (defined by originating centre) |
| 15 | Analysis or forecast generating processes identifier (defined by originating centre) |
| 16-17 | Hours of observational data cutoff after reference time (see Note 1) |
| 18 | Minutes of observational data cutoff after reference time |
| 19 | Indicator of unit of time range (see Code Table 4.4) |
| 20-23 | Forecast time in units defined by octet 18 |

Note:

# Hours greater than 65534 will be coded as 65534.

#### Entries in Code Table 4.0:  Product Definition Template Number

#### 50 	Analysis or forecast of spectral ocean wave energy at a given direction 
and frequency at a point in time

#### 52	Analysis or Forecast of Wave Parameters at the Sea Surface at a point in time

#### New Code table for the Type of Ocean Wave Spectral Partitioning

#### Code Table 4.225: Type of Ocean Wave Spectral Partitioning

| Code figure | Meaning |
| --- | --- |
| 0 | Total Spectrum |
| 1 | Wind Sea |
| 2 | Total Swell |
| 3 | Primary Swell |
| 4 | Secondary Swell |
| 5 | Primary Waves (without consideration of wind) |
| 6 | Secondary Waves (without consideration of wind) |
| 7-191 | Reserved |
| 102-254 | Reserved for local use |
| 255 | Missing |

#### New entries in Code Table 4.2

Product discipline 10:	Oceanographic products, Parameter category 0:	Waves

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | 2-dim Spectral Energy Density E(f,θ) | m²s |
| 1 | Frequency Spectral Energy Density E(f) = ∫E(f,θ)dθ | m²s |
| 2 | Directional Spectral Energy Density E(θ)= ∫E(f,θ)df / m0 | - |
| 3 | Significant Height of Combined Wind Waves and Swell [DEPRECATED] | m |
| 4 | Direction of Wind Waves [DEPRECATED] | Degree true |
| 5 | Significant Height of Wind Waves [DEPRECATED] | m |
| 6 | Mean Period of Wind Waves [DEPRECATED] | s |
| 7 | Direction of Swell Waves [DEPRECATED] | Degree true |
| 8 | Significant Height of Swell Waves [DEPRECATED] | m |
| 9 | Mean Period of Swell Waves [DEPRECATED] | s |
| 10 | Primary Wave Direction [DEPRECATED] | Degree true |
| 11 | Primary Wave Mean Period [DEPRECATED] | s |
| 12 | Secondary Wave Direction [DEPRECATED] | Degree true |
| 13 | Secondary Wave Mean Period [DEPRECATED] | s |
| 14 | Direction of Combined Wind Waves and Swell [DEPRECATED] | Degree true |
| 15 | Mean Period of Combined Wind Waves and Swell [DEPRECATED] | s |
| 16-19 | Reserved |  |
|  | Wave Heights |  |
| 20 | Significant Wave Height HS = 4 √ m0 | m |
| 21 | Significant wave u-component | m |
| 22 | Significant wave v-component | m |
| 23 | Significant Height of Waves with Periods below 10s | m |
| 24 | Significant Height of Waves with Periods below 12s | m |
| 25-29 | Reserved |  |
|  | Directions |  |
| 30 | Wave Direction (of the Spectral Peak) | Degree true |
| 31 | Wave Spectral Directional Width | - |
| 32 | Directional Spreading σ² = ∫ [2sin(θ/2) ]² E(θ) dθ | - |
| 33-39 | Reserved |  |
|  | Periods |  |
| 40 | Mean (Energy) Wave Period (Tm-10) | s |
| 41 | Wave Period (Tm01) (corresponding to the Mean Frequency) | s |
| 42 | Mean Wave Period (Tm02) (corresponding to the Mean Zero-Downcrossing Period Tz) | s |
| 43 | Peak Wave Period | s |
| 44 | Peak Period of 1D-Frequency Spectra | s |
| 45-49 | Reserved |  |
|  | Other Characteristics |  |
| 50 | Wave Steepness | - |
| 51 | Mean Square Slope | - |
| 52 | Kurtosis of Sea Surface Elevation | - |
| 53 | Peakedness (after Goda) | - |
| 54 | Benjamin-Feir-Index | - |
| 55 | Maximum Height of an Individual Wave | m |
| 56 | Period of Maximum Individual Wave | s |
| 57-59 | Reserved |  |
|  | Wind Forcing Parameters on the Wave Model Grid |  |
| 60 | Wind Velocity | m/s |
| 61 | Wind Direction | ° |
| 62 | U-Component | m/s |
| 63 | V-Component | m/s |
| 64 | Friction Velocity u* | m/s |
| 65 | Drag Coefficient CD | - |
| 66 | Wave Stress Τ | N/m² |
| 67-69 | Reserved |  |
|  | Wave Induced Currents |  |
| 70 | Stokes Drift | m/s |
| 71 | Stokes Drift u-component | m/s |
| 72 | Stokes Drift v-component | m/s |
| 73-79 | Reserved |  |
|  | Wave Measurements |  |
| 80 | Gridded Altimeter Wave Height | m |
| 81 | Gridded corrected Altimeter Wave Height | m |
| 82 | Gridded Altimeter Range Relative Correction | - |
| 82-99 | Reserved |  |
| 100 | Log-10-based 2-dim Spectral Energy Density E(f,θ) | - |
|  | Spectral Source Terms Si(f,θ) of the Energy Balance Equation |  |
| 101 | Wind Input Source Term | m²s |
| 102 | Quadruplet Wave-Wave Interaction Source Term | m²s |
| 103 | Triad Wave-Wave Interaction Source Term | m²s |
| 104 | White-Capping Dissipation Source Term | m²s |
| 105 | Swell Dissipation Source Term | m²s |
| 106 | Surf Breaking Dissipation Source Term | m²s |
| 107 | Bottom Friction Dissipation | m²s |
| 108 | Bottom Scattering Source Term | m²s |
| 109 | Reserved |  |
|  | Moments of the Spectrum E mn = ∫ fn E(f) df |  |
| 110 | 0’th order Moment m0 | m² |
| 111 | 1’th order Moment m1 | m²/s |
| 112 | 2’th order Moment m2 | m²/s² |
| 113 | 3’th order Moment m3 | m²/s³ |
| 114 | 4’th order Moment m4 | m²/s4 |
| 115 | 1’th order negative Moment m-1 | m²s |
| 116 | 2’th order negative Moment m-2 | m²s² |
| 117-254 | Reserved |  |
| 255 | Missing |  |

Note:

- The Spectrum may be a partition of a total Spectrum, see Code Table 4.2xx.

- Wave Energy normalized by ρg, directional bins are *degree true*, i.e. oceanographic convention