| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST – 3 SEPTEMBER 2010 |  | IPET-DRC-Ii / Doc. 2.3 (4) (12.VII. 2010) ------------------------- ITEM 2.3 ENGLISH ONLY |
| --- | --- | --- |

GRIB Variable GRID Definition Templates

Submitted by Richard Weedon (UKMO)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for two templates designed to define variable resolution GRIDS.

_________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve

the contents for preoperational implementation once validated.

BACKGROUND AND DISCUSSION

The Met Office produces data on variable resolution grids, such as our UKV domain. These grids have rows of constant latitude and columns of constant longitude, each with irregular spacing. We wish to store the latitude of every row and the longitude of every column, and propose two new Grid Definition Templates to store such fields.

PROPOSAL

New table entries in code table 4.0:

Code Table 3.1:		Grid Definition Template Number

Number		Meaning					Comments

4	Variable resolution latitude/longitude

5	Variable resolution rotated latitude/longitude

New Grid Definition Templates

Grid Definition Template 3.4: 	Variable resolution latitude/longitude

Octet Number(s)		Contents

15 	Shape of the earth (see Code Table 3.2)

16  	Scale factor of radius of spherical earth

17-20 	Scaled value of radius of spherical earth

21 	Scale factor of major axis of oblate spheroid earth

22-25 	Scaled value of major axis of oblate spheroid earth

26 	Scale factor of minor axis of oblate spheroid earth

27-30 	Scaled value of minor axis of oblate spheroid earth

31-34 	Ni - number of points along a parallel

35-38 	Nj - number of points along a meridian

39-42 	Basic angle of the initial production domain (see Note 1)

43-46 	Subdivisions of basic angle used to define extreme longitudes and latitudes, and direction increments

(see Note 1)

47 	Resolution and component flags (see Flag Table 3.3)

48 	Scanning mode (flags see Flag Table 3.4)

49-ii 	List of longitude for each grid column (see Note 1)

(ii+1)-jj 	List of latitudes for each grid row (see Note 1)

Notes: 	(1) 	Basic angle of the initial production domain and subdivisions of this basic angle are provided to

manage cases where the recommended unit of 10-6 degrees is not applicable to describe the extreme

longitudes and latitudes, and direction increments. For these last six descriptors, unit is equal to the

ratio of the basic angle and the subdivisions number. For ordinary cases, zero and missing values

should be coded, equivalent to respective values of 1 and 106 (10-6 degrees unit).

(2)	The resolution flag (bit 3-4 of Flag table 3.3) is not applicable.

(3) 	The list of longitudes and latitudes shall be coded in the octets immediately following the Grid

Definition Template (Octets 49 – nn and octets nn+1 – mm respectively).

(4) 	A scaled value of radius of spherical Earth, or major or minor axis of oblate spheroid Earth is derived

from applying appropriate scale factor to the value expressed in metres.

(5)	For the list of Ni longitudes and Nj latitudes is at the end of the section :

ii = 49 + Ni and jj = ii + 1 + Nj

Grid Definition Template 3.5: 	Variable resolution rotated latitude/longitude

15-48 	Same as grid definition template 3.4 (see Note 1)

49-52 	Latitude of the southern pole of projection

53-56 	Longitude of the southern pole of projection

57-60 	Angle of rotation of projection

61-ii 	List of longitude for each grid column (see Note 1)

(ii+1)-jj 	List of latitudes for each grid row (see Note 1)

Notes:	(1) 	Basic angle of the initial production domain and subdivisions of this basic angle are provided to

manage cases where the recommended unit of 10–6 degrees is not applicable to describe the extreme

longitudes and latitudes, and direction increments. For these last six descriptors, the unit is equal to

the ratio of the basic angle and the subdivisions number. For ordinary cases, zero and missing values

should be coded, equivalent to respective values of 1 and 106 (10–6 degrees unit).

(2) 	Three parameters define a general latitude/longitude coordinate system, formed by a general rotation

of the sphere. One choice for these parameters is:

(a)	The geographic latitude in degrees of the southern pole of the coordinate system, e.g θp;

(b) 	The geographic longitude in degrees of the southern pole of the coordinate system, e.g λp;

(c) 	The angle of rotation in degrees about the new polar axis (measured clockwise when

looking from the southern to the northern pole) of the coordinate system, assuming the new

axis to have been obtained by first rotating the sphere through λp degrees about the

geographic polar axis, and then rotating through (90 + θp) degrees so that the southern pole

moved along the (previously rotated) Greenwich meridian.

(3)	For the list of Ni longitudes and Nj latitudes is at the end of the section :

ii = 61 + Ni and jj = ii + 1 + Nj