| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST-3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc.3.3(11) (29.VII.2010) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Validation of EUCOS BUFR template for representation of radiosonde data

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains information on validation of the EUCOS

BUFR template for representation of radiosonde data with geopotential height as the vertical coordinate and a proposal for code table 0 02 191.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] Final Report, Joint meeting of ET DR&C and CT MTDCF, Montreal, 8 - 12 May 2006

[3] Final Report, Meeting of Expert Team on Data Representation and Codes, Darmstadt,

23 - 27 April 2007

[4] Final Report, Joint meeting of ET DR&C and CT MTDCF, Geneva, 1 - 5 September 2008

1. Background

The Joint meeting of ET DR&C and CT MTDCF (Montreal, 8 – 12 May 2006) reviewed a proposal for “HIGH RESOLUTION RADIOSONDE BUFR (LAND, SHIP OR MOBILE)” template which introduction had been coordinated by EUCOS, and suggested several changes to it. A new version of the EUCOS template, suitable for representation of high resolution radiosonde data with geopotential height as the vertical coordinate was submitted to the Meeting of Expert Team on Data Representation and Codes (Darmstadt, 23 to 27 April 2007) and recommended for validation. The Joint meeting of ET DR&C and CT MTDCF (Geneva, 1 - 5 September 2008) agreed on removal of 0 02 191 (Geopotential height calculation) from the EUCOS template and keeping this new version of the template for validation.

2. Validation of the EUCOS template

In February 2010, the UK MetOffice produced three BUFR samples of radiosonde data described by the 2007 version of EUCOS template, i.e. 0 02 191 (Geopotential height calculation) being included. All comments provided on these samples were accepted by the UK MetOffice with the exception of the suggestion for deleting of 0 02 191. During the following discussion, Mr. Alexander Kats (Russian Federation) supported re-introducing of 0 02 191 requesting a new code figure for “Geopotential height calculated from radar height”. This additional requirement justifies the existence of 0 02 191, because 0 07 009 (Geopotential height) would be used as the vertical coordinate for geopotential height calculated from GPS height as well as from radar height.

3. Proposal for code table 0 02 191

A new code table for “Geopotential height calculation” is proposed for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 02 191 | Geopotential height calculation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Code table 0 02 191

Geopotential height calculation

|  | Geopotential height calculation |
| --- | --- |
| Code figure |  |
| 0 | Geopotential height calculated from pressure |
| 1 | Geopotential height calculated from GPS height |
| 2 | Geopotential height calculated from radar height |
| 3 - 14 | Reserved |
| 15 | Missing value |

0 02 191 has been re-introduced into the EUCOS template as shown in the revisited version of the template below.

It is to be noted, however, that representation of radiosonde data using template TM 309052 does not require inclusion of 0 02 191 even as an additional parameter. TM 309052 contains 0 07 004 (Pressure) and 0 10 009 (Geopotential height) and it is obvious that pressure is the vertical coordinate and that geopotential height is derived (calculated) from pressure.

4.  EUCOS template for representation of radiosonde data with geopotential height as the vertical coordinate (revisited in July 2010)

This template is suitable for representation of high resolution radiosonde data with geopotential height as the vertical coordinate, the vertical resolution being limited by the length of BUFR message.

| 3 01 111 |  | Identification of launch site and instrumentation |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 0 25 061 |  | Software identification and version number | CCITT IA5 |
| 0 01 081 |  | Radiosonde serial number | CCITT IA5 |
| 0 01 082 |  | Radiosonde ascension number | Numeric |
| 0 02 067 |  | Radiosonde operating frequency | Hz, scale -5 |
| 0 02 095 |  | Type of pressure sensor | Code table |
| 0 02 096 |  | Type of temperature sensor | Code table |
| 0 02 097 |  | Type of humidity sensor | Code table |
| 0 02 081 |  | Type of balloon | Code table |
| 0 02 082 |  | Weight of balloon | kg, scale 3 |
| 0 02 084 |  | Type of gas used in balloon | Code table |
| 0 02 191 |  | Geopotential height calculation | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Surface station measurements |  |
| 0 10 004 |  | Pressure | Pa, scale –1 |
| 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, scale 2 |
|  | 0 12 101 | Temperature/dry-bulb temperature(scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 13 003 | Relative humidity | % |
| 0 07 032 |  | Height of sensor above local ground (for wind measurement) | m, scale 2 |
| 0 02 002 |  | Type of instrumentation for wind measurement | Flag table |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
| 0 20 003 |  | Present weather | Code table |
| 3 02 049 |  | Cloud information reported with vertical soundings |  |
|  | 0 08 002 | Vertical significance | Code table |
|  | 0 20 011 | Cloud amount (of low or middle clouds Nh) | Code table |
|  | 0 20 013 | Height of base of cloud (h) | m, scale –1 |
|  | 0 20 012 | Cloud type (low clouds CL) | Code table |
|  | 0 20 012 | Cloud type (middle clouds CM) | Code table |
|  | 0 20 012 | Cloud type (high clouds CH) | Code table |
|  | 0 08 002 | Vertical significance ( = missing value) | Code table |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Temperature, dew-point, relative humidity and wind data at height levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 055 |  | Temperature, dew-point, relative humidity and wind data at a height level with radiosonde position |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 13 009 | Relative humidity (see Note 4) | %, scale 1 |
|  | 0 12 103 | Dew-point temperature (scale 2) (see Note 4) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |

Notes:      (1)	Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

- Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds).

- Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

- If the radiosonde is equipped with a relative humidity sensor, 0 13 009 shall be reported as mandatory and dew-point temperature may be included as a derived value. If the radiosonde is equipped with a dew-point temperature sensor, 0 12 103 shall be reported and 0 13 009 shall be set to a missing value.