| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc. 3.3(14) (29.VII.2010 ) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for ATMS data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

The document proposes new BUFR Table B and Table D descriptors for representing ATMS data

________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the contents for pre-operational implementation.

Background

The ATMS (Advanced Technology Microwave Sounder) instrument is part of the next generation operational sensor suite selected to fly on the National Polar-Orbiting Operational Environmental Satellite System (NPOESS) spacecraft.   Sounding data from this instrument, when combined together with CrIS (Cross-Track Infrared Sounder) and VIIRS (Visible/Infrared Imager Radiometer Suite) data attached to the same satellite, will support continuing advances in NWP (Numerical Weather Prediction) models to improve short and medium-range weather forecasts.  At the first meeting of the IPET-DRC (Geneva, September 2009), NCEP presented an initial proposal for new BUFR Table B and Table D descriptors to support this effort.  This was agenda item 3.3.8.  Subsequent feedback was received from ECMWF and EUMETSAT as well as the CGMS Task Force on Satellite Data and Codes.  Sample ATMS data encoded according to the following proposal was then made available for validation on a NESDIS ftp server.   We would now like to request pre-operational approval for these new descriptors.

Proposal

#### (1) Add new Table D entry:

|  |  | ATMS (Advanced Technology Microwave Sounder) data |
| --- | --- | --- |
| 3 10 061 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 01 034 | Identification of originating/generating sub-center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 0 33 079 | Granule level quality flags |
|  | 0 33 080 | Scan level quality flags |
|  | 0 33 078 | Geolocation quality |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 25 075 | Satellite antenna corrections version number |
|  | 1 11 000 | Delayed replication of 11 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 0 05 042 | Channel number |
|  | 2 02 131 | Increase scale by 3 |
|  | 0 02 153 | Satellite channel center frequency |
|  | 0 02 154 | Satellite channel band width |
|  | 2 02 000 | Cancel increase scale |
|  | 0 02 104 | Antenna polarization |
|  | 0 12 066 | Antenna temperature |
|  | 0 12 163 | Brightness temperature |
|  | 0 12 158 | Noise-equivalent delta temperature while viewing cold target |
|  | 0 12 159 | Noise-equivalent delta temperature while viewing warm target |
|  | 0 33 081 | Channel data quality flags |

#### (2) Add new Table B entries:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 12 066 | Antenna temperature | K | 2 | 0 | 16 | C | 2 | 5 |
| 0 12 158 | Noise-equivalent delta temperature while viewing cold target | K | 2 | 0 | 12 | C | 2 | 4 |
| 0 12 159 | Noise-equivalent delta temperature while viewing warm target | K | 2 | 0 | 12 | C | 2 | 4 |
| 0 33 078 | Geolocation quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 33 079 | Granule level quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 080 | Scan level quality flags | Flag table | 0 | 0 | 20 | Flag table | 0 | 7 |
| 0 33 081 | Channel data quality flags | Flag table | 0 | 0 | 12 | Flag table | 0 | 4 |

(3) Add the following new code table entries to existing BUFR/CREX Table B descriptors:

0 02 104  (Antenna polarization)

6	Quasi horizontal polarization

7	Quasi vertical polarization

(4) Code/Flag tables for proposed new Table B descriptors:

0 33 078  Geolocation quality

| Code figure | Meaning |
| --- | --- |
| 0 | Nominal – altitude and Ephemeris data available |
| 1 | Missing at most a small gap of altitude and Ephemeris data |
| 2 | Missing more than a small gap of altitude and Ephemeris data, but no more than a granule boundary |
| 3 | Missing more than a granule boundary of altitude and Ephemeris data |
| 4-14 | Reserved |
| 15 | Missing |

0-33-079  Granule level quality flags

| Bit | Meaning |
| --- | --- |
| 1-5 | Reserved |
| 6 | The No. 1-No.7 health checks failed |
| 7 | The No. 8-No.15 health checks failed |
| 8 | The No. 16-No.23 health checks failed |
| 9 | The No. 24-No.31 health checks failed |
| 10 | The No. 32-No.39 health checks failed |
| 11 | The No. 40-No.47 health checks failed |
| 12 | The No. 48-No.55 health checks failed |
| 13 | The No. 56-No.63 health checks failed |
| 14 | The No. 64-No.70 health checks failed |
| 15 | Quadratic correction applied to the radiometric transfer function for non-linearity correction |
| All 16 | Missing value |

0-33-080  Scan level quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Divide-by-zero condition or computation loop failed to converge in the K/Ka and V (KAV) Band PRT |
| 8 | Divide-by-zero condition or computation loop failed to converge in the WG Band PRT |
| 9 | Divide-by-zero condition or computation loop failed to converge in the K/Ka, V, W, G Band Receiver Shelf PRT K temperature computation |
| 10 | Out of range condition for the K/Ka and V Band PRT |
| 11 | Out of range condition for the WG Band PRT |
| 12 | KAV PRT temperature inconsistency |
| 13 | WG PRT temperature inconsistency |
| 14 | Time Sequence Error |
| 15 | Data Gap - Missing scan(s) preceding the current scan |
| 16 | KAV PRT Sufficiency - Insufficient KAV PRT data are available |
| 17 | WG PRT Sufficiency - Insufficient WG PRT data are available |
| 18 | Space View antenna position error |
| 19 | Blackbody antenna position error |
| All 20 | Missing value |

0-33-081  Channel data quality flags

| Bit | Meaning |
| --- | --- |
| 1-2 | Reserved |
| 3 | Moon in Space View |
| 4 | Gain Error - The lowest blackbody count is smaller than or equal to the highest space view count in a scan |
| 5 | Calibration With Fewer Than Preferred Samples |
| 6 | Space View Data Sufficiency Check - Insufficient space view samples are available |
| 7 | Blackbody View Data Sufficiency Check - Insufficient blackbody view samples are available |
| 8 | Out of range condition for the Space View |
| 9 | Out of range condition for the BlackBody View |
| 10 | Space view inconsistency |
| 11 | BlackBody view inconsistency |
| All 12 | Missing value |

(5) Add the following new entry to Common Code Table C-13:

Under Data Category 021 = Radiances (satellite measured), add the following new International Data Sub-Category entry:

| 006 | Advanced technology microwave sounder |
| --- | --- |