| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc. 3.3(16) (29.VII.2010 ) ------------------------- ITEM3.3 ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for VIIRS data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

The document proposes new BUFR Table B and Table D descriptors for representing VIIRS data

________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the contents for pre-operational implementation.

Background

The VIIRS (Visible/Infrared Imager Radiometer Suite) instrument is part of the next generation operational sensor suite selected to fly on the National Polar-Orbiting Operational Environmental Satellite System (NPOESS) spacecraft.   Sounding data from this instrument, when combined together with CrIS (Cross-Track Infrared Sounder) and ATMS (Advanced Technology Microwave Sounder) data attached to the same satellite, will support continuing advances in NWP (Numerical Weather Prediction) models to improve short and medium-range weather forecasts.  The following proposal has been reviewed by colleagues from UKMO, Canada, ECMWF and EUMETSAT as well as the CGMS Task Force on Satellite Data and Codes.  Sample VIIRS data was also made available for validation on a NESDIS ftp server.   We would now like to request pre-operational approval for these new BUFR Table B and Table D descriptors.

Proposal

#### (1) Add new Table D entry:

|  |  | VIIRS (Visible/Infrared Imager Radiometer Suite) data |
| --- | --- | --- |
| 3 10 062 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 01 034 | Identification of originating/generating sub-center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 2 01 133 | Increase bit width |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 08 076 | Type of band |
|  | 0 33 082 | Geolocation quality flags |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 072 | Pixel(s) type |
|  | 0 08 029 | Remotely sensed surface type |
|  | 1 05 000 | Delayed replication of 5 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 0 05 042 | Channel number |
|  | 0 02 155 | Satellite channel wavelength |
|  | 0 33 083 | Radiance data quality flags |
|  | 0 14 043 | Channel radiance |
|  | 0 15 042 | Reflectance |

#### (2) Add new Table B entries:

| Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 02 155 | Satellite channel wavelength | m | 9 | 0 | 16 | m | 9 | 5 |
| 0 14 043 | Channel radiance | W m**-2 sr**-1 um**-1 | 4 | 0 | 23 | W m**-2 sr**-1 um**-1 | 4 | 7 |
| 0 15 042 | Reflectance | % | 2 | 0 | 14 | % | 2 | 5 |
| 0 33 082 | Geolocation quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 083 | Radiance data quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |

(3) Add the following note to Class 14 of Table B:

(7)	Channel radiance (014043) uses um to represent the wave number.

(4) Add the following new code table entries to existing BUFR/CREX Table B descriptors:

0 08 076  (Type of band)

5           M-band

6           I-band

7           Day/Night Band

0 08 072  (Pixel(s) type)

3           Probably clear
4           Probably cloudy

(5) Code/Flag tables for proposed new Table B descriptors:

0-33-082  Geolocation quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Invalid Input Data (Indicates that any of the Spacecraft Ephemeris or Attitude Data is Invalid) |
| 8 | Bad Pointing (Indicates that the sensor LOS does not intersect the geoid, is near the limb, has invalid sensor angles or other similar condition) |
| 9 | Bad Terrain (Indicates that the algorithm could not obtain a valid terrain value) |
| 10 | Invalid Solar Angles |
| 11 | Missing at most a small gap of altitude and Ephemeris data |
| 12 | Missing more than a small gap of altitude and Ephemeris data, but no more than a granule boundary |
| 13 | Missing more than a granule boundary of altitude and Ephemeris data |
| 14 | The number of encoder pulse values per delta time is not as expected |
| 15 | Solar Eclipse during Earth view scan |
| All 16 | Missing value |

0-33-083  Radiance data quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Poor calibration quality due to bad space view offsets, OBC view offsets, etc or use of a previous calibration view |
| 8 | Saturated Pixel |
| 9 | Missing Data - Data required for calibration processing is not available for processing |
| 10 | Calibrated pixel Radiance out of range |
| 11 | Calibrated pixel Reflectance or EBBT out of range |
| 12 | The Moon has corrupted the space view |
| 13 | Scan data is not Present (No valid data) |
| 14 | Quality for this scan-line is reduced. The value is determined by the combined number of steps required to find a replacement for thermistor or calibration source data |
| 15 | Bad Detector |
| All 16 | Missing value |

(6) Add the following new entry to Common Code Table C-13:

Under Data Category 021 = Radiances (satellite measured), add the following new International Data Sub-Category entry:

| 007 | Visible/Infrared Imager Radiometer Suite |
| --- | --- |