| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc. 2.3(21) (14.VIII.2010 ) ------------------------- ITEM 2.3 DRAFT ENGLISH ONLY |
| --- | --- | --- |

A BUFR sequence for NWP-generated vertical profiles

Submitted by Y. Pelletier (Canada)

________________________________________________________________

Summary and Purpose of Document

The document proposes a template for vertical profiles of common meteorological parameters generated by Numerical Weather Prediction process.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the contents and approve the proposed descriptors for validation.

Background

NWP-generated vertical profiles (from numerical upper-air analyses or forecasts) offer a means of exploring and assessing, for one location,  the vertical structure of various meteorological parameters in the model forecasts.  They are often used by operational meteorologists to supplement and enhance the information available from observed upper-air soundings or from gridded model data.

CMC has been producing NWP vertical profiles in BUFR, for internal use, since about 1992. Those first-generation profiles make extensive use of local descriptors. This makes them unfit for public dissemination or international exchange. Furthermore, since they remained largely unchanged since their inception about seventeen years ago, they do not reflect advances in available model parameters and in the BUFR tables since that time.

In undertaking to modernize the Canadian NWP-generated vertical profiles, we wished for the new descriptor sequence to be free of local descriptors. This would make the data intelligible to outside users and hopefully bring its usefulness to a wider audience and a greater number of visualization applications.  We also wanted to make the template generic enough that it could be adopted by any NWP producer, if it suited their purposes.  This in turn may eventually facilitate the exchange and comparison of NWP vertical profiles across models and visualization applications.

While there is, of course, common data content in an observed vertical profile and the forecast of a vertical profile, there are also substantial differences.  It is not practical to simply take a slightly modified 3 09 052 TEMP template and fill it with forecast model data. Several elements in a conventional vertical sounding do not apply to its NWP equivalent, and vice-versa. Furthermore, there are useful parameters which are not measurable in conventional soundings but which may be available from model output. In fact, many possible non-traditional parameters could be included. We tried to keep to a small number of particularly useful extra parameters for the greater number of users. We aimed to maintain a certain focus on the relevance in daily use of such a profile by the forecasters on the operational desk.

Finally, we intentionally limited the selection of extra parameters to mostly direct model output.  We did not include calculated indices such as CAPE,  turbulence index, and so on.  Each calculated field would add a layer of post-processing, maintenance and responsibility that perhaps in this case properly belong with the calculation layer and specialized scientific packages of the forecaster's workstation.

Specifications of the template

The template formulates a vertical profile for a single location, at a single reference time and time increment.

The geographical location of the profile is specified by latitude, longitude and elevation. The template includes descriptors allowing to specify the location's name,  WMO synoptic number or ICAO identifier, as applicable.

The template enables the provision of data at the model's surface, at 2 metres AGL, 10 metres AGL, and at successive pressure levels at the discretion of the generating centre. In experimental production using a similar template at CMC, we converted each level of our production model to pressure coordinate and inserted interpolated standard pressure levels. The experimental profiles were topped at 100 hPa.

We use short delayed replications to specify which level type is being used.

The data available at each level type is as follows:

| Level type | Data parameters |
| --- | --- |
| Model surface | Real-world elevation of location, model terrain elevation of location, Geopotential height, total column water vapour, cloud amount (total), pressure, MSL pressure. |
| 2 metres AGL | Temperature, wet bulb temperature, dew point temperature |
| 10 metres AGL | Wind speed and direction |
| Isobaric surface | Wind speed and direction, temperature, wet bulb temperature, dew point temperature, geopotential height Optional: divergence, relative vorticity, vertical motion (w-component) |

Proposal

It is proposed to create one new Table D sequence descriptor, requiring two new Table B element descriptors.

These descriptors are proposed for validation. If accepted as such, we expect  the template may continue to evolve to some extent before being proposed for pre-operational status.  We can provide daily experimental production (for a limited time and for specific locations as required for the validation) and we are eager to collaborate with validation partners.

Proposed sequence 3 09 070:

Vertical Profile for Numerical Weather Prediction Data

| Descriptor | Element or sequence name | Comments |
| --- | --- | --- |
| Identification |  |  |
| 0 01 035 | Originating Centre | Required |
| 0 01 032 | Originating Process | Required |
| 0 01 015 | Station name |  |
| 0 01 062 | Short ICAO location indicator |  |
| 3 01 001 | block # stn # |  |
| Location and reference time |  |  |
| 3 01 021 | lat long | Required |
| 2 07 001 | Increase scale factor by 1; reference value and data width are recalculated in accordance with the Table C specification of operator 2 07 YYY | This table C operator requires BUFR Edition 4 |
| 0 10 001 | Station elevation (non coordinate) | Required. This value is the official or best estimate of the actual elevation of the station. It is provided for comparison with the model's virtual terrain elevation. The two can be substantially different in rugged terrain. We increased the scale factor to make the value directly comparable with 0 07 030 below. |
| 2 07 000 | Cancel increase scale factor operator |  |
| 3 01 011 | yy mm dd |  |
| 3 01 012 | hh mm | Reference time of the forecast |
| 0 08 084 | Vertical significance for NWP | Set bit 9 to 1 (= virtual station height) |
| 0 07 030 | Height of station above mean sea level | Elevation of model terrain at the lat/lon of station. As qualified by 0 08 084, this value is both station and model specific. Required. |
| Vertical profile data |  |  |
| 0 25 031 | NWP-generated vertical profile thinning method | In this instance, the term "thinning" refers to a method that may be applied to select a subset of levels from a model that may have many native vertical levels. Selecting only a subset reduces the size of the pseudo-sounding, at the possible cost of information loss and extra processing. |
| 0 08 021 | Time significance | Set to 4 (= forecast) or 16 (= analysis) or 27 (=first guess) |
| 0 04 014 | Time increment in hours | Validity time of the forecast expressed as a Delta T from reference time. In the case of an analysis or 00 hour forecast, the value is set to zero. |
| Point data at station height (including column-integrated data) |  |  |
| 0 10 004 | Pressure |  |
| 0 10 051 | Pressure reduced to MSL |  |
| 0 10 009 | Geopotential Height |  |
| 0 20 010 | Cloud cover (total) |  |
| 0 13 095 | Total column water vapour |  |
| Replication loop for levels |  |  |
| 1 28 000 |  |  |
| 0 31 002 |  | The number of levels used in the vertical profile is determined by this replication. The number of levels is discretionary and comprises all agl levels and pressure levels. |
| Data on pressure coordinates |  |  |
| 1 13 000 |  | Short delayed replication (set to 1 if vertical coordinate is pressure; 0 otherwise) |
| 0 31 000 |  |  |
| 0 08 084 | Vertical significance for NWP | Set bit 1 to value=0 and other bits as appropriate |
| 0 07 004 | Pressure | Non-surface levels on the model's native vertical coordinate are transposed to pressure coordinate. This makes the levels more readily intelligible for human interpretation and easier to use by generic display applications. The levels may correspond exactly to native model levels, or be interpolated between model levels to pressure levels chosen by the generating centre. |
| 0 11 001 | Wind direction (degrees true) |  |
| 0 11 002 | Wind speed (m/s) |  |
| 0 12 101 | Temperature |  |
| 0 12 102 | Wet Bulb Temperature |  |
| 0 12 103 | Dew Point |  |
| 0 10 009 | Geopotential Height |  |
| 1 03 000 |  | Embedded short delayed replication. Set to 1 if optional enhanced model data is to be included. |
| 0 31 000 |  |  |
| 0 11 022 | Divergence |  |
| 0 11 021 | Relative vorticity |  |
| 0 11 005 | Vertical motion |  |
| Data at 10 metres AGL |  |  |
| 1 04 000 |  | Short delayed replication (set to 1 if vertical coordinate is 10 metres agl; 0 otherwise) |
| 0 31 000 |  |  |
| 0 08 084 | Vertical significance for NWP | Set bit 1 to value = 1 and bit 8 to value =1 |
| 0 07 006 | Height above station | Set to 10 m |
| 0 11 001 | Wind direction (degrees true) |  |
| 0 11 002 | Wind speed (m/s) |  |
| Data at 2 metres AGL |  |  |
| 1 05 000 |  | Short delayed replication (set to 1 if vertical coordinate is 2 metres agl; 0 otherwise) |
| 0 31 000 |  |  |
| 0 08 084 | Vertical significance for NWP |  |
| 0 07 006 | Height above station | Set to 2 m |
| 0 12 101 | Temperature |  |
| 0 12 102 | Wet Bulb Temperature |  |
| 0 12 103 | Dew Point Temperature |  |

| PROPOSED DESCRIPTORS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference Value | Data Width |
| 0 08 084 | Vertical significance for NWP | Flag Table | 0 | 0 | 12 |
| 0 25 031 | NWP-generated vertical profile thinning method | Code Table | 0 | 0 | 3 |

| Flag Table 0 08 084 |
| --- |
| Vertical significance for Numerical Weather Prediction |
| Bit No. | Meaning |
| 1 | Model "ground" surface |
| 2 | Standard level |
| 3 | Tropopause level |
| 4 | Maximum wind level |
| 5 | Significant temperature level |
| 6 | Significant humidity level |
| 7 | Significant wind level |
| 8 | Vertically interpolated level (This should be set to 1 for points on the vertical profile that fall between the model's native vertical levels). |
| 9 | Virtual station height |
| 10 | Reserved |
| 11 | Reserved |
| 12 | Reserved |
| All 12 | Missing |

| Code Table 0 08 031 |
| --- |
| NWP-generated vertical profile thinning method |
| Code Figure | Meaninggu9ᴀ9Thinning may be applied to reduce the number of levels of a pseudo-sounding containing ma |
| 0 | reserved |
| 1 | No thinning applied (all native model levels are included from base to top of pseudo-sounding). |
| 2 | Native model levels are present only if they are significant levels as per regulations B/C 25 for conventional TEMP soundings |
| 3 | A predefined subset of native model levels is present |
| 4 | No native model levels are present. All profile levels are interpolated to a predefined set of pressure coordinate levels |
| 5 | Reserved |
| 6 | Reserved |
| 7 | Missing |

Note: None of the code figures exclude the addition of interpolated levels at the discretion of the generating centre.

# Footnotes

Many existing visualization applications can probably deal readily with the display of a forecast of traditional sounding data and be adapted for the proposed template with relatively little effort; however non-traditional data may require some development work.

Who guarantees the validity of the scientific calculations?

The question may be asked: if that is the case, shouldn't the profiles be generated by the forecaster's workstation? The answer mainly depends on whether the workstation has access to all the required fields for calculations and to a data-cube of sufficient vertical resolution to obtain the level of detail required. In many cases, we suspect that will not be the case.  Furthermore, for various categories of third parties who have sufficient knowledge and may wish to use such a profile, pre-packaged vertical profiles may be currently the only way for them to have real-time access to model data of high vertical resolution.