| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc. 3.3 (22) (12.VIII.2010) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Template for representation of synoptic reports from fixed land stations in Germany

Submitted by Sibylle Krebber (DWD)

________________________________________________________________

Summary and Purpose of Document

This document presents the BUFR template which is meant for migration of FM12-Synop to TDCF in DWD and gives some explanations and continuative regulations for reporting data.

A new sequence for this purpose is proposed.

________________________________________________________________

ACTION PROPOSED

# The meeting is requested to review the document and to approve

the proposed sequence for validation.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

Discussion

#### Background

Regarding the FM12-SYNOP it is planned within DWD to finish the migration process this year.

To provide our users and customers of SYNOP data with the whole content of the existing code the recommended template TM 307086 suitable for SYNOP data in compliance with reporting practices in RA VI was extended.

#### Representation of the DWD template and proposed new sequence descriptor 0 07 078

The sequence 0 07 078 is proposed for validation. It is assumed that it will be slightly modified during the validation process.

| 3 07 086 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data for RA VI |
| --- | --- | --- |
|  | 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates |
|  | 3 02 031 | Pressure data |
|  | 3 02 035 | Basic synoptic “instantaneous” data |
|  | 3 02 036 | Clouds with bases below station level |
|  | 0 08 002 | Vertical significance |
|  | 3 02 037 | State of ground, snow depth, ground minimum temperature |
|  | 3 02 066 | Dangerous weather phenomena |
|  | 3 02 043 | Basic synoptic “period” data |
|  | 3 02 044 | Evaporation data |
|  | 1 01 002 | Replicate next descriptor 2 times |
|  | 3 02 045 | Radiation data (from 1 hour and/or 24 hour period) |
| 3 07 078 |  | Additional synoptical data |
|  | 0 01 023* | Observation Sequence number |
|  | * | Additional wind data |
|  | * | Additional weather |
|  | * | Additional “instantaneous” data |
|  | * | Additional present weather |
|  | * | Visibility in different directions |
|  | * | Sea data (Observations from a coastal station) |
|  | * | Clouds |
|  | * | Additional 9SpSpspsp groups |

*) not in WMO Template

The additions of DWD expands to

|  |  |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data in DWD | in FM12 | Unit, scale |
| --- | --- | --- | --- | --- | --- |
| 3 07 086 |  |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data for RA VI |  |  |
| Additional parameters in DWD |
| 3 07 078 | 0 01 023 |  | Observation Sequence number |  | Numeric, 0 |
|  |  |  | Additional wind data |  |  |
|  | 0 04 025 |  | Time period in minutes ( =-60 ) |  | Minute, 0 |
|  | 0 11 042 |  | Maximum wind speed (10 min mean wind) | 912ff | m s-1, 1 |
|  |  |  | 902tt 912ff .. mandatory ff>=18 |  |  |
|  | 1 04 000 |  | Delayed replication of 4 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 902tt | Minute, 0 |
|  | 0 11 042 |  | Maximum wind speed (10 min mean wind) | 912ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  |  |  | Significant change in wind speed and/or direction | e.g. 913ff 904tt 913ff |  |
|  | 1 12 000 |  | Delayed replication of 12 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=22 time of occurrence of wind shift) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 904tt | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=set to missing to cancel all previous time displacements ) |  | Minute, 0 |
|  |  |  | Additional weather |  |  |
|  | 1 06 000 |  | Delayed replication of 6 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 20 003 |  | Present weather | 962ww, 963w1w1, 964ww, 965w1w1, 966ww, 967w1w1 | Code table, 0 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  |  |  | Additional “instantaneous” data |  |  |
|  | 0 04 025 |  | Time period (= 0 minutes) |  | Minute, 0 |
|  | 0 02 177 |  | Method of snow depth measurement |  | Code table, 0 |
|  |  |  | Additional present weather |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 003 |  | Present weather | 960ww 961ww | Code table, 0 |
|  |  |  | Visibility in different directions |  |  |
|  | 1 03 000 |  | Delayed replication of 3 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 05 021 |  | Bearing or azimuth | 981VV-988VV | Degreetrue, 0 |
|  | 0 20 001 |  | Horizontal visibility | VV | m, –1 |
|  | 0 05 021 |  | Bearing or azimuth (=set to missing to cancel previous entry) | 981VV-988VV | Degreetrue, 0 |
|  |  |  | Sea data (Observations from a coastal station) |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |  |
|  |  | 0 02 038 | Method of sea/water temperature measurement |  | Code table, 0 |
|  |  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) |  | m, 2 |
|  |  | 0 22 043 | Sea/water temperature | 222.. 0sTwTwTw, 333 925TwTw | K, 2 |
|  |  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) |  | m, 2 |
|  | 1 03 000 |  | Delayed replication of 2 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 33 041 |  | Attribute of following value |  | Code tabel, 0 |
|  | 0 20 058 |  | Visibility seawards from a coastal station | 980VsVs | m,-1 |
|  | 0 22 061 |  | State of the sea | 924SVs | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 022 |  | Wind waves |  |  |
|  |  | 0 22 002 | Direction of wind waves |  | Degreetrue, 0 |
|  |  | 0 22 012 | Period of wind waves | 222.. 2PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves | HwHw | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 023 |  | Swell waves |  |  |
|  |  | 0 22 003 | Direction of swell waves | 222.. 3dw1dw1 dw2dw2 | Degreetrue, 0 |
|  |  | 0 22 013 | Period of swell waves | 4Pw1Pw1, 5Pw2Pw2 | s, 0 |
|  |  | 0 22 023 | Height of swell waves | Hw1Hw1, Hw2Hw2 | m, 1 |
|  |  |  | Clouds | 941CDp, 943CLDp, |  |
|  | 1 03 000 |  | Delayed replication of 3 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 012 |  | Cloud type (C) | 941C, 943CL | Code table, 0 |
|  | 0 20 090 |  | Special clouds | 993CS | Code table, 0 |
|  |  |  | Additional 9SpSpspsp groups |  |  |
|  | 1 13 000 |  | Delayed replication of 13 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 05 021 |  | Bearing or azimuth | Da, Dp | Degreetrue, 0 |
|  | 0 05 021 |  | Bearing or azimuth (different directions span a sector) | Da, Dp | Degreetrue, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 024 |  | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent, 5 = Severe) |  | Code table, 0 |
|  | 0 20 025 |  | Obscuration |  | Flag table, 0 |
|  | 0 20 026 |  | Character of obscuration |  | Code table, 0 |
|  | 0 20 027 |  | Phenomenon occurrence |  | Flag table, 0 |
|  | 0 20 063 |  | Special phenomena "to be developed" |  | Code table, 0 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |

#### Explanations and Regulations

The structure of the template with regard to the different time data based on the BUFR regulations.

94.5.3.4 "The consecutive occurrence of two identical element descriptors or identical sets of element descriptors from classes 04 to 07 inclusive shall demote a range of values bounded by the corresponding element values. This enables the definition of layers and simple time periods."

94.5.3.5 "The definition of line, areas, volumes and more complex time attributes shall be accomplished using descriptors from class 04 to 07 in association with suitable descriptors from class 08."

94.5.3.6 "The consecutive occurrence of two or more non-identical element descriptors from classes 04 to 07 inclusive shall infer that all such elements remain in effect until redefined, unless such elements define an increment."

E.g. for the purpose of a "significant change in wind speed and/or direction" the following sequence of descriptors was prepared:

|  |  |  | Significant change in wind speed and/or direction | e.g. 913ff 904tt 913ff |  |
| --- | --- | --- | --- | --- | --- |
|  | 1 12 000 |  | Delayed replication of 12 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=22 time of occurrence of wind shift) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 904tt | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=set to missing to cancel all previous time displacements ) |  | Minute, 0 |

The first "time period (or displacement)" is set to -10 minutes and has the significance of "time averaged". This means that all following values are 10 minute mean values.

The second "time (period or) displacement" has the significance of e.g. "start of phenomenon". This means that all following values have the additional information of the time of commencement.

Due to the different specified time significance the second "time period or displacement" does not redefined the time period specified for the calculation of average.

The third "time (period or) displacement" has the significance of "time of occurrence of wind shift" to determine the time of a significant change. This means that all following values have the additional information of the time of occurrence of wind shift.

Afterwards both the "time significance" and the "time (period or) displacement" is set to missing to cancel all previous time periods or displacements.

Similar is valid for the following sequence:

This sequence is meant for various 9SpSpspsp groups in diverse order and combination.

|  |  |  | Additional 9SpSpspsp groups |  |  |
| --- | --- | --- | --- | --- | --- |
|  | 1 13 000 |  | Delayed replication of 13 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 05 021 |  | Bearing or azimuth | Da, Dp | Degreetrue, 0 |
|  | 0 05 021 |  | Bearing or azimuth (different directions span a sector) | Da, Dp | Degreetrue, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 024 |  | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent, 5 = Severe) |  | Code table, 0 |
|  | 0 20 025 |  | Obscuration |  | Flag table, 0 |
|  | 0 20 026 |  | Character of obscuration |  | Code table, 0 |
|  | 0 20 027 |  | Phenomenon occurrence |  | Flag table, 0 |
|  | 0 20 063 |  | Special phenomena "to be developed" |  | Code table, 0 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |

Within the replication the first two descriptors "Time period (or displacement)" define a period or if set to missing cancel previous defined periods.

With "Time significance" set to an appropriate value and "Time (period or) displacement" it is possible to specify the time of commencement, occurrence or ending.

This does not redefine the specified period.

The next two descriptors "Bearing or azimuth" define a sector or if set to missing cancel previous defined sectors. Sometimes the information about a sector is needed if no specific direction of a phenomenon is applicable.