| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010 |  | IPET-DRC-II / Doc. 3.3 (24) (12.VIII.2010) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Additional entries in code and flag tables

Submitted by Sibylle Krebber (DWD)

________________________________________________________________

Summary and Purpose of Document

This document proposes additional entries in code tables and flag tables which were needed in the process of the migration of FM12-Synop to TDCF.

________________________________________________________________

ACTION PROPOSED

# The meeting is requested to review the document and approve

the contents for pre-operational implementation.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

Discussion

#### Background

In FM12-SYNOP a huge amount of possibilities is given to encode additional and special weather phenomenon with diverse combinations of 9SpSpspsp groups.

See: Manual on Codes Volume I.1, Code table 3778 - 9SpSpspsp Supplementary information.

To be able to encode all these information in BUFR properly, some additional entries in existing code and flag tables are needed.

Furthermore, in DWD the "lowest height of clouds" is reported in the national part of the synoptic report. We would appreciate a proper coding using the "Vertical significance".

#### Proposals

  - Entries in table 2555 Mw – "Water-spout(s), tornadoes, whirlwinds, dust devils" allow to encode "Dust devils" which is missing in 0 20 023 – Other weather phenomena. 
An additional entry is proposed:

0 20 023

Other weather phenomena

Bit No.	Status

1 	Dust/sand whirl	Operational

2 	Squalls	Operational

3 	Sand storm	Operational

4 	Dust storm	Operational

5 	Lightning - cloud to surface	Operational

6 	Lightning - cloud to cloud	Operational

7 	Lightning - distant	Operational

8 	Thunderstorm	Operational

9 	Funnel Cloud not touching surface	Operational

10 	Funnel cloud touching surface	Operational

11 	Spray	Operational

12 	Water-spout	Operational

13 	Wind shear	Operational

14	Dust devils	Pre-Operational

15-17 	Reserved	Operational

All 18 	Missing value	Operational

  - In table 2555 Mw – "Water-spout(s), tornadoes, whirlwinds, dust devils" following information is given

    - within 3 km of station

    - more than 3 km from station

In BUFR Flag table 020027 – "Phenomenon occurrence" there are (corresponding) entries

- At the station

- In the vicinity

The Question is whether

- "At the station" is equivalent to "within 3 km of station" and

- "In the vicinity" is equivalent to "more than 3 km from station"

- or do we need at least an editorial change for the entries?

Flag Table 020027 is completed (no additional entries are possible)!

Proposed editorial change in Flag table 0 20 027 (in case):

0 20 027

Phenomena occurrence

Bit No.	Status

1 	At time of observation	Operational

2 	In past hour	Operational

3 	In time period for past weather W1W2	Operational

4 	In time period specified	Operational

5 	Reserved	Operational

6 	Below station level	Operational

7 	At the station, i.e. within 3 km of station	Operational

8 	In the vicinity, i.e. more than 3 km from station	Operational

All 9 	Missing value	Operational

  - In Code table 3778 – "Supplementary information" some entries concerning the "Time significance" are given:

    - Time of commencement

    - Time of ending ...

    - Time of occurrence ...

The almost saturated BUFR Code table 0 08 021 – "Time significance" provides corresponding entries

- 17 – Start of phenomenon

- 29 – End of scan (if appropriate)

but no entries of "Time of occurrence" and no proper coding of "Time of ending"

Proposal of new entries and editorial changes in 0 08 021:

- 30 – Time of occurrence of a phenomenon

- change 29 in "End of scan or time of ending"

0 08 021

Time significance

Code figure	Status

0 	Reserved	Operational

1 	Time series	Operational

2 	Time averaged	Operational

3 	Accumulated	Operational

4 	Forecast	Operational

5 	Forecast time series	Operational

6 	Forecast time averaged	Operational

7 	Forecast accumulated	Operational

8 	Ensemble mean	Operational

9 	Ensemble mean time series	Operational

10 	Ensemble mean time averaged	Operational

11 	Ensemble mean accumulated	Operational

12 	Ensemble mean forecast	Operational

13 	Ensemble mean forecast time series	Operational

14 	Ensemble mean forecast time averaged	Operational

15 	Ensemble mean forecast accumulated	Operational

16 	Analysis	Operational

17 	Start of phenomenon	Operational

18 	Radiosonde launch time	Operational

19 	Start of orbit	Operational

20 	End of orbit	Operational

21 	Time of ascending node	Operational

22 	Time of occurrence of wind shift	Operational

23 	Monitoring period	Operational

24 	Agreed time limit for report reception	Operational

25 	Nominal reporting time	Operational

26 	Time of last known position	Operational

27 	First guess	Operational

28 	Start of scan	Operational

29 	End of scan or time of ending	Pre-Operational

30 	Time of occurrence	Pre-Operational

31 	Missing value	Operational

  - Code table 4077 – zz "Variation, location or intensity of phenomena"

zz=99 have the meaning: "Very heavy; killing; very severe; dense; greatly above normal; very thick; very good"

This is unrepresentable in BUFR Code table 0 20 024 - "Intensity of phenomena"

It is proposed to add as last possible entry something like "very severe" or even "disastrous".

0 20 024

Intensity of phenomena

Code figure	Status

0 	No phenomena	Operational

1 	Light	Operational

2 	Moderate	Operational

3 	Heavy	Operational

4 	Violent	Operational

5 	Severe	Operational

6 	Disastrous	Pre-Operational

7 	Missing value	Operational

  - Code table 3766 S8 – "Snowstorm phenomena (snow raised by the wind)"

To be able to encode all entries of table S8 with the combination of the BUFR descriptors 020025 020026 020027 the code tables should be augmented accordingly.

There is no entry for the information of "impossible to determine whether snow is falling or not".

0 20 025

Obscuration

Bit No.	Status

1 	Fog	Operational

2 	Ice fog	Operational

3 	Steam fog	Operational

4-6 	Reserved	Operational

7 	Mist	Operational

8 	Haze	Operational

9 	Smoke	Operational

10 	Volcanic ash	Operational

11 	Dust	Operational

12 	Sand	Operational

13 	Snow	Operational

14 	Cloud	Operational

15 	Precipitation	Operational

16 	Impossible to determine whether snow is falling or not	Pre-Operational

17-20 	Reserved	Operational

All 21 	Missing value	Operational

0 20 026

Character of obscuration

Code figure	Status

0 	No change	Operational

1 	Shallow	Operational

2 	Patches	Operational

3 	Partial	Operational

4 	Freezing	Operational

5 	Low drifting	Operational

6 	Blowing	Operational

7 	Increasing	Operational

8 	Decreasing	Operational

9 	In suspension in the air	Operational

10 	Wall	Operational

11 	Dense	Operational

12 	Whiteout	Operational

13	Drifting and blowing	Pre-Operational

14 	Reserved	Operational

15 	Missing value	Operational

#### Conclusion

The meeting is invited to consider the proposed new code table entries, and to endorse their addition to the existing table.