WORLD METEOROLOGICAL ORGANIZATION

COMMISSION FOR BASIC SYSTEMS

SECOND MEETING OF THE INTER-PROGRAMME EXPERT TEAM

ON DATA REPRESENTATION AND CODES

FINAL REPORT

BRASILIA, BRAZIL, 31 AUGUST - 3 SEPTEMBER 2010

DISCLAIMER

Regulation 42

Recommendations of working groups shall have no status within the Organization until they have been approved by the responsible constituent body.  In the case of joint working groups the recommendations must be concurred with by the presidents of the constituent bodies concerned before being submitted to the designated constituent body.

Regulation 43

In the case of a recommendation made by a working group between sessions of the responsible constituent body, either in a session of a working group or by correspondence, the president of the body may, as an exceptional measure, approve the recommendation on behalf of the constituent body when the matter is, in his opinion, urgent, and does not appear to imply new obligations for Members. He may then submit this recommendation for adoption by the Executive Council or to the President of the Organization for action in accordance with Regulation 9(5).

© World Meteorological Organization, 2009

The right of publication in print, electronic and any other form and in any language is reserved by WMO. Short extracts from WMO publications may be reproduced without authorization provided that the complete source is clearly indicated. Editorial correspondence and requests to publish, reproduce or translate this publication (articles) in part or in whole should be addressed to:

Chairperson, Publications Board

World Meteorological Organization (WMO)

7 bis, avenue de la Paix				Tel.: +41 (0)22 730 84 03

P.O. Box No. 2300				Fax: +41 (0)22 730 80 40

CH-1211 Geneva 2, Switzerland				E-mail: Publications@wmo.int

NOTE

The designations employed in WMO publications and the presentation of material in this publication do not imply the expression of any opinion whatsoever on the part of the Secretariat of WMO concerning the legal status of any country, territory, city or area or of its authorities, or concerning the delimitation of its frontiers or boundaries.

Opinions expressed in WMO publications are those of the authors and do not necessarily reflect those of WMO. The mention of specific companies or products does not imply that they are endorsed or recommended by WMO in preference to others of a similar nature which are not mentioned or advertised.

This document (or report) is not an official publication of WMO and has not been subjected to its standard editorial procedures. The views expressed herein do not necessarily have the endorsement of the Organization.

Executive Summary

The second meeting of Inter-Programme Expert Team on Data Representation and Codes (IPET-DRC) was held at the headquarters of INMET, Brazil from 31 August to 3 September 2010.

The meeting reviewed the current status of validation of the proposals on GRIB edition 2 (GRIB2), BUFR and CREX at or before the first meeting of IPET-DRC (Geneva, 15-18 September 2009), and confirmed that the following proposals have been validated. The meeting agreed those for operational use.

GRIB2 templates 3.44 (for WAFS data), 3.130 (for irregular latitude/longitude grid), 4.32 (for synthetic satellite data), 4.51/4.91 (for categorical forecasts) and 4.44/4.45/4.46/4.47 (for atmospheric aerosol data), and their relevant Code tables,

BUFR/CREX descriptors for volume (3D) radar data (Table B), ATMS data (Tables B/D), JASON2 OGDR data (Table B/D), IASI data (Tables B/D), NDVI data (Tables B/D) and lightning data (Table B/D) (for pre-operational use),  and their relevant Code/Flag tables

The meeting discussed a lot of proposals on additions and modifications to tables and templates of GRIB2, BUFR and CREX, and agreed the following proposal for operational use as well as new entries in Code/Flag tables and Common Code tables;

BUFR descriptors for all sky radiance data and VIIRS data

The meeting discussed the issue of different versioning between BUFR and CREX. The existing master tables of BUFR and CREX are in common use but have different version numbers for identification. The meeting agreed to use same version number for same master tables of BUFR and CREX, and the number should be incremented fully synchronously when the tables updated.

The meeting agreed the amendments to the Regulations for Reporting Traditional data in TDCF, i.e. B/C Regulations, to include instantaneous data from regional or national requirements in BUFR reports and to clarify reporting of high resolution sounding data. In addition, the meeting agreed the proposal to delete B/C35 for CLIMAT TEMP and CLIMAT TEMP SHIP based on the decision by the fifteenth session of the Commission for Climatology (CCl-XV) on discontinuation of the monthly upper-air CLIMAT TEMP reports.

Regarding traditional alphanumeric codes (TAC), the meeting reviewed the proposal by International Civil Aviation Organization (ICAO), and agreed the amendments to the aeronautical codes, FM15, FM16 and FM51 in compliance with the amendment 75 for ICAO Annex 3/WMO Technical Regulations [C.3.1].

The meeting reviewed the procedures for adoption of amendments to the Manual on Codes and agreed that fast track procedure could be twice a year (at present, generally once a year). Instead, the meeting was of the opinion that the procedure for pre-operational use should be limited to urgent requirements. The meeting also agreed that new entries for validation, which need approval by the president of CBS at present, could be allocated by IPET-DRC, taking into account the facts that entries for validation are possibly changed or even withdrawn in validation process and approval by the president of CBS is indispensable, after all, for operational use after validation process.

The meeting discussed again the task to identify the observation practice elements contained in the Manual on Codes and to pass them to OPAG-IOS for inclusion in observing standards documentation. The meeting expressed its concern about several aspects of this issue.

The meeting noted that current status of migration to TDCF derived from the WWW Monitoring exercises conducted in July 2009, October 2009, January 2010 and April 2010, which showed:

The numbers of stations, for which BUFR surface and upper-air data were expected or received, were 1062 out of the 4362 RBSN surface stations (24 per cent) and 239 out of the 791 RBSN upper-air stations (30 per cent), respectively.

Regarding the difficulty that WMO Members were experiencing in meeting the deadline of November 2010 to complete the migration of the data category 1, the meeting was of the opinion that the target dates in the original migration matrix should not be extended, because to do so would detract from the urgency of the migration and convey a sense that these dates, and indeed the migration itself, were not to be taken seriously. It would also be unfair to the WMO members which made the effort to adhere to the original target dates. However, to acknowledge the reality that many WMO Members will not meet the original target dates for Category 1, the meeting agreed that dual dissemination of TAC and BUFR could, if needed, continue past the original target dates and agreed to add the deadline of November 2014 to stop dual dissemination of Category 1 TAC and BUFR data. The meeting also agreed to add the deadline of November 2014 to stop dual dissemination of Category 4 TAC and BUFR in the same manner as Category 1, as a logical consequence.

The meeting was informed the progress in developing electronic publication of the Manual on Codes, incorporating files exported from the database of tables of GRIB2, BUFR and CREX in the Secretariat.

TABLE OF CONTENTS

PAGE

1.	ORGANIZATION OF THE MEETING

1.1	Opening of the meeting 	1

1.2	Approval of the agenda 	1

Annex to paragraph 1.2 - Agenda and list of participants 	A.1

2.	GRIB

2.1	Status of proposals at or before the IPET-DRC-I 	1

Annex to 2.1 	A.6

2.2	Amendments to GRIB (common aspects)

2.2.1	GRIB Calendar Identification 	2

2.3	Additions and modifications of templates and tables

2.3.1	Encoding wave spectra in GRIB Edition 2 	2

2.3.2	Waves parameters 	2

Annex to 2.3.1 and 2.3.2 	A.6

2.3.3	GRIB2 parameters for Fire Weather Products 	2

Annex to 2.3.3 	A.8

2.3.4	GRIB Variable GRID Definition Templates 	3

2.3.5	Logarithmic hybrid coordinate 	3

2.3.6	GRIB2 parameters for Climate Forecast Products 	3

Annex to 2.3.6 	A.9

2.3.7	GRIB2 parameters for Ice Analysis and Forecasting Products 	4

Annex to 2.3.7 	A.9

2.3.8	GRIB2 parameters for Storm Prediction 	4

Annex to 2.3.8 	A.10

2.3.9	Generalized vertical height coordinate in GRIB Edition 2 	4

Annex to 2.3.9 	A.10

2.3.10	New entries in Code Table 4.7 - Derived forecast 	4

Annex to 2.3.10 	A.13

2.3.11	Issues for Representing Space Weather in GRIB2 	5

2.3.12	Proposal for coding radioisotopes in GRIB2 	5

Annex to 2.3.12 	A.13

2.3.13	How to code precipitation amounts in GRIB2 or clarification of the application of statistical
processing 	5

Annex to 2.3.13 	A.22

3.	BUFR AND CREX

3.1	Status of proposals at or before the IPET-DRC-I 	6

Annex to 3.1 	A.24

3.2	Amendments to BUFR/CREX (common aspects)

3.2.1	Versioning of BUFR and CREX tables 	6

Annex to 3.2.1 	A.25

3.2.2	A new entry in Specifications of octet contents 	6

Annex to 3.2.2 	A.25

3.3	Additions and modifications of tables

3.3.1	Withdrawal of SIGMET templates proposed for validation 	7

3.3.2	National data in templates for surface observations 	7

Annex to 3.3.2 	A.26

3.3.3	A proposal for Universal BUFR template for representation of Lightning data Formulated in June 2010, including 3.3.20 (Change to Common Code Table C-13 - Sferics -) 	8

Annex to 3.3.3 	A.27

3.3.4	Update from JCOMM on developments of BUFR templates, including template for XBT data 	8

Annex to 3.3.4 	A.32

3.3.5	Revision of sub-categories for ozone data, including telecommunication headers 	9

Annex to 3.3.5 	A.33

3.3.6	Entries in Common Code table C-4 for a recording type 	9

Annex to 3.3.6 	A.33

3.3.7	Entries in Common Code table C-5 for multiple satellite products 	9

Annex to 3.3.7 	A.34

3.3.8	BUFR/CREX descriptors related to AWS 	9

Annex to 3.3.8 	A.34

3.3.9	Descriptors for all sky radiance 	10

Annex to 3.3.9 	A.40

3.3.10	Amendments to the Class 00 and use of UTF-8 	10

3.3.11	Validation of EUCOS BUFR template for representation of radiosonde data 	11

Annex to 3.3.11 	A.41

3.3.12	Examples of usage TM 307093 for representation of nominal values 	11

3.3.13	Proposal for modifications/additions related to representation of nominal values 	11

Annex to 3.3.13 	A.43

3.3.14	New BUFR descriptors for ATMS data 	11

Annex to 3.3.14 	A.44

3.3.15	New BUFR code table entries 	12

Annex to 3.3.15 	A.47

3.3.16	New BUFR descriptors for VIIRS data 	12

Annex to 3.3.16 	A.47

3.3.17	New BUFR/CREX Class 0 descriptors 	12

Annex to 3.3.17 	A.49

3.3.18	A note to BURF/CREX descriptors 0 20 019 and 0 20 020 	12

Annex to 3.3.18 	A.50

3.3.19	Change to BUFR Manual - Footnote to radiological elements -	13

Annex to 3.3.19 	A.50

3.3.21	A BUFR sequence for NWP-generated vertical profiles 	13

Annex to 3.3.21 	A.50

3.3.22	Template for representation of synoptic reports from fixed land stations in Germany 	13

Annex to 3.3.22 	A.54

3.3.23	Development of Code table 0 20 063 – Special phenomena New Code table 0 20 112 Supplementary cloud type 	13

Annex to 3.3.23 	A.59

3.3.24	Additional entries in code and flag tables 	14

Annex to 3.3.24 	A.63

3.3.25	Status of existing proposals related to satellite data 	14

Annex to 3.3.25 	A.67

3.3.26	New entry in Common Code Table C12 for COSMO 	15

Annex to 3.3.26 	A.68

3.3.27	Additional BUFR descriptors for the Evolution of clouds and Template version, additional notes
in BUFR table B 	15

Annex to 3.3.27 	A.68

3.4	Regulations for reporting traditional observation data in Table-Driven Code Forms (TDCF): BUFR and CREX

3.4.1	Amendments to B/C Regulations 	15

Annex to 3.4.1 	A.69

3.5	Master tables for scientific disciplines other than meteorology

3.5.1	Master Table 10 review and update 	16

4.	TRADITIONAL ALPHANUMERIC CODES

4.1	Amendments to the aeronautical codes, FM15, FM16 and FM51 	16

Annex to 4.1 	A.70

4.2	Discontinuation of the monthly upper-air CLIMAT TEMP reports 	16

4.3	Past weather reporting in hourly synoptic observation 	17

Annex to 4.3 	A.89

4.4	Observation practice in the Manual on Codes 	17

5.	MIGRATION TO TABLE DRIVEN CODE FORMS (TDCF)

5.1	Migration status

5.1.1	Result of WWW Monitoring 	18

Annex to 5.1.1 	A.90

5.1.2	Status of the national plans for the migration to TDCF and step-by -step migration by zone 	19

Annex to 5.1.2 	A.95

5.1.3	Data issued from Data Collection Platforms (DCPs) 	19

5.1.4	Information provided by members of the IPET-DRC 	20

5.2	Request from the CBS MG-XI on MTDCF 	22

Annex to 5.2 	A.96

5.3	Encoder software for BUFR/CREX available for MTDCF 	23

Annex to 5.3 	A.98

6.	MANUAL ON CODES

6.1	Electronic publication of the Manual on Codes, including database 	24

6.2	Procedures for amending the Manual on Codes 	24

Annex to 6.2 	A.100

7.	COLLABORATION WITH OTHER CBS TEAMS

7.1	Collaboration with the Inter-Programme Expert Team on Metadata and Data Interoperability
(IPET-MDI) 	25

7.2	Corrected and delayed reports in BUFR bulletins 	26

8.	CLOSURE OF THE MEETING 	27

SECOND MEETING OF THE INTER-PROGRAMME EXPERT TEAM

ON DATA REPRESENTATION AND CODES

(BRASILIA, BRAZIL, 31 AUGUST -3 SEPTEMBER 2010)

1.     ORGANIZATION OF THE MEETING

1.1	Opening of the meeting

1.1.1	The second meeting of the Inter-Programme Expert Team on Data Representation and Codes (IPET-DRC) was held at the headquarters of Instituto Nacional de Meteorologia (INMET), Brazil from 31 August to 3 September 2010 under the chairmanship of Dr Simon Elliott, chairman of the IPET-DRC.

1.1.2	On behalf of Mr Michel Jarraud, Secretary-General of WMO, Mr Atsushi Shimazaki of the Data Representation, Metadata and Monitoring Division of the WIS Branch, welcomed the participants.

1.1.3	Mr A. Shimazaki noted that IPET-DRC established by the fourteenth session of CBS has a prefix "Inter-Programme", which means recognition of the fact that the IPET-DRC has contributed and will continue contributing to all WMO Programmes. Significance of the work will be growing along with progress of the WMO Information System, in which organizations other than NMHSs are expected to be involved.

1.1.4	The sixty-second session of Executive Council invited CBS to consider extending the procedures for adoption of amendments to the Manual on Codes to other Manuals, such as the Manuals on the GDPFS and the GTS.  Mr A. Shimazaki expressed the necessity of review of the current procedures to amend the Manual on Codes so as to form the basis for other Manuals.

1.1.5	The EC session noted WMO Members' difficulties in meeting the deadline of November 2010 to complete the migration of the data category 1 (SYNOP, PILOT, TEMP and CLIMAT) and invited CBS to consider measures with a view to ensuring that all WMO Members continue accessing the observational data available on the GTS in the appropriate format as well as to facilitate and foster the migration from TAC to TDCF. In this respect, the meeting was invited to consider relevant proposals to be submitted to CBS.

1.2	Approval of the agenda

The meeting agreed on the agenda with an additional item. The list of participants is given in Annex to this paragraph as well as the updated agenda.

2.     GRIB

2.1	Status of proposals at or before the IPET-DRC-I

Several proposals on amendments to GRIB edition 2 (GRIB2) were agreed for validation at or before the first meeting of Inter-Programme Expert Team on Data Representation and Codes (IPET-DRC) (Geneva, 15-18 September 2009).

The meeting reviewed the current status of validation on those proposals and updated the tables as Annex to this document.  The following were taken account on this update.

Dr Luis Kornblueh, Max-Planck-Institut für Meteorologie kindly informed the Secretariat of validation status on their proposals before the meeting. Unfortunately, the validations have not been completed, but it was felt that they were making every effort for the validations complete. At the next meeting, the team might have good news from the Institute.

Regarding the proposal on Paleo climate, which had been approved for validation, Ms Sibylle Krebber reported that their proposal on the Section 1 GRIB2 duplicated with the proposal by the UK MetOffice (UKMO) at this meeting (see 2.2.1 below). A solution of this problem has not been reached due to complication indicated in 2.2.1 below.

2.2	Amendments to GRIB (common aspects)

2.2.1	GRIB Calendar Identification

UKMO produces data on a 360-day calendar, including many climate forecasts. This calendar has twelve 30-day months. It is invalid to translate such dates to a Gregorian calendar: therefore an additional octet in GRIB2 Section 1 for calendar identification, plus a new code table of calendar types were proposed.

Calendar identification will allow GRIB2 decoders to calculate dates (such as verification time) correctly for messages on a 360-day calendar. However, the proposed Octet has already occupied by the proposal from the Deutscher Wetterdienst (DWD) for Paleo climate as mentioned in 2.1. This problem could be solved by allocating another octet for the identification of 360-day calendar. However, the Japan Meteorological Agency (JMA) pointed out that adding octet to Section 1 would affect the current software package and suggested to make the proposed octet for the identification of 360-calendar (as well as octet for Paleo climate) optional. The meeting elaborated the suggestion along with the proposals and found that 1) JMA’s suggestion would be unworkable if octets following the optional octet(s) needed to be defined; 2) more general, the change in Section 1 that led to decoding/encoding software changes might trigger the new edition of GRIB, which was not a desirable outcome of those changes. Due to these concerns, the meeting concluded that more discussion was needed to find a solution.

2.3	Additions and modifications of templates and tables

2.3.1	Encoding wave spectra in GRIB Edition 2

2.3.2	Waves parameters

Two relevant issues were proposed by DWD and the European Centre for Medium Range Weather Forecast (ECMWF) on encoding wave data.

DWD proposed a template for the "Analysis or forecast of a multi component parameter or matrix element at a point in time" at the last meeting of the team. However, the proposal of the list of parameter was withdrawn because it seemed to be not very seminal and it was decided to discuss and consider this issue again based on the discussion on how to encode wave spectra in GRIB edition 2 between ECMWF and DWD wave experts in 2008. At the meeting, DWD restored the list of parameters withdrawn in the document.

On the other hand, ECMWF reported that they were preparing migration of its WAVE model from GRIB edition 1 to 2. At the present several parameters are produced by the model in GRIB 1 format using the local table defined by the Centre and documented in the official web site:

http://www.ecmwf.int/services/archive/d/parameters/order=/table=140/.

Some parameters contained in the table were not present in any code table in the GRIB 2 and need to be added to allow the migration to the new edition in ECMWF.

The meeting noted that the proposals by two centres had inconsistencies on duplicated table entries and moreover that the proposals by DWD and ECMWF were oriented to templates and table entries, respectively.

In view of the above, it was suggested to merge those two proposals, and the modified list of parameters to be added to Code table 4.2 with a note for definition of wave parameters had been submitted as one agreed proposal.

The meeting finally approved the proposal as Annex to these paragraphs for validation.

2.3.3	GRIB2 parameters for Fire weather products

At the first meeting of the IPET-DRC (Geneva, September 2009), the National Centres for Environmental Prediction (NCEP) of NOAA (USA) presented a proposal for new GRIB2 parameters to be used in fire weather forecasting as in the agenda item 2.3.8 of the first meeting of IPET-DRC. The first meeting provided feedback and requested NCEP to further refine the proposal accordingly.

NCEP provided the revised document to the IPET-DRC members via email in March 2010, including an offer to provide sample messages for validation.

The meeting noted that no further validation was necessary for the proposal and agreed the revised proposal as Annex to this paragraph to be approved by fast track.

2.3.4	GRIB variable grid definition templates

UKMO produces data on variable resolution grids, such as UKV (high-resolution UK model) domain. These grids have rows of constant latitude and columns of constant longitude, each with irregular spacing. In order to store the latitude of every row and the longitude of every column, two new Grid definition templates were proposed.

Comments (or concerns) were expressed by ECMWF that validation of grid is complex and grid templates should be minimized.

The team recommended further study was needed.

2.3.5	Logarithmic hybrid coordinate

The hybrid vertical coordinate is generally implemented in the following form:

pi =  Ai * Psfc + Bi 		(1)

(see Guide to GRIB Edition 2, or, for more details on the hybrid coordinate concept Bubnova et al, 1995)

However it is also possible to implement the hybrid coordinate using the natural logarithm of pressure:

log (pi) = ai * log (Psfc)  + bi 	(2)

(Claude Girard and André Plante, CMC internal note, 2010)

Logarithmic hybrid levels are in current use in the newer releases of the Canadian GEM NWP model. In 2010 the need arose to exchange data on the GEM LAM model's native vertical coordinates with the NOAA Earth System Research Laboratory/Chemical Sciences Division. In this case, encoding in GRIB2 was performed by defining a local entry in Code table 4.5 for the logarithmic hybrid vertical level (equation (2) above). With this slight modification, the existing GRIB2 hybrid level procedure was successfully used to exchange data on the model’s native logarithmic hybrid levels.

As can be seen readily from the equations above, a logarithmic hybrid level, like its non-logarithmic counterpart, is defined by a pair of numbers ah and bh. Logarithmic hybrid levels can simply use the representation mechanism described in the GRIB edition 2 regulations for hybrid vertical levels.  However since the conversion formula is different and cannot be mapped linearly to the non-logarithmic form, this level type must have its own entry numbers in Code tables 3.15 and 4.5. In every other respect the overall data representation approach is unchanged.

The meeting approved the proposal for validation as Annex to paragraph 2.3.9, remembering however that another, height-based, hybrid coordinate was recently approved for operational use and requesting suitable editorial changes to the proposal.

It was expressed that the Meteorological Service of Canada (MSC) and ECMWF would cooperate in validation.

2.3.6	GRIB2 parameters for climate forecast products

NCEP has identified some additional GRIB2 parameters needed for the launch of a new climate forecast model in late 2010. The list was sent to the members of IPET-DRC in March 2010 for discussion, including an offer to provide sample messages for validation.  A few technical comments were received and subsequently addressed.

The meeting agreed the proposal to be approved by fast track.

2.3.7	GRIB2 parameters for ice analysis and forecasting products

MSC plans to implement a new gridded analysis for sea and lake ice in the coming year. One new GRIB2 parameter has been identified as necessary for the products from this analysis.

The meeting expressed the wish that the clarification provided with the proposal for the new parameters should be suitably shortened and added as a note to Table 4.5. The meeting therefore agreed the proposal with additional note as Annex to this paragraph to be approved by fast track.

2.3.8	GRIB2 parameters for storm prediction

NCEP has identified an additional GRIB2 parameter needed for use by its Storm Prediction Centre.  NCEP prepared sample data for validation of this new entry.

The meeting agreed the proposal to be approved by fast track.

2.3.9	Generalized vertical height coordinate in GRIB edition 2

Many NWP models use "hybrid vertical coordinates" to describe the vertical model grid. In GRIB2 the vertical coordinate type is defined in Code table 4.5, and the "vertical coordinate values" are provided in section 4.

The “problem” of a clear definition of hybrid coordinates was already discussed at the IPET-DRC-I in September 2009, coming up with new entries in the table, distinguishing between pressure and height based hybrid vertical coordinates. To describe these coordinate systems two parameters (A(k) and B(k)), so called vertical coordinate pairs, are needed. But there are more complicated hybrid coordinates, like the height based SLEVE (Smooth LEvel VErtical) coordinate, suggested by Schär et al., that do not fit into the existing GRIB2 definitions. For the basic “SLEVE” coordinate three vertical coordinate values and two different topology height fields are needed to define the height of the model levels. Other SLEVE variants even use more complicated construction algorithms.

The COSMO model used by the Consortium for Small Scale Modelling (COSMO: consisting of the national weather services of Germany, Switzerland, Italy, Greece, Poland, Romania and Russia) has the option to use this SLEVE coordinate. The ICON model, an ongoing development of DWD and MPI Hamburg, will use it as well.

It can be foreseen, that there will be more “sophisticated” vertical coordinate systems in the future with even more complicated defining algorithms. To overcome this problem, it was considered practical to specify the vertical grid as a 3D field in GRIB2.

Therefore a new entry in Code table 4.5 has to be specified for this “generalized vertical height coordinate” in addition with a “grid number” (section 4), defining the corresponding file with the 3D GRIB2 fields of the vertical system.

The meeting approved the proposal with slight modifications to the Note to the Code table 4.5 for validation as Annex to this paragraph.

2.3.10	New entries in Code Table 4.7 - Derived forecast

The growing importance of forecasts and warnings on small spatial scales and for short lead times is linked to intensified activities in the field of regional and local ensemble prediction systems at several met institutes and research institutions. Many of these activities focus on variables such as precipitation and wind gusts which have non-normal and skewed probability (density) distributions. A comprehensive and suitable description of the (statistical) properties of such variables requires more derived quantities than e.g. ensemble mean and spread.

DWD therefore proposed to include the quantities "interquartile range" (range between the 25th and 75th quantile), "minimum of all ensemble members" and "maximum of all ensemble members" in Code table 4.7 -Derived forecast.

The meeting agreed the proposal as Annex to this paragraph to be approved by fast track.

2.3.11	Issues for representing space weather in GRIB2

The NCEP Space Weather Prediction Center (SWPC) is the official U.S. source of space weather alerts, watches and warnings. It provides real-time monitoring and forecasting of solar and geophysical events which impact satellites, power grids, communications, navigation and other technological systems. As part of this mission, SWPC also develops operational models and products.

SWPC is looking to use GRIB2 to disseminate many of their products.  Upon initial examination of the GRIB2 regulations, a couple of issues have been identified, which require consensus from the full IPET-DRC before specific proposals for grids and parameters can be submitted for validation.

Some expected products will be Earth-based, but many will be solar-based.  Initial solar-relative grids will be simple latitude and longitude grids with regular spacing. After some discussion, the meeting recommended that appropriate modifications be made to existing Grid definition templates and to Code table 3.2 to allow for representation of extraterrestrial bodies.

The meeting discussed the definition of the word, Space weather, and how those were observed. There is a discipline 3, "Space product" in the existing Code table 4.2; however, those are derived from satellite observations, but as above, many space weather products are solar-based and some are Earth-based.  In view of this, the meeting finally approved for validation to change the name of the current "Space products" to "Satellite products" and create new discipline "4    Space weather products".

2.3.12	Proposal for coding radioisotopes in GRIB2

DWD presented a proposal for describing model outputs containing radioactive isotopes (e.g. atmospheric dispersion models). The present GRIB2 manual allows the coding of "Nuclear /radiology" parameter via "Product discipline 0 (Meteorological products) - Category 18" in Code table 4.1, such as "Air concentration of Caesium 137" (number 0) and "Ground deposition of Caesium 137" (number 3).

However, in order not to end up with a long list for every isotope/constituent type combination and therefore filling up the table, DWD proposed to use the Product definition template 4.40 – 4.43 for “Atmospheric Chemical Constituents” in combination with new entries for isotopes in Table C-14.

The meeting agreed the proposal with modification of the note to be approved by fast track.

2.3.13	How to code precipitation amounts in GRIB2 or clarification of the application of 	statistical processing

When reconsidering how to encode the "Total precipitation" in GRIB edition 2, there are two possibilities of encoding practices exist in parallel as follows. This provoked a lively discussion and further thoroughly consideration:

Total precipitation rate (prate, product discipline 0, parameter category 1, number 52)

and

Total precipitation (psum, product discipline 0, parameter category 1, number 8)

According to the official WMO documentation for GRIB2, the parameter psum (number 8) is deprecated, and instead, prate (number 52) together with the statistical processing “accumulation” (Code table 4.10) and suitable product definition templates (e.g. PDT 4.8) is used for total precipitation summed up over a specified time interval.

The prate has unit, kg m-2 s-1. To conform with the units and the documentation in a strict sense, DWD suggested necessity to normalize a summed total precipitation amount (unit, kg m-2) by the associated time interval before encoding in GRIB2.

DWD suggested encoding the total precipitation rather with parameter number 8 and the statistical process "Accumulation". (The statistical process is needed to identify the period for the total precipitation amount.). The consequence was that for a lot of "rate" parameter the corresponding "time integrated" parameter was needed (again).

Unfortunately the proposal contradicts the definition of some "TIGGE" parameters, which were defined after ECMWF's proposal was agreed in 2006. But by mistake a very important part of the proposal was disregarded (Section 4 - Guidelines on how to resolve ambiguities) and "Accumulation" in Code table 4.10 - Type of statistical processing was not changed in "Accumulation (time integrated)".

DWD and ECMWF revised the proposal with changing the existing name as Annex to this paragraph. However, there was a strong concern on changing existing name and units of entries, which were related closely to the issue of backward compatibility of GRIB2 tables.

The Team agreed the proposal needs more discussions after the meeting.

3.     BUFR AND CREX

3.1	Status of proposals at the last Joint meeting of CT-MTDCF and ET-DRC

Several proposals on amendments to BUFR and CREX were agreed for validation at or before the first meeting of Inter-Programme Expert Team on Data Representation and Codes (IPET-DRC) (Geneva, 15-18 September 2009).

The meeting reviewed the current status of validation on those proposals and updated the tables as Annex to this paragraph.

3.2	Amendments to BUFR/CREX (common aspects)

3.2.1	Versioning of BUFR and CREX tables

BUFR and CREX share relevant tables, nevertheless use different version numbers for identifying same tables to be referred to. Obviously, this is due to historical circumstance. When CREX became effective in 2000, the tables of BUFR in operation turned to version 8. Since then, different version numbers have been given BUFR and CREX almost synchronously, however, using different version numbers for identification is inefficient and confusing, in particular, taking account of annual or more frequent updates of tables to be expected.  It was therefore proposed to use same version numbers for tables of BUFR and CREX.

The meeting realized the inconvenience and agreed to use same version numbers for tables of BUFR and CREX as Annex to this paragraph and those would be fully synchronously updated.

3.2.2	A new entry in Specifications of octet contents

In Regulations for Reporting Traditional Data in TDCF, the requested precision is specified for each reported element in compliance with the unit and scale defined for the relevant BUFR/CREX descriptor. The traditional alphanumeric codes (TAC) often allow inclusion of reported values of lower precision, although values with higher accuracy might be available from the measurements (wind direction, wind speed, horizontal visibility, minimum ground temperature, height of cloud base, direction of waves, etc.). For example, wind direction dd (d0d0, d1d1, ..., dndn) = 26 represents any value from 255 to 264 degrees true (Code table 0877).

If a BUFR message is obtained by conversion from TAC data, the accuracy of the BUFR encoded data corresponds to the accuracy of data in the TAC message, from which the conversion was performed. Therefore it might be useful to indicate that BUFR data were converted from a TAC message.

The meeting discussed in detail and tried to seek a better solution. Using two bits instead of 1 bit of the original proposal was one of solutions, which was proposed by CPTEC.  A descriptor referring to a code table was considered as another solution. It was also suggested that such a change to the structure of a BUFR message, and not involving a simple change to Table B or Table D, should be reserved for the next edition (edition 5) of BUFR.

The chair of the team concluded that validation of the original proposal should be done for edition 4 (BUFR), and more general solution for edition 5 (BUFR) should also be developed.

The meeting finally approved the proposal by Dr Červená (CHMI: Czech Hydrometeorological Institute) for validation as Annex to this paragraph.

3.3	Additions and modifications of tables

3.3.1	Withdrawal of SIGMET templates proposed for validation

Under agenda item 3.3 of the 2009 meeting of the IPET-DRC, document 3.3 (11) was submitted by Jeff Ator on behalf of the USA. This document proposed a new version of the Table D entry 3 16 030 for encoding of SIGMETs to be introduced with version 15 of BUFR Table D.  At the meeting several Table D descriptors were agreed for validation.

After initial validation activities involving the Jeff Ator (USA) and Eva Červená, a change of priorities in the USA means that there is no longer a need to adopt these entries and as such their validation is no longer being pursued.

The meeting noted the situation change in USA and agreed to withdraw the proposal for SIGMET templates.

In the same sense, it was confirmed that satellite descriptors in validation, which were deprecated at the last meeting of the team, could also be withdrawn.

3.3.2	National data in templates for surface observations

Mr Yves Pelletier noted that national and regional data requires specific processing by the recipient, in addition to the more generic processing of standard SYNOP data. For efficient and unambiguous specific processing to occur in relation to national or regional data, such data must be quickly identifiable within the template by the processing software, preferably by a unique and simple mechanism.

The proposals, submitted to this meeting, that national data should be appended at the end of an existing WMO SYNOP template, are very helpful toward that end. Mr Pelletier proposed to add an explicit significance qualifier to indicate national or regional data. This would remove any ambiguity, in either human or automatic interpretation, in the event that a commonly used element descriptor should be used in both the national and international portions of the message.

Secondly, it would be convenient, while pre-processing the data prior to decoding, to have at least some foreknowledge of the presence of national or regional content without having to decode the message.  This would help recipients triage messages into categories that would lead to different processing outcomes. For instance:

i. 	messages that do not contain national data,

ii. 	those that contain national data the recipient may wish to process further, and those that contain national data the recipient may wish to ignore

Mr Pelletier proposed that the triage activity could be facilitated by using one or more of the bit flags located in octet 8 (BUFR Edition 3) or octet 10 (BUFR Edition 4) of section 1. Ms Sibylle Krebber noted that an alternative solution to this problem would be the use of sub-categories.

The meeting noted the idea to use sub-categories and recommended this approach instead of the bit-flags. Mr Pelletier will provide a list of suitable sub-categories for validation along with the proposed significance qualifier as Annex to this paragraph.

A discussion took place regarding the best way to provide guidelines to NMHSs concerning the addition of national data to existing WMO BUFR templates. Mr Pelletier summarized the main principles he had taken into consideration while developing his proposal. Those were derived from a reading and interpretation in the BUFR context of relevant WMO Technical Regulations and the Manual on Codes. Namely:

a.	The national data shall use the code form being used to represent international and regional data in the same message.

b.	If national data is represented in BUFR or CREX alongside international and regional data, local descriptors shall not be used.

c.	National data must be reasonably easy to add to messages in accordance to regulations.

d.	National data must be easy to identify as such by the recipient.

e.	National data should be brief and shall not change the fundamental character of the SYNOP message.

f.	National data must be easy to discard or ignore if that is the wish of the recipient.

The meeting proposed that it would be pertinent to use these notes as the basis for guidelines to be placed in an annex to the Guide on BUFR.

3.3.3	A proposal for Universal BUFR template for representation of Lightning data 	Formulated in June 2010

As part of the Public Weather Services, UKMO has provided a GTS long range lightning message from the 1940s in the form old SFLOC messages which covered an area of 40W to 40E, 30 N to 70N. This was declared obsolete, as it no longer reflected the accuracy obtainable by modern systems. A replacement was sought as there was not a suitable alternative available.

At the last meeting of the team, initial proposal was submitted. The proposal was agreed by the team for validation, and since then, UKMO has taken every effort to achieve the migration. Currently the only national BUFR representation of lightning data in use is that developed by DWD, all of the elements are included here, but has been expanded to give further elements for other systems.

The validation of UKMO proposal for a Universal BUFR template for representation of lightning data was concluded in June 2010. In line with the procedures laid out in the General validation and implementation procedures, three independent decoders were identified – MSC (Yves Pelletier), ECMWF (Milan Dragosavac) and NCEP (Jeff Ator).  All three decoders successfully decoded the test data supplied by the UKMO using the Universal ATD template. Feedbacks from all three validations are incorporated in the proposal.

The suggested entry for the data category / sub category in the Code table C-13 for the ATD template was Category 0 Surface data - land / Sub category - 30 Spherics locations (SFLOC). However, as SFLOC’s were no longer produced and sferics was mis-spelt, then Category 0 Surface data - land / Sub category - 30 Sferics locations was proposed.

The meeting noted the efforts taken by UKMO, and agreed the proposal as Annex to these paragraph to be approved as pre-operational, taking account of urgent user needs.

3.3.4	Update from JCOMM on developments of BUFR templates, including template for XBT 	data

The Joint WMO-IOC Technical Commission on Oceanography and Marine Meteorology (JCOMM) has continued to make progress in its work relating to Table Driven Code Forms since the last meeting of IPET-DRC. There is an active Task Team on Table Driven Codes (JCOMM TT-TDC) which has been working via email channels to support other JCOMM teams and progress with enhancing and reviewing the templates relating to Marine and Oceanographic data.

This task team aims to include as much metadata as possible in BUFR templates in future and reviewing the data types which are common to many JCOMM observing platforms in order to create consistent descriptions of observations using new sequences, i.e. taking a holistic view when developing templates and consider requirements for consistency between the different templates, moving away from the traditional platform based approach to GTS messages. Terms of Reference for the JCOMM TT- TDC:

http://www.jcomm.info/index.php?option=com_content&task=view&id=66&Itemid=0

It was reported by JCOMM representative, Ms Hester Viola that the XBT template for water temperature profiles had been revised in the last year in response to comments from the IPET-DRC and expert data users. It was also reported the templates (3 15 004 and 3 15 005) were being validated and encoded by two separate centres; however it was not clear yet whether two centres had successfully decoded the data, so the template should stay in validation for now.

The meeting agreed the proposal of a new entry in the Code table 0 22 178 to be approved by the fast track.  Activities by JCOMM are also summarized in the Annex to this paragraph.

3.3.5	Revision of sub-categories for ozone data, including telecommunication headers

A WIS-WIGOS Pilot Project entitled "Improvement of Dissemination of Ozone (total column, profiles and surface) and Aerosol observations through the WIS" (GAW-IDOA) was approved by EC-WG on WIGOS and WIS. This pilot project aims at improving the availability of ozone and aerosol in real time. The data are intended to be disseminated in BUFR or CREX.

Regarding ozone data, there are 3 types of measurements:

- Total ozone (amount of ozone in an entire atmospheric column [DU]),

- Ozone vertical profiles from ozone soundings (partial pressure of ozone at particular levels [Pa]),

- Surface ozone (concentration of ozone in the atmospheric boundary layer [molmol-1]).

It was, however, noted the data sub-categories in Common Code table C-13 and telecommunication headers in Tables C6 and C7 in the Manual on the GTS were not sufficient to distinguish these types of observations.

Dr Červená (CHMI) proposed a new entry of Common Code table C-13 as well as correction to the existing entry 000 under category 008. The meeting agreed the proposal as Annex to this paragraph.

3.3.6	Entries in Common Code table C-4 for a recording type

During the intersessional period, the JCOMM community has requested (via its TT-TDC) several additions to the common code table C-4 based on new or updated recorder types being used for temperature profile data. The representative of JCOMM, Ms Viola requested the meeting that these codes be reviewed and adopted in the next round of revisions.

The meeting agreed the proposed entries as Annex to this paragraph.

3.3.7	Entries in Common Code table C-5 for multiple satellite products

At the IPET-DRC-I (Geneva, 2009) the issue of the identification of data and products resulting from the blending of measurements from more than one instrument was raised. This is discussed in paragraph 3.2.4 of the final report of that meeting.  The meeting recommended that, as a short term solution, "virtual satellite" identifiers should be added to Common Code Table C-5.

According to the recommendation, several new entries were proposed.  The meeting discussed the proposal and agreed the proposal with minor modification as Annex to this paragraph for fast track.

3.3.8	BUFR/CREX descriptors related to AWS

The 14th session of the Commission for Basic Systems (Dubrovnik, Croatia, 25 March - 2 April 2009) reviewed the Functional Specifications for Automatic Weather Stations and adopted draft Recommendation 6.1/2 (CBS-XIV).

The meeting was informed that a document was submitted to ET-AWS-6 (Geneva, 22 to 25 June 2010), containing detailed analysis of the requirements for representation of the listed variables, a revised version of the Functional Specifications for AWS and a proposal for several new BUFR/CREX descriptors, which had been recommended for validation by the IPET-DRC-I (Geneva, 15 – 18 September 2009).

The ET-AWS-6 meeting examined carefully all proposals in the document ET-AWS-6/Doc. 10.1, agreed with the proposed BUFR/CREX descriptors and procedures for representation of the listed variables, and suggested some modifications of the requirements. The ET AWS members were encouraged to participate actively in the validation process of the proposed descriptors.  Out of them, Dr Červená submitted to the second IPET DRC meeting only descriptors that had been modified or proposed since the previous IPET DRC meeting, i.e. descriptors for UV-B radiation, humidity, lightning, depth of fresh snow and soil heat flux.

The meeting approved the proposal for validation as Annex to this paragraph.

The meeting was informed on the request of Mr. Karl Monnik, the Chair of ET-AWS, regarding terminology used in the names of some descriptors from Class 14 as shown in the Annex to this paragraph.

3.3.9	Descriptors for all sky radiance

Upon the introduction of the BUFR table D sequences 3 10 027, 3 04 035 and 3 04 036 for the encoding of all sky radiance data from SEVIRI on METEOSAT, a typographic error was introduced.  Inside the 3 04 035 sequence, 0 08 001 was used instead of the intended 0 08 011.

In order to resolve the error, two new BUFR table D sequences were introduced: 3 04 037, which is the same as 3 04 035, except the errant references to 0 08 001 have been replaced by references to 0 08 011, and 3 10 028, which is the same as 3 10 027, except that, rather than referring to 3 04 035, it refers to 3 04 037.

The meeting agreed the corrected entries 3 10 028 and 3 04 037 and agreed to delete 3 04 035 and 3 10 027 as Annex to this paragraph.

The meeting noted that the originally proposed sequence for 3-04-035 containing the wrong reference to 0-08-001 has been corrected in situ on the WMO web site.

3.3.10	Amendments to the Class 00 and use of UTF-8

Encoding/decoding software for BUFR, CREX and GRIB2, i.e. Table Driven Code Forms (TDCF), require reference tables in an electronic form.  As reported at the last meeting of IPET-DRC, in view of growing demand of TDCF tables in electronic forms, the Secretariat has been establishing database to export electronic tables concerned, which will be provided through not GTS but the Internet and possible other media.

It is planned that the database will consist of columns in four languages, i.e. English, French, Russian and Spanish, where necessary, and therefore a character set that can deal with those languages is indispensable.  UTF-8 is widely used and it can represent characters used in TDCF tables, such as characters of above languages, Greek characters in formulae and units, and proper nouns in other languages, in two (or more, as the case may be) octets.

On 8 April 2010, the Secretariat released initial tables of BUFR/CREX, exported from the database in UTF-8, to the focal points for codes and data representation matters for check and comments, in particular, on impacts of using UTF-8 in their own encoding/decoding systems. The Secretariat has not received any negative comments on use of UTF-8 through this survey.

BUFR and CREX have a function to exchange BUFR/CREX tables in respective forms. If a character set to be represented by entries in Class 00 is expanded to UTF-8, those tables could be exchanged in BUFR or CREX messages as they are in the database.  However, according to the Manual on the GTS (see 2.2.2 of Part II), limited number of characters in CCITT IA5 are permitted on the GTS, and therefore UTF-8 must not be used in CREX messages, consequently, along with BUFR messages to ensure the compatibility and conversion between the two codes on the GTS.

Table below shows availability of element descriptors in Class 00 to represent table entries of BUFR and CREX.

| Table | Column | Corresponding Class 00 entry | Column | Corresponding Class 00 entry |
| --- | --- | --- | --- | --- |
| In common | F, X, Y | 0 00 010-011-012 |  |
| Table A | Entry (Code figure) | 0 00 001 | Data category description (Meaning) | 0 00 002-003 |
| Table B | Element name | 0 00 013-014 | Unit | 0 00 015 |
|  | Scale | 0 00 016-017 | Reference value | 0 00 018-019 |
|  | Data width | 0 00 020 |  |  |
| Table C | Operator name | none | Operation definition | none |
| Table D | Element name | 0 00 013-014 | Descriptor defining sequence (Table references) | 0 00 030 |
| Code/Flag tables | Code figure/Bit No. | none | <meaning of code/flag> | none |
| Common tables | <different by table> | none |  |  |

Element descriptors in Class 00 are insufficient for representing BUFR/CREX Tables C, Code/Flag tables and Common Code tables. Descriptors for Code/Flag tables are proposed separately by USA in the item 3.3 (17).  Exchanging Table C entries in BUFR or CREX seems meaningless, because a new Table C entry needs not only update of Table C, but also upgrade of encoder/decoder. It was suggested that Common Code tables could be represented by descriptors for code/flag tables.

3.3.11	Validation of EUCOS BUFR template for representation of radiosonde data

In February 2010, the UKMO produced three BUFR samples of radiosonde data described by the 2007 version of EUCOS template, in which 0 02 191 (geopotential height calculation) being included. All comments provided on these samples were accepted by the UK MetOffice with the exception of the suggestion for deleting of 0 02 191. During the following discussion, Mr. Alexander Kats (Russian Federation) supported re-introducing of 0 02 191 requesting a new code figure for “Geopotential height calculated from radar height”. This additional requirement justifies the existence of 0 02 191, because 0 07 009 (geopotential height) would be used as the vertical coordinate for geopotential height calculated from GPS height as well as from radar height. The updated template and the descriptor/the code table were proposed, accordingly.

The meeting approved the proposal for validation as Annex to this paragraph.

3.3.12	Examples of usage TM 307093 for representation of nominal values

Template TM 307093 is capable to express representative heights of sensors as well as nominal values of selected variables (elements) of a BUFR template to which it is appended. Dr Eva Červená demonstrated the usage of TM 307093 in two examples, where 307093 had been appended to TM 307091. The ET-AWS-6 meeting expressed appreciation of availability of this material that might be very useful for Centers that would try to validate TM 307093.

The IPET DRC-II approved these guidelines for usage of a bitmap operator appended to a sequence containing delayed replications.

3.3.13	Proposal for modifications/additions related to representation of nominal values

The meeting approved the proposal as Annex to this paragraph to be treated as editorial.

3.3.14	New BUFR descriptors for ATMS data

The ATMS (Advanced Technology Microwave Sounder) instrument is part of the next generation operational sensor suite selected to fly on the National Polar-Orbiting Operational Environmental Satellite System (NPOESS) spacecraft. Sounding data from this instrument, when combined together with CrIS (Cross-Track Infrared Sounder) and VIIRS (Visible/Infrared Imager Radiometer Suite) data attached to the same satellite, will support continuing advances in NWP (Numerical Weather Prediction) models to improve short and medium-range weather forecasts.

At the first meeting of the IPET-DRC (Geneva, September 2009), NCEP presented an initial proposal for new BUFR Table B and Table D descriptors to support this effort. Subsequent feedback was received from ECMWF and EUMETSAT as well as the CGMS Task Force on Satellite Data and Codes (TFSDC).  Sample ATMS data was then made available for validation from NESDIS.

The meeting noted the validation activities and agreed the proposal as Annex to this paragraph for fast track.

3.3.15	New BUFR code table entries

NCEP requested two sub-centres under the U.S. NOAA National Ocean Service (Common Code table C-1 and 11) and a new entry in the 0 20 056 - Cloud phase.

The meeting noted the validation activities and approved the proposal as Annex to this paragraph for fast track.

3.3.16	New BUFR descriptors for VIIRS data

The VIIRS (Visible/Infrared Imager Radiometer Suite) instrument is part of the next generation operational sensor suite selected to fly on the National Polar-Orbiting Operational Environmental Satellite System (NPOESS) spacecraft. Sounding data from this instrument, when combined together with CrIS (Cross-Track Infrared Sounder) and ATMS (Advanced Technology Microwave Sounder) data attached to the same satellite, will support continuing advances in NWP (Numerical Weather Prediction) models to improve short and medium-range weather forecasts.

In this respect, NCEP proposed descriptors of Tables B and D, and relevant amendments. The proposal had been reviewed by colleagues from UKMO, Canada, ECMWF and EUMETSAT as well as the CGMS Task Force on Satellite Data and Codes.  Sample VIIRS data was also made available for validation on a NESDIS ftp server.

The meeting agreed the proposal as Annex to this paragraph for fast track.

3.3.17	New BUFR/CREX Class 0 descriptors

BUFR/CREX Class 00 allows new Table B and D descriptors to be defined for use within a BUFR or CREX message.  However, when defining a descriptor whose units are "Code table" or "Flag table", there is currently no way to define the actual entries within that table.

NCEP proposed some new Class 00 descriptors along with Table D descriptors to remedy this shortcoming.  An email discussion between NCEP, ECMWF, JMA and EUMETSAT in early 2010 was done on this issue.

The meeting noted that NCEP was willing to assist in validating the proposal with assistance from MSC and DWD, and approved the entries for validation as Annex to this paragraph.

3.3.18	A note to BURF/CREX descriptors 0 20 019 and 0 20 020

BUFR/CREX descriptors 0 20 019 (significant present or forecast weather) and 0 20 020 (significant recent weather phenomena) are defined with UNIT = CCITT IA5 for BUFR and with UNIT = character for CREX. This, with no further specification, would allow reporting the weather phenomena in any text form, even in open language. The significant present or forecast weather and the recent weather phenomena of operational significance are supposed to be reported in accordance with Code table 4678 for w’w’ and the following notes.

The meeting noted the problem and approved the proposal by Dr Červená as Annex to this paragraph.

3.3.19	Change to BUFR Manual - Footnote to radiological elements -

In BUFR Table B, 0 24 001 and 0 24 011 have footnotes describing Becquerel and Sievert as “new” units with conversion from the standard units of Curie and rem. These footnotes are in the Manual, Volume I.2, 2009 edition tables and were almost certainly wrong before that.

The UKMO proposed to consider removing these footnotes as the units are now obsolete. Becquerel replaced Curie and Sievert replaced rem in the 1990 Recommendations of International Commission on Radiological Protection. There should be no need to explain conversions, but if it is considered to be otherwise, they should be in notes to the Common Code table C-6.

The meeting agreed with UKMO, and approved to delete the footnote * as Annex to this paragraph.

3.3.20	Change to Common Code Table C-13 - Sferics - (see paragraph 3.3.3)

3.3.21	A BUFR sequence for NWP-generated vertical profiles

NWP-generated vertical profiles (from numerical upper-air analyses or forecasts) offer a means of exploring and assessing, for one location, the vertical structure of various meteorological parameters in the model forecasts. They are often used by operational meteorologists to supplement and enhance the information available from observed upper-air soundings or from gridded model data.

Canadian Meteorological Centre (CMC) has been producing NWP vertical profiles in BUFR, for internal use, since about 1992. Those first-generation profiles make extensive use of local descriptors. This makes them unfit for public dissemination or international exchange. Furthermore, since they remained largely unchanged since their inception about seventeen years ago, they do not reflect advances in available model parameters and in the BUFR tables since that time.

In undertaking to modernize the Canadian NWP-generated vertical profiles, MSC proposed the new descriptor sequence to be free of local descriptors. This would make the data intelligible to outside users and hopefully bring its usefulness to a wider audience and a greater number of visualization applications.

The meeting approved the proposal for validation as Annex to this paragraph.

In this regard, it was expressed that NCEP would volunteer the validation. The samples of vertical profile are available from

http://collaboration.cmc.ec.gc.ca/cmc/cmoi/IPET-DRC/BUFR/NWP-profiles/

3.3.22	Template for representation of synoptic reports from fixed land stations in Germany

Regarding the FM12 SYNOP, it is planned within DWD to finish the migration process this year.

To provide its users and customers of SYNOP data with the whole content of the existing SYNOP messages, the recommended template, TM 307086 suitable for SYNOP data in compliance with reporting practices in RA VI was extended.  The meeting expressed its appreciation of this proposal as it would provide tools for representation of additional synoptic data, in particular for several groups SPSPspsp, not being yet explicitly available for encoding in TDCF.

The meeting approved the proposal as Annex to this paragraph.

Dr Červená and Mr Pelletier offered to work on validation with Ms Krebber.

3.3.23	Development of Code table 0 20 063 – Special phenomena New Code table 0 20 112 	Supplementary cloud type

In FM12-SYNOP, a huge amount of possibilities is given to encode additional and special weather phenomenon with diverse combinations of 9SPSPspsp groups.  So far it is not possible to encode all these information in BUFR.

In view above, DWD proposed the Code table 0 20 063 (Special phenomena) and the descriptor 0 20 136 (Supplementary cloud type) and a relevant Code table.

Some special combinations of 9SPSPspsp groups are meant to report defined thresholds of wind speed; e.g. 902tt  91218  903tt, i.e. time of commencement and time of ending of highest mean wind speed (>=17,5 m/s). These are mandatory groups in DWD, if the highest mean wind speed has risen above 17.5 m/s. The highest mean wind speed in this period is reported separately if it is greater than 18 m/s.

In the original proposal, there was an inconsistency between bit length (in descriptor) and number of entries (in code table) with the same reference 0 20 112. The meeting agreed 0 20 063 duly corrected as Annex to this paragraph for pre-operational and approved 0 20 136 for validation.

3.3.24	Additional entries in code and flag tables

As well as 3.3.23, DWD requested some additional entries in the existing Code tables, such as 0 20 023 and 0 20 027.

It was felt that entries for conventional observations should be consistent with the Manual on Codes, Volume I.1 and existing observation practices.  The meeting therefore agreed the proposal with some corrections as Annex to this paragraph.

3.3.25	Status of existing proposals related to satellite data

A number of proposals for amendments to BUFR to support the representation of satellite data have been agreed for validation at the IPET-DRC-I (Geneva, 2009) and the joint ET-DRC and CT-MTDCF meeting (Geneva, 2008). These are included in tables I and II of the annex to Document 3.1 of this meeting.

The meeting was informed by Dr Simon Elliott the status of these proposals and agreed for fast track or approved for validation as follows.

- JASON2 OGDR data

It was proposed to add the Table D sequence 3-40-010 and the Table B entries 0-04-023, 0-04-024, and 0-04-025. Data were encoded using the new sequence and exchanged with NOAA and BoM.  Once all parties had validated the encoding, the new entries were used for operational data exchange. This began in April 2010.   <fast track>

- IASI data

It was proposed to refine the Table D entry 3-40-008, originally proposed at the CT-MTDCF/ET-DRC meeting, by adding scope for principal component scores and a database identifier for the eigenvectors used.  It was also proposed to correct the Table B entry 0-40-016 also proposed at the CT-MTDCF/ET-DRC meeting and to deprecate the Table D entry 3-40-006 (which would be superseded by the revised 3-40-008 definition). <done>

During the further validation of this proposal, it was discovered that the Table B entry 0-40-015 had been used for the score quantization factor, and that this Table B entry had already been allocated for NDVI data.  As such it was decided to introduce a new Table B entry, 0-40-026 for the score quantization factor.  It should have units = numeric, scale = 2, reference = 0, width = 16. The Table D sequence, 3-40-008, was updated to include a reference to 0-40-026 rather than 0-40-015.

The sequence 3-40-008 is being used for the operational dissemination of IASI data (with a subset of channels and no PC scores) via the GTS, and has been used to exchange IASI data (containing no channels but 290 PC scores) with ECMWF. <fast track>

- NDVI data

It was proposed to define the Table D entry 3-40-009 for the encoding of NDVI data from AVHRR.  It was also proposed to add Table B entry 0-40-015 for the NDVI value itself and to redefine code table value 2 in Code Table 0-08-013 as "twilight". The data have been exchanged using this sequence with ECMWF and these proposed changes have been successfully decoded. <fast track>

- Sub-category C-13

CT-MTDCF/ET-DRC, paragraph 3.3.1 contains proposals for additional data categories in BUFR Table A, together with additional international data sub-categories in Common Code Table C-13.  The additional entries were proposed in order to meet existing requirements and include the scope for classification of anticipated data types.  During the validation process, the need for the additional international data sub-categories as Annex to this paragraph has been identified. <for validation>

- Enhanced IASI data

CT-MTDCF/ET-DRC, paragraph 3.3.5.2 contains proposals for the encoding of enhanced IASI data.  The proposals comprised the creation of Table D entries 3-40-006, 3-40-007 and 3-40-008.  Paragraph 2 above explains that the proposal for 3-40-006 was subsequently withdrawn, and the proposal for 3-40-008 underwent further fine-tuning during its final validation.  The proposed sequence 3-40-007 is used operationally for the exchange of IASI data (all channels) on EUMETSAT’s satellite multicast system, EUMETCast. <fast track>

Dr Simon Elliott as the chair of the team encouraged members to summarize the status of multiple outstanding proposals for validation into a single document.

3.3.26	New entry in Common Code Table C12 for COSMO

A list of sub-centres for the originating centres 250-COSMO was proposed by request of IPET-DRC-I.

The meeting agreed the proposal as Annex to this paragraph.

3.3.27	Additional BUFR descriptors for the Evolution of clouds and Template version, 	additional notes in BUFR table B

As well as 3.3.23 and 3.3.24, DWD proposed new descriptor 0 20 137 and its code table and also a descriptor on a new concept to define version number of templates.  Moreover, it proposed notes to Class 20 and Table B.

The new descriptor for template version number was approved for validation, although there was some discussion as well as 0 20 137 (descriptor and code table) and a note to Class 20 as Annex to this paragraph.  It was pointed out that 0 01 110 had already used by other entry. It was agreed to change to 0 01 113.

The meeting approved the proposal as Annex to this paragraph for validation.

3.4	Regulations for reporting traditional observation data in Table-Driven Code Forms 	(TDCF): BUFR and CREX

3.4.1	Amendments to B/C Regulations

Regulations for Reporting Traditional data in TDCF (B/C Regulations) are included in Part C of the Manual on Codes. Dr Červená proposed modifications of the existing text of Regulations B/C 1.9, 5.9 and 10.7 based on the outcome of the discussion with Météo-France and members of the IPET-DRC to allow easier and more suitable inclusion of additional “instantaneous” parameters. Moreover, some clarification is needed in Regulations B/C 25 for reporting of high resolution sounding data.

The meeting agreed the proposal as Annex to this paragraph.

In this regard, Mr Alexander Kats expressed his view that there is a need to develop a template for upper-air soundings with geopotential height as the vertical coordinate suitable for migration of TEMP data, and with pressure to be reported with precision in units of a Pa.  His concern was recognized by the team, and it was felt appropriate template need to be developed.

3.5	Master tables for scientific disciplines other than meteorology

3.5.1	Master Table 10 review and update

A comprehensive report on the Master table 10 was submitted by representative of JCOMM, Ms Hester Viola.

The Master Table 10 was developed many years ago and revised to some degree in 2008 by JCOMM (Hester VIOLA with advice from Robert Keeley).

In 2010, Mr Robert Keeley undertook at thorough review to address the issues highlighted at the 2008 ET DRC meeting. At that meeting there was some discussion about how to develop a process to maintain the Master Table 10 (and other Master Tables in general) and the roles and responsibilities of JCOMM (WMO and IOC/UNESCO).

In her report on the Master Table 10 management and updates, Ms Viola discussed the roles and responsibilities of all parties involved in developing and maintaining Master Table 10 and some of the challenges it involved. She sought feedback from the team on the proposed procedure for maintaining the Master Table and suggested that IOC/UNESCO and JCOMM should develop a validation plan for the Master Table.

The meeting expressed its support for the overall concept of different BUFR Master Tables and agreed to assist JCOMM where necessary to help advance the effort towards a Master Table 10 for oceanography.  This effort would be expected to provide a valuable set of "lessons learned" for the development of additional Master Tables in the future, including possibly for satellite data, atmospheric chemistry and other disciplines.

4.     TRADITIONAL ALPHANUMERIC CODES (TACs)

4.1	Amendments to the aeronautical codes, FM15, FM16 and FM51

Amendment 75 to ICAO Annex 3/WMO Technical Regulations [C.3.1] that were adopted by the ICAO Council on 22 February 2010 and will become applicable on 18 November 2010. Consequently, ICAO proposed amendments to the aeronautical codes, METAR (FM 15), SPECI (FM 16) and TAF (FM 51).

The Secretariat has sent the amendments to participants in this meeting before the meeting for comments.  A minor modification was made, accordingly.

The meeting approved the proposal as Annex to this paragraph.  Noting the possible additional financial burden or operational problems for the implementation of the amendments, the meeting recommended to submit them to the CBS Extraordinary session to be held in November 2010 in Namibia with the date of implementation in November 2011.

In this regard, the meeting strongly recommended that ICAO submit their requirements to WMO as soon as available, not waiting for a meeting of the IPET-DRC, so that the new procedures for the adoption of amendments be possibly used to better satisfy the ICAO time requirements.  In the case of the requirements related to Amendment 75 to ICAO Annex 3, if these requirements were submitted to the IPET-DRC in time for the inclusion of the relevant amendments in the list of amendments, which were submitted in 2009 to WMO Members for adoption between CBS sessions, it would have been possible to invite WMO Members to agree on the date of implementation of the amendments in November 2010.

4.2	Discontinuation of the monthly upper-air CLIMAT TEMP reports

The 62nd session of the Executive Council (EC-LXII) (Geneva, 8 to 18 June 2010) was informed that the 15th session of the Commission for Climatology (CCl-XV) (Antalya, Turkey, 19 - 24 February 2010) decided the provision, dissemination, monitoring and international exchange of the monthly upper-air CLIMAT TEMP reports shall be discontinued with immediate effect after the publication of the resolution in the abridged CCl-XV final report.

The meeting discussed measures that IPET-DRC should take, where appropriate, with respect to;

- FM75 CLIMAT TEMP, e.g. notes similar to those in aeronautical codes,

- B/C35 – Regulations for reporting CLIMAT TEMP and CLIMAT TEMP SHIP and data in TDCF

- migration matrix.

The meeting agreed;

- not to change FM 75 CLIMAT TEMP, FM 76 CLIMAT TEMP SHIP

- to delete B/C35 (by procedures between CBS sessions)

- to move FM75 CLIMAT TEMP, FM 76 CLIMAT TEMP SHIP to the category "Obsolete"

4.3	Past weather reporting in hourly synoptic observation

In Regulations for Reporting Traditional data in TDCF, the time period for reporting past weather is specified in regulations B/C 1.10.1.7.1, B/C 1.10.1.8.1, B/C 5.10.1.7.1, B/C 5.10.1.8.1, B/C 10.8.1.7.1 and B/C 10.8.1.8.1 as follows:

The time period (0 04 024) covered by past weather (1) and past weather (2) shall be expressed as a negative value in hours:

- Six hours, for observations at 0000, 0600, 1200, and 1800 UTC;

- Three hours for observations at 0300, 0900, 1500, and 2100 UTC;

- Two hours for intermediate observations if taken every two hours.

- One hour for intermediate observations if taken every hour.

In the TAC Regulations FM 12.2.6.6.1 and to FM 12.2.6.7.1, however, the definition of time period for reporting past weather from hourly synoptic observation is missing:

- Six hours, for observations at 0000, 0600, 1200, and 1800 UTC;

- Three hours for observations at 0300, 0900, 1500, and 2100 UTC;

- Two hours for intermediate observations if taken every two hours.

The negative impact of this shortcoming of the TAC regulations was clearly demonstrated in synoptic data produced by an RAVI country in BUFR, where time period 0 04 024 for past weather at 10 UTC and 11 UTC was reported as -4 and -5, respectively.

Taking into account the fact, Dr Červená proposed to add a new point (d) to FM 12.2.6.6.1 and to FM 12.2.6.7.1 as Annex to this paragraph.  The meeting considered the impact of this amendment and agreed the proposal to be approved by the procedures between CBS sessions.

4.4	Observation practice in the Manual on Codes

The tenth session of the CBS Management Group (MG) was held in Geneva, Switzerland from 24 to 26 June 2009.  The MG discussed the proposals of the OPAGs for the work plans of the ETs.  The MG invited the chairs of the OPAGs to review the work plans, taking in particular into account the decisions, guidance and requirements from sessions of Executive Council (EC-LXI) and Regional Associations (XIV-RA II, XV-RA IV).

The IPET DRC-II meeting discussed again the task to identify the observation practice elements contained in the Manual on Codes and to pass them to OPAG-IOS for inclusion in observing standards documentation.  The meeting expressed their concern about several aspects of this issue, in particular:

- Reduction of the text of regulations in the Manual on Codes, Volume I.1 would complicate significantly the work of observation experts,

- It is far from obvious to which “observing documentations” this extracted observation practices should be transferred,

- The elimination of observation practices might result in reducing some lines in the Manual.  The extracted text, however, would have to be replaced by hyperlinks that might be even longer than the extracted observation practice in case of several TAC regulations.

5.	MIGRATION TO TABLE DRIVEN CODE FORMS

5.1	Migration status

5.1.1	Result of WWW Monitoring

    - The Secretariat presented a monitoring report on the migration to TDCF based on the following information:

- The list of BUFR bulletins included in the catalogue of meteorological bulletins (Volume C1)  containing main synoptic observations from fixed land stations with TTA= ISM in the abbreviated heading TTAAii and radio soundings from fixed land stations with TTA= IUK or IUS in the abbreviated heading TTAAii;

- The monitoring statistics provided by MTN centres for the exercises of the Integrated WWW monitoring (IWM) and/or Annual Global Monitoring (AGM), and the Special MTN Monitoring (SMM) carried out from 1 to 15 July 2009, October 2009, January 2010 and April 2010.

    - From this monitoring report, the meeting noted that:

- The number of stations, for which BUFR surface data were expected or received, is 1062 out of the 4362 RBSN surface stations; BUFR surface data were expected from 862 stations (ref. Volume C1) and reported as received from 967 stations; the locations of the stations are shown in Figure 1 of the Annex to this paragraph;

- The number of stations, for which BUFR upper-air data were expected or received, is 239 out of the 791 RBSN upper-air stations; BUFR upper-air data were expected from 167 Stations under IUK bulletins and 101 under IUS bulletins (ref. Volume C1), and reported as received from 238 stations; the locations of the stations are shown in Figures 2 and 3 of the Annex to this paragraph.

    - The evolution of the numbers of RBSN stations for which BUFR surface or upper-air reports were included in Volume C1 or received by MTN centre are shown in Annex to this paragraph for the period April 2008 to April 2010. The increase of these numbers during this period is more than 100 per cent with a quasi linear progression for surface reports and a major increase in the beginning of the period for upper-air reports.

    - The meeting stressed the importance of the monitoring reports for the follow-up of the migration and invited the Secretariat to continue coordinating the monitoring exercises and providing analysis of the monitoring reports. The meeting invited the ET-OI to consider extending the monitoring of the availability of data to BUFR CLIMAT, BUFR PILOT, CREX SYNOP and marine BUFR data.

    - The meeting agreed to recommend:

- To invite the focal points for codes and data representation matters to continue reviewing the monitoring information and, if this does not reflects the status of implementation of the national migration plan, to ensure that action is being taken within their countries in order to mitigate the possible deficiencies in the insertion of BUFR bulletins into the GTS;

- To invite the RTH focal points:

- To continue reviewing the monitoring information,

- To take action to ensure that the BUFR bulletins are distributed on the GTS and that Volume C1 is updated,

- To ensure that their RTHS provide monitoring results for the monitoring exercises organised by the Secretariat, in particular the IWM, and post the monitoring results on the WMO server as soon as possible after the end of the monitoring period.

- To invite the Secretariat to make available monitoring reports on the migration as soon as possible after the end of the monitoring period.

5.1.2	Status of the national plans for the migration to TDCF and step-by-
	step migration by zone

    - Through the WMO letter OBS/DRM/TDCF (PR-6461) dated 17 November 2009 (see http://www.wmo.int/pages/prog/www/WMOCodes/MigrationInfoDocum.html), the WMO Members were invited:

- To provide information on the national migration plan of their country, in particular to provide/confirm the dates at which your country was or will be in a position to send and receive data in TDCF and stop needing receiving data in TAC for national purposes;

- To inform the Secretariat on any difficulties that their country could experience in meeting the deadline of November 2010 to complete the migration of the data category 1 (SYNOP, TEMP, PILOT and CLIMAT).

.

    - The Secretariat received information from 57 countries. In addition to these 57 countries listed, in 2008 nine countries provided information on the national migration plan of their country, in particular on the dates at which their country was or will be in a position to send and receive data in TDCF and stop receiving data in TAC. Out of 66 countries (see also annex to this paragraph):

- 46 countries (70 per cent)  were or will be in a position to send and receive data in TDCF, and 42 countries (64 per cent) will  be in a position to stop receiving data in TAC before 11/2010;

- 20 countries (30 per cent) will in a position to send and receive data in TDCF and stop needing receiving data in TAC for national purposes after 11/2010 or at a date not yet defined, or needed external assistance for the migration.

    - Eleven countries expressed the need for assistance for the migration: Bangladesh, Bosnia and Herzegovina, Cyprus, Lao PDR, Mauritius, Mongolia, Nigeria, Portugal, Sudan, United Republic of Tanzania and Uzbekistan. Advices on the possible assistance were provided by the Inter-Programme Expert Team on Data Representation and Codes. RTHs provided the following information on assistance that they could offer:

- RTH Brasilia can compile new bulletins and produce BUFR messages automatically. This capability allows RTH Brasilia to help other countries in the Region to convert their bulletins from TAC to BUFR, if necessary;

- Operating RTH Beijing, CMA keeps in contact with other WMO Members in its zone of responsibility and will endeavour to provide technical assistance and guide to them if required;

- RTH Prague will provide, upon request, a TDCF to TAC conversion facility for an NMHS unable to decode/process TDCF;

- RTH Wellington will continue to provide a TAC – TDCF conversion facility for associated NMHS who are unable to produce or decode TDCF.

    - The meeting recommended to urge the focal points for codes and data representation matters to provide or update the information on the national plans for the migration to TDCF.

5.1.3	Data issued from Data Collection Platforms (DCPs)

    - The question of migration of SYNOP data issued from DCPs was raised at the Joint fourth meeting of RARS Implementation Group and IGGDS Implementation Group (Geneva, Switzerland, 22 - 24 March 2010). The joint meeting noted that, in the case of DCPs in remote areas (e.g. buoys), upgrading the DCP for TDCF can be unpractical (very expensive or unfeasible) and raised the question of how to make the TAC-TDCF conversion of DCP messages after the collection by the satellite and before their injection into GTS.  The joint meeting felt this issue should be discussed by other CBS Expert Teams. The meeting noted that satellite operators (EUMETSAT and USA) are planning to encode DCP data into BUFR before their insertion into the GTS. The meeting stressed the importance of  ensuring the quality control of the data in accordance with the following procedures :

a.	In principle, DCP data collected by satellite operators should be sent back to the DCP operators before international exchange,

b.	Quality control of DCP data should be done by DCP operators,

c.	Quality controlled DCP data should be injected into GTS in cooperation with GTS centres concerned.

    - The meeting invited the ET-OI to further consider the exchange of the DCP data in TDCF on the GTS.

5.1.4	Information provided by members of the IPET-DRC

    - The meeting was informed of training activities within South and East Africa, in particular with the support of SADCC and the Tanzanian Meteorological Agency. There are many challenges which the Member countries still face in the implementation process. Some of the key issues are:

- Only SYNOP Message has been handled comfortably; TEMP and CLIMAT need time to be handled carefully with much understanding.

- Some Member countries have not managed to up-date the Message Switching System (MSS), thus unable to give the expected results outputs: very few African Countries do appear in the monitoring reports.

    - In view of the fact that SADC Meteorology Project has started to support members of SADC to conduct a training seminar aiming at members understand the issue of migration, the meeting recommended to support the organisation of the training activity, for example by supporting the participation of experts from the IPET-DRC or advanced Centres. With a view to making it possible to exchange the TDCF bulletins on the GTS, the meeting recommended that the required update of the MSS be considered with the highest priority with appropriate support, for example from the WMO Voluntary Cooperation Programme.

    - In Region II, the Theme Leader of Data Representation and Metadata provided assistance to several Member countries in Region II for the development of their national migration plan. Using the IWM and SMM reports, the Theme leader monitored the availability of TAC and TDCF reports and bulletins issued from Region II. The monitoring reports show that there was no significant progress in the migration in Region II during the last two years. The meeting noted with appreciation that RTH New Delhi will facilitate the TAC-TDCF conversion for its area of responsibility.

    - China has inserted the BUFR SYNOP and TEMP bulletins into the GTS since August 2008 and planned to insert BUFR PILOT bulletins into the GTS in November 2010.  The meeting recognized the need for a new entry in Common Code Table C-2 for Chinese 1680 MHz radiosonde system and suggest China to submit a respective proposal.

    - The status of the migration to TDCF in Region III was discussed during the a meeting of the Working Group on Implementation and Planning of the World Weather Watch in Region III held in Asuncion, Paraguay, from 19 to 23 April 2010. The meeting noted the low level of awareness of the problem in Region III. Information on the rationales for the migration, the time schedule and the consequences was provided to the participants with a view to speeding up the development of national migration plans within their own countries.

    - In Region IV, USA planned a transition period during which U.S. TAC observations would be converted to BUFR for insertion onto the GTS. The transition period would tentatively begin in October 2011 for Category 1 data and conclude for all data types in October 2015.  During this time, a simultaneous effort would be made to begin transitioning all U.S. observing systems and users to the direct use of BUFR.

    - Canada envisions putting BUFR TEMP data on the GTS by the end of 2010, alongside traditional TEMP bulletins. Being able to receive and process BUFR TEMP/PILOT data in place of the traditional alphanumeric data is more challenging and this will require assuring that national data display applications and NWP data assimilation system at CMC have the required capacity, and this exercise could be expected to conclude in 2011.  SYNOP data production in BUFR is being addressed, but it will take longer than TEMP data to reach operational production. The data must be converted to BUFR SYNOP from a variety of domestic sources.  A software framework for doing so is being developed. With regard to reception and processing of SYNOP data in BUFR, from domestic or international sources: the capacity to do so at the complete exclusion of the traditional alphanumeric synoptic data forms remains to be developed. Resourced plans exist to do so.  A timeline to November 2012 would appear reasonable for SYNOP migration in Canada.

    - Canada and USA proposed that a MTDCF regional plan be developed for the whole of RA IV, understanding that most other countries in RA IV are looking to the USA and Canada to lead the migration effort on behalf of the entire Region.

    - As was announced a year ago, Environment Canada released a BUFR library named libECBUFR, as open-source, under the LGPL license.  Some NMHSs, most notably Brazil’s INMET, have expressed an interest in using libECBUFR.  A new feature worth mentioning is that facilities for multilingual usage have been added in the last year. English and French are currently supported, and Canada would accept translation files in other languages.

    - The RA VI Management Group endorsed the establishment of a Task Team on Regional Migration to TDCF (TT-MTDCF) under the Technology Development and Implementation Working Group. The RA VI Rapporteur (Chair of TT-MTDCF) closely followed the migration process in RA VI and responded to questions/requirements expressed by RA VI countries, in particular testing BUFR messages from NMHSs.

    - There are already 20 countries/territories of RA VI producing at least one type of Category 1 data in BUFR (Belgium, Czech Republic, Denmark and Faroe Islands, France, Germany, Greece, Greenland, Hungary, Ireland, Israel, Italy, Jordan, Netherlands, Norway, Serbia, Sweden, Switzerland, The Former Yugoslav Republic of Macedonia, Turkey, United Kingdom of Great Britain and Northern Ireland); the underlined countries are producing all types of Category 1 data in BUFR. Moreover, some of the BUFR samples, received for testing e.g. from Romania, are practically ready to be distributed over the GTS.

    - RA VI Members were recommended to use TM 309052 for the representation and distribution of sounding data with the recommended resolution of 2 seconds. The meeting agreed to draw the attention of the ET-OI on its recommendation (see paragraph 3.4.1) that if high resolution data are reported, only one BUFR message should be sent when the 100 hPa level is reached and only one BUFR message shall be produced when the sounding is completed, provided that all standard and significant levels are properly identified in compliance with the relevant B/C 25 Regulations. With a view to monitoring the progress in the presentation of the sounding data with high resolution, the meeting invited the ET-OI to consider recommending the inclusion of information on the template used to present the sounding data, such as the resolution, in the column “remarks of the Volume C1 for each relevant bulletin.

    - Russian Federation was developing a national migration plan with a view to migrating, in a first step, surface data as soon as possible, and, in a second step, upper-air data.  Russian Federation will provide assistance to other countries of the Commonwealth of Independent States (CIS) within the framework of the cooperation programs of the CIS Interstate Council for Hydrometeorology.

5.2	Request from the CBS MG-XI on MTDCF

5.2.1	The eleventh session of the CBS Management Group (MG-XI) (Geneva, 17 - 19 March 2010) noted that WMO Members were experiencing difficulties in meeting the deadline of November 2010 to complete the migration of the data category 1 (SYNOP, TEMP, PILOT and CLIMAT) in accordance with the migration plan. The MG also noted that some RTHs had already offered to assist other countries in the migration to TDCF and agreed to encourage all RTHs to facilitate the migration to TDCF, in particular, by assisting countries in their zone of responsibility.

5.2.2	Noting the difficulties met by WMO Members in meeting the deadline of November 2010, the sixty-second session of Executive Council (EC-LVII) (Geneva, June 2010) invited CBS to consider measures with a view to ensuring that all WMO Members continue accessing the observational data available on the GTS in the appropriate format as well as to facilitate and foster the migration from TAC to TDCF.

5.2.3	As requested by the MG-XI and in view of discussion by the EC, the Secretariat has sent a letter to WMO Members on 21 July 2010,

urging

- Those Members not yet having developed or implemented their national migration plan to do so;

inviting

- Those Members having developed and/or implemented their national migration plan to assist other Members to do so, and to continue exchanging TAC and TDCF data in parallel when needed to ensure that all WMO Members continue accessing the observational data available on the GTS in the format they can use, waiting for further recommendation of CBS and decision by WMO Congress or EC on this question;

- To provide or continue providing updates of the national plan of your country for the migration to TDCF to the Secretariat, in particular updates concerning  the dates at which your country will be in a position to send and receive data in TDCF and stop needing receiving data in TAC for national purposes;

- To provide the Secretariat with any further information on the possibility for the Member countries to assist WMO Member countries in the migration to TDCF, in particular if a Member country operates an RTH;

- To update as required the list of national focal points for codes and data representation matters, including the migration to TDCF (see http://www.wmo.int/pages/prog/www/Documents/ FocalPoints-Migration.doc).

Migration matrix

5.2.4	The consensus of the meeting was that the target dates in the original migration matrix should not be extended, because to do so would detract from the urgency of the migration and convey a sense that these dates, and indeed the migration itself, were not to be taken seriously.  It would also be unfair to the WMO member states which made the effort to adhere to the original target dates.  However, to acknowledge the reality that many WMO member states will not meet the original target dates for Category 1 data, the meeting agreed that dual dissemination of TAC and BUFR could, if needed, continue past the original target dates and agreed to add the deadline of November 2014 to stop dual dissemination of Category 1 TAC and BUFR data.  The meeting also agreed to add the deadline of November 2014 to stop dual dissemination of Category 4 TAC and BUFR data in the same manner as Category 1, as a logical consequence. The meeting recommended amending the migration matrix as given in the Annex to this paragraph.

5.2.5	Regarding the marine data, the meeting noted that so far the BUOY and TESAC have begun migration, as well as TRACKOB and BATHY.  For other message types (e.g. SHIP, TEMP SHIP etc), the meeting was informed that validation of all these types will begin in mid 2011.

5.3	Encoder software for BUFR/CREX available for MTDCF

The meeting was informed of availability of encoder/decoder for the migration to TDCF developed by advanced centres free of charge for WMO Members, and invited to update the information included in the table;

http://www.wmo.int/pages/prog/www/WMOCodes/Software_encoder_decoder.doc

and also attached as Annex to this paragraph.

The meeting noted that a survey could be conducted to focal points for codes and data representation matters on software for migration operationally available, if needed.

At the last meeting of IPET-DRC (Geneva, 15 - 18 September 2009), an issue of erroneous BUFR messages, which were rejected from the WWW monitoring statistics, was reported. By and large, the meeting was supportive to take appropriate measures for confirming validity of format of BUFR reports.

Errors in BUFR reports can be categorised into three types.

Type A - Architecture level

Erroneous basic information to define architecture of a BUFR report, such as length of a BUFR report and each section, flag for existence of optional section, and replication factors, which are critical to decode a BUFR report

Type B - Attribute level

Erroneous attributes, in other words, "metadata", of observed or forecasted values, such as station ID and vertical levels of upper-air observations

Type C - Conversion level

Erroneous observed or forecasted values by incorrect algorithm or reference tables for conversion, such as tables of cloud type (0 20 012) and present weather (0 20 003), into which several TAC tables are combined

Type A errors are detected by decoders, because such reports cannot be decoded correctly.  Detection of type B errors needs advanced decoders, in which error detecting systems are incorporated.  However it would be impossible to detect all the errors on this level even by advanced decoders without information on meteorological validity.

BUFR needs conversions from observed or forecasted values to values in binary representation.  It is difficult to detect type C errors of some elements by decoders.  Quality monitoring with NWP models would be effective instead.

As discussed at the last meeting, comparison between original data and encoded BUFR reports would be simple and effective for the validity confirmation.  In view of limited resources available for this activity, validity of BUFR reports in category 1 should be confirmed at first.

The Secretariat invited participants to volunteer to select original TAC reports to be converted to BUFR (at least one centre) and to decode BUFR reports converted from TAC (at least two centres). However, there were many arguments on this initiative such as;

- software developer should do it

- data should be checked before release

The meeting stressed that it was important for originators of BUFR data converted from TAC, that these originators would check as much as possible for data conversion errors as well as structural errors in the BUFR messages prior to insertion of these messages onto the GTS.  However, the meeting recognized that originating centres might not be able to detect certain types of errors, so it would be necessary for receiving centres and other end users to carefully perform their own validation of these converted BUFR messages during the dual dissemination period, while the original corresponding TAC data would still be available. It was also noted that monitoring exercises for SYNOP and TEMP migration were currently being performed under the sponsorship of the WMO Secretariat.

6.	MANUAL ON CODES

6.1	Electronic publication of the Manual on Codes, including database

The Secretariat presented the current situation on electronic publication of the Manual on Codes as follows.

In order to facilitate access to reference information required for World Weather Watch operations, the fifteenth Congress (Cg-XV) reaffirmed that the Manual on Codes (WMO-No. 306) should be posted on the WMO server (see 3.1.4.4 in the report of Cg-XV).

Cg-XV took note the report of the 2007 Meeting of Presidents of Technical Commissions, which recommended that, instead of issuing supplements to publications, WMO issued updated versions of these publications electronically, provided this solution is cost effective.

In accordance with the above, the Secretariat published the 2009 edition of the Manual on Codes, Volume I.1 and I.2, and has provided them through the WMO web site (http://www.wmo.int/pages/prog/www/WMOCodes.html) and in CD-ROM.

As briefly informed at the last meeting of IPET-DRC (Geneva, 15 - 18 September 2009), the Secretariat has been developing database of tables of Table Driven Code Forms (TDCF), i.e. GRIB edition 2, BUFR and CREX in view of growing demand of the tables for computer processing.  On 8 April 2010, the Secretariat released preliminary electronic tables of BUFR and CREX exported from the database in txt, xml and doc forms to the focal points for codes and data representation matters, following detailed check by experts.

The expected publication of the Manual on Codes, Volume I.2 will incorporate tables of TDCFs in the database for efficiency and convenience. The Secretariat therefore drafted the Manual on Codes, Volume I.2 mainly in doc form that incorporates tables exported from the database.

The electronic Manual on Codes, Volume I.2 consists of three levels:

- Level 1:	main body of the Manual

- Level 2:	code bodies with links to tables

- Level 3:	tables

The level 1 consists of basic information, such as administrative information, information on composition of the Manual and technical terms, and also links to each code.

In the Manual, notes to tables will be appended to those for human reading (doc and pdf form) and validation entries will not be included as an official publication.

The Manual on Codes has been available in electronic form (pdf); however, some advantages of new form could be expected as follows;

- Better accessibility to necessary information

- Compatibility with tables of TDCFs for computer processing

- Flexibility of update (each file could be updated as appropriate and distributed from the WMO web site).

6.2	Procedures for amending the Manual on Codes

Procedures for amending the Manual on Codes have been introduced and modified with a view to saving time during the CBS sessions or reducing delays in approval of amendments in addition to the Regulations 9(5) of the WMO General Regulations, which sets down a role of the President of WMO on approval of any recommendation of an association or a commission.

Four types of procedures are available practically to amend the Manual on Codes at present; however, given that the 62nd session of Executive Council (EC-LXII) (Geneva, 8 -18 June 2010) invited CBS to consider extending the procedure for adoption of amendments between CBS sessions to other Manuals, such as the Manuals on the GDPFS and the GTS, it was felt that procedures established for the Manual on Codes could be adjusted, where necessary, so as to form the basis for procedures to amend other Manuals.

The Secretariat explained that users of TDCF have been increasing in accordance with the progress of migration to TDCF. Therefore, the three-step mechanism, in which focal points for codes and data representation matters are not involved, should be limited. Instead, the fast track should be initiated twice a year (if not needed, one could be cancelled) with date of implementation.

The three-step could remain with possible modifications, just in case, for emergency that cannot be covered by fast-track.

The meeting noted the Procedure for adoption of amendments between CBS sessions should be applied to amendments, which do not create an additional financial burden on Members nor pose operational problems (see paragraph 3.5.2.1 of the report of EC-LXII). Consequently, the Procedures for adoption of amendments during CBS sessions basically should be limited to major amendments to the Manual and amendments to the administrative aspects of the Manual.

For validation entries, approval by the president of CBS is required under the current procedures; however, entries for validation could be modified or even withdrawn, when it is inevitable, through validation processes. Furthermore, those entries never proceed to the approval processes for operational (or pre-operational) use, which also requires approval by the president of CBS, unless validations are completed.

The meeting discuss this feasibility and agreed that validation entries can be allocated by the chair of IPET-DRC, paying attention to practical problems not to be expected and accessibility of validation entries currently available from the WMO web site to be assured.

In accordance with the above, the meeting agreed the revised PROCEDURES FOR AMENDING THE MANUAL ON CODES as Annex to this paragraph.

7.	COLLABORATION WITH OTHER CBS TEAMS

7.1	Collaboration with the Inter-Programme Expert Team on Metadata and Data Interoperability (IPET-MDI)

7.1.1	CBS tasked the IPET-DRC to review and clarify the WMO data representations, in collaboration with the Inter-Programmed Expert Team on Metadata and data interoperability (IPET-MDI), to ensure efficient and effective implementations, interoperability and consistency with the WMO Metadata Core Profile and with the WMO data model that it is starting to be developed.

7.1.2	The meeting noted the information on the development of standards for WMO data and associated metadata relevant to WIGOS given in the document “WIGOS standardization framework for data and associated metadata” (see IPET-MDI-I/Doc. 4.2(1)). The IPET-MDI invited the Secretariat to continue updating the document “WIGOS standardization framework for data and associated metadata” with a view to fostering the awareness of the development of the standards for data and metadata for the development of the WIGOS.

7.1.3	The meeting noted the following action related to the development of a WMO conceptual model of data representation:

- A test of the transmission on the ICAO aeronautical fixed service (AFTN) of a METAR instance of the three-level Modelling of WMO data products based on BUFR/CREX tables presented in XML was carried out in July 2009.  The second session of the ET-ODR (Paris, November 2009) concluded that XML can be accepted for encoding & exchange OPMET data within the aviation community,

- A Memorandum of Understanding (MoU) between WMO and the Open Geospatial Consortium (OGC) was signed in November 2009. The WMO/OGC MoU is instrumental in providing the mechanism for the co-ordination between the activities carried out by OGC and WMO with a view to developing the use of ISO/OGC standards for the WIS. OGC established two Domain Working Groups (DWG): a Meteorology and Oceans DWG (Meteo DWG) and a Hydrology DWG (Hydrology DWG). OGC and WMO established a WMO-OGC coordination team for the Coordination of OGC and WMO activities.

7.1.4	The meeting noted with appreciation the work done by Mr G. Ross (UK) to convert BUFR to a canonical XML. The objective of automatically transforming all BUFR features, inherited features, discriminated features, association, attributes and coverages into ISO/OGC feature catalogues, is difficult to achieve at present. Instead the canonical XML should be developed and used to identify features required in restricted feature catalogues for individual communities, such as for Aviation, for Hydrology or for particular public requirements such as INSPIRE. Further work will be needed for particular implementations, but using a canonical XML it would be possible to define formal definitions of community feature catalogues using W3C and ISO standards which would allow the different catalogues to be maintained in line with the WMO BUFR maintenance process.

7.1.5	The meeting noted the information provided to the twentieth meeting of the ICAO Meteorology Group of the EANPG (Paris, 6 - 10 September 2010) (METG) concerning the migration towards table-driven data representation, and in particular the following intermediate milestones (completion dates and the responsible organization in brackets) that were considered necessary for:

- CBS IPET-MDI to undertake further tests using various models, including the weather information exchange model (WXXM), and to prepare documentation for the CBS-Ext. (2010) (second half of 2010; WMO);

- CBS-Ext.(2010) to endorse the XML model(s) for MET data in general, including OPMET, and to agree that WMO be responsible for the future governance and maintenance of these data models (second half of 2010; WMO);

- WMO Executive Committee to approve the use of the XML model(s) (first half of 2011; WMO);

- CBS IPET-DRC to begin the maintenance of the data models, ensuring that an appropriate provisions and/or references be included in the Manual on Codes (WMO – No. 306) (second half of 2011; WMO).

7.1.6	The meeting noted that, at this stage of development of the data models, it was no possible to assess the workload for the maintenance of the data models. Noting that the workload for the maintenance of the Manual on Codes was already very high, the meeting emphasized that the workload for the maintenance of the data models should be strictly limited. For example, with a view to avoiding the duplication of efforts for both the maintenance of the TDCF tables, including associated regulations, and the governance of the WMO data model(s), the meeting stressed the importance to ensure a strong linkage between the BUFR tables and the WMO data model(s) so that the main contribution of the IPET-DRC to the governance of the WMO model(s) remains with the maintenance of the BUFR Tables and associated regulations. The meeting noted that the work done for the development of a three-level Modelling of WMO data products based on TDCF tables and for the conversion of BUFR to a canonical XML showed that it is possible to envisage to derive Data models from the TDCF tables, starting for domains such as Aviation. Therefore the meeting agreed to invite the IPET-MDI to continue working on WMO data model(s) derived from TDCF tables.

7.1.7	With a view to satisfying the requirements of ICAO to use the WXXM model for the representation of OPMET data in XML, the meeting suggested to use the possibility to map a WMO data model for the Aviation domain and the WXXM model; such a mapping is facilitated by the use of 19100 series of geographical information standards.

7.2	Collaboration with the Expert Team on WIS-GTS Operation and Implementation (ET-OI)

7.2.1	Corrected and delayed reports in BUFR bulletins

At the CBS-Ext(06), a change to the Manual on the GTS was introduced into the Attachment II-12 (Recommendation 6.2/1 (CBS-Ext.(06)) with effect from 7 November 2007):

"A - for the first bulletin containing only corrected reports."

to become

"A - for the first bulletin containing corrected reports or information."

The wording of the updated text of Attachment II-12 allows both alternatives, i.e. to include only the corrected reports (subsets) or to include the complete set of reports. The procedure for "NIL reports" is clearly defined in both Manual on Codes and Manual on the GTS. But there are no unambiguous instructions for compilation of BUFR bulletins, containing corrected or delayed reports. Therefore, the meeting invited the ET-OI asked to provide clarification of this issue.

7.2.2	Specification of CCCC in a bulletin containing converted data (TAC <=> BUFR)

Within the "Step-by-step migration by zones", an RTH would convert TAC to BUFR, (and vice versa) for a country that is not yet able to produce/process data in TDCF. The meeting invited the ET-OI to specify explicitly whether this RTH should produce the converted data in a bulletin with the CCCC of the RTH (or a CCCC designated for the data converted by the RTH) or with the CCCC of the country that produced the original data.

7.2.3	Inclusion of metadata into a bulletin containing converted data from TAC to BUFR

Within the "Step-by-step migration by zones", an RTH would convert TAC to BUFR for a country that is not yet able to produce data in TDCF. The templates for representation of TAC data in TDCF require the inclusion of relevant metadata. As an optimal solution, the country should provide a complete list of the required entries, including the height of sensors above local ground. If not available, the RTH accomplishing the conversion of TAC data would have to depend on metadata published in Volume A, WMO-No. 9 [3]. It is to be noted, however, that metadata of stations identified as aerodromes “A” in the column Remarks in [3], do not provide information on Height of station above mean sea level (0 07 030), but that HA = “Official altitude of the aerodrome” is included in the column H/HA in [3]. The difference between “Official altitude of the aerodrome” and “Height of station above mean sea level” might be several meters, e.g. HA = 380 m and 0 07 030 = 364.0 m for the station 11518. Taking into account that 0 07 030 is to be reported with precision to tenths of a meter, 0 07 030 should be set to missing in a report from an aerodrome, if only metadata from Volume A are available in the process of conversion of TAC data to TDCF. The meeting invited the ET-OI to recommend that the RTHs accordingly include the relevant metadata when converting TAC to BUFR for a country that is not yet able to produce data in TDCF.

7.2.4		Other requests addressed to the ET-OI are given in the above paragraphs [list of paragraphs to be added after the meeting].

8.     CLOSURE OF THE MEETING

The Meeting was closed at 4:15 on Friday 3 September 2010, noting Dr Elliott and Messrs Pelletier and Ator on behalf of Dr Elliott, had led the meeting with diplomacy and efficiency.

- ANNEX TO PARAGRAPH 1.2

PROVISIONAL AGENDA

| 1 | ORGANIZATION OF THE MEETING |
| --- | --- |
| 1.1 | Opening of the meeting |
| 1.2 | Approval of the agenda |
| 1.3 | Working arrangement |
| 2 | GRIB |
| 2.1 | Status of proposals at or before the IPET-DRC-I |
| 2.2 | Amendments to GRIB (common aspects: regulations and specifications) |
| 2.3 | Additions and modifications of templates and tables |
| 3 | BUFR AND CREX |
| 3.1 | Status of proposals at or before the IPET-DRC-I |
| 3.2 | Amendments to BUFR/CREX (common aspects: regulations and specifications) |
| 3.3 | Additions and modifications of tables |
| 3.4 | Regulations for reporting traditional observation data in Table-Driven Code Forms (TDCF): BUFR and CREX |
| 3.5 | Master tables for scientific disciplines other than meteorology |
| 4 | TRADITIONAL ALPHANUMERIC CODES |
| 4.1 | Amendments to the aeronautical codes |
| 4.2 | Discontinuation of the monthly upper-air CLIMAT TEMP reports |
| 4.3 | Past weather reporting in hourly synoptic observation |
| 4.4 | Other issue |
| 5 | MIGRATION TO TABLE DRIVEN CODE FORMS (TDCF) |
| 5.1 | Migration status |
| 5.2 | Request from the CBS Management Group (MG-XI) on MTDCF |
| 5.3 | Encoder software for BUFR/CREX available for MTDCF |
| 6 | MANUAL ON CODES |
| 6.1 | Electronic publication of the Manual on Codes, including database |
| 6.2 | Procedures for amending the Manual on Codes |
| 7 | COLLABORATION WITH OTHER CBS TEAMS |
| 8 | CLOSURE OF THE MEETING |

Second meeting of the INTER-PROGRAMME EXPERT TEAM

ON DATA REPRESENTATION AND CODES (IPET-DRC)

(Brasilia, Brazil, 31 August - 3 September 2010)

LIST OF PARTICIPANTS

CHAIRPERSON:	Dr Simon ELLIOTT

EUMETSAT

EUMETSAT-ALLEE 1,

D-64295 DARMSTADT

Germany

Tel.:	+49 6151 807385

Fax:	+49 6151 807304

E-mail:	simon.elliott@eumetsat.int

VICE-CHAIRPERSON:	Mr José Mauro de REZENDE

Instituto Nacional de Meteorologia - INMET

Eixo Monumental - Via S1

70680-900 BRASILIA - DF

Brazil

Tel.	+55 61 3344 4488

Fax	+55 61 3343 2132

E-mail:	jmauro.rezende@inmet.gov.br

MEMBERS OF IPET-DRC:

AUSTRALIA	Dr Weiqing QU

Bureau of Meteorology

700 Collius Street, Docklands

VIC 3008

Australia

Tel.:	+61 3 9669 4236

Fax:	+61 3 9669 4128

E-mail:	w.qu@bom.gov.au

BRAZIL	Mr Waldenio Gambi de ALMEIDA

Centro de Previsão do Tempo e Estudos Climáticos-	CPTEC/INPE

Rodovia Presidente Dutra, km 39

Cachoeira Paulista – SP - Brazil

12630-000

Brazil

Tel.:	+55 12 3186-8541

Fax:	+55 12 3101-2835

E-mail:	waldenio.almeida@cptec.inpe.br

CANADA	Mr Yves PELLETIER

Centre Météorologique Canadien (CMC)

Meteorological Service of Canada (MSC)

2121 Voie de Service Nord

DORVAL, Quebec H9P 1J3

Canada

Tel.:	+1 514 421 4662

Fax:	+1 514 421 4679

E-mail:	yves.pelletier@ec.gc.ca

CHINA	Ms Fang ZHAO

China Meteorological Administration

46 Zhongguancun Nandajie

BEIJING 100081

China

Tel.:	+86 10 6840 7095

Fax:	+86 10 6217-3225

E-mail:	zhaof@cma.gov.cn

CZECH REPUBLIC	Dr (Ms) Eva ČERVENÁ

Czech Hydrometeorological Institute

Na Šabatce 17

143 06 Praha 4

Czech Republic

Tel.:	+420 244 032 215

Fax:	+420 244 032 135

E-mail:	cervena@chmi.cz

ECMWF	Dr Enrico FUCILE

ECMWF

Shinfield Park

READING, RG2 9AX

United Kingdom

Tel.:	+44 118 949 9454

Fax:	+44 118 986 9450

E-mail:	enrico.fucile@ecmwf.int

GERMANY	Ms Sibylle KREBBER

Deutscher Wetterdienst

Frankfurter Str. 135

D-63067 OFFENBACH

Germany

Tel.:	+49 69 8062 2647

Fax:	+49 69 8062 3829

E-mail:	sibylle.krebber@dwd.de

JAPAN	Mr Akira NAKAMORI

Japan Meteorological Agency

1-3-4, Otemachi

Chiyoda-ku

TOKYO 100-8122

Japan

Tel.:	+81 3 3218 3825

Fax:	+81 3 3212 8404

E-mail:	a_nakamori@met.kishou.go.jp

RUSSIAN FEDERATION	Mr Alexander KATS

Central Aerological Observatory - CAO

Russian Federation

Tel.:	+7 495 408-5533

Fax:	+7 495 576-3327

E-mail:	alexander.kats@cao-rmms.ru

alkats@thebat.net

UNITED KINGDOM	Mr Richard WEEDON

Met Office

Fitzroy Road

EXETER, DEVON

United Kingdom

Tel.:	+44 1392 884518

Fax:

E-mail:	richard.weedon@metoffice.gov.uk

UNITED REPUBLIC OF TANZANIA	Mr William Amos CHILLAMBO

Tanzania Meteorological Agency

P.O. Box 3056

JNIA-DAR-ES-SALAAM

United Republic of Tanzania

Tel.:	+255 22 2460706-8

Fax:	+255 22 2460735

E-mail:	chillambo@meteo.go.tz

wchillambo@yahoo.co.uk

UNITED STATES OF AMERICA	Mr Jeffrey ATOR

NOAA / NWS

5200 Auth Road   Room 301

CAMP SPRINGS, MD 20746

United States of America

Tel.:	+1 301 763 8000, Ext.7104

Fax:	+1 301 763 8381

E-mail:	jeff.ator@noaa.gov

INTERNATIONAL ORGANIZATION:

HMEI	Mr Marian MAJAN

IBL Software Engineering

Mierova 103

82105 Bratislava

Slovak Republic

Tel.:	+421 2 32662111

Fax:	+421 2 32662110

E-mail:	marian.majan@iblsoft.com

JCOMM	Ms Hester VIOLA

JCOMMOPS/IOC

8-10 Rue Hermès

31520 Ramonville Saint-Agne

France

Tel.:	+33 5 61 39 47 82

Fax:	+

E-mail:	viola@jcommops.org

WMO SECRETARIAT:

Mr Pierre KERHERVÉ

7 bis avenue de la Paix

Case postale 2300

1211 GENEVE 2

Switzerland

Tel:  +(41 22) 730 8218

Fax: +(41 22) 730 8021

Email: PKerherve@wmo.int

Mr Atsushi SHIMAZAKI

7 bis avenue de la Paix

Case postale 2300

1211 GENEVE 2

Switzerland

Tel:  +(41 22) 730 8313

Fax: +(41 22) 730 8021

Email: AShimazaki@wmo.int

OBSERVERS:

Mr Sergio Henrique Soares FERREIRA

Centro de Previsão do Tempo e Estudos Climáticos-	CPTEC/INPE

Rodovia Presidente Dutra, km 39

Cachoeira Paulista – SP - Brazil

12630-000

Brazil

Tel.:	+55 12 3186-8460

Fax:	+55 12 3101-2835

E-mail:	sergio.ferreira@cptec.inpe.br

Ms Flavia Rodrigues PINHEIRO

Marinha do Brasil

Centro de Hidrografia da Marinha – CHM

Rua Barão de Jaceguay – s/n

Ponta da Armação – Niteroi – RJ - Brasil

24048-900

Brazil

Tel.:	+55 21 2189-3280

Fax:	+55 21 2620-8861

E-mail:	flavia@smm.mil.br

Ms Renata Novaes CALADO

Marinha do Brasil

Centro de Hidrografia da Marinha – CHM

Rua Barão de Jaceguay – s/n

Ponta da Armação – Niteroi – RJ - Brasil

24048-900

Brazil

Tel.:	+55 21 2189-3274

Fax:	+55 21 2620-8861

E-mail:	renatacalado@gmail.com

- ANNEX TO PARAGRAPH 2.1

I.   Status of proposals at the first meeting of IPET-DRC

| Paragraph | Title | Validation (implementation date) |
| --- | --- | --- |
| 2.3.2 | Proposal for update to GRIB2 Tables | (15 Sep. 2010) |
| 2.3.4 | Coding of synthetic satellite data in GRIB2 | Done |
| 2.3.7 | Proposal for update to GRIB2 Tables | (15 Sep. 2010) |
| 2.3.8 | Proposal for update to GRIB2 Tables Fire weather products | Superseded by the Doc 2.3 (3) of this meeting |
| 2.3.9 | Proposal for update to GRIB2 Tables Model level |  |
| 2.3.10 | New GRIB2 table entries for WAFS data | Done |

II.   Status of proposals at the last Joint meeting of CT-MTDCF and ET-DRC

| Paragraph | Title | Validation (Implementation date) |
| --- | --- | --- |
| 2.1.6 | New grid definition template for irregular lat/long grid | Done |
| 2.1.7 | New templates for Categorical forecast data | Done |
| 2.1.8 | New templates for atmospheric aerosols | Done |
| 2.1.9 (1) | New parameters for new meteorological products except for a sign convention for meteorological fluxes | To be confirmed after meeting |
| 2.1.10 | Product Definition Template to encode multi component parameters (matrix or vector elements) | Superseded by the Doc 2.3 (1) of this meeting |
| 2.1.11 | Grid template for general unstructured grids | On going |
| 2.1.12 | New compression method – CCSDS szip | On going |
| 2.1.13 | GRIB2 for paleo climate | On going |

(1)  Proposals in the document at the joint meeting are partially implemented.

- ANNEX TO PARAGRAPH 2.3.1 and 2.3.2

The prognostic variable of a wave model is the distribution of wave energy with respect to frequency and direction, called the "Wave Spectrum".

The spectrum is a statistical quantity representing the average sea state of a certain region within a certain time period. However, this averaging is implicitly assumed and it is not applied in the post-processing of the model.

In order to reduce the number of degrees of freedom there exists a number of "integrated" parameters that characterize the spectrum. For example, the significant wave height is determined from the spectrum by integrating over all frequencies f (and directions)

Hs = 4 * sqrt(m0), where m0 = integral (f * E(f)) df

Hs approximates the average over the higher third of all waves that might be observed by a ship officer. Similarly, other integrated parameters like the "Mean Wave Period" or the "Maximum Height of an Individual Wave" can be derived (in a more or less complicated way) from the wave spectrum without any averaging in space or time.

Since wave models are not capable of describing the development of single waves it makes no sense to define a parameter "Height of an Individual Wave".

Thus, using expressions like "maximum" or "mean" in the spectral context is not contradictory to the GRIB2-orthonogality requirement.

The "Wave Directional Width" is a relative measure (like the relative humidity) and therefore dimensionless.

#### Add the new entries in Code table 4.2

Product discipline 10:	Oceanographic products, parameter category 0:	Waves

| Number | Parameter | Units |
| --- | --- | --- |
| 16 | Coefficient of drag with waves | - |
| 17 | Friction Velocity | m s-1 |
| 18 | Wave stress | N m-2 |
| 19 | Normalised Wave Stress | - |
| 20 | Mean square slope of waves | - |
| 21 | U-component surface Stokes drift | m s-1 |
| 22 | V-component surface Stokes drift | m s-1 |
| 23 | Period of maximum individual wave height | s |
| 24 | Maximum individual wave height | m |
| 25 | Inverse mean wave frequency | s |
| 26 | Inverse mean frequency of the wind waves | s |
| 27 | Inverse mean frequency of the total swell | s |
| 28 | Mean zero-crossing wave period | s |
| 29 | Mean zero-crossing period of the wind waves | s |
| 30 | Mean zero-crossing period of the total swell | s |
| 31 | Wave directional width | - |
| 32 | Directional width of the wind waves | - |
| 33 | Directional width of the total swell | - |
| 34 | Peak wave period | s |
| 35 | Peak period of the wind waves | s |
| 36 | Peak period of the total swell | s |
| 37 | Altimeter wave height | m |
| 38 | Altimeter corrected wave height | m |
| 39 | Altimeter range relative correction | - |
| 40 | 10 metre neutral wind speed over waves | m s-1 |
| 41 | 10 metre wind direction over waves | degrees |
| 42 | Wave energy spectrum | m2 s radian-1 |
| 43 | Kurtosis of the sea surface elevation due to waves | - |
| 44 | Benjamin-Feir index | - |
| 45 | Spectral peakedness factor | s-1 |
| 46 | 2-dim Spectral Energy Density E(f,θ) | m² s |
| 47 | Frequency Spectral Energy Density E(f) = ∫E(f,θ)dθ | m² s |
| 48 | Directional Spectral Energy Density E(θ)= ∫E(f,θ)df / m0 | - |
| 49-254 | Reserved |  |
| 255 | Missing |  |

Product discipline 10:  Oceanographic products, parameter category 4: Sub-surface properties

Number	Parameter		Units

7	Bathymetry		m

Add the new note to the Product discipline 10, parameter category 0 in Code table 4.2

*	Further information concerning the wave parameters can be found in WMO Publication No 702, “Guide to Wave Analysis and Forecasting (http://www.wmo.int/pages/prog/amp/mmop/documents/WMO%20No%20702/WMO702.pdf)

- ANNEX TO PARAGRAPH 2.3.3

Add the new parameter category to Code table 4.1:

Product Discipline 2:	Land surface products

Category	Description

4		Fire weather products

Add the new parameters to Code Table 4.2:

Product discipline 0:	Meteorological products, parameter category 19:	Physical atmospheric properties

26		Convective outlook			Code table 4.224

Product Discipline 2:	Land surface products,	parameter category 4:	Fire weather products

0	Fire outlook	Code table 4.224

1	Fire outlook due to dry thunderstorm	Code table 4.224

Add the new Code table 4.224:

Code table 4.224 – Categorical outlook

Code figure	Meaning

0		No risk area

1		Reserved

2		General thunderstorm risk area

3		Reserved

4		Slight risk area

5		Reserved

6		Moderate risk area

7		Reserved

8		High risk area

9-10		Reserved

11		Dry thunderstorm (dry lightning) risk area

12-13		Reserved

14		Critical risk area

15-17		Reserved

18		Extremely critical risk area

19-254		Reserved

255		Missing

- ANNEX TO PARAGRAPH 2.3.5

See Annex to paragraph 2.3.9

- ANNEX TO PARAGRAPH 2.3.6

Add the new entries in GRIB2 Code table 4.2

Product Discipline 10 (Oceanographic products)

Parameter Category 4 (Sub-surface properties)

| Number | Parameter | Units |
| --- | --- | --- |
| 4 | Ocean vertical heat diffusivity | m2 s-1 |
| 5 | Ocean vertical salt diffusivity | m2 s-1 |
| 6 | Ocean vertical momentum diffusivity | m2 s-1 |

- ANNEX TO PARAGRAPH 2.3.7

Add the new entry in GRIB2 Code table 4.2

Product Discipline 10 (Oceanographic products)

Parameter Category 2 (Ice)

| Number | Parameter | Units |
| --- | --- | --- |
| 9 | Ice internal pressure | Pa * m |

Ice internal pressure or stress (Pa * m) is the integrated pressure across the vertical thickness of a layer of ice. It is produced when concentrated ice reacts to external forces such as wind and ocean currents. There is a maximum internal pressure that a given layer of ice can withstand, depending on the ice layer’s mechanical resistance. Ice internal pressure can be represented as a bi-dimensional horizontal vector.  For our purposes, only the module of the vector is required.

Add the note to Code table 4.5

Note:

(1)	Ice internal pressure or stress (Pa * m) is the integrated pressure across the vertical thickness of a layer of ice. It is produced when concentrated ice reacts to external forces such as wind and ocean currents.

- ANNEX TO PARAGRAPH 2.3.8

Add the new entry in GRIB2 Code table 4.2

Product Discipline 0 (Meteorological products)

Parameter Category 7 (Thermodynamic Stability Indices)

| Number | Parameter | Units |
| --- | --- | --- |
| 15 | Updraft helicity | m2 s-2 |

- ANNEX TO PARAGRAPH 2.3.9

# All changes listed below are highlighted in red (Changes for validation or having pre-operational status are highlighted in yellow.)

Add the new entries and the Notes to Code table 4.5)

| Code table 4.5 – Fixed surface types and units |  |
| --- | --- |
| Code figure | Meaning | Unit |
| 0 | Reserved | – |
| 1 | Ground or water surface | – |
| 2 | Cloud base level | – |
| 3 | Level of cloud tops | – |
| 4 | Level of 0°C isotherm | – |
| 5 | Level of adiabatic condensation lifted from the surface | – |
| 6 | Maximum wind level | – |
| 7 | Tropopause | – |
| 8 | Nominal top of atmosphere | – |
| 9 | Sea bottom | – |
| 10 | Entire atmosphere | – |
| 11 | Cumulonimbus (CB) base | m |
| 12 | Cumulonimbus (CB) top | m |
| 13–19 | Reserved |  |
| 20 | Isothermal level | K |
| 21–99 | Reserved |  |
| 100 | Isobaric surface | Pa |
| 101 | Mean sea level |  |
| 102 | Specific altitude above mean sea level | m |
| 103 | Specified height level above ground | m |
| 104 | Sigma level | “sigma” value |
| 105 | Hybrid level | – |
| 106 | Depth below land surface | m |
| 107 | Isentropic (theta) level | K |
| 108 | Level at specified pressure difference from ground to level | Pa |
| 109 | Potential vorticity surface | K m2 kg–1 s–1 |
| 110 | Reserved |  |
| 111 | Eta level * | – |
| 112 | Reserved |  |
| 113 | Logarithmic hybrid coordinate | – |
| 114-116 | Reserved |  |
| 117 | Mixed layer depth | m |
| 118 | Hybrid height level | - |
| 119 | Hybrid pressure level | - |
| 120 | Pressure Thickness | Pa |
| 121–149 | Reserved |  |
| 150 | Generalized vertical height coordinate (4) |  |
| 151-159 | Reserved |  |
| 160 | Depth below sea level | m |
| 161–191 | Reserved |  |
| 192–254 | Reserved for local use |  |
| 255 | Missing |  |

Note:

(2)	Hybrid height level (Code figure 118) can be defined as:

z(k) = A(k) + B(k) * orog

(k=1,...,NLevels; orog=orography; z(k)=height in metres at level k)                                           -preoperational

(3)	Hybrid pressure level, for which code figure 119 shall be used instead of 105, can be defined as:

p(k) = A(k) + B(k) * sp

(k=1,...,NLevels; sp=surface pressure; p(k)=pressure at level k)                                                 -preoperational

(4)	Hybrid log-pressure level (Code figure 113) can be defined as:
     log (pi) = ai * log (Psfc)  + bi
     (i=1, …, Nlevels); Psfc = surface pressure ;  log (pi) = natural logarithm of pressure at level i)

(5)	The definition of a generalized vertical height coordinate implies the absence of coordinate values in Section 4 but the presence of an external 3D-GRIB message that specifies the height of every model grid point in meters (see Notes for Section 4), i.e. this GRIB message will contain the field with discipline=0, category=3, parameter=6 (Geometric height).

# Modify the Contents of the Section 4 and add the Note (4) to the Section

Section 4 – Product definition section
Octet No.	Contents

1–4	Length of section in octets (nn)

5	Number of section (4)

6–7	Number of coordinate values after template or number of information according to

3D vertical coordinate GRIB2 message (see Note 1 and 4)

8–9	Product definition template number (see Code table 4.0)

10–xx	Product definition template (see Template 4.X,  where X is the product definition 	template  number given in octets 8–9)

[xx+1]–nn	Optional list of coordinate values or vertical grid information (see Notes 2 ,3, 4 and 5)

Notes:

- Two distinct pressure-based hybrid coordinate formulations can be expressed in GRIB Edition 2. If the hybrid coordinate being used is based on pressure, then level type 105 (Code Table 4.5) shall be used to specify the vertical level type.  If the formulation is based on the natural logarithm of pressure then level type 113 (Code Table 4.5) shall be used. In both cases notes 1-3 (above) apply fully.

- In case of generalized vertical height coordinate (fixed surface type 150), no pairs of coordinate values follow after template, but N additional information (each 4 octets long), starting with the number of vertical levels and the identification number of the used vertical system in the additional GRIB2 message with the 3D vertical system. This identification number together with additional optional information are local use vertical grid definitions:

[xx+1] – [xx+4]	Number of vertical levels (NLEV)

[xx+5] – [xx+8]	Identification number of 3D vertical grid GRIB2 message (NGRID)

(defined by originating centre)

[xx+9] – [xx+4*N]  Local use definitions (optional)

# Modify and add to the “Guide to GRIB2” (Chapter 3.2, page 73ff)

- complete all definitions concerning TABLE 4.5 and Section 4

- distinguish between pressure and height based vertical coordinate

- add example for use of “generalized height coordinate”

# Description of pressure based coordinate system

(…)

The hybrid pressure based coordinate system has been introduced in numerical models to have both sigma-type levels near the earth and pressure levels at the top of the atmosphere. The above formula is generalized as follows:

# Ph = ah ( Psfc  +  bh

Hybrid vertical coordinate values, when present, are encoded as the pair of numbers ah and bh in IEEE 32-bit floating point format.  Each pair represents a hybrid vertical coordinate level. With the surface pressure field Psfc, the values of Ph can be calculated from the above formula.  Note that this implies the surface pressure field accompanies data on hybrid vertical coordinates.  The capability of GRIB2 to encode multiple data sets in a single message makes this straightforward to accomplish.

(……)

# Add description of height based coordinate system

(……)

# Add description of generalized height coordinate system

If the defining algorithms for the vertical grid are too complicated, the 3D vertical grid will be provided as a GRIB2 file by using the “generalized vertical height coordinate” (TABLE 4.5: 150). To illustrate the usage, see the following example (only section 4) for a temperature field including the 3D vertical grid GRIB2 message.

# Example for usage of the “generalized vertical coordinate” system:

# Temperature field  of layer 13/14 has following section 4

1-4	104-107	38	This Section is 38 octets long

5	108	4	This is Section 4

6-7	109-110	2	No vertical coordinate pairs follow after the template but 2 					numbers with vertical grid information

8-9	111-112	0	The Product Definition Template Number is 4.0 – an analysis or 					forecast at a horizontal level or in a horizontal layer at a point in time

10	113	0	The parameter category is 0 – temperature  products

11	114	0	The parameter number is 0  - temperature (in K)

12	115	2	A forecast generated this product (the generating process)

13	116	All 1’s	No information

14	117	All 1’s	No information on the forecast generating process

15-16	118-119	3	The observational data cut-off was 3 hours after the reference time

17	120	30	The observational data cut-off was 30 minutes after the observational 			cut-off hour

18	121	1	The time is given in hours

19-22	122-125	12	The forecast time is 12 hours after the reference time

23	126	150	The first fixed surface is a general height coordinate surface

24	127	0	The scale factor of first fixed surface is 0

25-28	128-131	13	The scaled value of first fixed surface is 13

29	132	150	The  second fixed surface is a general height coordinate surface

30	133	0	The scale factor of the second fixed surface is 0

31-34	134-137	14	The scaled value of the second fixed surface is 14

35-36	138-139	61	The vertical grid GRIB2 file contains 61 levels (NL)

37-38	140-141	13	Grid identification number of 3D vertical GRIB2 message 						(NGRID); defined by originating centre

The corresponding 3D vertical grid GRIB2 file provided by grid number NGRID=13 consists of NLEV=61 model height levels, the height fields  for level 13 and 14 have the following section 4:

1-4	104-107	38	This Section is 38 octets long

5	108	4	This is Section 4

6-7	109-110	2	No vertical coordinate pairs follow after the template but 2 					numbers with vertical grid information

8-9	111-112	0	The Product Definition Template Number is 4.0 – an analysis or 					forecast at a horizontal level or in a horizontal layer at a point in time

10	113	3	The parameter category is 3 – mass  products

11	114	6	The parameter number is 6  - geometric height ( in m )

12	115	2	A forecast generated this product (the generating process)

13	116	All 1’s	No information

14	117	All 1’s	No information on the forecast generating process

15-16	118-119	3	The observational data cut-off was 3 hours after the reference time

17	120	30	The observational data cut-off was 30 minutes after the observational 			cut-off hour

18	121	1	The time is given in hours

19-22	122-125	12	The forecast time is 12 hours after the reference time

23	126	150	The first fixed surface is a general coordinate surface

24	127	0	The scale factor of first fixed surface is 0

25-28	128-131	13 (14)	The scaled value of first fixed surface is 13 for level 13 (2nd  field 			: 14)

29	132	1	not defined

30	133	1	not defined

31-34	134-137	1	not defined

35-36	138-139	61	The vertical grid GRIB2 file contains 61 levels (NL)

37-38	140-141	13	Grid identification number of 3D vertical GRIB2 message 						(NGRID)

- ANNEX TO PARAGRAPH 2.3.10

# Add the new entries and the Note (2) to Code table 4.7

# 7      Interquartile range

8      Minimum of all ensemble members

9      Maximum of all ensemble members

Note:

(2) It should be noted that the reference for "minimum of all ensemble members" and "maximum of all ensemble members" is the set of ensemble members and not a time interval and should not be confused with the max. and min. described by PDT 4.8.

- ANNEX TO PARAGRAPH 2.3.12

# The proposed solution below introduces

  - a set of new parameter numbers in Code Table 4.2 for Product discipline 0 / category 18

  - new entries in Code table 4.230 (Common Table C-14) for radioactive isotopes

# To illustrate the proposed usage we add an example (Template 4.40) for element coding.

# Add the new entries in Code Table 4.1 (in red)

Product Discipline 0:	Meteorological products, 	parameter category 18:	Nuclear/radiology

Number		Parameter						Units

0		Air concentration of Caesium 137 				Bq m-3

1		Air concentration of Iodine 131 				Bq m-3

2	Air concentration of radioactive pollutant			Bq m-3

3	Ground deposition of Caesium 137				Bq m-2

4	Ground deposition of Iodine 131				Bq m-2

5	Ground deposition of radioactive pollutant			Bq m-2

6	Time-integrated air concentration of caesium pollutant*	Bq s m-3

7	Time-integrated air concentration of iodine pollutant*	Bq s m-3

8	Time-integrated air concentration of radioactive pollutant*	Bq s m-3

9		Reserved

10               Air concentration						Bq m-3

11	Wet deposition						Bq m-2

12	Dry deposition							Bq m-2

13		Total deposition (wet + dry)					Bq m-2

14-191	Reserved

192-254	Reserved for local use

255		Missing

Note: * Parameter deprecated - See Regulation 92.6.2 and use another parameter instead.

Parameters from 10 onwards may be used in combination with Product definition templates 4.40 – 4.43 and Common Code table C-14 (Code table 4.230) to represent any type of radioisotope.

# Add the new entries in Common Code table C-14 (in red)

To keep in mind, constituents are arranged in the following code number sections for ordering and expansion reasons:

1-9999 : inorganic molecules

10000-19999: organic molecules with C, H, O, N, S

20000-29999: organic molecules with Cl, F, I

30000-59999: undefined (potentially of use for isotopes)

60000-65535: chemical families and group tracers, special diagnostic tracers

The new entries for radioisotopes start with 30000. The list of isotopes is put in red from 30010-30294. The numbering may be different in order to allow more entries or if other ordering criteria are wanted.

# Common Code table C-14: Atmospheric chemical or physical constituent type

| Code figure | Meaning | Chemical formula |
| --- | --- | --- |
| 0 | Air | -- |
| 1 | Water vapour | H2O |
| 2 | Atomic oxygen | O |
| 3 | Ozone | O3 |
| 4 | Molecular hydrogen | H |
| 5 | Hydroxyl radical | OH |
| 6 | Hydroperoxyl radical | HO2 |
| 7 | Hydrogen peroxide | H2O2 |
| 8 | Atomic nitrogen | N |
| 9 | Ammonia | NH3 |
| 10 | Ammonium | NH4+ |
| 11 | Nitrogen monoxide | NO |
| 12 | Nitrogen dioxide | NO2 |
| 13 | Nitrate radical | NO3 |
| 14 | Nitrous oxide | N2O |
| 15 | Dinitrogen pentoxide | N2O5 |
| 16 | Nitrous acid | HONO |
| 17 | Nitric acid | HNO3 |
| 18 | Peroxynitric acid | HO2NO2 |
| 19 | Carbon monoxide | CO |
| 20 | Carbon dioxide | CO2 |
| 21 | Sulphur dioxide | SO2 |
| 22 | Sulphate | SO42- |
| 23 | Radon | Rn |
| 24 | Elemental mercury | Hg(0) |
| 25 | Divalent mercury | Hg2+ |
| 26 | Atomic chlorine | Cl |
| 27 | Chlorine monoxide | ClO |
| 28 | Dichlorine peroxide | Cl2O2 |
| 29 | Hypochlorous acid | HClO |
| 30 | Chlorine nitrate | ClONO2 |
| 31 | Chlorine dioxide | ClO2 |
| 32 | Atomic bromine | Br |
| 33 | Bromine monoxide | BrO |
| 34 | Bromine chloride | BrCl |
| 35 | Hydrogen bromide | HBr |
| 36 | Hypobromous acid | HBrO |
| 37 | Bromine nitrate | BrONO2 |
| 38-9999 | Reserved |  |
| 10000 | Methane | CH4 |
| 10001 | Methyl peroxy radical | CH3O2 |
| 10002 | Methyl hydroperoxide | CH3O2H |
| 10003 | Formaldehyde (= Methanal) | CH2O |
| 10004 | Methanol | CH3OH |
| 10005 | Formic acid | CH3OOH |
| 10006 | Hydrogen Cyanide | HCN |
| 10007 | Aceto nitrile | CH3CN |
| 10008 | Ethane | C2H6 |
| 10009 | Ethene (= Ethylene) | C2H4 |
| 10010 | Ethyne (= Acetylene) | C2H2 |
| 10011 | Ethanol | C2H5OH |
| 10012 | Acetic acid | C2H5OOH |
| 10013 | Peroxyacetyl nitrate | CH3C(O)OONO2 |
| 10014 | Propane | C3H8 |
| 10015 | Propene | C3H6 |
| 10016 | Butanes | C4H10 |
| 10017 | Isoprene | C5H10 |
| 10018 | Alpha pinene | C10H16 |
| 10019 | Beta pinene | C10H16 |
| 10020 | Limonene | C10H16 |
| 10021 | Benzene | C6H6 |
| 10022 | Toluene | C7H8 |
| 10023 | Xylene | C8H10 |
| 10024-10499 | reserved for other simple organic molecules (e.g. higher aldehydes, alcohols, peroxides,…) |  |
| 10500 | Dimethyl sulphide | CH3SCH3 (DMS) |
| 10501-20000 | Reserved |  |
| 20001 | Hydrogen chloride |  |
| 20002 | CFC-11 |  |
| 20003 | CFC-12 |  |
| 20004 | CFC-113 |  |
| 20005 | CFC-113a |  |
| 20006 | CFC-114 |  |
| 20007 | CFC-115 |  |
| 20008 | HCFC-22 |  |
| 20009 | HCFC-141b |  |
| 20010 | HCFC-142b |  |
| 20011 | Halon-1202 |  |
| 20012 | Halon-1211 |  |
| 20013 | Halon-1301 |  |
| 20014 | Halon-2402 |  |
| 20015 | Methyl chloride (HCC-40) |  |
| 20016 | Carbon tetrachloride (HCC-10) |  |
| 20017 | HCC-140a | CH3CCl3 |
| 20018 | Methyl bromide (HBC-40B1) |  |
| 20019 | Hexachlorocyclohexane (HCH) |  |
| 20020 | Alpha hexachlorocyclohexane |  |
| 20021 | Hexachlorobiphenyl (PCB-153) |  |
| 20022-29999 | Reserved |  |
| 30000 | Radioactive pollutant (tracer, defined by originating centre) |  |
| 30001 - 30009 | Reserved |  |
| 30010 | Hydrogen | H-3 |
| 30011 | Hydrogen organic bounded | H-3o |
| 30012 | Hydrogen inorganic | H-3a |
| 30013 | Beryllium 7 | Be-7 |
| 30014 | Beryllium 10 | Be-10 |
| 30015 | Carbon 14 | C-14 |
| 30016 | Carbon 14 CO2 | C-14CO2 |
| 30017 | Carbon 14 other gases | C-14og |
| 30018 | Nitrogen 13 | N-13 |
| 30019 | Nitrogen 16 | N-16 |
| 30020 | Fluorine 18 | F-18 |
| 30021 | Sodium 22 | Na-22 |
| 30022 | Phosphate 32 | P-32 |
| 30023 | Phosphate 33 | P-33 |
| 30024 | Sulfur 35 | S-35 |
| 30025 | Chlorine 36 | Cl-36 |
| 30026 | Potassium 40 | K-40 |
| 30027 | Argon 41 | Ar-41 |
| 30028 | Calcium 41 | Ca-41 |
| 30029 | Calcium 45 | Ca-45 |
| 30030 | Titanium 44 | Ti-44 |
| 30031 | Scandium 46 | Sc-46 |
| 30032 | Vanadium 48 | V-48 |
| 30033 | Vanadium 49 | V-49 |
| 30034 | Chrome 51 | Cr-51 |
| 30035 | Manganese 52 | Mn-52 |
| 30036 | Manganese 54 | Mn-54 |
| 30037 | Iron 55 | Fe-55 |
| 30038 | Iron 59 | Fe-59 |
| 30039 | Cobalt 56 | Co-56 |
| 30040 | Cobalt 57 | Co-57 |
| 30041 | Cobalt 58 | Co-58 |
| 30042 | Cobalt 60 | Co-60 |
| 30043 | Nickel 59 | Ni-59 |
| 30044 | Nickel 63 | Ni-63 |
| 30045 | Zinc 65 | Zn-65 |
| 30046 | Gallium 67 | Ga-67 |
| 30047 | Gallium 68 | Ga-68 |
| 30048 | Germanium 68 | Ge-68 |
| 30049 | Germanium 69 | Ge-69 |
| 30050 | Arsenic 73 | As-73 |
| 30051 | Selenium 75 | Se-75 |
| 30052 | Selenium 79 | Se-79 |
| 30053 | Rubidium 81 | Rb-81 |
| 30054 | Rubidium 83 | Rb-83 |
| 30055 | Rubidium 84 | Rb-84 |
| 30056 | Rubidium 86 | Rb-86 |
| 30057 | Rubidium 87 | Rb-87 |
| 30058 | Rubidium 88 | Rb-88 |
| 30059 | Krypton 85 | Kr-85 |
| 30060 | Krypton 85 metastable | Kr-85m |
| 30061 | Krypton 87 | Kr-87 |
| 30062 | Krypton 88 | Kr-88 |
| 30063 | Krypton 89 | Kr-89 |
| 30064 | Strontium 85 | Sr-85 |
| 30065 | Strontium 89 | Sr-89 |
| 30066 | Strontium 89/90 | Sr-8990 |
| 30067 | Strontium 90 | Sr-90 |
| 30068 | Strontium 91 | Sr-91 |
| 30069 | Strontium 92 | Sr-92 |
| 30070 | Yttrium 87 | Y-87 |
| 30071 | Yttrium 88 | Y-88 |
| 30072 | Yttrium 90 | Y-90 |
| 30073 | Yttrium 91 | Y-91 |
| 30074 | Yttrium 91 metastable | Y-91m |
| 30075 | Yttrium 92 | Y-92 |
| 30076 | Yttrium 93 | Y-93 |
| 30077 | Zirconium 89 | Zr-89 |
| 30078 | Zirconium 93 | Zr-93 |
| 30079 | Zirconium 95 | Zr-95 |
| 30080 | Zirconium 97 | Zr-97 |
| 30081 | Niobium 93 metastable | Nb-93m |
| 30082 | Niobium 94 | Nb-94 |
| 30083 | Niobium 95 | Nb-95 |
| 30084 | Niobium 95 metastable | Nb-95m |
| 30085 | Niobium 97 | Nb-97 |
| 30086 | Niobium 97 metastable | Nb-97m |
| 30087 | Molybdenum 93 | Mo-93 |
| 30088 | Molybdenum 99 | Mo-99 |
| 30089 | Technetium 95 metastable | Tc-95m |
| 30090 | Technetium 96 | Tc-96 |
| 30091 | Technetium 99 | Tc-99 |
| 30092 | Technetium 99 metastable | Tc-99m |
| 30093 | Rhodium 99 | Rh-99 |
| 30094 | Rhodium 101 | Rh-101 |
| 30095 | Rhodium 102 metastable | Rh-102m |
| 30096 | Rhodium 103 metastable | Rh-103m |
| 30097 | Rhodium 105 | Rh-105 |
| 30098 | Rhodium 106 | Rh-106 |
| 30099 | Palladium 100 | Pd-100 |
| 30100 | Palladium 103 | Pd-103 |
| 30101 | Palladium 107 | Pd-107 |
| 30102 | Ruthenium 103 | Ru-103 |
| 30103 | Ruthenium 105 | Ru-105 |
| 30104 | Ruthenium 106 | Ru-106 |
| 30105 | Silver 108 metastable | Ag-108m |
| 30106 | Silver 110 metastable | Ag-110m |
| 30107 | Cadmium 109 | Cd-109 |
| 30108 | Cadmium 113 metastable | Cd-113m |
| 30109 | Cadmium 115 metastable | Cd-115m |
| 30110 | Indium 114 metastable | In-114m |
| 30111 | Tin 113 | Sn-113 |
| 30112 | Tin 119 metastable | Sn-119m |
| 30113 | Tin 121 metastable | Sn-121m |
| 30114 | Tin 122 | Sn-122 |
| 30115 | Tin 123 | Sn-123 |
| 30116 | Tin 126 | Sn-126 |
| 30117 | Antimony 124 | Sb-124 |
| 30118 | Antimony 125 | Sb-125 |
| 30119 | Antimony 126 | Sb-126 |
| 30120 | Antimony 127 | Sb-127 |
| 30121 | Antimony 129 | Sb-129 |
| 30122 | Tellurium 123 metastable | Te-123m |
| 30123 | Tellurium 125 metastable | Te-125m |
| 30124 | Tellurium 127 | Te-127 |
| 30125 | Tellurium 127 metastable | Te-127m |
| 30126 | Tellurium 129 | Te-129 |
| 30127 | Tellurium 129 metastable | Te-129m |
| 30128 | Tellurium 131 metastable | Te-131m |
| 30129 | Tellurium 132 | Te-132 |
| 30130 | Iodine 123 | I-123 |
| 30131 | Iodine 124 | I-124 |
| 30132 | Iodine 125 | I-125 |
| 30133 | Iodine 126 | I-126 |
| 30134 | Iodine 129 | I-129 |
| 30135 | Iodine 129 elementary gaseous | I-129g |
| 30136 | Iodine 129 organic bounded | I-129o |
| 30137 | Iodine 131 | I-131 |
| 30138 | Iodine 131 elementary gaseous | I-131g |
| 30139 | Iodine 131 organic bounded | I-131o |
| 30140 | Iodine 131 gaseous elementary and organic bounded | I-131go |
| 30141 | Iodine 131 aerosol | I-131a |
| 30142 | Iodine 132 | I-132 |
| 30143 | Iodine 132 elementary gaseous | I-132g |
| 30144 | Iodine 132 organic bounded | I-132o |
| 30145 | Iodine 132 gaseous elementary and organic bounded | I-132go |
| 30146 | Iodine 132 aerosol | I-132a |
| 30147 | Iodine 133 | I-133 |
| 30148 | Iodine 133 elementary gaseous | I-133g |
| 30149 | Iodine 133 organic bounded | I-133o |
| 30150 | Iodine 133 gaseous elementary and organic bounded | I-133go |
| 30151 | Iodine 133 aerosol | I-133a |
| 30152 | Iodine 134 | I-134 |
| 30153 | Iodine 134 elementary gaseous | I-134g |
| 30154 | Iodine 134 organic bounded | I-134o |
| 30155 | Iodine 135 | I-135 |
| 30156 | Iodine 135 elementary gaseous | I-135g |
| 30157 | Iodine 135 organic bounded | I-135o |
| 30158 | Iodine 135 gaseous elementary and organic bounded | I-135go |
| 30159 | Iodine 135 aerosol | I-135a |
| 30160 | Xenon 131 metastable | Xe-131m |
| 30161 | Xenon 133 | Xe-133 |
| 30162 | Xenon 133 metastable | Xe-133m |
| 30163 | Xenon 135 | Xe-135 |
| 30164 | Xenon 135 metastable | Xe-135m |
| 30165 | Xenon 137 | Xe-137 |
| 30166 | Xenon 138 | Xe-138 |
| 30167 | Xenon sum of all Xenon isotopes | Xe-sum |
| 30168 | Caesium 131 | Cs-131 |
| 30169 | Caesium 134 | Cs-134 |
| 30170 | Caesium 135 | Cs-135 |
| 30171 | Caesium 136 | Cs-136 |
| 30172 | Caesium 137 | Cs-137 |
| 30173 | Barium 133 | Ba-133 |
| 30174 | Barium 137 metastable | Ba-137m |
| 30175 | Barium 140 | Ba-140 |
| 30176 | Cerium 139 | Ce-139 |
| 30177 | Cerium 141 | Ce-141 |
| 30178 | Cerium 143 | Ce-143 |
| 30179 | Cerium 144 | Ce-144 |
| 30180 | Lanthanum 140 | La-140 |
| 30181 | Lanthanum 141 | La-141 |
| 30182 | Praseodymium 143 | Pr-143 |
| 30183 | Praseodymium 144 | Pr-144 |
| 30184 | Praseodymium 144 metastable | Pr-144m |
| 30185 | Samarium 145 | Sm-145 |
| 30186 | Samarium 147 | Sm-147 |
| 30187 | Samarium 151 | Sm-151 |
| 30188 | Neodymium 147 | Nd-147 |
| 30189 | Promethium 146 | Pm-146 |
| 30190 | Promethium 147 | Pm-147 |
| 30191 | Promethium 151 | Pm-151 |
| 30192 | Europium 152 | Eu-152 |
| 30193 | Europium 154 | Eu-154 |
| 30194 | Europium 155 | Eu-155 |
| 30195 | Gadolinium 153 | Gd-153 |
| 30196 | Terbium 160 | Tb-160 |
| 30197 | Holmium 166 metastable | Ho-166m |
| 30198 | Thulium 170 | Tm-170 |
| 30199 | Ytterbium 169 | Yb-169 |
| 30200 | Hafnium 175 | Hf-175 |
| 30201 | Hafnium 181 | Hf-181 |
| 30202 | Tantalum 179 | Ta-179 |
| 30203 | Tantalum 182 | Ta-182 |
| 30204 | Rhenium 184 | Re-184 |
| 30205 | Iridium 192 | Ir-192 |
| 30206 | Mercury 203 | Hg-203 |
| 30207 | Thallium 204 | Tl-204 |
| 30208 | Thallium 207 | Tl-207 |
| 30209 | Thallium 208 | Tl-208 |
| 30210 | Thallium 209 | Tl-209 |
| 30211 | Bismuth 205 | Bi-205 |
| 30212 | Bismuth 207 | Bi-207 |
| 30213 | Bismuth 210 | Bi-210 |
| 30214 | Bismuth 211 | Bi-211 |
| 30215 | Bismuth 212 | Bi-212 |
| 30216 | Bismuth 213 | Bi-213 |
| 30217 | Bismuth 214 | Bi-214 |
| 30218 | Polonium 208 | Po-208 |
| 30219 | Polonium 210 | Po-210 |
| 30220 | Polonium 212 | Po-212 |
| 30221 | Polonium 213 | Po-213 |
| 30222 | Polonium 214 | Po-214 |
| 30223 | Polonium 215 | Po-215 |
| 30224 | Polonium 216 | Po-216 |
| 30225 | Polonium 218 | Po-218 |
| 30226 | Lead 209 | Pb-209 |
| 30227 | Lead 210 | Pb-210 |
| 30228 | Lead 211 | Pb-211 |
| 30229 | Lead 212 | Pb-212 |
| 30230 | Lead 214 | Pb-214 |
| 30231 | Astatine 217 | At-217 |
| 30232 | Radon 219 | Rn-219 |
| 30233 | Radon 220 | Rn-220 |
| 30234 | Radon 222 | Rn-222 |
| 30235 | Francium 221 | Fr-221 |
| 30236 | Francium 223 | Fr-223 |
| 30237 | Radium 223 | Ra-223 |
| 30238 | Radium 224 | Ra-224 |
| 30239 | Radium 225 | Ra-225 |
| 30240 | Radium 226 | Ra-226 |
| 30241 | Radium 228 | Ra-228 |
| 30242 | Actinium 225 | Ac-225 |
| 30243 | Actinium 227 | Ac-227 |
| 30244 | Actinium 228 | Ac-228 |
| 30245 | Thorium 227 | Th-227 |
| 30246 | Thorium 228 | Th-228 |
| 30247 | Thorium 229 | Th-229 |
| 30248 | Thorium 230 | Th-230 |
| 30249 | Thorium 231 | Th-231 |
| 30250 | Thorium 232 | Th-232 |
| 30251 | Thorium 234 | Th-234 |
| 30252 | Protactinium 231 | Pa-231 |
| 30253 | Protactinium 233 | Pa-233 |
| 30254 | Protactinium 234 metastable | Pa-234m |
| 30255 | Uranium 232 | U-232 |
| 30256 | Uranium 233 | U-233 |
| 30257 | Uranium 234 | U-234 |
| 30258 | Uranium 235 | U-235 |
| 30259 | Uranium 236 | U-236 |
| 30260 | Uranium 237 | U-237 |
| 30261 | Uranium 238 | U-238 |
| 30262 | Plutonium 236 | Pu-236 |
| 30263 | Plutonium 238 | Pu-238 |
| 30264 | Plutonium 239 | Pu-239 |
| 30265 | Plutonium 240 | Pu-240 |
| 30266 | Plutonium 241 | Pu-241 |
| 30267 | Plutonium 242 | Pu-242 |
| 30268 | Plutonium 244 | Pu-244 |
| 30269 | Neptunium 237 | Np-237 |
| 30270 | Neptunium 238 | Np-238 |
| 30271 | Neptunium 239 | Np-239 |
| 30272 | Americium 241 | Am-241 |
| 30273 | Americium 242 | Am-242 |
| 30274 | Americium 242 metastable | Am-242m |
| 30275 | Americium 243 | Am-243 |
| 30276 | Curium 242 | Cm-242 |
| 30277 | Curium 243 | Cm-243 |
| 30278 | Curium 244 | Cm-244 |
| 30279 | Curium 245 | Cm-245 |
| 30280 | Curium 246 | Cm-246 |
| 30281 | Curium 247 | Cm-247 |
| 30282 | Curium 248 | Cm-248 |
| 30283 | Curium 243/244 | Cm-243244 |
| 30284 | Plutonium 238/Americium 241 | Pu-238Am-241 |
| 30285 | Plutonium 239/240 | Pu-239240 |
| 30286 | Berkelium 249 | Bk-249 |
| 30287 | Californium 249 | Cf-249 |
| 30288 | Californium 250 | Cf-250 |
| 30289 | Californium 252 | Cf-252 |
| 30290 | Sum aerosol particulates | SumAer |
| 30291 | Sum Iodine | SumIod |
| 30292 | Sum noble gas | SumNG |
| 30293 | Activation gas | ActGas |
| 30294 | Cs-137 Equivalent | EquCs137 |
| 30295 - 59999 | Reserved |  |
| 60000 | HOx radical (OH+HO2) |  |
| 60001 | Total inorganic and organic peroxy radicals (HO2 + RO2) | RO2 |
| 60002 | Passive Ozone |  |
| 60003 | NOx expressed as nitrogen | NOx |
| 60004 | All nitrogen oxides (NOy) expressed as nitrogen | NOy |
| 60005 | Total inorganic chlorine | Clx |
| 60006 | Total inorganic bromine | Brx |
| 60007 | Total inorganic chlorine except HCl, ClONO2: ClOx |  |
| 60008 | Total inorganic bromine except HBr, BrONO2: BrOx |  |
| 60009 | Lumped Alkanes |  |
| 60010 | Lumped Alkenes |  |
| 60011 | Lumped Aromatic Compounds |  |
| 60012 | Lumped Terpenes |  |
| 60013 | Non-methane volatile organic compounds expressed as carbon | NMVOC |
| 60014 | Anthropogenic non-methane volatile organic compounds expressed as carbon | aNMVOC |
| 60015 | Biogenic non-methane volatile organic compounds expressed as carbon | bNMVOC |
| 60016 | Lumped oxygenated hydrocarbons | OVOC |
| 60017-61999 | Reserved |  |
| 62000 | Total aerosol |  |
| 62001 | Dust dry |  |
| 62002 | Water in ambient |  |
| 62003 | Ammonium dry |  |
| 62004 | Nitrate dry |  |
| 62005 | Nitric acid trihydrate |  |
| 62006 | Sulphate dry |  |
| 62007 | Mercury dry |  |
| 62008 | Sea salt dry |  |
| 62009 | Black carbon dry |  |
| 62010 | Particulate organic matter dry |  |
| 62011 | Primary particulate organic matter dry |  |
| 62012 | Secondary particulate organic matter dry |  |
| 62013-65534 | Reserved |  |
| 65535 | Missing |  |

# Example: Use of Template 4.40

Product definition template 4.40: Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents

| Octet Number(s) |  | Contents |
| --- | --- | --- |
| 10 | 18 | Parameter category (see Code table 4.1): Nuclear/Radiology or Atmospheric Chemical Constituent |
| 11 | 10 | Parameter number (see Code table 4.2): Air concentration |
| 12-13 | 30172 | Atmospheric chemical constituent type (see Code table 4.230): Cs 137 |
| 14 |  | Type of generating process (see Code table 4.3) |
| 15 |  | Background generating process identifier (defined by originating centre) |
| 16 |  | Analysis or forecast generating process identifier (defined by originating centre) |
| 17-18 |  | Hours of observational data cutoff after reference time (see Note 1) |
| 19 |  | Minutes of observational data cutoff after reference time |
| 20 |  | Indicator of unit of time range (see Code table 4.4) |
| 21-24 |  | Forecast time in units defined by octet 20 |
| 25 |  | Type of first fixed surface (see Code table 4.5) |
| 26 |  | Scale factor of first fixed surface |
| 27-30 |  | Scaled value of first fixed surface |
| 31 |  | Type of second fixed surface (see Code table 4.5) |
| 32 |  | Scale factor of second fixed surface |
| 33-36 |  | Scaled value of second fixed surface |

- ANNEX TO PARAGRAPH 2.3.13

# Add the Note under Code Table 4.10 : Type of statistical processing

Note: Statistical processing shall not change a parameter unit, e.g. from kg m-2 s-1 to kg m-2. The "Type of statistical processing" is used to specify the statistical process which was applied to values of the same parameter to derive the processed field data. It does not provide calculation rules for processing given coded values.

# Add as Notes to Regulations 92.6 Section 4 – Product definition section or at an appropriate place in Code table 4.2:

# Examples for encoding precipitation data

"Convective Precipitation Rate" as a time discrete parameter of the numerical weather model shall be coded with "at a point in time" templates, parameter number 37 (Convective precipitation rate), category 1 (Moisture), discipline 0 (Meteorological products). It is seen as an instantaneous value at the forecast time.

"Total precipitation rate" as sum of convective and large-scale precipitation rate is still a rate and shall be coded with "at a point in time" templates, parameter number 94 (Total precipitation rate), category 1 (Moisture), discipline 0 (Meteorological products). It is the instantaneous value at the forecast time.

"Total precipitation" shall be coded with type of statistical processing 1 (Accumulation), parameter number 52 (Total precipitation), category 1 (Moisture), discipline 0 (Meteorological products)."

# Withdraw the "Parameter deprecated" note in Code table 4.2. for:

| DISCIPLINE | CATEGORY | NUMBER | PARAMETER NAME | UNITS |
| --- | --- | --- | --- | --- |
| 0 | 1 | 9 | Large scale precipitation (non-convective) | kg m-2 |
| 0 | 1 | 10 | Convective precipitation | kg m-2 |
| 0 | 18 | 6 | Time-integrated air concentration of caesium pollutant | Bq s m-3 |
| 0 | 18 | 7 | Time-integrated air concentration of iodine pollutant | Bq s m-3 |
| 0 | 18 | 8 | Time-integrated air concentration of radioactive pollutant | Bq s m-3 |

# As an exception (with note in Code table 4.2), to solve the problem with existing parameters which are used in the following sense (e.g. in TIGGE project), an editorial change of name and unit of parameters in Code table 4.2 is proposed:

| DISCIPLINE | CATEGORY | NUMBER | PARAMETER NAME | UNITS |
| --- | --- | --- | --- | --- |
| 0 | 0 | 10 | Time-integrated latent heat net flux(1) | W m-2 s |
| 0 | 0 | 11 | Time-integrated sensible heat net flux(1) | W m-2 s |
| 0 | 1 | 52 | Total precipitation(3) | kg m-2 |
| 0 | 1 | 53 | Total(2) snowfall water equivalent(3) | kg m-2 |
| 0 | 4 | 9 | Time-integrated net short wave radiation flux(1) | W m-2 s |
| 0 | 5 | 5 | Time-integrated net long wave radiation flux(1) | W m-2 s |
| 0 | 6 | 24 | Sunshine duration(3) | s |

# Notes:

# (1) or (3) Editorial change of parameter name and unit in GRIB master table version 7. (Due to the clarification that statistical processing shall not change a parameter unit.)

# Withdraw parameters in Code table 4.2 in validation status:

| 0 | 1 | 79 | Evaporation rate | kg m-2 s-1 |
| --- | --- | --- | --- | --- |

# Add new parameters in Code table 4.2:

| DISCIPLINE | CATEGORY | NUMBER | PARAMETER NAME | UNITS |
| --- | --- | --- | --- | --- |
| 0 | 0 | 21 | Latent heat net flux | W m-2 |
| 0 | 0 | 22 | Sensible heat net flux | W m-2 |
| 0 | 1 | 87 | Large scale rain | kg m-2 |
| 0 | 1 | 88 | Rain precipitation | kg m-2 |
| 0 | 1 | 89 | Convective snowfall water equivalent | kg m-2 |
| 0 | 1 | 90 | Large scale snowfall water equivalent | kg m-2 |
| 0 | 1 | 91 | Graupel (snow pellets) precipitation | kg m-2 |
| 0 | 1 | 92 | Freezing rain precipitation | kg m-2 |
| 0 | 1 | 93 | Ice pellets precipitation | kg m-2 |
| 0 | 1 | 94 | Total precipitation rate | kg m-2 s-1 |
| 0 | 1 | 95 | Total(2) snowfall rate water equivalent | kg m-2 s-1 |
| 0 | 1 | 96 | Hail precipitation | kg m-2 |
| 0 | 1 | 97 | Convective rain | kg m-2 |
| 0 | 4 | 13 | Net short wave radiation flux | W m-2 |
| 0 | 5 | 7 | Net long wave radiation flux | W m-2 |

- ANNEX TO PARAGRAPH 3.1

I.   Status of proposals at the first meeting of IPET-DRC

| Paragraph | Title | Validation |
| --- | --- | --- |
| 3.3.2 | Update from JCOMM on developments for BUFR templates: New XBT template and queries about a revised VOS template | Ongoing |
| 3.3.3 | BUFR descriptors required by Recommendation 6.1/2 (CBSXIV), Add1 | Superseded by Doc 3.3(8) of this meeting |
| 3.3.4 | A proposal for Universal BUFR template for representation of Lightning data Formulated in June 2009 | Superseded by Doc 3.3 (3) of this meeting |
| 3.3.8 | New BUFR descriptors for ATMS data | Superseded by Doc 3.3 (14) of this meeting |
| 3.3.11 | Proposal for new version of 3-16-030 sequence | Superseded by Doc 3.3 (1) of this meeting |
| 3.3.12&3.3.14 | Proposal for new Standardized BUFR Template for AMDAR / Additional descriptors for AMDAR data and BUFR Template for AMDAR, version 3 | Ongoing |
| 3.3.13 | Proposed new BUFR Template for Integration of routine Aircraft measurement into a Global Observing System (IAGOS) | Not yet |
| 3.3.15 | Updates to BUFR tables in support of the exchange of satellite data | Superseded by Doc 3.3 (25) of this meeting |

II.   Status of proposals at the Joint meeting of CT-MTDCF and ET-DRC

| Paragraph | Title | Validation |
| --- | --- | --- |
| 3.1.2 | Template for synoptic reports from sea stations suitable for ship observation data from VOS stations | Ongoing |
| 3.1.3 (1) | Air Chemistry | Operational |
| 3.1.4 | IEEE representation (for BUFR Edition 5) | Pending |
| 3.1.5 (1) | National and WMO station identification and the AWS BUFR templates: TM307092 and TM307093 | Ongoing |
| 3.1.7 | Proposal for updated template for temperature profiles, descriptors and new or updated code table entries * (some of new entries in the code tables are pre-operational) | Ongoing |
| 3.1.8.2 | BUFR/CREX Templates for Tide Elevation Data | Ongoing |
| 3.1.13 | Entries for volume (3-D) radar data | Done with 0 01 097 revised |
| 3.1.15 | Template for the wave observations from different platforms suitable for WAVEOB data (table references shall be changed) | Ongoing |
| 3.3.1 | CGMS/WMO Task Force on Satellite Data Codes for Common Code Table C-13 | Superseded by Doc 3.3 (25) of this meeting |
| 3.3.5.2 | Table B and Table D entries for encoding of enhanced data from IASI | Superseded by Doc 3.3 (25) of this meeting |
| 3.4 | Master table for oceanographic data | Superseded by Doc 3.5 of this meeting |
| 3.5.3 | New descriptors for representation of UV radiation data | Superseded by Doc 3.3 (8) of this meeting |
| 3.5.5 | New Descriptors for Surface Aviation Observations | Ongoing |

Note: (1) Proposal in the document at the joint meeting has been partially implemented.

III.   Status of proposals at the meeting of ET-DRC in Darmstadt

| Paragraph | Title | Implementation date |
| --- | --- | --- |
| 3.1.2 | CREX Templates for tide elevation | Canceled |
| 3.1.4 | Air Chemistry | Ongoing; 0 15 021 superseded by the Doc 3.1.3 (1) of Joint meeting and now operational |
| 3.1.8 | EUCOS template for radiosonde data | Superseded by Doc 3.3 (11) of this meeting |
| 3.1.10 | New Table B descriptors for passive remote sensing by star occultation | Canceled |

- ANNEX TO PARAGRAPH 3.2.1

The current version numbers of BUFR and CREX are 14 and 6, respectively, and 15 and 7 are allocated for "pre-operational to be implemented by next amendment". The version numbers of master tables of BUFR and CREX to be effective on 15 September 2010 will be;

(a)	15 and 7 as "Version implemented on 15 September 2010" for BUFR and CREX, respectively

(b)	16, which is in common for both BUFR and CREX, as "Pre-operational to be implemented by next amendment"

(c)	8 - 15 for CREX as "Not used"

- ANNEX TO PARAGRAPH 3.2.2

Add the new entry in Section 3, Octet No.7, Bit 3:

| Section 3 – Data description section |
| --- |
| Octet No. | Contents |
| 7 | Bit 3 = 1 | Data converted from a TAC message |
|  | Bit 3 = 0 | Other data |

Example:

Wind direction 0 11 001 = 260 is reported in a BUFR message.

If Bit 3 = 1, than 0 11 001 = 260 represents any value from 255 to 264 degrees true.

If Bit 3 = 0, than it may be expected, that 0 11 001 = 260 represents just only 260 degrees true.

- ANNEX TO PARAGRAPH 3.3.2

Add the new Table B Descriptor and the flag table (for validation)

| Descriptor | Element Name | Unit | Scale | Reference value | Bit Width |
| --- | --- | --- | --- | --- | --- |
| 0 08 084 | Significance of supplemental data | Flag table | 0 | 0 | 6 |

Flag Table 0 08 084

| Bit number | Meaning |
| --- | --- |
| 1 | Data determined by national decision |
| 2 | Data determined by regional decision |
| 3-5 | Reserved |
| All 6 | Missing |

Example: in practice, a BUFR SYNOP message containing national data could therefore have the following outline:

3 07 080	WMO standard data

0 08 084	Supplementary surface data significance (bit 1 set to 1)

0 04 024          	Time displacement (reset to 0 )  (if required)

0 XX YYY      	Nationally determined data

0 XX YYY

…

Data category	International Subcategory	Name

000	100	Hourly synoptic observations from fixed-land stations

(SYNOP) with additional national data

101	Intermediate synoptic observations from fixed-land 				stations (SYNOP) with additional national data

102	Main synoptic observations from fixed-land stations

(SYNOP) with additional national data

103	Hourly synoptic observations from mobile land stations 			(SYNOP MOBIL) with additional national data

104	Intermediate synoptic observations from mobile

land stations (SYNOP MOBIL) with additional

national data

105	Main synoptic observations from mobile land stations 			(SYNOP MOBIL) with additional national data

- ANNEX TO PARAGRAPH 3.3.3, including 3.3.20

Where possible existing code sequences have been adopted, new and modified descriptors are detailed below with the full BUFR template at Annex A.  New descriptors are highlighted in blue.

Note: As there can be around 10-40 strokes recorded per second, the template was designed so that replication was only used for the location and height of each sensor contributing to a lightning single strike.

Add the new descriptors and modify the existing descriptors.

a)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 111 | x-axis error ellipse major component | m | -1 | 0 | 17 |

Actual value e. g. 6400m range 0 to 1,000,000 m

b)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 112 | y-axis error ellipse minor component | m | -1 | 0 | 17 |

Here, if x=y then it is a radial error, and the angle (see 020114) will be zero

Actual value 2410 m, range 0 to 1,000,000 m

c)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 113 | z-axis error ellipse component | m | -1 | 0 | 17 |

Here, if x=y=z then it is a spherical error, and the angle (see 020115) will be zero

Actual Value 2460 m, range as above

d)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 114 | Angle of x-axis in error ellipse | Degree | 2 | -18000 | 16 |

Here is the angle of the error defined in b & c above. Cartesian with sign bit

Actual value 33.40 range -180.00 to 180.00

e)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 115 | Angle of z-axis in error ellipse | Degree | 2 | -18000 | 16 |

Here is the angle of the error defined in b, c  & d above. Cartesian with sign bit

Actual value 12.45.

f)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 116 | Emission height of cloud stroke | m | 0 | 0 | 16 |

This parameter is used by DWD (LINET)  for height above ground of stroke Actual Value 1200m range 0-20000

g)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 117 | Amplitude of lightning strike | A | -1 | 0 | 20 |

Here we would need to introduce a amplitude measure in Amps or kA. This value was first developed nationally by DWD.  This has been modified to allow negative values from original proposal of scale = 0 and data width =19.

Example 5.6KA coded as 5600 range -320000 to 320000

h)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 118 | Lightning detection error | m | 0 | 0 | 19 |

This seems to be radial error measured in Metres or Km. An alternative for systems not capable of describing in x,y and z. This value was first developed nationally by DWD.

Example 6900m range 0 to 500000

i)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 119 | Lightning discharge polarity | Code table | 0 | 0 | 2 |

| 0 | Not Defined |
| --- | --- |
| 1 | Positive |
| 2 | Negative |
| 3 | Missing Data |

Here we have a simple table self explanatory, changed from “Polarity of stroke” from a suggestion by Jeff Ator/Eva Červená

j)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 25 035 | Decision Method for Polarity | Code table | 0 | 0 | 3 |

| 0 | Not defined |
| --- | --- |
| 1 | Individual voltage deflection |
| 2 | Current based, above a threshold |
| 3 | Voltage based, above a threshold |
| 4 | Consensus of sensors, current above a threshold |
| 5 | Consensus of sensors, voltage above a threshold |
| 6 | Reserved |
| 7 | Missing data |

Certain sensors use a current decision above a threshold, others directly measure the voltage deflection .Changed to 25 group from a suggestion by Jeff Ator/Eva Červená

k)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 121 | Threshold value for polarity decision | V | 3 | 0 | 16 |

Used with j) 020121 or all zero if not defined, typically +1.000 Volt.

l)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 122 | Threshold value for polarity decision | A | 0 | 0 | 16 |

Used with j) 020122 or all zero if not defined, typically +2000 A.

m)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 123 | Minimum threshold for detection | V m-1 | 3 | 0 | 16 |

This is the minimum signal level acceptable for processing.

e.g. 0.005v or 5mv, or typically just above the noise floor of the detector.

n)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 124 | Lightning stroke or flash | Code table | 0 | 0 | 2 |

| 0 | Not defined |
| --- | --- |
| 1 | Lightning stroke |
| 2 | Lightning flash, by manual observation, or if equipment insensitive to stroke resolution |
| 3 | Missing data |

o)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 25 175 | Modified residual | Numeric | 2 | 0 | 13 |

Here the modified residual calculated from the loci of the sensors and signal to noise ratios for the flash. Actual value 0.71 range 0.00 to 10.00. Changed to 25 group from a suggestion by Jeff Ator/Eva Červená

p) Existing code

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 20 023 | Other Weather | Flag table | 0 | 0 | 18 |

Used to indicate cloud to ground or cloud to cloud.

q)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 25 063 | Central processor or system identifier | Code table | 0 | 0 | 8 |

| 0 | Not defined |
| --- | --- |
| 1 | Main processor |
| 2 | Backup processor |
| 3-254 | Reserved |
| 255 | Missing data |

This is where we identify the Flash Location Processor or system identity so that in multi integrated system we can identify where the event location was developed. Typically a value of 1 here.

Moved to 25 group from a suggestion by Jeff Ator/Eva Červená

r)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 1 00 001 | Delayed replication of 1 descriptor |  |  |  |  |
| 0 31 002 | Extended delayed descriptor replication factor | Numeric |  |  |  |
| 3 01 058 | New sequence descriptor |  |  |  |  |

As presented, this will define the number or sensors and locations taking part in the lightning stroke. This would be a minimum of 4 for ATDnet, typically 8 sensors contributing to the actual strike.

s)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 02 184 | Type of lightning sensor | Code table | 0 | 0 | 4 |

Here we need to add new entry 6 as recommended the ATDnet VLF waveform correlated sensor.

t)

| Table Reference | Element Name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0 02 121 | Mean frequency | Hz | -8 | 0 | 7 |

Here this is where systems could be split into cells that work on different frequencies

It would be needed to know which sensors are associated with this frequency

Actual value 13777 Hz so scales are changed, with 202136,201236, before and reset after with 201000 and 202000.

u) A new descriptor 004008 was rejected in favour of using the existing 004006 descriptor and resetting to the desired scale as detailed below

201152  to increase data width to 30 bits

202135  to get scale 7

004006

202000

201000

v) Amend the Sub-Category 30 in the Category 0 of Common Code table C-13 as follows.

From

Category 0 Surface data – Land Sub Category 30 Spherics Locations (SFLOC)

To

Category 0 Surface data – Land Sub Category 30 Sferics Locations

Universal BUFR Template for representation of lightning data.

This template is to be submitted for representation of high resolution lightning data from Land, Ship, Mobile, Aircraft or Satellite. Developed by Paula Taylor - Observations Research & Development - UK Met Office.

| 3 01 058 |  | Date/time of lightning event |  |
| --- | --- | --- | --- |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 012 | Hour | Hour |
|  |  | Minute | Minute |
| 2 01 152 |  |  |  |
| 2 02 135 |  |  |  |
|  | 0 04 006 | Seconds | Second |
| 2 02 000 |  |  |  |
| 2 01 000 |  |  |  |
|  |  | Horizontal and vertical coordinates of lightning event |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 20 111 | x-axis error ellipse | m scale -1,0,17 |
|  | 0 20 112 | y-axis error ellipse | m scale -1,0,17 |
|  | 0 20 113 | z-axis error ellipse | m scale -1,0,17 |
|  | 0 20 114 | Angle of x-axis in error ellipse | Degree scale 2,-18000,16 |
|  | 0 20 115 | Angle of z-axis in error ellipse | Degree scale 2,-18000,16 |
|  | 0 20 116 | Emission height of cloud stroke | M scale 0,0,16 |
|  |  | Emission information |  |
|  | 0 20 117 | Amplitude of lightning strike | A, scale -1,0,20 |
|  | 0 20 118 | Lightning detection error | m, scale 0,0,19 |
|  | 0 20 119 | Lightning discharge polarity | Code table scale 0,0,2 |
|  | 0 25 035 | Decision method for polarity (v or a) | Code table scale 0,0,3 |
|  | 0 20 121 | Threshold voltage for polarity decision | V scale 3,0,16 |
|  | 0 20 122 | Threshold current for polarity decision | A scale 0,0,16 |
|  | 0 20 123 | Minimum threshold for detection | V scale 3,0,16 |
|  | 0 20 124 | Lightning stroke or flash | Code table scale 0,0,2 |
|  | 0 25 175 | Modified residual | Numeric scale2,0,13 |
|  | 0 20 023 | Other weather (for c2g or c2c identification) | Flag table scale 0,0,18 |
|  |  | Sensor processing |  |
|  | 0 25 063 | Central processor identifier | Code table, scale 0,0,8 |
| 202136 |  |  |  |
| 201136 |  |  |  |
|  | 0 02 121 | Mean frequency (to define centre frequency, if used) | Hertz, scale-8,0,7 |
| 201000 |  |  |  |
| 202000 |  |  |  |
|  | 0 25 061 | Software identification and version number | CCITT IA5 |
|  | 0 02 184 | Type of lightning detection sensor | Code table |
|  | 0 02 189 | Capability to discriminate lightning strike | Flag table |
|  | 0 25 036 | Atmospherics location method | Code table |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor Number of Sensors contributing | Numeric |
| 3 01 059 |  | Identification of sensor site and instrumentation |  |
|  | 3 01 021 | Latitude (high accuracy) of sensor | Degree, scale 5 |
|  |  | Longitude (high accuracy) of sensor | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 032 | Height of sensor above local ground (for lightning) | m, scale 1 |

- ANNEX TO PARAGRAPH 3.3.4

Add the entry for XBT/XCTD Launcher Type

0 22 178

XBT/XCTD launcher Type

Code figure

91			TURO/CSIRO Quoll Autolauncher

<<Activities by JCOMM>>

The JCOMM TT-TDC has recently been working to update the VOS Template, based on requirements of the JCOMM Ship Observations Team and for climatological purposes, specifically, there are some extra metadata and data types that need to be added, e.g.

-	At least 6 VOSClim climate elements (included in Appendix B)

-	Need for a Unique ID on each message (CRC or key)

-	Other items useful to data managers and program managers

-	There is also a need for encryption of Ship IDs/call signs as per WMO Executive Council 	Resolution 27 (EC-LIX) and the changes made in 2008 (based on comments by Dr Liz Kent) 	will also be expanded upon as other similar issues exist with existing code tables.

While working on this update, the JCOMM Task Team decided to implement a new approach to developing BUFR templates. The aim of this approach was to develop a set of generic sequences which could be used for any Marine Observing platform to report data types, as components of the template. This new approach was drafted in June 2010 and the initial draft documents were sent out to the IPET-DRC for comments in July 2010, including a new version of the VOS Template, which relies on these newly proposed sequences.

IPET-DRC, in particular Dr Eva Červená, was thanked by JCOMM for the feedback on the draft documents sent out in July.  Initially JCOMM will request the addition of 26 new sequences to capture common Marine/Ocean data types. It was anticipated that later this year, JCOMM will request the addition of 26 new sequences to capture common Marine data types.

It was noted that in coming months the VOS template and the 26 proposed sequences will be finalised and again sent out via email to the IPET-DRC, in two separate documents, for comment. Some additional descriptors would be proposed at that time and several requests for extra entries in existing code tables will be requested.

The team agreed that a new descriptor will be needed for salinity to express sea water salinity with units of PSU.

Dr Eva Červená commented that the original VOS templates (in validation) would need to be removed in the future. The Ship Observations Team and JCOMM Task team agrees that this would be useful once a revised template is finalised.

- ANNEX TO PARAGRAPH 3.3.5

Modify the name of entry 000 and add the new entry 002 in the Category 008 of Common Code Table C-13

| Data categories | International data sub-categories (BUFR Ed. 4, CREX Ed.2) |
| --- | --- |
| Code figure | Name | Code figure | Name |
| 008 | Physical/chemical | 000 | Surface ozone |
|  | constituents | 001 | Ozone vertical sounding |
|  |  | 002 | Total ozone |

Proposal for modifications/additions in Tables C6 and C7 of the Manual on the GTS

- Surface ozone

It is proposed to change the current wording “Ozone measurement at surface” to “Surface ozone” because total ozone measurement is also performed at the surface.

| BUFR | T1T2A1 = ISE | Surface ozone |
| --- | --- | --- |
| CREX | T1T2A1 = KSE | Surface ozone |

- Total ozone  and Ozone sounding

| BUFR | T1T2A1 = IUE | Ozone vertical sounding |
| --- | --- | --- |
| CREX | T1T2A1 = KUE | Ozone vertical sounding |
| BUFR | T1T2A1 = IUL | Total ozone |
| CREX | T1T2A1 = KUL | Total ozone |

The above proposals will be submitted also to the Meeting of the CBS Expert Team on WIS-GTS Operation and Implementation (ET-OI) (Geneva, 22 to 24 September 2010).

- ANNEX TO PARAGRAPH 3.3.6

Add the new entries to Common Code table C-4 for a recording type:

| Requesting Agency | Reason for addition | Code to use (if available) | Name of code table element |
| --- | --- | --- | --- |
| National Oceanographic Data Center of NOAA/USA | For historical XBT data provided by the US Navy. | 7 | Sippican MK-8 Linear Recorder |
| Atlantic Oceanographic Marine Laboratory of NOAA/USA | A new system has been adopted on some ships recording XBT data | 49 | TSK MK-150 Compatible recorder for both XBT and XCTD |
| Australian CSIRO | A new system has been designed as an update to its Devil System | 72 | TURO/CSIRO Quoll XBT Acquisition System |

- ANNEX TO PARAGRAPH 3.3.7

Add the four entries to Common Code Table C-5

| Code figure for I6I6I6 | Code figure for BUFR (Code table 0-01-007) | Code figure for GRIB Edition 2 | Meaning |
| --- | --- | --- | --- |
| 850 | 850 | 850 | Combination of TERRA and AQUA |
| 851 | 851 | 851 | Combination of NOAA 16 to NOAA 19 |
| 852 | 852 | 852 | Combination of Metop-1 to Metop-3 |
| 853 | 853 | 853 | Combination of METEOSAT and DMSP |

Entries 850, 851 and 852 will be used in the specification of the satellites used to create atmospheric motion vectors.  Entry 853 will be used in the specification of the satellites used to create multi-sensor precipitation data.

Update the entry in Common Code Table C-5 stating “850-998 Reserved” with “870-998 Reserved”.

Add as a clarification (in brackets) to Common Code Table C-5 the terms Metop-B, Metop-A and Metop-C after METOP-1, METOP-2 and METOP-3 respectively.

Add the Note to the Common Code table C-5

Note:	Within the ranges 000 to 849 and 870 to 998, even deciles indicate polar orbiting satellites and odd deciles indicate geostationary satellites.  The range from 850 to 869 shall be used to indicate combinations of satellites, so the aforementioned decile rule does not apply to values in this range.

- ANNEX TO PARAGRAPH 3.3.8

For UV-B radiation

A proposal for representation of UV radiation was developed in cooperation of Météo-France and the Czech Hydrometeorological Institute (CHMI). The proposed descriptor 0 14 072 was recommended for validation in September 2008. At the ET-AWS-6 meeting, Mr. Michel Leroy formulated new requirements for UV-B radiation; based on them descriptor 0 14 072 has been modified as shown below.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 072 | Global UV irradiation | J m-2 | 0 | –4000000 | 23 | J m-2 | 0 | 7 |

Note:

- Global UV irradiation (0 14 072) is UV energy integrated over period specified for spectral band specified. 0 14 072 shall be preceded by a time period descriptor and by 0 02 071 (Spectrographic wavelength) and 0 02 072 (Spectrographic width). E.g. If 0 14 072 is used for Global UV-B irradiation, 0 02 071 and 0 02 072 shall specify spectral band 280 to 315 nm.

For Humidity

The ET-AWS-6 meeting recommended changing the name of 0 13 111 from “Soil moisture, volumetric or water potential” to “Soil moisture”.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 111 | Soil moisture | g kg-1 | 0 | 0 | 10 | g kg-1 | 0 | 4 |

For Lightning

Detailed discussion about the unit of 0 20 126 (Lightning rate of discharge) has resulted into deleting of the note originally proposed to refer to this descriptor and to modification of the unit to become “h-1” preferred by the ET-AWS-6 meeting.

Additional discussion took place in July 2010, regarding the data width of 0 20 126. Ms Paula Taylor (UK) explained that the maximum value 100 000 requested by the ET AWS corresponded to sensors capable of detection up to 30 km, but not to detectors with the operation range of 200 km. Consequently, the data width of 0 20 126 has remained unchanged, but the data width of 0 20 127 (Lightning – distance from station) was modified to cover the range of 200 km. Moreover, also scale and data width of 0 20 128 (Lightning – direction from station) was modified as the existing scale 0 (the direction expressed in whole degrees) would lead to gross errors at longer detection ranges.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 126 | Lightning rate of discharge | h-1 | 0 | 0 | 23 | h-1 | 0 | 7 |
| 0 20 127 | Lightning - distance from station | m | -3 | 0 | 8 | m | -3 | 3 |
| 0 20 128 | Lightning - direction from station | Degree true | 1 | 0 | 12 | Degree true | 1 | 4 |

For Depth of fresh snow

The existing BUFR/CREX descriptor 0 13 012 Depth of fresh snow (m, 2, -2, 12) is not capable to meet the requested demand for high precision (in 0.001 m). To avoid the necessity to apply all three operators 201Y, 202Y and 203Y, a new descriptor 0 13 118 was proposed for validation. This proposal had been discussed with IPET-DRC members in February 2010, and consequently supported by the ET-AWS-6 meeting.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 118 | Depth of fresh snow (high accuracy) | m | 3 | 0 | 14 | m | 3 | 5 |

For Soil heat flux

At the end of the ET-AWS-6 meeting, the author of this document received preliminary specification for “Soil heat flux” from Mr. Francesco Sabatini (CAgM). Based on this requirement, a new BUFR/CREX descriptor 0 14 057 (Soil heat flux) is proposed for validation.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 057 | Soil heat flux | J m-2 | –1 | –1000 | 11 | J m-2 | –1 | 4 |

Radiation terminology

At the end of June 2010, Mr. Karl Monnik, the Chair of ET-AWS, distributed a proposal for replacing the terms “radiation” and “irradiation” in the names of the descriptors from Class 14, currently in the stage of validation, by “radiant exposure".

According to radiation experts of CHMI, the following terms could be used (all of them correct, having identical meaning) :

“radiation integrated over period specified” or

"irradiation" or

“radiant exposure".

If the term “radiant exposure" were to be used in the names of BUFR/CREX descriptors, it would have to be applied not only in the descriptors proposed for validation, but also in the already operational entries of Class 14.

Note: Mr. Monnik spotted an editorial mistake in the name of 0 14 054 that should be corrected to “Photosynthetically active radiation, integrated over period specified”.

Revised Annex to draft Recommendation 6.1/2 (CBS-XIV) – JUNE 2010

Functional Specifications for Automatic Weather Stations

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | Status 5) |
| --- | --- | --- | --- | --- | --- |
| ATMOSPHERIC PRESSURE |  |  |  |  |  |
| Atmospheric Pressure | 500 – 1080 hPa | 10 Pa | I, V | 0 10 004 | OP |
| TEMPERATURE 9) |  |  |  |  |  |
| Ambient air temperature (over specified surface) 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 101 | OP |
| Dew-point temperature 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 103 | OP |
| Ground (surface) temperature (over specified surface) 14) | -80 °C – +80 °C | 0.1 K | I, V | 0 12 120 | VAL |
| Soil temperature14) | -50 °C – +50 °C | 0.1 K | I, V | 0 12 130 | OP |
| Snow temperature 14) | -80 °C – 0 °C | 0.1 K | I, V | 0 12 131 | VAL |
| Water temperature - river, lake, sea, well | -2 °C – +100 °C | 0.1 K | I, V | 0 13 082 or 0 22 043 | OP OP |
| HUMIDITY 9) |  |  |  |  |  |
| Relative humidity | 0 – 100% | 1% | I, V | 0 13 003 | OP |
| Mass mixing ratio | 0 – 100% | 1% | I, V | 0 13 110 | VAL |
| Soil moisture | 0 – 103 g kg-1 | 1 g kg-1 | I, V | 0 13 111 | VAL |
| Water vapour pressure | 0 – 100 hPa | 10 Pa | I, V | 0 13 004 | OP |
| Evaporation/evapotranspiration | 0 – 0.2 m | 0.1 kg m-2 0.0001 m | T | 0 13 033 | OP |
| Object wetness duration | 0 – 86 400 s | 1 s | T | 0 13 112 | VAL |
| WIND |  |  |  |  |  |
| Direction | 0 11,13); 1( – 360( | 1( | I, V | 0 11 001 | OP |
| Speed | 0 – 75 m s-1 | 0.1 m s-1 | I, V | 0 11 002 | OP |
| Gust Speed | 0 – 150 m s-1 | 0.1 m s-1 | I, V | 0 11 041 | OP |
| X,Y component of wind vector Z component of wind vector (horizontal and vertical profile) | -150 – 150 m s-1 -40 – 40 m s-1 | 0.1 m s-1 | I, V | 0 11 003 0 11 004 0 11 006 | OP OP OP |
| Turbulence type (Low levels and wake vortex) 16) | up to 15 types | BUFR Table Not specified yet | I, V | - | N |
| Turbulence intensity 16) | up to 15 types | BUFR Table Not specified yet | I, V | - | N |
| RADIATION 6) |  |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 | OP |
| Background luminance | 0 – 1∙105 Cd m-2 | 1 Cd m-2 | I, V | 0 14 056 | VAL |
| Global downward solar radiation | 0 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 028 | OP |
| Global upward solar radiation | -1∙108 – 0 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 052 | VAL |
| Diffuse solar radiation | 0 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 029 | OP |
| Direct solar radiation | 0 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 030 | OP |
| Downward long-wave radiation | 0 – 6∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | OP |
| Upward long-wave radiation | -6∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | OP |
| Net radiation | -1∙108 – 1∙108 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 053 | VAL |
| UV-B radiation 8) | 0 – 26∙104 J m-2 | 1 J m-2 | I, T, V | 0 14 072 | VAL |
| Photosynthetically active radiation 22) | 0 – 6∙107 J m-2 | 1∙103 J m-2 | I, T, V | 0 14 054 | VAL |
| Surface albedo | 0 – 100% | 1% | I, V | 0 14 019 | OP |
| Soil heat Flux | -1∙104 – 1∙104 J m-2 | 1. 101 J m-2 | I, T, V | 0 14 057 | VAL |

| CLOUDS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Cloud base height | 0 – 30 km | 10 m | I, V | 0 20 013 | OP |
| Cloud top height | 0 – 30 km | 10 m | I, V | 0 20 014 | OP |
| Cloud type, convective vs. other types | up to 30 classes | BUFR Table | I | 0 20 012 | OP |
| Cloud hydrometeor concentration | 1 – 700 hydrometeors dm-3 | 1 hydrometeor dm-3 | I, V | 0 20 130 | VAL |
| Effective radius of cloud hydrometeors | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 131 | VAL |
| Cloud liquid water content | 1∙10-5–1.4∙10-2 kg m-3 | 1∙10-5 kg m-3 | I, V | 0 20 132 | VAL |
| Optical depth within each layer | Not specified yet | Not specified yet | I, V | - | N |
| Optical depth of fog | Not specified yet | Not specified yet | I, V | - | N |
| Height of inversion | 0 – 1 000 m | 10 m | I, V | 0 20 093 | VAL |
| Cloud cover | 0 – 100% | 1% | I, V | 0 20 010 | OP |
| Cloud amount | 0 – 8/8 | 1/8 | I, V | 0 20 011 | OP |
| PRECIPITATION |  |  |  |  |  |
| Accumulation 7) | 0 – 1600 mm | 0.1 kg m-2, 0.0001 m | T | 0 13 011 | OP |
| Depth of fresh snowfall | 0 –1000 cm | 0.001 m | T | 0 13 118 | VAL |
| Duration | up to 86 400 s | 60 s | T | 0 26 020 | OP |
| Size of precipitating element 17) | 1∙10-3 – 0.25 m | 1∙10-3 m | I, V | 0 13 058 0 20 066 | OP OP |
| Intensity - quantitative | 0 – 2000 mm h-1 | 0.1 kg m-2 s-1, 0.1 mm h-1 | I, V | 0 13 155 | OP |
| Type | up to 30 types | BUFR Table | I, V | 0 20 021 | OP |
| Rate of ice accretion | 0 – 1 kg dm-2 h-1 | 1∙10-3 kg dm-2 h-1 | I, V | 0 13 114 | VAL |
| OBSCURATIONS |  |  |  |  |  |
| Obscuration type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Hydrometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Lithometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Hydrometeor radius | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 133 | VAL |
| Extinction coefficient | 0 – 1 m-1 | 0.00001 m-1 | I, V | 0 15 029 | VAL |
| Meteorological Optical Range 10) | 1 – 100 000 m | 1 m | I, V | 0 15 051 | VAL |
| Runway visual range | 1 – 4 000 m | 1 m | I, V | 0 20 061 | OP |
| Other weather type | up to 18 types | BUFR Table | I, V | 0 20 023 | OP |
| LIGHTNING |  |  |  |  |  |
| Lightning rates of discharge | 0 – 100 000 | h-1 | I, V | 0 20 126 | VAL |
| Lightning discharge type (cloud to cloud, cloud to surface) | 3 types | BUFR Code Table | I, V | 0 20 023 | OP |
| Lightning discharge polarity | 2 types | BUFR Code Table | I, V | 0 20 119 | VAL |
| Lightning discharge energy | Not specified yet | Not specified yet | I, V | - | N |
| Lightning - distance from station | 0 – 3∙104 m | 103 m | I, V | 0 20 127 | VAL |
| Lightning - direction from station | 1( – 360( | 1 degree | I, V | 0 20 128 | VAL |

| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Flow discharge – river | 0 – 2.5∙105 m3 s-1 | 0.1 m3 s-1 | I, V | 0 23 040 | VAL |
| Flow discharge – well | 0 – 50 m3 s-1 | 0.001 m3 s-1 | I, V | 0 23 041 | VAL |
| Ground water level | 0 – 1 800 m | 0.01 m | I, V | 0 13 074 | VAL |
| Ice surface temperature 14) | -80 °C – +0 °C | 0.5 K | I, V | 0 12 132 | VAL |
| Ice thickness - river, lake 15) | 0 – 50 m | 0.01 m | I, V | 0 08 029 0 13 115 | VAL |
| Ice thickness - glacier, sea 15) | 0 – 4 270 m | 1 m | I, V | 0 08 029 0 13 115 | VAL |
| Water level | 0 – 100 m | 0.01 m | I, V | 0 13 071 0 13 072 | OP OP |
| Wave height | 0 – 50 m | 0.1 m | V | 0 22 021 | OP |
| Wave period 18) | 0 – 100 s | 1 s | V | 2 01 129 0 22 011 2 01 000 | OP |
| Wave direction | 0 13); 1 – 360 degrees | 1 degrees | V | 0 22 001 | OP |
| 1D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | V, T | 2 01 135 0 22 069 2 01 000 | OP |
| 2D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | V, T | 2 01 135 0 22 069 2 01 000 | OP |
| Water practical salinity 18) | 0 – 400 psu12 | 10-3 psu | I, V | 2 01 130 0 22 064 2 01 000 | OP |
| Water conductivity 18) | 0 – 600 S m-1 | 10-6 S m-1 | I, V | 2 01 132 0 22 066 2 01 000 | OP |
| Water pressure 18) 19) | 0 – 11x107 Pa | 100 Pa | I, V | 2 07 001 0 22 065 2 07 000 | OP |
| Ice thickness 18) | 0 – 3 m | 0.015 m | T | 2 01 133 2 02 129 0 20 031 2 02 000 2 01 000 | OP |
| Ice mass | 0 – 50 kg m-1 | 0.5 kg m-1 (on 32 mm rod) | T | 0 20 135 | VAL |
| Snow density (liquid water content) | 100 – 700 kg m-3 | 1 kg m-3 | T | 0 13 117 | VAL |
| Tidal elevation with respect to local chart datum 18) | -10 – +30 m | 0.001 m | I, V | 2 01 129 0 22 038 2 01 000 | OP |
| Tidal elevation with respect to national land datum 18) | -10 – +30 m | 0.001 m | I, V | 2 01 129 0 22 037 2 01 000 | OP |
| Meteorological residual tidal elevation (surge or offset) 18) 20) | -10 – +16m | 0.001 m | I, V | 0 22 040 Note 20) | OP |
| Ocean Current - Direction | 0 13); 1( – 360( | 1( | I, V | 0 22 004 or 0 22 005 | OP OP |
| Ocean Current - Speed | 0 – 10 m s-1 | 0.01 m s-1 | I, V | 0 22 031 or 0 22 032 | OP OP |
| OTHER SURFACE VARIABLES |  |  |  |  |  |
| Runway conditions | up to 10 types | BUFR Table | I, V | 0 20 085 | OP |
| Braking action/friction coefficient | up to 7 types | BUFR Table | I, V | 0 20 089 | OP |
| State of ground | up to 30 types | BUFR Table | I, V | 0 20 062 | OP |
| Type of surface specified | up to 15 types | BUFR Table | I, V | 0 08 010 | OP |
| Snow depth | 0 – 25 m | 0.01 m | T | 0 13 013 | OP |
| OTHER |  |  |  |  |  |
| Gamma radiation dose rate 21) | 1 – 103 nSv h-1 | 0.1 nSv h-1 | I, T | 0 24 014 | VAL |
| Categories of stability | 9 types | BUFR Table | I, V | 0 13 041 | OP |

Notes:

- Name of variable, in line with WMO vocabulary and Technical Regulations.

- Maximum Effective Range - Maximum range of measuring capability; units traceable to SI.

- Minimum Reported Resolution – Lower resolution of reporting is not permitted.

- Mode of Observation – Type of data being reported:

I:  Instantaneous – 1-minute value (instantaneous as defined in WMO-No. 8, Part II, paragraph 1.3.2.4);

V:  Variability – Average (mean), Standard Deviation, Maximum, Minimum, Range, Median, etc. of samples – those reported depend upon meteorological variable;

T: Total – Integrated value over defined period; maximum 24 hours for all parameters except radiation which requires a maximum of one hour (exception, see note 6), and precipitation accumulation (6 hours maximum). The relevant element descriptor shall be preceded by a time period descriptor 0 04 024 (in hours) or 0 04 025 (in minutes).

A:  Average (mean) value.

- BUFR/CREX descriptors for representation of the listed variables;

OP:   Operational descriptors of BUFR/CREX Table B, Version Number 14.

VAL: Descriptors to be validated.

N:     Not yet specified requirements.

- Radiation energy amounts are given over a 24-hour period.

- Maximum interval: 6 hours.

- Definition of UV-B according to WMO-No. 8 (Vol. 1, Chapter on Radiation). Descriptor 0 14 072 (Global UV irradiation) was recommended for validation in September 2008, revised in July 2010.

- Humidity related variables (i.e. dew point) expressed as temperature are collected under temperature.

- MOR uniquely related to "extinction coefficient", (, by MOR = -ln(5%)/(.

- Direction to indicate 0 (zero) if speed = 0.

- Absolute Salinity (kg.kg-1) is now being used for ocean applications (IOC Res XXV-7). However, salinity that is reported to national oceanographic data centers remains the Practical Salinity (psu). Ocean water is about 35 psu. Lake Asal (Ethiopia) is the most saline body of water on earth with 348 psu salt concentration.

- Calm.

- Temperature data represented by 0 12 101, 0 12 103, 0 12 113, 0 12 120, 0 12 130, 0 12 131 and 0 12 132 shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values. Temperature t (in degrees Celsius) shall be converted into temperature T (in degrees Kelvin) using equation: T = t + 273.15.

- Ice thickness 0 13 115 shall be preceded by 0 08 029 (Surface type) set to 11, 12, 13 or 14 to specify river, lake, sea or glacier, respectively.

- If the UNIT is specified as “BUFR Table”, the BUFR descriptor cannot be proposed without the content of the table being available.

- 0 13 058 (Size of precipitation element) is capable to express size of any precipitation element, apart from hailstones. Size of hailstones shall be represented by 0 20 066.

- These requirements being confirmed, it has to be noted that the selected descriptors are suitable for the normal operating conditions and shall be combined with appropriate operator descriptors to allow representation of the extreme values or the requested high precision.

- Operator 2 07 Y is recommended to be used with Water pressure 0 22 065 (Pa, -3, 0, 17), if the data are produced in BUFR, Edition 4. The same result, i.e. change to (Pa, -2, 0, 21) would be obtained by the combined use of the less sophisticated operators 201Y and 202Y:

2 01 132

2 02 129

0 22 065 Reported value of “Water pressure”

2 02 000

2 01 000

- The following sequence is to be used to change data width and reference value of 0 22 040 (m, 3, -5000, 14) to become (m, 3, -10000, 15):

2 01 129

2 03 015

0 22 040 New reference value = -10000

2 03 255

0 22 040 Reported value of “Meteorological residual tidal elevation”

2 01 000

2 03 000

- Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.

- Photosynthetically active radiation (PAR). Various forms of the electromagnetic energy flux in the 400 – 700 nm wavelength range, either as integrated spectra or using different weighting functions. For example converted to the photosynthetic photon flux (PPF) in quanta per second per square meter, or mole of quanta per second per square meter or microeinsteins per second per square meter. Approximate conversion is 1 J m-2 s-1 equivalent to 5 μE m-2 s-1 based on a mean wavelength of 550 nm.

The introduced changes are written in blue or marked by side bars.

- ANNEX TO PARAGRAPH 3.3.9

Add the following sequences to BUFR table D:

(All sky radiance product main sequence)

3 10 028 	3 01 071 	Product information

3 01 011 	Date

3 01 013 	Time

3 01 021 	Latitude / longitude

0 30 021 	Number of pixels per row

0 30 022 	Number of pixels per column

0 10 002 	Orbit height

3 04 036 	All sky radiance cloud coverage

0 02 152 	Satellite instrument used

0 02 167 	Radiance computational method

1 01 011 	Replication operator

3 04 037 	All sky radiance data

(All sky radiance data)

3 04 037 	0 02 153 	Satellite channel centre frequency

0 02 154 	Satellite channel band width

0 12 063 	Brightness temperature

0 08 011 	Pixel type: clear

0 12 063 	Brightness temperature (clear)

0 08 011 	Pixel type: cloudy

0 12 063 	Brightness temperature (cloudy)

0 08 011 	Cancel type

0 08 003 	Vertical significance: low cloud

0 12 063 	Brightness temperature (low cloud)

0 08 003 	vertical significance: mid cloud

0 12 063 	Brightness temperature (mid cloud)

0 08 003 	vertical significance: high cloud

0 12 063 	Brightness temperature

- ANNEX TO PARAGRAPH 3.3.11

Add the new entry and the code table for “Geopotential height calculation” for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 02 191 | Geopotential height calculation | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Code table 0 02 191 - Geopotential height calculation

|  | Geopotential height calculation |
| --- | --- |
| Code figure |  |
| 0 | Geopotential height calculated from pressure |
| 1 | Geopotential height calculated from GPS height |
| 2 | Geopotential height calculated from radar height |
| 3 - 14 | Reserved |
| 15 | Missing value |

0 02 191 has been re-introduced into the EUCOS template as shown in the revisited version of the template below.

It is to be noted, however, that representation of radiosonde data using template TM 309052 does not require inclusion of 0 02 191 even as an additional parameter. TM 309052 contains 0 07 004 (Pressure) and 0 10 009 (Geopotential height) and it is obvious that pressure is the vertical coordinate and that geopotential height is derived (calculated) from pressure.

EUCOS template for representation of radiosonde data with geopotential height as the vertical coordinate (revisited in July 2010)

This template is suitable for representation of high resolution radiosonde data with geopotential height as the vertical coordinate, the vertical resolution being limited by the length of BUFR message.

| 3 01 111 |  | Identification of launch site and instrumentation |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 0 25 061 |  | Software identification and version number | CCITT IA5 |
| 0 01 081 |  | Radiosonde serial number | CCITT IA5 |
| 0 01 082 |  | Radiosonde ascension number | Numeric |
| 0 02 067 |  | Radiosonde operating frequency | Hz, scale -5 |
| 0 02 095 |  | Type of pressure sensor | Code table |
| 0 02 096 |  | Type of temperature sensor | Code table |
| 0 02 097 |  | Type of humidity sensor | Code table |
| 0 02 081 |  | Type of balloon | Code table |
| 0 02 082 |  | Weight of balloon | kg, scale 3 |
| 0 02 084 |  | Type of gas used in balloon | Code table |
| 0 02 191 |  | Geopotential height calculation | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Surface station measurements |  |
| 0 10 004 |  | Pressure | Pa, scale –1 |
| 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, scale 2 |
|  | 0 12 101 | Temperature/dry-bulb temperature(scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 13 003 | Relative humidity | % |
| 0 07 032 |  | Height of sensor above local ground (for wind measurement) | m, scale 2 |
| 0 02 002 |  | Type of instrumentation for wind measurement | Flag table |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, scale 2 |
| 0 20 003 |  | Present weather | Code table |
| 3 02 049 |  | Cloud information reported with vertical soundings |  |
|  | 0 08 002 | Vertical significance | Code table |
|  | 0 20 011 | Cloud amount (of low or middle clouds Nh) | Code table |
|  | 0 20 013 | Height of base of cloud (h) | m, scale –1 |
|  | 0 20 012 | Cloud type (low clouds CL) | Code table |
|  | 0 20 012 | Cloud type (middle clouds CM) | Code table |
|  | 0 20 012 | Cloud type (high clouds CH) | Code table |
|  | 0 08 002 | Vertical significance ( = missing value) | Code table |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Temperature, dew-point, relative humidity and wind data at height levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 055 |  | Temperature, dew-point, relative humidity and wind data at a height level with radiosonde position |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 13 009 | Relative humidity (see Note 4) | %, scale 1 |
|  | 0 12 103 | Dew-point temperature (scale 2) (see Note 4) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |

Notes:      (1)	Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

- Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds).

- Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

- If the radiosonde is equipped with a relative humidity sensor, 0 13 009 shall be reported as mandatory and dew-point temperature may be included as a derived value. If the radiosonde is equipped with a dew-point temperature sensor, 0 12 103 shall be reported and 0 13 009 shall be set to a missing value.

- ANNEX TO PARAGRAPH 3.3.13

Modify text of bit No.1 and bit No.2 in the Flag table 0 08 083 (Nominal value indicator):

Bit No.		Meaning

1		Adjusted to or with respect to representative height of sensor above local ground (or

deck of marine platform)

2		Adjusted to or with respect to representative height of sensor above water surface

to allow reporting the representative height of a sensor, to which the actual height of the sensor is adjusted. The existing wording, strictly speaking, allows only reporting the nominal values of measured elements “adjusted with respect to representative heights of sensors”.

Editorial correction in TM 307093

In the existing template TM 307093, the construction of the data present bit-map is described:

| 2 36 000 | Backward reference bit map |
| --- | --- |
| 1 01 000 | Delayed replication of 1 descriptor |
| 0 31 001 | Delayed descriptor replication factor = number of element descriptors |
| 0 31 031 | Data present indicator |

This is not correct if TM 307093 is appended to a data sequence with delayed replications. It is proposed to modify the text “Delayed descriptor replication factor = number of element descriptors” to become “Delayed descriptor replication factor = number of data items”.

Add the Note to TM 307093

If TM 307093 is appended to a data sequence with delayed replications, e.g. TM 307091 or TM 307092, a multi-subset BUFR message should not be compressed. The bits set to 0 in the “data present bit-map” might not correspond to the same elements after the compression as prior to the compression.  Therefore it is proposed to add a note under template TM 307093:

Note:

If TM 307093 is applied to a data sequence containing delayed replications, a multi-subset BUFR message shall not be compressed, per regulation 94.6.3 viii.

- ANNEX TO PARAGRAPH 3.3.14

Add the new Table D entry:

|  |  | ATMS (Advanced Technology Microwave Sounder) data |
| --- | --- | --- |
| 3 10 061 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating centre |
|  | 0 01 034 | Identification of originating/generating sub-centre |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 0 33 079 | Granule level quality flags |
|  | 0 33 080 | Scan level quality flags |
|  | 0 33 078 | Geolocation quality |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 25 075 | Satellite antenna corrections version number |
|  | 1 11 000 | Delayed replication of 11 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 0 05 042 | Channel number |
|  | 2 02 131 | Increase scale by 3 |
|  | 0 02 153 | Satellite channel center frequency |
|  | 0 02 154 | Satellite channel band width |
|  | 2 02 000 | Cancel increase scale |
|  | 0 02 104 | Antenna polarization |
|  | 0 12 066 | Antenna temperature |
|  | 0 12 163 | Brightness temperature |
|  | 0 12 158 | Noise-equivalent delta temperature while viewing cold target |
|  | 0 12 159 | Noise-equivalent delta temperature while viewing warm target |
|  | 0 33 081 | Channel data quality flags |

Add the new Table B entries:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 12 066 | Antenna temperature | K | 2 | 0 | 16 | C | 2 | 5 |
| 0 12 158 | Noise-equivalent delta temperature while viewing cold target | K | 2 | 0 | 12 | C | 2 | 4 |
| 0 12 159 | Noise-equivalent delta temperature while viewing warm target | K | 2 | 0 | 12 | C | 2 | 4 |
| 0 33 078 | Geolocation quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 33 079 | Granule level quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 080 | Scan level quality flags | Flag table | 0 | 0 | 20 | Flag table | 0 | 7 |
| 0 33 081 | Channel data quality flags | Flag table | 0 | 0 | 12 | Flag table | 0 | 4 |

Add the following new Code table entries to existing BUFR/CREX Code table 0 02 104:

0 02 104 (Antenna polarization)

6	Quasi horizontal polarization

7	Quasi vertical polarization

Add the Code/Flag tables for the new Table B descriptors:

0 33 078  Geolocation quality

| Code figure | Meaning |
| --- | --- |
| 0 | Nominal – altitude and Ephemeris data available |
| 1 | Missing at most a small gap of altitude and Ephemeris data |
| 2 | Missing more than a small gap of altitude and Ephemeris data, but no more than a granule boundary |
| 3 | Missing more than a granule boundary of altitude and Ephemeris data |
| 4-14 | Reserved |
| 15 | Missing |

0-33-079  Granule level quality flags

| Bit | Meaning |
| --- | --- |
| 1-5 | Reserved |
| 6 | The No. 1-No.7 health checks failed |
| 7 | The No. 8-No.15 health checks failed |
| 8 | The No. 16-No.23 health checks failed |
| 9 | The No. 24-No.31 health checks failed |
| 10 | The No. 32-No.39 health checks failed |
| 11 | The No. 40-No.47 health checks failed |
| 12 | The No. 48-No.55 health checks failed |
| 13 | The No. 56-No.63 health checks failed |
| 14 | The No. 64-No.70 health checks failed |
| 15 | Quadratic correction applied to the radiometric transfer function for non-linearity correction |
| All 16 | Missing value |

0-33-080  Scan level quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Divide-by-zero condition or computation loop failed to converge in the K/Ka and V (KAV) Band PRT |
| 8 | Divide-by-zero condition or computation loop failed to converge in the WG Band PRT |
| 9 | Divide-by-zero condition or computation loop failed to converge in the K/Ka, V, W, G Band Receiver Shelf PRT K temperature computation |
| 10 | Out of range condition for the K/Ka and V Band PRT |
| 11 | Out of range condition for the WG Band PRT |
| 12 | KAV PRT temperature inconsistency |
| 13 | WG PRT temperature inconsistency |
| 14 | Time Sequence Error |
| 15 | Data Gap - Missing scan(s) preceding the current scan |
| 16 | KAV PRT Sufficiency - Insufficient KAV PRT data are available |
| 17 | WG PRT Sufficiency - Insufficient WG PRT data are available |
| 18 | Space View antenna position error |
| 19 | Blackbody antenna position error |
| All 20 | Missing value |

0-33-081  Channel data quality flags

| Bit | Meaning |
| --- | --- |
| 1-2 | Reserved |
| 3 | Moon in space view |
| 4 | Gain error - the lowest black-body count is smaller than or equal to the highest space view count in a scan |
| 5 | Calibration with fewer than preferred samples |
| 6 | Space view data sufficiency check - insufficient space view samples are available |
| 7 | Black-body view data sufficiency check - insufficient black-body view samples are available |
| 8 | Out of range condition for the Space view |
| 9 | Out of range condition for the Black-body View |
| 10 | Space view inconsistency |
| 11 | Black-body view inconsistency |
| All 12 | Missing value |

Add the new entry to Common Code Table C-13:

Under Data Category 021 = Radiances (satellite measured), add the following new International Data Sub-Category entry:

| 006 | Advanced technology microwave sounder |
| --- | --- |

- ANNEX TO PARAGRAPH 3.3.15

Add the new entry to BUFR code table:

0-20-056  “Cloud phase”

4	 			Clear

Add the new entries to Common Code tables:

C-1 and C-11  “Originating Centers”

177			U.S. NOAA National Ocean Service

C-12  “Sub-centres of Originating centres”

| 177 | U.S. NOAA National Ocean Service | 1 | Center for Operational Oceanographic Products and Services |
| --- | --- | --- | --- |
|  |  | 2 | Coastal Survey Development Laboratory |

- ANNEX TO PARAGRAPH 3.3.16

#### Add the new Table D entry:

|  |  | VIIRS (Visible/Infrared Imager Radiometer Suite) data |
| --- | --- | --- |
| 3 10 062 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating centre |
|  | 0 01 034 | Identification of originating/generating sub-centre |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 2 01 133 | Increase bit width |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 08 076 | Type of band |
|  | 0 33 082 | Geolocation quality flags |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 072 | Pixel(s) type |
|  | 0 08 029 | Remotely sensed surface type |
|  | 1 05 000 | Delayed replication of 5 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 0 05 042 | Channel number |
|  | 0 02 155 | Satellite channel wavelength |
|  | 0 33 083 | Radiance data quality flags |
|  | 0 14 043 | Channel radiance |
|  | 0 15 042 | Reflectance |

#### Add the new Table B entries:

| Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 02 155 | Satellite channel wavelength | m | 9 | 0 | 16 | m | 9 | 5 |
| 0 14 043 | Channel radiance | W m-2 sr-1 um-1 | 4 | 0 | 23 | W m-2 sr-1 um-1 | 4 | 7 |
| 0 15 042 | Reflectance | % | 2 | 0 | 14 | % | 2 | 5 |
| 0 33 082 | Geolocation quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 083 | Radiance data quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |

Add the Note to Class 14 of Table B:

(7)	Channel radiance (014043) uses um to represent the wave number.

Add the new code table entries to existing BUFR/CREX Code table 0 08 072 and 0 08 076:

0 08 072  (Pixel(s) type)

3           Probably clear
4           Probably cloudy

0 08 076  (Type of band)

5           M

6           I

7           Day/night

Add the new Code/Flag tables for proposed new Table B descriptors:

0-33-082  Geolocation quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Invalid Input Data (Indicates that any of the Spacecraft Ephemeris or Attitude Data is Invalid) |
| 8 | Bad Pointing (Indicates that the sensor LOS does not intersect the geoid, is near the limb, has invalid sensor angles or other similar condition) |
| 9 | Bad Terrain (Indicates that the algorithm could not obtain a valid terrain value) |
| 10 | Invalid Solar Angles |
| 11 | Missing at most a small gap of altitude and Ephemeris data |
| 12 | Missing more than a small gap of altitude and Ephemeris data, but no more than a granule boundary |
| 13 | Missing more than a granule boundary of altitude and Ephemeris data |
| 14 | The number of encoder pulse values per delta time is not as expected |
| 15 | Solar Eclipse during Earth view scan |
| All 16 | Missing value |

0-33-083  Radiance data quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Poor calibration quality due to bad space view offsets, OBC view offsets, etc or use of a previous calibration view |
| 8 | Saturated Pixel |
| 9 | Missing Data - Data required for calibration processing is not available for processing |
| 10 | Calibrated pixel Radiance out of range |
| 11 | Calibrated pixel Reflectance or EBBT out of range |
| 12 | The Moon has corrupted the space view |
| 13 | Scan data is not Present (No valid data) |
| 14 | Quality for this scan-line is reduced. The value is determined by the combined number of steps required to find a replacement for thermistor or calibration source data |
| 15 | Bad Detector |
| All 16 | Missing value |

Add the new sub-category to Common Code Table C-13 under Data category 021 = Radiances (satellite measured):

| 007 | Visible/Infrared Imager Radiometer Suite |
| --- | --- |

- ANNEX TO PARAGRAPH 3.3.17

Add the new entries to Class 00 of Table B:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 00 024 | Code figure | CCITT IA5 | 0 | 0 | 64 | Character | 0 | 8 |
| 0 00 025 | Code figure meaning | CCITT IA5 | 0 | 0 | 496 | Character | 0 | 62 |
| 0 00 026 | Bit number | CCITT IA5 | 0 | 0 | 16 | Character | 0 | 2 |
| 0 00 027 | Bit number meaning | CCITT IA5 | 0 | 0 | 496 | Character | 0 | 62 |

Add thenew entries to Category 00 of Table D:

|  |  | Code table definition |
| --- | --- | --- |
| 3 00 015 | 0 00 030 | Descriptor defining sequence (FXY) |
|  | 1 02 000 | Delayed replication of 2 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 0 00 024 | Code figure |
|  | 0 00 025 | Code figure meaning |
|  |  | Flag table definition |
| 3 00 016 | 0 00 030 | Descriptor defining sequence (FXY) |
|  | 1 02 000 | Delayed replication of 2 descriptors |
|  | 0 31 001 | Delayed descriptor replication factor |
|  | 0 00 026 | Bit number |
|  | 0 00 027 | Bit number meaning |

- ANNEX TO PARAGRAPH 3.3.18

Add the Note under Class 20, referring to 0 20 019 and to 0 20 020:

(8)	0 20 019 (Significant present or forecast weather) and 0 20 020 (Significant recent weather phenomena) shall be used in accordance with Code Table 4678 (Reference: Manual on Codes, WMO-No. 306, Volume I.1).

- ANNEX TO PARAGRAPH 3.3.19

Delete the footnote *  below to the Class 24

*	New named unit	In other	Old special unit		Relationship,

and symbol	SI units	and symbol		old to new units

becquerel (Bq)	s–1	curie (Ci)		1 Ci = 3.7 x 1010 Bq

sievert (Sv)	J kg-1	rem (rem)		1 rem = 0.01 Sv

- ANNEX TO PARAGRAPH 3.3.21

3 09 070: Vertical profile for numerical weather prediction data

| Descriptor | Element or sequence name | Comments |
| --- | --- | --- |
| Identification |  |  |
| 0 01 035 | Originating Centre | Required |
| 0 01 032 | Originating Process | Required |
| 0 01 015 | Station name |  |
| 0 01 062 | Short ICAO location indicator |  |
| 3 01 001 | block # stn # |  |
| Location and reference time |  |  |
| 3 01 021 | lat long | Required |
| 2 07 001 | Increase scale factor by 1; reference value and data width are recalculated in accordance with the Table C specification of operator 2 07 YYY | This table C operator requires BUFR Edition 4 |
| 0 10 001 | Station elevation (non coordinate) | Required. This value is the official or best estimate of the actual elevation of the station. It is provided for comparison with the model's virtual terrain elevation. The two can be substantially different in rugged terrain. We increased the scale factor to make the value directly comparable with 0 07 030 below. |
| 2 07 000 | Cancel increase scale factor operator |  |
| 3 01 011 | yy mm dd |  |
| 3 01 012 | hh mm | Reference time of the forecast |
| 0 08 086 | Vertical significance for NWP | Set bit 9 to 1 (= virtual station height) |
| 0 07 030 | Height of station above mean sea level | Elevation of model terrain at the lat/lon of station. As qualified by 0 08 084, this value is both station and model specific. Required. |
| Vertical profile data |  |  |
| 0 25 031 | NWP-generated vertical profile thinning method | In this instance, the term "thinning" refers to a method that may be applied to select a subset of levels from a model that may have many native vertical levels. Selecting only a subset reduces the size of the pseudo-sounding, at the possible cost of information loss and extra processing. |
| 0 08 021 | Time significance | Set to 4 (= forecast) or 16 (= analysis) or 27 (=first guess) |
| 0 04 014 | Time increment in hours | Validity time of the forecast expressed as a Delta T from reference time. In the case of an analysis or 00 hour forecast, the value is set to zero. |
| Point data at station height (including column-integrated data) |  |  |
| 0 10 004 | Pressure |  |
| 0 10 051 | Pressure reduced to MSL |  |
| 0 10 009 | Geopotential Height |  |
| 0 20 010 | Cloud cover (total) |  |
| 0 13 095 | Total column water vapour |  |
| Replication loop for levels |  |  |
| 1 28 000 |  |  |
| 0 31 002 |  | The number of levels used in the vertical profile is determined by this replication. The number of levels is discretionary and comprises all agl levels and pressure levels. |
| Data on pressure coordinates |  |  |
| 1 13 000 |  | Short delayed replication (set to 1 if vertical coordinate is pressure; 0 otherwise) |
| 0 31 000 |  |  |
| 0 08 086 | Vertical significance for NWP | Set bit 1 to value=0 and other bits as appropriate |
| 0 07 004 | Pressure | Non-surface levels on the model's native vertical coordinate are transposed to pressure coordinate. This makes the levels more readily intelligible for human interpretation and easier to use by generic display applications. The levels may correspond exactly to native model levels, or be interpolated between model levels to pressure levels chosen by the generating centre. |
| 0 11 001 | Wind direction (degrees true) |  |
| 0 11 002 | Wind speed (m/s) |  |
| 0 12 101 | Temperature |  |
| 0 12 102 | Wet Bulb Temperature |  |
| 0 12 103 | Dew Point |  |
| 0 10 009 | Geopotential Height |  |
| 1 03 000 |  | Embedded short delayed replication. Set to 1 if optional enhanced model data is to be included. |
| 0 31 000 |  |  |
| 0 11 022 | Divergence |  |
| 0 11 021 | Relative vorticity |  |
| 0 11 005 | Vertical motion |  |
| Data at 10 metres AGL |  |  |
| 1 04 000 |  | Short delayed replication (set to 1 if vertical coordinate is 10 metres agl; 0 otherwise) |
| 0 31 000 |  |  |
| 0 08 086 | Vertical significance for NWP | Set bit 1 to value = 1 and bit 8 to value =1 |
| 0 07 006 | Height above station | Set to 10 m |
| 0 11 001 | Wind direction (degrees true) |  |
| 0 11 002 | Wind speed (m/s) |  |
| Data at 2 metres AGL |  |  |
| 1 05 000 |  | Short delayed replication (set to 1 if vertical coordinate is 2 metres agl; 0 otherwise) |
| 0 31 000 |  |  |
| 0 08 086 | Vertical significance for NWP |  |
| 0 07 006 | Height above station | Set to 2 m |
| 0 12 101 | Temperature |  |
| 0 12 102 | Wet Bulb Temperature |  |
| 0 12 103 | Dew Point Temperature |  |

| DESCRIPTORS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference Value | Data Width |
| 0 08 086 | Vertical significance for NWP | Flag Table | 0 | 0 | 12 |
| 0 25 031 | NWP-generated vertical profile thinning method | Code Table | 0 | 0 | 3 |

| Flag Table 0 08 086 |
| --- |
| Vertical significance for Numerical Weather Prediction |
| Bit No. | Meaning |
| 1 | Model "ground" surface |
| 2 | Standard level |
| 3 | Tropopause level |
| 4 | Maximum wind level |
| 5 | Significant temperature level |
| 6 | Significant humidity level |
| 7 | Significant wind level |
| 8 | Vertically interpolated level (This should be set to 1 for points on the vertical profile that fall between the model's native vertical levels). |
| 9 | Virtual station height |
| 10 | Reserved |
| 11 | Reserved |
| All 12 | Missing |

| Code Table 0 25 031 |
| --- |
| NWP-generated vertical profile thinning method |
| Code Figure | Meaninggu54ᴀ54Thinning may be applied to reduce the number of levels of a pseudo-sounding containing ma |
| 0 | Reserved |
| 1 | No thinning applied (all native model levels are included from base to top of pseudo-sounding). |
| 2 | Native model levels are present only if they are significant levels as per regulations B/C 25 for conventional TEMP soundings |
| 3 | A predefined subset of native model levels is present |
| 4 | No native model levels are present. All profile levels are interpolated to a predefined set of pressure coordinate levels |
| 5 | Reserved |
| 6 | Reserved |
| 7 | Missing |

Note: None of the code figures exclude the addition of interpolated levels at the discretion of the generating centre.

- ANNEX TO PARAGRAPH 3.3.22

The sequence 3 02 067 is proposed for validation. It is assumed that it will be slightly modified during the validation process.

| 3 07 086 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data for RA VI |
| --- | --- | --- |
|  | 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates |
|  | 3 02 031 | Pressure data |
|  | 3 02 035 | Basic synoptic “instantaneous” data |
|  | 3 02 036 | Clouds with bases below station level |
|  | 0 08 002 | Vertical significance |
|  | 3 02 037 | State of ground, snow depth, ground minimum temperature |
|  | 3 02 066 | Dangerous weather phenomena |
|  | 3 02 043 | Basic synoptic “period” data |
|  | 3 02 044 | Evaporation data |
|  | 1 01 002 | Replicate next descriptor 2 times |
|  | 3 02 045 | Radiation data (from 1 hour and/or 24 hour period) |
| 3 02 067 |  | Additional synoptical data |
|  | 0 08 084* | Significance of supplemental data |
|  | 0 01 023* | Observation Sequence number |
|  | * | Additional “instantaneous” data |
|  | * | Additional present weather |
|  | * | Visibility in different directions |
|  | * | Sea data (Observations from a coastal station) |
|  | * | Clouds |
|  | * | Additional wind data |
|  | * | Additional weather |
|  | * | Additional 9SpSpspsp groups |

*) not in WMO Template

The additions of DWD expands to

|  |  |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data in DWD | in FM12 | Unit, scale |
| --- | --- | --- | --- | --- | --- |
| 3 07 086 |  |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data for RA VI |  |  |
| Additional parameters in DWD |
| 3 02 067 | 0 08 084 |  | Significance of supplemental data |  | Flag table, 0 |
|  | 0 01 023 |  | Observation Sequence number |  | Numeric, 0 |
|  |  |  | Additional “instantaneous” data |  |  |
|  | 0 04 025 |  | Time period (= 0 minutes) |  | Minute, 0 |
|  | 0 02 177 |  | Method of snow depth measurement |  | Code table, 0 |
|  |  |  | Additional present weather |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 003 |  | Present weather | 960ww 961ww | Code table, 0 |
|  |  |  | Visibility in different directions |  |  |
|  | 1 03 000 |  | Delayed replication of 3 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 05 021 |  | Bearing or azimuth | 981VV-988VV | Degreetrue, 0 |
|  | 0 20 001 |  | Horizontal visibility | VV | m, –1 |
|  | 0 05 021 |  | Bearing or azimuth (=set to missing to cancel previous entry) | 981VV-988VV | Degreetrue, 0 |
|  |  |  | Sea data (Observations from a coastal station) |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |  |
|  |  | 0 02 038 | Method of sea/water temperature measurement |  | Code table, 0 |
|  |  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) |  | m, 2 |
|  |  | 0 22 043 | Sea/water temperature | 222.. 0sTwTwTw, 333 925TwTw | K, 2 |
|  |  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) |  | m, 2 |
|  | 1 03 000 |  | Delayed replication of 2 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 33 041 |  | Attribute of following value |  | Code tabel, 0 |
|  | 0 20 058 |  | Visibility seawards from a coastal station | 980VsVs | m,-1 |
|  | 0 22 061 |  | State of the sea | 924SVs | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 022 |  | Wind waves |  |  |
|  |  | 0 22 002 | Direction of wind waves |  | Degreetrue, 0 |
|  |  | 0 22 012 | Period of wind waves | 222.. 2PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves | HwHw | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 023 |  | Swell waves |  |  |
|  |  | 0 22 003 | Direction of swell waves | 222.. 3dw1dw1 dw2dw2 | Degreetrue, 0 |
|  |  | 0 22 013 | Period of swell waves | 4Pw1Pw1, 5Pw2Pw2 | s, 0 |
|  |  | 0 22 023 | Height of swell waves | Hw1Hw1, Hw2Hw2 | m, 1 |
|  |  |  | Clouds | 941CDp, 943CLDp, |  |
|  | 1 03 000 |  | Delayed replication of 3 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 012 |  | Cloud type (C) | 941C, 943CL | Code table, 0 |
|  | 0 20 090 |  | Special clouds | 993CS | Code table, 0 |
|  |  |  | Additional wind data |  |  |
|  | 0 04 025 |  | Time period in minutes ( =-60 ) |  | Minute, 0 |
|  | 0 11 042 |  | Maximum wind speed (10 min mean wind) | 912ff | m s-1, 1 |
|  |  |  | 902tt 912ff .. mandatory ff>=18 |  |  |
|  | 1 04 000 |  | Delayed replication of 4 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 902tt | Minute, 0 |
|  | 0 11 042 |  | Maximum wind speed (10 min mean wind) | 912ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  |  |  | Significant change in wind speed and/or direction | e.g. 913ff 904tt 913ff |  |
|  | 1 12 000 |  | Delayed replication of 12 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=22 time of occurrence of wind shift) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 904tt | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement ( = 0 to eliminate the previous value of time displacements ) |  | Minute, 0 |
|  |  |  | Additional weather |  |  |
|  | 1 06 000 |  | Delayed replication of 6 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 20 003 |  | Present weather | 962ww, 963w1w1, 964ww, 965w1w1, 966ww, 967w1w1 | Code table, 0 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  |  |  | Additional 9SpSpspsp groups |  |  |
|  | 1 13 000 |  | Delayed replication of 13 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 05 021 |  | Bearing or azimuth | Da, Dp | Degreetrue, 0 |
|  | 0 05 021 |  | Bearing or azimuth (different directions span a sector) | Da, Dp | Degreetrue, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 024 |  | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent, 5 = Severe) |  | Code table, 0 |
|  | 0 20 025 |  | Obscuration |  | Flag table, 0 |
|  | 0 20 026 |  | Character of obscuration |  | Code table, 0 |
|  | 0 20 027 |  | Phenomenon occurrence |  | Flag table, 0 |
|  | 0 20 063 |  | Special phenomena "to be developed" |  | Code table, 0 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |

#### Explanations and Regulations (to be discussed during the validation process)

The structure of the template with regard to the different time data based on the BUFR regulations.

94.5.3.4 "The consecutive occurrence of two identical element descriptors or identical sets of element descriptors from classes 04 to 07 inclusive shall demote a range of values bounded by the corresponding element values. This enables the definition of layers and simple time periods."

94.5.3.5 "The definition of line, areas, volumes and more complex time attributes shall be accomplished using descriptors from class 04 to 07 in association with suitable descriptors from class 08."

94.5.3.6 "The consecutive occurrence of two or more non-identical element descriptors from classes 04 to 07 inclusive shall infer that all such elements remain in effect until redefined, unless such elements define an increment."

E.g. for the purpose of a "significant change in wind speed and/or direction" the following sequence of descriptors was prepared:

|  |  |  | Significant change in wind speed and/or direction | e.g. 913ff 904tt 913ff |  |
| --- | --- | --- | --- | --- | --- |
|  | 1 12 000 |  | Delayed replication of 12 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=22 time of occurrence of wind shift) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 904tt | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement ( = 0 to eliminate the previous value of time displacements |  | Minute, 0 |

The first "time period (or displacement)" is set to -10 minutes and has the significance of "time averaged". This means that all following values are 10 minute mean values.

The second "time (period or) displacement" has the significance of e.g. "start of phenomenon". This means that all following values have the additional information of the time of commencement.

Due to the different specified time significance the second "time period or displacement" does not redefined the time period specified for the calculation of average.

The third "time (period or) displacement" has the significance of "time of occurrence of wind shift" to determine the time of a significant change. This means that all following values have the additional information of the time of occurrence of wind shift.

Afterwards both the "time significance" and the "time (period or) displacement" is set to 0 to cancel all previous time periods or displacements.

Similar is valid for the following sequence:

This sequence is meant for various 9SpSpspsp groups in diverse order and combination.

|  |  |  | Additional 9SpSpspsp groups |  |  |
| --- | --- | --- | --- | --- | --- |
|  | 1 13 000 |  | Delayed replication of 13 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) |  | Minute, 0 |
|  | 0 05 021 |  | Bearing or azimuth | Da, Dp | Degreetrue, 0 |
|  | 0 05 021 |  | Bearing or azimuth (different directions span a sector) | Da, Dp | Degreetrue, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 024 |  | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent, 5 = Severe) |  | Code table, 0 |
|  | 0 20 025 |  | Obscuration |  | Flag table, 0 |
|  | 0 20 026 |  | Character of obscuration |  | Code table, 0 |
|  | 0 20 027 |  | Phenomenon occurrence |  | Flag table, 0 |
|  | 0 20 063 |  | Special phenomena "to be developed" |  | Code table, 0 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |

Within the replication the first two descriptors "Time period (or displacement)" define a period or are set to missing if the period is not specified.

With "Time significance" set to an appropriate value and "Time (period or) displacement" it is possible to specify the time of commencement, occurrence or ending.

This does not redefine the specified period.

The next two descriptors "Bearing or azimuth" define a sector or are set to missing if the sector is not specified. Sometimes the information about a sector is needed if no specific direction of a phenomenon is applicable.

- ANNEX TO PARAGRAPH 3.3.23

a.   Add the new Code table for supplementary information in "Special phenomena"

0 20 063

Special phenomena

(To be developed)

Code figure				Status

0	Reserved		Pre-operational

1	Highest wind speed gusts greater than 11.5 m/s	Pre-operational

2	Highest mean wind speed greater than 17.5 m/s	Pre-operational

3-5	Reserved		Pre-operational

7	Visibility greater than 100000 m    	Pre-operational

8-9	Reserved		Pre-operational

10-19	Mirage

10 	Mirage - No specification		Pre-operational

11	Mirage - Image of distant object raised (looming)	Pre-operational

12 	Mirage - Image of distant object raised clear above the horizon	Pre-operational

13 	Mirage - Inverted image of distant object	Pre-operational

14	Mirage - Complex, multiple images of distant object (images not inverted)

Pre-operational

15	Mirage - Complex, multiple images of distant object (some images being inverted)

Pre-operational

16 	Mirage - Sun or moon seen appreciably distorted	Pre-operational

17 	Mirage - Sun visible, although astronomically below the horizon	Pre-operational

18 	Mirage - Moon visible, although astronomically below the horizon	Pre-operational

19	Reserved		Pre-operational

20-22	Day darkness, worst in direction specified

20 	Day darkness, bad, worst in direction specified	Pre-operational

21 	Day darkness, very bad, worst in direction specified	Pre-operational

22 	Day darkness, black, worst in direction specified	Pre-operational

23-30	Reserved		Pre-operational

  - Coloration and/or convergence of clouds associated with a tropical disturbance

31 	Slight coloration of clouds at sunrise associated with a tropical disturbance

Pre-operational

32 	Deep-red coloration of clouds at sunrise associated with a tropical disturbance

Pre-operational

33 	Slight coloration of clouds at sunset associated with a tropical disturbance

Pre-operational

34 	Deep-red coloration of clouds at sunset associated with a tropical disturbance

Pre-operational

35 	Convergence of CH clouds at a point below 45° forming or increasing and

associated with a tropical disturbance	Pre-operational

36 	Convergence of CH clouds at a point above 45° associated with a tropical disturbance				Pre-operational

37 	Convergence of CH clouds at a point below 45° dissolving or diminishing and

associated with a tropical disturbance	Pre-operational

38 	Convergence of CH clouds at a point above 45° associated with a tropical disturbance				Pre-operational

39	Reserved		Pre-operational

40-43	Hoar frost or coloured precipitation

40 	Hoar frost on horizontal surfaces	Pre-operational

41 	Hoar frost on horizontal and vertical surfaces	Pre-operational

42 	Precipitation containing sand or desert dust	Pre-operational

43 	Precipitation containing volcanic ash	Pre-operational

44-49	Reserved		Pre-operational

50-59	Nature and/or type of squall

50	Calm or light wind followed by a squall	Pre-operational

51	Calm or light wind followed by a succession of squalls	Pre-operational

52 	Gusty weather followed by a squall	Pre-operational

53 	Gusty weather followed by a succession of squalls	Pre-operational

54 	Squall followed by gusty weather	Pre-operational

55	General gusty weather with squall at intervals	Pre-operational

56	Squall approaching station		Pre-operational

57 	Line squall		Pre-operational

58 	Squall with drifting or blowing dust or sand	Pre-operational

59	Line squall with drifting or blowing dust or sand	Pre-operational

60-69	Variation of temperature during the period specified, associated with glaze or rime

60 	Temperature steady		Pre-operational

61 	Temperature falling, without going below 0°C	Pre-operational

62 	Temperature rising, without going above 0°C	Pre-operational

63 	Temperature falling to a value below 0°C	Pre-operational

64 	Temperature rising to a value above 0°C	Pre-operational

65 	Irregular variation, oscillations of temperature passing through 0°C	Pre-operational

66 	Irregular variation, oscillations of temperature not passing through 0°C	Pre-operational

67 	Variation of temperature not observed	Pre-operational

68 	Not allocated		Pre-operational

69 	Variation of temperature unknown owing to lack of thermograph	Pre-operational

70-79	Variation of visibility during the period specified

70 	Visibility has not varied (sun* visible) towards direction specified	Pre-operational

71	Visibility has not varied (sun* invisible) towards direction specified	Pre-operational

72 	Visibility has increased (sun* visible) towards direction specified	Pre-operational

73 	Visibility has increased (sun* invisible) towards direction specified	Pre-operational

74 	Visibility has decreased (sun* visible) towards direction specified	Pre-operational

75 	Visibility has decreased (sun* invisible) towards direction specified	Pre-operational

76	Fog coming from direction specified	Pre-operational

77 	Fog has lifted, without dissipating	Pre-operational

78 	Fog has dispersed without regard to direction	Pre-operational

79 	Moving patches or banks of fog	Pre-operational

80-89	Optical phenomena

80 	Brocken spectre		Pre-operational

81	Rainbow		Pre-operational

82 	Solar or lunar halo		Pre-operational

83	Parhelia or anthelia		Pre-operational

84 	Sun pillar		Pre-operational

85 	Corona		Pre-operational

86 	Twilight glow		Pre-operational

87 	Twilight glow on the mountains (Alpenglühen)	Pre-operational

88 	Mirage		Pre-operational

89 	Zodiacal light		Pre-operational

90	St. Elmo's fire		Pre-operational

91-1022	Reserved		Pre-operational

1023	Missing value		Pre-operational

b.   Add the new descriptor for Supplementary cloud type

| TABLE REFERENCE |  | BUFR | CREX |
| --- | --- | --- | --- |
| F | X | Y | ELEMENT NAME | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Char) | Status |
| 0 | 20 | 136 | Supplementary cloud type | Code table | 0 | 0 | 9 | Code table | 0 | 3 | Validation |

0 20 136

Supplementary cloud type

Code figure				Status

0-7	Nature of clouds of vertical development

0 	Isolated cumulus humilis and/or cumulus mediocris of vertical development

Validation

1 	Numerous cumulus humilis and/or cumulus mediocris of vertical development

Validation

2 	Isolated cumulus congestus of vertical development  	Validation

3 	Numerous cumulus congestus of vertical development  	Validation

4 	Isolated cumulonimbus of vertical development  	Validation

5 	Numerous cumulonimbus of vertical development  	Validation

6 	Isolated cumulus and cumulonimbus of vertical development  	Validation

7 	Numerous cumulus and cumulonimbus of vertical development  	Validation

8-9	Reserved		Validation

10-19	Orographic clouds

11 	Isolated orographic clouds, pileus, incus, forming	Validation

12 	Isolated orographic clouds, pileus, incus, not changing	Validation

13 	Isolated orographic clouds, pileus, incus, dissolving	Validation

14 	Irregular banks of orographic cloud, föhn bank, etc., forming	Validation

15 	Irregular banks of orographic cloud, föhn bank, etc., not changing	Validation

16 	Irregular banks of orographic cloud, föhn bank, etc., dissolving	Validation

17 	Compact layer of orographic cloud, föhn bank, etc., forming	Validation

18 	Compact layer of orographic cloud, föhn bank, etc., not changing	Validation

19 	Compact layer of orographic cloud, föhn bank, etc., dissolving	Validation

20-29	Cloud conditions over mountains and passes

20 	All mountains open, only small amounts of cloud present	Validation

21 	Mountains partly covered with detached clouds (not more than half the peaks can be 			seen) 	Validation

22 	All mountain slopes covered, peaks and passes free	Validation

23 	Mountains open on observer’s side (only small amounts of cloud present), 	Validation

but a continuous wall of cloud on the other side

24 	Clouds low above the mountains, but all slopes and mountains open 	Validation

(only small amounts of cloud on the slopes)

25 	Clouds low above the mountains, peaks partly covered by precipitation trails or clouds

Validation

26 	All peaks covered but passes open, slopes either open or covered	Validation

27 	Mountains generally covered but some peaks free, slopes wholly or partially covered

Validation

28 	All peaks, passes and slopes covered	Validation

29 	Mountains cannot be seen owing to darkness, fog, snowstorm, precipitation, etc.

Validation

30-34	Reserved		Validation

35-39	Condensation trails

35 	Non-persistent condensation trails	Validation

36 	Persistent condensation trails covering less than 1/8 of the sky	Validation

37 	Persistent condensation trails covering 1/8 of the sky	Validation

38 	Persistent condensation trails covering 2/8 of the sky	Validation

39 	Persistent condensation trails covering 3/8 or more of the sky	Validation

40-49	Cloud conditions observed from a higher level

40 	No cloud or mist observed from a higher level	Validation

41 	Mist, clear above observed from a higher level	Validation

42 	Fog patches observed from a higher level	Validation

43 	Layer of slight fog observed from a higher level	Validation

44 	Layer of thick fog observed from a higher level	Validation

45 	Some isolated clouds observed from a higher level	Validation

46 	Isolated clouds and fog below observed from a higher level	Validation

47 	Many isolated clouds observed from a higher level	Validation

48 	Sea of clouds observed from a higher level	Validation

49 	Bad visibility obscuring the downward view observed from a higher level	Validation

50-510	Reserved		Validation

511	Missing value		Validation

- ANNEX TO PARAGRAPH 3.3.24

  - Entries in table 2555 Mw – "Water-spout(s), tornadoes, whirlwinds, dust devils" allow to encode "Dust devils" which is missing in 0 20 023 – Other weather phenomena. 
An additional entry is proposed:

0 20 023

Other weather phenomena

Bit No.	Status

1 	Dust/sand whirl	Operational

2 	Squalls	Operational

3 	Sand storm	Operational

4 	Dust storm	Operational

5 	Lightning - cloud to surface	Operational

6 	Lightning - cloud to cloud	Operational

7 	Lightning - distant	Operational

8 	Thunderstorm	Operational

9 	Funnel Cloud not touching surface	Operational

10 	Funnel cloud touching surface	Operational

11 	Spray	Operational

12 	Water-spout	Operational

13 	Wind shear	Operational

14	Dust devils	Pre-operational

15-17 	Reserved	Operational

All 18 	Missing value	Operational

  - In table 2555 Mw – "Water-spout(s), tornadoes, whirlwinds, dust devils" following information is given

    - within 3 km of station

    - more than 3 km from station

In BUFR Flag table 020027 – "Phenomenon occurrence" there are (corresponding) entries

- At the station

- In the vicinity

The Question is whether

- "At the station" is equivalent to "within 3 km of station" and

- "In the vicinity" is equivalent to "more than 3 km from station"

- or do we need at least an editorial change for the entries?

Flag Table 020027 is completed (no additional entries are possible)!

Proposed editorial change in Flag table 0 20 027 (in case):

0 20 027

Phenomena occurrence

Bit No.	Status

1 	At time of observation	Operational

2 	In past hour	Operational

3 	In time period for past weather W1W2	Operational

4 	In time period specified	Operational

5 	Reserved	Operational

6 	Below station level	Operational

7 	At the station	Operational

8 	In the vicinity	Operational

All 9 	Missing value	Operational

Notes:

* ....

(1) In conjunction with the observation of water spouts or funnel clouds i.e. within 3 km of station.

(2) In conjunction with the observation of water spouts or funnel clouds i.e. more than 3 km from station.

  - In Code table 3778 – "Supplementary information" some entries concerning the "Time significance" are given:

    - Time of commencement

    - Time of ending ...

    - Time of occurrence ...

The almost saturated BUFR Code table 0 08 021 – "Time significance" provides corresponding entries

- 17 – Start of phenomenon

- 29 – End of scan (if appropriate)

but no entries of "Time of occurrence" and no proper coding of "Time of ending"

Proposal of new entries and editorial changes in 0 08 021:

- 30 – Time of occurrence of a phenomenon

- change 29 in "End of scan or time of ending"

0 08 021

Time significance

Code figure	Status

0 	Reserved	Operational

1 	Time series	Operational

2 	Time averaged	Operational

3 	Accumulated	Operational

4 	Forecast	Operational

5 	Forecast time series	Operational

6 	Forecast time averaged	Operational

7 	Forecast accumulated	Operational

8 	Ensemble mean	Operational

9 	Ensemble mean time series	Operational

10 	Ensemble mean time averaged	Operational

11 	Ensemble mean accumulated	Operational

12 	Ensemble mean forecast	Operational

13 	Ensemble mean forecast time series	Operational

14 	Ensemble mean forecast time averaged	Operational

15 	Ensemble mean forecast accumulated	Operational

16 	Analysis	Operational

17 	Start of phenomenon	Operational

18 	Radiosonde launch time	Operational

19 	Start of orbit	Operational

20 	End of orbit	Operational

21 	Time of ascending node	Operational

22 	Time of occurrence of wind shift	Operational

23 	Monitoring period	Operational

24 	Agreed time limit for report reception	Operational

25 	Nominal reporting time	Operational

26 	Time of last known position	Operational

27 	First guess	Operational

28 	Start of scan	Operational

29 	End of scan or time of ending	Pre-operational

30 	Time of occurrence	Pre-operational

31 	Missing value	Operational

  - Code table 4077 – zz "Variation, location or intensity of phenomena"

zz=99 have the meaning: "Very heavy; killing; very severe; dense; greatly above normal; very thick; very good"

This is unrepresentable in BUFR Code table 0 20 024 - "Intensity of phenomena"

It is proposed to add as last possible entry something like "very severe" or even "disastrous".

0 20 024

Intensity of phenomena

Code figure	Status

0 	No phenomena	Operational

1 	Light	Operational

2 	Moderate	Operational

3 	Heavy	Operational

4 	Violent	Operational

5 	Severe	Operational

6 	Very severe	Pre-operational

7 	Missing value	Operational

  - Code table 3766 S8 – "Snowstorm phenomena (snow raised by the wind)"

To be able to encode all entries of table S8 with the combination of the BUFR descriptors 020025 020026 020027 the code tables should be augmented accordingly.

There is no entry for the information of "impossible to determine whether snow is falling or not".

0 20 025

Obscuration

Bit No.	Status

1 	Fog	Operational

2 	Ice fog	Operational

3 	Steam fog	Operational

4-6 	Reserved	Operational

7 	Mist	Operational

8 	Haze	Operational

9 	Smoke	Operational

10 	Volcanic ash	Operational

11 	Dust	Operational

12 	Sand	Operational

13 	Snow	Operational

14 	Cloud	Operational

15 	Precipitation	Operational

16 	Impossible to determine whether snow is falling or not	Pre-operational

17-20 	Reserved	Operational

All 21 	Missing value	Operational

0 20 026

Character of obscuration

Code figure	Status

0 	No change	Operational

1 	Shallow	Operational

2 	Patches	Operational

3 	Partial	Operational

4 	Freezing	Operational

5 	Low drifting	Operational

6 	Blowing	Operational

7 	Increasing	Operational

8 	Decreasing	Operational

9 	In suspension in the air	Operational

10 	Wall	Operational

11 	Dense	Operational

12 	Whiteout	Operational

13	Drifting and blowing	Pre-operational

14 	Reserved	Operational

15 	Missing value	Operational

- ANNEX TO PARAGRAPH 3.3.25

| Data category | International data sub-category |
| --- | --- |
| 5 | Single level upper-air data (satellite) | 1 | Cloud properties |
| 12 | Surface data (satellite) | 8 | Soil moisture |
| 12 | Surface data (satellite) | 9 | Normalised differential vegetation index (NDVI) |
| 12 | Surface data (satellite) | 10 | Normalised radar backscatter |
| 12 | Surface data (satellite) | 11 | Surface emissivity |
| 30 | Calibration dataset (satellite) | 0 | Subsetted data |
| 30 | Calibration dataset (satellite) | 1 | Collocated data |
| 30 | Calibration dataset (satellite) | 2 | On-board calibration data |
| 30 | Calibration dataset (satellite) | 3 | Bias Monitoring |
| 30 | Calibration dataset (satellite) | 4 | Near Real-Time Correction |
| 30 | Calibration dataset (satellite) | 5 | Re-analysis Correction |

- ANNEX TO PARAGRAPH 3.3.26

New entries in Common Code table C-12: Sub-Centres of Originating Centres defindes by entries in Common Tables C-1 or C-11

Add new entries for Region VI and centre 00250 - COnsortium for Small scale MOdelling  (COSMO)

Code figure	Name	Code figure	Name	Status

250	COSMO	76	RHM (Russia)

(COnsortium for Small scale MOdelling)	78	DWD (Germany)

80	USAM (Italy)

96	HNMS (Greece)

215	MCH (Switzerland)

220	IMGW (Poland)

242	NMA (Romania)

- ANNEX TO PARAGRAPH 3.3.27

a.  Add the new descriptor for Evolution of clouds

| TABLE REFERENCE |  | BUFR | CREX |
| --- | --- | --- | --- |
| F | X | Y | ELEMENT NAME | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Char) | Status |
| 0 | 20 | 137 | Evolution of clouds | Code table | 0 | 0 | 4 | Code table | 0 | 2 | Validation |

0 20 137

Evolution of clouds

Code figure				Status

0	 No change	Validation

1	 Cumulification	Validation

2	 Slow elevation	Validation

3	 Rapid elevation	Validation

4	 Elevation and stratification	Validation

5	 Slow lowering	Validation

6	Rapid lowering	Validation

7 	Stratification	Validation

8 	Stratification and lowering	Validation

9 	Rapid change	Validation

10-14	Reserved 	Validation

15	Missing value	Validation

b.   Add in the Manual on codes, Volume I.2, Attachment II

LIST OF ALPHANUMERIC CODE TABLES RELATED TO

BUFR AND CREX CODE TABLES AND FLAG TABLES

| BUFR/CREX code or flag table | Related code table, regulation or code form in alphanumeric codes | Remarks |
| --- | --- | --- |
| 0 13 057 | Rt — Code table 3552 | — |
| 0 20 040 | S8' — Code table 3776 | — |
| 0 20 137 | n3 — Code table 2863 | — |

c.   Add the new descriptor for Template version number

| TABLE REFERENCE |  | BUFR | CREX |
| --- | --- | --- | --- |
| F | X | Y | ELEMENT NAME | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Char) | Status |
| 0 | 01 | 113 | Template version number defined by originating centre | Numeric | 1 | 0 | 9 | Numeric | 1 | 3 | Validation |

d.   Add the note under Class 20

Notes:

(9)	A true direction from which a phenomenon or clouds are moving value 0 shall indicate "at the station" whereas value 500 shall indicate "all directions".

- ANNEX TO PARAGRAPH 3.4.1

Modify the Regulations B/C 1.9, 5.9 and 10.7

B/C 1.9 “Instantaneous” data required by regional or national reporting practices

If regional or national reporting practices require inclusion of additional “instantaneous” parameters, the sequence descriptor 3 07 080 shall be supplemented by the required element descriptors being preceded by a relevant time period descriptor set to zero, i.e. 0 04 024 = 0 or 0 04 025 = 0.

B/C 5.9 “Instantaneous” data required by regional or national reporting practices

If regional or national reporting practices require inclusion of additional “instantaneous” parameters, the sequence descriptor 3 07 090 shall be supplemented by the required element descriptors being preceded by a relevant time period descriptor set to zero, i.e. 0 04 024 = 0 or 0 04 025 = 0.

B/C 10.7 “Instantaneous” data required by regional or national reporting practices

If regional or national reporting practices require inclusion of additional “instantaneous” parameters, the sequence descriptor 3 08 009 shall be supplemented by the required element descriptors being preceded by a relevant time period descriptor set to zero, i.e. 0 04 024 = 0 or 0 04 025 = 0.

Modify the Regulations B/C 25

General

A BUFR (or CREX) message should be sent when the 100 hPa level is reached.  In any case, a BUFR (or CREX) message shall be produced when the sounding is completed containing data from the entire sounding.

If high resolution data are reported, only one BUFR message should be sent when the 100 hPa level is reached and only one BUFR message shall be produced when the sounding is completed, provided that all standard and significant levels are properly identified in compliance with the relevant B/C 25 Regulations.

B/C 25.7.2.2 Extended vertical sounding significance – Flag table 0 08 042

- All bits set to 0 indicate a level determined by national decision or a level of no significance that has been included when high resolution data are reported.

- ANNEX TO PARAGRAPH 4.1

Amend METAR and SPECI as follows.

FM 15–XIV METAR	Aerodrome routine meteorological report (with or without trend forecast)

FM 16–XIV SPECI	Aerodrome special meteorological report (with or without trend forecast)

C O D E F O R M :

METAR							KMH or

or	COR	CCCC	YYGGggZ	NIL	AUTO	dddffGfmfm 	KTor	dndndnVdxdxdx

SPECI							MPS

NsNsNshshshs

or

RDRDR/VRVRVRVRi		VVhshshs

VVVV	VNVNVNVNDv	or	 w´w´	or

or		RDRDR/VRVRVRVRVVRVRVRVRi		NSC

VVVVNDV				or

or				NCD

CAVOK

WS RDRDR

T´T´/T´dT´d	QPHPHPHPH	REw´w´	or	(WTsTs/SS´)	(RDRDR/ERCReReRBRBR)

WS ALL RWY

NsNsNshshshs

KMH or	VVVV 	w´w´	or

(TTTTT	TTGGgg	dddffGfmfm 	KT or	or	or	VVhshshs

or			MPS	CAVOK	NSW	or

NOSIG)						NSC

(RMK . . . . . . . . . . )

Notes:

(1)	METAR is the name of the code for an aerodrome routine meteorological report. SPECI is the name of the code for an aerodrome special meteorological report. A METAR report and a SPECI report may have a trend forecast appended.

(2)	The groups contain a non-uniform number of characters. When an element or phenomenon does not occur, the corresponding group, or the extension of a group, is omitted from a particular report. Detailed instructions are given for each group in the following Regulations. The groups enclosed in brackets are used in accordance with regional or national decisions. Groups may have to be repeated in accordance with the detailed instructions for each group. The code words COR and NIL shall be used, as appropriate, for corrected and missing reports, respectively.

(3)	The code form includes a section containing the trend forecast identified either by a change indicator (TTTTT = BECMG or TEMPO as the case may be), or by the code word NOSIG.

(4)	The governing criteria for issuing SPECI reports are specified in publication WMO-No. 49 – Technical Regulations [C.3.1].

R E G U L A T I O N S:

15.1	General

15.1.1	The code name METAR or SPECI shall be included at the beginning of each individual report.

15.1.2	When a deterioration of one weather element is accompanied by an improvement in another element (for example, lowering of clouds and an improvement in visibility), a single SPECI report shall be issued.

15.2	Group CCCC

The identification of the reporting station in each individual report shall be indicated by means of the ICAO location indicator.

15.3	Group YYGGggZ

15.3.1	The day of the month and the time of observation in hours and minutes UTC followed, without a space, by the letter indicator Z shall be included in each individual METAR report.

15.3.2	This group shall be included in each individual SPECI report. In SPECI reports, this group shall indicate the time of occurrence of the change(s) which justified the issue of the report.

15.4	Code word AUTO

The optional code word AUTO shall be inserted before the wind group when a report contains fully automated observations without human intervention. The ICAO requirement is that all of the specified elements shall be reported. However, if any element cannot be observed, the group in which it would have been encoded shall be replaced by the appropriate number of solidi. The number of solidi depends on the number of symbolic letters for the specific group which is not able to be reported; i.e. four for the visibility group, two for the present weather group and three or six for the cloud group, as appropriate.

KMH or

15.5	Groups dddffGfmfm	KT or	dndndnVdxdxdx

MPS

15.5.1	The mean true direction in degrees rounded off to the nearest 10 degrees from which the wind is blowing and the mean speed of the wind over the 10-minute period immediately preceding the observation shall be reported for dddff followed, without a space, by one of the abbreviations KMH, KT or MPS, to specify the unit used for reporting wind speed.  Values of wind direction less than 100° shall be preceded by 0 and a wind from true north shall be reported as 360. Values of wind speed less than 10 units shall be preceded by 0.  	However, when the 10-minute period includes a marked discontinuity in the wind characteristics, only data after the discontinuity shall be used for obtaining mean wind speed and maximum gust values, and mean wind direction and variations of the wind direction, hence the time interval in these circumstances shall be correspondingly reduced.

Notes:

(1)	KMH, KT and MPS are the standard ICAO abbreviations for kilometres per hour, knots and metres per second, respectively.

(2)	The unit of wind speed used is determined by national decision. However, the primary unit prescribed in ICAO Annex 5 for wind speed is the metre per second (MPS)kilometre per hour (KMH), with the knot (KT) permitted for use as a non-SI alternative unit until a termination date is decided.

(3)	A marked discontinuity occurs when there is an abrupt and sustained change in wind direction of 30° or more, with a wind speed of 5 m s-120 km h–1 (10 kt) or more before or after the change, or a change in wind speed of 5 m s-120 km h–1 (10 kt) or more, lasting at least two minutes.

15.5.2	In the case of variable wind direction, ddd shall be encoded as VRB when the mean wind speed is less than 1.5 m s-1 (3 knots) (2 m s–1 or 6 km h–1). A variable wind at higher speeds shall be reported only when the variation of wind direction is 180° or more or when it is impossible to determine a single wind direction, for example when a thunderstorm passes over the aerodrome.

15.5.3	If, during the 10-minute period preceding the observation, the total variation in wind direction is 60° or more but less than 180° and the mean wind speed is 1.5 m s-1 (3 knots) (2 m s–1 or 6 km h–1) or more, the observed two extreme directions between which the wind has varied shall be given for dndndnVdxdxdx in clockwise order. Otherwise this group shall not be included.

15.5.4	“Calm” shall be coded as 00000 followed immediately, without a space, by one of the abbreviations KMH, KT or MPS to specify the unit, used normally for reporting wind.

15.5.5	If, during the 10-minute period preceding the observation, the maximum wind gust speed exceeds the mean speed by 5 m s-1 (10 knots) (5 m s–1 or 20 km h–1) or more, this maximum speed shall be reported as Gfmfm immediately after dddff, followed immediately, without a space, by one of the abbreviations KMH, KT or MPS to specify the units used for reporting wind speed. Otherwise the element Gfmfm shall not be included.

Note:	It is recommended that the wind measuring systems should be such that peak gusts should represent a three-second average.

15.5.6	For wind speeds of 100 units or greater, the exact number of wind speed units shall be given in lieu of the two-figure code ff or fmfm. When the wind speed is 50 m s-1 (100 knots) or more (50 m s–1 or 200 km h–1), the groups ff and fmfm shall be preceded by the letter indicator P and reported as P49MPS (P99KT)P99 KT (P49 MPS or P199 KMH).

Note:	There is no aeronautical requirement to report surface wind speeds of 50 m s-1 200 km h–1 (100 kt) or more; however, provision has been made for reporting wind speeds up to 99 m s-1 399 km h–1 (199 kt) for non-aeronautical purposes, as necessary.

15.6	Groups VVVV VVVVNDV VNVNVNVNDv

Note:	The coding of visibility is based on the use of the metre and kilometre, in accordance with the units specified in ICAO Annex 5.

15.6.1	The group VVVV shall be used to report prevailing visibility. When the horizontal visibility is not the same in different directions and when the visibility is fluctuating rapidly and the prevailing visibility cannot be determined, the group VVVV shall be used to report the lowest visibility. When visibility sensors are used and they are sited in such a manner that no directional variations can be given, the abbreviation NDV shall be appended to visibility reported.

15.6.2	Directional variation in visibility VNVNVNVNDv

When the horizontal visibility is not the same in different directions and when the minimum visibility is different from the prevailing visibility, and less than 1 500 metres or less than 50% of the prevailing visibility, and less than 5000 metres, the group VNVNVNVNDv shall also be used to report the minimum visibility and, when possible, its general direction in relation to the aerodrome reference point indicated by reference to one of the eight points of the compass. If the minimum visibility is observed in more than one direction, the Dv shall represent the most operationally significant direction.

15.6.3	Visibility shall be reported using the following reporting steps:

(a)	Up to 800 metres rounded down to the nearest 50 metres;

(b)	Between 800 and 5 000 metres rounded down to the nearest 100 metres;

(c)	Between 5 000 metres up to 9 999 metres rounded down to the nearest 1 000 metres;

(d)	With 9999 indicating 10 km and above.

15.6.4	Code word CAVOK

Regulation 15.10 shall apply.

RDRDR/VRVRVRVRi

15.7	Groups	or

RDRDR/VRVRVRVRVVRVRVRVRi

Note:	The coding of runway visual range is based on the use of the metre in accordance with the unit specified in ICAO Annex 5.

15.7.1	During periods when either the horizontal visibility reported in the group VVVV or the runway visual range for one or more runways available for landing is observed to be less than 1 500 metres, one or more groups under Regulation 15.7 shall be included in the report. The letter indicator R followed immediately, without a space, by the runway designator DRDR shall always precede the RVR reports.

15.7.2	The groups shall be repeated to report runway visual range values for each runway, up to a maximum of four, which is available for landing and for which runway visual range is determined.

15.7.3	Runway designator DRDR

The designator of each runway for which runway visual range is reported shall be indicated by DRDR. Parallel runways should be distinguished by appending to DRDR letters L, C or R indicating the left, central or right parallel runway, respectively. The letter(s) shall be appended to DRDR as necessary in accordance with the standard practice for runway designation, as laid down by ICAO in Annex 14 — Aerodromes, Volume I — Aerodrome design and operations, paragraphs 5.2.2.4 and 5.2.2.5.

15.7.4	Mean value and tendency of runway visual range over the 10-minute period immediately preceding the observation VRVRVRVRi

15.7.4.1	The runway visual range values to be reported shall be representative of the touchdown zone of the active landing runway(s) up to a maximum of four.

15.7.4.2	The mean value of the runway visual range over the 10-minute period immediately preceding the observation shall be reported for VRVRVRVR. However, when the 10-minute period includes a marked discontinuity in the RVR (for example, sudden advection of fog, rapid onset or cessation of an obscuring snow shower), only data after the discontinuity shall be used for obtaining mean RVR values and variations thereof, hence the time interval in these circumstances shall be correspondingly reduced.

Notes:

(1)	See Regulation 15.7.5.

(2)	Any observed value which does not fit the reporting scale in use should be rounded down to the nearest lower step in the scale.

(3)	A marked discontinuity occurs when there is an abrupt and sustained change in runway visual range, lasting at least two minutes, consistent with the issuance of aerodrome special meteorological reports (SPECI) selected special reports given in Technical Regulation [C.3.1.] 4.3.3.

15.7.4.3	If the runway visual range values during the 10-minute period preceding the observation show a distinct upward or downward tendency such that the mean during the first five minutes varies by 100 metres or more from the mean during the second five minutes of the period, this shall be indicated by i = U for upward and i = D for downward tendency of runway visual range values. When no distinct change in runway visual range is observed, i = N shall be used. When it is not possible to determine the tendency, i shall be omitted.

15.7.5	Significant variations of runway visual range RDRDR/VRVRVRVRVVRVRVRVRi

When the RVR at a runway varies significantly and when during the 10-minute period preceding the nominal observation time the one-minute mean extreme values assessed vary from the mean value by more than 50 metres or more than 20% of the mean value, whichever is greater, the one-minute mean minimum and the one-minute mean maximum values shall be given in that order in the form RDRDR/VRVRVRVRVVRVRVRVRi instead of the 10-minute mean. Extreme RVR values shall be reported in accordance with Regulation 15.7.6 and the tendency shall be indicated in accordance with Regulation 15.7.4.3.

15.7.6	Extreme values of runway visual range

When actual RVR values are outside the measuring range of the observing system in use, the following procedure shall apply:

(a)	When the RVR, to be reported in accordance with the Technical Regulations, is greater than the maximum value which can be assessed with the system in use, the group VRVRVRVR shall be preceded by the letter indicator P (PVRVRVRVR) in which VRVRVRVR is the highest value which can be assessed. When the RVR is assessed to be more than 2 000 metres, it shall be reported as P2000;

(b)	When the RVR is below the minimum value which can be assessed with the system in use, the group VRVRVRVR shall be preceded by the letter indicator M (MVRVRVRVR) in which VRVRVRVR is the lowest value which can be assessed. When the RVR is assessed to be less than 50 metres, it shall be reported as M0050.

15.8	Group w´w´

15.8.1	One or more groups w´w´, but not more than three, shall be used to report all present weather phenomena observed at or near the aerodrome and of significance to aeronautical operations in accordance with Code table 4678. Appropriate intensity indicators and letter abbreviations (Code table 4678) shall be combined in groups of two to nine characters to indicate present weather phenomena.

15.8.2	If the observed present weather cannot be reported by use of Code table 4678, the group w´w´ shall be omitted from the report.

15.8.3	The w´w´ groups shall be ordered as follows:

(a)	First, if appropriate, the qualifier for intensity or for proximity, followed without a space by;

(b)	If appropriate, the abbreviation for the descriptor followed without a space by;

(c)	The abbreviation for the observed weather phenomenon or combinations thereof.

15.8.4	Intensity shall be indicated only with precipitation, precipitation associated with showers and/or thunderstorms, funnel cloud, duststorm or sandstorm. If the intensity of the phenomena reported in the group is either light or heavy, this shall be indicated by the appropriate sign (see Code table 4678 and specially Note (5)). No indicator shall be included in the group when the intensity of the reported phenomenon is moderate.

15.8.5	The intensity of present weather phenomena reported in the group w´w´ shall be determined by the intensity at the time of observation.

15.8.6	If more than one significant weather phenomenon is observed, separate w´w´ groups shall be included in the report in accordance with Code table 4678. However, if more than one form of precipitation is observed, the appropriate letter abbreviations shall be combined in a single group with the dominant type of precipitation being reported first. In such a single group, the intensity shall refer to the total precipitation and be reported with one or no indicator as appropriate. When an automatic observing system is used and when the type of the precipitation cannot be identified by this system, the abbreviation UP shall be used for precipitation. The abbreviation UP may be combined, as necessary, with the following characteristics of present weather: FZ, SH and TS.

15.8.7	The qualifier SH shall be used to indicate precipitation of the shower type. When associated with the indicator VC, the type and intensity of precipitation shall not be specified.

Note:	Showers are produced by convective clouds. They are characterized by their abrupt beginning and end and by the generally rapid and sometimes great variations in the intensity of the precipitation. Drops and solid particles falling in a shower are generally larger than those falling in non-showery precipitation. Between showers, openings may be observed unless stratiform clouds fill the intervals between the cumuliform clouds.

15.8.8	The qualifier TS shall be used whenever thunder is heard or lightning is detected at the aerodrome within the 10-minute period preceding the time of observation. When appropriate, TS shall be followed immediately, without a space, by relevant letter abbreviations to indicate any precipitation observed. The letter abbreviation TS on its own shall be used when thunder is heard or lightning detected at the aerodrome but no precipitation observed.

Note:	A thunderstorm shall be regarded as being at the aerodrome from the time thunder is first heard, whether or not lightning is seen or precipitation is observed at the aerodrome. A thunderstorm shall be regarded as having ceased or being no longer at the aerodrome at the time thunder is last heard, and the cessation is confirmed if thunder is not heard for 10 minutes after this time.

15.8.9	The qualifier FZ shall be used only to indicate supercooled water droplets or supercooled precipitation.

Notes:

(1)	Any fog consisting predominantly of water droplets at temperatures below 0°C shall be reported as freezing fog (FZFG) whether it is depositing rime ice or not.

(2)	Whether or not the supercooled precipitation is of the shower type shall not be specified.

15.8.10	The qualifier VC shall be used to indicate the following significant weather phenomena observed in the vicinity of the aerodrome: TS, DS, SS, FG, FC, SH, PO, BLDU, BLSA, BLSN and VA. Regulations referring to the combination of VC and FG are given in Regulation 15.8.17.

Notes:

(1)	Such weather phenomena should be reported with the qualifier VC only when observed between approximately 8 km and 16 km from the aerodrome reference point. The actual range for which the qualifier VC is to be applied will be determined locally, in consultation with aeronautical authorities.

(2)	See Regulation 15.8.7.

15.8.11	The letter abbreviation GR shall be used to report hail only when the diameter of the largest hailstones observed is 5 mm or more. The letter abbreviation GS shall be used to report small hail (diameter of the hailstones less than 5 mm) and/or snow pellets.

15.8.12	The letter abbreviation IC shall be used to indicate the phenomenon ice crystals (diamond dust). For w´w´ = IC to be reported, the visibility shall be reduced by this phenomenon to 5 000 metres or less.

15.8.13	The letter abbreviations FU, HZ, DU and SA (except DRSA) shall be used only when the obstruction to vision consists predominantly of lithometeors and the visibility is reduced by the reported phenomenon to 5 000 metres or less.

15.8.14	The letter abbreviation BR shall be used when the obstruction to vision consists of water droplets or ice crystals. For w´w´= BR to be reported, the visibility reported in the group VVVV shall be at least 1 000 metres but not more than 5 000 metres.

15.8.15	The letter abbreviation FG shall be used when the obstruction to vision consists of water droplets or ice crystals (fog or ice fog). For w´w´= FG to be reported without the qualifiers MI, BC, PR or VC, the visibility reported in the group VVVV shall be less than 1 000 metres.

15.8.16	For w´w´= MIFG to be reported, the visibility at two metres above ground level shall be 1 000 metres or more and the apparent visibility in the fog layer shall be less than 1 000 metres.

15.8.17	The letter abbreviation VCFG shall be used to report any type of fog observed in the vicinity of the aerodrome.

15.8.18	The letter abbreviation BCFG shall be used to report fog patches and the letter abbreviation PRFG to report fog covering part of the aerodrome; the apparent visibility in the fog patch or bank shall be less than 1 000 metres, the fog extending to at least two metres above ground level.

Note:	BCFG should be used only when the visibility in parts of the aerodrome is 1 000 metres or more although, when the fog is close to the observing point, the minimum visibility reported by VNVNVNVNDv will be less than 1 000 metres.

15.8.19	The letter abbreviation SQ shall be used to report squalls when a sudden increase in wind speed is observed of at least 8 m s-1 (16 knots) (32 km h–1, 8 m s–1), the speed rising to 11 m s-1 (22 knots) (44 km h–1, 11 m s–1) or more and lasting for at least one minute.

15.8.20	Regulation 15.10 shall apply.

NsNsNshshshs

or

VVhshshs

15.9	Group	or

NSC

or

NCD

15.9.1	Cloud amount and cloud height NsNsNshshshs

15.9.1.1	Cloud amount, cloud type and height of cloud base shall be reported to describe only the clouds of operational significance, i.e. clouds with the height of base below 1500 meters (5000 ft) or below the highest minimum sector altitude, whichever is greater, or cumulonimbus or towering cumulus at any height. The cloud amount NsNsNs shall be reported as few (1 to 2 oktas), scattered (3 to 4 oktas), broken (5 to 7 oktas) or overcast (8 oktas), using the three-letter abbreviations FEW, SCT, BKN and OVC followed, without a space, by the height of the base of the cloud layer (mass) hshshs. If there are no clouds below 1 500 m (5 000 ft) or below the highest minimum sector altitude, whichever is greater, no cumulonimbus and no towering cumulus and no restriction on vertical visibility, and the abbreviations CAVOK is not appropriate, then the abbreviation NSC shall be used. When an automatic observing system is used and no clouds are detected by that system, the abbreviation NCD shall be used.

15.9.1.2	The amount of each cloud layer (mass) shall be determined as if no other clouds were existing.

15.9.1.3	The cloud group shall be repeated to report different layers or masses of cloud. The number of groups shall not exceed three, except that significant convective clouds, when observed, shall always be reported.

Note:	The following clouds shall be reported as significant convective clouds:

(a)	Cumulonimbus cloud (CB);

(b)	Cumulus congestus of great vertical extent (TCU). The contraction TCU, taken from the term “towering cumulus”, is an ICAO abbreviation used in aeronautical meteorology to describe this cloud.

15.9.1.4	The selection of layers or masses of cloud to be reported shall be made in accordance with the following criteria:

1st group:	the lowest individual layer (mass) of any amount, to be 	reported as FEW, SCT, BKN or OVC;

2nd group:	the next individual layer (mass) covering more than two 	oktas, to be reported as SCT, BKN or OVC;

3rd group:	the next higher individual layer (mass) covering more than 	four oktas, to be reported as BKN or OVC;

Additional groups:	significant convective clouds (CB or TCU) when observed 	and not already reported in one of the three groups above.

The order of reporting the groups shall be from lower to higher levels.

15.9.1.5	The height of cloud base shall be reported in steps of 30 m (100 ft) up to 3 000 m (10 000 ft). Any observed value which does not fit the reporting scale in use shall be rounded down to the nearest lower step in the scale.

Note:	See Note (2) to Regulation 15.7.4.2.

15.9.1.6	When cumulonimbus clouds or towering cumulus clouds are detected by the automatic observing system and the cloud amount and the height of cloud base cannot be observed, the cloud amount and the height of cloud base should be replaced by //////.

15.9.1.7	Types of cloud other than significant convective clouds shall not be identified. Significant convective clouds, when observed, shall be identified by appending the letter abbreviations CB (cumulonimbus) or TCU (cumulus congestus of great vertical extent), as appropriate, to the cloud group without a space. When an automatic observing system is used and the cloud type cannot be observed by that system, the cloud type in each cloud group shall be replaced by ///.

Note:	When an individual layer (mass) of cloud is composed of cumulonimbus and towering cumulus clouds with a common cloud base, the type of cloud should be reported as cumulonimbus only and the amount of clouds shall be encoded as the sum of the CB and TCU amounts.

15.9.2	Vertical visibility VVhshshs

When the sky is obscured and information on vertical visibility is available, the group VVhshshs shall be reported, where hshshs is the vertical visibility in units of 30 metres (hundreds of feet). When information on vertical visibility is not available, the group shall read VV///.

Notes:

(1)	The vertical visibility is defined as the vertical visual range into an obscuring medium.

(2)	See Note (2) to Regulation 15.7.4.2.

15.9.3	Regulation 15.10 shall apply.

15.10	Code word CAVOK

The code word CAVOK shall be included in place of the groups under Regulations 15.6, 15.8 and 15.9, when the following conditions occur simultaneously at the time of observation:

(a)	Visibility reported in the group VVVV is 10 km or more and criteria for inclusion of the group VNVNVNVNDV are not met;

(b)	No cloud below 1 500 metres (5 000 ft) or below the highest minimum sector altitude, whichever is greater, and no cumulonimbus and no towering cumulus;

(c)	No significant weather phenomena (see Code table 4678).

Note:	Highest minimum sector altitude is defined in ICAO PANS–OPS, Part 1 – Definitions, as the lowest altitude which may be used under emergency conditions which will provide a minimum clearance of 300 metres (1 000 ft) above all objects located in an area contained within a sector of a circle of 46 km (25 nautical miles) radius centred on a radio aid to navigation.

15.11	Group T´T´/T´dT´d

15.11.1	The observed air temperature and dew-point temperature rounded to the nearest whole degree Celsius shall be given for T´T´/T´dT´d. Observed values involving 0.5°C shall be rounded up to the next higher Celsius degree.

15.11.2	Rounded whole degree values of air temperature and dew-point temperature of –9°C to +9°C shall be preceded by 0; for example, +9°C shall be reported as 09.

15.11.3	Temperatures below 0°C shall be immediately preceded by M, that is minus; for example, –9°C shall be reported as M09 and –0.5°C shall be reported as M00.

15.12	Group QPHPHPHPH

15.12.1	The observed QNH value rounded down to the nearest whole hectopascal shall be given for PHPHPHPH preceded, without a space, by the letter indicator Q.

15.12.2	If the value of QNH is less than 1000 hPa, it shall be preceded by 0; for example, QNH 995.6 shall be reported as Q0995.

Notes:

(1)	When the first digit following the letter indicator Q is either 0 or 1, the QNH value is reported in the unit hectopascal (hPa).

(2)	The unit prescribed by ICAO Annex 5 for pressure is the hectopascal.

15.13	Supplementary information – groups

WS RDRDR

REw´w´	or	(WTsTs/SS´ )	(RDRDR/ERCReReRBRBR)

WS ALL RWY

15.13.1	For international dissemination, the section on supplementary information shall be used only to report recent weather phenomena of operational significance, available information on wind shear in the lower layers and, subject to regional air navigation agreement, sea-surface temperature and state of the sea, and also subject to regional air navigation agreement, the state of the runway.

15.13.2	Recent weather phenomena of operational significance REw´w´

15.13.2.1	Up to three groups of information on recent weather shall be given by the indicator letters RE followed, without a space, by the appropriate abbreviations, in accordance with Regulation 15.8 (but no intensity of the recent weather phenomena shall be indicated) if the following weather phenomena were observed during the period since the last routine report, or last hour, whichever is shorter, but not at the time of observation:

— Freezing precipitation;

— Moderate or heavy drizzle, rain or snow;

— Moderate or heavy: ice pellets, hail, small hail and/or snow pellets;

— Blowing snow;

— Sandstorm or duststorm;

— Thunderstorm;

— Funnel cloud(s) (tornado or water-spout);

— Volcanic ash.

When an automatic observing system is used and when the type of the precipitation cannot be identified by this system, the abbreviation REUP shall be used for recent precipitation. It may be combined with the characteristics of the present weather in accordance with Regulation 15.8.6.

WS RDRDR

15.13.3	Wind shear in the lower layers	 or

WS ALL RWY

Information on the existence of wind shear along the take-off path or approach path between one runway level and 500 metres (1 600 ft) significant to aircraft operations shall be reported whenever available and if local circumstances so warrant, using the group set WS RDRDR repeated as necessary. If the wind shear along the take-off path or approach path is affecting all runways in the airport, WS ALL RWY shall be used.

Note: Concerning runway designator DRDR, Regulation 15.7.3 applies.

15.13.4	Supplementary information other than specified by Regulations 15.13.2 and 15.13.3 shall be added only in accordance with regional decision.

15.13.5	Sea-surface temperature and the state of the sea (WTsTs/SS´)

15.13.5.1	The sea-surface temperature shall, by regional agreement, be reported according to the regional ICAO Regulation 15.11. The state of the sea shall be reported in accordance with Code table 3700.

15.13.6	State of the runway (RDRDR/ERCReReRBRBR)

15.13.6.1	Subject to regional air navigation agreement, information on the state of the runway provided by the appropriate airport authority shall be included. The runway deposits ER, the extent of runway contamination CR, the depth of deposit eReR and the friction coefficient/braking action BRBR shall be indicated in accordance with code tables 0919, 0519, 1079 and 0366, respectively. The state of the runway group shall be replaced by the abbreviation SNOCLO when the aerodrome is closed due to extreme deposit of snow. If contaminations on a single runway or on all runways at an aerodrome have ceased to exist, this should be reported by replacing the last six digits of the group by CLRD//.

Note:	Concerning runway designator DRDR, Regulation 15.7.3 applies. Additional code figures 88 and 99 are reported in accordance with the European Air Navigation Plan, FASID, Part III-AOP, Attachment A.: The code figure 88 indicates “all runways”; the code figure 99 shall be used if a new runway state report is not available in the time for dissemination of the appropriate METAR message, in which case the previous runway state report will be repeated.

15.14	Trend forecasts

Note:	The governing criteria for issuing trend forecasts are specified in publication WMO-No. 49 – Technical Regulations [C.3.1].

15.14.1	When included in METAR or SPECI reports, the trend forecasts shall be in coded form.

15.14.2	When a change, required to be indicated in accordance with the governing criteria for significant changes, is expected for one or several of the observed elements — wind, horizontal visibility, present weather, clouds or vertical visibility — one of the following change indicators shall be used for TTTTT: BECMG or TEMPO.

Note:	Where possible, values corresponding to the local operating minima should be selected to indicate changes.

15.14.3	The time group GGgg, preceded without a space by one of the letter indicators TT = FM (from), TL (until) or AT (at), shall be used as appropriate, to indicate the beginning (FM) or the end (TL) of a forecast change, or the time (AT) at which specific forecast condition(s) is (are) expected.

15.14.4	The change indicator BECMG shall be used to describe expected changes to meteorological conditions which reach or pass specified threshold criteria at either a regular or irregular rate.

15.14.5	Changes in meteorological conditions which reach or pass specified threshold criteria for trend forecasts shall be indicated as follows:

(a)	When the change is forecast to begin and end wholly within the trend forecast period: by the change indicator BECMG followed by the letter indicators FM and TL respectively with their associated time groups, to indicate the beginning and end of the change (for example, for a trend forecast period from 1000 to 1200 UTC in the form: BECMG FM1030 TL1130);

(b)	When the change is forecast to occur from the beginning of the trend forecast period and be completed before the end of that period: by the change indicator BECMG followed only by the letter indicator TL and its associated time group (the letter indicator FM and its associated time group being omitted), to indicate the end of the change (for example: BECMG TL1100);

(c)	When the change is forecast to begin during the trend forecast period and be completed at the end of that period: by the change indicator BECMG followed only by the letter indicator FM and its associated time group (the letter indicator TL and its associated time group being omitted), to indicate the beginning of the change (for example: BECMG FM1100);

(d)	When it is possible to specify a time for the change to occur during the trend forecast period: by the change indicator BECMG followed by the letter indicator AT and its associated time group, to indicate the time of the change (for example: BECMG AT1100);

(e)	When changes are forecast to take place at midnight UTC, the time shall be indicated:

(i)	By 0000 when associated with FM and AT;

(ii)	By 2400 when associated with TL.

15.14.6	When the change is forecast to commence at the beginning of the trend forecast period and be completed by the end of that period, or when the change is forecast to occur within the trend forecast period but the time of the change is uncertain (possibly shortly after the beginning of the trend forecast period, or midway or near the end of that period), the change shall be indicated by only the change indicator BECMG (letter indicator(s) FM and TL or AT and associated time group(s) being omitted).

15.14.7	The change indicator TEMPO shall be used to describe expected temporary fluctuations to meteorological conditions which reach or pass specified threshold criteria and last for a period of less than one hour in each instance and in the aggregate cover less than half of the forecast period during which the fluctuations are expected to occur.

15.14.8	Periods of temporary fluctuations to meteorological conditions which reach or pass specified threshold criteria shall be indicated as follows:

(a)	When the period of temporary fluctuations is forecast to begin and end wholly within the trend forecast period: by the change indicator TEMPO followed by the letter indicators FM and TL respectively with their associated time groups, to indicate the beginning and end of the fluctuations (for example, for a trend forecast period from 1000 to 1200 UTC in the form: TEMPO FM1030 TL1130);

(b)	When the period of temporary fluctuations is forecast to occur from the beginning of the trend forecast period but cease before the end of that period: by the change indicator TEMPO followed only by the letter indicator TL and its associated time group (the letter indicator FM and its associated time group being omitted), to indicate the cessation of the fluctuations (for example: TEMPO TL1130);

(c)	When the period of temporary fluctuations is forecast to begin during the trend forecast period and cease by the end of that period: by the change indicator TEMPO followed only by the letter indicator FM and its associated time group (the letter indicator TL and its associated time group being omitted), to indicate the beginning of the fluctuation (for example: TEMPO FM1030).

15.14.9	When the period of temporary fluctuations to meteorological conditions is forecast to occur from the beginning of the trend forecast period and cease by the end of that period, the temporary fluctuations shall be indicated by only the change indicator TEMPO (letter indicators FM and TL and associated time groups being omitted).

15.14.10	Following the change groups TTTTT TTGGgg, only the group(s) referring to the element(s) which is (are) forecast to change significantly shall be included. However, in the case of significant changes of the clouds, all cloud groups, including any significant layer(s) or masses not expected to change, shall be given.

15.14.11	Regulation 15.5.6 shall apply.

15.14.12	Inclusion of significant forecast weather w’w’, using the appropriate abbreviations in accordance with Regulation 15.8, shall be restricted to indicate:

(1)	the onset, cessation or change in intensity of the following weather phenomena:

- Freezing precipitation;

- Moderate or heavy precipitation (including showers);

- Duststorm;

- Sandstorm;

- Thunderstorm (with precipitation)

- Other weather phenomena - given in Code table 4678 as agreed by the meteorological authority and air traffic services authority and operators concerned

(2)	the onset or cessation of the following weather phenomena:

- Freezing fog;

- Ice crystals;

- Low drifting dust, sand or snow;

- Blowing dust, sand or snow;

- Thunderstorm (without precipitation);

- Squall;

- Funnel cloud (tornado or waterspout).

15.14.13	To indicate the end of significant weather phenomena w´w´, the abbreviation NSW (Nil Significant Weather) shall replace the group w´w´.

15.14.14	When no cloud below 1 500 metres (5 000 ft) or the highest minimum sector altitude, whichever is greater, and no cumulonimbus and no towering cumulus are forecast, and CAVOK is not appropriate, the abbreviation NSC shall be used.

15.14.15	When none of the elements listed in Regulation 15.14.2 is expected to change significantly as to require a change to be indicated, this shall be indicated by the code word NOSIG. NOSIG (no significant change) shall be used to indicate meteorological conditions which do not reach or pass specified threshold criteria.

15.15	Group (RMK . . . . . . . . . . )

The indicator RMK denotes the beginning of a section containing information included by national decision which shall not be disseminated internationally.

Amend TAF as follows.

FM 51–XIV TAF Aerodrome forecast

C O D E F O R M :

TAF AMD or		NIL	 	KMH

TAF COR or	CCCC YYGGggZ	or	dddffGfmfm	or KT

TAF		Y1Y1G1G1/Y2Y2G2G2	or	or MPS

CNL

NsNsNshshshs

or VVhshshs

VVVV	w’w’	or NSC

or

CAVOK

(TXTFTF/YFYFGFGFZ	TNTFTF/YFYFGFGFZ)

PROB C2C2 or					w’w’	NsNsNshshshs

PROB C2C2 TTTTT	YYGG/YeYeGeGe		KMH	VVVV	or	or VVhshshs

or TTTTT		dddffGfmfm	or KT		NSW	or NSC

or			or MPS	or

TTYYGGgg

CAVOK

Notes:

(1)	TAF is the name of the code for an aerodrome forecast.

(2)	Owing to the variability of meteorological elements in space and time, to limitations of forecasting techniques and to limitations caused by the definitions of some of the elements, the specific value of any of the elements given in a forecast shall be understood by the recipient to be the most probable value which the element is likely to assume during the period of the forecast. Similarly, when the time of occurrence or change of an element is given in a forecast, this time shall be understood to be the most probable time.

(3)	The groups enclosed in brackets are used in accordance with regional air navigation agreements.

(4)	Aerodrome forecasts are dealt with in publication WMO-No. 49 – Technical Regulations [C.3.1].

(5)	The code words “AMD”, “CNL”, “COR” and “NIL” shall be included, as appropriate, for amended, cancelled, corrected and missing forecasts, respectively.

R E G U L A T I O N S:

51.1	General

51.1.1	The code name TAF shall be included at the beginning of each individual aerodrome forecast.

51.1.2	The group YYGGggZ, shall be included in each individual forecast to report the date and time of origin of forecast.

51.1.3	The description of forecast conditions shall contain at least information about wind, visibility, weather and cloud or vertical visibility.

51.1.4	The forecast shall cover the period Y1Y1G1G1 to Y2Y2G2G2. The forecast period may be divided into two or more self-contained parts by the use of the time indicator group TTYYGGgg in the form of FMYYGGgg. A complete description of the forecast prevailing conditions shall be given at the beginning of the forecast or the self-contained parts designated by FMYYGGgg. If any element is expected to change significantly during the forecast period or a self-contained part thereof, one or more sets of change groups TTTTT YYGG/YeYeGeGe shall be added after the complete description of the conditions prevailing before the change. Each change group shall be followed by the modified elements subject to Regulation 51.1.5.

Notes:

(1)	The governing criteria for inclusion of change groups are specified in publication WMO-No. 49 – Technical Regulations [C.3.1].

(2)	See Regulation 51.8.1.

51.1.5	The group w´w´ and/or the group NsNsNshshshs or VVhshshs shall be omitted if the corresponding element(s) is (are) expected to be absent or not significant. After change groups TTTTT YYGG/YeYeGeGe, elements shall be omitted if they are not expected to differ significantly from the preceding values they possessed in the coded forecast (see Regulations 51.5.2, 51.6.1.7 and 51.6.3). However, in case of significant change of the clouds, all cloud groups, including any significant layer(s) or masses not expected to change, shall be given.

51.2	Group CCCC

51.2.1	ICAO location indicators shall be used.

51.2.2	When the same forecast in a TAF bulletin applies to more than one aerodrome, a separate forecast shall be issued for each aerodrome concerned. Only one indicator CCCC shall prefix each coded forecast.

KMH or

51.3	Group dddffGfmfm	KT or

MPS

51.3.1	The mean direction and speed of the forecast wind shall be indicated by dddff immediately followed, without a space, by one of the letter code indicators KMH, KT or MPS, as the case may be.

Notes:

(1)	KMH, KT and MPS are the standard ICAO abbreviations for kilometres per hour, knots and metres per second, respectively.

(2)	The unit of wind speed used is determined by national decision. However, the primary unit prescribed in ICAO Annex 5 for wind speed is the metre per second (MPS)kilometre per hour (KMH), with the knot (KT) permitted for use as a non-SI alternative unit until a termination date is decided – subject to a decision which is currently under review by ICAO.

51.3.2	Regulations 15.5.2 and 15.5.4 shall apply.

51.3.3	ddd shall normally be encoded as VRB only when the mean wind speed is less than 1.5 m s-1 (3 knots) (2 m s–1 or 6 km h–1). A variable wind at higher speeds shall be indicated only when it is impossible to forecast a single wind direction.

51.3.4	When it is forecast that the maximum wind speed will exceed the mean speed by 5 m s-1 (10 knots) (5 m s–1 or 20 km h–1) or more, the maximum wind speed shall be indicated by adding Gfmfm immediately after dddff.

Note:	If after a change group the wind is reported again, Gfmfm should be included, or not, in accordance with these same criteria.

51.3.5	Regulation 15.5.6 shall apply.

51.4	Group VVVV

Note:	The coding of visibility is based on the use of the metre and kilometre, in accordance with the units specified in ICAO Annex 5.

51.4.1	When the horizontal visibility is forecast not to be the same in different directions, the prevailing visibility shall be given for VVVV. When the prevailing visibility cannot be forecast, the group VVVV shall be used to forecast the minimum visibility.

51.4.2	Regulation 51.7 shall apply.

51.4.3	Values to indicate forecast visibility shall be in conformity with those set out in Regulation 15.6.3.

w´w´

51.5	Group	or

NSW

51.5.1	Inclusion of significant forecast weather w'w', using the appropriate abbreviations in accordance with Regulation 15.8, shall be restricted to indicate:

(1)	the occurrence, cessation or change in intensity of the following weather phenomena:

– Freezing precipitation;

– Moderate or heavy precipitation (including showers);

– Duststorm;

– Sandstorm;

– Thunderstorm (with precipitation);

(2)	the occurrence or cessation of the following weather phenomena:

– Ice crystals;

– Freezing fog;

– Low drifting dust, sand or snow;

– Blowing dust, sand or snow;

– Thunderstorm (without precipitation);

– Squall;

– Funnel cloud (tornado or waterspout).

– Other weather phenomena - given in code table 4678 shall be included as agreed by the meteorological authority with the air traffic services authority and operators concerned.

51.5.2	To indicate the end of significant weather phenomena w´w´, the abbreviation NSW (Nil Significant Weather) shall replace the group w´w´.

Note: See Regulation 51.8.3.

51.5.3	Regulation 51.7 shall apply.

NsNsNshshshs

or

51.6	Group	VVhshshs

or

NSC

51.6.1	Cloud amount and cloud height NsNsNshshshs

51.6.1.1	The cloud amount NsNsNs shall be given as few (1 to 2 oktas), scattered (3 to 4 oktas), broken (5 to 7 oktas) or overcast (8 oktas), using the three-letter abbreviations FEW, SCT, BKN and OVC followed, without a space, by the height of the base of the cloud layer (mass) hshshs.

51.6.1.2	Subject to Regulation 51.6.1.4, in any cloud group, NsNsNs shall be the total amount of cloud that the forecaster expects to be at the level given by hshshs.

51.6.1.3	The cloud group shall be repeated to indicate different layers or masses of cloud forecast. The number of groups shall not exceed three, except that cumulonimbus clouds and/or towering cumulus clouds, when forecast, shall always be included.

51.6.1.4	The selection of forecast layers or masses of cloud to be included shall be made in accordance with the following criteria:

1st group:	the lowest individual layer (mass) of any amount, to be indicated as FEW, SCT, BKN or OVC;

2nd group:	the next individual layer (mass) covering more than two oktas, to be indicated as SCT, BKN or OVC;

3rd group:	the next higher individual layer (mass) covering more than four oktas, to be indicated as BKN or OVC;

Additional groups:	Cumulonimbus clouds (CB) and/or towering cumulus clouds when forecast, if not already included in one of the three groups above.

The order of inclusion of the groups shall be from lower to higher levels.

51.6.1.5	The height of the base of forecast cloud layer (mass) shall be coded in units of 30 metres (100 ft) in the form hshshs.

51.6.1.6	Types of forecast clouds other than cumulonimbus clouds and towering cumulus clouds shall not be given. Cumulonimbus clouds and towering cumulus clouds when expected shall be indicated by appending the letter abbreviations CB and TCU, respectively to the cloud group without a space. In case CB and TCU are forecast with the same height of cloud base, the cloud amount shall be the sum of the CB and TCU amounts and the cloud type given as CB.

51.6.2	Vertical visibility VVhshshs

When the sky is expected to be obscured and clouds cannot be forecast and information on vertical visibility is available, the group VVhshshs shall be used in lieu of NsNsNshshshs, where hshshs shall be the vertical visibility in units of 30 metres (hundreds of feet).

Note: See Note (1) to Regulation 15.9.2.

51.6.3	Cloud information shall be limited to cloud of operational significance, i.e. cloud below 1500 metres (5 000 ft) or below the highest minimum sector altitude, whichever is greater, and Cumulonimbus and/or towering cumulus whenever forecast. In applying this limitation, when no Cumulonimbus and no towering cumulus and no cloud below 1 500 m (5 000 ft) or below the highest minimum sector altitude, whichever is greater, are forecast, and CAVOK is not appropriate, the abbreviation NSC shall be used.

51.6.4	Regulation 51.7 shall apply.

51.7	Code word CAVOK

When it is expected that the following conditions will apply simultaneously, the code word CAVOK shall be included in place of the groups VVVV, w´w´ and NsNsNshshshs or VVhshshs:

(a)	Visibility: 10 km or more;

(b)	No cloud below 1 500 metres (5 000 ft) or below the highest minimum sector altitude, whichever is greater, and no cumulonimbus and no towering cumulus;

(c)	No significant weather phenomena (see Code table 4678).

Note: See note under Regulation 15.10.

TTTTT YYGG/YeYeGeGe

51.8	Groups	or

TTYYGGgg

51.8.1	These groups shall be used when, during the period Y1Y1G1G1 to Y2Y2G2G2, a change in some or all of the elements forecast is expected to occur at some intermediate time YYGGgg or during the period YYGG to YeYeGeGe. Such groups shall not be introduced until all the data groups necessary to describe the elements forecast in the period Y1Y1G1G1 to Y2Y2G2G2 or YYGGgg have been given.

Notes:

(1)	If the end of the forecast period is midnight, YeYe should be the date before midnight and GeGe should be indicated as 24.

(2)	See Note (1) to Regulation 51.1.4.

51.8.2	The time indicator group TTYYGGgg in the form of FMYYGGgg (from YYGGgg) shall be used to indicate the beginning of a self-contained part of the forecast indicated by YYGGgg. When the group FMYYGGgg is used, all forecast conditions given before the group FMYYGGgg are superseded by the conditions indicated after the group.

51.8.3	The change groups TTTTT YYGG/YeYeGeGe in the form of BECMG YYGG/YeYeGeGe shall indicate a change in forecast meteorological conditions expected to occur at either a regular or irregular rate at an unspecified time within the period YYGG to YeYeGeGe. The duration of the period YYGG to YeYeGeGe shall normally not exceed two hours and in any case shall not exceed four hours. The change groups shall be followed by a description of all the elements for which a change is forecast. When an element is not described in data groups which follow the change groups, the description of this element for the period between Y1Y1G1G1 and Y2Y2G2G2 shall be considered to remain valid subject to Regulation 51.1.5.

Note:	The conditions described after the groups BECMG YYGG/YeYeGeGe are those expected to prevail from YeYeGeGe until Y2Y2G2G2, unless a further change is expected, in which case a further set of change groups BECMG YYGG/YeYeGeGe or FMYYGGgg must be used.

51.8.4	The change groups TTTTT YYGG/YeYeGeGe in the form of TEMPO YYGG/YeYeGeGe shall indicate frequent or infrequent temporary fluctuations in forecast meteorological conditions which are expected to last less than one hour in each instance and, in the aggregate cover, less than half of the period indicated by YYGG/YeYeGeGe.

Notes:

(1)	If the modified forecast condition is expected to last one hour or more, Regulation 51.8.2 or 51.8.3 applies, i.e. the change groups BECMG YYGG/YeYeGeGe or FMYYGGgg must be used at the beginning and end of the period during which conditions are expected to depart from those forecast prior to YYGG or YYGGgg.

(2)	To keep forecasts clear and unambiguous, the use of change indicators should be carefully considered and kept to a minimum. In particular, the overlapping of change periods should be avoided. At any time during the period of validity of the TAF, only one possible variation in the prevailing forecast conditions should normally be indicated. The subdivision of the forecast period by FMYYGGgg should be used to avoid too complex forecasts in cases where many significant changes in weather conditions are expected to occur throughout the forecast period.

51.9	Groups PROBC2C2 YYGG/YeYeGeGe

51.9.1	In order to indicate the probability of occurrence of alternative value(s) of forecast element(s) during a defined period of time, the groups PROBC2C2 YYGG/YeYeGeGe shall be placed directly before the alternative value(s). For C2C2, only the values 30 and 40 shall be used to indicate the probabilities 30 and 40%, respectively.

Note:	A probability of less than 30% of actual values deviating from those forecast is not considered to justify the use of the group PROB. When the possibility of an alternative value is 50% or more, this should be indicated by the use of BECMG, TEMPO or FM as appropriate.

51.9.2	A probability statement may also be related to the occurrence of temporary fluctuations. In this case, the group PROBC2C2 shall be placed immediately before the change group TEMPO and the group YYGG/YeYeGeGe shall be placed after TEMPO (for example PROB30 TEMPO 2922/3001).

51.9.3	The group PROBC2C2 shall not be used in combination with the change indicator group BECMG or the time indicator group FMYYGGgg.

51.10	Group (TXTFTF/YFYFGFGFZ  TNTFTF/YFYFGFGFZ)

51.10.1	To indicate forecast maximum and minimum temperatures expected to occur at the time indicated by YFYFGFGFZ, the letter indicator TX for the maximum forecast temperature and TN for the minimum forecast temperature shall precede TFTF without a space. Up to a maximum of four temperatures shall be included, i.e. two maximum temperatures and two minimum temperatures.

51.10.2	Temperatures between –9°C and +9°C shall be preceded by 0; temperatures below 0°C shall be preceded by the letter M, that is, minus.

51.11	Amended aerodrome forecast

An amended aerodrome forecast in code form shall be identified by the use of the prefix TAF AMD in place of TAF, and it shall cover the whole remaining validity period of the original TAF.

Amend SYMBOLIC LETTERS AND REMARKS as follows.

SYMBOLIC LETTERS AND REMARKS

AS TO THE METHODS OF CODING

FsFsFs	Outgoing short-wave radiation, in joules, integrated over 24 hours.

(FM 88)

F3F3F3	Identification of originating/generating centre (Common Code table C-1 – See Attachment 1)

(FM 86, FM 87, FM 88)

F4F4F4	Identification of originating/generating sub-centre (defined by centre F3F3F3 if necessary – 	Table to be supplied to WMO Secretariat by centre)

(FM 86, FM 87, FM 88)

FFFF	Amount of radiation, in kilojoules per square metre, over a 1-hour period.

(FM 12, FM 13, FM 14)

F24F24F24F24	Amount of radiation, in joules per square centimetre, over a 24-hour period.

(FM 12, FM 13, FM 14)

f	Wind speed derived from movement of cloud elements. (Code table 1200)

(FM 85)

fe	Speed of movement of echo pattern. (Code table 1236)

(FM 20)

ff	Wind speed, in units indicated by iw.

(FM 12, FM 13, FM 14, FM 18, FM 22)

(1)	If wind speed is 99 units or more, see Regulation 12.2.2.3.3.

—	Wind speed, in kilometres per hour or knots or metres per second.

(FM 15, FM 16, FM 51)

(1)	For wind speeds of 100 units or more, see Regulations 15.5.6 or 51.3.5, as 		appropriate.

—	Wind speed, in knots.

(FM 45)

(1)	For wind speeds of 100 units or more, see Regulation 45.3.6.2.

—	Wind speed, in units indicated by iu.

(FM 63, FM 64)

fmfm	Maximum wind speed, in kilometres per hour or knots or metres per second.

(FM 15, FM 16, FM 51)

(1)	See Note (1) under ff (second specification).

fsfs	Speed, in knots, of system, front or area.

(FM 20, FM 45, FM 46)

(1)	fsfs denotes the speed of the system at the position indicated by the preceding 		group(s).

—	Speed, in knots, of tropical cyclone or other system.

(FM 85)

ftafta	Main transport speed in atmosphere, in metres per second.

(FM 22)

ftwftw	Main transport speed in water, in metres per second.

(FM 22)

Amend the Code table as follows.

4678

w′w′ Significant present and forecast weather

| QUALIFIER | WEATHER PHENOMENA |
| --- | --- |
| INTENSITY OR PROXIMITY 1 | DESCRIPTOR 2 | PRECIPITATION 3 | OBSCURATION 4 | OTHER 5 |
| – Light Moderate (no qualifier) + Heavy (well developed in the case of dust/sand whirls (dust devils) and funnel clouds) VC In the vicinity | MI Shallow BC Patches PR Partial (covering part of the aerodrome) DR Low drifting BL Blowing SH Shower(s) TS Thunderstorm FZ Freezing (supercooled) | DZ Drizzle RA Rain SN Snow SG Snow grains IC Ice crystals (diamond dust) PL Ice pellets GR Hail GS Small hail and/or snow pellets UP Unknown precipitation | BR Mist FG Fog FU Smoke VA Volcanic ash DU Widespread dust SA Sand HZ Haze | PO Dust/sand whirls (dust devils) SQ Squalls FC Funnel cloud(s) (tornado or water-spout) SS Sandstorm DS Duststorm |

The w´w´ groups shall be constructed by considering columns 1 to 5 in the table above in sequence, that is, intensity, followed by description, followed by weather phenomena. An example could be: +SHRA (heavy shower(s) of rain).

N O T E S :

(1)	Entries in this code table are based on the descriptions of hydrometeors and lithometeors found in publication WMO-No. 407 – International Cloud Atlas, Volume I (Manual on the observation of clouds and other meteors).

(2)	Regulation 15.8 shall apply.

(3)	More than one form of precipitation shall be combined, the dominant type of precipitation being reported first, for example +SNRA.

(4)	More than one phenomenon other than a precipitation combination noted shall be reported in separate w´w´ groups in the order of the columns, for example –DZ FG.

(5)	Intensity shall be indicated only with precipitation, precipitation associated with showers and/or thunderstorms, duststorm or sandstorm, and funnel clouds.

(6)	Not more than one descriptor shall be included in a w´w´ group, for example –FZDZ.

(7)	The descriptors MI, BC and PR shall be used only in combination with the letter abbreviation FG, for example MIFG.

(8)	The descriptor DR (low drifting) shall be used for dust, sand or snow raised by the wind to less than two metres above the ground. BL (blowing) shall be used to indicate dust, sand or snow raised by the wind to a height of two metres or more above the ground. The descriptors DR and BL shall be used only in combination with the letter abbreviations DU, SA and SN, for example BLSN.

(9)	When blowing snow is observed with snow falling from cloud, both phenomena are reported, e.g. SN BLSN. When due to blowing snow the observer cannot determine whether or not snow is also falling from cloud, then only BLSN shall be reported.

(10)	The descriptor SH shall be used only in combination with one or more of the letter abbreviations RA, SN, GS, GR and UP to indicate precipitation of the shower type at the time of observation, for example SHSN.

(11)	The descriptor TS, if not used on its own, shall be used only in combination with one or more of the letter abbreviations RA, SN, GS, GR and UP to indicate thunderstorm with precipitation at the aerodrome, for example TSSNGS.

(12)	The descriptor FZ shall be used only in combination with the letter abbreviations FG, DZ, RA and UP for example FZRA.

(13)	The proximity qualifier VC shall be used only in combination with the letter abbreviations TS, DS, SS, FG, FC, SH, PO, BLDU, BLSA, BLSN and VA.

(14)	UP is to be used only in reports from fully automated stations unable to distinguish precipitation type.

- ANNEX TO PARAGRAPH 4.3

It is proposed to add a new point (d) to FM 12.2.6.6.1 and to FM 12.2.6.7.1:

(d)  One hour for intermediate observations if taken every hour.

- ANNEX TO PARAGRAPH 5.1.1

- ANNEX TO PARAGRAPH 5.1.2

- ANNEX TO PARAGRAPH 5.2

# NOTES:

(1)	Aviation Codes require ICAO coordination and approval, except for AMDAR.

(2)	SAREP and RADOB require coordination by the ESCAP/WMO Typhoon Committee.

(3)	For category 5, codes need to be reviewed in order to decide whether or not they should be migrated to BUFR/CREX.

(4)	Codes in category 6 are not to be migrated.

(5)	All dates above are meant as "not later than".  However, Members and Organizations are encouraged to start experimental exchange, and, if all relevant conditions (see below) are satisfied, to start operational exchange as soon as possible.

- Start of experimental exchange means: data will be made available in BUFR (CREX) but not operationally, i.e. in addition to the current alphanumeric codes, which are still operational.

- Start of operational exchange means: data will be made available in BUFR (CREX) whereby some (but not all) Members rely on them operationally.  Still the current alphanumeric codes will be distributed (parallel distribution).

- Migration complete means: at this date the BUFR (CREX) exchange becomes the standard WMO practice.  Parallel distribution of TAC and TDCF may continue and will be discontinued step by step whenever possible with respective advance notification.

- Parallel distribution of TAC and BUFR stopped means: at this date parallel TAC and BUFR distribution is terminated. For archiving purposes and at places where BUFR (CREX) exchange still causes problems the alphanumeric codes may be used only for the exchange of data between two NMHSs.

Relevant conditions to be satisfied before experimental exchange may start:

- Corresponding BUFR/CREX-tables and templates are available;

- Training of concerned testing parties has been completed;

- Required software of testing parties (encoding, decoding, viewing) is implemented;

Relevant conditions to be satisfied before operational exchange may start:

- Corresponding BUFR/CREX-tables and templates are fully validated;

- Training of all concerned parties has been completed;

Relevant conditions to be satisfied before TAC ceasing may end:

- All required software (encoding, decoding, viewing) is operational.

- ANNEX TO PARAGRAPH 5.3

Table - Encoder/decoder available for migration to TDCF

| BUFR SOFTWARE | APPLICABILITY (OS) | LANGUAGE | SOURCE CODE | AVAILABILITY | SUPPORT |
| --- | --- | --- | --- | --- | --- |
| ECMWF (DECODING/ ENCODING) | UNIX, LINUX, Windows with GIGWIN emulator | FORTRAN | YES | INTERNET, FREE DOWNLOAD, DOCUMENTATION ON LINE http://www.ecmwf.int/products/data/software/ (also CREX/GRIB 1/GRIB 2) | ECMWF WILL ANSWER LIMITED QUERIES BY EMAIL ECMWF WILL UPDATE TABLES AND MAKE NEW VERSION FOR NEW EDITION |
| NCEP, USA (DECODING/ ENCODING) | UNIX, LINUX | FORTRAN, C | YES | INTERNET, FREE DOWNLOAD, DOCUMENTATION ON LINE http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/ http://www.nco.ncep.noaa.gov/pmb/codes/GRIB2/ | LIMITED FREE TECHNICAL SUPPORT (VIA TELEPHONE, E-MAIL, ETC.) ONLINE REFERENCE GUIDE AT URL IN THE LEFT COLUMN (BUFR) IN-LINE COMMENTS (GRIB2) |
| DWD, GERMANY (DECODING/ ENCODING) | UNIX, WINDOWS | C | NO | AT REQUEST, AT COST (FROM 100 $ TO 2500$) www.ebp.de | DWD WILL ANSWER LIMITED QUERIES BY EMAIL DWD WILL UPDATE TABLES AND MAKE NEW VERSION FOR NEW EDITION AND NEW OS VERSION |
| BUFR-World (DWD) (DECODING/ ENCODING/ GUI) | WINDOWS, UNIX, LINUX, SOLARIS, … | JAVA | NO | AT REQUEST, AT COST | LIMITED SUPPORT |
| UKMO, UK (DECODING/ ENCODING) | UNIX | FORTRAN? | ? | AT REQUEST FREE | NO SUPPORT, NOR FOLLOW UP |
| INPE, BRAZIL | WINDOWS/UNIX | FORTRAN | YES | FREE DOWNLOAD "MBUFRTOOLS" under "decoding/encoding" at http://downloads.cptec.inpe.br/publicacoes/distribuicao.jsp | LIMITED SUPPORT |
| MSC, CANADA ENCODING/DECODING | Unix/Linux, Cygwin (GNU development tools) | C | YES | Free (LGPL license) http://launchpad.net /libecbufr | LIMITED SUPPORT. SOFTWARE UPDATES, BUG REPORTS/FIXES AND TABLES AVAILABLE ON DOWNLOAD SITE |

- ANNEX TO PARAGRAPH 6.2

PROCEDURES FOR AMENDING THE MANUAL ON CODES

Note:  Meanings of marks below are as follows.

Text --- No changes

Text --- Addition or modification

Text --- Deletion or modification

Text --- Move from other article

Text --- Move to other article

1.	General validation and implementation procedures

1.1	Proposal of amendments

Amendments to the Manual on Codes must be proposed in writing to the WMO Secretariat. The proposal shall specify the needs, purposes and requirements and include information on a contact point for technical matters.

1.2	Drafting recommendation

The Inter-Programme Expert Team on Data Representation and Codes (IPET-DRC)1, supported by the Secretariat, shall validate the stated requirements (unless it is consequential to an amendment to the WMO Technical Regulations) and develop a draft recommendation to respond to the requirements, as appropriate.

1.3	Date of implementation

A draft recommendation of the ET-DRC must be validated. A draft recommendation of the ET-DRC must be endorsed by the Implementation/Coordination Team on Information Systems and Services (ICT-ISS) of the Open Programme Area Group on Information Systems and Services (OPAG-ISS). The IPET-DRC should define a date of implementation in order to give sufficient time to the WMO Members to implement the amendments after the date of notification; the IPET-DRC should document the reasons to propose a time span of less than six months except for the fast track procedure.

1.4	Procedures for approval

After a draft recommendation of the IPET-DRC is validated in accordance with the procedure given in section 6 below, depending on the type of amendments, the IPET-DRC may select one of the following procedures for the approval of the amendments:

•	Fast-track procedure (see section 2 below);

•	Procedure for the adoption of amendments between CBS sessions (see section 3 	below);

•	Procedure for the adoption of amendments during CBS sessions (see section 4 	below).

1.5	Urgent introduction

Regardless of above procedures, as an exceptional measure, the following procedure accommodates urgent user needs to introduce new entries in BUFR/CREX tables A, B and D, code and flag tables of BUFR, CREX and GRIB edition 2 and Common Code tables.

(a)	A draft recommendation developed by IPET-DRC shall be validated according to 6.1, 6.2 and 	6.3 below.

(b)	The draft recommendation for pre-operational use, which can be used in operational data 	and products, shall be approved by the chairpersons of IPET-DRC and OPAG-ISS, and the 	president of CBS. The list of pre-operational entries is kept on-line on 	the WMO web server;

(c)	Pre-operational entries need to be approved by one of the procedures in 1.4 for 	operational use.

1.6	Version number

The version number of the master table will be incremented.

1.7	Issuing updated version

Once amendments to the Manual on Codes are adopted, an updated version of the relevant part of the Manual shall be issued in the four languages: English, French, Russian and Spanish. The Secretariat will inform all WMO Members of the availability of a new updated version of that part at the date of notification mentioned in 1.3.

2.	Fast-track procedure

2.1	Scope

The fast-track procedure can be used for additions to BUFR or CREX Tables A, B, and D with associated code tables or flag tables, to code or flag tables or templates in GRIB and to common tables C.

2.2	Endorsement

An ET-DRC draft recommendation must be validated in accordance with the procedures given in section 6 below. Draft recommendations developed by the IPET-DRC, including a date of implementation of the amendments, must be endorsed by the chairperson of OPAG-ISS.

The filling of reserved and unused entries in the existing code and flag tables is considered as minor adjustments, and will be done by the Secretary-General in consultation with the president of CBS. For other types of amendments, the English version of the draft recommendation, including a date of implementation, should be distributed to the focal points for codes and data representation matters for comments, with a deadline of two months for the reply. It should then be submitted to the president of CBS for adoption on behalf of the Executive Council (EC).

2.3	Approval

2.3.1	Minor adjustments

The filling of reserved and unused entries in the existing code and flag tables, and Common Code tables is considered as minor adjustments, and will be done by the Secretary-General in consultation with the president of CBS.

2.3.2	Other types of amendments

For other types of amendments, the English version of the draft recommendation, including a date of implementation, should be distributed to the focal points for codes and data representation matters for comments, with a deadline of two months for the reply. It should then be submitted to the president of CBS for adoption on behalf of the Executive Council (EC).

2.4	Frequency

The implementation of amendments approved through the fast track procedure can be twice shall normally be limited to one per a year in May and November. If the Chair/co-Chair of ET-DRC and OPAG-ISS agree that an exceptional situation exists, a second fast track implementation can be initiated.

| IPET-DRC |  | chairperson of OPAG-ISS |  | president of CBS |  |  |
| --- | --- | --- | --- | --- | --- | --- |

or

| IPET-DRC |  | chairperson of OPAG-ISS |  | Focal points for code and data representation matters |  | president of CBS |
| --- | --- | --- | --- | --- | --- | --- |

Figure 1 - Adoption of amendments by fast track procedure

3.	Procedures for the adoption of amendments between CBS sessions

3.1	Approval of draft recommendation

For the direct adoption of amendments between CBS sessions, as a first step, the ET-DRC submits its draft recommendation developed by the IPET-DRC, including a date of implementation of the amendments, shall be submitted to the chairperson of OPAG-ISS and president and vice-president of CBS for approval. In a second step, upon approval of the president of CBS, the Secretariat sends the recommendation in the four languages (English, French, Russian and Spanish), including a date of implementation of the amendments, to all WMO Members for comments to be submitted within two months; WMO Members are invited to designate a focal point responsible to discuss any comments/disagreements with the ET-DRC. If the discussion between the ET-DRC and the focal point cannot result in an agreement on a specific amendment by a WMO Member, this amendment will be reconsidered by the ET DRC. Those WMO Members not having replied within the two months following the dispatch of the amendments are implicitly considered as having agreed with the amendments. In a third step, once amendments are agreed by WMO Members, and after consultation with the Chair and co-Chair of the OPAG-ISS and the president and vice-president of CBS, the Secretariat notifies at the same time the WMO Members and the members of the Executive Council of the approved amendments and of the date of their implementation.

3.2	Circulation to Members

In a second step, uUpon approval of the president of CBS, the Secretariat sends the recommendation in the four languages (English, French, Russian and Spanish), including a date of implementation of the amendments, to all WMO Members for comments to be submitted within two months following the dispatch of the amendments.

3.3	Agreement

Those WMO Members not having replied within the two months following the dispatch of the amendments are implicitly considered as having agreed with the amendments.

3.4	Coordination

WMO Members are invited to designate a focal point responsible to discuss any comments/disagreements with the IPET-DRC. If the discussion between the IPET-DRC and the focal point cannot result in an agreement on a specific amendment by a WMO Member, this amendment will be reconsidered by the IPET-DRC.

3.5	Notification

In a third step, oOnce amendments are agreed by WMO Members, and after consultation with the chairperson of the OPAG-ISS and the president and vice-president of CBS, the Secretariat notifies at the same time the WMO Members and the members of the Executive Council of the approved amendments and of the date of their implementation.

| IPET-DRC |  | chairperson of OPAG-ISS and president/vice-president of CBS |  | Agreed by WMO Members |  | WMO Members and EC informed |
| --- | --- | --- | --- | --- | --- | --- |

Figure 2 - Adoption of amendments between CBS sessions

4.	Procedures for the adoption of amendments during CBS sessions

For the adoption of amendments during CBS sessions, the IPET-DRC submits its recommendation, including a date of implementation of the amendments, to the Implementation/Coordination Team on Information Systems and Services (ICT-ISS) of the Open Programme Area Group on Information Systems and Services (OPAG-ISS) ICT-ISS. The recommendation is then submitted to a CBS session and then to an EC session.

5.	Procedures for the correction of existing entries in the BUFR and CREX tables

5.1	Introducing a new descriptor

If an erroneous specification of an entry is found in an operational BUFR or CREX Eelement descriptor or Ssequence descriptor, a new descriptor should preferably be added to the appropriate table through the fast-track procedure or the procedure for adoption of amendments between CBS sessions. The new descriptor should be used instead of the old one for encoding (especially if it concerns data width). An appropriate explanation shall be added to the notes of the table to clarify the practice along with the date of the change. This situation is considered a minor adjustment according to 2.22.3.1 above.

5.2	Correcting erroneous specification

As an exceptional measure for erroneous entries in Table B, if it is found absolutely necessary to correct an erroneous specification of an existing entry by changing its specification, the following rules shall apply:

5.2.1	The name and unit of an element descriptor shall remain unchanged except for minor 	clarifications.

5.2.2	Scale, reference value and bit width may be corrected to required values.

5.2.3	Such a change will be submitted through the fast-track procedure.

5.2.4	The version number of the master will be incremented.

| IPET-DRC |  | Meeting of ICT-ISS |  | CBS sessions |  | EC sessions |
| --- | --- | --- | --- | --- | --- | --- |

Figure 3 - Adoption of amendments during CBS sessions

6.	Validation procedures

6.1	Documentation of need and purpose

The need for, and the purpose of, the proposal for changes should be documented.

6.2	Documentation of result

This documentation must include the results of validation testing of the proposal as described below.

6.3	Testing with encoder/decoder

For new or modified WMO code and data representation forms, proposed changes should be tested by the use of at least two independently developed encoders and two independently developed decoders which incorporated the proposed change. Where the data originated from a necessarily unique source (for example, the data stream from an experimental satellite), the successful testing of a single encoder with at least two independent decoders would be considered adequate. Results should be made available to the IPET-DRC with a view to verifying the technical specifications.

7.	Urgent introduction of new descriptors or entries in BUFR, CREX and GRIB 	edition 2 tables

As agreed by CBS (see the Abridged Final Report with Resolutions and Recommendations of the Extraordinary Session (2002) of the Commission for Basic Systems (WMO-No. 955), 6.2.66 of the general summary), a three-step mechanism for the introduction of new descriptors or entries in BUFR, CREX and GRIB edition 2 tables accommodates urgent user needs, as follows:

(a) Approval (by the chairperson of ET-DRC, the chairperson of OPAG-ISS and the president of CBS) of allocated entries after an expression of requirements. The list of allocated entries awaiting validation is kept on-line on the WMO web server;

(b) After validation (according to 6.1, 6.2 and 6.3 above), declaration of pre-operational use (after approval by the chairperson of ET-DRC, the chairperson of OPAG-ISS and the president of CBS). The list of pre-operational entries is kept on-line on the WMO web server;

(c) Finally, adoption of the amendments in accordance with the procedures detailed in sections 2, 3 or 4 above.

# Footnotes

See http://www.wmo.int/pages/prog/www/ois/Operational_Information/VolC1.html

Reference : Manual on the GTS – Attachment I-5 – Plan for monitoring the operation of the GTS – paragraphs 5 and 6, and Table A

By “canonical” it is meant to imply a standard XML, repeatable across implementations, which contains all the information available in the BUFR bulletin.

Reference: see paragraphs 53 and 54 of the WIGOS standardization framework for data and associated metadata” (see IPET-MDI-I/Doc. 4.2(1)).