| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 2.1 (2) (8. V. 2012) ------------------------- ITEM 2.1 ENGLISH ONLY |
| --- | --- | --- |

Modification of the format of the GRIB templates tables

Submitted by Enrico Fucile (ECMWF)

_______________________________________________________________________

Summary and Purpose of Document

The current format of the GRIB templates tables is not suitable for the automatic use in decoding software. A new format is proposed. The introduction of size, type and name of the element is proposed.

_______________________________________________________________________

ACTION PROPOSED

The Team is invited to consider the proposed change and implement it in the next release of electronic tables.

REFERENCES:

DISCUSSIONS

The current format of the GRIB templates tables is made of two columns: octet number and contents. This format is clear in most of the cases, as it gives the meaning of each octet of the message, but is not suitable to implement the automatic update of decoding software from the electronic format of the tables for two reasons.

- Presence of repetitions.

In several templates the concept of repetition of a group of elements is used without mentioning it explicitly. One example is the repetition of the group of elements describing the time statistical process in all the templates concerning products with a time statistics in a continuous or non continuous interval. As an example the time statistics part of product definition template 4.8 is reported below

Octet No.	Contents

42		n - number of time range specifications describing the time intervals used to calculate the 
		statistically processed field

43-46	Total number of data values missing in statistical process

47-58   Specification of the outermost (or only) time range over which statistical 
			processing is done

47	Statistical process used to calculate the processed field from the field at each time incre-
		ment during the time range (see Code table 4.10)

48	Type of time increment between successive fields used in the statistical processing (see 
		Code table 4.11)

49	Indicator of unit of time for time range over which statistical processing is done (see Code 
		table 4.4)

50-53	Length of the time range over which statistical processing is done, in units defined by the 
		previous octet

54	Indicator of unit of time for the increment between the successive fields used (see Code 
		table 4.4)

55-58	Time increment between successive fields, in units defined by the previous octet (see Notes 3 
		and 4)

59-nn   These octets are included only if n > 1, where nn = 46 + 12 x n

59-70	As octets 47 to 58, next innermost step of processing

71-nn	Additional time range specifications, included in accordance with the value of n. Contents 
		as octets 47 to 58, repeated as necessary

In this table format the repetition of the elements defined in the octets 47 to 58 for a number of times given by octet 42 is not expressed in a formatted way that can be interpreted by an automatic script. Therefore the automatic processing of that sequence of octets is not possible and this is making the electronic format of the GRIB templates not usable for the purpose for which it has been produced.

This problem can be solved by the introduction of three new columns in the table format: size, type and name.

- The name is introduced to be able to reference uniquely the element through the template.

- The type is introduced to include the information that a particular entry is expressing the number of repetitions (repetition_number type), to mark the start of the repetition sequence (repetition type) and to link the sequence to the repetition number through it’s name (repetition(n)).

- The size is introduced to express the number of elements to be repeated for type repetition and the number of octets for the other types.

The same octet sequence in the new table format is reported below.

Octet No.	Size 	Type 	Name	Contents

42	1	repetition_ number	n	n - number of time range specifications describing the

time intervals used to calculate the statistically

processed  field

43-46	4	unsigned		Total number of data values missing in statistical

process

47  	6	repetition(n)		Time statistical processing

47	1	code_ table		Statistical process used to calculate the processed field

from the field at each time increment during the time

range (see Code table 4.10)

48	1	code_ table		Type of time increment between successive fields used

in the statistical processing (see code table 4.11)

49	1	code_ table		Indicator of unit of time for time range over which

statistical processing is done (see Code table 4.4)

50-53	4	unsigned		Length of the time range over which statistical

processing is done, in units defined by the previous

octet

54	1	code_ table		Indicator of unit of time for the increment between the

successive fields used (see Code table 4.4)

55-58	4	unsigned		Time increment between successive fields, in units

defined by the previous octet (see Notes 3 and 4)

- Element type and size is not expressed.

Another problem affecting the current format of the tables is that the type of each element is not expressed in the table itself and therefore it is impossible without this information to build the necessary decoding rules only from the electronic format of the template tables. This has been source of ambiguity in the past as the signedness of the elements is not always clear. As suggested above the introduction of a new column “type” with the possible values: signed, unsigned, ieee_float, char, code, repetition and repetition_number, will solve the problem and eliminate any ambiguity.

The information regarding the number of octets occupied by each element could be extracted in most of the cases from the octet number. However in some cases the presence of variables in the expression of the octet number is making difficult and very error prone the process of extracting the size. Therefore it is suggested to add explicitly a size column indicating the number of elements to be repeated for the repetition type and the number of octets for all the other types.

PROPOSAL

To address the problems expressed above it is proposed to add to the template tables the following columns:

- Name. Expressing the name of the element to be used in subsequent references to it in the same template. The name does not need to be unique across all the set of templates and sections, but it must be unique within the template in which it is defined.

- Type. Expressing the type of the element with the following options:

  - signed: the element is a signed integer as defined in regulation 92.1.5

  - unsigned: is an positive integer for which there isn’t any bit dedicated to the sign

  - ieee: floating point ieee format defined in note (20) of the GRIB format description

  - code_table: unsigned associated to a code table

  - repetition_number: number of repetitions in a repetition sequence expressed as unsigned

  - repetition(N): marking the start of the repetition sequence with repetition_number N

  - byte: a specific format to be processed bit by bit as for the bit map or for the data section

- Size. Expressing the number of elements to be repeated for a repetition type and the number of octets for all the other types.