| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 2.1 (4) (9. V. 2012) ------------------------- ITEM 2.1 ENGLISH ONLY |
| --- | --- | --- |

GRIB Calendar Identification

Submitted by Richard Weedon (UKMO)

Extended by an additional template by Luis Kornblueh (MPIM) /Sibylle Krebber (DWD)

_______________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for changes to GRIB2 to allow for the identification of Calendar Types in Section 1.

_______________________________________________________________________

ACTION PROPOSED

The meeting is invited to review the validation evidence and pass the proposal for pre-operational status.

REFERENCES:

- Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

- Final report of the third meeting of the Inter-Programme Expert Team on Data Representation and Codes, Australia, Melbourne, 20 - 23 September 2011

- Doc. 2.1 (1) of IPET-DRC-IV, GRIB Calendar Identification, submitted by Richard Weedon (UKMO)

BACKGROUND AND DISCUSSION

Following discussion with the IPET-DRC subgroup regarding calendar identification in GRIB2, The Met Office proposes the following extension GRIB2 to allow the optional use of templates in Section 1, with thanks to Enrico Fucile for the concept.

We include a template for paleontological offset, based on a previous DWD proposal.

Changes appear in red.

The original proposal is extended by an additional template for Calendar definition and paleontological offset needed at MPIM. Additions appear in green.

PROPOSAL

Changes to Regulations:

92.3.3 	Octets beyond 21 are for an Identification Template and need not be present.

92.3.4 	Calendar is assumed to be Gregorian unless otherwise stated in an Identification Template.

Changes to Section 1 Specification:

Section 1 – Identification section

Octet No. 	Contents

1–4 		Length of section in octets (21 or nn)

5 		Number of section (1)

6–7 		Identification of originating/generating centre (see Common Code table C-11)

8–9 		Identification of originating/generating subcentre

(allocated by originating/generating centre)

10 		GRIB Master tables version number (see Code table 1.0 and Note 1)

11 		Version number of GRIB Local tables used to augment Master tables

(see Code table 1.1 and Note 2)

12 		Significance of reference time (see Code table 1.2)

13–14 		Year (4 digits)

15 		Month

16 		Day

17 		Hour

18 		Minute

19 		Second

20 		Production status of processed data in this GRIB message (see Code table 1.3)

21 		Type of processed data in this GRIB message (see Code table 1.4)

22–23 		Identification Template Number (optional, see Code table 1.5)

24–nn 		Identification Template (optional, see Template 1.X, where X is the

identification template number given in octets 22–23)

Notes:

(1) 	Local tables shall define those parts of the Master table which are reserved for local use

except for the case described below. In any case, the use of Local tables in messages

intended for non-local or international exchange is strongly discouraged.

(2) 	If octet 10 contains 255 then only Local tables are in use, the Local table version number

(octet 11) must not be zero nor missing, and Local tables may include entries from the

entire range of the tables.

(3) 	If octet 11 is zero, octet 10 must contain a valid Master table version number and only those parts of the tables not reserved for local use may be used.

New Code Tables:

| Code table 1.5 - Identification Template Number |
| --- |
| Octet No. | Contents |
| 0 | Calendar Definition |
| 1 | Paleontological Offset |
| 2 | Calendar definition and paleontological offset |
| 3-32767 | Reserved |
| 32768-65534 | Reserved for local use |
| 65535 | Missing |

| Code table 1.6 - Type of Calendar |
| --- |
| Octet No. | Contents |
| 0 | Gregorian |
| 1 | 360-day |
| 255 | Missing (assume Gregorian) |

New Identification Definition Templates

| Identification Template 1.0 - Calendar Definition |
| --- |
| Octet No. | Contents |
| 24 | Type of calendar (See Code Table 1.6) |

| Identification Template 1.1 - Paleontological Offset |
| --- |
| Octet No. | Contents |
| 24-25 | Number of tens of thousands of years of offset |

| Identification Template 1.2 - Calendar definition and paleontological offset |
| --- |
| Octet No. | Contents |
| 24 | Type of calendar (See Code Table 1.6) |
| 25-26 | Number of tens of thousands of years of offset |