| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 2.2 (1) ( 19. IV. 2012) ------------------------- ITEM 2.2 ENGLISH ONLY |
| --- | --- | --- |

Additions and modifications of templates and tables

Transverse Mercator GRIB2 Template

# Submitted by Richard Weedon (UKMO)

_______________________________________________________________________

# Summary and Purpose of Document

The document contains a proposal for a new GRIB2 template for Transverse Mercator Projections

_______________________________________________________________________

# ACTION PROPOSED

The meeting is invited to discuss the validation of this proposal and pass for    pre-operational implementation

# REFERENCES:

# Background

This proposal was originally submitted at the ET-DRC 2011 (Melbourne)  which agreed to grant validation status. During the course of validation process a number of minor changes have been made –

‘IEEE 32-bit floating-point values’  added to Octets 48 – 51

The units of octets 61 - 84 have been changed to 10-2 m

The entry for code table 3.2 entry has been amended to read:

Earth represented by the OSGB 1936 Datum, using

- the Airy_1830 Spheroid (semi-major axis = 6377563.396m,  f = 1/299.3249646),

- the Greenwich meridian as 0 Longitude,

- the Newlyn datum as mean sea level, 0 height.

Discussion

The United Kingdom Met Office use the Ordnance Survey of Great Britain’s coordinate

reference system (OSGB) for model output and observational data in a number of systems. This

coordinate reference system is a specific implementation of a Transverse Mercator projection.

To encode certain data outputs for transmission as GRIB2 messages, a new GRIB2 grid

definition template is proposed.

# Proposal

A new GRIB2 grid definition template, capable of defining the OSGB coordinate reference

system.

Grid definition template 3.12 Transverse Mercator

Octet No.        Contents

| 15 | Shape of the Earth (see Code table 3.2) |
| --- | --- |
| 16 | Scale factor of radius of spherical Earth |
| 17 – 20 | Scaled value of radius of spherical Earth |
| 21 | Scale factor of major axis of oblate spheroid Earth |
| 22 – 25 | Scaled value of major axis of oblate spheroid Earth |
| 26 | Scale factor of minor axis of oblate spheroid Earth |
| 27 – 30 | Scaled value of minor axis of oblate spheroid Earth |
| 31 – 34 | Ni number of points along i-axis |
| 35 – 38 | Nj number of points along j-axis |
| 39 – 42 | LaR geographic latitude of reference point |
| 43 – 46 | LoR geographic longitude of reference point |
| 47 | Resolution and component flags (see Flag table 3.3) |
| 48 - 51 | m scale factor at reference point ratio of distance on map to distance on spheroid (IEEE 32-bit floating-point values) |
| 52 – 55 | XR false easting, i-direction coordinate of reference point [Note: units in 10-2 m] |
| 56 – 59 | YR false northing, j-direction coordinate of reference point, [Note: units in 10-2 m] |
| 60 | Scanning mode (flags see Flag table 3.4) |
| 61 – 64 | Di i-direction increment length, [Note: units in 10-2 m] |
| 65 – 68 | Dj j-direction increment length [Note: units in 10-2 m] |
| 69 – 72 | x1 i-direction coordinate of the first grid point [Note: units in 10-2 m] |
| 73 – 76 | y1 j-direction coordinate of the first grid point [Note: units in 10-2 m] |
| 77 – 80 | x2 i-direction coordinate of the last grid point [Note: units in 10-2 m] |
| 81 – 84 | y2 j-direction coordinate of the last grid point [Note: units in 10-2 m] |