| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 2.2 (7) ( 10.V.2012) ------------------------- ITEM 2.2 ENGLISH ONLY |
| --- | --- | --- |

Generalized vertical height coordinate in GRIB Edition 2

- Revised proposal -

Submitted by Luis Kornblueh (MPI for Meteorology), Sibylle Krebber (DWD)

_______________________________________________________________________

Summary and Purpose of Document

The document contains a revised proposed addition of a new vertical coordinate type to define a general vertical height coordinate without knowing the defining algorithms.

_______________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the contents for pre-operational

REFERENCES:

- Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

- Schättler, U., DWD, 2010 (internal paper): Vertical Coordinate Parameters in the COSMO Model and GRIB. Available from 
http://www.cosmo-model.org/content/model/modules/default.htm

- Schär, C., D. Leuenberger, O. Fuhrer, D. Lüthi and C. Girard, 2002: A new terrain-following vertical coordinate formulation for atmospheric prediction models. Mon. Wea. Rev., 130, pp. 2459-2480.

- Final report of the second meeting of the Inter-Programme Expert Team on Data Representation and Codes, Brasilia, Brazil, 31 August – 3 September 2010,
2.3.9 Generalized vertical height coordinate in GRIB Edition 2.

DISCUSSIONS

In 2010 a new entry in Code table 4.5 for a generalized vertical height coordinate was proposed (IPET-DRC-II/Doc. 2.3(9)). The proposal was approved for validation.

During the validation process additional entries were proposed. Whereas the proposed optional local entries were withdrawn.

An Universal Unique Identifier UUID has been introduced, because it cannot be assured that the centre and local identifier are sufficiently accessible and are maintained properly in the context of climate modelling usage.

UUIDs are documented as part of ISO/IEC 11578:1996 "Information technology – Open Systems Interconnection – Remote Procedure Call (RPC)" and more recently in ITU-T Rec. X.667 | ISO/IEC 9834-8:2005. The IETF has published Standards Track RFC 4122 that is technically equivalent with ITU-T Rec. X.667 | ISO/IEC 9834-8.

This will assure that a given GRIB message is generated using the associated vertical grid GRIB message with the same UUID.

A UUID is a 16-byte (128-bit) number. In its canonical form, a UUID is represented by 32  hexadecimal digits, displayed in five groups separated by hyphens, in the form 8-4-4-4-12 for a total of 36 characters (32 digits and four hyphens).

REVISED PROPOSAL

- New entry for the generalized vertical height coordinate in Code Tables 4.5 (Fixed surface types and units) with explaining comments.

| Code table 4.5 - Fixed surface types and units |
| --- |
| Octet No. | Contents |
| 120-149 | Reserved |
| 150 | Generalized vertical height coordinate (x+1) |
| 151-159 | Reserved |

Notes:

(x+1)	The definition of a generalized vertical height coordinate implies the absence of coordinate values in Section 4 but the presence of an external 3D-GRIB message that specifies the height of every model grid point in metres (see Notes for Section 4), i.e. this GRIB message will contain the field with discipline = 0, category = 3, parameter = 6 (Geometric height).

- Additions to Section 4 of the GRIB Edition 2 Regulations including an additional note to specify the interpretation of the numbers in the “Optional list of coordinate values” for new vertical coordinate type.

Proposed changes to the Manual on Codes (GRIB Edition 2 regulations)

| Section 4 – Product definition section |
| --- |
| Octet No. | Contents |
| 1–4 | Length of section in octets (nn) |
| 5 | Number of section (4) |
| 6–7 | Number of coordinate values after template or number of information according to 3D vertical coordinate GRIB2 message (see Note 1 and 5) |
| 8–9 | Product definition template number (see Code table 4.0) |
| 10–xx | Product definition template (see Template 4.X, where X is the product definition template number given in octets 8–9) |
| [xx+1]–nn | Optional list of coordinate values or vertical grid information (see Notes 2, 3, 4 and 5) |

Notes:

- Coordinate values are intended to document the vertical discretization associated with model data on hybrid coordinate vertical levels. A number of zero in octets 6–7 indicates that no such values are present. Otherwise the number corresponds to the whole set of values.

- Hybrid systems, in this context, employ a means of representing vertical coordinates in terms of a mathematical combination of pressure and sigma coordinates. When used in conjunction with a surface pressure field and an appropriate mathematical expression, the vertical coordinate parameters may be used to interpret the hybrid vertical coordinate.

- Hybrid coordinate values, if present, should be encoded in IEEE 32-bit floating point format. They are intended to be encoded as pairs.

- Two distinct pressure-based hybrid coordinate formulations can be expressed in GRIB Edition 2. If the hybrid coordinate being used is based on pressure, then level type 105 (Code Table 4.5) shall be used to specify the vertical level type.  If the formulation is based on the natural logarithm of pressure then level type 113 (Code Table 4.5) shall be used. In both cases notes 1-3 (above) apply fully.

- In case of generalized vertical height coordinate (fixed surface type 150), no pairs of coordinate values follow after template, but 6 additional information (each 4 octets long and encoded in IEEE 32-bit floating point format), starting with the number of vertical levels and the identification number of the used vertical system in the additional GRIB2 message with the 3D vertical system. This identification number together with an UUID (Universally Unique IDentifier) in 4 parts allows an unique identification of the grid.

[xx+1]		-  [xx+4]		Number of vertical levels

[xx+5]		-  [xx+8]		Identification number of 3D vertical grid GRIB2 message

(defined by originating centre)

[xx+9]		-  [xx+12]	UUID part 1 of 4

[xx+13]	-  [xx+16]	UUID part 2 of 4

[xx+17]	-  [xx+20]	UUID part 3 of 4

[xx+21]	-  [xx+24]	UUID part 4 of 4

- Addition of a brief exposition in the Guide to GRIB Edition 2.

Proposed Changes and Additions to the “Guide to GRIB2”

The Guide to GRIB2 should be updated (Chapter 3.2, page 73ff) as follows:

- complete all definitions concerning TABLE 4.5 and Section 4

- distinguish between pressure and height based vertical coordinate

- add example for use of “generalized height coordinate”

Description of pressure based coordinate system

(…)

The hybrid pressure based coordinate system has been introduced in numerical models to have both sigma-type levels near the earth and pressure levels at the top of the atmosphere. The above formula is generalized as follows:

Ph = ah  Psfc  +  bh

Hybrid vertical coordinate values, when present, are encoded as the pair of numbers ah and bh in IEEE 32-bit floating point format.  Each pair represents a hybrid vertical coordinate level. With the surface pressure field Psfc, the values of Ph can be calculated from the above formula.  Note that this implies the surface pressure field accompanies data on hybrid vertical coordinates.  The capability of GRIB2 to encode multiple data sets in a single message makes this straightforward to accomplish.

(……)

Add description of height based coordinate system

(……)

Add description of generalized height coordinate system

If the defining algorithms for the vertical grid are too complicated, the 3D vertical grid will be provided as a GRIB2 message by using the “generalized vertical height coordinate” (TABLE 4.5: 150). To illustrate the usage, see the following example (only section 4) for a temperature field including the 3D vertical grid GRIB2 message.

Example for usage of the “generalized vertical coordinate” system:

Temperature field  of layer 13/14 has following section 4

1-4			 104-107		38	This Section is 38 octets long

5			 108		4	This is Section 4

6-7			109-110		6	6 numbers with vertical grid information follow

after the template

8-9			111-112		0	The Product Definition Template Number is 4.0 – an 						analysis or forecast at a horizontal level or in a horizontal 					layer at a point in time

10			113		0	The parameter category is 0 – temperature  products

11			114		0	The parameter number is 0  - temperature (in K)

12			115		2	A forecast generated this product (the generating process)

13			116		All 1’s	No information

14			117		All 1’s	No information on the forecast generating process

15-16			118-119		3	The observational data cut-off was 3 hours after the 									reference time

17			120		30	The observational data cut-off was 30 minutes after the

observational cut-off hour

18			121		1	The time is given in hours

19-22			122-125		12	The forecast time is 12 hours after the reference time

23			126		150	The first fixed surface is a general height coordinate surface

24			127		0	The scale factor of first fixed surface is 0

25-28			128-131		13	The scaled value of first fixed surface is 13

29			132		150	The  second fixed surface is a general height 									coordinate surface

30			133		0	The scale factor of the second fixed surface is 0

31-34			134-137		14	The scaled value of the second fixed surface is 14

35-38			138-141		61	The vertical grid GRIB2 message contains 61 levels (NLEV)

39-42			142-145		13	Grid number of 3D vertical GRIB2 message (NGRID); 								defined by originating centre

43-46			146-149		   	Part 1 of UUID

47-50			150-153		  	Part 2 of UUID

51-54			154-157		   	Part 3 of UUID

55-58			158-161		   	Part 4 of UUID

The corresponding 3D vertical grid GRIB2 message provided by grid number NGRID=13 and UUID consists of NLEV=61 model height levels, the height fields  for level 13 and 14 have the following section 4:

1-4			104-107		38	This Section is 38 octets long

5			108		4	This is Section 4

6-7			109-110		6	6 numbers with vertical grid information follow

after the template

8-9			111-112		0	The Product Definition Template Number is 4.0 – an 						analysis or forecast at a horizontal level or in a horizontal 					layer at a point in time

10			113		3	The parameter category is 3 – mass  products

11			114		6	The parameter number is 6  - geometric height ( in m )

12			115		2	A forecast generated this product (the generating process)

13			116		All 1’s	No information

14			117		All 1’s	No information on the forecast generating process

15-16			118-119		3	The observational data cut-off was 3 hours after the reference time

17			120		30	The observational data cut-off was 30 minutes after the

observational cut-off hour

18			121		1	The time is given in hours

19-22			122-125		12	The forecast time is 12 hours after the reference time

23			126		150	The first fixed surface is a general coordinate surface

24			127		0	The scale factor of first fixed surface is 0

25-28			128-131		13 (14)	The scaled value of first fixed surface is 13 for level 13

(2nd  field : 14)

29			132		1	The  second fixed surface is Ground or water surface

30			133		0	The scale factor of the second fixed surface is not required

31-34			134-137		0	The scaled value of the second fixed surface is not required

35-38			138-141		61	The vertical grid GRIB2 message contains 61 levels (NLEV)

39-42			142-145		13	Grid number of 3D vertical GRIB2 message (NGRID); 								defined by originating centre

43-46			146-149		   	Part 1 of UUID

47-50			150-153		  	Part 2 of UUID

51-54			154-157		   	Part 3 of UUID

55-58			158-161		   	Part 4 of UUID