| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 – 25 MAY 2012 |  | IPET-DRC-IV / Doc.3.2 (10) (7. V. 2012) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

New BUFR/CREX entries for NPP data

Submitted by Jeff Ator (U.S.A.)

________________________________________________________________

Summary and Purpose of Document

The document proposes new entries to the BUFR and CREX tables for use with NPP data.

________________________________________________________________

ACTION PROPOSED

The team is requested to review and approve the contents of this

document for pre-operational implementation.

DISCUSSION

At IPET-DRC-III  (Melbourne, September 2011), additions to the BUFR/CREX tables were proposed by the U.S./NESDIS for use with SST (Sea surface temperature), AOP (Aerosol optical thickness) and OMPS (Ozone mapping and profiler suite) data from NPP.  These new entries were reviewed and subsequently approved for validation.

Since that time, validation of SST has been completed with kind assistance from IBL, EUMETSAT and ECMWF, so the entries shown below are now requested for pre-operational approval.  The entries for AOP and OMPS are still awaiting validation, but this is expected to occur within the next 3-6 months

PROPOSAL

Pre-operational status is requested for the following additions to the BUFR/CREX tables, for use with NPP SST (Sea surface temperature) data:

Add new entry to Table D:

|  |  | SST (Sea surface temperature) data |
| --- | --- | --- |
| 3 10 063 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 01 034 | Identification of originating/generating sub-center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 2 01 133 | Increase bit width |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 33 082 | Geolocation quality flags |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 075 | Ascending/descending orbit qualifier |
|  | 0 08 013 | Day/night qualifier |
|  | 0 08 072 | Pixel(s) type |
|  | 0 33 084 | Pixel level quality flag |
|  | 0 07 062 | Depth below sea surface |
|  | 0 33 086 | Quality of pixel level retrieval |
|  | 0 22 043 | Sea/water temperature |
|  | 0 07 062 | Depth below sea surface (top of layer) |
|  | 0 07 062 | Depth below sea surface (bottom of layer) |
|  | 0 33 086 | Quality of pixel level retrieval |
|  | 0 22 043 | Sea/water temperature |

Add new entry to Common Code Table C-13:

Data Category				International subcategory

12	Surface data (satellite)			12	Sea surface temperature

Add new bit to Table B entry 0-33-082 - Geolocation quality flags

6	Within South Atlantic anomaly

Add new entries to Table B:

|  | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 33 084 | Pixel level quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 086 | Quality of pixel level retrieval | Code table | 0 | 0 | 3 | Code table | 0 | 1 |

0-33-084 – Pixel level quality flags

| Bit | Meaning |
| --- | --- |
| 1-5 | Reserved |
| 6 | Bulk SST outside of validation range |
| 7 | Skin SST outside of validation range |
| 8 | Sensor Zenith Angle > 40 Degrees (Pixel is not within 40 degrees of Nadir and therefore is not of high quality) |
| 9 | Degradation - Horizontal Cell Size > 1.3km (HCS > 1.3 km, swath width > 1700 km, Sensor Zenith Angle > 50.3 degrees) |
| 10 | Exclusion: No Ocean in pixel |
| 11 | Degradation: AOT > 0.6 (AOT in horizontal cell > 0.6 on the slant path (AOT @550nm)) |
| 12 | Exclusion: Aerosol Optical Thickness (AOT)> 1.0 (AOT in horizontal cell > 1.0 on the slant path (AOT @550nm)) |
| 13 | Sun Glint present in pixel |
| 14 | Ice Concentration Threshold Exceeded (SST not retrieved due to ice concentration exceeding threshold in System Spec) |
| 15 | Thin Cirrus detected in pixel |
| All 16 | Missing value |

0-33-086 - Quality of pixel level retrieval

| Code figure | Description |
| --- | --- |
| 0 | Not Retrieved |
| 1 | Excluded |
| 2 | Degraded |
| 3 | High Quality |
| 4-6 | Reserved |
| 7 | Missing value |