| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 3.2 (11) (09.V.2012) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

A BUFR Sequence to Append Data for National Use to Canadian SYNOP Reports

Submitted by Yves Pelletier (Canada)

_______________________________________________________________________

Summary and Purpose of Document

The document contains a proposed Table D sequence and two new Table B element descriptors to represent data for national use in Canadian SYNOP BUFR.

_______________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the sequence and new element descriptors for validation.

DISCUSSION

The FM 12 SYNOP code form permits the expression of data for national use in Section 5 (figure group 555). Canadian TAC SYNOP features some data elements that are conveyed in this manner.  As part of its national plan for the Migration to Table-Driven Code Forms, Canada wishes to express these data elements as a BUFR sequence and append it, for national and limited international distribution, to the main body of its BUFR SYNOP produced in accordance with the B/C regulations. While distribution of this subset of data is expected to be limited,  international sharing is likely to occur. For this reason, Canada wishes to avoid using local descriptors to express its data for national use. Using standard WMO BUFR Tables would facilitate decoding by interested Members, and even by potential third parties within Canada.

PROPOSAL

- A Table D sequence, 3 07 100, is proposed for Canadian SYNOP Section 5 data. (See below). The sequence is intended for comments and validation.

- Three new Table B descriptors are requested to express data elements relating to snow accumulation and water equivalent snow accumulation. (See below). The descriptors are intended for validation along with the Table D sequence.

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT DESCRIPTION |
| --- | --- | --- |
| F X Y |  | Synoptic Data for National Use (Canada) |
| 3 07 100 |  |  |  |
|  | 0 04 024 | Time period | (value = -6): following values apply to the 6 hour period preceding reference time. |
|  | 1 02 000 | Short delayed descriptor replication of two descriptors |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 13 057 | Time of beginning/end of precipitation | Time of Precipitation beginning/end (National Use SYNOP code 909RtDc) |
|  | 0 26 020 | Duration of precipitation |  |
|  | 1 01 000 | Depth of newly-fallen snow |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 13 012 | Depth of Fresh Snow | (National SYNOP code 931ss) |
| 3 01 002 |  |  |  |
|  | 0 04 004 | Hour | set to 6 reporting time is always 0600Z |
|  | 0 04 005 | Minute | set to 0 |
|  | 0 04 024 | Time period in hours | Set to -24 ; values apply to the 24 hour period ending at the last T=06Z |
|  | 1 03 000 | Delayed descriptor replication | Bright sunshine |
|  | 0 31 000 | Delayed descriptor replication factor |  |
|  | 0 02 006 | Data Obtained by | Value=1, obtained by derivation |
|  | 0 14 031 | Bright Sunshine | (National Use SYNOP code 5SSSS) |
|  | 0 02 006 | Data Obtained by | Value=0, Obtained by measurement |
|  | 1 04 000 | Short Delayed replication of 4 descriptors | Snowfall Amount/Water Equivalent |
|  | 0 31 000 | Short Delayed descriptor replication factor |  |
|  | 0 02 175 | Method of precipitation measurement |  |
|  | 0 13 119 | Snowfall amount | New descriptor (National SYNOP code 1SSSS) |
|  | 0 02 175 | Method of precipitation measurement |  |
|  | 0 13 120 | Amount of water equivalent of snow | New descriptor (National SYNOP code 2SwSwSwSw) |
|  | 1 07 000 | Short Delayed replication | Max wind speed/direction |
|  | 0 31 000 | Short Delayed replication factor |  |
|  | 0 08 021 | Time significance | Value=30, "time of occurrence" |
|  | 0 04 004 | Hour | Time of occurrence in hours (National SYNOP code 4FhFTFTFI) |
|  | 0 04 005 | Minutes | Time of occurrence minutes |
|  | 0 11 001 | Wind direction | (National Use SYNOP code 3dmdm) |
|  | 0 08 023 | First order statistics | max, value=2 |
|  | 0 11 002 | Wind Speed | (National Use SYNOP code fmfm) |
|  | 0 08 021 |  | Value=0, cancel |
|  | 0 04 024 | Time period in hours | Value=0, reset to initial time value |
| 3 01 002 |  |  |  |
|  | 0 04 004 | Hour | Reset to original value, the observation time |
|  | 0 04 005 | Minute | Reset to original value, the observation time |

Proposed new element descriptors

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 02 006 | Data obtained by | Code Table | 0 | 0 | 3 | Code Table | 0 | 1 |
| 0 13 119 | Snowfall amount | m | 3 | -10 | 14 | m | 3 | 5 |
| 0 13 120 | Snow amount, Water Equivalent | kg/m2 | 1 | -10 | 14 | kg/m2 | 1 | 5 |

0 02 006

Data Element Obtained By

| Code figure |  |
| --- | --- |
| 0 | Measurement |
| 1 | Derivation from other data |
| 2-6 | Reserved |
| 7 | Missing |