| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 3.2 (2) ( 7 .V.2012) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

ASECNA CREX template for SYNOP data

Submitted by Eva Červená (Czech Republic)

_______________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for representation of SYNOP data encoded manually in CREX messages.

_______________________________________________________________________

ACTION PROPOSED

The meeting is invited to recommend the proposed Alternative A and/or B for implementation.

REFERENCES:

[1] Manual on Codes, WMO-No. 306, Volume I.2

[2] Manual on Codes, WMO-No. 306, Volume II

[3] Letter from the Permanent Representative of Senegal on a proposal for ASECNA

templates for reporting observations in CREX and BUFR

DISCUSSIONS

In February 2012, Members of IPET DRC received a letter from the Permanent Representative of Senegal with a proposal for ASECNA  templates for reporting observations in CREX and BUFR. Annex 4 of this document contained a proposal for representation of SYNOP encoded manually in CREX using a new template D 07 103 = D 07 087 D 07 101. The only difference between the alredy operational D 07 089 = D 07 087 D 07 088 and the newly proposed template D 07 103 was the addition of detailed representation of ground minimum temperature within the new template D 07 101:

| B 04 024 | Time period or displacement = - 12 | Hour, 0, 4 |
| --- | --- | --- |
| B 07 032 | Height of sensor above local ground | m, 2, 5 |
| B 12 121 | Ground minimum temperature TgTg Transmitted at 06 UTC | °C, 2, 4 |

PROPOSAL

It is proposed to consider using the below included Alternative A and/or Alternative B, taking into account that manual encoding is involved. The Alternative C has bee added merely to make the proposal complete.

Alternative A

It is suggested to use the existing CREX descriptors D 07 087, B 12 122 and D 07 088 instead of D 07 103 = D 07 087 D 07 101.  B 12 122 is ground minimum temperature of the preceding night, which reporting at 0600 UTC is required by regulation 1/12.6.1.

| D 07 087 | “Instantaneous” parameters of sequence D 07 089 |
| --- | --- |
| B 12 122 | Ground minimum temperature of the preceding night TgTg Transmitted at 06 UTC |
| D 07 088 | “Periodic” parameters of sequence D 07 089 |

Alternative B

If reporting of ground minimum temperature of preceding 12 hours is really required, it is suggested to use the existing CREX descriptors D 07 087, B 12 113 and D 07 088 instead of D 07 103 = D 07 087 D 07 101.  B 12 113 is ground minimum temperature, past 12 hours and is fully sufficient to represent the ground minimum temperature of required preceding 12 hours.

| D 07 087 | “Instantaneous” parameters of sequence D 07 089 |
| --- | --- |
| B 12 113 | Ground minimum temperature (scale 2), past 12 hours TgTg Transmitted at 06 UTC |
| D 07 088 | “Periodic” parameters of sequence D 07 089 |

Alternative C

If neither Alternative A nor Alternative B were acceptable, it is suggested to use the existing CREX sequence D 07 089 supplemented by a new descriptor D 02 068 (to represent the required minimum ground temperature over period specified) instead of the proposed D 07 103 = D 07 087 D 07 101 for synoptic messages from a fixed land station suitable for manual encoding of SYNOP into CREX.

| D 07 089 |  | CREX sequence for synoptic messages from a fixed land station suitable for manual encoding of SYNOPs in CREX |
| --- | --- | --- |
|  | D 07 087 | “Instantaneous” parameters of sequence D 07 089 |
|  | D 07 088 | “Periodic” parameters of sequence D 07 089 |
| D 02 068 |  | Ground minimum temperature over period speciﬁed |
|  | B 04 024 | Time period or displacement = - 12 | Hour, 0, 4 |
|  | B 07 032 | Height of sensor above local ground | m, 2, 5 |
|  | B 12 121 | Ground minimum temperature TgTg Transmitted at 06 UTC | °C, 2, 4 |