| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FOURTH MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES EXETER, UK, 21 - 25 MAY 2012 |  | IPET-DRC-IV / Doc. 3.2 (8) (11. V. 2012) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

A 1st Draft for BUFR template for exchange of LIDAR and Ceilometer data

Submitted by

Mr. Myles Turp (United Kingdom)

Mr. Owen Cox (United Kingdom)

Dr Dirk Klugmann (United Kingdom)

Dr Harald Flentje  (DWD)

________________________________________________________________

Summary and Purpose of Document

A part of  COST Action ES0702)  EG-CLIMET http://www.eg-climet.org A Special Working Group was formed to look at the “Harmonisation of European automatic lidar and ceilometer network calibrations, recording formats and archiving protocols”. As part of these activities it was agreed that a common BUFR format should be agreed for these data. Subsequent discussions have resulted in a first draft of the ‘raw’ data template which is currently under review by the LIDAR experts. As you will see there are still some questions to be answered regarding the range of measurements which we hope to address soon.

________________________________________________________________

ACTION PROPOSED

At this early stage we would only like comments on the concept of the template and not detailed discussion on the individual descriptors. It would be useful for representatives to go back to their respective countries if there is an expression of interest in these data and contributing to this template.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] http://www.wmo.int/pages/prog/www/WMOCodes.html

## 1. Purpose of this Template

This proposal is split into 2 parts. The first details a proposed format suitable for the ‘RAW’ data which will be suitable to multiple LIDAR types. The second is based on the format proposed for the Wind Profiler ‘product’ data (submitted in a separate document). We have called this ‘Common active sensing product data template’. Note that this format is also being discussed so we are not yet in a position to ask for any of the templates to be validated.

2. Background

Automatic LIDARS’s and ceilometers can be used to evaluate NWP models either by retrieving geophysical parameters (eg. extinction profiles, cloud base heights and mixing heights) or by comparison with simulated backscatter profiles (based on forward operators). Assimilation of backscatter profiles in NWP model is also a possible objective. Other users concern data for air traffic and security, such as cloud base height, aerosol layers and their properties. Having a BUFR template agreed will ensure that data will be in a format suitable for international exchange.

3. Proposal

The following has been taken from existing BUFR descriptors, the ones highlighted in blue will require changes to the existing code tables. Any new descriptor are indicated in red.

PART 1 - Raw data template

Desciptor D   Descriptor B   	Element  			Unit        		scale   	ref value      data width (bits)	Comments

3 01 001	0 01 001		WMO BLOCK NUMBER			NUMERIC		0	0		7

0 01 002		WMO STATION NUMBER				NUMERIC	0	0		10

3 01 021	0 05 001 	LATITUDE (HIGH ACCURACY) 			DEGREE 	5 	-9000000 	15

0 06 001 	LATITUDE INCREMENT (HIGH ACCURACY) 	DEGREE 	5 	-9000000 	15

0 07 001 	HEIGHT OF STATION				M 		0 	-400 		15

3 01 011	0 04 001 	YEAR 						YEAR 		0 	0 	  	12

0 04 002 	MONTH 						MONTH 		0 	0 		4

0 04 003 	DAY 						DAY 		0 	0 		6

3 01 013`0 04 004 	HOUR 						HOUR 		0 	0 		5

0 04 005 	MINUTE 					MINUTE 	0 	0 		6

0 04 006   	 SECONDS					SECONDS	0	0		6

0 08 021		TIME SIGNIFICANCE				CODE TABLE	0	0		5	2 = Time average

0 04 026		TIME PERIOD OR DISPLACEMENT		MINUTE		0	-4096		13 	see note 2

0 02 121		MEAN FREQUENCY				HZ		-8	0		7	see note 3

Vertical Offset angle					DEGREES					SEE NOTE 1

LIDAR Instrument type					CCITT IA5	0	0		64

Instrument Software version				CCITT IA5	0	0		96

Processing software version				CCITT IA5	0	0		96

Range							M

Field of view						RADIANS

Divergence						RADIANS

Replication based on number of wavelengths – n=1 – 16 – is separate descriptor (number of wavelengths also required??)

Wavelength						METERS

Pulse Duration						SECONDS

Replication based on number of detectors – n=1 – 32 – is separate descriptor (number of detectors also required??)

Receiving wavelength					METERS

Polarity							BOOLEAN

Detector							BOOLEAN

Replication details – this is standard for most messages containing multiple data

1 01 000	Delayed Replication of 1 descriptor - 1 XX YYY this ignores the first replication.

0 31 002	Extended delayed descriptor replication factor  (Numeric)

0 07 007 	HEIGHT 						M 		0 	-1000 		17	See note 4

Overlap function

Energy per pulse

Pulse Repetition Rate

0 21 xxx	ATTENUATED LIDAR BACKSCATTER 		M-1 SR-1  	2	-10000000	25	See note 5

NEW DESCRIPTOR REQUIREMENTS

Vertical Offset angle	- Angle between zenith and instrument.  Ceilometers are offset from vertical to prevent specular reflection from ice clouds –

Typical value - 4.0	Range – 0.1 – 10.0?

LIDAR Instrument type - Character field?  Or id, for example 0=LD40, 1=CT25k, 2=CL31, 3=CT75k, 4=CL51, 5=CHM15k, 6=Nimbus, etc

This would be best as a character field to allow the easy expansion of new instruments

Typical value – CHM15K	Range – 10 Characters?

Instrument Software version - Version number of manufacturers firmware used at instrument.

Typical value – CHM15K	Range – 10 Characters?

Could we use 0 25 061 ??? and incorporate into below

Processing software version - Version number of processing software used to create BUFR file

Could we use 0 25 061 ??? and incorporate into above

Range - Should this be a profile of n elements long describing the height of each observation?  Or simply two variables, n gates and gate width dz

Field of view - Angle viewable by instrument

Divergence - Angular extent of the beam

Replication based on number of wavelengths – n=1 – 16 – is separate descriptor (number of wavelengths also required??)

Wavelength - Wavelength of the emitted pulse

Pulse Duration - Length of time pulse is emitted for

Replication based on number of detectors – n=1 – 32 – is separate descriptor (number of detectors also required??)

Receiving wavelength -

Polarity -

Detector - Only photovoltaic or photoncount, so could just be boolean, i.e photoncount = true, photovoltaic = false

DATA VALUES

Overlap function

Energy per pulse

Pulse Repetition Rate

0 21 xxx	ATTENUATED LIDAR BACKSCATTER 		M-1 SR-1  	2	-10000000	25	See note 5

PART 2 - Common active sensing product data template – (condensed version to be standardised with Wind Profiler data)

A Table D descriptor would assigned for the whole template (3 xx xxx)  known as the ‘common active sensing product data template) which would also be used to record the meta data for LIDARNET.

Desciptor D   Descriptor B   	Element  			Unit        		scale   	ref value      data width (bits)	Comments

3 01 001	0 01 001		WMO BLOCK NUMBER				NUMERIC	0	0		7

0 01 002		WMO STATION NUMBER				NUMERIC	0	0		10

3 01 021	0 05 001 	LATITUDE (HIGH ACCURACY) 			DEGREE 	5 	-9000000 	15

0 06 001 	LATITUDE INCREMENT (HIGH ACCURACY) 	DEGREE 	5 	-9000000 	15

0 07 001 	HEIGHT OF STATION				M 		0 	-400 		15

0 02 003		TYPE OF MEASURING EQUIPMENT USED		CODE TABLE	0	0		4	see note 1

3 01 011	0 04 001 	YEAR 						YEAR 		0 	0 	  	12

0 04 002 	MONTH 						MONTH 		0 	0 		4

0 04 003 	DAY 						DAY 		0 	0 		6

3 01 013`0 04 004 	HOUR 						HOUR 		0 	0 		5

0 04 005 	MINUTE 					MINUTE 	0 	0 		6

0 04 006   	SECONDS					SECONDS	0	0		6

0 08 021		TIME SIGNIFICANCE				CODE TABLE	0	0		5	2 = Time average

0 04 026		TIME PERIOD OR DISPLACEMENT		MINUTE		0	-4096		13 	see note 2

0 02 121		MEAN FREQUENCY				HZ		-8	0		7	see note 3

Replication details – this is standard for most messages containing multiple data

1 01 000	Delayed Replication of 1 descriptor - 1 XX YYY this ignores the first replication.

0 31 002	Extended delayed descriptor replication factor  (Numeric)

DATA SPECIFIC TO LIDAR

Descriptors to be repeated (the number will depend on the number of replications as detailed above)

0 07 007 	HEIGHT 						M 		0 	-1000 		17	See note 4

0 21 xxx		ATTENUATED LIDAR BACKSCATTER 		M-1 SR-1  	2	-10000000	25	See note 5

NOTES

- 0 02 003 – Add new code table for LIDAR (or  perhaps multiple to cover different types of LIDAR’s)

- 0 04 026 – We would prefer to use a separate descriptor to state the time stamp is at ‘start’, ‘middle’ or ‘end’ of the reporting period – this is not used correctly for some wind profiler data so could also cause confusion with other data types.

- 0 02 121 – For LIDAR data it would be more appropriate to use wavelength (022075 ‘average wavelength’ could be used instead?) – due to the frequency range it will be necessary to change the scale and data widths to suit the ranges required using 201xxx and 202xxx modifiers.

- 0 07 007 – For height use class 7 (Location – vertical) as this is the most applicable

- 0 21 xxx –  A new descriptor (class 21?) ATTENUATED LIDAR BACKSCATTER – this will be used to store the raw backscatter data which will be the same for all LIDAR’s

Measurements will be between values 10-E4 – 10-E7) – possibly increase this range???

General notes:

For Wind profiler data we have proposed that an ‘uncertainty’ value is used to give the user an indication of how reliable each measurement is together with a new descriptor for ‘Vertical Resolution’ which will replace ‘range gate length’ which we have found is often misinterpreted.

We may also want to include the following information – although this might be better placed in the ‘raw’ template

- beamwidth

- pulse length

- laser wavelength