| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(10) (19.VIII.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for CrIS data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for the addition of new BUFR descriptors to be used for Cross-track Infrared Sounder (CrIS) radiance data.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve the contents for preoperational implementation.

BACKGROUND AND DISCUSSION

The CrIS instrument is part of the next generation operational sensor suite selected to fly on the National Polar-orbiting Operational Environmental Satellite System (NPOESS) spacecraft.  The atmospheric data collected from the instrument will allow for the calculation of temperature and moisture profiles at high (~ daily) temporal resolution. The CrIS will provide over one thousand spectral channels of information in the infrared at an improved horizontal spatial resolution and measure temperature profiles with improved vertical resolution to an accuracy approaching one degree Kelvin.  The accurate, detailed atmospheric and moisture observations acquired from CrIS will be used for weather and climate applications.

While the first launch of NPOESS has been delayed, simulated CrIS BUFR data was provided to potential users last winter.  In addition to the validation completed by the United States, both Simon Elliot (EUMETSAT) and Milan Dragosavac (ECMWF) have provided valuable contributions to the BUFR table entries and validated the test data.

PROPOSAL

#### (1) Add new Table D entry:

|  |  | (CrIS (Cross-Track Infrared Sounder) radiance data) |
| --- | --- | --- |
| 3 10 060 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 3 04 030 | Location of satellite platform |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 075 | Ascending/Descending orbit qualifier |
|  | 2 01 133 | Increase bit width |
|  | 0 05 041 | Scan line number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 05 045 | Field of regard number |
|  | 0 05 043 | Field of view number |
|  | 0 05 040 | Orbit number |
|  | 0 10 001 | Height of land surface |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 2 02 127 | Increase scale |
|  | 2 01 125 | Increase bit width |
|  | 0 21 166 | Land fraction |
|  | 2 01 000 | Cancel increase bit width |
|  | 2 02 000 | Cancel increase scale |
|  | 0 08 012 | Land/Sea qualifier |
|  | 0 20 010 | Cloud cover (total) |
|  | 0 20 014 | Height of top of cloud |
|  | 0 02 165 | Radiance type flags |
|  | 0 33 075 | Scan-level quality flags |
|  | 1 07 003 | Replicate 7 descriptors 3 times |
|  | 0 08 076 | Type of band |
|  | 0 06 029 | Wave number (start of range) |
|  | 0 06 029 | Wave number (end of range) |
|  | 0 25 140 | Start channel |
|  | 0 25 141 | End channel |
|  | 0 33 076 | Calibration quality flags |
|  | 0 33 077 | Field of view quality flags |
|  | 0 08 076 | Type of band (“Missing” = Cancel) |
|  | 0 33 078 | Geolocation quality |
|  | 0 33 003 | Quality information |
|  | 1 04 000 | Delayed replication of 4 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 2 01 133 | Increase bit width |
|  | 0 05 042 | Channel number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 14 044 | Channel radiance |

#### (2) Add new Table B entries:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 02 165 | Radiance type flags | Flag table | 0 | 0 | 15 | Flag table | 0 | 5 |
| 0 05 045 | Field of regard number | Numeric | 0 | 0 | 8 | Numeric | 0 | 3 |
| 0 06 029 | Wave number | m-1 | 1 | 0 | 22 | m-1 | 1 | 7 |
| 0 14 044 | Channel radiance | Wm-2sr-1cm-1 | 7 | -100000 | 22 | Wm-2sr-1cm-1 | 7 | 7 |
| 0 33 075 | Scan-level quality flags | Flag table | 0 | 0 | 13 | Flag table | 0 | 5 |
| 0 33 076 | Calibration quality flags | Flag table | 0 | 0 | 9 | Flag table | 0 | 3 |
| 0 33 077 | Field-of-view quality flags | Flag table | 0 | 0 | 19 | Flag table | 0 | 7 |
| 0 33 078 | Geolocation quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

(3) Rename 0 21 166 (ASCAT land fraction) to 0 21 166 (Land fraction)

(4) Add the following new code table entries to existing BUFR/CREX Table B descriptors:

0 08 076  (Type of band)

2	Long-wave infrared

3	Medium-wave infrared

4	Short-wave infrared

(5) Flag tables for proposed new Table B descriptors:

0 02 165  Radiance type flags

| Bit | Meaning |
| --- | --- |
| 1 | Clear path |
| 2 | Partly cloudy path |
| 3 | Cloudy path |
| 4 | Apodized |
| 5 | Unapodized |
| 6 | Reconstructed |
| 7 | Cloud cleared |
| 8-14 | Reserved |
| All 15 | Missing value |

0 33 075  Scan-level quality flags

| Bit | Meaning |
| --- | --- |
| 1 | Gap in Raw Data Record (RDR) data detected (i.e., missing scan(s) preceding the current scan) |
| 2 | Recorded time is not in sequence (i.e., the scan start time is out of sequence) |
| 3 | Lamda monitored calculation cannot be updated (see Note 1) |
| 4 | The measured temperatures of any instrument components (e.g., beam-splitter, scan mirror, scan baffle, etc.) are outside the allowable ranges (see Note 2) |
| 5 | At least one of the monitored instrument temperatures has drifted more than a specified tolerance value |
| 6-12 | Reserved |
| All 13 | Missing value |

Note 1:  Set to 1 if laser wavelength calculation is invalid due to laser diode bias current and/or laser diode temperature measurements being outside the predetermined allowable ranges.  These ranges are tunable.  In this case Lamda monitored calculation shall have 1 bit per scan.

Note 2:  These temperatures are used to compute the “environmental” contribution to the Internal Calibration Target (ICT) radiances.  When this bit is set to 1, the invalid temperatures shall be replaced with the validated temperature values of the ICT.

0 33 076  Calibration quality flags

| Bit | Meaning |
| --- | --- |
| 1 | Lunar intrusion on first deep space view (see Note) |
| 2 | Lunar intrusion on second deep space view (see Note) |
| 3-8 | Reserved |
| All 9 | Missing value |

Note:  Set to 1 if at least one spectrum in the deep space moving average was invalidated due to a lunar intrusion.

0 33 077  Field-of-view quality flags

| Bit | Meaning |
| --- | --- |
| 1 | Degraded SDR quality |
| 2 | Invalid SDR quality (see Note 1) |
| 3 | Invalid SDR geolocation information |
| 4 | Degraded radiometric calibration |
| 5 | Invalid radiometric calibration (see Note 2) |
| 6 | Degraded spectral calibration |
| 7 | Invalid spectral calibration (see Note 3) |
| 8 | Fringe count error detected and corrected (see Note 4) |
| 9 | Day/night indicator (see Note 5) |
| 10 | Invalid RDR data (see Note 6) |
| 11 | Significant fringe count error detected (see Note 7) |
| 12 | Bit trim failed |
| 13-18 | Reserved |
| All 19 | Missing value |

SDR = Science Data Record

RDR = Raw Data Record

Note 1: SDR quality is invalid if bit trim failed (see bit 12), or fringe count error detected (see bit 11), or invalid Raw Data Record (RDR) data (see bit 10), or invalid radiometric calibration (see bit 5), or invalid spectral calibration (see bit 7).

Note 2: Radiometric calibration is invalid if radiometric calibration is not performed, or if it is performed with invalid calibration data (e.g., deep space window size = 0).

Note 3: Spectral calibration is invalid if fringe count error detected and corrected (see bit 8), or if Neon calibration is suspect and Lamda monitored calculation cannot be updated (see “Scan-level quality flags" (0-33-075) - bit 3).

Note 4: Set to 0 if no fringe count error was detected (see bit 11), or a fringe count error was detected but it was not corrected.

Note 5: Set to 0 if day (solar zenith angle < 90).  Set to 1 if night (solar zenith angle > 90).

Note 6: This flag indicates the instrument exhibited operational errors and the associated interferogram(s) is/are excluded from SDR processing.

Note 7: This flag indicates a significant number of fringes have been missed, shifting the interferogram ZPD outside of a window monitored by the instrument, and the interferogram is excluded from SDR processing.

0 33 078  Geolocation quality

| Code figure | Meaning |
| --- | --- |
| 0 | Nominal – altitude and Ephemeris data available |
| 1 | Missing at most a small gap of altitude and Ephemeris data |
| 2 | Missing more than a small gap of altitude and Ephemeris data, but no more than a granule boundary |
| 3 | Missing more than a granule boundary of altitude and Ephemeris data |
| 4-14 | Reserved |
| 15 | Missing |

(6) Add the following new entry to Common Code Table C-13:

Under Data Category 021 = Radiances (satellite measured), add the following new International Data Sub-Category entry:

| 005 | Cross-track infrared sounder |
| --- | --- |