| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(12) (3.IX.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Proposal for new Standardized BUFR Template for AMDAR

Submitted by Secretariat

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new BUFR Template to be used in the reporting of particulate data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and recommend the proposed additions to be submitted to the next CBS session or directly included in Manual on Codes, WMO-No. 306, Volume I.2.

.

References:

[1]	Final Report of the Ad-hoc Steering Group Meeting on the WIGOS Pilot Project for AMDAR (Geneva, Switzerland, 2-3 July 2008);

[2]		AMDAR Reference Manual, Aircraft Meteorological Data Relay, WMO-No. 958, Geneva, Switzerland, 2003;

[3]		http://www.wmo.int/pages/prog/www/WMOCodes/TemplateExamples.html;

[4]		Manual on Codes, WMO-No. 306, Volume I.2; and

[5]		Development of a BUFR Template for AMDAR, WIGOS-PP-AMDAR-2/Doc. 3.1, 
De Bilt, The Netherlands, 2009.

[6]	WIGOS Pilot Project for AMDAR “To Enhance Delivery of Aeronautical Data from AMDAR Platforms to Users”/Doc 3.1.3 De Bilt, The Netherlands, 2009

[7]	Final Report WMO Integrated Observing System (WIGOS) Pilot Project for AMDAR Second Session (De Bilt, The Netherlands 10-12 February 2009)

- BACKGROUND

The Ad-Hoc Steering Group Meeting on the WIGOS Pilot Project for AMDAR (Geneva, Switzerland, 2-3 July 2008), discussed the status on the operational use and suitability of existing AMDAR BUFR templates and the group agreed on the need to develop and validate a new standardized BUFR template for a global AMDAR use.  Deliberations on this issue resulted in Ad-Hoc Steering Group designing Sub-project under the Pilot Project for AMDAR No. 1 entitled, “Development of a standardized BUFR Template for AMDAR”.

- Overview of BUFR templates for AMDAR

The Current versions of the BUFR template available in AMDAR Reference Manual are:

- 3 11 001 (BUFR template for aircraft reports)

- 3 11 002 (BUFR template for ACARS reports)

It should be noted that sequence descriptors 3 11 003 and 3 11 004 are not BUFR templates, 3 11 003 (ACARS standard reported variables) and 3 11 004 (ACARS supplementary reported variables) are nested with in BUFR template 3 11 002.

The current BUFR templates for AMDAR include:

- 3 11 005 (BUFR template for standard AMDAR reports, CBS-Ext. (02))

- 3 11 008 (BUFR template for aircraft ascent / descent profile without latitude / longitude indicated at each level (CBS-XIII (05))

- 3 11 009 (BUFR template for aircraft ascent/descent profile with latitude / longitude given for each level (CBS-XIII (05))

- 3 11 010 (BUFR template for single level AMDAR data - to be validated (since 2003).

Detailed description of the templates may be found in the Annex to this document.

Note: Sequence descriptors 3 11 006 and 3 11 007 are not BUFR templates.  3 11 006 (Aircraft 
ascent / descent profile data for one level without latitude / longitude) and 3 11 007 (Aircraft 
ascent / descent profile data for one level with latitude/longitude) are nested in BUFR templates 
3 11 008 and 3 11 009, respectively.

BUFR templates 3 11 008 and 3 11 009 were developed to allow representation of vertical profiles of wind direction, wind speed, temperature and humidity during the aircraft ascent or descent that could to some extent replicate a radiosounde profile, in particular, in the areas with low-density of the surface-based sounding network.  BUFR messages containing these 
ascent / descent profile data may be produced at ACARS Centres, using AMDAR data transmitted from the aircraft provided that the extended (not yet validated) template 3 11 010 will be used.  It is to be noted that all elements required in the profile templates 3 11 008 and 3 11 009 are included in the template 3 11 010.

- PROPOSAL FOR NEW STANDARDIZED BUFR TEMPLATE FOR AMDAR

At the 2nd Session for the WIGOS Pilot Project AMDAR it is proposed to use the 3 11 010 BUFR Template as a starting point for the development of the required standardized template for AMDAR.  Template 3 11 010 included has yet to be validated and therefore any additions, reductions and other modifications may be performed without the necessity to introduce a new sequence descriptor for the modified template. The meeting proposed a new version to this Template referred to 3 11 010, version 1.

The meeting agreed on a number of new elements and agreed on deleted 0 08 004 (Phase of flight) from Template 3 11 010 version 1. The meeting also identified a number of elements that could be classed as optional, these are listed in Table 1. The meeting agreed on a proposal for a “Standardized BUFR Template for AMDAR 3 11 010 version 2”, see Table 1 below. As part of the evaluation process the meeting proposed that the AMDAR community and major NWP Centres would evaluate the new Standardized BUFR Template for AMDAR and decide whether these optional elements are required, AMDAR BUFR Template 3 11 010 version 2 was then made available for comment.

| 0 | 01 | 008 |  | Aircraft identification (1) |
| --- | --- | --- | --- | --- |
| 0 | 01 | 023 | Optional | Sequence number (2) |
| 0 | 01 | 100 | Optional | Flight number (3) (4) |
| 3 | 01 | 011 |  | Year, month and day |
| 3 | 01 | 013 |  | Hour, minute and second |
| 3 | 01 | 021 |  | Latitude and longitude (high accuracy) |
| 0 | 07 | 010 |  | Flight level (5) |
| 0 | 07 | 004 |  | Pressure (5) |
| 0 | 10 | 096 |  | GNSS Altitude |
| 0 | 08 | 009 |  | Detailed phase of flight (6) |
| 0 | 11 | 001 |  | Wind direction |
| 0 | 11 | 002 |  | Wind speed |
| 0 | 02 | 064 |  | Aircraft roll angle quality |
| 0 | 11 | 100 | Optional | True aircraft speed (7) |
| 0 | 11 | 101 | Optional | Aircraft ground velocity (u-component) (4) |
| 0 | 11 | 102 | Optional | Aircraft ground velocity (v-component) (4) |
| 0 | 11 | 103 | Optional | Aircraft ground velocity (w-component) (4) |
| 0 | 11 | 104 | Optional | Aircraft true direction (4) |
| 0 | 12 | 101 |  | Temperature / dry-bulb temperature (8) |
| 0 | 13 | 002 |  | Mixing ratio |
| 0 | 13 | 003 |  | Relative humidity |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 12 | 103 | Optional | Dew-point temperature (9) |
| 0 | 33 | 026 |  | Moisture quality |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 042 | Optional | Airframe icing (10) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 043 | Optional | Peak liquid water content (11) |
| 0 | 20 | 044 | Optional | Average liquid water content (11) |
| 0 | 20 | 045 | Optional | Supercooled water droplet conditions (11) |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 33 | 025 | Optional | ACARS interpolated values (12) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors (13) |
| 0 | 31 | 001 |  | Delayed descriptor replication factor (14) |
| 0 | 11 | 075 | Optional | Intensity (EDR) |
| 0 | 11 | 076 | Optional | Peak (EDR) |
| 0 | 11 | 039 | Optional | Extended time of occurrence of peak EDR (15) |
| 1 | 02 | 000 |  | Delayed replication of 2 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 037 | Optional | Turbulence index (EDR) |
| 0 | 11 | 077 | Optional | EDR reporting interval (16) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 034 | Optional | Vertical gust velocity (17) |
| 0 | 11 | 035 | Optional | Vertical gust acceleration (17) |
| 0 | 11 | 036 | Optional | Maximum derived equivalent vertical gust speed (17) |
| 0 | 33 | 079 |  | AMDAR quality information (18) (4) |

Table 1. Standardized BUFR Template for AMDAR 3 11 010 version 2.

Notes for Standardized BUFR Template for AMDAR data 3 11 010, version 2:

- Aircraft identifier 0 01 008 can cope with ASDAR, ADS and other AMDAR identities. ADS reports use a 24-bit ICAO airframe identifier, equating to an 8-character BCD number. Look at developing a standard naming convention for the various AMDAR regions and/or programmes. The meeting agreed that additional information such aircraft type and navigation systems would be part of the Meta data, not part of the Standardized BUFR Template for AMDAR. It was noted that AMDAR Meta data would be addressed by the WIGOS Pilot Project for AMDAR.

- The sequence number is a simple observation count to be included in the down-linked message.  It should be reset at 0000 UTC each day and can be useful for quality control, data management and archiving purposes. The meeting has made the recommendation that if this parameter is not used by an operational AMDAR programme or NWP Centre then this parameter be removed from the new Standardized BUFR Template for AMDAR.

- 0 01 100 (Flight number) has been introduced as an optional entry to provide information on the departure airport and the expected arrivals airport. This element will assist with the quality control of aircraft track data, by providing information on the route the aircraft is expected to take.

- Refer to Table 2 for the required BUFR and CREX descriptors for the new elements, including the units, scale, reference value and data width.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 01 100 | Flight number | CCITT IA5 | 0 | 0 | 64 | character | 0 | 8 |
| 0 11 100 | True aircraft speed | m.s-1 | 1 | 0 | 12 | m.s-1 | 1 | 4 |
| 0 11 101 | Aircraft velocity u-component | m.s-1 | 1 | –4096 | 13 | m.s-1 | 1 | 4 |
| 0 11 102 | Aircraft velocity v-component | m.s-1 | 1 | –4096 | 13 | m.s-1 | 1 | 4 |
| 0 11 103 | Aircraft velocity w-component | m.s-1 | 1 | –512 | 10 | m.s-1 | 1 | 4 |
| 0 11 104 | Aircraft true heading | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| 0 33 079 | AMDAR quality information | Flag table | 0 | 0 | 24 | Flag table | 0 | 8 |

Table 2. Proposal for new AMDAR descriptors in 3 11 010, version 2

For Table 2, AMDAR descriptors, the data width for Flight number, 0 01 100, will be dependant on the expected length of the flight number, e.g. AF5097, BA2736, LH3700. To properly define the expected data width an accurate estimate of the number characters used in generating a flight number will be required. Presently 8 characters has been used as an estimate as the maximum length for any given flight number.

- Flight level is defined relative to the ICAO International Standard Atmosphere (ISA) standard sea level pressure pane (1013.25 hPa) and is readily converted to static air pressure altitude using standard formulae.  The original resolution (either 100ft or 10ft) is sufficiently represented by 0 07 010 (Flight level) that is reported in meters with precision in units of a meter.  The descriptor shown is designed to deal with high-resolution flight level data. The definition of Flight level is identical to that of pressure altitude, as defined in FM42

- This phase of flight table is expanded to indicate wind quality from roll angle, or roll and pitch combined and also to indicate the method of ascent and descent observation interval selection either by time or pressure increments. The meeting agreed that the Phase of flight 0 08 004 would not be included in the new Standardized BUFR Template for AMDAR as the required level of detail has been incorporated in the detailed phase of flight 0 08 009. The meeting also discussed whether there is a requirement for adding a new condition to the detailed phase of flight 0 08 009 that would cover an aircraft being placed in a holding pattern.

- Refer to AMDAR Reference Manual for definition.

- It is suggested that this parameter be renamed Air Temperature and that dry bulb temperature be removed.

- 0 12 103 Dew-point temperature had been introduced in the templates for AMDAR profile data to simulate radiosonding data.

- The old ACARS airframe icing code table 0 20 041 is not included.

- A special automatic icing report, including these elements, is expected to become available from some aircraft and a down-link code has been published.

- 0 33 025 ACARS interpolated values was primarily used in the USA AMDAR Programme to indicate time and position being reported or interpolated. It is suggested that the name for this element be changed to ACARS interpolated values indicator.

- Delayed replication 1 03 000 refers to the following three descriptors 0 11 075, 0 11 076 and 0 11 039 to allow reporting of the Extended time of occurrence of peak EDR of all included values of 0 11 076 (Peak (EDR)). This allows each turbulence peak to be reported.

Explanatory remarks to Note (13):

According to Note (14), up to ten values of 0 11 076 (Peak (EDR)) may be reported.  However, 0 11 039 (Extended time of occurrence of peak EDR) was included only once in the template 3 11 010, version 0.  Therefore, it was not clear to which out of those ten values of 0 11 076, the time specification 0 11 039 referred.  If it had been the maximum value, the name of 0 11 039 should have been modified to read “Extended time of occurrence of maximum peak EDR”.  If the time information on all the reported values of 0 11 076 (Peak (EDR)) is required, then 0 11 039 (Extended time of occurrence of peak EDR) should be included under the delayed replication as shown in the proposed template 3 11 010, version 2.

Moreover, 0 11 039 is a code table, allowing to represent one-minute interval of the peak occurrence, e.g., code figure 5 means that the peak occurred between 5 and 6 minutes prior to observation time.  This information may be expressed in much better and more flexible way by inclusion of 0 08 021 (Time significance) and two consecutive entries 0 04 025 (time period or displacement in minutes). E.g. 0 04 025 = -6 and 0 04 025 = -5 specify interval of the peak occurrence between 5 and 6 minutes prior to the observation time (not shown in the proposed template).

- Some aircraft report up to 10 pairs of (EDR) values per observation.  The corresponding times and position could be found by interpolation from the previous report. If the aircraft does not report it the number of replication 0 31 001 is set to zero.

- 0 11 039 allows observation intervals up to one hour.  0 11 038 allows up to 15 minutes only whereas observation intervals of 30 minutes or more are commonly used, hence 0 11 038 had been replaced by 0 11 039.

- The EDR observing interval and associated averaging time differs according to individual observing schedule and cannot be assumed to be identical to the observation interval for the main elements.  It is desirable to include this information in the coded data.

- Vertical gust velocity 0 11 034, Vertical gust acceleration 0 11 035 and Maximum derived equivalent vertical gust speed 0 11 036 have been added to meet the request for reflecting all entries of 3 11 004 in the Standardized BUFR template for AMDAR. The current ICAO standard for automated turbulence reporting is EDR.

- Refer to Table 3 for detail definition of 0 33 079 AMDAR quality information.

| Bit No. |  |
| --- | --- |
| 1 | Date suspected |
| 2 | Hour suspected |
| 3 | Minute suspected |
| 4 | Latitude suspected |
| 5 | Longitude suspected |
| 6 | Flight level suspected |
| 7 | Wind direction suspected |
| 8 | Wind speed suspected |
| 9 | Air temperature suspected |
| 10 | Relative humidity suspected |
| 11 | Mixing ratio suspected |
| 12 | Turbulence suspected |
| 13 | Icing suspected |
| 14-23 | Reserved |
| All 24 | Missing value |

Table 3. 0 33 079 AMDAR quality information

- Evaluation of Proposed Template by the AMDAR community and major NWP Centres

4.1	AMDAR quality information

Following discussions with Mr Milan Dragosavac and Dr. Eva Cervena FROM IPET-DRC a proposal for a more sophisticated method of quality control representation, usage of the operator 2 22 000 (Quality information) and the operator 2 04 007 (Add associated field), was put forward to the members of the AMDAR Panel for their consideration. This proposal (ANNEX) demonstrated the advantages and disadvantages of all three methods of quality control representation for AMDAR data. Following the evaluation of the proposal by AMDAR Panel Members it was determined that the advantages of the original method proposed, Flag table 0 33 079, would better suite the AMDAR Programme, in particular the advantage that the Flag tables are managed even by simple BUFR encoders/decoders.

4.2	Turbulence Report (EDR)

The USA AMDAR Programme expressed some concern that the event based reporting of EDR reports from USA based aircraft would be lost in a new Template. The following information was regarded as essential in EDR reporting;

- Currently there are 8 encoded characters representing turbulence.  This present method no longer maps to the turbulence index table represented by 0 11 37.

- There is a requirement to add the ability to label values "unknown".

The USA AMDAR Programme provided two approaches that could be used.

1.  Store the data in the AMDAR template with out decoding. The possible encoded values are:

{'0','1','2','3','4','5','6','7','8','9',

'A','B','C','D','E','F','G','H','I','J','K','L',

'M','N','O','P','Q','R','S','T','U','V','W','X','Y','Z',

'(','-',')','/',':',';'}

2.  Decode the turbulence data before translating to BUFR.  Current downlinked turbulence data include the following;

- 10s of seconds

- Running minimum confidence

- Running number of Bad

- Software version running on the aircraftPeak EDR (real number with 2 significant digits - .02 resolution)

- Mean EDR (real number with 2 significant digits - .02 resolution)

- Peak EDR Confidence

- Mean EDR Confidence

- Peak Location

- Number of good EDRs

A more comprehensive requirement is list in ANNEX 2 of this document. 	The information in ANNEX 2 contains two parts, a down-linked message header and from 1 to 6 message body that contains the actual EDR information. Unlike the previous standard, there is a requirement to have temporal and location information for each individual report.  Previously, this information had to be manually interpretted.

  - Aircraft Positional Information

The AMDAR Science and Technical Sub-Group requested that Flight level (0 07 010) be replaced with static pressure (0 07 004) as this value is primarily there before any altitude value is calculated by the aircrafts on-board algorithms. Only the left-over of the so-called built-in error remain any other effect of calculation methods, rounding, or formatting are avoided. For any meteorological application of the AMDAR data the pressure value is needed but not the flight level.

The Sub-Group also recommended that as well as the True Airspeed, Ground Speed (lines 0 11 100 to 103) the new standardized AMDAR BUFR Template include Aircraft True Heading (0 11 104) this would provide enough information to better understand wind vector errors. Furthermore a number of operational AMDAR Programmes have recommended that the proposed new AMDAR BUFR Template include an additional Class 10 non-coordinate location (vertical) parameter GNSS (Global Navigation Satellite System) Altitude (0 10 96).

ANNEX 1:

WIGOS PILOT PROJECT FOR AMDAR

Proposals for representation of Quality information

Eva Červená, 29 March 2009

Background

At the second session of the WIGOS PILOT PROJECT for AMDAR (10 -13 February 2009), a new version of AMDAR BUFR Template was developed (3 11 010, version 2). In this template, Quality information was proposed to be represented by a flag table 0 33 079

0 33 079 AMDAR quality information

| Bit No. |  |
| --- | --- |
| 1 | Date suspected |
| 2 | Hour suspected |
| 3 | Minute suspected |
| 4 | Latitude suspected |
| 5 | Longitude suspected |
| 6 | Flight level suspected |
| 7 | Wind direction suspected |
| 8 | Wind speed suspected |
| 9 | Air temperature suspected |
| 10 | Relative humidity suspected |
| 11 | Mixing ratio suspected |
| 12 | Turbulence suspected |
| 13 | Icing suspected |
| 14-23 | Reserved |
| All 24 | Missing value |

However, BUFR offers also other, more sophisticated methods for representation of quality information, i.e. usage of the operator 2 22 000 (Quality information) or the operator 2 04 007 (Add associated field).

This document is intended to demonstrate advantages and disadvantages of the three methods for representation of quality information in the following order:

- operator 2 22 000 (Quality information),

- flag table 0 33 079 (AMDAR quality information),

- operator 2 04 007 (Add associated field).

1. Operator 2 22 000 (Quality information)

| 3 11 010, version 3 | BUFR Template for AMDAR |
| --- | --- |
| 2 22 000 | Quality information follows |
| 1 01 000 | Delayed replication of 1 descriptor (see Note) |
| 0 31 001 | Delayed descriptor replication factor (see Note) |
| 0 31 031 | Data present indicator (see Note) |
| 0 01 033 | Identification of originating/generating center |
| 0 01 032 | Generating application |
| 1 01 000 | Delayed replication of 1 descriptor |
| 0 31 001 | Delayed descriptor replication factor |
| 0 33 007 | Per cent confidence |

Note: The data present bit-map is a bit string containing bits equal in number to the number of data values.  It is constructed by replicating the Data present indicator 0 31 031, using delayed replication in this case. In the bit map produced with 0 31 031, a bit set to 0 means “data present” and a bit set to 1 means “data not present”.

Advantages:

- Percentage confidence may be reported.

- The bit map links each quality control value with the element for which the quality information is required.

- If quality information is required for some additional element, the template remains unchanged.

Disadvantages:

- Quality information operator 2 22 000 is the most sophisticated method for representation of quality information and requires availability of a universal BUFR SW and of advanced level of users.

2. Flag table 0 33 079 (AMDAR quality information)

In this case, 3 11 010, version 3 is supplemented merely by 0 33 079, therefore the outcome is corresponding to 3 11 010, version 2:

3 11 010, version 3

0 33 079 AMDAR quality information

Advantages:

- If quality information is required for some additional element, the template remains unchanged – the flag table will be supplemented by a new entry.

- Flag tables are managed even by simple BUFR encoders/decoders.

Disadvantages:

- Percentage confidence cannot be expressed; merely “suspected” may be reported.

- Generally speaking, there might be more than one element of the same name in a template, for which the quality information is required. However, in the template 3 11 010, the quality information is required for elements that are included only once.

Note: The names of elements in the template and in the flag table entries have to have identical names to avoid any confusion. To meet this requirement, it is proposed to modify the entries 12 and 13 in the flag table 0 33 079 to be in compliance with element names of 0 20 042 (Airframe icing) and 0 11 037 (Turbulence index) in BUFR Table B.

0 33 079 AMDAR quality information

| Bit No. |  |
| --- | --- |
| 1 | Date suspected |
| 2 | Hour suspected |
| 3 | Minute suspected |
| 4 | Latitude suspected |
| 5 | Longitude suspected |
| 6 | Flight level suspected |
| 7 | Wind direction suspected |
| 8 | Wind speed suspected |
| 9 | Air temperature suspected |
| 10 | Relative humidity suspected |
| 11 | Mixing ratio suspected |
| 12 | Turbulence index suspected |
| 13 | Airframe icing suspected |
| 14-23 | Reserved |
| All 24 | Missing value |

3. Operator 2 04 007 (Add associated field)

Advantages:

- Percentage confidence may be reported.

- The operator 2 04 007 specifies each quality control value with the element for which the quality information is required.

Disadvantages:

- If quality information is required for some additional element, the template will have to be modified, i.e. a new version of the template issued as demonstrated below.

BUFR Template for AMDAR with operators 2 04 007

| 0 | 01 | 008 |  | Aircraft identification (1) |
| --- | --- | --- | --- | --- |
| 0 | 01 | 023 | Optional | Sequence number (2) |
| 0 | 01 | 100 | Optional | Flight number (3) (4) |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) |
| 0 | 31 | 021 |  | Associated field significance = 7 (Percentage confidence) |
| 3 | 01 | 011 |  | Year, month and day (see Note) |
| 0 | 04 | 004 |  | Hour (see Note) |
| 0 | 04 | 005 |  | Minute (see Note) |
| 2 | 04 | 000 |  | Cancel Add associated field |
| 0 | 04 | 006 |  | Second |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) |
| 0 | 31 | 021 |  | Associated field significance = 7 (Percentage confidence) |
| 3 | 01 | 021 |  | Latitude and longitude (high accuracy) (see Note) |
| 0 | 07 | 010 |  | Flight level (5) (see Note) |
| 2 | 04 | 000 |  | Cancel Add associated field |
| 0 | 08 | 009 |  | Detailed phase of flight (6) |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) |
| 0 | 31 | 021 |  | Associated field significance = 7 (Percentage confidence) |
| 0 | 11 | 001 |  | Wind direction (see Note) |
| 0 | 11 | 002 |  | Wind speed (see Note) |
| 2 | 04 | 000 |  | Cancel Add associated field |
| 0 | 02 | 064 |  | Aircraft roll angle quality |
| 0 | 11 | 100 | Optional | True aircraft speed (7) |
| 0 | 11 | 101 | Optional | Aircraft ground velocity (u-component) (4) |
| 0 | 11 | 102 | Optional | Aircraft ground velocity (v-component) (4) |
| 0 | 11 | 103 | Optional | Aircraft ground velocity (w-component) (4) |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) |
| 0 | 31 | 021 |  | Associated field significance = 7 (Percentage confidence) |
| 0 | 12 | 101 |  | Air temperature (see Note) |
| 0 | 13 | 002 |  | Mixing ratio (see Note) |
| 0 | 13 | 003 |  | Relative humidity (see Note) |
| 2 | 04 | 000 |  | Cancel Add associated field |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 12 | 103 | Optional | Dew-point temperature (9) |
| 0 | 33 | 026 |  | Moisture quality |
| 1 | 04 | 000 |  | Delayed replication of 4 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) |
| 0 | 31 | 021 |  | Associated field significance = 7 (Percentage confidence) |
| 0 | 20 | 042 | Optional | Airframe icing (10) (see Note) |
| 2 | 04 | 000 |  | Cancel Add associated field |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 043 | Optional | Peak liquid water content (11) |
| 0 | 20 | 044 | Optional | Average liquid water content (11) |
| 0 | 20 | 045 | Optional | Supercooled water droplet conditions (11) |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 33 | 025 | Optional | ACARS interpolated values (12) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors (13) |
| 0 | 31 | 001 |  | Delayed descriptor replication factor (14) |
| 0 | 11 | 075 | Optional | Intensity (EDR) |
| 0 | 11 | 076 | Optional | Peak (EDR) |
| 0 | 11 | 039 | Optional | Extended time of occurrence of peak EDR (15) |
| 1 | 05 | 000 |  | Delayed replication of 5 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) |
| 0 | 31 | 021 |  | Associated field significance = 7 (Percentage confidence) |
| 0 | 11 | 037 | Optional | Turbulence index (EDR) (see Note) |
| 2 | 04 | 000 |  | Cancel Add associated field |
| 0 | 11 | 077 | Optional | EDR reporting interval (16) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 034 | Optional | Vertical gust velocity (17) |
| 0 | 11 | 035 | Optional | Vertical gust acceleration (17) |
| 0 | 11 | 036 | Optional | Maximum derived equivalent vertical gust speed (17) |

Note:

Each data element is preceded by 7 bits containing the quality information (Percentage confidence).

ANNEX 2:

The documentation contains 2 sections, a down-linked message header and from 1 to 6 message body that contains the actual EDR information. Unlike the previous standard, we have temporal and location information for each individual report.  Currently this information is interpreted. The proposal for AMDAR Turbulence (Eddy Dissipation Rate (EDR)) reporting is for one down-linked message containing the following information:

Message header

| Name of element | unit | range of values | required precision |
| --- | --- | --- | --- |
| Down-link day | day | 0 - 30 | 1 |
| Down-link hour | hour | 0 - 23 | 1 |
| Down-link minute | minute | 0 - 59 | 1 |
| Flight id | character | nnnnnn |  |
| Tail number | character | nnnnnn |  |
| Origination airport | character | nnn |  |
| Destination airport | character | nnn |  |

From 1 to 6 different EDR reports with the following attributes:

| Name of element | unit | range of values | required precision |
| --- | --- | --- | --- |
| Latitude | deg | -90.000 to 90.000 | 0.001 |
| Longitude | deg | -180.000 to 180.000 | 0.001 |
| altitude | ft | 0 to 70000 | 10 |
| Hour | hour | 0 to 23 | 1 |
| minute | minute | 0 to 59 | 1 |
| 10s of seconds | 10s of seconds | 0 to 5 | 1 |
| Algorithm version |  | 0 to 10 | 1 |
| Peak Edr | (m)2/3 per second | 0 to .84 | 0.02 |
| Mean Edr | (m)2/3 per second | 0 to .84 | 0.02 |
| Peak Edr Confidence |  | 0 to 1 | 0.1 |
| Mean Edr Confidence |  | 0 to 1 | 0.1 |
| Running minimum confidence |  | 0 to 1 | 0.1 |
| Running number of bad |  | 0 to 40 | 4 |
| Peak Location |  | 0 to 1 | 0.1 |
| Number of good Edrs |  | 0 to 10 | 1 |
| Static Air Temperature | Deg C | -99.9 to 99.9 | 0.1 |
| wind direction | Degrees | 0 to 359 | 1 |
| wind speed | knots | 0 to 999 | 1 |