| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(13) (3.IX.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Proposed new BUFR Template for Integration of routine Aircraft measurement into a Global Observing System (IAGOS)

Submitted by WMO Secretariat

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the addition of new BUFR Template to be used in the reporting of particulate data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and recommend the proposed modification.

.

References:

[1] Manual on Codes, WMO-No. 306 Volume I.2.

[2] Common Code Tables, BufrCommon-11-2008.doc

- BACKGROUND

The Integration of routine Aircraft measurement into a Global Observing System (IAGOS) is a Design Study for New Infrastructures in the European Commission Sixth Framework Programme (FP6). It pursues the preparation of the distributed infrastructure IAGOS for observations of atmospheric composition, aerosols, clouds and contrails on the global scale from commercial in-service aircraft. Central elements are the aeronautical certification for installation and deployment on Airbus long-range aircraft, the design of new instrumentation for aerosol, cloud particles and for stratospheric water vapour, and the design of real time data provision to meteorological services.

Observations in the Upper Troposphere and Lower Stratosphere are critical for improving the scientific understanding of chemistry-climate interactions, particularly those associated with the roles of clouds, aerosols and chemical composition. This information is essential for improving the scientific basis related to predictions of global climate change and for the assessment of surface air pollution, including the influence of aviation impacts and of emissions from other parts of the world on Europe. 
 	As part of the IAGOS development it was decided that a real-time dissemination of IAGOS observations was required.  Following the WMO WIGOS Pilot Project for AMDAR meeting at KNMI (10-12 February) the IAFGOS team started the development of a new BUFR Template.

- PROPOSAL

###### IAGOS Template for single observation 3 11 011 (Preliminary version):

| TABLE REFERENCES | TABLE ELEMENT NAME | BUFR |
| --- | --- | --- |
|  |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) |
| F | X | Y | F | X | Y |  |  |  |  |  |
| 0 | 01 | 008 |  |  |  | Aircraft registration number or other identification | CCITT IA5 | 0 | 0 | 64 |
| 3 | 11 | 011 | 0 | 01 | 023 | Observation sequence number | Numeric | 0 | 0 | 9 |
|  |  |  | 0 | 08 | 004 | Phase of aircraft flight | Code table | 0 | 0 | 3 |
|  |  |  | 3 | 01 | 011 | Year/Month/Day | Year | 0 | 0 | 22 |
|  |  |  | 3 | 01 | 013 | Hour/Minute/Second | Month | 0 | 0 | 17 |
|  |  |  | 0 | 05 | 002 | Latitude (coarse accuracy), TBC (1) | Degree | 2 | –9000 | 15 |
|  |  |  | 0 | 06 | 002 | Longitude (coarse accuracy) TBC (1) | Degree | 2 | –18000 | 16 |
|  |  |  | 0 | 07 | 004 | Pressure | Pa | –1 | 0 | 14 |
|  |  |  | 0 | 11 | 001 | Wind direction | Degree true | 0 | 0 | 9 |
|  |  |  | 0 | 11 | 002 | Wind speed | m s–1 | 1 | 0 | 12 |
|  |  |  | 0 | 12 | 001 | Temperature/dry-bulb temperature | K | 1 | 0 | 12 |
|  |  |  | 1 | 06 | 000 | Delayed replication of 6 descriptors |  |  |  | 0 |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |  |  |  | 8 |
| H2O or CO2 (3) | 0 | 08 | 046 | (PRE) Atmospheric chemical or physical constituent type (2) | Code Table | 0 | 0 | 16 |
|  |  |  | 2 | 01 | 139 | Increase data width from 9 to 20 |  |  |  | 0 |
|  |  |  | 2 | 02 | 126 | Decrease scale from 9 to 7 |  |  |  | 0 |
|  | 0 | 15 | 026 | Concentration of pollutant | mol mol-1 | 20 | 0 | 20 |
|  |  |  | 2 | 02 | 000 | Cancel change scale |  |  |  | 0 |
|  |  |  | 2 | 01 | 000 | Cancel change data width |  |  |  | 0 |
|  |  |  | 1 | 06 | 000 | Delayed replication of 6 descriptors |  |  |  | 0 |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |  |  |  | 8 |
| O3, CH4, CO, NOx, or NOy (3) | 0 | 08 | 046 | (PRE) Atmospheric chemical or physical constituent type (2) | Code Table | 0 | 0 | 16 |
|  |  |  | 2 | 01 | 138 | Increase data width from 9 to 19 |  |  |  | 0 |
|  |  |  | 2 | 02 | 130 | Increase scale from 9 to 11 |  |  |  | 0 |
|  | 0 | 15 | 026 | Concentration of pollutant | mol mol-1 | 19 | 0 | 19 |
|  |  |  | 2 | 02 | 000 | Cancel change scale |  |  |  | 0 |
|  |  |  | 2 | 01 | 000 | Cancel change data width |  |  |  | 0 |
| (5.1) | 0 | 15 | 052 | Decimal logarithm (Aerosol particle number density, particles of diameter greater than 5 nm) | Numeric | 1 | 60 | 6 |
| (5.1) | 0 | 15 | 053 | Decimal logarithm (Aerosol particle number density, particles of diameter greater than 14 nm) | Numeric | 2 | 600 | 9 |
| (5.1) | 0 | 15 | 054 | Decimal logarithm (Aerosol particle number density, particles of diameter between 0.25 and 2.5 µm) | Numeric | 2 | 550 | 9 |
| (5.2) | 0 | 15 | 055 | non volatile aerosol ratio | Numeric | 2 | 0 | 7 |
|  |  |  | 1 | 01 | 002 | Next descriptor replicated 2 times |  |  |  | 0 |
|  |  |  | 0 | 10 | 004 | Pressure | Pa | –1 | 0 | 14 |
| (5.3) | 0 | 13 | 099 | Decimal logarithm (Cloud particle density in altitude range) | Numeric | 1 | 0 | 7 |
| (5.3) | 0 | 13 | 100 | Decimal logarithm (Columnar cloud particle area in altitude range) | Numeric | 1 | -70 | 7 |
| (5.3) | 0 | 13 | 101 | Decimal logarithm (Columnar cloud particle volume in altitude range) | Numeric | 1 | -140 | 7 |

###### IAGOS Template for an ascent or descent profile 3 11 012 :

| TABLE REFERENCES | TABLE ELEMENT NAME | BUFR |
| --- | --- | --- |
|  |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) |
| F | X | Y | F | X | Y |  |  |  |  |  |
| 3 | 11 | 012 |  |  |  | IAGOS profile report |  |  |  |  |
|  |  |  | 0 | 01 | 008 | Aircraft registration number or other identification (1) | CCITT IA5 | 0 | 0 | 64 |
|  |  |  | 1 | 01 | 000 | Delayed replication of next descriptor |  |  |  | 0 |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |  |  |  | 8 |
|  |  |  | 3 | 11 | 011 | single IAGOS observation |  |  |  | 331-402 (4) |

Note: The new proposed descriptors are identified in red.

  - The “coarse” latitude and longitude have been selected because the Real Time Transmission Unit that is designed for IAGOS aircraft has only the accuracy of 0.01 degree at its disposal. This makes an accuracy of 1.1 km in the horizontal position of the measurement. Real Time users will be asked if this is sufficient. Therefore the use of coarse latitude and longitude will be confirmed.

  - The Code Table C-14 (from Common Code Tables, BufrCommon-11-2008.doc) was used to document the atmospheric constituent type. This table has still to be approved.

  - From the uncertainty range (minimum and maximum value) of the volume mixing ratio of each of the 7 species measured (O3, H20, CH4, CO2, CO, NOx, NOy), we first determined the parameters SCALE, WIDTH, and REF_VALUE separately for each species (see Annex 1). Groups of species were also tried and it was possible to define 2 groups, (H2O, CO2) and (O3, CH4, CO, NOx, NOy) with common SCALE, WIDTH, and REF_VALUE parameters. Two loops were defined in the template, for each of the groups. This has 2 advantages:

- The use of loops with indication in the section 4 of their replication factor allows a variable size of the BUFR report that can be adapted to the different configurations of the IAGOS equipped aircraft. The 5 possible configurations are :

  - C1 : measurements of H2O, O3, CO, cloud droplets only

  - C2 : measurements of H2O, O3, CO, NOx, cloud droplets only

  - C3 : measurements of H2O, O3, CO, NOy, cloud droplets only

  - C4 : measurements of H2O, O3, CO, aerosols, cloud droplets only

  - C5 : measurements of H2O, O3, CO, CO2, CH4, cloud droplets only

- Other species that would accept the same SCALE, WIDTH, and REF_VALUE parameters as those of one of the 2 groups can be added to the BUFR report without change of the template.

The coding for water vapour volume mixing ratio is consistent with an accuracy of 1 ppm, which is not the case for the actual water vapour sensor (currently the accuracy is 5 to 10 % relative humidity). The proposed coding takes into account future evolutions in sensor design. This also applies for other measured chemical parameters.

  - In order to check the tables in this document, a simulation of the contents of section 4 of the BUFR report was done (see Appendix 2). The total size in bits of section 4 is given in the table below:

| IAGOS configurations | Size of (3 11 011) | Size of (3 11 012) (40 levels) | Size for n levels |
| --- | --- | --- | --- |
| C1 or C4 | 395 | 13312 | 72+n*331 |
| C2 or C3 | 430 | 14712 | 72+n*366 |
| C5 | 466 | 16152 | 72+n*402 |

  - It is propose to include 7 new element descriptors for the IAGOAS BUFR Template.

    - Aerosol number densities (in particles/m3) will be measured in 3 size domains. As the range of variation is large and the relative accuracy is limited, we propose to code the logarithm of the number densities (see proposed descriptors 0 15 052 to 054).

    - The ratio of particles that are volatile is measured after heating the air sample (0 15 055).

    - All IAGOS equipped aircraft will measure the size distribution of cloud droplets or ice particles. There are 10 size classes (or size bins) and the measurement is done every 0,1 sec.  Cumulative count of all particles between the current pressure level pi and a pressure level such that pi+1 < pi is done. In the report 3 11 012, levels pi and pi+1 are adjacent. This leads to a vertical column of particles (in unit of particles/m2) for which we propose the element descriptor 0 13 099. The pressure lower and upper limits of the cloud are given by 2 pressure descriptors 0 10 004 named pmax and pmin such that pi ( pmax ( pmin ( pi+1. The layers (pi, pmax) and (pmin, pi+1) are clear sky. The layer (pmax, pmin) is cloudy if pmax > pmin.

Taking advantage of the size distribution measured, we will also provide a total area of the particles present in an atmospheric layer (in unit of m2/m2, without dimension), and a total volume of particles (in unit of m3/m2). All 3 parameters 0 13 099 to 0 13 101 need the 2 descriptors 0 10 004 for the definition of the limits of the vertical column. The 3 cloud parameters will be provided by their logarithm (base 10), which is consistent with a constant relative accuracy in the variation range.

The conversion into a logarithmic scale doesn’t allow to code “clear sky” with zero values of the column of cloud particles. Clear sky between levels pi and  pi+1 is indicated by convention with values of pmax and pmin such that pmax ( pmin. In such a case, the values of the altitude integrated observations of number of particles, total area, and total volume have to be decoded as zero values, even if they are given as “unknown” values. The “unknown” values of these quantities are only relevant in the case where a cloud is indicated with pmax > pmin and the Cloud Probe was not able to perform the correct measurement.

More details are given in document RT_BCP_use.doc.

  - The levels of the vertical atmospheric profiles are determined in flight, either as characteristic levels (for the global set of parameters measured), or as pressure levels. The method is selected with respect to its accuracy. In most cases, the characteristic level method is more efficient. With missing data (instruments not working properly), the pressure level method is more straightforward.

ANNEX 1

Compute BUFR specification

| # |  | specifications | BUFR type specifications | Output specifications |
| --- | --- | --- | --- | --- |
|  |  | absolute uncertainty | Minimum value | Maximum value | SCALE | WIDTH | REF | Deltax | xMin | xMax |
| 8 | CH4 | 1.000E-10 | 1.000E-06 | 2.600E-06 | 10 | 14 | 10000 | 1.000E-10 | 1.000E-06 | 2.638E-06 |
| 9 | CO2 | 1.000E-07 | 3.000E-04 | 2.000E-03 | 7 | 15 | 3000 | 1.000E-07 | 3.000E-04 | 3.577E-03 |
| 10 | aer.vol.ratio | 5.000E-02 | 0.000E+00 | 1.000E+00 | 2 | 7 | 0 | 1.E-02 | 0.000E+00 | 1.260E+00 |
| 11 | O3 | 2.000E-09 | 5.000E-09 | 5.000E-06 | 9 | 13 | 0 | 1.000E-09 | 0.000E+00 | 8.190E-06 |
| 12 | H2O vmr | 1.000E-06 | 3.000E-06 | 6.000E-02 | 6 | 16 | 0 | 1.000E-06 | 0.000E+00 | 6.553E-02 |
| 13 | CO | 2.000E-09 | 4.000E-09 | 1.000E-06 | 9 | 10 | 0 | 1.000E-09 | 0.000E+00 | 1.022E-06 |
| 14 | NOx | 5.000E-11 | 1.000E-11 | 1.000E-07 | 11 | 14 | 0 | 1.000E-11 | 0.000E+00 | 1.638E-07 |
| 15 | NOy | 5.000E-11 | 1.000E-10 | 1.000E-07 | 11 | 14 | 0 | 1.000E-11 | 0.000E+00 | 1.638E-07 |
| 16 | 5nm<D | 5.000E+05 | 1.000E+07 | 1.000E+11 | -5 | 20 | 0 | 1.000E+05 | 0.000E+00 | 1.049E+11 |
|  | log10(16) | 1.250E-01 | 7.000E+00 | 1.100E+01 | 1 | 6 | 60 | 1.000E-01 | 6.000E+00 | 1.220E+01 |
| 17 | 14nm<D | 5.000E+05 | 1.000E+07 | 1.000E+11 | -5 | 20 | 0 | 1.000E+05 | 0.000E+00 | 1.049E+11 |
|  | log10(17) | 7.500E-02 | 7.000E+00 | 1.100E+01 | 2 | 9 | 600 | 1.000E-02 | 6.000E+00 | 1.110E+01 |
| 18 | .25µ<D<2.5µ | 5.000E+04 | 1.000E+06 | 1.000E+10 | -4 | 20 | 0 | 1.000E+04 | 0.000E+00 | 1.049E+10 |
|  | log10(18) | 5.000E-02 | 6.000E+00 | 1.000E+01 | 2 | 9 | 550 | 1.000E-02 | 5.500E+00 | 1.060E+01 |
| 19 | Cloud particle density in altitude range |  | 1.000E+01 | 1.000E+12 |  |  |  |  | 1.000E+00 | 3.981E+12 |
|  | Log10(Cloud particle density in altitude range) | 1.000E-01 | 1.000E+00 | 1.200E+01 | 1 | 7 | 0 | 1.E-01 | 0.000E+00 | 1.260E+01 |
| 20 | Columnar cloud particle area in altitude range |  | 3.00E-07 | 2.50E+02 |  |  |  |  | 1.000E-07 | 3.981E+05 |
|  | Log10(Columnar cloud particle area in altitude range) | 1.000E-01 | -6.523E+00 | 2.398E+00 | 1 | 7 | -70 | 1.E-01 | -7.000E+00 | 5.600E+00 |
| 21 | Columnar cloud particle volume in altitude range |  | 7.500E-12 | 1.180E-04 |  |  |  |  | 1.000E-14 | 3.981E-02 |
|  | Log10(Columnar cloud particle volume in altitude range) | 1.000E-01 | -1.112E+01 | -3.928E+00 | 1 | 7 | -140 | 1.E-01 | -1.400E+01 | -1.400E+00 |
|  | standard chem. species |  |  |  | 9 | 9 | 0 |  |  |  |

Groups

| # |  | specifications | BUFR type specifications | Output specifications |
| --- | --- | --- | --- | --- |
|  |  | absolute uncertainty | Minimum value | Maximum value | SCALE | WIDTH | REF | Deltax | xMin | xMax |
| 8 | CH4 | 1.000E-10 | 1.000E-06 | 2.600E-06 | 10 | 14 | 10000 | 1.000E-10 | 1.000E-06 | 2.638E-06 |
| 9 | CO2 | 1.000E-07 | 3.000E-04 | 2.000E-03 | 7 | 15 | 3000 | 1.000E-07 | 3.000E-04 | 3.577E-03 |
| 11 | O3 | 2.000E-09 | 5.000E-09 | 5.000E-06 | 9 | 13 | 0 | 1.000E-09 | 0.000E+00 | 8.190E-06 |
| 12 | H2O vmr | 1.000E-06 | 3.000E-06 | 6.000E-02 | 6 | 16 | 0 | 1.000E-06 | 0.000E+00 | 6.553E-02 |
| 13 | CO | 2.000E-09 | 4.000E-09 | 1.000E-06 | 9 | 10 | 0 | 1.000E-09 | 0.000E+00 | 1.022E-06 |
| 14 | NOx | 5.000E-11 | 1.000E-11 | 1.000E-07 | 11 | 14 | 0 | 1.000E-11 | 0.000E+00 | 1.638E-07 |
| 15 | NOy | 5.000E-11 | 1.000E-10 | 1.000E-07 | 11 | 14 | 0 | 1.000E-11 | 0.000E+00 | 1.638E-07 |
|  | all species | 5.000E-11 | 1.000E-11 | 6.000E-02 | 11 | 33 | 0 | 1.000E-11 | 0.000E+00 | 8.590E-02 |
|  |  |  |  |  |  |  |  |  | 0.000E+00 | 0.000E+00 |
| 8 | CH4 | 1E-10 | 0.000001 | 0.0000026 | 10 | 14 | 10000 | 1E-10 | 1.000E-06 | 2.638E-06 |
| 9 | CO2 | 1.000E-07 | 3.000E-04 | 2.000E-03 | 7 | 15 | 3000 | 1.000E-07 | 3.000E-04 | 3.577E-03 |
| 11 | O3 | 2E-09 | 5E-09 | 0.000005 | 9 | 13 | 0 | 1E-09 | 0.000E+00 | 8.190E-06 |
| 13 | CO | 2E-09 | 4E-09 | 0.000001 | 9 | 10 | 0 | 1E-09 | 0.000E+00 | 1.022E-06 |
| 14 | NOx | 5E-11 | 1E-11 | 0.0000001 | 11 | 14 | 0 | 1E-11 | 0.000E+00 | 1.638E-07 |
| 15 | NOy | 5E-11 | 1E-10 | 0.0000001 | 11 | 14 | 0 | 1E-11 | 0.000E+00 | 1.638E-07 |
|  | without H2O | 5E-11 | 1E-11 | 0.002 | 11 | 28 | 0 | 1E-11 | 0.000E+00 | 2.684E-03 |
|  |  |  |  |  |  |  |  |  | 0.000E+00 | 0.000E+00 |
|  |  |  |  |  |  |  |  |  | 0.000E+00 | 0.000E+00 |
| 8 | CH4 | 1.000E-10 | 1.000E-06 | 2.600E-06 | 10 | 14 | 10000 | 1.000E-10 | 1.000E-06 | 2.638E-06 |
| 11 | O3 | 2.000E-09 | 5.000E-09 | 5.000E-06 | 9 | 13 | 0 | 1.000E-09 | 0.000E+00 | 8.190E-06 |
| 13 | CO | 2.000E-09 | 4.000E-09 | 1.000E-06 | 9 | 10 | 0 | 1.000E-09 | 0.000E+00 | 1.022E-06 |
| 14 | NOx | 5.000E-11 | 1.000E-11 | 1.000E-07 | 11 | 14 | 0 | 1.000E-11 | 0.000E+00 | 1.638E-07 |
| 15 | NOy | 5.000E-11 | 1.000E-10 | 1.000E-07 | 11 | 14 | 0 | 1.000E-11 | 0.000E+00 | 1.638E-07 |
|  | without(H2O,CO2) | 5.000E-11 | 1.000E-11 | 5.000E-06 | 11 | 19 | 0 | 1.000E-11 | 0.000E+00 | 5.243E-06 |
|  |  |  |  |  |  |  |  |  | 0.000E+00 | 0.000E+00 |
|  |  |  |  |  |  |  |  |  | 0.000E+00 | 0.000E+00 |
| 9 | CO2 | 1.000E-07 | 3.000E-04 | 2.000E-03 | 7 | 15 | 3000 | 1.000E-07 | 3.000E-04 | 3.577E-03 |
| 12 | H2O vmr | 1.000E-06 | 3.000E-06 | 6.000E-02 | 6 | 16 | 0 | 1.000E-06 | 0.000E+00 | 6.553E-02 |
|  | only(H2O,CO2) | 1.000E-07 | 3.000E-06 | 6.000E-02 | 7 | 20 | 0 | 1.000E-07 | 0.000E+00 | 1.049E-01 |

ANNEX 2

Content Simulation

|  |  |  |  |  |  |  | length (bit) | position from start of report | value in BUFR section 4 | comment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | 1st bit | last bit |  |  |
| 0 | 01 | 008 |  |  |  | Aircraft registration number or other identification | 64 | 1 | 64 | "IAGOS01_" | other identification for IAGOS aircraft #01: “IAGOS01_” |
| 3 | 11 | 011 | 0 | 01 | 023 | Observation sequence number | 9 | 65 | 73 |  |  |
|  |  |  | 0 | 08 | 004 | Phase of aircraft flight | 3 | 74 | 76 |  | not the same determination as in AMDAR report. This parameter cannot be used to test the validity of wind observations because aircraft attitude parameters are not available. |
|  |  |  | 3 | 01 | 011 | Year/Month/Day | 0 | 77 | 76 |  |  |
|  |  |  | 0 | 04 | 001 | Year | 12 | 77 | 88 |  |  |
|  |  |  | 0 | 04 | 002 | Month | 4 | 89 | 92 |  |  |
|  |  |  | 0 | 04 | 003 | Day | 6 | 93 | 98 |  |  |
|  |  |  | 3 | 01 | 013 | Hour/Minute/Second | 0 | 99 | 98 |  |  |
|  |  |  | 0 | 04 | 004 | Hour | 5 | 99 | 103 |  |  |
|  |  |  | 0 | 04 | 005 | Minute | 6 | 104 | 109 |  |  |
|  |  |  | 0 | 04 | 006 | Second | 6 | 110 | 115 |  |  |
|  |  |  | 0 | 05 | 002 | Latitude (coarse accuracy) | 15 | 116 | 130 |  |  |
|  |  |  | 0 | 06 | 002 | Longitude (coarse accuracy) | 16 | 131 | 146 |  |  |
|  |  |  | 0 | 07 | 004 | Pressure | 14 | 147 | 160 |  |  |
|  |  |  | 0 | 11 | 001 | Wind direction | 9 | 161 | 169 |  |  |
|  |  |  | 0 | 11 | 002 | Wind speed | 12 | 170 | 181 |  |  |
|  |  |  | 0 | 12 | 001 | Temperature/dry-bulb temperature | 12 | 182 | 193 |  |  |
|  |  |  | 1 | 6 | 0 | Delayed replication of 6 descriptors | 0 | 194 | 193 |  |  |
|  |  |  | 0 | 31 | 1 | Delayed descriptor replication factor | 8 | 194 | 201 | 1 | only H2O present |
|  |  |  | 2 | 1 | 139 | Increase data width from 9 to 20 | 0 | 202 | 201 |  |  |
|  |  |  | 2 | 2 | 126 | Decrease scale from 9 to 7 | 0 | 202 | 201 |  |  |
|  |  |  | 0 | 08 | 046 | (PRE) Atmospheric chemical or physical constituent type | 16 | 202 | 217 | 1 | H2O (AWAITING VALIDATION) COMMON CODE TABLE C-14 |
|  |  |  | 0 | 15 | 026 | Concentration of pollutant (mol mol-1) | 20 | 218 | 237 |  |  |
|  |  |  | 2 | 02 | 000 | Cancel change scale | 0 | 238 | 237 |  |  |
|  |  |  | 2 | 01 | 000 | Cancel change data width | 0 | 238 | 237 |  |  |
|  |  |  | 1 | 6 | 0 | Delayed replication of 6 descriptors | 0 | 238 | 237 |  |  |
|  |  |  | 0 | 31 | 1 | Delayed descriptor replication factor | 8 | 238 | 245 | 2 | only O3 and CO present |
|  |  |  | 2 | 1 | 138 | Increase data width from 9 to 19 | 0 | 246 | 245 |  |  |
|  |  |  | 2 | 2 | 130 | Increase scale from 9 to 11 | 0 | 246 | 245 |  |  |
|  |  |  | 0 | 8 | 46 | (PRE) Atmospheric chemical or physical constituent type (2) | 16 | 246 | 261 | 0 4 | O3 CO |
|  |  |  | 0 | 15 | 26 | Concentration of pollutant | 19 | 262 | 280 |  |  |
|  |  |  | 2 | 2 | 0 | Cancel change scale | 0 | 316 | 315 |  |  |
|  |  |  | 2 | 1 | 0 | Cancel change data width | 0 | 316 | 315 |  |  |
|  |  |  | 0 | 15 | 052 | Decimal logarithm (Aerosol particle number density, particles of diameter greater than 5 nm) | 6 | 316 | 321 |  | element descriptor to be defined |
|  |  |  | 0 | 15 | 053 | Decimal logarithm (Aerosol particle number density, particles of diameter greater than 14 nm) | 9 | 322 | 330 |  | element descriptor to be defined |
|  |  |  | 0 | 15 | 054 | Decimal logarithm (Aerosol particle number density, particles of diameter between 0.25 and 2.5 µm) | 9 | 331 | 339 |  | element descriptor to be defined |
|  |  |  | 0 | 15 | 055 | non volatile aerosol ratio | 7 | 340 | 346 |  | element descriptor to be defined |
|  |  |  | 0 | 10 | 004 | Pressure | 14 | 347 | 360 |  | 1st boundary for the 3 following elements |
|  |  |  | 0 | 10 | 004 | Pressure | 14 | 361 | 374 |  | 2nd boundary for the 3 following elements |
|  |  |  | 0 | 13 | 099 | Decimal logarithm (Cloud particle density in altitude range) | 7 | 375 | 381 |  | element descriptor to be defined |
|  |  |  | 0 | 13 | 100 | Decimal logarithm (Columnar cloud particle area in altitude range) | 7 | 382 | 388 |  | element descriptor to be defined |
|  |  |  | 0 | 13 | 101 | Decimal logarithm (Columnar cloud particle volume in altitude range) | 7 | 389 | 395 |  | element descriptor to be defined |

|  |  |  |  |  |  |  | length (bit) | position from start of report | value in BUFR section 4 | comment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | 1st bit | last bit |  |  |
| 3 | 11 | 012 |  |  |  | IAGOS profile report |  |  |  |  |  |
|  |  |  | 0 | 01 | 008 | Aircraft registration number or other identification (1) | 64 | 1 | 64 | "IAGOS01_" |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of next descriptor | 0 | 65 | 64 |  |  |
|  |  |  | 0 | 31 | 1 | Delayed descriptor replication factor | 8 | 65 | 72 | 40 | a complete profile has between nobs=35 and 50 observations |
|  |  |  | 3 | 11 | 011 | single IAGOS observation | 331 | 73 | 13312 |  | in case where nobs=40, total size of section 4 of IAGOS report is 64+8+331*40=13312 bits |