| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(14) (11.IX.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Additional descriptors for AMDAR data and

BUFR Template for AMDAR, version 3

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for the additional BUFR descriptors needed for representation of EDR reporting in BUFR, and the BUFR Template modified according to these requirements.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and recommend the proposed descriptors and template for validation.

References:

[1]	Manual on Codes, WMO-No. 306, Volume I.2; and

[2]		Development of a BUFR Template for AMDAR, WIGOS-PP-AMDAR-2/Doc. 3.1, 
De Bilt, The Netherlands, 2009.

[3]	WIGOS Pilot Project for AMDAR “To Enhance Delivery of Aeronautical Data from AMDAR Platforms to Users”/Doc 3.1.3 De Bilt, The Netherlands, 2009

[4]	Final Report WMO Integrated Observing System (WIGOS) Pilot Project for AMDAR Second Session (De Bilt, The Netherlands 10-12 February 2009)

[5]    Proposal for Standardized BUFR Template for AMDAR, Doc. 3.3(12), IPET-DRC-I,

Geneva, 15 to 18 September 2009

- BACKGROUND

Document Doc. 3.3(12) “Proposal for Standardized BUFR Template for AMDAR” was submitted for the IPET-DRC-I (Geneva, 15 to 18 September 2009) on 3 September 2009 [5].

Annex II in Doc. 3.3(12) contains requirements of the USA AMDAR Programme that had been express only very recently and therefore could not be reflected in the Standardized BUFR Template for AMDAR 3 11 010 version 2 in [5]. Moreover, 0 10 096 that was proposed for the new required entry GNSS Altitude in [5], is already used for Mean dynamic topography. And with introduction of 0 07 004 (Pressure) as the vertical coordinate, the Note (5) to template 3 11 010, version 2, requires corresponding modification. Also some editorial changes are to be introduced (all modifications are written in blue in this document).

- BUFR TEMPLATE FOR AMDAR, 3 11 010, version 3

| 0 | 01 | 008 |  | Aircraft identification (1) |
| --- | --- | --- | --- | --- |
| 0 | 01 | 023 | Optional | Sequence number (2) |
| 0 | 01 | 100 | Optional | Flight number (3) (4) |
| 0 | 01 | 110 | Optional | Aircraft tail number (4) (19) |
| 0 | 01 | 111 | Optional | Origination airport (4) (19) |
| 0 | 01 | 112 | Optional | Destination airport (4) (19) |
| 3 | 01 | 011 |  | Year, month and day |
| 3 | 01 | 013 |  | Hour, minute and second |
| 3 | 01 | 021 |  | Latitude and longitude (high accuracy) |
| 0 | 07 | 010 |  | Flight level (5) |
| 0 | 07 | 004 |  | Pressure (5) |
| 0 | 10 | 053 |  | GNSS Altitude (4) |
| 0 | 08 | 009 |  | Detailed phase of flight (6) |
| 0 | 11 | 001 |  | Wind direction |
| 0 | 11 | 002 |  | Wind speed |
| 0 | 02 | 064 |  | Aircraft roll angle quality |
| 0 | 11 | 100 | Optional | True aircraft speed (7) |
| 0 | 11 | 101 | Optional | Aircraft ground velocity (u-component) (4) |
| 0 | 11 | 102 | Optional | Aircraft ground velocity (v-component) (4) |
| 0 | 11 | 103 | Optional | Aircraft ground velocity (w-component) (4) |
| 0 | 11 | 104 | Optional | Aircraft true heading (4) |
| 0 | 12 | 101 |  | Air Temperature (8) |
| 0 | 13 | 002 |  | Mixing ratio |
| 0 | 13 | 003 |  | Relative humidity |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 12 | 103 | Optional | Dew-point temperature (9) |
| 0 | 33 | 026 |  | Moisture quality |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 042 | Optional | Airframe icing (10) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 043 | Optional | Peak liquid water content (11) |
| 0 | 20 | 044 | Optional | Average liquid water content (11) |
| 0 | 20 | 045 | Optional | Supercooled large droplet (SLD) conditions (11) |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 33 | 025 | Optional | ACARS interpolated values indicator (12) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors (13) |
| 0 | 31 | 001 |  | Delayed descriptor replication factor (14) |
| 0 | 11 | 075 | Optional | Mean turbulence intensity (EDR) |
| 0 | 11 | 076 | Optional | Peak turbulence intensity (EDR) |
| 0 | 11 | 039 | Optional | Extended time of occurrence of peak EDR (15) |
| 1 | 02 | 000 |  | Delayed replication of 2 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 037 | Optional | Turbulence index (EDR) |
| 0 | 11 | 077 | Optional | Reporting interval or averaging time for EDR (16) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 034 | Optional | Vertical gust velocity (17) |
| 0 | 11 | 035 | Optional | Vertical gust acceleration (17) |
| 0 | 11 | 036 | Optional | Maximum derived equivalent vertical gust speed (17) |
| 0 | 33 | 079 |  | AMDAR quality information (18) (4) |
| 1 | 17 | 000 |  | Delayed replication of 17 descriptors (19) |
| 0 | 31 | 001 |  | Delayed descriptor replication factor (19) |
| 3 | 01 | 021 | Optional | Latitude and longitude (high accuracy) |
| 0 | 07 | 007 | Optional | Height |
| 3 | 01 | 013 | Optional | Hour, minute and second |
| 0 | 11 | 105 | Optional | EDR algorithm version (4) |
| 0 | 11 | 076 | Optional | Peak turbulence intensity (EDR) |
| 0 | 11 | 075 | Optional | Mean turbulence intensity (EDR) |
| 0 | 11 | 106 | Optional | Peak EDR confidence (4) |
| 0 | 11 | 107 | Optional | Mean EDR confidence (4) |
| 0 | 11 | 108 | Optional | Running minimum confidence (4) |
| 0 | 11 | 109 | Optional | Running number of bad (4) |
| 0 | 11 | 110 | Optional | Peak Location (4) |
| 0 | 11 | 111 | Optional | Number of good EDR (4) |
| 0 | 12 | 101 | Optional | Air temperature |
| 0 | 11 | 001 | Optional | Wind direction |
| 2 | 01 | 130 | Optional | Change data width |
| 0 | 11 | 084 | Optional | Wind speed |
| 2 | 01 | 000 | Optional | Cancel change data width |

Table 1. Standardized BUFR Template for AMDAR 3 11 010 version 3.

Notes for Standardized BUFR Template for AMDAR data 3 11 010, version 3:

- Aircraft identifier 0 01 008 can cope with ASDAR, ADS and other AMDAR identities. ADS reports use a 24-bit ICAO airframe identifier, equating to an 8-character BCD number. Look at developing a standard naming convention for the various AMDAR regions and/or programmes. The meeting agreed that additional information such aircraft type and navigation systems would be part of the Meta data, not part of the Standardized BUFR Template for AMDAR. It was noted that AMDAR Meta data would be addressed by the WIGOS Pilot Project for AMDAR.

- The sequence number is a simple observation count to be included in the down-linked message.  It should be reset at 0000 UTC each day and can be useful for quality control, data management and archiving purposes. The meeting has made the recommendation that if this parameter is not used by an operational AMDAR programme or NWP Centre then this parameter be removed from the new Standardized BUFR Template for AMDAR.

- 0 01 100 (Flight number) has been introduced as an optional entry to provide information on the departure airport and the expected arrivals airport. This element will assist with the quality control of aircraft track data, by providing information on the route the aircraft is expected to take.

- Refer to Table 2 for the required BUFR and CREX descriptors for the new elements, including the units, scale, reference value and data width.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 01 100 | Flight number | CCITT IA5 | 0 | 0 | 64 | character | 0 | 8 |
| 0 11 100 | True aircraft speed | m s-1 | 1 | 0 | 12 | m s-1 | 1 | 4 |
| 0 11 101 | Aircraft velocity u-component | m s-1 | 1 | –4096 | 13 | m s-1 | 1 | 4 |
| 0 11 102 | Aircraft velocity v-component | m s-1 | 1 | –4096 | 13 | m s-1 | 1 | 4 |
| 0 11 103 | Aircraft velocity w-component | m s-1 | 1 | –512 | 10 | m s-1 | 1 | 4 |
| 0 11 104 | Aircraft true heading | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| 0 33 079 | AMDAR quality information | Flag table | 0 | 0 | 24 | Flag table | 0 | 8 |
| 0 10 053 | Global Navigation Satellite System Altitude | m | 0 | 1000 | 17 | m | 0 | 5 |
| 0 01 110 | Aircraft tail number | CCITT IA5 | 0 | 0 | 48 | character | 0 | 6 |
| 0 01 111 | Origination airport | CCITT IA5 | 0 | 0 | 24 | character | 0 | 3 |
| 0 01 112 | Destination airport | CCITT IA5 | 0 | 0 | 24 | character | 0 | 3 |
| 0 11 105 | EDR algorithm version | numeric | 0 | 0 | 6 | numeric | 0 | 2 |
| 0 11 106 | Peak EDR confidence | numeric | 1 | 0 | 4 | numeric | 1 | 2 |
| 0 11 107 | Mean EDR confidence | numeric | 1 | 0 | 4 | numeric | 1 | 2 |
| 0 11 108 | Running minimum confidence | numeric | 1 | 0 | 4 | numeric | 1 | 2 |
| 0 11 109 | Running number of bad | numeric | 0 | 0 | 5 | numeric | 0 | 2 |
| 0 11 110 | Peak Location | numeric | 1 | 0 | 4 | numeric | 1 | 2 |
| 0 11 111 | Number of good EDR | numeric | 0 | 0 | 4 | numeric | 0 | 2 |

Table 2. Proposal for new AMDAR descriptors in 3 11 010, version 3

For Table 2, AMDAR descriptors, the data width for Flight number, 0 01 100, will be dependant on the expected length of the flight number, e.g. AF5097, BA2736, LH3700. To properly define the expected data width an accurate estimate of the number characters used in generating a flight number will be required. Presently 8 characters has been used as an estimate as the maximum length for any given flight number.

- The AMDAR Science and Technical Sub-Group requested that Flight level (0 07 010) be replaced with static pressure (0 07 004) as this value is primarily there before any altitude value is calculated by the aircrafts on-board algorithms. Only the left-over of the so-called built-in error remain any other effect of calculation methods, rounding, or formatting are avoided. For any meteorological application of the AMDAR data the pressure value is needed but not the flight level.

- This phase of flight table is expanded to indicate wind quality from roll angle, or roll and pitch combined and also to indicate the method of ascent and descent observation interval selection either by time or pressure increments. The meeting agreed that the Phase of flight 0 08 004 would not be included in the new Standardized BUFR Template for AMDAR as the required level of detail has been incorporated in the detailed phase of flight 0 08 009. The meeting also discussed whether there is a requirement for adding a new condition to the detailed phase of flight 0 08 009 that would cover an aircraft being placed in a holding pattern.

- Refer to AMDAR Reference Manual for definition.

- This parameter has been renamed Air Temperature.

- 0 12 103 Dew-point temperature had been introduced in the templates for AMDAR profile data to simulate radiosonding data.

- The old ACARS airframe icing code table 0 20 041 is not included.

- A special automatic icing report, including these elements, is expected to become available from some aircraft and a down-link code has been published.

- 0 33 025 ACARS interpolated values was primarily used in the USA AMDAR Programme to indicate time and position being reported or interpolated. The name for this element has been changed to ACARS interpolated values indicator.

- Delayed replication 1 03 000 refers to the following three descriptors 0 11 075, 0 11 076 and 0 11 039 to allow reporting of the Extended time of occurrence of peak EDR of all included values of 0 11 076 (Peak (EDR)). This allows each turbulence peak to be reported.

Explanatory remarks to Note (13):

According to Note (14), up to ten values of 0 11 076 (Peak (EDR)) may be reported.  However, 0 11 039 (Extended time of occurrence of peak EDR) was included only once in the template 3 11 010, version 0.  Therefore, it was not clear to which out of those ten values of 0 11 076, the time specification 0 11 039 referred.  If it had been the maximum value, the name of 0 11 039 should have been modified to read “Extended time of occurrence of maximum peak EDR”.  If the time information on all the reported values of 0 11 076 (Peak (EDR)) is required, then 0 11 039 (Extended time of occurrence of peak EDR) should be included under the delayed replication as shown in the proposed template 3 11 010, version 3.

Moreover, 0 11 039 is a code table, allowing to represent one-minute interval of the peak occurrence, e.g., code figure 5 means that the peak occurred between 5 and 6 minutes prior to observation time.  This information may be expressed in much better and more flexible way by inclusion of 0 08 021 (Time significance) and two consecutive entries 0 04 025 (time period or displacement in minutes). E.g. 0 04 025 = -6 and 0 04 025 = -5 specify interval of the peak occurrence between 5 and 6 minutes prior to the observation time (not shown in the proposed template).

- Some aircraft report up to 10 pairs of (EDR) values per observation.  The corresponding times and position could be found by interpolation from the previous report. If the aircraft does not report it the number of replication 0 31 001 is set to zero.

- 0 11 039 allows observation intervals up to one hour.  0 11 038 allows up to 15 minutes only whereas observation intervals of 30 minutes or more are commonly used, hence 0 11 038 had been replaced by 0 11 039.

- The EDR observing interval and associated averaging time differs according to individual observing schedule and cannot be assumed to be identical to the observation interval for the main elements.  It is desirable to include this information in the coded data.

- Vertical gust velocity 0 11 034, Vertical gust acceleration 0 11 035 and Maximum derived equivalent vertical gust speed 0 11 036 have been added to meet the request for reflecting all entries of 3 11 004 in the Standardized BUFR template for AMDAR. The current ICAO standard for automated turbulence reporting is EDR.

- Refer to Table 3 for detail definition of 0 33 079 AMDAR quality information.

| Bit No. |  |
| --- | --- |
| 1 | Date suspected |
| 2 | Hour suspected |
| 3 | Minute suspected |
| 4 | Latitude suspected |
| 5 | Longitude suspected |
| 6 | Flight level suspected |
| 7 | Wind direction suspected |
| 8 | Wind speed suspected |
| 9 | Air temperature suspected |
| 10 | Relative humidity suspected |
| 11 | Mixing ratio suspected |
| 12 | Turbulence index suspected |
| 13 | Airframe icing suspected |
| 14-23 | Reserved |
| All 24 | Missing value |

Table 3. 0 33 079 AMDAR quality information

- Up to 6 EDR reports is requested by the USA AMDAR Programme. If the aircraft does not report it the number of replication 0 31 001 is set to zero.