| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(15) (10.IX.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX – ADDITIONS AND MODIFICATIONS

Updates to BUFR tables in support of the exchange of satellite data

Submitted by Simon Elliott (EUMETSAT)

________________________________________________________________

Summary and Purpose of Document

This document proposes a number of changes to BUFR Tables B and D and the associated code tables in order to support the encoding of meteorological products derived from data from METEOSAT, JASON-2 and METOP satellites.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the submitted proposal and to consider the possible allocation of the requested code table and descriptor entries.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

Discussion

#### 1. Background

A number of updates to the requirements for the representation of satellite products from EUMETSAT in BUFR have arisen since the 2008 Meeting of the Expert on Data Representation and Codes in Geneva.  These requirements are collected in this document, which will also be discussed by the CGMS Task Force on Satellite Data and Codes during its virtual meeting on 14 September 2009.

2. Revised templates for the exchange of JASON-2 OGDR data

The Tables D sequence descriptor 3-40-005 has been defined for the representation of OGDR data from JASON-2.  This sequence has a preoperational status and is being used by NOAA and EUMETSAT to exchange data operationally on the GTS and via satellite dissemination.

Since the inception of this sequence descriptor, there have been a number of improvements in the ground segment near-real-time processor used to derive the OGDR products.  These improvements have led to more parameters being derived, which in turn means that a new BUFR encoding sequence is required.

The following sequence (based heavily on the existing 3-40-005 sequence) is proposed (new entries are in italics and underlined):

Sequence descriptor: 3-40-010 – JASON-2 OGDR data

| BUFR | Description | Unit | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
| F X Y | Satellite |  |  |  |  |
| 0 01 007 | SATELLITE IDENTIFIER |  |  |  |  |
| 0 02 019 | SATELLITE INSTRUMENTS |  |  |  |  |
| 0 01 096 | ACQUISITION STATION IDENTIFIER |  |  |  |  |
| 0 25 061 | SOFTWARE IDENTIFICATION |  |  |  |  |
| 0 05 044 | SATELLITE CYCLE NUMBER |  |  |  |  |
| 0 05 040 | ORBIT NUMBER |  |  |  |  |
| 0 01 030 | NUMERICAL MODEL IDENTIFIER |  |  |  |  |
|  | Datation |  |  |  |  |
| 0 04 001 | YEAR |  |  |  |  |
| 0 04 002 | MONTH |  |  |  |  |
| 0 04 003 | DAY |  |  |  |  |
| 0 04 004 | HOUR |  |  |  |  |
| 0 04 005 | MINUTE |  |  |  |  |
| 0 04 007 | SECONDS WITHIN A MINUTE |  |  |  |  |
|  | Location and Surface Type |  |  |  |  |
| 0 05 001 | LATITUDE (HIGH ACCURACY) |  |  |  |  |
| 0 06 001 | LONGITUDE (HIGH ACCURACY) |  |  |  |  |
| 0 08 029 | REMOTELY SENSED SURFACE TYPE |  |  |  |  |
| 0 08 074 | ALTIMETER ECHO TYPE |  |  |  |  |
| 0 08 077 | RADIOMETER SENSED SURFACE TYPE |  |  |  |  |
|  | Flags |  |  |  |  |
| 0 40 011 | INTERPOLATION FLAG |  |  |  |  |
| 0 25 097 | THREE DIMENSIONAL ERROR ESTIMATE OF THE NAVIGATOR ORBIT |  |  |  |  |
| 0 25 095 | ALTIMETER STATE FLAG |  |  |  |  |
| 0 25 098 | ALTIMETER DATA QUALITY FLAG |  |  |  |  |
| 0 25 099 | ALTIMETER CORRECTION QUALITY FLAG |  |  |  |  |
| 0 21 144 | ALTIMETER RAIN FLAG |  |  |  |  |
| 0 25 096 | RADIOMETER STATE FLAG |  |  |  |  |
| 0 40 012 | RADIOMETER DATA QUALITY FLAG |  |  |  |  |
| 0 40 013 | RADIOMETER BRIGHTNESS TEMPERATURE INTERPRETATION FLAG |  |  |  |  |
| 0 21 169 | ICE PRESENCE INDICATOR |  |  |  |  |
| 0 40 023 | AUXILIARY ALTIMETER STATE FLAGS | FLAG TABLE | 0 | 0 | 5 |
| 0 40 024 | METEOROLOGICAL MAP AVAILABILITY | CODE TABLE | 0 | 0 | 3 |
| 0 40 025 | INTERPOLATION FLAG FOR MEAN DIURNAL TIDE | CODE TABLE | 0 | 0 | 2 |
|  | Altimeter: Ku Band |  |  |  |  |
| 0 22 151 | KU BAND OCEAN RANGE |  |  |  |  |
| 0 22 162 | RMS OF 20 Hz KU BAND OCEAN RANGE |  |  |  |  |
| 0 22 163 | NUMBER OF 20Hz VALID POINTS FOR KU BAND |  |  |  |  |
| 0 25 160 | KU BAND NET INSTRUMENTAL CORRECTION |  |  |  |  |
| 0 25 133 | SEA STATE BIAS CORRECTION ON KU BAND |  |  |  |  |
| 0 22 156 | KU BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 164 | RMS 20 HZ KU BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 165 | NUMBER OF 20HZ VALID POINTS FOR KU BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 166 | KU BAND NET INSTRUMENTAL CORRECTION FOR SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 21 137 | KU BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 21 138 | STD KU BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 22 167 | NUMBER OF VALID POINTS FOR KU BAND BACKSCATTER |  |  |  |  |
| 0 21 139 | KU BAND NET INSTRUMENTAL CORRECTION FOR AGC |  |  |  |  |
| 0 21 118 | ATTENUATION CORRECTION ON SIGMA-0 |  |  |  |  |
| 0 21 145 | KU BAND AUTOMATIC GAIN CONTROL |  |  |  |  |
| 0 21 146 | RMS KU BAND AUTOMATIC GAIN CONTROL |  |  |  |  |
| 0 21 147 | NUMBER OF VALID POINTS FOR KU BAND AUTOMATIC GAIN CONTROL |  |  |  |  |
|  | Altimeter: C band |  |  |  |  |
| 0 22 168 | C BAND OCEAN RANGE |  |  |  |  |
| 0 22 169 | RMS OF C BAND OCEAN RANGE |  |  |  |  |
| 0 22 170 | NUMBER OF 20Hz VALID POINTS FOR C BAND |  |  |  |  |
| 0 25 161 | C BAND NET INSTRUMENTAL CORRECTION |  |  |  |  |
| 0 25 162 | SEA STATE BIAS CORRECTION ON C BAND |  |  |  |  |
| 0 22 171 | C BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 172 | RMS 20HZ C BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 173 | NUMBER OF 20HZ VALID POINTS FOR C BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 174 | C BAND NET INSTRUMENTAL CORRECTION FOR SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 21 170 | C BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 21 171 | RMS C BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 22 175 | NUMBER OF VALID POINTS FOR C BAND BACKSCATTER |  |  |  |  |
| 0 21 172 | C BAND NET INSTRUMENTAL CORRECTION FOR AGC |  |  |  |  |
| 0 21 118 | ATTENUATION CORRECTION ON SIGMA-0 |  |  |  |  |
| 0 21 173 | C BAND AUTOMATIC GAIN CONTROL |  |  |  |  |
| 0 21 174 | RMS C BAND AUTOMATIC GAIN CONTROL |  |  |  |  |
| 0 21 175 | NUMBER OF VALID POINTS FOR C BAND AUTOMATIC GAIN CONTROL |  |  |  |  |
|  | Radiometer |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 13 090 | RADIOMETER WATER VAPOR CONTENT |  |  |  |  |
| 0 13 091 | RADIOMETER LIQUID CONTENT |  |  |  |  |
|  | Wind |  |  |  |  |
| 0 07 002 | HEIGHT OR ALTITUDE |  |  |  |  |
| 0 11 097 | WIND SPEED FROM ALTIMETER |  |  |  |  |
| 0 11 098 | WIND SPEED FROM RADIOMETER |  |  |  |  |
| 0 07 002 | HEIGHT OR ALTITUDE |  |  |  |  |
| 0 11 095 | U COMPONENT OF THE MODEL WIND VECTOR |  |  |  |  |
| 0 11 096 | V COMPONENT OF THE MODEL WIND VECTOR |  |  |  |  |
|  | Dynamic Topography |  |  |  |  |
| 0 10 096 | MEAN DYNAMIC TOPOGRAPHY |  |  |  |  |
| 0 10 081 | ALTITUDE OF COG ABOVE REFERENCE ELLIPSOID |  |  |  |  |
| 0 10 082 | INSTANTANEOUS ALTITUDE RATE |  |  |  |  |
| 0 10 083 | OFF NADIR ANGLE OF THE SATELLITE FROM PLATFORM DATA |  |  |  |  |
| 0 10 101 | SQUARED OFF NADIR ANGLE OF THE SATELLITE FROM WAVEFORM DATA |  |  |  |  |
| 0 25 132 | IONOSPHERIC CORRECTION FROM MODEL ON KU BAND |  |  |  |  |
| 0 25 163 | ALTIMETER IONOSPHERIC CORRECTION ON KU BAND |  |  |  |  |
| 025 126 | MODEL DRY TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 25 128 | MODEL WET TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 25 164 | RADIOMETER WET TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 10 085 | MEAN SEA SURFACE HEIGHT |  |  |  |  |
| 0 10 097 | MEAN SEA SURFACE HEIGHT FROM ALTIMETER ONLY |  |  |  |  |
| 0 10 086 | GEOID'S HEIGHT |  |  |  |  |
| 0 10 087 | OCEAN DEPTH/LAND ELEVATION |  |  |  |  |
| 0 10 092 | SOLID EARTH TIDE HEIGHT |  |  |  |  |
| 0 10 088 | GEOCENTRIC OCEAN TIDE HEIGHT SOLUTION 1 |  |  |  |  |
| 0 10 089 | GEOCENTRIC OCEAN TIDE HEIGHT SOLUTION 2 |  |  |  |  |
| 0 10 098 | LOADING TIDE HEIGHT GEOCENTRIC OCEAN TIDE SOLUTION 1 |  |  |  |  |
| 0 10 099 | LOADING TIDE HEIGHT GEOCENTRIC OCEAN TIDE SOLUTION 2 |  |  |  |  |
| 0 10 090 | LONG PERIOD TIDE HEIGHT |  |  |  |  |
| 0 10 100 | N0N-EQUILIBRIUM LONG PERIOD TIDE HEIGHT |  |  |  |  |
| 0 10 093 | GEOCENTRIC POLE TIDE HEIGHT |  |  |  |  |
| 0 25 127 | SEA SURFACE HEIGHT CORRECTION DUE TO PRESSURE LOADING |  |  |  |  |
| 0 40 014 | HIGH FREQUENCY FLUCTUATIONS OF THE SEA SURFACE TOPOGRAPHY CORRECTION |  |  |  |  |
| 0 10 102 | SEA SURFACE HEIGHT ANOMOLY | M | 3 | -32768 | 16 |

Proposal for code and flag tables

0 40 023

# Auxiliary altimeter state flags

| Bit number |  |
| --- | --- |
| 1 | Band sequence ( 0 = 3Ku_1C_3Ku, 1 = 2Ku_1C_2Ku |
| 2 | C band frequency (0 = 320 MHz, 1 = 100 MHz) |
| 3 | C band status (0 = On, 1 = Off) |
| 4 | Ku band status (0 = On, 1 = Off) |
| All 5 bits | Missing |

0 40 024

# Meteorological map availability

| Code figure |  |
| --- | --- |
| 0 | 2 maps available (6 hours apart) |
| 1 | 2 maps available (> 6 hours apart) |
| 2 | 1 map available; data extrapolated |
| 3 | No maps used |
| 4 to 6 | Reserved |
| 7 | Missing value |

0 40 025

# Interpolation flag for mean diurnal tide

| Code figure |  |
| --- | --- |
| 0 | Good |
| 1 | Bad |
| 2 | Reserved |
| 3 | Missing value |

It is further proposed that a note is added to Table D, Class 40, recommending that 3-40-010 is to be used in preference to 3-40-005.

3. Proposals for refinement of IASI data encoding arising from validation activities

At the 2008 Meeting of the Expert Team on Data Representation and Codes in Geneva (Docs 3-3-5(1) and 3-3-5(2)), the following three sequences related to IASI data were proposed for validation:

3-40-006 – “IASI principal component scores”

3-40-007 – “IASI Level 1c data (all channels)”

3-40-008 – “IASI Level 1c data (subset of channels)”

After one year of validation activities it has been possible to refine these sequences somewhat.  As a result of this validation, it is proposed to:

- Add a section to the 3-40-008 sequence for the inclusion of principal component scores with selected channels

- Deprecate the sequence 3-40-006 originally intended for the representation of IASI principal component scores

- Add to sequence 3-40-008 a database identification (0-25-062) descriptor for the specification of eingenvalue data sets used for the principal component analysis

- Correct the proposed definition of 0-40-016  (Residual RMS in band) to be: numeric, scale 3, offset 0, width 14 bits

The updated sequence for 3-40-008 is given below:

IASI sequence combining PC scores, channel selection and enhanced data (to be 3-40-008)

|  | Satellite processing information |
| --- | --- |
| 0-01-007 | Satellite identifier |
| 0-01-031 | Identification of originating/generating centre |
| 0-02-019 | Satellite instruments |
| 0-02-020 | Satellite classification |
|  | Date and time |
| 0-04-001 | Year |
| 0-04-002 | Month |
| 0-04-003 | Day |
| 0-04-004 | Hour |
| 0-04-005 | Minute |
| 2-02-131 | Add 3 to scale |
| 2-01-138 | Add 10 to width |
| 0-04-006 | Second |
| 2-01-000 | Reset width |
| 2-02-000 | Reset scale |
|  | Location information |
| 0-05-001 | Latitude (high accuracy) |
| 0-06-001 | Longitude (high accuracy) |
| 0-07-024 | Satellite zenith angle |
| 0-05-021 | Bearing or azimuth |
| 0-07-025 | Solar zenith angle |
| 0-05-022 | Solar azimuth |
| 0-05-043 | Field of view number |
| 0-05-040 | Orbit number |
| 2-01-133 | Add 5 to width |
| 0-05-041 | Scan line number |
| 2-01-000 | Reset width |
| 2-01-132 | Add 4 to width |
| 0-25-070 | Major frame count |
| 2-01-000 | Reset width |
| 2-02-126 | Subtract 2 from scale |
| 0-07-001 | Height of station |
| 2-02-000 | Reset scale |
|  | Quality information |
| 1-03-003 | Repeat next 3 descriptor 3 times |
| 0-25-140 | Start channel |
| 0-25-141 | End channel |
| 0-33-060 | GQisFlagQual |
| 0-33-061 | QGisQualIndex |
| 0-33-062 | QGisQualIndexLoc |
| 0-33-063 | QGisQualIndexRad |
| 0-33-064 | QGisQualIndexSpect |
| 0-33-065 | GQisSysTecSondQual |
| 0-40-020 | GQisFlagQualDetailed - Quality flag for the system |
|  | IASI subset of channels |
| 1-01-010 | Repeat next 1 descriptor 10 times |
| 3-40-002 | IASI Level 1c band description |
| 1-04-000 | Delayed replication of next 4 descriptors |
| 0-31-002 | Extended delayed replication factor |
| 2-01-136 | Add 8 to width |
| 0-05-042 | Channel number |
| 2-01-000 | Reset width |
| 0-14-046 | Scaled IASI radiance |
|  | Instrument band definition |
| 1-08-003 | Repeat next 8 descriptors 3 times |
| 0-25-140 | Start channel |
| 0-25-141 | End channel |
| 0-40-015 | Quantization factor |
| 0-40-016 | Residual RMS in band |
| 0-25-062 | Database indentification |
|  | Principal component scores for band |
| 1-01-000 | Delayed replication of one descriptor |
| 0-31-002 | Extended delayed replication factor |
| 0-40-017 | Non-normalised principal component score |
|  | AVHRR scene analysis |
| 0-02-019 | Satellite instruments |
| 0-25-051 | AVHRR channel combination |
| 1-01-007 | Repeat next 1 descriptor 7 times |
| 3-40-004 | IASI Level 1c AVHRR single scene sequence |
| 0-20-081 | Cloud amount in segment |
| 0-08-029 | Remotely sensed surface type |
| 0-20-083 | Amount of segment covered by scene |
| 0-08-029 | Remotely sensed surface type |
| 0-40-018 | Average of imager measurements |
| 0-40-019 | Variance of imager measurements |
| 0-40-021 | Fraction of weighted AVHRR pixel in IASI FOV covered with snow/ice |
| 0-40-022 | Number of missing, bad or failed AVHRR pixels |

4. Proposal for a normalised differential vegetation index (NDVI) sequence

At the request of some of its users, EUMETSAT has introduced a normalized differential vegetation index (NDVI) product.  This product is derived from the AVHRR instrument on METOP.  These data are being encoded in BUFR and disseminated to ECMWF using the RMDCN.

The NDVI product also includes information about illumination (day/twilight/night), land/coast/sea identification and a cloud mask.  In order to encode the data without having to use local descriptors, it is proposed to add the following (new entries in italics and underlined):

Sequence descriptor: 3-40-009 – Normalised differential vegetation index (NDVI)

0-01-007	Satellite identifier

0-01-031	Generating centre

0-02-019	Satellite instrument

0-02-020	Satellite classification

3-01-011	Date

3-01-013	Time

0-05-040	Orbit number

2-01-136	Add 8 bits to width of next descriptor

0-05-041	Scan linen umber

2-01-000	Reset descriptor width

0-25-071	Frame count

0-05-001	Latitude (high accuracy)

0-05-001	Latitude (high accuracy)

0-06-001	Longitude (high accuracy)

0-06-001	Longitude (high accuracy)

1-07-064	Repeat next 7 descriptors 64 times

1-06-032 	Repeat next 6 descriptors 32 times

0-08-012	Land/sea qualifier

0-08-013	Day/night qualifier

0-08-065	Sun-glint indicator

0-08-072	Pixel(s) type

0-13-039	Terrain type (ice/snow)

0-40-015	Normalised differential vegetation index (NDVI)

Element descriptor:

Table B entry:	0-40-015

Name:		Normalised differential vegetation index (NDVI)

Units:		Numeric

Scale:		2

Reference:	-100

Width:		8

The NDVI values can (theoretically) range from -1 to 1.

The proposed descriptor allows values from -1.00 to 1.54, with a precision of 0.01.

5. Proposed addition of code table entry for twilight

In order to be able to distinguish twilight conditions from day and night, it is proposed to make use of currently reserved value in the code table for descriptor 0-08-013 (Day/night qualifier).

The current definition of the code table is:

0-08-013	Day/Night qualifier

Code Figure

0 		Night

1 		Day

2 		Reserved

3 		Missing value

It is proposed to update this to be as follows:

0-08-013	Day/Night qualifier

Code Figure

0 		Night

1 		Day

2 		Twilight

3 		Missing value

6. Conclusion

The meeting is invited to consider the proposed new BUFR descriptors and code table entries, and to endorse their addition to the existing tables.