| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(3) (4.IX.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

BUFR descriptors required by Recommendation 6.1/2 (CBS-XIV)

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains analysis of the requirements in Recommendation 6.1/2 (CBS-XIV) for representation of the listed variables in BUFR and a proposal for new BUFR-CREX descriptors required in the Recommendation.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and to recommend the included proposals.

References:

[1]  Manual on Codes, WMO-No. 306, Volume I.2.

[2]  Draft Recommendation 6.1/2 (CBS-XIV), Commission for Basic Systems, Fourteenth

Session, Dubrovnik, Croatia, 2009.

[3] Joint Meeting of the CT on Migration to Table Driven Code Forms and of the ET on

Data Representation and Codes. Final Report. Geneva, 1. - 5. September 2008.5 - 8  December 2005ntion on International Civil Aviation

1. Background

Fourteenth Session of the Commission for Basic Systems (Dubrovnik, Croatia, 25 March to 2 April 2009) reviewed the revised Functional Specifications for Automatic Weather Stations based on input from other technical commissions and adopted draft Recommendation 6.1/2 (CBS-XIV). The Commission requested the OPAG-ISS to develop BUFR descriptors for all the variables listed in the “Functional Specifications for Automatic Weather Stations” as included in the Annex to this document.

Analysis of the Annex to draft Recommendation 6.1/2 indicated that some of the listed variables may be represented by already existing BUFR descriptors, although they are marked with N in the list (N = not existing BUFR representation). On the other hand, there are several variables with the assigned BUFR descriptors not capable to meet the requested “Maximum Effective Range” or “Minimum Reported Resolution”. Moreover, if the UNIT is specified as “BUFR Table”, the BUFR descriptor cannot be proposed without the content of the table being available. Mr Karl Monnik, the Chairman of ET-AWS was approached in June 2009 to provide clarification and completing of the requirements. Contributions to the discussion of Ms Paula Taylor (UK) and of Messrs Jeff Ator (USA), Etienne Charpentier (WMO), Robert Keeley (DFO-MPO), Michel Leroy (France), Yves Pelletier (Canada), Weiqing Qu (Australia) and Karel Vaníček (Czech Republic) have been also considered.

2. Variables that may be represented by already existing BUFR descriptors

2.1. X, Y, Z components of wind vector

“X,Y,Z component of wind vector (horizontal and vertical profile)” may be represented by

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 11 003 | u-component | m s-1 | 1 | –4096 | 13 | m s-1 | 1 | 4 |
| 0 11 004 | v-component | m s-1 | 1 | –4096 | 13 | m s-1 | 1 | 4 |
| 0 11 006 | w-component | m s-1 | 2 | –4096 | 13 | m s-1 | 2 | 4 |

The name of the descriptors might be supplemented by “of wind vector”, if required.

0 11 003 (u-component) and 0 11 004 (v-component) are fully capable to meet the ET-AWS requirements to express horizontal components of wind of 150.0 m s-1. However, 0 11 006 (w-component) is able to express vertical component of wind up to 40.94 m s-1, i.e. with higher precision for smaller range of values than requested in the Annex.

2.2. UV-B radiation

In 2008, a proposal for representation of UV-B radiation was developed in cooperation of Météo-France and Czech Hydrometeorological Institute. The proposed descriptor 0 14 072 was recommended for validation in September 2008 [3] with a note as included below.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 072 | Global UV irradiation | J m-2 | –3 | –8192 | 14 | J m-2 | –3 | 4 |

Note:

- Global UV irradiation (0 14 072) is UV energy integrated over period specified for spectral band specified. 0 14 072 shall be preceded by a time period descriptor and by 0 02 071 (Spectrographic wavelength) and 0 02 072 (Spectrographic width). E.g. If 0 14 072 is used for Global UV-B irradiation, 0 02 071 and 0 02 072 shall specify spectral band 280 to 315 nm.

2.3. Size of precipitation element

The requested “Size of precipitation element” may be represented by two already existing descriptors:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 058 | Size of precipitation element | m | 4 | 0 | 7 | mm | 1 | 3 |
| 0 20 066 | Maximum diameter of hailstones | m | 3 | 0 | 8 | m | 3 | 3 |

0 13 058 (Size of precipitation element) is capable to express size of any precipitation element (and with higher precision than requested in the Annex), apart from hailstones. Size of hailstones may be represented by 0 20 066 up to 0.254 m. The range up to 0.5 m as requested in the Annex is suggested to be reconsidered.

2.4. Lightning discharge polarity and Lightning discharge type

In 2008, a proposal for Universal BUFR template for representation of lightning data was developed by Ms Paula Taylor (UK). Among other new descriptors, 0 20 119 (Polarity of Stroke) was proposed and recommended for validation in September 2008 [3]. In June 2009, it was agreed to rename this descriptor to become “Lightning discharge polarity”.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 119 | Lightning discharge polarity | Code table | 0 | 0 | 2 | Code table | 0 | 1 |

| Code figure |  |
| --- | --- |
| 0 | Not defined |
| 1 | Positive |
| 2 | Negative |
| 3 | Missing value |

Lightning discharge type (cloud to cloud, cloud to surface) may be represented by entries of Flag table 0 20 023 (Other weather phenomena) as it is done in the Universal BUFR template for representation of lightning data (ground sensors are able to distinguish only cloud-to-cloud and cloud-to-surface).

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 023 | Other weather phenomena | Flag table | 0 | 0 | 18 | Flag table | 0 | 6 |

| Bit No. |  |
| --- | --- |
| 5 | Lightning – cloud to surface |
| 6 | Lightning – cloud to cloud |
| 7 | Lightning – distant |

3. Proposed modifications of some requirements included in Recommendation 6.1/2

3.1. Temperature

BUFR descriptors 0 12 101, 0 12 103, 0 12 113 and 0 12 130 are defined with scale 2, i.e. with precision in hundredths of K, whereas the “Minimum Reported Resolution” = 0.1 K is required in the Annex to Recommendation 6.1/2. The same applies to 0 12 131 and 0 12 132 proposed in 4.1 and 4.8, respectively.  It is suggested to ET-AWS to add a Note (x) under the Functional Specifications for AWS:

- Temperature data represented by 0 12 101, 0 12 103, 0 12 113, 0 12 130, 0 12 131 and 0 12 132 shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values. Temperature t (in degrees Celsius) shall be converted into temperature T (in degrees Kelvin) using equation: T = t + 273.15.

3.2. Vertical component of wind vector

0 11 006 (w-component), discussed in paragraph 2.1., is suitable for representation of the vertical component of wind. The Maximum Effective Range 0 – 40 m s-1 should be introduced in the Functional Specifications for AWS for vertical component of wind.

3.3. Turbulence type and intensity

BUFR representation is requested for variables “Turbulence type (Low levels and wake vortex)” and for “Turbulence intensity” in the Annex to Recommendation 6.1/2. In both cases, the requirement for a BUFR table up to 15 types is stated. To propose a new descriptor, however, the content of the table must be available. It is suggested to ask the ET-AWS experts to provide entries for the requested code (or flag) tables.

3.4. Radiation

Several problems were detected in the requirements for representation of radiation data in the Annex to Recommendation 6.1/2 (the enormous range of values of background luminance, precision in J m -2 and range of values requested for majority of the variables, etc.). Discussion resulted into the following modifications in the Radiation part of the Annex:

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) |
| --- | --- | --- | --- | --- |
| RADIATION |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 |
| Background luminance | 0 – 1∙105 Cd m-2 | 1 Cd m-2 | I, V | N |
| Global downward solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 028 |
| Global upward solar radiation | -1∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | N |
| Diffuse solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 029 |
| Direct solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 030 |
| Downward long-wave radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 |
| Upward long-wave radiation | -1∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 |
| Net radiation | -1∙107 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | N |
| UV-B radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 072 |
| Photosynthetically active radiation 10) | 0 – 1∙107 μE m-2 | 1∙103 μE m-2 | I, T, V | N |
| Surface albedo | 0 – 100% | 1% | I, V | 0 14 019 |

Note (10):

Photosynthetically active radiation (PAR) The electromagnetic energy in the 400– 700 nm wavelength range. Measured as the photosynthetic photon flux (PPF) in quanta per second per square meter, or mole of quanta per second per square meter or microeinsteins per second per square meter.  Approximate conversion is 1 J m-2 s-1 equivalent to 5 μE m-2 s-1.

3.5. Depth of fresh snowfall

Descriptor 0 13 015 (Snowfall (average rate), ms-1, 7, 0, 12) was selected for the variable “Depth of fresh snowfall” in the Annex to Recommendation 6.1/2. It is suggested to replace it with 0 13 012 (Depth of fresh snow, m, 2, -2, 12); it is to be noted that depth of fresh snow of less than 0.005 m is indicated by 0 13 012 set to -0.01 m.

3.6. Hydrologic and marine data

Several problems were detected in the requirements for representation of hydrologic and marine data in the Annex to Recommendation 6.1/2, i.e. majority of the selected descriptors do not have sufficient scale and/or reference value and/or data width to meet the requirements (highlighted in the table below). E.g. 0 23 017 (Flow discharge of major recipient, m3 s-1, 6, 0, 20) is able to express values 0.000000 to 1.048574 m3 s-1, whereas representation of values 0.0 to 250000.0 m3 s-1  is requested for “Flow discharge – river” in the Annex.

Descriptors 0 13 071 (Upstream water level) and 0 13 072 (Downstream water level) are able to meet requirements in the Annex, but not the additional requirements (written in red in the table below) expressed by the Chairman of ET-AWS in June 2009.

| VARIABLE | Maximum Effective Range | Minimum Reported Resolution | Range provided by BUFR descriptors | Precision provided by BUFR descriptors | BUFR / CREX |
| --- | --- | --- | --- | --- | --- |
| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |  |  |
| Flow discharge – river | 0 – 2.5∙105 m3 s-1 | 0.1 m3 s-1 | 0 – 1.048574 m3 s-1 | 0.000001 m3 s-1 | 0 23 017 |
| Flow discharge – well | 0 – 50 m3 s-1 | 0.001 m3 s-1 | 0 – 1.048574 m3 s-1 | 0.000001 m3 s-1 | 0 23 017 |
| Ice thickness - glacier, sea | 0 – 4 270 m | 1 m |  |  | 0 20 031 not suitable |
| Water level | -100 – 100 m | 0.001 m | 0 – 163.82 m 0 – 163.82 m | 0.01 m 0.01 m | 0 13 071 0 13 072 |
| Wave height | 0 – 50 m | 0.1 m | OK | OK | 0 22 021 |
| Wave period | 0 – 100 s | 1 s | 0 – 62 s | 1 s | 0 22 011 |
| Wave direction | 0 12); 1 – 360 degrees | 1° | OK | OK | 0 22 001 |
| 1D spectral wave energy density | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | 0 - 4194.302 m2Hz-1 | 0.001 m2Hz-1 | 0 22 069 |
| 2D spectral wave energy density | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | 0 - 4194.302 m2Hz-1 | 0.001 m2Hz-1 | 0 22 069 |
| Sea salinity | 0 – 40 % [0 – 400 psu] | 10-4 % [10-3 psu] | 0.00 – 163.82 psu 0.00 – 163.82 psu 0.000– 131.070 psu | 0.01 psu 0.01 psu 0.001 psu | 0 22 059 0 22 062 0 22 064 |
| Conductivity | 0 – 600 S m-1 | 10-6 S m-1 | 0 – 67.108862 S m-1 | 0.000001 S m-1 | 0 22 066 |
| Water pressure | 0 – 11x107 Pa | 100 Pa | 0 – 131 070 000 Pa | 1000 Pa | 0 22 065 |
| Ice thickness | 0 – 3 m | 0.015 m | 0 – 1.26 m | 0.01 m | 0 20 031 |
| Tidal elevation with respect to local chart datum | -10 – +30 m | 0.001 m | 0.00 – 163.82 m -10.000 – 22.766 m | 0.01 m 0.001 m | 0 22 035 0 22 038 |
| Tidal elevation with respect to national land datum | -10 – +30 m | 0.001 m | -10.000 – 22.766 m | 0.001 m | 0 22 037 |
| Meteorological residual tidal elevation (surge or offset) | -10 – +16m | 0.001 m | 0.00 – 163.82 m -5.000 – 3.190 m -5.000 – 11.382 m | 0.01 m 0.001 m 0.001 m | 0 22 036 0 22 039 0 22 040 |
| Ocean Current - Direction | 0 12); 1( – 360( | 1( | OK | OK | 0 22 004 0 22 005 |
| Ocean Current - Speed | 0 – 10 m s-1 | 0.01 m s-1 | OK | OK | 0 22 031 0 22 032 |

0 23 017 (m3 s-1, 6, 0, 20) data width is not sufficient,

0 20 031 (Ice deposit (thickness)) is not suitable to represent "Ice thickness - glacier, sea",

0 13 071 (m, 2, 0, 14) - scale and reference value is not sufficient and

0 13 072 (m, 2, 0, 14) - scale and reference value is not sufficient to meet the additional

requirements expressed by the Chairman of ET-AWS

0 22 011 (s, 0, 0, 6) - data width is not sufficient,

0 22 069 (m-2Hz-1, 3, 0, 22) - data width is not sufficient,

0 22 059 (psu, 2, 0, 14) - scale and data width is not sufficient,

0 22 062 (psu, 2, 0, 14) - scale and data width is not sufficient,

0 22 064 (psu, 3, 0, 17) - data width is not sufficient,

0 22 066 (S m-1, 6, 0, 26) - data width is not sufficient,

0 22 065 (Pa, -3, 0, 17) - scale is not sufficient,

0 20 031 (m, 2, 0, 7) - scale and data width is not sufficient

0 22 035 (m, 2, 0, 14) - scale and reference value is not sufficient,

0 22 038 (m, 3, -10000, 15) - data width is not sufficient,

0 22 037 (m, 3, -10000, 15) - data width is not sufficient,

0 22 036 (m, 2, 0, 14) - scale and reference value is not sufficient,

0 22 039 (m, 3, -5000, 13) - reference value and data width is not sufficient,

0 22 040 (m, 3, -5000, 14) - reference value and data width is not sufficient.

Oceanographic experts were contacted in July 2009 to provide their comments on this part of Annex to Recommendation 6.1/2:

- Mr. Robert Keeley expressed his opinion that the ranges of existing BUFR descriptors would be mostly sufficient, apart from the extreme conditions in some cases.

- Mr. Etienne Charpentier suggested completing the list by inclusion of descriptors 0 22 042, 0 22 043 and 0 22 045 for representation of sea/water temperature.

- Further discussion between the oceanographic experts, ET-AWS and IPET-DRC will be needed. If the requirements are confirmed, the IPET DRC may suggest usage of the selected descriptors suitable for the normal operating conditions combined with appropriate operator descriptors to allow representation of the extreme values.

4. Proposal for new BUFR/CREX descriptors (and modification of descriptor 0 15 029)

4.1. Temperature

0 12 131 (Snow temperature) is proposed for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 12 131 | Snow temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |

4.2. Humidity

Three new descriptors are proposed for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 110 | Mass mixing ratio | % | 0 | 0 | 7 | % | 0 | 3 |
| 0 13 111 | Soil moisture, volumetric or water potential | g kg-1 | 0 | 0 | 10 | g kg-1 | 0 | 4 |
| 0 13 112 | Object wetness duration | s | 0 | 0 | 17 | s | 0 | 5 |

4.3. Radiation

Four descriptors are proposed for validation in compliance with the modified requirements included in paragraph 3.4, with the exception of 0 14 054 (Photosyntetically active radiation) that is proposed with Unit = J m-2 as requested in the Annex to Recommendation 6.1/2 instead of the recently required [μE m-2]:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 056 | Background luminance | Cd m-2 | 0 | 0 | 18 | Cd m-2 | 0 | 6 |
| 0 14 052 | Global upward solar radiation, integrated over period specified | J m-2 | -2 | - 1048574 | 20 | J m-2 | -2 | 7 |
| 0 14 053 | Net radiation (high accuracy), integrated over period specified | J m-2 | -2 | - 1048574 | 21 | J m-2 | -2 | 7 |
| 0 14 054 | Photosyntetically active radiation, integrated over period specified | J m-2 | –3 | 0 | 16 | J m-2 | –3 | 5 |

Moreover, it is suggested to ask the ET-AWS experts to consider the possibility to use the term “irradiation” instead of “radiation integrated over period specified” in the names of 0 14 052, 0 14 053 and 0 14 054 in compliance with the terminology used for Global UV irradiation (0 14 072).

4.4. Clouds

Four new descriptors are proposed for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 130 | Cloud hydrometeor concentration | Numeric | 0 | 0 | 10 | Numeric | 0 | 3 |
| 0 20 131 | Effective radius of cloud hydrometeors | m | 5 | 0 | 6 | m | 5 | 2 |
| 0 20 132 | Cloud liquid water content | kg m-3 | 5 | 0 | 11 | kg m-3 | 5 | 4 |
| 0 20 093 | Height of inversion | m | -1 | 0 | 8 | m | -1 | 3 |

And a Note under Class 20:

Cloud hydrometeor concentration 0 20 130 represents the number of hydrometeors in 1 dm3.

4.5. Precipitation

If the existing descriptors 0 13 058 (Size of precipitation element) and 0 20 066 (Maximum diameter of hailstones) are not acceptable for representation of the requested “Size of precipitation element”, a new descriptor 0 13 113 (Size of precipitation element (coarse accuracy)) may be introduced. In this case, it would be convenient to rename 0 13 058 to become “Size of precipitation element (high accuracy)”.

The following descriptors are proposed for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 113 | Size of precipitation element (coarse accuracy) | m | 3 | 0 | 9 | mm | 3 | 3 |
| 0 13 114 or 0 20 134 | Rate of ice accretion | kg m-2 h-1 | 1 | 0 | 11 | kg m-2 h-1 | 1 | 4 |

4.6. Obscuration

It is proposed to introduce two new descriptors (0 20 133 and 0 15 051) and to modify the already existing descriptor 0 15 029 (Extinction coefficient, m-1, 0, 0, 10), currently under validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 133 | Hydrometeor radius | m | 5 | 0 | 6 | m | 5 | 2 |
| 0 15 051 | Meteorological Optical Range | m | 0 | 0 | 18 | m | 0 | 6 |

According to the preliminary information from Dr Sioris, a researcher at Environment Canada, representation of “Extinction coefficient” may require a descriptor with the following specification:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 15 029 | Extinction coefficient | m-1 | 9 | 0 | 30 | m-1 | 9 | 10 |

4.7. Lightning

Three new descriptors are proposed for validation, including a new descriptor for the variable “Lightning rates of discharge”. Descriptor 0 13 059 (Number of flashes (thunderstorm), 0, 0, 7), chosen in the Annex, is not suitable for representation of this variable, i.e. it is not capable of expressing values up to 100 000 requested in the Annex. Moreover, Ms Paula Taylor stated that the maximum value might reach 4 500 000 detections in a single storm.

Representation of variables “Lightning discharge polarity” and “Lightning discharge type (cloud to cloud, cloud to surface)” may be accomplished using the existing descriptors as suggested in the paragraph 2.4 above.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 126 | Lightning rates of discharge | Numeric | 0 | 0 | 23 | Numeric | 0 | 7 |
| 0 20 127 | Lightning - distance from station | m | -3 | 0 | 6 | m | -3 | 2 |
| 0 20 128 | Lightning - direction from station | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |

And a Note under Class 20:

Lightning rates of discharge 0 20 126 shall be preceded by a time period descriptor, e.g. by 0 04 024 set to 1 if lightning rates of discharge per hour is to be reported.

4.8. Hydrologic and marine data

Eight new descriptors are proposed for validation, including a new descriptor for the variable "Ice thickness - glacier, sea”. Descriptor 0 20 031 (Ice deposit (thickness)), chosen in the Annex, is not suitable for representation of this variable as it is meant for deposit of glaze, rime and/or wet snow.

Requirements for representation of the other variables included in this part of the Annex to Recommendation 6.1/2 have to be subjected to further discussion as mentioned in the paragraph 3.6 above.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 23 040 | Flow discharge – river | m3 s-1 | 1 | 0 | 22 | m3 s-1 | 1 | 7 |
| 0 23 041 | Flow discharge – well | m3 s-1 | 3 | 0 | 16 | m3 s-1 | 3 | 5 |
| 0 13 074 | Ground water level | m | 2 | 0 | 18 | m | 2 | 6 |
| 0 12 132 | Ice surface temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |
| 0 13 115 | Ice thickness - river, lake | m | 2 | 0 | 13 | m | 2 | 4 |
| 0 13 116 | Ice thickness - glacier, sea | m | 0 | 0 | 13 | m | 0 | 4 |
| 0 20 135 | Ice mass (on a rod) | kg m-1 | 1 | 0 | 10 | kg m-1 | 1 | 3 |
| 0 13 117 | Snow density (liquid water content) | kg m-3 | 0 | 0 | 10 | kg m-3 | 0 | 3 |

As an alternative solution, suggested by Mr. Jeff Ator, the above proposed 0 13 115 (Ice thickness - river, lake) and 0 13 116 (Ice thickness - glacier, sea) might be replaced by one descriptor 0 13 115 (Ice thickness) being preceded by 0 08 029 (Surface type) that would provide the required specification:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 115 | Ice thickness | m | 2 | 0 | 19 | m | 2 | 6 |

And a Note under Class 13:

Ice thickness 0 13 115 shall be preceded by 0 08 029 (Surface type) set to 11, 12, 13 or 14 to specify river, lake, sea or glacier, respectively.

If this alternative solution is preferred by the IPET DRC meeting, the name of 0 08 029 will have to be changed from the current “Remotely sensed surface type” to “Surface type” and the following code figures introduced into 0 08 029 - Surface type:

| Code figure |  |
| --- | --- |
| 11 | river |
| 12 | lake |
| 13 | sea |
| 14 | glacier |

4.9. Other

According to information obtained from the WMO Secretariat, the variable “Gamma radiation dose rate” is meant to be used for reporting this element under normal conditions, nuclear accidents excluded. The proposed descriptor 0 24 014 is fully capable to express background values plus the increments caused by precipitation or sudden thaw.

0 24 014 (Gamma radiation dose rate) is proposed for validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 24 014 | Gamma radiation dose rate | nSv h-1 | 1 | 0 | 14 | nSv h-1 | 1 | 4 |

And a Note under Class 24:

Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.

5. Conclusion

Further discussion between ET-AWS and IPET-DRC and with the oceanographic experts is desirable to clarify the indicated problems. The outcome of this work should be a set of BUFR descriptors suitable for representation of all variables listed in the “Functional Specifications for Automatic Weather Stations”. To reach this goal, the IPET DRC meeting may invite the ET AWS to examine carefully all suggestions and proposals included in this document (section 2, 3 and 4), including the suggested revision of some of the requirements for variables in Annex to Recommendation 6.1/2 (CBS-XIV), provided that IPET DRC meeting would support these suggestions and proposals.

IPET-DRC / Doc. 3.3(3) ADD1 contains a revised version of the Annex to Recommendation 6.1/2 (CBS-XIV) based on the suggestions and proposals included in document IPET-DRC / Doc. 3.3(3). Should the IPET-DRC meeting suggest any changes, another version of the Annex to Recommendation 6.1/2 (CBS-XIV) would be produced.

Annex to draft Recommendation 6.1/2 (CBS-XIV)                    ANNEX

Functional Specifications for Automatic Weather Stations

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) |
| --- | --- | --- | --- | --- |
| ATMOSPHERIC PRESSURE |  |  |  |  |
| Atmospheric Pressure | 500 – 1080 hPa | 10 Pa | I, V | 0 10 004 |
| TEMPERATURE 9) |  |  |  |  |
| Ambient air temperature (over specified surface) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 101 |
| Dew-point temperature | -80 °C – +60 °C | 0.1 K | I, V | 0 12 103 |
| Ground (surface) temperature (over specified surface) | -80 °C – +80 °C | 0.1 K | I, V | 0 12 113 |
| Soil temperature | -50 °C – +50 °C | 0.1 K | I, V | 0 12 130 |
| Snow temperature | -80 °C – 0 °C | 0.1 K | I, V | N |
| Water temperature - river, lake, sea, well | -2 °C – +100 °C | 0.1 K | I, V | 0 13 082 |
| HUMIDITY 9) |  |  |  |  |
| Relative humidity | 0 – 100% | 1% | I, V | 0 13 003 |
| Mass mixing ratio | 0 – 100% | 1% | I, V | N |
| Soil moisture, volumetric or water potential | 0 – 103 g kg-1 | 1 g kg-1 | I, V | N |
| Water vapour pressure | 0 – 100 hPa | 10 Pa | I, V | 0 13 004 |
| Evaporation/evapotranspiration | 0 – 0.2 m | 0.1 kg m-2, 0.0001 m | T | 0 13 033 |
| Object wetness duration | 0 – 86 400 s | 1 s | T | N |
| WIND |  |  |  |  |
| Direction | 0 11,13); 1( – 360( | 1( | I, V | 0 11 001 |
| Speed | 0 – 75 m s-1 | 0.1 m s-1 | I, V | 0 11 002 |
| Gust Speed | 0 – 150 m s-1 | 0.1 m s-1 | I, V | 0 11 041 |
| X,Y,Z component of wind vector (horizontal and vertical profile) | 0 – 150 m s-1 | 0.1 m s-1 | I, V | N |
| Turbulence type (Low levels and wake vortex) | up to 15 types | BUFR Table | I, V | N |
| Turbulence intensity | up to 15 types | BUFR Table | I, V | N |
| RADIATION 6) |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 |
| Background luminance | 1∙10-6 – 2∙104 Cd m-2 | 1∙10-6 Cd m-2 | I, V | N |
| Global downward solar radiation | 0 – 6∙106 J m-2 | 1 J m-2 | I, T, V | N |
| Global upward solar radiation | 0 – 4∙106 J m-2 | 1 J m-2 | I, T, V | N |
| Diffuse solar radiation | 0 – 4∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 023 |
| Direct solar radiation | 0 – 5∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 025 |
| Downward long-wave radiation | 0 – 3∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 002 |
| Upward long-wave radiation | 0 – 3∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 002 |
| Net radiation | 0 – 6∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 016 |
| UV-B radiation 8) | 0 – 1.2∙103 J m-2 | 1 J m-2 | I, T, V | N |
| Photosynthetically active radiation | 0 – 3∙106 J m-2 | 1 J m-2 | I, T, V | N |
| Surface albedo | 1 – 100% | 1% | I, V | 0 14 019 |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) |
| --- | --- | --- | --- | --- |
| CLOUDS |  |  |  |  |
| Cloud base height | 0 – 30 km | 10 m | I, V | 0 20 013 |
| Cloud top height | 0 – 30 km | 10 m | I, V | 0 20 014 |
| Cloud type, convective vs. other types | up to 30 classes | BUFR Table | I | 0 20 012 |
| Cloud hydrometeor concentration | 1 – 700 hydrometeors dm-3 | 1 hydrometeor dm-3 | I, V | N |
| Effective radius of cloud hydrometeors | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | N |
| Cloud liquid water content | 1∙10-5–1.4∙10-2 kg m-3 | 1∙10-5 kg m-3 | I, V | N |
| Optical depth within each layer | Not specified yet | Not specified yet | I, V | N |
| Optical depth of fog | Not specified yet | Not specified yet | I, V | N |
| Height of inversion | 0 – 1 000 m | 10 m | I, V | N |
| Cloud cover | 0 – 100% | 1% | I, V | 0 20 010 |
| Cloud amount | 0 – 8/8 | 1/8 | I, V | 0 20 011 |
| PRECIPITATION |  |  |  |  |
| Accumulation 7) | 0 – 1000 mm | 0.1 kg m-2, 0.0001 m | T | 0 13 011 |
| Depth of fresh snowfall | 0 –1000 cm | 0.001 m | T | 0 13 015 |
| Duration | up to 86 400 s | 60 s | T | 0 26 020 |
| Size of precipitating element | 1∙10-3 – 0.5 m | 1∙10-3 m | I, V | N |
| Intensity - quantitative | 0 – 2000 mm h-1 | 0.1 kg m-2 s-1, 0.1 mm h-1 | I, V | 0 13 155 |
| Type | up to 30 types | BUFR Table | I, V | 0 20 021 |
| Rate of ice accretion | 0 – 1 kg dm-2 h-1 | 1∙10-3 kg dm-2 h-1 | I, V | N |
| OBSCURATIONS |  |  |  |  |
| Obscuration type | up to 30 types | BUFR Table | I, V | 0 20 025 |
| Hydrometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 |
| Lithometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 |
| Hydrometeor radius | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | N |
| Horizontal Extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | N |
| Slant – extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | N |
| Meteorological Optical Range 10) | 1 – 100 000 m | 1 m | I, V | N |
| Runway visual range | 1 – 4 000 m | 1 m | I, V | 0 20 061 |
| Other weather type | up to 18 types | BUFR Table | I, V | 0 20 023 |
| LIGHTNING |  |  |  |  |
| Lightning rates of discharge | 0 – 100 000 | Number h-1 | I, V | 0 13 059 |
| Lightning discharge type (cloud to cloud, cloud to surface) | up to 10 types | BUFR Table | I, V | N |
| Lightning discharge polarity | 2 types | BUFR Table | I, V | N |
| Lightning discharge energy | Not specified yet | Not specified yet | I, V | N |
| Lightning - distance from station | 0 – 3∙104 m | 103 m | I, V | N |
| Lightning - direction from station | 1( – 360( | 1 degree | I, V | N |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) |
| --- | --- | --- | --- | --- |
| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |  |
| Flow discharge – river | 0 – 2.5∙105 m3 s-1 | 0.1 m3 s-1 | I, V | 0 23 017 |
| Flow discharge – well | 0 – 50 m3 s-1 | 0.001 m3 s-1 | I, V | 0 23 017 |
| Ground water level | 0 – 1 800 m | 0.01 m | I, V | N |
| Ice surface temperature | -80 °C – +0 °C | 0.5 K | I, V | N |
| Ice thickness - river, lake | 0 – 50 m | 0.01 m | I, V | N |
| Ice thickness - glacier, sea | 0 – 4 270 m | 1 m | I, V | 0 20 031 |
| Water level | 0 – 100 m | 0.01 m | I, V | 0 13 071 0 13 072 |
| Wave height | 0 – 50 m | 0.1 m | V | 0 22 021 |
| Wave period | 0 – 100 s | 1 s | V | 0 22 011 |
| Wave direction | 0 13); 1 – 360 degrees | 1 degrees | V | 0 22 001 |
| 1D spectral wave energy density | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | V, T | 0 22 069 |
| 2D spectral wave energy density | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | V, T | 0 22 069 |
| Sea salinity | 0 – 40 % 12) [0 – 400 psu] | 10-4 % [10-3 psu] | I, V | 0 22 059 0 22 062 0 22 064 |
| Conductivity | 0 – 600 S m-1 | 10-6 S m-1 | I, V | 0 22 066 |
| Water pressure | 0 – 11x107 Pa | 100 Pa | I, V | 0 22 065 |
| Ice thickness | 0 – 3 m | 0.015 m | T | 0 20 031 |
| Ice mass | 0 – 50 kg m-1 | 0.5 kg m-1 (on 32 mm rod) | T | N |
| Snow density (liquid water content) | 100 – 700 kg m-3 | 1 kg m-3 | T | N |
| Tidal elevation with respect to local chart datum | -10 – +30 m | 0.001 m | I, V | 0 22 035 0 22 038 |
| Tidal elevation with respect to national land datum | -10 – +30 m | 0.001 m | I, V | 0 22 037 |
| Meteorological residual tidal elevation (surge or offset) | -10 – +16m | 0.001 m | I, V | 0 22 036 0 22 039 0 22 040 |
| Ocean Current - Direction | 0 13); 1( – 360( | 1( | I, V | 0 22 004 0 22 005 |
| Ocean Current - Speed | 0 – 10 m s-1 | 0.01 m s-1 | I, V | 0 22 031 0 22 032 |
| OTHER SURFACE VARIABLES |  |  |  |  |
| Runway conditions | up to 10 types | BUFR Table | I, V | 0 20 085 |
| Braking action/friction coefficient | up to 7 types | BUFR Table | I, V | 0 20 089 |
| State of ground | up to 30 types | BUFR Table | I, V | 0 20 062 |
| Type of surface specified | up to 15 types | BUFR Table | I, V | 0 08 010 |
| Snow depth | 0 – 25 m | 0.01 m | T | 0 13 013 |
| OTHER |  |  |  |  |
| Gamma radiation dose rate | 1 – 103 nSv h-1 | 0.1 nSv h-1 | I, T | N |
| Categories of stability | 9 types | BUFR Table | I, V | 0 13 041 |

Notes:

- Name of variable, in line with WMO vocabulary and Technical Regulations.

- Maximum Effective Range – Maximum range of measuring capability; units traceable to SI.

- Minimum Reported Resolution – Lower resolution of reporting is not permitted.

- Mode of Observation – Type of data being reported:

I:  Instantaneous – 1-minute value (instantaneous as defined in WMO-No. 8, Part II, paragraph 1.3.2.4);

V:  Variability – Average (mean), Standard Deviation, Maximum, Minimum, Range, Median, etc. of samples – those reported depend upon meteorological variable;

T: Total – Integrated value during defined period (over a fixed period(s)); maximum
24 hours for all parameters except radiation which requires a maximum of one hour (exception, see note 6), and precipitation accumulation (6 hours maximum).

A:  Average (mean) value.

- BUFR/CREX – Present ability to represent variable by BUFR Tables, N = not existing, to be defined (registered).

- Radiation energy amounts are given over a 24-hour period.

- Maximum interval: 6 H.

- Definition of UV-B according to WMO-No. 8 (Vol. 1, Chapter on Radiation).

- Humidity related variables (i.e. dew point) expressed as temperature are collected under temperature.

- MOR uniquely related to "extinction coefficient", (, by MOR = -ln(5%)/(.

- Direction to indicate 0 (zero) if speed = 0.

- Salinity of 1% (1 g of salt per 100 g of water), or 10 ‰ converts to 10.000 ppm (parts per million), which equals 10 psu (practical salinity units). Ocean water is about 3.5% salt, i.e. 35.000 ppm or 35 psu. Lake Asal (Ethiopia) is the most saline body of water on earth with 34.8% [348 psu] salt concentration. BUFR/CREX table references 0 22 0590, 22 0620 and 22 064, however, only allow for a maximum of 163.830 "Part per thousand" [or psu], less than the required maximum range.

- Calm.