| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(3) ADD1 (4.IX.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Revised Annex to Recommendation 6.1/2 (CBS-XIV)

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a revised version of the Annex to Recommendation 6.1/2 (CBS-XIV) based on the suggestions and proposals included in document IPET-DRC / Doc. 3.3(3).

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document.

References:

[1]  Červená, E.: BUFR descriptors required by Recommendation 6.1/2 (CBS-XIV),

Doc. 3.3(3). First meeting of IPET-DRC, Geneva, 15 to 18 September 2009.

Annex to draft Recommendation 6.1/2 (CBS-XIV) – Version of 4 September 2009

Functional Specifications for Automatic Weather Stations

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | See Doc. 3.3(3) |
| --- | --- | --- | --- | --- | --- |
| ATMOSPHERIC PRESSURE |  |  |  |  |  |
| Atmospheric Pressure | 500 – 1080 hPa | 10 Pa | I, V | 0 10 004 |  |
| TEMPERATURE 9) |  |  |  |  |  |
| Ambient air temperature (over specified surface) 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 101 |  |
| Dew-point temperature 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 103 |  |
| Ground (surface) temperature (over specified surface) 14) | -80 °C – +80 °C | 0.1 K | I, V | 0 12 113 |  |
| Soil temperature14) | -50 °C – +50 °C | 0.1 K | I, V | 0 12 130 |  |
| Snow temperature 14) | -80 °C – 0 °C | 0.1 K | I, V | 0 12 131 | 4.1 |
| Water temperature - river, lake, sea, well | -2 °C – +100 °C | 0.1 K | I, V | 0 13 082 0 22 043 | 3.6 |
| HUMIDITY 9) |  |  |  |  |  |
| Relative humidity | 0 – 100% | 1% | I, V | 0 13 003 |  |
| Mass mixing ratio | 0 – 100% | 1% | I, V | 0 13 110 | 4.2 |
| Soil moisture, volumetric or water potential | 0 – 103 g kg-1 | 1 g kg-1 | I, V | 0 13 111 | 4.2 |
| Water vapour pressure | 0 – 100 hPa | 10 Pa | I, V | 0 13 004 |  |
| Evaporation/evapotranspiration | 0 – 0.2 m | 0.1 kg m-2, 0.0001 m | T | 0 13 033 |  |
| Object wetness duration | 0 – 86 400 s | 1 s | T | 0 13 112 | 4.2 |
| WIND |  |  |  |  |  |
| Direction | 0 11,13); 1( – 360( | 1( | I, V | 0 11 001 |  |
| Speed | 0 – 75 m s-1 | 0.1 m s-1 | I, V | 0 11 002 |  |
| Gust Speed | 0 – 150 m s-1 | 0.1 m s-1 | I, V | 0 11 041 |  |
| X,Y component of wind vector Z component of wind vector (horizontal and vertical profile) | 0 – 150 m s-1 0 – 40 m s-1 | 0.1 m s-1 | I, V | 0 11 003 0 11 004 0 11 006 | 2.1 and 3.2 |
| Turbulence type (Low levels and wake vortex) | up to 15 types | BUFR Table ??? | I, V | N | 3.3 |
| Turbulence intensity | up to 15 types | BUFR Table ??? | I, V | N | 3.3 |
| RADIATION 6) |  |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 |  |
| Background luminance | 0 – 1∙105 Cd m-2 | 1 Cd m-2 | I, V | 0 14 056 | 3.4 , 4.3 |
| Global downward solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 028 | 3.4 |
| Global upward solar radiation | -1∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 052 | 3.4 , 4.3 |
| Diffuse solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 029 | 3.4 |
| Direct solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 030 | 3.4 |
| Downward long-wave radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | 3.4 |
| Upward long-wave radiation | -1∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | 3.4 |
| Net radiation | -1∙107 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 053 | 3.4 , 4.3 |
| UV-B radiation 8) | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 072 | 2.2 |
| Photosynthetically active radiation 15) | 0 – 1∙107 J m-2 | 1∙103 J m-2 | I, T, V | 0 14 054 | 3.4 , 4.3 |
| Surface albedo | 0 – 100% | 1% | I, V | 0 14 019 |  |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | See Doc. 3.3(3) |
| --- | --- | --- | --- | --- | --- |
| CLOUDS |  |  |  |  |  |
| Cloud base height | 0 – 30 km | 10 m | I, V | 0 20 013 |  |
| Cloud top height | 0 – 30 km | 10 m | I, V | 0 20 014 |  |
| Cloud type, convective vs. other types | up to 30 classes | BUFR Table | I | 0 20 012 |  |
| Cloud hydrometeor concentration | 1 – 700 hydrometeors dm-3 | 1 hydrometeor dm-3 | I, V | 0 20 130 | 4.4 |
| Effective radius of cloud hydrometeors | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 131 | 4.4 |
| Cloud liquid water content | 1∙10-5–1.4∙10-2 kg m-3 | 1∙10-5 kg m-3 | I, V | 0 20 132 | 4.4 |
| Optical depth within each layer | Not specified yet | Not specified yet | I, V | N |  |
| Optical depth of fog | Not specified yet | Not specified yet | I, V | N |  |
| Height of inversion | 0 – 1 000 m | 10 m | I, V | 0 20 093 | 4.4 |
| Cloud cover | 0 – 100% | 1% | I, V | 0 20 010 |  |
| Cloud amount | 0 – 8/8 | 1/8 | I, V | 0 20 011 |  |
| PRECIPITATION |  |  |  |  |  |
| Accumulation 7) | 0 – 1000 mm | 0.1 kg m-2, 0.0001 m | T | 0 13 011 |  |
| Depth of fresh snowfall16) | 0 –1000 cm | 0.01 m | T | 0 13 015 0 13 012 | 3.5 |
| Duration | up to 86 400 s | 60 s | T | 0 26 020 |  |
| Size of precipitating element 17) | 1∙10-3 – 0.25 m | 1∙10-3 m | I, V | 0 13 058 0 20 066 | 2.3 |
| Intensity - quantitative | 0 – 2000 mm h-1 | 0.1 kg m-2 s-1, 0.1 mm h-1 | I, V | 0 13 155 |  |
| Type | up to 30 types | BUFR Table | I, V | 0 20 021 |  |
| Rate of ice accretion | 0 – 1 kg dm-2 h-1 | 1∙10-3 kg dm-2 h-1 | I, V | 0 13 114 (0 20 134) | 4.5 |
| OBSCURATIONS |  |  |  |  |  |
| Obscuration type | up to 30 types | BUFR Table | I, V | 0 20 025 |  |
| Hydrometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 |  |
| Lithometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 |  |
| Hydrometeor radius | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 133 | 4.6 |
| Horizontal Extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | 0 15 029 | 4.6 |
| Slant – extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | N |  |
| Meteorological Optical Range 10) | 1 – 100 000 m | 1 m | I, V | 0 15 051 | 4.6 |
| Runway visual range | 1 – 4 000 m | 1 m | I, V | 0 20 061 |  |
| Other weather type | up to 18 types | BUFR Table | I, V | 0 20 023 |  |
| LIGHTNING |  |  |  |  |  |
| Lightning rates of discharge | 0 – 4 500 000 | Number h-1 | I, V | 0 13 059 0 20 126 | 4.7 |
| Lightning discharge type (cloud to cloud, cloud to surface) | 3 types | BUFR Code Table | I, V | 0 20 023 | 2.4 |
| Lightning discharge polarity | 2 types | BUFR Code Table | I, V | 0 20 119 | 2.4 |
| Lightning discharge energy | Not specified yet | Not specified yet | I, V | N |  |
| Lightning - distance from station | 0 – 3∙104 m | 103 m | I, V | 0 20 127 | 4.6 |
| Lightning - direction from station | 1( – 360( | 1 degree | I, V | 0 20 128 | 4.6 |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | See Doc. 3.3(3) |
| --- | --- | --- | --- | --- | --- |
| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |  |  |
| Flow discharge – river | 0 – 2.5∙105 m3 s-1 | 0.1 m3 s-1 | I, V | 0 23 017 0 23 040 | 4.8 |
| Flow discharge – well | 0 – 50 m3 s-1 | 0.001 m3 s-1 | I, V | 0 23 017 0 23 041 | 4.8 |
| Ground water level | 0 – 1 800 m | 0.01 m | I, V | 0 13 074 | 4.8 |
| Ice surface temperature 14) | -80 °C – +0 °C | 0.5 K | I, V | 0 12 132 | 3.1 and 4.8 |
| Ice thickness - river, lake | 0 – 50 m | 0.01 m | I, V | 0 13 115 | 4.8 |
| Ice thickness - glacier, sea | 0 – 4 270 m | 1 m | I, V | 0 20 031 0 13 116 | 4.8 |
| Water level | 0 – 100 m | 0.01 m | I, V | 0 13 071 0 13 072 | 3.6 |
| Wave height | 0 – 50 m | 0.1 m | V | 0 22 021 |  |
| Wave period 18) | 0 – 100 s ??? | 1 s | V | 0 22 011 | 3.6 |
| Wave direction | 0 13); 1 – 360 degrees | 1 degrees | V | 0 22 001 |  |
| 1D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 ?? | 10-3 m2Hz-1 | V, T | 0 22 069 | 3.6 |
| 2D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 ?? | 10-3 m2Hz-1 | V, T | 0 22 069 | 3.6 |
| Sea salinity 18) | 0 – 40 % 12) [0 – 400 psu] ??? | 10-4 % [10-3 psu] | I, V | 0 22 059 0 22 062 0 22 064 | 3.6 |
| Conductivity 18) | 0 – 600 S m-1 ??? | 10-6 S m-1 | I, V | 0 22 066 | 3.6 |
| Water pressure 18) | 0 – 11x107 Pa | 100 Pa ??? | I, V | 0 22 065 | 3.6 |
| Ice thickness 18) | 0 – 3 m ??? | 0.015 m ??? | T | 0 20 031 | 3.6 |
| Ice mass | 0 – 50 kg m-1 | 0.5 kg m-1 (on 32 mm rod) | T | 0 20 135 | 4.8 |
| Snow density (liquid water content) | 100 – 700 kg m-3 | 1 kg m-3 | T | 0 13 117 | 4.8 |
| Tidal elevation with respect to local chart datum 18) | -10 – +30 m ??? | 0.001 m | I, V | 0 22 035 0 22 038 | 3.6 |
| Tidal elevation with respect to national land datum 18) | -10 – +30 m ??? | 0.001 m | I, V | 0 22 037 | 3.6 |
| Meteorological residual tidal elevation (surge or offset) 18) | -10 – +16m ??? | 0.001 m | I, V | 0 22 036 0 22 039 0 22 040 | 3.6 |
| Ocean Current - Direction | 0 13); 1( – 360( | 1( | I, V | 0 22 004 0 22 005 |  |
| Ocean Current - Speed | 0 – 10 m s-1 | 0.01 m s-1 | I, V | 0 22 031 0 22 032 |  |
| OTHER SURFACE VARIABLES |  |  |  |  |  |
| Runway conditions | up to 10 types | BUFR Table | I, V | 0 20 085 |  |
| Braking action/friction coefficient | up to 7 types | BUFR Table | I, V | 0 20 089 |  |
| State of ground | up to 30 types | BUFR Table | I, V | 0 20 062 |  |
| Type of surface specified | up to 15 types | BUFR Table | I, V | 0 08 010 |  |
| Snow depth | 0 – 25 m | 0.01 m | T | 0 13 013 |  |
| OTHER |  |  |  |  |  |
| Gamma radiation dose rate 19) | 1 – 103 nSv h-1 | 0.1 nSv h-1 | I, T | 0 24 014 | 4.9 |
| Categories of stability | 9 types | BUFR Table | I, V | 0 13 041 |  |

Notes:

- Name of variable, in line with WMO vocabulary and Technical Regulations.

- Maximum Effective Range – Maximum range of measuring capability; units traceable to SI.

- Minimum Reported Resolution – Lower resolution of reporting is not permitted.

- Mode of Observation – Type of data being reported:

I:  Instantaneous – 1-minute value (instantaneous as defined in WMO-No. 8, Part II, paragraph 1.3.2.4);

V:  Variability – Average (mean), Standard Deviation, Maximum, Minimum, Range, Median, etc. of samples – those reported depend upon meteorological variable;

T: Total – Integrated value during defined period (over a fixed period(s)); maximum
24 hours for all parameters except radiation which requires a maximum of one hour (exception, see note 6), and precipitation accumulation (6 hours maximum).

A:  Average (mean) value.

- BUFR/CREX – Present ability to represent variable by BUFR Tables, N = not existing, to be defined (registered).

- Radiation energy amounts are given over a 24-hour period.

- Maximum interval: 6 H.

- Definition of UV-B according to WMO-No. 8 (Vol. 1, Chapter on Radiation).

- Humidity related variables (i.e. dew point) expressed as temperature are collected under temperature.

- MOR uniquely related to "extinction coefficient", (, by MOR = -ln(5%)/(.

- Direction to indicate 0 (zero) if speed = 0.

- Salinity of 1% (1 g of salt per 100 g of water), or 10 ‰ converts to 10.000 ppm (parts per million), which equals 10 psu (practical salinity units). Ocean water is about 3.5% salt, i.e. 35.000 ppm or 35 psu. Lake Asal (Ethiopia) is the most saline body of water on earth with 34.8% [348 psu] salt concentration. BUFR/CREX table references 0 22 0590, 22 0620 and 22 064, however, only allow for a maximum of 163.830 "Part per thousand" [or psu], less than the required maximum range.

- Calm.

- Temperature data represented by 0 12 101, 0 12 103, 0 12 113, 0 12 130, 0 12 131 and 0 12 132 shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values. Temperature t (in degrees Celsius) shall be converted into temperature T (in degrees Kelvin) using equation: T = t + 273.15.

- Photosynthetically active radiation (PAR) The electromagnetic energy in the 400– 700 nm wavelength range. Measured as the photosynthetic photon flux (PPF) in quanta per second per square meter, or mole of quanta per second per square meter or microeinsteins per second per square meter.  Approximate conversion is 1 J m-2 s-1 equivalent to 5 μE m-2 s-1 (suggested by the Chairman of ET AWS).

- Depth of fresh snow of less than 0.005 m is indicated by 0 13 012 set to -0.01 m

- 0 13 058 (Size of precipitation element) is capable to express size of any precipitation element, apart from hailstones. Size of hailstones shall be represented by 0 20 066.

- If these requirements are confirmed, it has to be noted that the selected descriptors are suitable for the normal operating conditions and shall be combined with appropriate operator descriptors to allow representation of the extreme values.

- Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.