| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES GENEVA, 15-18 SEPTEMBER 2009 |  | IPET-DRC-I / Doc. 3.3(8) (28.VIII.2009) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for ATMS data

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for the addition of new BUFR descriptors to be used for Advanced Technology Microwave Sounder (ATMS) data.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve the contents for validation.

BACKGROUND AND DISCUSSION

The ATMS (Advanced Technology Microwave Sounder) instrument is part of the next generation operational sensor suite selected to fly on the National Polar-Orbiting Operational Environmental Satellite System (NPOESS) spacecraft.  Sounding data from this instrument, when combined together with CrIS (Cross-Track Infrared Sounder) data attached to the same satellite, will support continuing advances in NWP (Numerical Weather Prediction) models to improve short and medium-range weather forecasts.

During the past year, the below proposal was submitted for review by members of the CGMS TFSDC (Task Force on Satellite Data and Codes).  Their feedback was much appreciated and is incorporated into the final proposal below, which we now ask to be accepted for validation status.  In the coming months we expect to be able to provide samples of test data in order to complete the validation procedure.

PROPOSAL

Please note that descriptor 0-33-078 (as shown below) has already been defined and approved for use with CrIS data, and is merely included below for clarity since it is not yet present in any official WMO tables.

#### (1) Add new Table D entry:

|  |  | ATMS (Advanced Technology Microwave Sounder) data |
| --- | --- | --- |
| 3 10 061 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 0 33 079 | Granule level quality flags |
|  | 0 33 080 | Scan level quality flags |
|  | 0 33 078 | Geolocation quality |
|  | 1 15 000 | Delayed replication of 15 descriptors |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 05 042 | Channel number |
|  | 0 02 153 | Satellite channel center frequency |
|  | 0 02 154 | Satellite channel band width |
|  | 0 02 104 | Antenna polarization |
|  | 0 12 066 | Antenna temperature |
|  | 0 12 163 | Brightness temperature |
|  | 0 33 081 | Channel data quality flags |

#### (2) Add new Table B entries:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 12 066 | Antenna temperature | K | 2 | 0 | 16 | C | 2 | 5 |
| 0 33 078 | Geolocation quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 33 079 | Granule level quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 080 | Scan level quality flags | Flag table | 0 | 0 | 20 | Flag table | 0 | 7 |
| 0 33 081 | Channel data quality flags | Flag table | 0 | 0 | 12 | Flag table | 0 | 4 |

(3) Add the following new code table entries to existing BUFR/CREX Table B descriptors:

0 02 104  (Antenna polarization)

6	Quasi-horizontal polarization

7	Quasi-vertical polarization

(4) Code/Flag tables for proposed new Table B descriptors:

0 33 078  Geolocation quality

| Code figure | Meaning |
| --- | --- |
| 0 | Nominal – altitude and Ephemeris data available |
| 1 | Missing at most a small gap of altitude and Ephemeris data |
| 2 | Missing more than a small gap of altitude and Ephemeris data, but no more than a granule boundary |
| 3 | Missing more than a granule boundary of altitude and Ephemeris data |
| 4-14 | Reserved |
| 15 | Missing |

0-33-079  Granule level quality flags

| Bit | Meaning |
| --- | --- |
| 1-5 | Reserved |
| 6 | The No. 1-No.7 health checks failed |
| 7 | The No. 8-No.15 health checks failed |
| 8 | The No. 16-No.23 health checks failed |
| 9 | The No. 24-No.31 health checks failed |
| 10 | The No. 32-No.39 health checks failed |
| 11 | The No. 40-No.47 health checks failed |
| 12 | The No. 48-No.55 health checks failed |
| 13 | The No. 56-No.63 health checks failed |
| 14 | The No. 64-No.70 health checks failed |
| 15 | Quadratic correction applied to the radiometric transfer function for non-linearity correction |
| All 16 | Missing value |

0-33-080  Scan level quality flags

| Bit | Meaning |
| --- | --- |
| 1-6 | Reserved |
| 7 | Divide-by-zero condition or computation loop failed to converge in the K/Ka and V (KAV) Band PRT |
| 8 | Divide-by-zero condition or computation loop failed to converge in the WG Band PRT |
| 9 | Divide-by-zero condition or computation loop failed to converge in the K/Ka, V, W, G Band Receiver Shelf PRT K temperature computation |
| 10 | Out of range condition for the K/Ka and V Band PRT |
| 11 | Out of range condition for the WG Band PRT |
| 12 | KAV PRT temperature inconsistency |
| 13 | WG PRT temperature inconsistency |
| 14 | Time Sequence Error |
| 15 | Data Gap - Missing scan(s) preceding the current scan |
| 16 | KAV PRT Sufficiency - Insufficient KAV PRT data are available |
| 17 | WG PRT Sufficiency - Insufficient WG PRT data are available |
| 18 | Space View antenna position error |
| 19 | Blackbody antenna position error |
| All 20 | Missing value |

0-33-081  Channel data quality flags

| Bit | Meaning |
| --- | --- |
| 1-4 | Reserved |
| 5 | Moon in Space View |
| 6 | Gain Error - The lowest blackbody count is smaller than or equal to the highest space view count in a scan |
| 7 | Calibration With Fewer Than Preferred Samples |
| 8 | Space View Data Sufficiency Check - Insufficient space view samples are available |
| 9 | Blackbody View Data Sufficiency Check - Insufficient blackbody view samples are available |
| 10 | Out of range condition for the Space View |
| 11 | Space view inconsistency |
| All 12 | Missing value |