| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.2.3 (12) (9. IX. 2011) ------------------------- ITEM 2.3 ENGLISH ONLY |
| --- | --- | --- |

Space Weather in GRIB2

Submitted by Jeff Ator (U.S.A.)

________________________________________________________________

Summary and Purpose of Document

The document proposes a methodology for reporting space weather in GRIB2.

________________________________________________________________

ACTION PROPOSED

The team is requested to approve the contents for validation.

DISCUSSION

At the IPET-DRC II meeting in Brasilia (August 2010), the team discussed ideas for the representation of space weather in GRIB2.  This was initiated by a topical paper from the U.S., and the results are documented in item 2.3.11 of the final report from the meeting.

In accordance with the guidance provided by IPET-DRC II, the NCEP Space Weather Prediction Center (SWPC) has worked closely with the UKMO and AFWA over the past year to develop a formal proposal for validation.  We hope to validate these new additions in the coming months so they can be adopted for fast-track implementation in May 2012.

PROPOSAL

___________________________________________________________________________________

Rename Code table 3.2 as “Shape of the reference system” and add the following new entries:

Code table 3.2 – Shape of the reference system

Code figure	Meaning

9		Earth model assumed WGS84 with corrected geomagnetic coordinates (latitude and longitude) defined by Gustafsson et al., 1992

10	Sun assumed spherical with radius = 695,990,000 m (Allen, C.W., 1976 Astrophysical Quantities (3rd Ed.; London: Athlone)) and Stonyhurst latitude and longitude system with origin at the intersection of the solar central meridian (as seen from Earth) and the solar equator (Thompson, W, Coordinate systems for solar image data, A&A 449, 791–803 (2006)).

11	Sun assumed spherical with radius = 695,990,000 m (Allen, C.W., 1976 Astrophysical Quantities (3rd Ed.; London: Athlone)) and Carrington latitude and longitude system that rotates with a sidereal period of 25.38 days (Thompson, W, Coordinate systems for solar image data, A&A 449, 791–803 (2006)).

___________________________________________________________________________________

Add the following new entries to Code table 4.5:

Code table 4.5 - Fixed surface types and units

Code figure	Meaning

170	Ionospheric D-region level

171	Ionospheric E-region level

172	Ionospheric F1-region level

173	Ionospheric F2-region level

___________________________________________________________________________________

In Code table 0.0, rename existing entry #3 as “Satellite products” and add new entry #4:

Code table 0.0 - Discipline of processed data in the GRIB message, number of GRIB Master
	table

Code figure	Meaning

3	Satellite products

4	Space weather products

___________________________________________________________________________________

Add the following new entries to Code table 4.1:

Code table 4.1 - Parameter category by product discipline

| Product Discipline 4 – Space Weather Products |
| --- |
| Category (octet 10) | Description |
| 0 | Temperature |
| 1 | Momentum |
| 2 | Charged particle mass and number |
| 3 | Electric and magnetic fields |
| 4 | Energetic particles |
| 5 | Waves |
| 6 | Solar electromagnetic emissions |
| 7 | Terrestrial electromagnetic emissions |
| 8 | Imagery |
| 9 | Ion-neutral coupling |
| 10-191 | Reserved |
| 192-254 | Reserved for Local Use |
| 255 | Missing |

___________________________________________________________________________________

Add the following new entries to Code table 4.2:

Code table 4.2 - Parameter number by product discipline and parameter category

Product discipline 4 – Space weather products, parameter category 0: Temperature

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Temperature | K |
| 1 | Electron temperature | K |
| 2 | Proton temperature | K |
| 3 | Ion temperature | K |
| 4 | Parallel temperature | K |
| 5 | Perpendicular temperature | K |
| 6-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 1: Momentum

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Velocity magnitude (Speed) | m s-1 |
| 1 | 1st vector component of velocity (coordinate system dependent) | m s-1 |
| 2 | 2nd vector component of velocity (coordinate system dependent) | m s-1 |
| 3 | 3rd vector component of velocity (coordinate system dependent) | m s-1 |
| 4-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 2: Charged particle mass and number

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Particle number density | m-3 |
| 1 | Electron density | m-3 |
| 2 | Proton density | m-3 |
| 3 | Ion density | m-3 |
| 4 | Vertical electron content | m-2 |
| 5 | HF absorption frequency | Hz |
| 6 | HF absorption | dB |
| 9 | Spread F | m |
| 10 | h’F | m |
| 11 | Critical frequency | Hz |
| 13 | Scintillation | Numeric |
| 14-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 3: Electric and magnetic fields

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Magnetic field magnitude | T |
| 1 | 1st vector component of magnetic field | T |
| 2 | 2nd vector component of magnetic field | T |
| 3 | 3rd vector component of magnetic field | T |
| 4 | Electric field magnitude | V m-1 |
| 5 | 1st vector component of electric field | V m-1 |
| 6 | 2nd vector component of electric field | V m-1 |
| 7 | 3rd vector component of electric field | V m-1 |
| 8-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 4: Energetic particles

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Proton flux (differential) | (m2 s sr eV)-1 |
| 1 | Proton flux (integral) | (m2 s sr )-1 |
| 2 | Electron flux (differential) | (m2 s sr eV)-1 |
| 3 | Electron flux (integral) | (m2 s sr)-1 |
| 4 | Heavy ion flux (differential) | (m2 s sr eV/nuc)-1 |
| 5 | Heavy ion flux (integral) | (m2 s sr)-1 |
| 6 | Cosmic ray neutron flux | h-1 |
| 7-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 5: Waves

| Number | Parameter | Units |
| --- | --- | --- |
| 0-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 6: Solar electromagnetic emissions

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Integrated Solar Irradiance | W m-2 |
| 1 | Solar X-ray Flux (XRS Long) | W m-2 |
| 2 | Solar X-ray Flux (XRS Short) | W m-2 |
| 3 | Solar EUV Irradiance | W m-2 |
| 5 | Solar Spectral Irradiance | W m-2 nm-1 |
| 6 | F10.7 | W m-2 Hz-1 |
| 7 | Solar radio emissions | W m-2 Hz-1 |
| 8-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 7: Terrestrial electromagnetic emissions

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Limb intensity | m-2 s-1 |
| 1 | Disk intensity | m-2 s-1 |
| 2 | Disk intensity day | m-2 s-1 |
| 3 | Disk intensity night | m-2 s-1 |
| 4-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 8: Imagery

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | X-ray radiance | W sr-1 m-2 |
| 1 | EUV radiance | W sr-1 m-2 |
| 2 | H-alpha radiance | W sr-1 m-2 |
| 3 | White light radiance | W sr-1 m-2 |
| 4 | CaII-K radiance | W sr-1 m-2 |
| 5 | White light coronagraph radiance | W sr-1 m-2 |
| 6 | Heliospheric radiance | W sr-1 m-2 |
| 7 | Thematic mask | numeric |
| 8-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 9: Ion-neutral coupling

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Pedersen conductivity | S m-1 |
| 1 | Hall conductivity | S m-1 |
| 2 | Parallel conductivity | S m-1 |
| 3-191 | Reserved |  |
| 192-254 | Reserved for Local Use |  |
| 255 | Missing |  |