| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 – 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc 2.3 (1) rev ------------------------- ITEM 2.3 ENGLISH ONLY |
| --- | --- | --- |

Additions and modifications of templates and tables

Transverse Mercator GRIB2 Template

Submitted by Richard Weedon (UKMO)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for a new GRIB2 template for Tranverse Mercator Projections

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and recommend for validation

Transverse Mercator GRIB2 Template

Background

The United Kingdom Met Office use the Ordnance Survey of Great Britain’s coordinate

reference system (OSGB) for model output and observational data in a number of systems. This

coordinate reference system is a specific implementation of a Transverse Mercator projection.

To encode certain data outputs for transmission as GRIB2 messages, a new GRIB2 grid

definition template is proposed.

Proposal

A new GRIB2 grid definition template, capable of defining the OSGB coordinate reference

system.

Grid definition template 3.12 Transverse Mercator

Octet No.        Contents

| 15 | Shape of the Earth (see Code table 3.2) |
| --- | --- |
| 16 | Scale factor of radius of spherical Earth |
| 17 – 20 | Scaled value of radius of spherical Earth |
| 21 | Scale factor of major axis of oblate spheroid Earth |
| 22 – 25 | Scaled value of major axis of oblate spheroid Earth |
| 26 | Scale factor of minor axis of oblate spheroid Earth |
| 27 – 30 | Scaled value of minor axis of oblate spheroid Earth |
| 31 – 34 | Ni number of points along i-axis |
| 35 – 38 | Nj number of points along j-axis |
| 39 – 42 | LaR geographic latitude of reference point |
| 43 – 46 | LoR geographic longitude of reference point |
| 47 | Resolution and component flags (see Flag table 3.3) |
| 48 - 51 | m scale factor at reference point ratio of distance on map to distance on spheroid |
| 52 – 55 | XR false easting, i-direction coordinate of reference point [Note: units in 10-2 m] |
| 56 – 59 | YR false northing, j-direction coordinate of reference point, [Note: units in 10-2 m] |
| 60 | Scanning mode (flags see Flag table 3.4) |
| 61 – 64 | Di i-direction increment length, [Note: units in 10-3 m] |
| 65 – 68 | Dj j-direction increment length [Note: units in 10-3 m] |
| 69 – 72 | x1 i-direction coordinate of the first grid point [Note: units in 10-3 m] |
| 73 – 76 | y1 j-direction coordinate of the first grid point [Note: units in 10-3 m] |
| 77 – 80 | x2 i-direction coordinate of the last grid point [Note: units in 10-3 m] |
| 81 – 84 | y2 j-direction coordinate of the last grid point [Note: units in 10-3 m] |

Code Table 3.2:     Shape of the Earth

Code Figure           Meaning

...

9,                            Earth represented by the OSGB 1936 Datum, using

the Airy_1830 Spheroid,

the Greenwich meridian as 0 Longitude,

the Newlyn datum as mean sea level, 0 height

Ordnance Survey of Great Britain Coordinate Reference System

An example of use of this template would be encoding the OSGB CRS, which may be defined

using the following parameters:

PROJCS["British_National_Grid",

GEOGCS["GCS_OSGB_1936",

DATUM["D_OSGB_1936",

SPHEROID["Airy_1830",6377563.396,299.3249646]],

PRIMEM["Greenwich",0.0],

UNIT["Degree",0.0174532925199433]],

PROJECTION["Transverse_Mercator"],

PARAMETER["False_Easting",400000.0],

PARAMETER["False_Northing",-100000.0],

PARAMETER["Central_Meridian",-2.0],

PARAMETER["Scale_Factor",0.9996012717],

PARAMETER["Latitude_Of_Origin",49.0],

UNIT["Meter",1.0]]

This would be able to be encoded using the proposal detailed above.