| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.3.3(10) (2. IX. 2011) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

New BUFR/CREX entries for NPP data

Submitted by Jeff Ator (U.S.A.)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for new entries to the BUFR and CREX tables for use with NPP data.

________________________________________________________________

ACTION PROPOSED

The team is requested to discuss the content of this

document and recommend the contents for validation.

#### DISCUSSION

#### The NPOESS preparatory project (NPP) satellite is currently scheduled for launch on 25 October 2011.  In preparation for this long-awaited event, enhancements to the BUFR/CREX tables were previously proposed by the U.S./NESDIS for CrIS (Cross-track infrared sounder), ATMS (Advanced Technology Microwave Sounder) and VIIRS (Visible Infrared/Imager Radiometer Suite) data, and these were subsequently validated using simulated data and approved by the IPET-DRC for operational use.

#### NESDIS would now like to propose additional table entries for use with SST (Sea surface temperature), AOP (Aerosol optical thickness) and OMPS (Ozone mapping and profiler suite) data from NPP.  We request that the following table entries be reserved for use in validation, because we expect to initiate the validation process within the next 2-3 months.

#### PROPOSAL

#### Add new entries to Table D:

|  |  | SST (Sea surface temperature) data |
| --- | --- | --- |
| 3 10 063 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 01 034 | Identification of originating/generating sub-center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 2 01 133 | Increase bit width |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 33 082 | Geolocation quality flags |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 075 | Ascending/descending orbit qualifier |
|  | 0 08 013 | Day/night qualifier |
|  | 0 08 072 | Pixel(s) type |
|  | 0 33 084 | Pixel level quality flag |
|  | 0 07 062 | Depth below sea surface |
|  | 0 33 086 | Quality of pixel level retrieval |
|  | 0 22 043 | Sea/water temperature |
|  | 0 07 062 | Depth below sea surface (top of layer) |
|  | 0 07 062 | Depth below sea surface (bottom of layer) |
|  | 0 33 086 | Quality of pixel level retrieval |
|  | 0 22 043 | Sea/water temperature |

|  |  | AOT (Aerosol optical thickness) data |
| --- | --- | --- |
| 3 10 064 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 01 034 | Identification of originating/generating sub-center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 2 01 133 | Increase bit width |
|  | 0 05 041 | Scan line number |
|  | 0 05 043 | Field of view number |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 33 082 | Geolocation quality flags |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 075 | Ascending/descending orbit qualifier |
|  | 0 33 086 | Quality of pixel level retrieval |
|  | 0 08 029 | Surface type |
|  | 0 08 046 | Atmospheric chemical or physical constituent type |
|  | 0 33 085 | Aerosol optical thickness quality flags |
|  | 0 15 049 | Aerosol Angstrom wavelength exponent |
|  | 1 02 011 | Repeat the following 2 descriptors 11 times |
|  | 0 02 155 | Satellite channel wavelength |
|  | 0 15 024 | Optical depth |

|  |  | OMPS (Ozone mapping and profiler suite) nadir profile data |
| --- | --- | --- |
| 3 10 065 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating center |
|  | 0 01 034 | Identification of originating/generating sub-center |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 2 07 003 | Increase scale and bit width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 05 040 | Orbit number |
|  | 0 33 082 | Geolocation quality flags |
|  | 3 01 021 | Latitude, Longitude (high accuracy) |
|  | 2 01 129 | Increase bit width |
|  | 0 07 002 | Height or altitude |
|  | 2 01 000 | Cancel increase bit width |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 05 021 | Bearing or azimuth |
|  | 0 07 025 | Solar zenith angle |
|  | 0 05 022 | Solar azimuth |
|  | 0 08 075 | Ascending/descending orbit qualifier |
|  | 0 33 071 | Profile ozone quality |
|  | 0 33 070 | Total ozone quality |
|  | 0 20 021 | Type of preciptation |
|  | 0 15 045 | Sulfur dioxide |
|  | 0 15 046 | Volcano contamination index |
|  | 0 08 065 | Sun-glint indicator |
|  | 0 33 087 | Extent of satellite within South Atlantic anomaly |
|  | 0 08 003 | Vertical significance (satellite observations) |
|  | 0 10 004 | Pressure |
|  | 0 08 003 | Vertical significance (satellite observations) |
|  | 2 07 002 | Increase scale and bit width |
|  | 0 15 001 | Total ozone |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 1 05 012 | Repeat the following 5 descriptors 12 times |
|  | 0 10 040 | Number of retrieved layers |
|  | 0 10 004 | Pressure |
|  | 2 07 002 | Increase scale and bit width |
|  | 0 15 005 | Ozone p |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 08 046 | Atmospheric chemical or physical constituent type |
|  | 1 07 019 | Repeat the following 7 descriptors 19 times |
|  | 0 10 040 | Number of retrieved layers |
|  | 0 10 004 | Pressure |
|  | 0 08 090 | Decimal scale of following signficand |
|  | 2 07 006 | Increase scale and bit width |
|  | 0 15 008 | Significand of volumetric mixing ratio |
|  | 2 07 000 | Cancel increase scale and bit width |
|  | 0 08 090 | Decimal scale of following significand (“Missing” = cancel) |

Add new entry to Common Code Table C-13

Data Category				International subcategory

12	Surface data (satellite)			12	Sea surface temperature

Add new entries to Common Code Table C-14

62020 		Smoke – high absorption

62021		Smoke – low absorption

Add new bit to 0-33-082 - Geolocation quality flags

6	Within South Atlantic anomaly

#### Add new entries to Table B:

|  | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 15 045 | Sulfur dioxide | DU | 0 | 0 | 10 | DU | 0 | 4 |
| 0 15 046 | Volcano contamination index | Numeric | 0 | 0 | 10 | Numeric | 0 | 4 |
| 0 15 049 | Aerosol Angstrom wavelength exponent | Numeric | 4 | 0 | 16 | Numeric | 0 | 5 |
| 0 33 084 | Pixel level quality flags | Flag table | 0 | 0 | 16 | Flag table | 0 | 6 |
| 0 33 085 | Aerosol optical thickness quality flags | Flag table | 0 | 0 | 18 | Flag table | 0 | 6 |
| 0 33 086 | Quality of pixel level retrieval | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 33 087 | Extent of satellite within South Atlantic anomaly (based on climatological data) | Code table | 0 | 0 | 4 | Code table | 0 | 1 |

0-33-084 – Pixel level quality flags

| Bit | Meaning |
| --- | --- |
| 1-5 | Reserved |
| 6 | Bulk SST outside of validation range |
| 7 | Skin SST outside of validation range |
| 8 | Sensor Zenith Angle > 40 Degrees (Pixel is not within 40 degrees of Nadir and therefore is not of high quality) |
| 9 | Degradation - Horizontal Cell Size > 1.3km (HCS > 1.3 km, swath width > 1700 km, Sensor Zenith Angle > 50.3 degrees) |
| 10 | Exclusion: No Ocean in pixel |
| 11 | Degradation: AOT > 0.6 (AOT in horizontal cell > 0.6 on the slant path (AOT @550nm)) |
| 12 | Exclusion: Aerosol Optical Thickness (AOT)> 1.0 (AOT in horizontal cell > 1.0 on the slant path (AOT @550nm)) |
| 13 | Sun Glint present in pixel |
| 14 | Ice Concentration Threshold Exceeded (SST not retrieved due to ice concentration exceeding threshold in System Spec) |
| 15 | Thin Cirrus detected in pixel |
| All 16 | Missing value |

0-33-085 – Aerosol Optical Thickness quality flags

| Bit | Meaning |
| --- | --- |
| 1-5 | Reserved |
| 6 | Bright Surface in horizontal cell (OverLand only); Shallow or Turbid Water in horizontal cell (OverOcean only) |
| 7 | Solar Zenith Angle > 80 degrees = Exclusion (Quality of AOT/APSP degraded or AOT/APSP not retrieved due to pixels in horizontal cell with solar zenith angles greater than 80 degrees) |
| 8 | AOT in Degraded Range: 65<Solar Zenith Angle<=80 deg (Quality of AOT/APSP degraded due to pixels in horizontal cell with solar zenith angles greater than 65 but less than or equal to 80 degrees) |
| 9 | Fire Present in Horizontal Cell (Quality of AOT/APSP degraded or AOT/APSP not retrieved due to fire in horizontal cell) |
| 10 | Snow/Ice Present in Horizontal Cell (Quality of AOT/APSP degraded or AOT/APSP not retrieved due to snow/ice in horizontal cell) |
| 11 | Cloud Shadow Present in Horizontal Cell (Quality of AOT/APSP degraded or AOT/APSP not retrieved due to cloud shadows in horizontal cell) |
| 12 | Sun Glint Present in Horizontal Cell (Quality of AOT/APSP degraded or AOT/APSP not retrieved due to sun glint in horizontal cell) |
| 13 | Bad SDR Data Present in Horizontal Cell (Quality of AOT/APSP degraded or AOT/APSP not retrieved due to bad SDR data in horizontal cell) |
| 14 | Thin Cirrus Present in Horizontal Cell – Cirrus Contamination –(Quality of AOT/APSP degraded or AOT/APSP not retrieved due to thin cirrus in horizontal cell) |
| 15 | Cloud present in Adjacent Horizontal Cell (Quality of AOT/APSP possibly degraded due to adjacent clouds) |
| 16 | Cloud Contamination - Quality of AOT degraded or AOT not retrieved due to clouds (not including thin cirrus) in horizontal cell) |
| 17 | AOT/APSP is outside of the SystemSpecificationRange (Quality of AOT or APSP degraded due to AOT or APSP value being outside of Spec (and LUT) range |
| All 18 | Missing value |

0-33-086 - Quality of pixel level retrieval

| Code figure | Description |
| --- | --- |
| 0 | Not Retrieved |
| 1 | Excluded |
| 2 | Degraded |
| 3 | High Quality |
| 4-6 | Reserved |
| 7 | Missing value |

0-33-087

Extent of satellite within South Atlantic anomaly (based on Climatological data)

| Code Figure | Meaning |
| --- | --- |
| 0 | Less than or equal to 10% |
| 1 | Greater than 10% but less than or equal to 20% |
| 2 | Greater than 20% but less than or equal to 30% |
| 3 | Greater than 30% but less than or equal to 40% |
| 4 | Greater than 40% but less than or equal to 50% |
| 5 | Greater than 50% but less than or equal to 60% |
| 6 | Greater than 60% but less than or equal to 70% |
| 7 | Greater than 70% but less than or equal to 80% |
| 8 | Greater than 80% |
| 9-14 | Reserved |
| 15 | Missing value |