| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc. 3.3 (12) (07.IX.2011) ------------------------- ITEM ENGLISH ONLY |
| --- | --- | --- |

### Revision of Sequence 3 02 067

# Submitted by Sibylle Krebber (DWD)

________________________________________________________________

# Summary and Purpose of Document

This document contains a revised version of sequence 3 02 067 which was proposed last year for validation.

_________________________________________________________________

# ACTION PROPOSED

The meeting is requested to review the document and proposed the revised sequence for validation.

References:

- Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

- Final report of the second meeting of the inter-programme expert team on data representation and codes (IPET-DRC-II), Brasilia, Brazil, 31 August – 3 September 2010

- Document 3.3 (22) of IPET-DRC-II

#### Background and discussion

Last year a new sequence 3 02 067 was proposed, which is suitable for additional SYNOP data (especially data which can be encoded in section 3 of FM12-SYNOP).

After some discussion this sequence was thoroughly worked over by Eva Cervena and Sibylle Krebber in October 2010.

Especially the order of descriptors were changed. Instantaneous data were followed by period data. Regarding a significant change in wind speed and/or wind direction it is difficult to encode such phenomenon clearly in BUFR. For encoding mean wind speed a time period specification is needed (10 min period). At the same time other time specifications (e.g. time of occurrence of wind shift) are needed. Therefore time increments are used instead of time displacements to solve this problem.

With many thanks for Eva Cervena the revised version of sequence 3 02 067 is now proposed for validation.

#### Proposals

#### The existing sequence 3 02 067 for validation is to be replaced in BUFR table D by the

#### revised sequence:

| 3 02 067 |  |  | Additional synoptical parameters |  |  |
| --- | --- | --- | --- | --- | --- |
|  | 0 01 023 |  | Observation Sequence number |  | Numeric, 0 |
|  |  |  | Additional “instantaneous” data |  |  |
|  | 0 04 025 |  | Time period (= 0 minutes) |  | Minute, 0 |
|  | 0 02 177 |  | Method of snow depth measurement 0 Manual observation 1 Ultrasonic method 2 Video camera method 3-13 Reserved 14 Others 15 Missing value |  | Code table, 0 |
|  |  |  | Additional present weather |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 003 |  | Present weather | 960ww 961ww | Code table, 0 |
|  |  |  | Visibility in different directions |  |  |
|  | 1 02 000 |  | Delayed replication of 2 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 05 021 |  | Bearing or azimuth | 981VV-988VV | Degreetrue, 0 |
|  | 0 20 001 |  | Horizontal visibility | VV | m, –1 |
|  | 0 05 021 |  | Bearing or azimuth (=set to missing to cancel previous entry) |  | Degreetrue, 0 |
|  |  |  | Sea data (Observations from a coastal station) |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |  |
|  |  | 0 02 038 | Method of sea/water temperature measurement |  | Code table, 0 |
|  |  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) |  | m, 2 |
|  |  | 0 22 043 | Sea/water temperature | 222.. 0sTwTwTw | K, 2 |
|  |  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) |  | m, 2 |
|  | 1 03 000 |  | Delayed replication of 3 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 33 041 |  | Attribute of following value |  | Code tabel, 0 |
|  | 0 20 058 |  | Visibility seawards from a coastal station | 980VsVs | m,-1 |
|  | 0 22 061 |  | State of the sea | 924SVs | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 022 |  | Wind waves |  |  |
|  |  | 0 22 002 | Direction of wind waves |  | Degreetrue, 0 |
|  |  | 0 22 012 | Period of wind waves | 222.. 2PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves | HwHw | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 023 |  | Swell waves |  |  |
|  |  | 0 22 003 | Direction of swell waves | 222.. 3dw1dw1 dw2dw2 | Degreetrue, 0 |
|  |  | 0 22 013 | Period of swell waves | 4Pw1Pw1, 5Pw2Pw2 | s, 0 |
|  |  | 0 22 023 | Height of swell waves | Hw1Hw1, Hw2Hw2 | m, 1 |
|  |  |  | Clouds | 941CDp, 943CLDp |  |
|  | 1 05 000 |  | Delayed replication of 5 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 137 |  | Evolution of Clouds | 940Cn3 | Code table, 0 |
|  | 0 20 012 |  | Cloud type (C) | 941C, 943CL | Code table, 0 |
|  | 0 20 090 |  | Special clouds | 993CS | Code table, 0 |
|  | 0 20 136 |  | Supplementary Cloud type | 949C0, 949Ca, 950Nmn3, 951Nv | Code table, 0 |
|  |  |  | Additional “period” data |  |  |
|  | 0 04 025 |  | Time period in minutes ( = reference period of fresh fallen snow ) 1) |  | Minute, 0 |
|  | 0 13 012 |  | Depth of fresh snow 1) |  | m, 2 |
|  |  |  | Additional wind data |  |  |
|  | 0 04 025 |  | Time period in minutes ( =-60 ) |  | Minute, 0 |
|  | 0 11 042 |  | Maximum wind gust speed (10 min mean wind) | 912ff | m s-1, 1 |
|  |  |  | 902tt 912ff .. mandatory ff>=18 |  |  |
|  | 1 04 000 |  | Delayed replication of 4 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 902tt | Minute, 0 |
|  | 0 11 042 |  | Maximum wind gust speed (10 min mean wind) | 912ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  |  |  | Significant change in wind speed and/or direction | e.g. 913ff 904tt 913ff |  |
|  | 1 15 000 |  | Delayed replication of 15 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 015 |  | Time increment (=-xx1 ) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=22 time of occurrence of wind shift) |  | Code table, 0 |
|  | 0 04 015 |  | Time increment (=+xx2 ) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (= 0 minutes) |  | Minute, 0 |
|  | 0 04 015 |  | Time increment (=+(xx1-xx2), non negative to reset the time to the actual time ) |  | Minute, 0 |
|  |  |  | Additional weather |  |  |
|  | 1 03 000 |  | Delayed replication of 6 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 20 003 |  | Present weather | 962ww, 963w1w1, 964ww, 965w1w1, 966ww, 967w1w1 | Code table, 0 |
|  |  |  | Additional 9SpSpspsp groups |  |  |
|  | 1 11 000 |  | Delayed replication of 13 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 05 021 |  | Bearing or azimuth * | Da, Dp | Degreetrue, 0 |
|  | 0 05 021 |  | Bearing or azimuth * | Da, Dp | Degreetrue, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 024 |  | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent, 5 = Severe) |  | Code table, 0 |
|  | 0 20 025 |  | Obscuration |  | Flag table, 0 |
|  | 0 20 026 |  | Character of obscuration |  | Code table, 0 |
|  | 0 20 027 |  | Phenomenon occurrence |  | Flag table, 0 |
|  | 0 20 063 |  | Special phenomena |  | Code table, 0 |