| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.3.3 (14) rev (12. VIII. 2011) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Request of new entries in Common Code Table C-2 for radiosondes of China

Submitted by Fang ZHAO (China)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for new entries in Common Code Table C-2 to identify the radiosondes of China.

________________________________________________________________

ACTION PROPOSED

The Expert Team is invited to discuss the content of this document and recommend the proposed new entries as pre-operational.

Background

- Second meeting of the IPET-DRC recommended the need for new entries in Common Code Table C-2 for Chinese 1680 MHz radiosonde system and suggested China to submit a respective proposal (5.1.4.3 in final report).

- Two issues were raised for TEMP report of China:

- No Sections 6 and 7 in FM 35 TEMP reports, and also with missing values for descriptors 002011, 002013, 002014 and 002003 in BUFR.

- Not reporting wind significant levels in TTBB and TTDD parts of TEMP messages, either for BUFR.

PROPOSAL

It is proposed to add new entries in Common Code Table C-2 to identify the radiosondes of China:

| date of assignment of number | code figure for rara | code figure for BUFR (code table 0 02 011) | Radiosonde type |
| --- | --- | --- | --- |
| ??/05/2012 | 31 | 131 | Taiyuan GTS1-1 (China ) |
| ??/05/2012 | 32 | 132 | Shanghai GTS1 (China) |
| ??/05/2012 | 33 | 133 | Nanjing GTS1-2 (China) |

Note:

- Code figure 32 is re-allocated.

- The brief introduction of the 3 radiosondes are as follows:

| Type | Introduction | Manufacturer |
| --- | --- | --- |
| GTS1 | the thermistor as temperature sensor the humidity sensitive resistor as humidity sensor the silicon piezoresistance as pressure sensor operating at 1675MHz and compatible with GFE(L) secondary wind-finding radar | Shanghai Changwang Weather Technology Co., Ltd. |
| GTS1-1 |  | Taiyuan Radio factory |
| GTS1-2 | the thermistor as a temperature sensor the humidity sensitive capacitor as a humidity sensor the diaphragm capsule capacitor as a pressure sensor operating at 1675MHz and compatible with GFE(L) secondary wind-finding radar | Nanjing Daqiao Machine Co., Ltd. |

Conclusion

The meeting is invited to agree to the proposed modifications to Common Code Table C-2, and to consider them as pre-operational.

Coming actions

The upper-air observation division of the Department of Integrated Observations of CMA confirms that after the approval of the proposal, the coding software in each upper-air observation site would be modified to fix the absence of Section 6 and wind significant levels in TAC, and also for BUFR after converted from TAC at national level. It would be done at the end of this year.

Acknowledgement

We wish to thank Mr. Alexander Kats (Russian Federation) for his concern of all these issues and the efforts to push the fix of the problems with many comments and suggestions for us.