| WORLD METEOROLOGICAL ORGANIZATION _________________________ CBS INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES (IPET-DRC) THIRD MEETING Melbourne, Australia, 20-23 September 2011 |  | IPET-DRC-III/Doc. 3.3 (15) (12.IX.2011) ___________ ITEM 3.3 ENGLISH only |
| --- | --- | --- |

BUFR template for CRYOSAT-2 SIRAL altimeter

(Submitted by Enrico Fucile (ECMWF))

Summary and the Purpose of the Document A proposal is made for a BUFR template for SIRAL altimeter.

ACTION PROPOSED

The team is invited to discuss the content of the proposal and approve the proposed template and table entries for validation.

# Background and discussion

CryoSat-2 is one of the European Space Agency (ESA) Earth Explorer Opportunity Missions. It carries a radar altimeter instrument (SIRAL) capable of sensing surface wind speed and significant wave height (SWH) among other parameters. Both parameters are very valuable for the meteorological and ocean wave communities. They can be used for the validation of the numerical atmospheric and ocean wave models.

ESA has decided to make available this useful type of data to the meteorological community. However, it lacks the necessary expertise to prepare and submit a BUFR template and has reached an agreement with ECMWF that the latter will do this on behalf of ESA.

# Proposal

The following new table B descriptors are proposed for validation.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 01 040 | Processing centre id code | CCITTIA5 | 0 | 0 | 48 | Character | 0 | 6 |
| 0 02 139 | SIRAL instrument configuration | Code Table | 0 | 0 | 2 | Code Table | 0 | 1 |
| 0 25 180 | LRM mode percent | % | 2 | 0 | 16 | % | 2 | 5 |
| 0 25 181 | L2 processing flag | Code Table | 0 | 0 | 2 | Code Table | 0 | 1 |
| 0 25 182 | L1 processing flag | Code Table | 0 | 0 | 2 | Code Table | 0 | 1 |
| 0 25 183 | L1 processing quality | % | 2 | 0 | 14 | % | 2 | 5 |
| 0 25 184 | L2 product status | Code Table | 0 | 0 | 2 | Code Table | 0 | 1 |
| 0 10 079 | Off nadir angle of the satellite from platform data | Degree | 4 | 0 | 16 | Degree | 4 | 5 |
| 0 21 176 | High frequency variability correction | m | 3 | 0 | 16 | m | 3 | 5 |
| 0 21 177 | Corrected OCOG backscatter coefficient | dB | 2 | 0 | 16 | dB | 2 | 5 |
| 0 21 178 | std of 20 HZ OCOG backscatter coefficient | dB | 2 | 0 | 16 | dB | 2 | 5 |
| 0 21 179 | Number of 20 HZ valid points for OCOG backscatter coefficient | Numeric | 0 | 0 | 16 | Numeric | 0 | 5 |
| 0 21 180 | Number of 20 HZ valid points for ocean backscatter coefficient | Numeric | 0 | 0 | 8 | Numeric | 0 | 3 |
| 0 21 181 | 20 Hz ocean backscatter coefficient | dB | 2 | 0 | 16 | dB | 2 | 5 |
| 0 21 182 | 20 Hz Ku-band peakiness | Numeric | 3 | 0 | 16 | Numeric | 3 | 5 |
| 0 22 142 | Square of significant wave height | m2 | 3 | -33554432 | 26 | m2 | 3 | 8 |
| 0 22 143 | Std of 20 Hz SWH-squared | m2 | 3 | -8388608 | 24 | m2 | 3 | 8 |
| 0 22 144 | Number of 20 Hz valid points for SWH squeared | Numeric | 0 | 0 | 9 | Numeric | 0 | 3 |
| 0 22 145 | std of 20 Hz ocean range | m | 3 | -33554432 | 31 | m | 3 | 10 |
| 0 22 146 | OCOG range | m | 3 | 0 | 31 | m | 3 | 10 |
| 0 22 147 | std of 20Hz OCOG range | m | 3 | -8388608 | 31 | m | 3 | 10 |
| 0 22 148 | Number of 20 Hz valid points for ocean range | Numeric | 0 | 0 | 9 | Numeric | 0 | 3 |
| 0 22 149 | 20 Hz significant wave height squeared | m2 | 3 | -33554432 | 26 | m2 | 3 | 8 |

0 02 139

SIRAL INSTRUMENT CONFIGURATION

| Code Figure | Meaning |
| --- | --- |
| 0 | SIRAL NOMINAL |
| 1 | SIRAL REDUNDANT |
| 2 | MISSING VALUE |

0 25 181

L2 PROCESSING FLAG

| Code Figure | Meaning |
| --- | --- |
| 0 | OK |
| 1 | PERCENTAGE OF L2B RECORDS FREE OF PROCESSING ERRORS IS LESS THAN ACCEPTABLE THRESHOLD |
| 2 | MISSING VALUE |

0 25 182

L1 PROCESSING FLAG

| Code Figure | Meaning |
| --- | --- |
| 0 | OK |
| 1 | PERCENTAGE OF L1B RECORDS FREE OF PROCESSING ERRORS IS LESS THAN ACCEPTABLE THRESHOLD |
| 2 | MISSING VALUE |

0 25 184

L2 PRODUCT STATUS

| Code Figure | Meaning |
| --- | --- |
| 0 | OK |
| 1 | PRODUCT AS A DURATION SHORTER THAN THE INPUT PRODUCT |
| 2 | MISSING VALUE |

The following BUFR template is proposed for validation.

TABLE		TABLE		ELEMENT NAME

REFERENCE	REFERENCE

F X Y

(CRYOSAT-2 Siral altimeter)

3 12 199   	0 01 007  	satellite id

0 02 019   	Satellite instrument

0 02 139   	SIRAL instrument configuration

0 01 096   	Acquisition station name

0 01 040   	Processing centre

0 25 061   	Software version

0 05 040   	Orbit number

0 05 044   	Satellite cycle number

0 08 075   	Ascending flag

0 08 077   	Altimeter surface type flag

0 04 001   	Year

0 04 002   	Month

0 04 003   	Day

0 04 004   	Hour

0 04 005   	Minute

0 04 006   	Second

0 05 001   	Latitude

0 06 001   	Longitude

0 10 081   	Altitude of COG

0 22 156   	Significant wave height

0 22 142   	Square of significant wave height

1 01 020

0 22 149   	20 Hz significant wave height squared

0 22 143   	std of 20 Hz SWH-squared

0 22 144   	Number of 20Hz valid points for SWH squeared

0 21 137   	Corrected ocean backscatter coefficient

1 01 020

0 21 181   	20 Hz ocean backscatter coefficient

0 21 138   	std Corrected ocean backscatter coefficient

0 21 180   	Number of 20 HZ valid points for ocean backscatter coefficient

0 21 177   	Corrected OCOG backscatter coefficient

0 21 178   	std of 20 HZ OCOG backscatter coefficient

0 21 179   	Number of 20 HZ valid points for OCOG backscatter coefficient

0 10 079   	Off nadir angle of the satellite from platform data

0 10 085   	Mean sea surface height

0 10 086   	Geoid height

0 10 087   	Ocean depth/land elevation

0 10 089   	Total geocentric ocean tide height (solution 2)

0 10 090   	Long perion tide height

0 10 091   	Tidal loading height

0 10 092   	Solid earth tide height

0 10 093   	Geocentric pole tide height

0 11 097   	Altimeter wind speed

0 21 093   	Peakiness ( average of 20 Hz values)

1 01 020

0 21 182   	20 Hz ku band peakiness ( 20 values)

0 33 053   	Ocean retracking quality

0 22 151   	Range to ocean surface

0 22 145   	STD of 20 Hz ocean range

0 22 148   	Number of 20 Hz valid points for ocean range

0 22 146   	OCOG range

0 22 147   	STD of 20Hz OCOG range

0 25 126   	Dry tropospheric correction

0 25 128   	Model wet tropospheric correction

0 25 127   	Inverse barometer correction

0 21 176   	High frequency variability correction

0 25 132   	Ionospheric correction

0 25 133   	Sea state bias correction

0 25 182   	L1 processing flag

0 25 183   	L1 processing quality

0 25 180   	LRM mode percent

0 25 184   	L2 product status

0 25 181   	L2 processing flag

0 33 080   	L2 processing quality