| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.3.3(2) (5. VIII. 2011) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Validation of BUFR/CREX descriptors related to AWS

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains BUFR/CREX descriptors that were proposed for validation by the sixth meeting of ET AWS (Geneva, 22 to 25 June 2010) and with some modifications by the second meeting of IPET-DRC  (Brasilia, 31 August to 3 September 2010).

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and recommend the included BUFR/CREX descriptors as pre-operational.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2

[2] Sixth meeting of Expert Team on Requirements and Implementation AWS Platforms.

Final Report, Geneva, 22 to 25 June 2010.

[3] Second meeting of the Inter-Programme Expert Team on Data Representation and

Codes. Final Report, Brasilia, 31 August to 3 September 2010.

[4] International Meteorological Vocabulary, WMO-No. 182

5 - 8  December 2005ntion on International Civil Aviation

1. Background

14th Session of the Commission for Basic Systems (Dubrovnik, Croatia, 25 March to 2 April 2009) reviewed the Functional Specifications for Automatic Weather Stations and adopted draft Recommendation 6.1/2 (CBS-XIV).

A document was submitted to ET-AWS-6 (Geneva, 22 to 25 June 2010), containing detailed analysis of the requirements for representation of the listed variables, a revised version of the Functional Specifications for AWS and a proposal for several new BUFR/CREX descriptors. The ET-AWS-6 meeting examined carefully these proposals, agreed with the proposed new BUFR/CREX descriptors and procedures for representation of the listed variables, and suggested some modifications of the requirements.

The Second meeting of the Inter-Programme Expert Team on Data Representation and Codes approved the proposed or modified BUFR/CREX descriptors for validation. The ET AWS members were encouraged to participate actively in the validation process of the proposed new descriptors.

BUFR messages have been created in the Czech Hydrometeorological Institute (CHMI) using the encoding/decoding software of CHMI and ECMWF. These messages contain extreme values of the elements as requested in the Functional Specifications for AWS, which documents the capability of the validated descriptors to meet the requirements. The validation process lead to changing the specification for “Soil heat flux”; no other requirements have been expressed by the ET-AWS. Consequently the descriptors included in paragraph 2 of this document are suggested for being pronounced pre-operational.

The current version of the Functional Specifications for AWS is included in the Annex.

The problem of terminology for radiation is still to be solved.

2. BUFR/CREX descriptors proposed to become pre-operational

For Temperature

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 12 120 | Ground temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |
| 0 12 131 | Snow temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |

For Humidity

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 110 | Mass mixing ratio | % | 0 | 0 | 7 | % | 0 | 3 |
| 0 13 111 | Soil moisture | g kg-1 | 0 | 0 | 10 | g kg-1 | 0 | 4 |
| 0 13 112 | Object wetness duration | s | 0 | 0 | 17 | s | 0 | 5 |

For Radiation

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 052 | Global upward solar radiation, integrated over period specified | J m-2 | -2 | –1048574 | 20 | J m-2 | -2 | 7 |
| 0 14 053 | Net radiation (high accuracy), integrated over period specified | J m-2 | -2 | –1048574 | 21 | J m-2 | -2 | 7 |
| 0 14 054 | Photosynthetically active radiation, integrated over period specified | J m-2 | –3 | 0 | 16 | J m-2 | –3 | 5 |
| 0 14 056 | Background luminance | Cd m-2 | 0 | 0 | 18 | Cd m-2 | 0 | 6 |
| 0 14 057 | Soil heat flux | J m-2 | –2 | –1048574 | 21 | J m-2 | –2 | 7 |
| 0 14 072 | Global UV irradiation | J m-2 | 0 | –4000000 | 23 | J m-2 | 0 | 7 |
| 0 02 072 | Spectrographic width | m | 13 | 0 | 30 | m | 13 | 10 |

With a Note under Class 14:

- Global UV irradiation (0 14 072) is UV energy integrated over period specified for spectral band specified. 0 14 072 shall be preceded by a time period descriptor and by 0 02 071 (Spectrographic wavelength) and 0 02 072 (Spectrographic width). E.g. If 0 14 072 is used for Global UV-B irradiation, 0 02 071 and 0 02 072 shall specify spectral band 280 to 315 nm.

For Clouds

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 130 | Cloud hydrometeor concentration | Numeric | 0 | 0 | 10 | Numeric | 0 | 3 |
| 0 20 131 | Effective radius of cloud hydrometeors | m | 5 | 0 | 6 | m | 5 | 2 |
| 0 20 132 | Cloud liquid water content | kg m-3 | 5 | 0 | 11 | kg m-3 | 5 | 4 |
| 0 20 093 | Height of inversion | m | -1 | 0 | 8 | m | -1 | 3 |

With a Note under Class 20:

Cloud hydrometeor concentration 0 20 130 represents the number of hydrometeors in 1 dm3.

For Precipitation

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 114 | Rate of ice accretion | kg m-2 h-1 | 1 | 0 | 11 | kg m-2 h-1 | 1 | 4 |
| 0 13 118 | Depth of freshsnow (high accuracy) | m | 3 | 0 | 14 | m | 3 | 5 |

The name of 0 20 032 is requested to be changed from the current “Rate of ice accretion” to “Rate of ice accretion (estimated)".

For Obscuration

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 133 | Hydrometeor radius | m | 5 | 0 | 6 | m | 5 | 2 |
| 0 15 029 | Extinction coefficient | m-1 | 9 | 0 | 30 | m-1 | 9 | 10 |
| 0 15 051 | Meteorological Optical Range | m | 0 | 0 | 18 | m | 0 | 6 |

For Lightning

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 126 | Lightning rate of discharge | h-1 | 0 | 0 | 23 | h-1 | 0 | 7 |
| 0 20 127 | Lightning - distance from station | m | -3 | 0 | 8 | m | -3 | 3 |
| 0 20 128 | Lightning - direction from station | Degree true | 1 | 0 | 12 | Degree true | 1 | 4 |
| 0 20 119 | Lightning discharge polarity | Code table | 0 | 0 | 2 | Code table | 0 | 1 |

0 20 119 - Lightning discharge polarity:

| Code figure |  |
| --- | --- |
| 0 | Not defined |
| 1 | Positive |
| 2 | Negative |
| 3 | Missing value |

For Hydrologic and marine data

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 23 040 | Flow discharge – river | m3 s-1 | 1 | 0 | 22 | m3 s-1 | 1 | 7 |
| 0 23 041 | Flow discharge – well | m3 s-1 | 3 | 0 | 16 | m3 s-1 | 3 | 5 |
| 0 13 074 | Ground water level | m | 2 | 0 | 18 | m | 2 | 6 |
| 0 12 132 | Ice surface temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |
| 0 13 115 | Ice thickness | m | 2 | 0 | 19 | m | 2 | 6 |
| 0 20 135 | Ice mass (on a rod) | kg m-1 | 1 | 0 | 10 | kg m-1 | 1 | 3 |
| 0 13 117 | Snow density (liquid water content) | kg m-3 | 0 | 0 | 10 | kg m-3 | 0 | 3 |

With a Note under Class 13:

Ice thickness 0 13 115 shall be preceded by 0 08 029 (Surface type) set to 11, 12, 13 or 14 to specify river, lake, sea or glacier, respectively.

The name of 0 08 029 has been changed to “Surface type” and the following code figures introduced:

0 08 029 - Surface type:

| Code figure |  |
| --- | --- |
| 11 | river |
| 12 | lake |
| 13 | sea |
| 14 | glacier |

For Other

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 24 014 | Gamma radiation dose rate | nSv h-1 | 1 | 0 | 14 | nSv h-1 | 1 | 4 |

With a Note under Class 24:

Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.

3. Radiation terminology

In June 2010, Mr. Karl Monnik, the Chair of ET-AWS, distributed a proposal for replacing the terms “radiation” and “irradiation” in the names of the descriptors from Class 14, currently in the stage of validation, by “radiant exposure".

According to radiation experts of CHMI, the following terms could be used (all of them correct, having identical meaning) :

“radiation integrated over period specified” or

"irradiation" or

“radiant exposure".

If the term “radiat exposure" were to be used in the names of BUFR/CREX descriptors, it would have to be applied not only in the descriptors proposed for validation, but also in the already operational entries of Class 14.

According to International Meteorological Vocabulary, WMO-No. 182:

Radiant exposure (at a point of surface, for a given duration)           [J m-2]

[irradiation]

Time integral of irradiance. For constant irradiance, it is the product of irradiance and its duration.

Irradiance (at a point of surface)                                                          [W m-2]

[flux of radiation per unit area (at a point of surface)]

Quotient of the radiant flux incident on an element of the surface containing the point by the area of that element.

Annex

Revised Annex to draft Recommendation 6.1/2 (CBS-XIV) – JULY 2011

Functional Specifications for Automatic Weather Stations

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | Status 5) |
| --- | --- | --- | --- | --- | --- |
| ATMOSPHERIC PRESSURE |  |  |  |  |  |
| Atmospheric Pressure | 500 – 1080 hPa | 10 Pa | I, V | 0 10 004 | OP |
| TEMPERATURE 9) |  |  |  |  |  |
| Ambient air temperature (over specified surface) 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 101 | OP |
| Dew-point temperature 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 103 | OP |
| Ground (surface) temperature (over specified surface) 14) | -80 °C – +80 °C | 0.1 K | I, V | 0 12 120 | VAL |
| Soil temperature14) | -50 °C – +50 °C | 0.1 K | I, V | 0 12 130 | OP |
| Snow temperature 14) | -80 °C – 0 °C | 0.1 K | I, V | 0 12 131 | VAL |
| Water temperature - river, lake, sea, well | -2 °C – +100 °C | 0.1 K | I, V | 0 13 082 or 0 22 043 | OP OP |
| HUMIDITY 9) |  |  |  |  |  |
| Relative humidity | 0 – 100% | 1% | I, V | 0 13 003 | OP |
| Mass mixing ratio | 0 – 100% | 1% | I, V | 0 13 110 | VAL |
| Soil moisture | 0 – 103 g kg-1 | 1 g kg-1 | I, V | 0 13 111 | VAL |
| Water vapour pressure | 0 – 100 hPa | 10 Pa | I, V | 0 13 004 | OP |
| Evaporation/evapotranspiration | 0 – 0.2 m | 0.1 kg m-2 0.0001 m | T | 0 13 033 | OP |
| Object wetness duration | 0 – 86 400 s | 1 s | T | 0 13 112 | VAL |
| WIND |  |  |  |  |  |
| Direction | 0 11,13); 1( – 360( | 1( | I, V | 0 11 001 | OP |
| Speed | 0 – 75 m s-1 | 0.1 m s-1 | I, V | 0 11 002 | OP |
| Gust Speed | 0 – 150 m s-1 | 0.1 m s-1 | I, V | 0 11 041 | OP |
| X,Y component of wind vector Z component of wind vector (horizontal and vertical profile) | -150 – 150 m s-1 -40 – 40 m s-1 | 0.1 m s-1 | I, V | 0 11 003 0 11 004 0 11 006 | OP OP OP |
| Turbulence type (Low levels and wake vortex) 16) | up to 15 types | BUFR Table Not specified yet | I, V | - | N |
| Turbulence intensity 16) | up to 15 types | BUFR Table Not specified yet | I, V | - | N |
| RADIATION 6) |  |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 | OP |
| Background luminance | 0 – 1∙105 Cd m-2 | 1 Cd m-2 | I, V | 0 14 056 | VAL |
| Global downward solar radiation | 0 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 028 | OP |
| Global upward solar radiation | -1∙108 – 0 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 052 | VAL |
| Diffuse solar radiation | 0 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 029 | OP |
| Direct solar radiation | 0 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 030 | OP |
| Downward long-wave radiation | 0 – 6∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | OP |
| Upward long-wave radiation | -6∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | OP |
| Net radiation | -1∙108 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 053 | VAL |
| UV-B radiation 8) | 0 – 26∙104 J m-2 | 1 J m-2 | I, T, V | 0 14 072 | VAL |
| Photosynthetically active radiation 22) | 0 – 6∙107 J m-2 | 1∙103 J m-2 | I, T, V | 0 14 054 | VAL |
| Surface albedo | 0 – 100% | 1% | I, V | 0 14 019 | OP |
| Soil heat Flux | -1∙108 – 1∙108 J m-2 | 1. 102 J m-2 | I, T, V | 0 14 057 | VAL |

| CLOUDS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Cloud base height | 0 – 30 km | 10 m | I, V | 0 20 013 | OP |
| Cloud top height | 0 – 30 km | 10 m | I, V | 0 20 014 | OP |
| Cloud type, convective vs. other types | up to 30 classes | BUFR Table | I | 0 20 012 | OP |
| Cloud hydrometeor concentration | 1 – 700 hydrometeors dm-3 | 1 hydrometeor dm-3 | I, V | 0 20 130 | VAL |
| Effective radius of cloud hydrometeors | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 131 | VAL |
| Cloud liquid water content | 1∙10-5–1.4∙10-2 kg m-3 | 1∙10-5 kg m-3 | I, V | 0 20 132 | VAL |
| Optical depth within each layer | Not specified yet | Not specified yet | I, V | - | N |
| Optical depth of fog | Not specified yet | Not specified yet | I, V | - | N |
| Height of inversion | 0 – 1 000 m | 10 m | I, V | 0 20 093 | VAL |
| Cloud cover | 0 – 100% | 1% | I, V | 0 20 010 | OP |
| Cloud amount | 0 – 8/8 | 1/8 | I, V | 0 20 011 | OP |
| PRECIPITATION |  |  |  |  |  |
| Accumulation 7) | 0 – 1600 mm | 0.1 kg m-2, 0.0001 m | T | 0 13 011 | OP |
| Depth of fresh snowfall | 0 –1000 cm | 0.001 m | T | 0 13 118 | VAL |
| Duration | up to 86 400 s | 60 s | T | 0 26 020 | OP |
| Size of precipitating element 17) | 1∙10-3 – 0.25 m | 1∙10-3 m | I, V | 0 13 058 0 20 066 | OP OP |
| Intensity - quantitative | 0 – 2000 mm h-1 | 0.1 kg m-2 s-1, 0.1 mm h-1 | I, V | 0 13 155 | OP |
| Type | up to 30 types | BUFR Table | I, V | 0 20 021 | OP |
| Rate of ice accretion | 0 – 1 kg dm-2 h-1 | 1∙10-3 kg dm-2 h-1 | I, V | 0 13 114 | VAL |
| OBSCURATIONS |  |  |  |  |  |
| Obscuration type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Hydrometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Lithometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Hydrometeor radius | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 133 | VAL |
| Extinction coefficient | 0 – 1 m-1 | 0.00001 m-1 | I, V | 0 15 029 | VAL |
| Meteorological Optical Range 10) | 1 – 100 000 m | 1 m | I, V | 0 15 051 | VAL |
| Runway visual range | 1 – 4 000 m | 1 m | I, V | 0 20 061 | OP |
| Other weather type | up to 18 types | BUFR Table | I, V | 0 20 023 | OP |
| LIGHTNING |  |  |  |  |  |
| Lightning rates of discharge | 0 – 100 000 | h-1 | I, V | 0 20 126 | VAL |
| Lightning discharge type (cloud to cloud, cloud to surface) | 3 types | BUFR Code Table | I, V | 0 20 023 | OP |
| Lightning discharge polarity | 2 types | BUFR Code Table | I, V | 0 20 119 | VAL |
| Lightning discharge energy | Not specified yet | Not specified yet | I, V | - | N |
| Lightning - distance from station | 0 – 3∙104 m | 103 m | I, V | 0 20 127 | VAL |
| Lightning - direction from station | 1( – 360( | 1 degree | I, V | 0 20 128 | VAL |

| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Flow discharge – river | 0 – 2.5∙105 m3 s-1 | 0.1 m3 s-1 | I, V | 0 23 040 | VAL |
| Flow discharge – well | 0 – 50 m3 s-1 | 0.001 m3 s-1 | I, V | 0 23 041 | VAL |
| Ground water level | 0 – 1 800 m | 0.01 m | I, V | 0 13 074 | VAL |
| Ice surface temperature 14) | -80 °C – +0 °C | 0.5 K | I, V | 0 12 132 | VAL |
| Ice thickness - river, lake 15) | 0 – 50 m | 0.01 m | I, V | 0 08 029 0 13 115 | VAL |
| Ice thickness - glacier, sea 15) | 0 – 4 270 m | 1 m | I, V | 0 08 029 0 13 115 | VAL |
| Water level | 0 – 100 m | 0.01 m | I, V | 0 13 071 0 13 072 | OP OP |
| Wave height | 0 – 50 m | 0.1 m | V | 0 22 021 | OP |
| Wave period 18) | 0 – 100 s | 1 s | V | 2 01 129 0 22 011 2 01 000 | OP |
| Wave direction | 0 13); 1 – 360 degrees | 1 degrees | V | 0 22 001 | OP |
| 1D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | V, T | 2 01 135 0 22 069 2 01 000 | OP |
| 2D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | V, T | 2 01 135 0 22 069 2 01 000 | OP |
| Water practical salinity 18) | 0 – 400 psu12 | 10-3 psu | I, V | 2 01 130 0 22 064 2 01 000 | OP |
| Water conductivity 18) | 0 – 600 S m-1 | 10-6 S m-1 | I, V | 2 01 132 0 22 066 2 01 000 | OP |
| Water pressure 18) 19) | 0 – 11x107 Pa | 100 Pa | I, V | 2 07 001 0 22 065 2 07 000 | OP |
| Ice thickness 18) | 0 – 3 m | 0.015 m | T | 2 01 133 2 02 129 0 20 031 2 02 000 2 01 000 | OP |
| Ice mass | 0 – 50 kg m-1 | 0.5 kg m-1 (on 32 mm rod) | T | 0 20 135 | VAL |
| Snow density (liquid water content) | 100 – 700 kg m-3 | 1 kg m-3 | T | 0 13 117 | VAL |
| Tidal elevation with respect to local chart datum 18) | -10 – +30 m | 0.001 m | I, V | 2 01 129 0 22 038 2 01 000 | OP |
| Tidal elevation with respect to national land datum 18) | -10 – +30 m | 0.001 m | I, V | 2 01 129 0 22 037 2 01 000 | OP |
| Meteorological residual tidal elevation (surge or offset) 18) 20) | -10 – +16m | 0.001 m | I, V | 0 22 040 Note 20) | OP |
| Ocean Current - Direction | 0 13); 1( – 360( | 1( | I, V | 0 22 004 or 0 22 005 | OP OP |
| Ocean Current - Speed | 0 – 10 m s-1 | 0.01 m s-1 | I, V | 0 22 031 or 0 22 032 | OP OP |
| OTHER SURFACE VARIABLES |  |  |  |  |  |
| Runway conditions | up to 10 types | BUFR Table | I, V | 0 20 085 | OP |
| Braking action/friction coefficient | up to 7 types | BUFR Table | I, V | 0 20 089 | OP |
| State of ground | up to 30 types | BUFR Table | I, V | 0 20 062 | OP |
| Type of surface specified | up to 15 types | BUFR Table | I, V | 0 08 010 | OP |
| Snow depth | 0 – 25 m | 0.01 m | T | 0 13 013 | OP |
| OTHER |  |  |  |  |  |
| Gamma radiation dose rate 21) | 1 – 103 nSv h-1 | 0.1 nSv h-1 | I, T | 0 24 014 | VAL |
| Categories of stability | 9 types | BUFR Table | I, V | 0 13 041 | OP |

Notes:

- Name of variable, in line with WMO vocabulary and Technical Regulations.

- Maximum Effective Range - Maximum range of measuring capability; units traceable to SI.

- Minimum Reported Resolution – Lower resolution of reporting is not permitted.

- Mode of Observation – Type of data being reported:

I:  Instantaneous – 1-minute value (instantaneous as defined in WMO-No. 8, Part II, paragraph  1.3.2.4);

V:  Variability – Average (mean), Standard Deviation, Maximum, Minimum, Range, Median, etc. of samples – those reported depend upon meteorological variable;

T: Total – Integrated value over defined period; maximum 24 hours for all parameters except radiation which requires a maximum of one hour (exception, see note 6), and precipitation accumulation (6 hours maximum). The relevant element descriptor shall be preceded by a time period descriptor 0 04 024 (in hours) or 0 04 025 (in minutes).

A:  Average (mean) value.

- BUFR/CREX descriptors for representation of the listed variables;

OP:   Operational descriptors of BUFR/CREX Table B, Version Number 14.

VAL: Descriptors to be validated.

N:     Not yet specified requirements.

- Radiation energy amounts are given over a 24-hour period.

- Maximum interval: 6 hours.

- Definition of UV-B according to WMO-No. 8 (Vol. 1, Chapter on Radiation). Descriptor 0 14 072 (Global UV irradiation) was recommended for validation in September 2008, revised in July 2010.

- Humidity related variables (i.e. dew point temperature) expressed as temperature are collected under temperature.

- MOR uniquely related to "extinction coefficient", (, by MOR = -ln(5%)/(.

- Direction to indicate 0 (zero) if speed = 0.

- Absolute Salinity (kg.kg-1) is now being used for ocean applications (IOC Res XXV-7). However, salinity that is reported to national oceanographic data centers remains the Practical Salinity (psu). Ocean water is about 35 psu. Lake Asal (Ethiopia) is the most saline body of water on earth with 348 psu salt concentration.

- Calm.

- Temperature data represented by 0 12 101, 0 12 103, 0 12 113, 0 12 120, 0 12 130, 0 12 131 and 0 12 132 shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values. Temperature t (in degrees Celsius) shall be converted into temperature T (in degrees Kelvin) using equation: T = t + 273.15.

- Ice thickness 0 13 115 shall be preceded by 0 08 029 (Surface type) set to 11, 12, 13 or 14 to specify river, lake, sea or glacier, respectively.

- If the UNIT is specified as “BUFR Table”, the BUFR descriptor cannot be proposed without the content of the table being available.

- 0 13 058 (Size of precipitation element) is capable to express size of any precipitation element, apart from hailstones. Size of hailstones shall be represented by 0 20 066.

- These requirements being confirmed, it has to be noted that the selected descriptors are suitable for the normal operating conditions and shall be combined with appropriate operator descriptors to allow representation of the extreme values or the requested high precision.

- Operator 2 07 Y is recommended to be used with Water pressure 0 22 065 (Pa, -3, 0, 17), if the data are produced in BUFR, Edition 4. The same result, i.e. change to (Pa, -2, 0, 21) would be obtained by the combined use of the less sophisticated operators 201Y and 202Y:

2 01 132

2 02 129

0 22 065 Reported value of “Water pressure”

2 02 000

2 01 000

- The following sequence is to be used to change data width and reference value of 0 22 040 (m, 3, -5000, 14) to become (m, 3, -10000, 15):

2 01 129

2 03 015

0 22 040 New reference value = -10000

2 03 255

0 22 040 Reported value of “Meteorological residual tidal elevation”

2 01 000

2 03 000

- Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.

- Photosynthetically active radiation (PAR). Various forms of the electromagnetic energy flux in the 400 – 700 nm wavelength range, either as integrated spectra or using different weighting functions. For example converted to the photosynthetic photon flux (PPF) in quanta per second per square meter, or mole of quanta per second per square meter or microeinsteins per second per square meter.  Approximate conversion is 1 J m-2 s-1 equivalent to 5 μE m-2 s-1 based on a mean wavelength of 550 nm.

The changes introduced in 2010 are written in blue or marked by side bars. The recent change in specification for “Soil heat flux” is written in red.