| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.3.3(5),Rev2 (9. IX. 2011) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

New entries in Common Code Tables

Submitted by Jeff Ator (U.S.A.)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for new entries to Common Code Tables C-2, C-5 and C-8 along with some new entries to related BUFR Code Tables.

________________________________________________________________

ACTION PROPOSED

The team is requested to discuss the content of this

document and recommend the contents for fast-track implementation.

DISCUSSION

Some new entries are proposed to be added to Common and BUFR Code tables under the fast-track mechanism.

The CALIPSO and CloudSat satellites (and associated C-8 entries) are a joint venture between NASA and CNES and are part of the same mission as AQUA and AURA.  The KOMPSAT-5 satellite is a new South Korean satellite which will support GPS radio occultation.

The remaining entries are for use with a new radiosonde that will soon be introduced into operations in the U.S.A.Note that:

- The current C-2 entry #52 is for a radiosonde model (Vaisala RS80-57H) that is no longer manufactured and no longer in use.

- The 0-02-066 entries are reworded to provide more detail.  In both cases, the underlying ground systems are unchanged and refer to the same models as before.  Both are manufactured by InterMet.

PROPOSAL

Add new entries to the Common Code table C-5

| Code figure for | Code figure for | Code figure for |  |
| --- | --- | --- | --- |
| I6I6I6 | BUFR | GRIB |  |
|  | (Code table 0 01 007) | Edition 2 |  |
| 787 | 787 | 787 | CALIPSO |
| 788 | 788 | 788 | CloudSat |
| 825 | 825 | 825 | KOMPSAT-5 |

Add new entries to the Common Code table C-8

| Code | Agency | Type | Instrument short name | Instrument long name |
| --- | --- | --- | --- | --- |
| 56 | CNES | Imaging multi-spectral radiometer | IIR | Imaging Infrared Radiometer |
| 303 | NASA | Lidar | CALIOP | Cloud-Aerosol Lidar with Orthogonal Polarization |

Add new entry to the Common Code table C-2

| Date of assignment of number (necessary after 30/06/2007) | Code figure for ra ra (Code table 3685) | Code figure for BUFR (Code table 0 02 011) |  |
| --- | --- | --- | --- |
| 01/10/2011 | 52 | 152 | Vaisala RS92-NGP with silicon capacitor, capacitance wire, and heated twin thin-film capacitance RH sensors |

Add new entries to BUFR Code tables

0 02 095 – Type of pressure sensor

Code figure

3	Silicon capacitor

0 02 096 – Type of temperature sensor

Code figure

3	Capacitance wire

0 02 097 – Type of humidity sensor

Code figure

7	Humicap heated twin thin-film capacitance sensors

Reword existing entries in BUFR Code tables

0 02 066 – Radiosonde ground receiving system

Code figure

- InterMet IMS 2000

- InterMet IMS 1500C