| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.3.3(8) (31. VIII.2011) ------------------------- ITEM 3.3 ENGLISH ONLY |
| --- | --- | --- |

Representation of Horizontal Visibility

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for addition of a Note under Class 20 to express horizontal visibility 82 km and more; in case of conversion from TAC data, horizontal visibility greater than 70 km.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document and

to recommend the proposed Note as preoperational.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1

[2] Manual on Codes, WMO-No. 306, Volume I.2

1. Background

Descriptor 0 20 001 (Horizontal visibility, m, -1, 0, 13) is capable to express only values up to 81 900 m, therefore visibility e.g. 90 km, 100 km and above cannot be represented by this descriptor. Moreover, code table 4377 for representation of horizontal visibility VV in TAC data contains the code figure 89 to express visibility greater than 70 km.

2. A new Note to be added under Class 20

It is proposed to add a note under Class 20:

Horizontal visibility greater than 81900 m shall be expressed by 0 20 001 set to 81900 m; if TDCF data are converted from TAC data, 0 20 001 set to 81900 m shall indicate horizontal visibility greater then 70000 m.

3. Corresponding additions to B/C Regulations

If IPET DRC-III meeting agrees with the suggested addition of a new Note under Class 20, it is proposed to add the following B/C Regulations:

B/C 1.4.2.2.2, B/C 5.4.2.2.2 and B/C 10.4.2.2.2

Horizontal visibility greater than 81900 m shall be expressed by 0 20 001 set to 81900 m; if TDCF data are converted from TAC data, 0 20 001 set to 81900 m shall indicate horizontal visibility greater then 70000 m.