| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ---------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION AND CODES MELBOURNE, AUSTRALIA, 20 - 23 SEPTEMBER 2011 |  | IPET-DRC-III / Doc.3.4(2) (5. VII.2011) ------------------------- ITEM 3.4 ENGLISH ONLY |
| --- | --- | --- |

CREX template examples in the Manual on Codes

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposal for updating CREX Template Examples

in the Manual on Codes to CREX Edition 2.

________________________________________________________________

ACTION PROPOSED

The Expert Team is invited to discuss the content of this document and recommend the proposed updating of CREX Template Examples.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2, Part C

1. Background

All CREX Template Examples included in the Manual on Codes, WMO-No. 306, Volume I.2, Part C, contain messages encoded in CREX edition 1. But CREX edition 1 may be used only up to the first Tuesday of November 2012. And even now, usage of CREX edition 2 is to be preferred.

2. Proposal for inclusion of a new total ozone example

Within the WIS-WIGOS Pilot Project entitled “Improvement of Dissemination of Ozone (total column, profiles and surface) and Aerosol observations through the WIS” (GAW-IDOA), “Guidance for Reporting Total Ozone Data in Near Real Time” was developed in early 2011. A CREX message, containing total ozone measurement from a Brewer spectrophotometer obtained from averaged observations on 16 January 2011, encoded in CREX edition 2, is presented and explained in this guide.

In the current Manual on Codes [1], an example of total ozone measurement from a Dobson spectrophotometer obtained from a single observation encoded in CREX edition 1, is included. It is proposed to replace it by the example of total ozone measurement from a Brewer ground-based spectrophotometer obtained from averaged observations on 4 May 2011 as shown below in the ANNEX.

3. Proposal for updating of the other CREX examples

It is proposed to replace also the other CREX examples with corresponding data encoded in CREX, edition 2. If not feasible for all of them, the examples of CREX edition 1 and the examples of CREX edition 2 would be separated, the examples of CREX edition 2 preferably listed first.

ANNEX

TOTAL OZONE MEASUREMENT FROM A BREWER GROUND-BASED SPECTROPHOTOMETER OBTAINED FROM AVERAGED OBSERVATIONS

KULD40 OKOH 041643

CREX++

T0002071500 A008002 P00089001 U00 S001 Y20110504 H0748 D07042++

11 649 Hradec Kralove       5018 01583 00285 2011 05 04 07

48 08 0526 001 98   00 00022 04 0383 09 0012 11 157++

7777

| CREX |  |  |  |
| --- | --- | --- | --- |
| T0002071500 |  | CREX master table CREX edition number CREX table version number BUFR Master Table version number used Version number of local table | 00 02 07 15 00 |
| A008002 |  | Data category International data subcategory | 008 002 |
| P00089001 |  | Originating centre (Common Code Table C-11) Originating sub-centre (Common Code Table C-12) | 00089 001 |
| U00 |  | Update sequence number (00 for original and delayed messages; incremented for corrected messages) | 00 |
| S001 |  | Number of subsets included in the report | 001 |
| Y20110504 |  | Year Month Day | 2011 05 04 |
| H0748 |  | Hour Minute | 07 48 |
| D07042 | D01001 |  |  |
|  | B01001 | WMO block number | 11 |
|  | B01002 | WMO station number | 649 |
|  | B01015 | Station or site name (1) | Hradec Kralove^^^^^^ |
|  | D01024 |  |  |
|  | B05002 | Latitude (2) (3) 50.18 deg N | 5018 |
|  | B06002 | Longitude (2) (3) 15.83 deg E | 01583 |
|  | B07001 | Height of station | 00285 |
|  | D01011 |  |  |
|  | B04001 | Year (of ozone measurement) | 2011 |
|  | B04002 | Month (of ozone measurement) | 05 |
|  | B04003 | Day (of ozone measurement) | 04 |
|  | D01012 |  |  |
|  | B04004 | Hour (of ozone measurement) (4) | 07 |
|  | B04005 | Minute (of ozone measurement) (4) | 48 |
|  | B08021 | Time significance = 8 = ensemble mean(5) | 08 |
|  | B04025 | Time period (in minutes) | 0526 |
|  | D01070 |  |  |
|  | B02143 | Ozone instrument type | 001 |
|  | B02142 | Ozone instrument serial number (1) | 98^^ |
|  | B02144 | Light source type for Brewer spectrophotometer (6) | 00 |
|  | D07031 |  |  |
|  | B08022 | Number of measurements | 00022 |
|  | B08023 | First order statistic = 4 = mean value | 04 |
|  | B15001 | Value (average) of ozone measurement | 0383 |
|  | B08023 | First order statistic = 9 = best estimate of std deviation | 09 |
|  | B15001 | Best estimate of std deviation of the ozone measurement | 0012 |
|  | B08023 | First order statistic = 11 = harmonic mean | 11 |
|  | B15002 | Harmonic mean of the air mass | 157 |
| 7777 |  |  |  |

Notes:

- Characters “^^^^^^” are used for visualization of the corresponding number of space characters.

- Latitude and longitude shall be reported in degrees with precision in hundredths of a degree.

- South latitude and west longitude shall be assigned negative values.

- Hour and minute specifies the time of the first measurement of the series.

- “Ensemble mean” indicates that a number of distinct values corresponding to a set of time locations are averaged.

- Ozone measurements of only one light source shall be selected, i.e. the best light source of the day.