Annex A: Table B descriptors – BUFR "Generalised Coordinates" Modifiers and their Function

Table 1 in the main section is a summarisation of these Annex A tables. The tables are a subset of the Version 14 tables extended in several ways to create structures which were used to investigate techniques to derive fully decoded XML from BUFR Bulletins. This decoding also included a proper interpretation of the Modifiers as they act on target descriptors.

The extensions include:

- An XML name for the BUFR descriptor ID. In this way 0 01 001 becomes F0X01Y001 which is only one character larger and conforms to XML requirements for names and IDs.

- A NAMESPACE for each BUFR Class: e.g. BCID for Class 1, in case of duplicate names within classes.

- A lowerCamelCase NAME for each descriptor. That is initial lower case letter unless the start contains acronyms – such as WMO. As the XML may be directed at not specialists, because of the large variety of descriptor names it is important to try to avoid obscure contractions. Only obvious contractions should be used (e.g. ID for Identifier, and Temp for Temperature).

- For the Modifiers/Generalised Coordinates, and assessment of the Modifier function in order to create a sensible XML hierarchical structure.

The naming exercise came up with some problems. In fact it was possible to create names which were not duplicated across classes, but the namespaces were retained. Duplication occurred WITHIN classes however due to the BUFR practice of replicating descriptors with different precisions. This occurred in Class 12 Temperature in a systematic manner, but is illustrated in Class 5 and 6: e.g.

| F0X05Y001 | Latitude (high accuracy) | hiPrecsnLat |
| --- | --- | --- |
| F0X05Y002 | Latitude (coarse accuracy) | lowPrecsnLat |

In fact this is another “Coding construct” within BUFR which will not translate to a general (GML based) XML. In transforming from BUFR to XML the distinction is redundant. A Latitude is a Latitude and the precision in a presentational issue.  However in transforming from XML to BUFR (which has not been investigated) this distinction would have to be applied using some mechanism such as retaining BUFR identifiers (F0X05Y001 etc.) or applying templates – as happens now in writing BUFR bulletins.

Class 0, used to code up the BUFR tables is a specialised class and is not included here

| ID | description | Name | Modifier Type |
| --- | --- | --- | --- |
| Class 1 - Identification | Namespace BCID |  |
| F0X01Y001 | WMO block number | WMOblock | Property - ID |
| F0X01Y002 | WMO station number | WMOstation | Property - ID |
| F0X01Y003 | WMO Region number/geographical area | WMOregion | Property - ID |
| F0X01Y004 | WMO Region sub-area (see Note 9) | oldWMOsubArea | Property - ID |
| F0X01Y005 | Buoy/platform identifier | buoyID | Property - ID |
| F0X01Y006 | Aircraft flight number | flightID | Property - ID |
| F0X01Y007 | Satellite identifier | satelliteID | Property - ID |
| F0X01Y008 | Aircraft registration number or other identification | aircraftID | Property - ID |
| F0X01Y009 | Type of commercial aircraft | aircraftType | Property - ID |
| F0X01Y010 | Stationary buoy platform identifier; e.g. C-MAN buoys | fixedBuoy | Property - ID |
| F0X01Y011 | Ship or mobile land station identifier | shipID | Property - ID |
| F0X01Y012 | Direction of motion of moving observing platform * | platformDirn | Property |
| F0X01Y013 | Speed of motion of moving observing platform * | platformSpeed | Property |
| F0X01Y014 | Platform drift speed (high precision) | platformDrift | Property |
| F0X01Y015 | Station or site name | stationName | Property - ID |
| F0X01Y018 | Short station or site name | stationShortname | Property - ID |
| F0X01Y019 | Long Station or site name | stationLongName | Property - ID |
| F0X01Y020 | WMO Region sub-area | WMOsubArea | Property - ID |
| F0X01Y021 | Synoptic feature identifier | synopticFeatureID | Property - ID |
| F0X01Y022 | Name of feature (see Note 11) | synopticFeatureName | Property - ID |
| F0X01Y023 | Observation sequence number | obsSequenceNum | Property - ID |
| F0X01Y024 | Wind Speed source | windSpeedSrce | Property - Source |
| F0X01Y025 | Storm identifier (see Note 1) | stormID | Property - ID |
| F0X01Y026 | WMO storm name * | stormName | Property - ID |
| F0X01Y027 | WMO long storm name * | longStormName | Property - ID |
| F0X01Y028 | Aerosol optical Depth (AOD) source | aerosolOpticalDepth | Property - Source |
| F0X01Y029 | SSI Source | surfSolarIrradSrce | Property - Source |
| F0X01Y030 | Numerical model identifier (see Note 13) | NWPmodelID | Property - ID |
| F0X01Y031 | Identification of originating/generating centre (see Note 10) | oldOriginCentreID | Property - Originator |
| F0X01Y032 | Generating application defined by originating/generating centre (Notes 3, 4 and 5) | generatingApp | Property - ID |
| F0X01Y033 | Identification of originating/generating centre | originCentreID | Property - Originator |
| F0X01Y034 | Identification of originating/generating sub-centre | subCentreID | Property - Originator |
| F0X01Y035 | Originating Centre | originCentre | Property - Originator |
| F0X01Y036 | Agency in charge of operating the observing platform | operatingAgency | Property - Operator |
| F0X01Y037 | SIGMET sequence identifier | SIGMETseqID | Property - ID |
| F0X01Y038 | Source of Sea Ice Fraction | seaIceFractionSrce | Property - Source |
| F0X01Y039 | Graphical Area Forecast (GFA) sequence identifier | GFASeqID | Property - ID |
| F0X01Y041 | Absolute platform velocity - first component (see Note 6) | platformAbsV_1 | Property |
| F0X01Y042 | Absolute platform velocity - second component (see Note 6) | platformAbsV_2 | Property |
| F0X01Y043 | Absolute platform velocity - third component (see Note 6) | platformAbsV_3 | Property |
| F0X01Y050 | Platform transmitter ID number | transmitterNum | Property - ID |
| F0X01Y051 | Platform transmitter ID number | transmitterID | Property - ID |
| F0X01Y052 | Platform transmitter ID | platTransmitterID | Property - ID |
| F0X01Y053 | Tsunameter report sequence number triggered by a tsunami event | tsunamiRepSeqNum | Property - ID |
| F0X01Y060 | Aircraft reporting point (Beacon identifier) | beaconID | Property - ID |
| F0X01Y062 | Short ICAO location indicator | ICAOshort | Property - ID |
| F0X01Y063 | ICAO location indicator | ICAOlong | Property - ID |
| F0X01Y064 | Runway designator | runwayID | Property - ID |
| F0X01Y065 | ICAO region identifier | ICAOregion | Property - ID |
| F0X01Y075 | Tide station identification | tideStationID | Property - ID |
| F0X01Y080 | Ship line number according to SOOP | shipLineNum | Property - ID |
| F0X01Y081 | Radiosonde serial number | sondeSerialID | Property - ID |
| F0X01Y082 | Radiosonde ascension number (see Note 12) | sondeAscentID | Property - ID |
| F0X01Y083 | Radiosonde release number (see Note 12) | sondeReleaseID | Property - ID |
| F0X01Y085 | Observing platform manufacturer's model | platformModelID | Property - ID |
| F0X01Y086 | Observing platform manufacturer's serial number | platformSerialID | Property - ID |
| F0X01Y087 | WMO Marine observing platform extended identifier | WMOmarineID | Property - ID |
| F0X01Y090 | Technique for making up initial perturbations | initialPeturb | Property - Source |
| F0X01Y091 | Ensemble member number | ensembleNum | Property - ID |
| F0X01Y092 | Type of ensemble forecast | ensembleType | Property - ID |
| F0X01Y093 | Balloon lot number | balloonLotID | Property - ID |
| F0X01Y094 | WBAN Number | WBAN | Property - ID |
| F0X01Y095 | Observer identification | observerID | Property - ID |
| F0X01Y096 | Station acquisition | stationAcquisition | Property - ID |
| F0X01Y097 | Star catalog number | starCatalogNum | Property - ID |
| F0X01Y098 | Type of product | productType | Property |
| F0X01Y099 | Unique product definition | productDefinition | Property - ID |
| F0X01Y101 | State identifier | stateID | Property - ID |
| F0X01Y102 | National station number | nationalStationNum | Property - ID |
| F0X01Y103 | IMO Number. Unique Lloyd's registry | IMOLloydsRegNum | Property - ID |
| F0X01Y110 | Aircraft tail number | aircraftTailNum | Property - ID |
| F0X01Y111 | Origination airport | originAirport | Property - ID |
| F0X01Y112 | Destination airport | destinationAirport | Property - ID |
| F0X01Y124 | Grid point identifier | gridPointID | Property - ID |
| F0X01Y144 | Snapshot identifier | snapshotID | Property - ID |
| ID | description | Name | Modifier Type |
| Class 2 - Instrumentation | Namespace BCIn |  |
| F0X02Y001 | Type of station | station | Property - Instrumentation |
| F0X02Y002 | Type of instrumentation for wind measurement | wind | Property - Instrumentation |
| F0X02Y003 | Type of measuring equipment used | equipment | Property - Instrumentation |
| F0X02Y004 | Type of instrumentation for evaporation measurement or type of crop for which evapotranspiration is reported | evaporation | Property - Instrumentation |
| F0X02Y005 | Precision of temperature observation | PrecisionTemp | Property - Instrumentation |
| F0X02Y007 | Type of sensor for water level measuring instrument | waterLevelInstrType | Property - Instrumentation |
| F0X02Y011 | Radiosonde type | radiosonde | Property - Instrumentation |
| F0X02Y012 | Radiosonde computational method | sondeComputation | Property - Instrumentation |
| F0X02Y013 | Solar and infrared radiation correction | solarIRcorrect | Property - Instrumentation |
| F0X02Y014 | Tracking technique/status of system used | tracking | Property - Instrumentation |
| F0X02Y015 | Radiosonde completeness | sondeComplete | Property - Instrumentation |
| F0X02Y016 | Radiosonde configuration | sondeConfig | Property - Instrumentation |
| F0X02Y019 | Satellite instruments | SatInstr | Property - Instrumentation |
| F0X02Y020 | Satellite classification | SatClass | Property - Instrumentation |
| F0X02Y021 | Satellite instrument data used in processing * | SatInstrData | Property - Instrumentation |
| F0X02Y022 | Satellite data-processing technique used | SatTechnique | Property - Instrumentation |
| F0X02Y023 | Satellite derived wind computation method | SatWindMethod | Property - Instrumentation |
| F0X02Y024 | Integrated mean humidity computational method | SatHumidityMethod | Property - Instrumentation |
| F0X02Y025 | Satellite channel(s) used in computation | SatChannels | Property - Instrumentation |
| F0X02Y026 | Cross-track resolution | crossTrack | Property - Instrumentation |
| F0X02Y027 | Along-track resolution | alongTrack | Property - Instrumentation |
| F0X02Y028 | Segment size at nadir in x-direction | segmentX | Property - Instrumentation |
| F0X02Y029 | Segment size at nadir in y-direction | segmentY | Property - Instrumentation |
| F0X02Y030 | Method of current measurement | currentMethod | Property - Instrumentation |
| F0X02Y031 | Duration and time of current measurement | currentDuration | Property - Instrumentation |
| F0X02Y032 | Indicator for digitization | digitization | Property - Instrumentation |
| F0X02Y033 | Method of salinity/depth measurement | salinityMethod | Property - Instrumentation |
| F0X02Y034 | Drogue type | drogue | Property - Instrumentation |
| F0X02Y035 | Cable length | cableLength | Property - Instrumentation |
| F0X02Y036 | Buoy type | buoy | Property - Instrumentation |
| F0X02Y037 | Method of tidal observation | tidalMethod | Property - Instrumentation |
| F0X02Y038 | Method of water temperature and/or salinity measurement | waterTempSalMethod | Property - Instrumentation |
| F0X02Y039 | Method of wet-bulb temperature measurement | wetBulbMethod | Property - Instrumentation |
| F0X02Y040 | Method of removing velocity and motion of platform from current | currentCorrection | Property - Instrumentation |
| F0X02Y041 | Method for estimating reports related to synoptic features | synopticFeatureMethod | Property - Instrumentation |
| F0X02Y042 | Indicator for sea-surface current speed | surfaceCurrent | Property - Instrumentation |
| F0X02Y044 | Indicator for method of calculating spectral wave data | spectralWaveMethod | Property - Instrumentation |
| F0X02Y045 | Indicator for type of platform | platformType | Property - Instrumentation |
| F0X02Y046 | Wave measurement instrumentation | waveInstr | Property - Instrumentation |
| F0X02Y047 | Deep-ocean tsunameter type | tsunameterType | Property - Instrumentation |
| F0X02Y048 | Satellite sensor indicator | SatSensor | Property - Instrumentation |
| F0X02Y049 | Geostationary satellite data-processing technique used | GeoSatTechnique | Property - Instrumentation |
| F0X02Y050 | Geostationary sounder satellite channels used | GeoSatSounders | Property - Instrumentation |
| F0X02Y051 | Indicator to specify observing method for extreme temperatures | MaxMinTempMethod | Property - Instrumentation |
| F0X02Y052 | Geostationary imager satellite channels used | GeoSatImagers | Property - Instrumentation |
| F0X02Y053 | GOES-I/M brightness temperature characteristics | GOESbrightness | Property - Instrumentation |
| F0X02Y054 | GOES-I/M soundings parameter characteristics | GOESsoundings | Property - Instrumentation |
| F0X02Y055 | Geostationary soundings statistical parameters | GeoSatStatistics | Property - Instrumentation |
| F0X02Y056 | Geostationary soundings accuracy statistics | GeoSatAccuracy | Property - Instrumentation |
| F0X02Y057 | Origin of first guess information for GOES-I/M soundings | GOESfirstGuess | Property - Instrumentation |
| F0X02Y058 | Valid times of first guess information for GOES-I/M soundings | GOESvalidTimes | Property - Instrumentation |
| F0X02Y059 | Origin of analysis information for GOES-I/M soundings | GOESanalysis | Property - Instrumentation |
| F0X02Y060 | Origin of surface information for GOES-I/M soundings | GOESsurface | Property - Instrumentation |
| F0X02Y061 | Aircraft navigational system | AIRNAV | Property - Instrumentation |
| F0X02Y062 | Type of aircraft data relay system | AIRrelay | Property - Instrumentation |
| F0X02Y063 | Aircraft roll angle | AIRroll | Property - Instrumentation |
| F0X02Y064 | Aircraft roll angle quality | AIRrollQ | Property - Instrumentation |
| F0X02Y065 | ACARS ground-receiving station | ACARSstation | Property - Instrumentation |
| F0X02Y066 | Radiosonde ground receiving system | sondeReceive | Property - Instrumentation |
| F0X02Y067 | Radiosonde operating frequency | sondeFreq | Property - Instrumentation |
| F0X02Y070 | Original specification of latitude/longitude | LatLonSpec | Property - Instrumentation |
| F0X02Y071 | Spectrographic wavelength | spectWavelength | Property - Instrumentation |
| F0X02Y072 | Spectrographic width | spectWidth | Property - Instrumentation |
| F0X02Y080 | Balloon manufacturer | balloonMaker | Property - Instrumentation |
| F0X02Y081 | Type of balloon | balloonType | Property - Instrumentation |
| F0X02Y082 | Weight of balloon | balloonWeight | Property - Instrumentation |
| F0X02Y083 | Type of balloon shelter | balloonShelter | Property - Instrumentation |
| F0X02Y084 | Type of gas used in balloon | balloonGas | Property - Instrumentation |
| F0X02Y085 | Amount of gas used in balloon | balloonGasAmount | Property - Instrumentation |
| F0X02Y086 | Balloon flight train length | balloonTrainLength | Property - Instrumentation |
| F0X02Y091 | Entry sensor 4/20 mA | entrySensor | Property - Instrumentation |
| F0X02Y095 | Type of pressure sensor | pressureSensor | Property - Instrumentation |
| F0X02Y096 | Type of temperature sensor | tempSensor | Property - Instrumentation |
| F0X02Y097 | Type of humidity sensor | humiditySensor | Property - Instrumentation |
| F0X02Y098 | Type of wave sensor | waveSensorType | Property - Instrumentation |
| F0X02Y099 | Polarisation | polarisation | Property - Instrumentation |
| F0X02Y100 | Radar constant * | radarConst | Property - Instrumentation |
| F0X02Y101 | Type of antenna | antennaType | Property - Instrumentation |
| F0X02Y102 | Antenna height above tower base | antennaHeight | Property - Instrumentation |
| F0X02Y103 | Radome | radome | Property - Instrumentation |
| F0X02Y104 | Antenna polarisation | antennaPolarisation | Property - Instrumentation |
| F0X02Y105 | Maximum antenna gain | antennaMaxGain | Property - Instrumentation |
| F0X02Y106 | 3-dB beamwidth | beamwidth | Property - Instrumentation |
| F0X02Y107 | Sidelobe suppression | sideLobe | Property - Instrumentation |
| F0X02Y108 | Crosspol discrimination (on axis) | crosspol | Property - Instrumentation |
| F0X02Y109 | Antenna speed (azimuth) | antennaVazimuth | Property - Instrumentation |
| F0X02Y110 | Antenna speed (elevation) | antennaVelevation | Property - Instrumentation |
| F0X02Y111 | Radar incidence angle | incidenceAngle | Property - Instrumentation |
| F0X02Y112 | Radar look angle | lookAngle | Property - Instrumentation |
| F0X02Y113 | Number of azimuth looks | NumAzimuthLooks | Property - Instrumentation |
| F0X02Y114 | Antenna effective surface area | antennaArea | Property - Instrumentation |
| F0X02Y115 | Type of surface observing equipment | surfaceObsType | Property - Instrumentation |
| F0X02Y116 | Percentage of 320 MHz band processed | percent320MHz | Property - Instrumentation |
| F0X02Y117 | Percentage of 80 MHz band processed | percent80MHz | Property - Instrumentation |
| F0X02Y118 | Percentage of 20 MHz band processed | percent20MHz | Property - Instrumentation |
| F0X02Y119 | RA-2 instrument operations | RA-2 | Property - Instrumentation |
| F0X02Y120 | Ocean wave frequency | waveFreq | Property - Instrumentation |
| F0X02Y121 | Mean frequency | meanFreq | Property - Instrumentation |
| F0X02Y122 | Frequency agility range | FreqAgility | Property - Instrumentation |
| F0X02Y123 | Peak power | peakPower | Property - Instrumentation |
| F0X02Y124 | Average power | averagePower | Property - Instrumentation |
| F0X02Y125 | Pulse repetition frequency | pulseFreq | Property - Instrumentation |
| F0X02Y126 | Pulse width | pulseWidth | Property - Instrumentation |
| F0X02Y127 | Receiver intermediate frequency | receiverFreq | Property - Instrumentation |
| F0X02Y128 | Intermediate frequency bandwidth | freqBandwidth | Property - Instrumentation |
| F0X02Y129 | Minimum detectable signal | minSignal | Property - Instrumentation |
| F0X02Y130 | Dynamic range | dynamicRange | Property - Instrumentation |
| F0X02Y131 | Sensitivity time control (STC) | sensitivityTime | Property - Instrumentation |
| F0X02Y132 | Azimuth pointing accuracy | azimuthAccuracy | Property - Instrumentation |
| F0X02Y133 | Elevation pointing accuracy | elevationAccuracy | Property - Instrumentation |
| F0X02Y134 | Antenna beam azimuth | antennaAzimuth | Property - Instrumentation |
| F0X02Y135 | Antenna elevation | antennaElevation | Property - Instrumentation |
| F0X02Y136 | Range processed by range attenuation correction | rangeAttenuation | Property - Instrumentation |
| F0X02Y137 | Radar Dual PRF ratio | radarDualPRFRatio | Property - Instrumentation |
| F0X02Y138 | Antenna rotation direction | antennaRotDirn | Property - Instrumentation |
| F0X02Y140 | Satellite radar beam azimuth angle | SatAzimuth | Property - Instrumentation |
| F0X02Y141 | Measurement type | measurementType | Property - Instrumentation |
| F0X02Y142 | Ozone instrument serial number/identification | ozoneInstrID | Property - Instrumentation |
| F0X02Y143 | Ozone instrument type | ozoneInstrType | Property - Instrumentation |
| F0X02Y144 | Light source type for Brewer spectrophotometer | BrewerType | Property - Instrumentation |
| F0X02Y145 | Wave length setting for Dobson instruments | DobsonWaveLength | Property - Instrumentation |
| F0X02Y146 | Source conditions for Dobson instruments | DobsonSource | Property - Instrumentation |
| F0X02Y147 | Method of transmission to collection centre | transmissionMethod | Property - Instrumentation |
| F0X02Y148 | Data collection and/or location system | dataCollectSystem | Property - Instrumentation |
| F0X02Y149 | Type of data buoy | dataBuoyType | Property - Instrumentation |
| F0X02Y150 | TOVS/ATOVS/AVHRR instrumentation channel number | ATOVSchannel | Property - Instrumentation |
| F0X02Y151 | Radiometer identifier | radiometerID | Property - Instrumentation |
| F0X02Y152 | Satellite instrument used in data processing (see Note 6) | SatInstrUsed | Property - Instrumentation |
| F0X02Y153 | Satellite channel centre frequency | SatChannelFreq | Property - Instrumentation |
| F0X02Y154 | Satellite channel band width | SatChannelBandwidth | Property - Instrumentation |
| F0X02Y156 | Percentage of valid KU ocean retracker measurements | validKUretracker | Property - Instrumentation |
| F0X02Y157 | Percentage of valid S ocean retracker measurements | validSretracker | Property - Instrumentation |
| F0X02Y158 | RA-2 instrument | RA-2Instr | Property - Instrumentation |
| F0X02Y159 | MWR instrument | MWRinstr | Property - Instrumentation |
| F0X02Y160 | Wave length of the radar | radarWavelength | Property - Instrumentation |
| F0X02Y163 | Height assignment method | heightMethod | Property - Instrumentation |
| F0X02Y164 | Tracer correlation method | tracerMethid | Property - Instrumentation |
| F0X02Y165 | Radiance type flags | radianceTypeFlags | Property - Instrumentation |
| F0X02Y166 | Radiance type | radianceType | Property - Instrumentation |
| F0X02Y167 | Radiance computational method | radianceMethod | Property - Instrumentation |
| F0X02Y168 | Hydrostatic pressure of lower end of cable (thermistor string) | cableEndPressure | Property - Instrumentation |
| F0X02Y169 | Anemometer type | anemometer | Property - Instrumentation |
| F0X02Y171 | Instrument serial number for water temperature profile | serialNumWaterTempInstr | Property - Instrumentation |
| F0X02Y172 | Product type for retrieved atmospheric gases | atmosGasProduct | Property - Instrumentation |
| F0X02Y173 | Square of the off-nadir angle (see Note 7) | nadirAngleSq | Property - Instrumentation |
| F0X02Y174 | Mean across track pixel number | MeanAcrossTrackNum | Property - Instrumentation |
| F0X02Y175 | Method of precipitation measurement | precipMethod | Property - Instrumentation |
| F0X02Y176 | Method of state of ground measurement | groundStateMethod | Property - Instrumentation |
| F0X02Y177 | Method of snow depth measurement | snowDepthMethod | Property - Instrumentation |
| F0X02Y178 | Method of liquid content measurement of precipitation | liquidPrecipMethod | Property - Instrumentation |
| F0X02Y179 | Type of sky condition algorithm | skyConditionMethid | Property - Instrumentation |
| F0X02Y180 | Main present weather detecting system | mainPresentWX | Property - Instrumentation |
| F0X02Y181 | Supplementary present weather sensor | supplPresentWX | Property - Instrumentation |
| F0X02Y182 | Visibility measurement system | visibilityMethod | Property - Instrumentation |
| F0X02Y183 | Cloud detection system | cloudSystem | Property - Instrumentation |
| F0X02Y184 | Type of lightning detection sensor | lightningSensor | Property - Instrumentation |
| F0X02Y185 | Method of evaporation measurement | evaporationMethod | Property - Instrumentation |
| F0X02Y186 | Capability to detect precipitation phenomena | precipCapability | Property - Instrumentation |
| F0X02Y187 | Capability to detect other weather phenomena | otherWXmethod | Property - Instrumentation |
| F0X02Y188 | Capability to detect obscuration | obscurationMethod | Property - Instrumentation |
| F0X02Y189 | Capability to discriminate lightning strikes | lightningMethod | Property - Instrumentation |
| F0X02Y190 | Lagrangian drifter submergence (% time submerged) | drifterTime | Property - Instrumentation |
| F0X02Y191 | Geopotential height calculation | geopotHeightMethod | Property - Instrumentation |
| ID | description | Name | Modifier Type |
| Class 4 - Location (time) | Namespace BCT |  |
| F0X04Y001 | Year | year | CRS - Temporal |
| F0X04Y002 | Month | month | CRS - Temporal |
| F0X04Y003 | Day | day | CRS - Temporal |
| F0X04Y004 | Hour | hour | CRS - Temporal |
| F0X04Y005 | Minute | minute | CRS - Temporal |
| F0X04Y006 | Second | second | CRS - Temporal |
| F0X04Y007 | Seconds within a minute (microsecond accuracy) | microseconds | CRS - Temporal |
| F0X04Y008 | Seconds within a minute (high accuracy) | hiAccSecInMinute | CRS - Temporal |
| F0X04Y011 | Time increment | yearIncrement | CRS - Temporal |
| F0X04Y012 | Time increment | monthIncrement | CRS - Temporal |
| F0X04Y013 | Time increment | dayIncrement | CRS - Temporal |
| F0X04Y014 | Time increment | hourIncrement | CRS - Temporal |
| F0X04Y015 | Time increment | minuteIncrement | CRS - Temporal |
| F0X04Y016 | Time increment | secondIncrement | CRS - Temporal |
| F0X04Y017 | Reference time period for accumulated or extreme data | accumulationPeriod | CRS - Temporal Datum |
| F0X04Y021 | Time period or displacement | yearPeriod | CRS - Temporal |
| F0X04Y022 | Time period or displacement | monthPeriod | CRS - Temporal |
| F0X04Y023 | Time period or displacement | dayPeriod | CRS - Temporal |
| F0X04Y024 | Time period or displacement | hourPeriod | CRS - Temporal |
| F0X04Y025 | Time period or displacement | minutePeriod | CRS - Temporal |
| F0X04Y026 | Time period or displacement | secondPeriod | CRS - Temporal |
| F0X04Y031 | Duration of time relating to following value | hourFollowing | CRS - Temporal |
| F0X04Y032 | Duration of time relating to following value | minuteFollowing | CRS - Temporal |
| F0X04Y041 | Time difference, UTC - LMT (see Note 6) | UTC-LMT | CRS - Temporal |
| F0X04Y043 | Day of the year | yearday | CRS - Temporal |
| F0X04Y051 | Principal time of daily reading of maximum temperature | maxTempTime | CRS - Temporal |
| F0X04Y052 | Principal time of daily reading of minimum temperature | minTempTime | CRS - Temporal |
| F0X04Y053 | Number of days with precipitation equal to or more than 1 mm | daysOfPrecip | CRS - Temporal |
| F0X04Y059 | Times of observation used to compute the reported mean values | observationTimesUsed | CRS - Temporal Datum |
| F0X04Y065 | Short time increment | shortMinuteIncrement | CRS - Temporal |
| F0X04Y066 | Short time increment | shortSecondIncremt | CRS - Temporal |
| F0X04Y073 | Short time period or displacement | shortDayPeriod | CRS - Temporal |
| F0X04Y074 | Short time period or displacement | shortHourPeriod | CRS - Temporal |
| F0X04Y075 | Short time period or displacement | shortMinutePeriod | CRS - Temporal |
| F0X04Y080 | Averaging period for following value | averagingPeriod | Property - Role |
| F0X04Y086 | Long time period or displacement | longSecondPeriod | CRS - Temporal |
| ID | description | Name | Modifier Type |
| Class 5 - Location (horizontal - 1) | Namespace BCX |  |
| F0X05Y001 | Latitude (high accuracy) | hiPrecsnLat | CRS - WGS84 |
| F0X05Y002 | Latitude (coarse accuracy) | lowPrecsnLat | CRS - WGS84 |
| F0X05Y011 | Latitude increment (high accuracy) | hiPrecsnLatIncremt | CRS - WGS84 |
| F0X05Y012 | Latitude increment (coarse accuracy) | lowPrecsnLatIncremt | CRS - WGS84 |
| F0X05Y015 | Latitude displacement (high accuracy) | hiPrecsnLatDisplace | CRS - WGS84 |
| F0X05Y016 | Latitude displacement (coarse accuracy) | lowPrecsnLatDisplace | CRS - WGS84 |
| F0X05Y021 | Bearing or azimuth | bearing | CRS - Parametric |
| F0X05Y022 | Solar azimuth | solarAzimuth | CRS - Parametric |
| F0X05Y023 | Sun to satellite azimuth difference | azimuthDifference | CRS - Parametric |
| F0X05Y030 | Direction (spectral) | spectralDirn | CRS - Parametric |
| F0X05Y031 | Row number | rowNum | CRS - Parametric |
| F0X05Y033 | Pixel size on horizontal - 1 | pixelSize1 | CRS - Parametric |
| F0X05Y034 | Along track row number | alongTrackRow | CRS - Parametric |
| F0X05Y035 | Maximum size of X-dimension | maxSizeX | CRS - Parametric |
| F0X05Y036 | Ship transect number according to SOOP | shipTransect | CRS - Parametric |
| F0X05Y040 | Orbit number | orbitNum | CRS - Parametric |
| F0X05Y041 | Scan line number | scanLineNum | CRS - Parametric |
| F0X05Y042 | Channel number | channelNum | CRS - Parametric |
| F0X05Y043 | Field of view number | FieldOfView | CRS - Parametric |
| F0X05Y044 | Satellite cycle number | SatCycleNum | CRS - Parametric |
| F0X05Y045 | Field of regard number | fieldRegardNum | CRS - Parametric |
| F0X05Y052 | Channel number increment | channelIncremt | CRS - Parametric |
| F0X05Y053 | Field of view number increment | FieldOfViewIncremt | CRS - Parametric |
| F0X05Y060 | Y angular position from centre of gravity | YangularPosition | CRS - Parametric |
| F0X05Y061 | Z angular position from centre of gravity | ZangularPosition | CRS - Parametric |
| ID | description | Name | Modifier Type |
| Class 6 - Location (horizontal - 2) | Namespace BCY |  |
| F0X06Y001 | Longitude (high accuracy) | hiPrecsnLon | CRS - WGS84 |
| F0X06Y002 | Longitude (coarse accuracy) | lowPrecsnLon | CRS - WGS84 |
| F0X06Y011 | Longitude increment (high accuracy) | hiPrecsnLonIncremt | CRS - WGS84 |
| F0X06Y012 | Longitude increment (coarse accuracy) | lowPrecsnLonIncremt | CRS - WGS84 |
| F0X06Y015 | Longitude displacement (high accuracy) | hiPrecsnLonDisplace | CRS - WGS84 |
| F0X06Y016 | Longitude displacement (coarse accuracy) | lowPrecsnLonDisplace | CRS - WGS84 |
| F0X06Y021 | Distance | distance | CRS - Parametric |
| F0X06Y029 | Wave number | waveNum | CRS - Parametric |
| F0X06Y030 | Wave number (spectral) | spectralWaveNum | CRS - Parametric |
| F0X06Y031 | Column number | columnNum | CRS - Parametric |
| F0X06Y033 | Pixel size on horizontal - 2 | PixelSize2 | CRS - Parametric |
| F0X06Y034 | Cross-track cell number | crossTrackCell | CRS - Parametric |
| F0X06Y035 | Maximum size of Y-dimension | maxSizeY | CRS - Parametric |
| F0X06Y040 | Radius of confidence | radiusOfConfidence | CRS - Parametric |
| ID | description | Name | Modifier Type |
| Class 7 - Location (vertical) | Namespace BCV |  |
| F0X07Y001 | Height of station (see Note 1) | heightStation | CRS - Vertical |
| F0X07Y002 | Height or altitude | height_1 | CRS - Vertical |
| F0X07Y003 | Geopotential | geopotential_1 | CRS - Parametric |
| F0X07Y004 | Pressure | pressure | CRS - Parametric |
| F0X07Y005 | Height increment | heightIncremt | CRS - Vertical |
| F0X07Y006 | Height above station | heightAboveStation | CRS - Vertical |
| F0X07Y007 | Height | height_2 | CRS - Vertical |
| F0X07Y008 | Geopotential | geopotential_2 | CRS - Parametric |
| F0X07Y009 | Geopotential height | geopotentialHeight | CRS - Parametric |
| F0X07Y010 | Flight level | flightLevel | CRS - Parametric |
| F0X07Y011 | Pressure (high precision) | hiPrecsnPressure | CRS - Parametric |
| F0X07Y012 | Grid point altitude | gridPtAltitude | CRS - Parametric |
| F0X07Y021 | Elevation (see Note 2) | elevation | CRS - Parametric |
| F0X07Y022 | Solar elevation | solarElevation | CRS - Parametric |
| F0X07Y024 | Satellite zenith angle | SatZenith_1 | CRS - Parametric |
| F0X07Y025 | Solar zenith angle | solarZenith | CRS - Parametric |
| F0X07Y026 | Satellite zenith angle | SatZenith_2 | CRS - Parametric |
| F0X07Y030 | Height of station ground above mean sea level (see Note 3) | stationHeight-MSL | CRS - Parametric |
| F0X07Y031 | Height of barometer above mean sea level (see Note 4) | barometerHeight-MSL | CRS - Parametric |
| F0X07Y032 | Height of sensor above local ground (or deck of marine platform) | heightSensor-Platform | CRS - Parametric |
| F0X07Y033 | Height of sensor above water surface (see Note 6) | heightSensor-Water | CRS - Parametric |
| F0X07Y035 | Maximum size of –z dimension | maxSizeZ | CRS - Parametric |
| F0X07Y036 | Level index of Z | levelIndexZ | CRS - Parametric |
| F0X07Y040 | Impact parameter (see Note 7) | impactParameter | CRS - Parametric |
| F0X07Y061 | Depth below land surface | depthLand | CRS - Parametric |
| F0X07Y062 | Depth below sea/water surface | depthSea | CRS - Parametric |
| F0X07Y063 | Depth below sea/water surface (cm) | depthSeaCm | CRS - Parametric |
| F0X07Y064 | Representative height of sensor above station (see Note 8) | effectiveSensorHeight | CRS - Parametric |
| F0X07Y065 | Water pressure | waterPressure | CRS - Parametric |
| F0X07Y070 | Drogue depth | drogueDepth | CRS - Parametric |
| ID | description | Name | Modifier Type |
| Class 8 - Significance qualifiers | Namespace BCS |  |
| F0X08Y001 | Vertical sounding significance | soundingVerticalSig | Inheritance - Discrimination |
| F0X08Y002 | Vertical significance (surface observations) | surfaceVerticalSig | Inheritance - Discrimination |
| F0X08Y003 | Vertical significance (satellite observations) | SatVerticalSig | Inheritance - Discrimination |
| F0X08Y004 | Phase of aircraft flight | flightPhase | Property - Quality |
| F0X08Y005 | Meteorological attribute significance | MetAttributeSig | Inheritance - Discrimination |
| F0X08Y006 | Ozone vertical sounding significance | ozoneVerticalSig | Inheritance - Discrimination |
| F0X08Y007 | Dimensional significance | dimensionalSig | Property |
| F0X08Y008 | Radiation vertical sounding significance | radiationVerticalSig | Inheritance - Discrimination |
| F0X08Y009 | Detailed phase of flight | flightPhaseDetail | Property - Quality |
| F0X08Y010 | Surface qualifier (temperature data) | surfaceTempSig | Inheritance - Discrimination |
| F0X08Y011 | Meteorological feature | MetFeature | Inheritance - Discrimination |
| F0X08Y012 | Land/sea qualifier | landSea | Property |
| F0X08Y013 | Day/night qualifier | dayNight | Property |
| F0X08Y014 | Qualifier for runway visual range | runwayVisualRange | Property - Quality |
| F0X08Y015 | Significance qualifier for sensor | sensorSigQualifier | Property - Role |
| F0X08Y016 | Change qualifier of a trend-type forecast or an aerodrome forecast | TRENDchange | Property - Role |
| F0X08Y017 | Qualifier of the time when the forecast change is expected | nextForecast | Property |
| F0X08Y018 | SEAWINDS land/ice surface type | SEAWINDlandIce | Property |
| F0X08Y019 | Qualifier for following centre identifier | followingCentreIDQ | Property - Role |
| F0X08Y020 | Total number of missing entities (with respect to accumulation or averaged) | numberMissing | Property - Quality |
| F0X08Y021 | Time significance | timeSig | Property - role |
| F0X08Y022 | Total number (with respect to accumulation or average) | totalNumber | Property - Quality |
| F0X08Y023 | First-order statistics | firstOrderStatistic | Inheritance - Discrimination |
| F0X08Y024 | Difference statistics | differenceStatistic | Inheritance - Discrimination |
| F0X08Y025 | Time difference qualifier (see Note 5) | timeDifferenceSig | Property - Role |
| F0X08Y026 | Matrix significance | matrixSig | Inheritance - Discrimination |
| F0X08Y027 | Matrix geometry | matrixGeom | Inheritance - Discrimination |
| F0X08Y028 | Remotely-sensed surface type | remoteSurfaceType | Property - Role |
| F0X08Y029 | Surface type | surfaceTypeSig | Property - Role |
| F0X08Y030 | Manual on Codes (Volume I.1, Section C) Code table from which data are derived | sectionC_CodeTable | Property - ID |
| F0X08Y031 | Data category - CREX table A | CREX_TableA | Property - ID |
| F0X08Y032 | Status of operation | opStatus | Property - Role |
| F0X08Y033 | Method of derivation of percentage confidence (see Note 6) | percentConfMethod | Property - Role |
| F0X08Y035 | Type of monitoring exercise | monitoringExercise | Property - Role |
| F0X08Y036 | Type of centre or station performing monitoring | monitoringCentreType | Property - Role |
| F0X08Y039 | Time significance (Aviation forecast) | timeSig | Property - Role |
| F0X08Y040 | Flight Level significance | flightLevelSig | Property - Quality |
| F0X08Y041 | Data significance | dataSig | Inheritance - Discrimination |
| F0X08Y042 | Extended vertical sounding significance | extendedSoundingSig | Inheritance - Discrimination |
| F0X08Y043 | Atmospheric chemical or physical constituent type | atmosConstType | Property |
| F0X08Y044 | CAS registry number | CASRegistryNum | Property - ID |
| F0X08Y045 | Particulate matter characterization | particleChar | Property |
| F0X08Y046 | Atmospheric chemical or physical constituent type | atmosConstSubType | Property |
| F0X08Y049 | Number of observations | numberObs | Property - Quality |
| F0X08Y050 | Qualifier for number of missing values in calculation of statistic | missingQualifier1 | Property - Quality |
| F0X08Y051 | Qualifier for number of missing values in calculation of statistic | missingQualifier2 | Property - Quality |
| F0X08Y052 | Condition for which number of days of occurrence follows | numberDaysEvent | Inheritance - Discrimination |
| F0X08Y053 | Day of occurrence qualifier | dayEventQualifier | Property - Quality |
| F0X08Y054 | Qualifier for wind speed or wind gusts | windSpeedQual | Property - Quality |
| F0X08Y060 | Sample scanning mode significance | scanningModeSig | Property |
| F0X08Y065 | Sun-glint indicator | sunGlint | Property - Quality |
| F0X08Y066 | Semi-transparency indicator | semiTransparent | Property - Quality |
| F0X08Y070 | TOVS/ATOVS product qualifier | ATOVSqualifier | Property - ID |
| F0X08Y072 | Pixel(s) type | pixelType | Property - Quality |
| F0X08Y074 | Altimeter echo type | echoType | Property - Quality |
| F0X08Y075 | Ascending/descending orbit qualifier | ascendDescendOrbit | Property |
| F0X08Y076 | Type of band | bandType | Property - ID |
| F0X08Y077 | Radiometer sensed surface type | sensedSurfaceType | Property - Quality |
| F0X08Y079 | Product status | productStatus | Property - Quality |
| F0X08Y080 | Qualifier for GTSPP quality flag | GTSPP_Q_flag | Property |
| F0X08Y081 | Type of equipment | GTSPP_Q_flag | Property |
| F0X08Y082 | Modification of sensor height to another value | sensorHeightCorrectn | Property - Quality |
| F0X08Y083 | Nominal value indicator | nominalValueFlag | Property - Quality |
| F0X08Y085 | Beam identifier | beamID | Property |
| F0X08Y090 | Decimal scale of following significands | decimalScale | Property |

## Annex B:

### BUFR Data Model Description

## Domain Objects

Type:		Package

Package:	BUFR_featureCatalogue

Detail:		Last modified on 18/01/2006.

Notes:

Domain Objects

Created By:	gil.ross on 11/01/2006

Last Modified:	24/09/2010, Version:1.0

### BUFR_catalogue

Stereotype: «metaclass», Package: Domain Objects

Detail:	 Last modified on 24/09/2010.

Notes:	BUFR_catalogue is a conceptual catalogue which in reality is that part of the BUFR Tables concerned with data modelling rather than metadata or coding formats.

BUFR Tables (Modeling Tables in Italics)

BUFR Table A	metadata information which lists the Data Category within which a BUFR bulletin (instance) exists.

BUFR Table B	The main modeling Table, consisting of 29 sub-tables of BUFR Descriptor Classes (Feature and Modifier Classes). Each class consists of up to 255 simple features or modifiers which also includes coding information (precisions and units). Features and modifiers have numerical values (in named units of measure) or are code or flag values. There are over 1000 simple (unmodified) feature entries And over 400 modifier entries.

BUFR Table C	A mixture of coding instructions (mostly to affect precision information) and modeling and coding information used to identify quality and verification statistics. The modeling information in Table C is so specific to QC and verification tasks it is NOT included in this outline BUFR-ISO model.

BUFR Table D	Coding macros used as templates in the coding and decoding process.

Code and Flag Tables

These are tables related to every Table B entry whose values are codes of flags. A Table B entry which is a code can take any one of the code values listed, while those which are flags can take multiple values listed. There are nearly 400 different sub-tables mapping to Table B entries which are codes or flags. These include 160 modifiers which can take 1800 different modifier codes.

Common Code Tables

These are code tables which are not specific to BUFR, although they map to entries in the BUFR metadata or to some Table B entries. There are 12 Common Code Tables with more than 1600 entries defining originating centres and sub-centres, instrumentation types and techniques, satellite and satellite instrument identifiers, units of measure and data sub-categories of Table A.

Not included in these tables are other WMO catalogues listing WMO and ICAO observing stations, ships of the voluntary observing fleet, daily data reporting schedules, etc. etc.

Columns

| Name | Type | Notes |
| --- | --- | --- |
| BUFR_class | BUFR_classEnumeration | This is essentially the BUFR Table B index of tables (BUFR_descriptors) augmented with a class namespace and a class type (modifier or feature) |

Relationships

| Association | Notes |
| --- | --- |
| BUFR_descriptors. | The BUFR_catalogue is composed of 29 classes of these ~1500 descriptors |

### BUFR_descriptors

Stereotype: «metaclass», Package: Domain Objects

Detail:	  Last modified on 24/09/2010.

Notes:	The set of 29 classes of BUFR Table B descriptor types. There are 8 modifier classes and 21 feature classes. Classes with BUFR_ClassCode less than 10 are modifiers, 10 or greater are simple features.
BUFR identifiers (here descriptorCode) are f xx yyy or in XML suitable form FfXxxYyyy where:
Ff	indicates the descriptor code type 0, 1, 2 or 3. Table B model descriptors are all f = 0.
Xxx	for the Table B model is the BUFR_classCode representing 0 to 45 in 29 values. F0Xxx indicates the Table B class.
Yyyy	is the entry in the Table B class table for a single descriptor. The values can range from 0 to 255.
Where the valueType is codeTable or flagTable, the value FfXxxYyyy identifies the particular codeFlagTable in which the code or flag values can be dereferenced.

Columns

| Name | Type | Notes |
| --- | --- | --- |
| descriptorCode | char | The BUFR Table B code number e.g. BUFR Table B class 12 entry 001 (dry bulb temperature) has BUFR code 0 12 001 or F0X12Y001 in XML code. |
| description | char | The description e.g. “dry bulb temperature” for F0X12Y001 |
| name | char | A camelCase name with a class namespace prefix. This is a component added to the BUFR Tables e.g. BT1_dryBulbTemp for F0X12Y001 |
| valueType |  | The data type of the descriptor value, number code or flag: number for F0X12Y001 (the units, Kelvin, is listed in the precisionInformation.) |
| value | valueType | The value in an instance of the descriptor |
| precisionInformation |  | The data type associated with the coding precision information and unit of measure. This is both model and coding information included to complete the Table B information. |

Relationships

| Association | Notes |
| --- | --- |
| BUFR_catalogue. | The BUFR catalogue is composed of BUFR Descriptors. |
| BUFR_modifier. | A BUFR_descriptor is either a modifier or a feature |
| BUFR_simpleFeature. | A BUFR_descriptor is either a simple feature or a modifier |

### BUFR_feature

Stereotype: «abstract», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	The name BUFR_feature elides the ISO distinction between featureType and features in a feature instance, because BUFR declares its feature types within every instance. There is no fixed catalogue of BUFR features, the BUFR model defines the language to be used to define the feature types in an instance (in BUFR – a bulletin). Data collectors can use the language to define new information describing new data. 
BUFR features match up to one or more BUFR descriptors. When it matches to a single descriptor, the feature is described as a single feature. Other features are combined descriptors, where a feature (either a simple feature or a modified feature) is changed by a modifier. Since modifier can be used iteratively, the possible number of feature (types) can be huge.

Relationships

| discriminatedFeature | BUFR_modifiedFeature. | modifiedFeatures are discriminated Features (ISO 19126), with inherited properties of the feature the modifier operates on. |
| --- | --- | --- |
|  | BUFR_simpleFeature | All features inherit from or are BUFR_simpleFeatures |
|  | BUFR_featureCollection | An collection (aggregation) of BUFR_features collected by a modifier acting as a groupingModifier in a hierarchy. |
|  | BUFR_modifier.modifies BUFR_feature.is modified by | Relationship between any feature and an appropriate modifier. |
|  | Mapping_BUFR-ISO_feature. BUFR_feature. | This is a conceptual mapping between WMO defined BUFR Features and an ISO catalogue acting as a sub-catalogue of the BUFR catalogue. |
|  | note. | Note attached to the object in the UML diagram |

### BUFR_featureCollection

Stereotype: «type», Package: Domain Objects

Detail:	 Last modified on 24/09/2010.

Notes:	A featureCollection is the result of a modifier operating in two modes, including as a groupingModifier acting on a set of features. As an example the following pseudo BUFR code:

The modifier with name surfaceVerticalSig in modifier class 8, classNamespace BCS, has a code value 21. This denotes that the collection of features cloudAmount, cloudType and cloudBaseHeight have been measured with an instrument, and are the lowest detected layer. F0 denotes a Table B code (BUFR F number 0) in Class X08 (BUFR Table B class 08 – Significance qualifier) and Y002 denotes descriptor 2 which defines the significance of a layer in the vertical measured from instruments on the surface (ground) of the earth.

<F0X08Y002 name="BCS_surfaceVerticalSig" type=”modifier”>

<value units="CODE TABLE " code=”21”>First instrument detected cloud layer</value>

<F0X20Y011 name="BObs_cloudAmount" type=”feature”>

<value units="CODE TABLE " code=”6”> 6 oktas	7/10 - 8/10</value>

</F0X20Y011>

<F0X20Y012 name="BObs_cloudType" type=”feature”>

<value units="CODE TABLE " code=”59”> Cloud not visible owing to darkness, fog, duststorm, sandstorm, or other analogous phenomena </value>

</F0X20Y012>

<F0X20Y013 name="BObs_cloudBaseHeight" type=”feature”>

<value units="M ">1800</value>

</F0X20Y013>

</F0X08Y002>

Relationships

| Association | Notes |
| --- | --- |
| BUFR_feature | A feature collection in ISO is also a feature. The collection is an aggregate of features, grouped by a modifier in groupingModifier mode. |
| BUFR_modifiedFeature | A featureCollection is itself an example of one type of modifiedFeature |

### BUFR_modifiedFeature

Stereotype: «type», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	A modified feature is a feature altered by a BUFR_modifier. The feature being modified may be a simple feature, a feature collection or an already modified feature

Relationships

| Association | Notes |
| --- | --- |
| BUFR_feature. | A modifiedFeature is a type of the feature |

### BUFR_modifier

Stereotype: «abstract», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	A modifier is a BUFR descriptor of Class code less than 10. In BUFR these are known as Generalised Coordinates. They act on features to produce modifications in at least 4 ways, sometimes in multiple modes. The 4 mechanisms are characterised as 4 “functions” in concept, and also as 4 “types” of modifier. These are 4 different mechanisms in ISO (and XML) which are a single mechanism in BUFR.

Modifier Function

groupFeatureCollection	The only modelling hierarchy mechanism in BUFR. (Other than mainly coding blocks (such as replications and subsets) in a BUFR bulletin or instance).

createFeatureAttribute	  The operation which adds an attribute (as in ISO FC_featureAttribute) to a feature. These attributes can be a number of ISO property types, geographical identifier, role, source, originator, operator, horizontal, vertical and temporal position (all of which can be parametric in distinction to ISO19110-2 which recognises only parametric locations in the third (vertical) dimension), temporal attribute, instrumentation or technique qualifier and quality information.

createDiscriminantedFeatureAttribute	An operation which performs an inheritance association on a feature to derive a discriminatedFeature. This modifier is described as a discriminantModifier. 
An example is where a simpleFeature F0X12Y001 is the “dry bulb temperature” which is used in unmodified form to denote the “air temperature” measured at the surface. This is actually measured in a Stephenson screen at 1.5 or 2 metres above bare soil.

However if F0X12Y001 is modified by a F0X08Y042 flag of 1 – “extended vertical significance qualifier” in a BUFR TEMP profile (a sounding profile of upper air observations) it denotes a surface temperature, while with a flag value of 3 it denotes the temperature measured at the tropopause. In pseudo BUFR-XML:

a)

<F0X08Y042 name=”BCS_extendedSoundingSig” type=”modifier”>

<value units="FLAG TABLE " bit=”1”>Surface</value>

<F0X12Y001 name=”BT1_dryBulbTemp” type=”feature”>

<value units=”K”>nnn.n</value>

</F0X12Y001>

</F0X08Y042>

Or

b)

<F0X08Y042 name=”BCS_extendedSoundingSig” type=”modifier”>

<value units="FLAG TABLE " bit=”3”>Tropopause level</value>

<F0X12Y001 name=”BT1_dryBulbTemp” type=”feature”>

<value units=”K”>nnn.n</value>

</F0X12Y001>

</F0X08Y042>

These are two completely different temperature types and would never be compared or combined. They both inherit from the F0X12Y001 simpleFeature and in ISO 19126 the modifier is equivalent to a discriminatedAttribute.

createCoverageCoordinate	This operation associates another simple feature with a discriminatedAttribute to create a discriminatedFeature which measures the value in an independent dimension in the “vertical” (which is usually a parametric coordinate). The modifier is classed as a discriminantCoverageModifier.
An example is a temperature modified by a vertical level of a pressure where the simpleFeature “dry bulb temperature” is converted into an elevated temperature measured at 500 hectoPascals, and the discriminantCoverageModifier creates a fourth coverage coordinate of 500 hPa. Of course in any BUFR bulletin (instance) which included this, the other three coordinates of horizontal location and dateTime would apply to the entire observation (probably also with geographic identifier, surface station information, instrumentation and operator information).

c)

<F0X07Y004 name=”BCV_pressure” type=”modifier”>

<value units="Pa">500000</value>

<F0X12Y001 name=”BT1_dryBulbTemp” type=”feature”>

<value units=”K”>nnn.n</value>

</F0X12Y001>

</F0X07Y004>

Nested Modifiers	Modifiers can be nested. In some cases the order of the nested modifiers can be switched without misunderstanding, but in general nesting order may be non-commutative. (A.B.Feature is not the same as B.A.Feature).

An example with all functions together is taken from a TEMP sounding:

d)

<F0X08Y042 name=”BCS_extendedSoundingSig” type=”modifier”>

<value units="FLAG TABLE " bit=”2”>Standard level</value>

<F0X07Y004 name=”BCV_pressure” type=”modifier”>

<value units=”Pa”>50000</value>

<F0X11Y001 name”BWT_windDirn“ type=”feature”>

<value units=”degrees true”>nnn</value>

</F0X11Y001>

<F0X11Y002 name”BWT_windSpeed” type=”feature>

<value units=”m s-1”>nnnn</value>

</F0X11Y002>

<F0X11Y061 name”BWT_shear_1kmBelow” type=”feature”>

<value units=”m s-1”>nnnn</value>

</F0X11Y061>

<F0X11Y062 name”BWT_shear_1kmAbove” type=”feature”>

<value units=”m s-1”>nnnn</value>

</F0X11Y062>

</FX07Y004>

</F0X08Y042>

Here the extended sounding significance (F0X08Y042) can either be taken as discriminatedAttribute or a role attribute for the discriminantCoverageModifier (F0X07Y004) (as in c)) both of which act as groupingModifiers for the 4 features in a featureCollection.

Columns

| Name | Type | Notes |
| --- | --- | --- |
| modifierType | char | A type assigned to the modifier. As in example d) in this section above, there is some degree of arbitrariness in the ISO association which should be used. |
| attributeType | char | An featureAttribute property assigned to each modifier. Thes include clear properties such as identifier, instrumentation and various role types, to discriminatedAttribute, horizontal, vertical and temporal coordinates and datums etc. |
| coverageCoordinateName | char | Where a coverage coordinate is included, it is the prescribed feature or modifier which follows or is assigned to the modifier |
| coverageCoordinateCode | int | The code value of the previous term |

Functions (these are the conceptual functionality of a modifer and do not exist in function form)

| Name | Type | Notes |
| --- | --- | --- |
| createFeatureAttribute | Conceptual | The operation which adds an attribute (as in ISO FC_featureAttribute) to a feature. |
| createDiscriminatedFeatureAttrtibute | Conceptual | An operation which performs an inheritance association on a feature to derive a discriminatedFeature. |
| groupFeatureCollection | Conceptual | The only modelling hierarchy mechanism in BUFR. |
| createCoverageCoordinate | Conceptual | An operation associating another simple feature or modifier with a discriminatedAttribute to create a discriminatedFeature which measures the value in an independent dimension in the “vertical” (which is usually a parametric coordinate). |

Relationships

| Association | Notes |
| --- | --- |
| groupingModifier. | A notional type of modifier which creates a featureCollection type of feature |
| BUFR_descriptors. | A BUFR_modifier is a BUFR_descriptor in BUFR_Class less than 10 |
| BUFR_modifier. BUFR_modifier. | BUFR_modifiers can be nested in order. This can also be identified as a secondary modification to the primary modifier, assigning a role for example. |
| BUFR_modifier.modifies BUFR_feature.is modified by | The relationship between features and modifiers |
| discriminantModifier. | A type of modifier which applies an inheritance relation to the modified feature creating a discriminatedFeature |
| discriminantCoverageModifier. | A type of modifier which applies a coverage coordinate (and implicitly an inheritance relation) to the modified feature creating a discriminatedFeature with a third, fourth or higher coordinate value. |
| attributeModifier.. | A type of modifier which assigns an attribute to the modifiedFeature |

### BUFR_simpleFeature

Stereotype: «type», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	Simple features are the basis of all features. They are unmodified Table B descriptors where the class code number is 10 or greater.

Relationships

| Association | Notes |
| --- | --- |
| BUFR_feature | All features inherit from BUFR_simpleFeature. All features have at the basis one or more simpleFeatures which are unmodified Table B descriptors of code > 9 |
| BUFR_descriptors | All features inherit from BUFR_simpleFeature each of which is a BUFR_descriptor in BUFR terminology. |

### FC_FeatureCatalogue

Stereotype: «metaclass», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	FC_FeatureCatalogue is the ISO 19110 class in Table B1. This represents an ISO feature catalogue created from a sub-set of the BUFR catalogue for a specific community who require a simple catalogue built in the ISO style. The first community to create a catalogue specifically tied to BUFR is the Aviation community represented by EUROCONTROL who are developing WXCM, the Weather eXchange Conceptual Model.
Mapping the weather features to WMO elements in BUFR is necessary, not only because ICAO defines the requirements, but with WMO, they maintain the existing codes read worldwide by millions of  pilots each day.

Relationships

| Association | Notes |
| --- | --- |
| FC_FeatureType. | The feature types contained in FC_FeatureCatalogue |

### FC_FeatureType

Stereotype: «abstract», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	The types of features in the ISO feature catalogue which are mapped from the BUFR features used by the specific community who use the catalogue.

Relationships

| Association | Notes |
| --- | --- |
| Mapping_BUFR_ISO_feature. | A mapping to the equivalent feature type in the BUFR feature catalogue |
| FC_FeatureCatalogue. | The community feature catalogue holding these feature types. |

### attributeModifier

Stereotype: «type», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	 A type of modifier which assigns an attribute to the (as in ISO FC_featureAttribute) to a modifiedFeature. These attributes can be a number of ISO property types, geographical identifier, role, source, originator, operator, horizontal, vertical and temporal position (all of which can be parametric in distinction to ISO19110-2 which recognises only parametric locations in the third (vertical) dimension), temporal attribute, instrumentation or technique qualifier and quality information.

Relationships

| Association | Notes |
| --- | --- |
| BUFR_modifier. | A type of modifier which assigns an attribute to the modifiedFeature |

### discriminantCoverageModifier

Stereotype: «type», Package: Domain Objects

Detail:  Last modified on 24/09/2010.

Notes:	A type of modifier which associates another simple feature with a discriminatedAttribute to create a discriminatedFeature which measures the value in an independent dimension in the “vertical” (which is usually a parametric coordinate). The modifier is classed as a discriminantCoverageModifier.
Example c) in the BUFR_modifier section above shows this effect.

Relationships

| Association | Notes |
| --- | --- |
| BUFR_modifier. | A type of BUFR_modifier which associates another simple feature with a discriminatedAttribute to create a discriminatedFeature which measures the value in an independent dimension |

### discriminantModifier

Stereotype: «type», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	A type of modifier which applies an inheritance association on a feature to derive a discriminatedFeature. This modifier is described as a discriminantModifier. 
The examples a) and b) in BUFR_modifier section above are examples..

Relationships

| Association | Notes |
| --- | --- |
| BUFR_modifier. | A type of BUFR_modifier which applies an inheritance relation to the modified feature creating a discriminatedFeature |

### groupingModifier

Stereotype: «type», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	 The only modelling hierarchy mechanism in BUFR. (Other than the - essentially coding - blocks (such as replications and subsets) in a BUFR bulletin or instance).

Relationships

| Association | Notes |
| --- | --- |
| BUFR_modifier. | A type of BUFR_modifier which creates BUFR_featureCollections, and is the only modelling hierarchy mechanism in BUFR. |

### Mapping_BUFR-ISO_feature

Stereotype: «interface», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	The interface which maps BUFR to ISO and back. It is a a conceptual mapping because, even if a formal mapping from a BUFR instance to an ISO instance can be created, a transformation fronm BUFR to ISO instances is likely to be mediated through databases at individual data repositories,  which are often very dissimilar.

Relationships

| Association | Notes |
| --- | --- |
| BUFR_feature. | Mapping from ISO to BUFR |
| FC_FeatureType. | Mapping from BUFR to ISO |

### BUFR_classEnumeration

Stereotype: «table», Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	This data type is the list of Table B classes augmented with a class namespace and a class type.

Columns

| Name | type | Notes |
| --- | --- | --- |
| BUFR_className | char |  |
| BUFR_classCode | int |  |
| BUFR_classNamespace | char |  |
| BUFR_classDescription | char |  |
| BUFR_classType | char | The type of descriptor: modifier with classCode .≤ 9 Feature with classCode > 9 |

### precisionInformation

Stereotype: , Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	The precision information is, apart from the units, the coding information needed to convert to and from the BUFR coded value which is stored in an unsigned integer. This makes the values all fixed point numbers or integers. 
precision information is included in this model for completeness, as BUFR Table B stores this information with the rest of the descriptor information.

Columns

| Name | Type | Notes |
| --- | --- | --- |
| BUFR_units | char | The units used in the BUFR coding. These are SI or derived from SI but contain some non-SI units, such as kilofeet, mandated by aviation law. . |
| BUFR_scale | int | The scale is the power of ten mantissa required to convert the coded BUFR value to the defined units. |
| BUFR_reference | int | An offset value to be added to the coded value (before rescaling) converting from an unsigned number to a signed value |
| BUFR_width | int | The number of bits used to store the coded value |
| CREX_units | char | The units used in the CREX character form coding |
| CREX_scale | int | The scale is the power of ten mantissa required to convert the coded BUFR value to the defined units |
| CREX_width | int | The number of 8 bit characters used to store the coded value |

### valueType

Stereotype: , Package: Domain Objects

Detail:	Last modified on 24/09/2010.

Notes:	The data type of descriptor values found in an instance of the values. BUFR types are:
number:	integer or fixed point.
characters: 	characters from the CCITT IA5 character set 
code table:	code values matching a value or set of values in a look-up table. In ISO terms this can be either a fixed enumeration or an expandable list – no distinction is made. However: there is a maximum value defined by the precisionInformation BUFR_width; unused values are declared as reserved; missing values are the largest allowed value
flag table:	a flag value is a set of binary 1-0 flags. Flags can take multiple values, and the positions in the bit sequence where the bit is set to 1 are the values which apply together. If all the bit sequence values are 1, this indicates a missing value.