| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING BEIJING, CHINA, 20 - 24 JULY 2015 |  | IPET-DRMM-III / Doc. 3.2 (12) (15. 7. 2015) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

Revision of BUFR sequence 3 02 067

Submitted by Sibylle Krebber (DWD)

_______________________________________________________________________

Summary and Purpose of Document

This document contains minor revision of sequence 3 02 067 – additional synoptical parameters.

_______________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the revised sequence and approve it for the next fast track cycle FT2015-2.

DISCUSSIONS

The sequence 3 02 067 (additional synoptical parameters) was first proposed in 2010. Revisions were proposed in 2011 and 2012. This sequence is meant for encoding all parameters in BUFR which could be encoded in FM12-SYNOP so far (e.g. a huge amount of possible 9SPSPspsp groups in section 3).

In the last years no further comments and requirements had been received. Therefore the validation process should be finalised.

Only a minor revision is reasonable in the amount of descriptors at the delayed replication of the “visibility in different directions”.

PROPOSAL

#### The existing sequence 3 02 067 for validation is to be replaced in BUFR table D by the revised sequence:

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME | ELEMENT DESCRIPTION |
| --- | --- | --- | --- |
| F X Y |  |  |  |
|  |  | (Additional synoptical parameters) |  |
| 3 02 067 | 0 01 023 | Observation sequence number |  |
|  |  | Additional “instantaneous” data |  |
|  | 0 04 025 | Time period or displacement | = 0 minutes |
|  | 0 02 177 | Method of snow depth measurement | = 0 Manual observation, = 1 Ultrasonic method, = 2 Video camera method, = 3-13 Reserved, = 14 Others, = 15 Missing value |
|  |  | Additional present weather |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 20 003 | Present weather | 960ww, 961ww |
|  |  | Visibility in different directions |  |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 05 021 | Bearing or azimuth | 981VV-988VV |
|  | 0 20 001 | Horizontal visibility | VV |
|  | 0 05 021 | Bearing or azimuth | Set to missing (cancel) |
|  |  | Sea data (observations from a coastal station) |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 056 | Sea/water temperature | Sea surface temperature, method of measurement, and depth below sea surface |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 33 041 | Attribute of following value |  |
|  | 0 20 058 | Visibility seawards from a coastal station | 980VsVs |
|  | 0 22 061 | State of the sea | 924SVs |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 022 | Wind waves |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 3 02 023 | Swell waves |  |
|  |  | Clouds |  |
|  | 1 04 000 | Delayed replication of 4 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving or in which they are observed | Da, Dp |
|  | 0 20 137 | Evolution of clouds | 940Cn3 |
|  | 0 20 012 | Cloud type | 941CDp, 943CLDp |
|  | 0 20 090 | Special clouds | 993CsDa |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 20 054 | True direction from which a phenomenon or |  |
|  |  | clouds are moving or in which they are observed |  |
|  | 0 20 137 | Evolution of clouds |  |
|  | 0 20 136 | Supplementary cloud type | 948C0Da, 949CaDa, 950Nmn3, 951Nvn4 |
|  |  | Additional "period" data |  |
|  | 0 04 025 | Time period or displacement | Reference period of fresh fallen snow |
|  | 0 13 012 | Depth of fresh snow |  |
|  |  | Additional wind data |  |
|  | 0 04 025 | Time period or displacement | = -60 minutes |
|  | 0 11 042 | Maximum wind speed (10-minute mean wind) | 912ff 902tt 912ff .. mandatory ff>=18 |
|  | 1 04 000 | Delayed replication of 4 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 08 021 | Time significance | = 30 Time of occurrence, = 17 Start of phenomenon |
|  | 0 04 025 | Time period or displacement | = -xx ¦ 902tt |
|  | 0 11 042 | Maximum wind speed (10-minute mean wind) | 912ff |
|  | 0 08 021 | Time significance | Set to missing (cancel) |
|  |  | Significant change in wind speed and/or direction |  |
|  | 1 15 000 | Delayed replication of 15 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 08 021 | Time significance | = 30 Time of occurrence, |
|  |  |  | = 17 Start of phenomenon |
|  | 0 04 015 | Time increment | = -xx1 |
|  | 0 08 021 | Time significance | = 2 Time averaged |
|  | 0 04 025 | Time period or displacement | = -10 minutes, or number of minutes after a significant change of wind |
|  | 0 11 001 | Wind direction | 915dd |
|  | 0 11 002 | Wind speed | 913ff |
|  | 0 08 021 | Time significance | = 22 Time of occurrence of wind shift |
|  | 0 04 015 | Time increment | = +xx2 |
|  | 0 08 021 | Time significance | = 2 Time averaged |
|  | 0 04 025 | Time period or displacement | = -10 minutes, or number of minutes after a significant change of wind |
|  | 0 11 001 | Wind direction | 915dd |
|  | 0 11 002 | Wind speed | 913ff |
|  | 0 08 021 | Time significance | Set to missing (cancel) |
|  | 0 04 025 | Time period or displacement | = 0 minutes |
|  | 0 04 015 | Time increment | = +(xx1-xx2) ¦ Non negative to reset the time to the actual time |
|  |  | Additional weather |  |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 04 025 | Time period or displacement | = -xx, i.e. from |
|  | 0 04 025 | Time period or displacement | = -xx, i.e. to |
|  | 0 20 003 | Present weather | 962ww, 963w1w1, 964ww, 965w1w1, 966ww, 967w1w1 |
|  |  | Additional 9SpSpspsp groups |  |
|  | 1 10 000 | Delayed replication of 10 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 04 025 | Time period or displacement | = -xx, i.e. from |
|  | 0 04 025 | Time period or displacement | = -xx, i.e. to |
|  | 0 05 021 | Bearing or azimuth | Da, Dp |
|  | 0 05 021 | Bearing or azimuth | Da, Dp |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving | Da, Dp |
|  | 0 20 024 | Intensity of phenomena | = 1 Light, = 2 Moderate = 3 Heavy = 4 Violent = 5 Severe |
|  | 0 20 025 | Obscuration |  |
|  | 0 20 026 | Character of obscuration |  |
|  | 0 20 027 | Phenomena occurrence |  |
|  | 0 20 063 | Special phenomena |  |