| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING BEIJING, CHINA, 20 - 24 JULY 2015 |  | IPET-DRMM-III / Doc. 3.2 (13) (15. 7. 2015) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR

New BUFR elements and sequence for international exchange of Road Weather Information

Submitted by Sibylle Krebber, Vanessa Stauch (DWD)

_______________________________________________________________________

Summary and Purpose of Document

New elements and a sequence are proposed to encode road weather information in BUFR.

_______________________________________________________________________

ACTION PROPOSED

The team is requested to review the proposal and approve the new elements and sequence for validation.

ANNEXES:

- ET/DR&C/Doc. 5.3(3) submitted bei Eva Cervená

- Response2comments_UK_CMHI-RoadWeatherInformation.pdf (Response from Eva Cervená to the Comments on BUFR template for cross-border exchange of Road Weather Information, received from Mr. Stanley Kellett (UK))

DISCUSSIONS

Based on several recent bilateral data exchange activities with neighbouring countries, DWD would like to motivate the resumption of the development of a BUFR template for cross-border exchange of Road Weather Information. The aim is to facilitate the standardised transmission of this data within the WMO framework and, specifically, to include descriptors in the WMO BUFR tables that have thus far been used as local descriptors in a template for bilateral road weather data exchange between the Czech Hydrometeorological Institute (CHMI) and German Weather Service (DWD)

In 2007, Eva Cervená presented a proposed BUFR template at the ET DR&C meeting. The template was designed to allow the bilateral exchange of road weather data between the national weather services CHMI and DWD. The purpose of the presentation was to inform about this development in the context of the Regional TDCF Migration Plan. The presentation resulted in a discussion between Stanley Kellett (UK MetOffice) and Eva Cervená, but ebbed away over the following years.

Now, DWD would like to continue the standardization of road weather information encoded in BUFR.

PROPOSAL

The following new BUFR table B entries and corresponding code tables are proposed:

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH |
| 0 01 104 | State / federal state identifier | CCITT IA5 | 0 | 0 | 32 | CCITT IA5 | 0 | 4 |
| 0 01 105 | Highway designator | CCITT IA5 | 0 | 0 | 40 | CCITT IA5 | 0 | 5 |
| 0 01 106 | Routes kilometre of highway | m | -2 | 0 | 14 | m | -2 | 5 |
| 0 03 016 | Position of road sensors | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 03 017 | Extended type of station | Flag table | 0 | 0 | 6 | Flag table | 0 | 2 |
| 0 03 018 | Type of road | Code table | 0 | 0 | 5 | Code table | 0 | 2 |
| 0 03 019 | Type of construction | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 12 128 | Road surface temperature | K | 2 | 0 | 16 | C | 2 | 5 |
| 0 12 129 | Road sub-surface temperature | K | 2 | 0 | 16 | C | 2 | 5 |
| 0 13 116 | Water film thickness | m | 3 | 0 | 7 | m | 3 | 2 |
| 0 20 138 | Road surface condition | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Code and Flag-tables:

0 03 016   Position of road sensors

| Code figure |  |
| --- | --- |
| 0 | Fast lane between the wheel tracks |
| 1 | Fast lane between the wheel tracks in the opposite direction |
| 2 | Fast lane in the wheel tracks |
| 3 | Fast lane in the wheel tracks in the opposite direction |
| 4 | Slow lane between the wheel tracks |
| 5 | Slow lane between the wheel tracks in the opposite direction |
| 6 | Slow lane in the wheel tracks |
| 7 | Slow lane in the wheel tracks in the opposite direction |
| 8 - 14 | Reserved |
| 15 | Missing value |

0 03 017   Extended type of station

| Bit No. |  |
| --- | --- |
| 1 | Automatic |
| 2 | Manned |
| 3 | Event triggered |
| 4 | Longer time period than the standard |
| 5 | Reserved |
| all 6 | Missing value |

0 03 018   Type of road

| Code figure |  |
| --- | --- |
| 0 | Free track without further information |
| 1 | Free track, embankment |
| 2 | Free track, flat relative to surroundings |
| 3 | Free track, water basin(s) in vicinity |
| 4 | Free track, forest |
| 5 | Free track, cleft |
| 6 | Free track, on hilltop |
| 7 | Free track, on hilltop, forest |
| 8 | Free track, in valley |
| 9 | Free track, in valley, forest |
| 10 | Free track, north inclination |
| 11 | Free track, north inclination, forest |
| 12 | Free track, south inclination |
| 13 | Free track, south inclination, forest |
| 14-19 | Reserved |
| 20 | Bridge without further information |
| 21 | Bridge across a valley in a urban area |
| 22 | Bridge across a valley with forest/meadows/fields |
| 23 | Bridge across street/track |
| 24 | Bridge across big river/canal |
| 25 | Bridge across river/canal of medium size |
| 26 | Bridge across a small stream/loading canal |
| 27-30 | Reserved |
| 31 | Missing value |

0 03 019   Type of construction

| Code figure |  |
| --- | --- |
| 0 | Asphalt |
| 1 | Concrete |
| 2 | Concrete construction |
| 3 | Steel-girder construction |
| 4 | Box girder bridge |
| 5 | Orthotrope slab |
| 6 | Drain asphalt |
| 7-14 | Reserved |
| 15 | Missing value |

0 20 138   Road surface condition

| Code figure |  |
| --- | --- |
| 0 | Dry |
| 1 | Moist |
| 2 | Wet |
| 3 | Rime |
| 4 | Snow |
| 5 | Ice |
| 6 | Glaze |
| 7 | Not dry |
| 8-14 | Reserved |
| 15 | Missing value |

Add new BUFR sequence in BUFR table D:

This sequence is proposed to be used for representation of road weather data.

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME | ELEMENT DESCRIPTION |
| --- | --- | --- | --- |
| F X Y |  |  |  |
|  |  | (Road weather information) |  |
|  |  | Station identification |  |
| 3 07 102 | 3 01 089 | National station identification |  |
|  | 0 01 018 | Short station or site name | For identification of the road weather monitoring site |
|  | 0 01 015 | Station or site name |  |
|  | 0 01 104 | State / federal state identifier |  |
|  | 0 01 105 | Highway designator |  |
|  | 0 01 106 | Routes kilometre of highway |  |
|  | 0 03 017 | Extended type of station |  |
|  | 0 03 018 | Type of road |  |
|  | 0 03 019 | Type of construction |  |
|  | 3 01 011 | Year, month, day |  |
|  | 3 01 012 | Hour, minute |  |
|  | 3 01 021 | Latitude/longitude (high accuracy) |  |
|  | 0 07 030 | Height of station ground above mean sea level |  |
|  |  | Temperature, humidity and visibility data |  |
|  | 0 07 032 | Height of sensor above local ground |  |
|  | 0 12 101 | Temperature/dry-bulb temperature |  |
|  | 0 12 103 | Dew-point temperature |  |
|  | 0 13 003 | Relative humidity |  |
|  | 0 07 032 | Height of sensor above local ground | Set to missing (cancel) |
|  | 0 20 001 | Horizontal visibility |  |
|  |  | Road temperature and other data |  |
|  | 1 09 000 | Delayed replication of 9 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 03 016 | Position of road sensors |  |
|  | 0 12 128 | Road surface temperature |  |
|  | 1 02 000 | Delayed replication of 2 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 07 061 | Depth below land surface | = 0.30 m in the first replication, = e.g. 0.15 or 0.07 m in the second replication |
|  | 0 12 129 | Road sub-surface temperature |  |
|  | 0 07 061 | Depth below land surface | Set to missing (cancel) |
|  | 0 13 116 | Water film thickness |  |
|  | 0 20 138 | Road surface condition |  |
|  |  | Precipitation data |  |
|  | 0 04 025 | Time period | = - 15 minutes |
|  | 0 20 024 | Intensity of phenomena | Intensity (light, moderate, heavy) of precipitation |
|  | 0 13 055 | Intensity of precipitation |  |
|  | 0 20 021 | Type of precipitation |  |
|  | 0 13 011 | Total precipitation / total water equivalent of snow |  |
|  |  | Wind data |  |
|  | 0 07 032 | Height of sensor above local ground |  |
|  | 0 08 021 | Time significance | = 2 Time averaged |
|  | 0 04 025 | Time period | = –10 minutes |
|  | 0 11 001 | Wind direction |  |
|  | 0 11 002 | Wind speed |  |
|  | 0 08 021 | Time significance | Set to missing (cancel) |
|  |  | Maximum wind gust |  |
|  | 0 04 025 | Time period in minutes |  |
|  | 0 11 043 | Maximum wind gust direction |  |
|  | 0 11 041 | Maximum wind gust speed |  |
|  |  | State of functionality |  |
|  | 0 33 005 | Quality information (AWS data) |  |

Remarks:

- To represent Intensity of precipitation, type of precipitation and state of functionality, 
0 20 024 (Code table), 0 20 021(Flag table) and 0 33 005 (Flag table) are used, respectively.

- Some more descriptors are required to reduce the workload with respect to the station database, e.g. for identification of the federal state, identification of the highway, etc.

- The majority of stations has only one position on the road and one sub-surface temperature sensor. Delayed replications have been introduced to increase flexibility and volume efficiency.

- Each position of road sensors includes the measurements of

  - road surface temperature

  - road sub-surface temperatures

  - water film thickness

  - road surface condition

- Some types of station do not have the ability to identify the surface condition accurately. They can only report conditions such as "not dry" or "glazed". The code table for road surface conditions has been adjusted accordingly.

Annexes: