| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING BEIJING, CHINA, 20 - 24 JULY 2015 |  | IPET-DRMM-III / Doc. 3.2 (15) (xx. 6. 2015) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

# BUFR AND CREX

# Synoptic reports from sea stations suitable for VOS observation data

# Submitted by David Berry

_______________________________________________________________________

# Summary and Purpose of Document

Revised BUFR sequence and elements to encode synoptic reports from Voluntary Observing Ships taking into account requirements for consistency between marine and land instrumental metadata.

_______________________________________________________________________

# ACTION PROPOSED

The team is requested to review the proposal and approve the new sequence and elements for validation.

# REFERENCES:

# Final report of the Second Meeting of the Inter-Programme Expert Team on Data Representation Maintenance and Monitoring (IPET-DRMM-II).

# E-SURFMAR recommended ship-to-shore data formats.

# IPET-DRMM-III / Doc 4.2.2 (2).

# DISCUSSIONS

This proposal updates the sequences, and associated descriptors, for reporting Synoptic reports from sea stations suitable for VOS observation data approved for validation at the second meeting of the IPET-DRMM (IPET-DRMM II). The primary change to the sequence takes into account comments at IPET-DRMM II and uses class 3 descriptors for the reporting of humidity and air temperature instrumentation common to both land and marine observations. Other changes include: the addition of a unique identifier for the report; the addition of information on the method used to adjust pressure observations to sea level; and the addition of sequences to allow the reporting of limited bio-geochemical data on the GTS in response to requests from E-SURFMAR. These data are presently observed and reported in real-time but not currently shared on the GTS. The observed units and range for these parameters are given in Table 1. The values in parentheses give the units and converted ranges for BUFR.

Table 1: E-SURFMAR bio-geochemical parameters, units and ranges

| Name | Units | Min | Max | Resolution | Notes |
| --- | --- | --- | --- | --- | --- |
| pCO2 | µatm (Pa) | 100 (10.1325) | 1100 (111.4575) | 0.5 (0.0506625) | Unit conversion to pascal required. |
| Turbidity | NTU | 0 | 20 | 0.01 | New unit required – Nephelometric Turbidity Unit. Lumen’s not suitable. |
| Fluorescence | µg l-1 | 0 | 50 | 0.025 |  |
| Dissolved nitrates | µmol l-1 | 0 | 100 | 0.05 |  |
| Atmospheric CO2 | ppm (ppt) | 350 0.3500 | 450 (0.4500) | 0.1 (0.0001) | Unit conversion to parts per thousand required |

The reporting of ocean turbidity requires the addition of a new unit to BUFR - nephelometric turbidity units (NTU). This is the measurement unit used by the oceanographic community for the measurement of turbidity and is measured directly using instruments calibrated against a standardized sample. There is no simple / easy conversion to lumens - the units currently used for reporting turbidity from class 13 (0 13 084) in BUFR.

# PROPOSAL

Note: Text shaded grey has previously been approved for validation but has not yet been validated. Text in red is either new, awaiting validation status or undergone significant change since last approval for validation status.

BUFR/CREX Table B

Class 01 – BUFR/CREX Identification

Add

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 01 | 114 | Encrypted ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 352 | CCITT IA5 | 0 | 44 |

Class 3 – BUFR/CREX Instrumentation

Add

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 03 | 001 | Surface station type | Code table | 0 | 0 | 5 | Code table | 0 | 2 |
| 0 | 03 | 002 | Type of humidity sensor | Code table | 0 | 0 | 5 | Code table | 0 | 2 |
| 0 | 03 | 003 | Thermometer / hygrometer housing | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 03 | 004 | Type of screen / shelter / radiation shield | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 03 | 005 | Horizontal width of screen or shield (x) | m | 3 | 0 | 16 | m | 3 | 5 |
| 0 | 03 | 006 | Horizontal depth of screen or shield (y) | m | 3 | 0 | 16 | m | 3 | 5 |
| 0 | 03 | 007 | Vertical height of screen or shield (z) | m | 3 | 0 | 16 | m | 3 | 5 |
| 0 | 03 | 008 | Artificially ventilated screen or shield | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 03 | 009 | Amount of forced ventilation at time of reading | m s-1 | 1 | 0 | 9 | m s-1 | 1 | 3 |
| 0 | 03 | 013 | Type of thermometer | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 03 | 016 | Material for thermometer / hygrometer housing | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 03 | 017 | Hygrometer heating | Code table | 0 | 0 | 2 | Code table | 0 | 1 |
| 0 | 03 | 018 | Instrument owner | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 03 | 019 | Configuration of louvers for thermometer / hygrometer screen | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 03 | 020 | Psychrometric coefficient | K-1 | 6 | 0 | 10 | K-1 | 6 | 3 |

Note: the majority of descriptors above were previously proposed at IPET-DRMM-II but have undergone significant revision.

Class 10 – BUFR/CREX Non coordinate location (vertical)

Add

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 10 | 038 | Maximum height of deck cargo above summer load line | m | 0 | 0 | 6 | m | 0 | 2 |
| 0 | 10 | 039 | Departure of reference level (summer maximum load line) from actual sea level | m | 0 | -32 | 6 | m | 0 | 3 |

Class 11 – BUFR/CREX Wind and turbulence

Amend

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 11 | 104 | Aircraft true heading / true heading of ship or other mobile observing platform | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |

Note: Amendment is change of name.

Add

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 11 | 007 | Relative wind direction (in degrees off bow) | Degree | 0 | 0 | 9 | Degree | 0 | 3 |
| 0 | 11 | 008 | Relative wind speed | m s-1 | 1 | 0 | 12 | m s-1 | 1 | 4 |

Class 25 – BUFR/CREX Processing information

Add

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 25 | 185 | Encryption method | Code table | 0 | 0 | 8 | Code table | 0 | 3 |
| 0 | 25 | 186 | Encryption key version | CCITT IA5 | 0 | 0 | 96 | CCITT IA5 | 0 | 12 |
| 0 | 25 | 187 | Method for reducing pressure to sea level | Code Table | 0 | 0 | 5 | Code Table | 0 | 2 |

Class 41 – BUFR/CREX Oceanographic / bio-geochemical parameters

Add

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (char) |
| 0 | 41 | 001 | pCO2 | Pa | 3 | 0 | 18 | Atm | 3 | 6 |
| 0 | 41 | 002 | Fluorescence | kg l-1 | 12 | 0 | 16 | kg l-1 | 12 | 5 |
| 0 | 41 | 003 | Dissolved nitrates | µmol kg-1 | 3 | 0 | 17 | µmol kg-1 | 3 | 5 |
| 0 | 41 | 004 | Atmospheric CO2 | ppt | 5 | 30000 | 15 | ppt | 5 | 5 |
| 0 | 41 | 005 | Turbidity | NTU | 2 | 0 | 12 | NTU | 2 | 4 |

BUFR/CREX Table D

Category 01 – BUFR/CREX Location and identification sequences

Add

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 01 | 018 |  |  |  | (Encrypted ship's call sign and encryption method) |  |
|  |  |  | 0 | 01 | 114 | Encrypted ship or mobile land station identifier |  |
|  |  |  | 0 | 25 | 185 | Encryption method |  |
|  |  |  | 0 | 25 | 186 | Encryption key version |  |

Category 02 – BUFR/CREX Meteorological sequences common to surface data

Add

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 062 |  |  |  | (Ship “instantaneous” data) |  |
|  |  |  | 0 | 25 | 187 | Method for reducing pressure report to sea level |  |
|  |  |  | 3 | 02 | 001 | Pressure and 3-hour pressure change |  |
|  |  |  | 3 | 02 | 093 | Extended ship temperature and humidity data |  |
|  |  |  | 1 | 03 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 053 | Ship visibility data |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 004 | General cloud information |  |
|  |  |  | 3 | 02 | 005 | Cloud layer |  |
|  |  |  | 0 | 08 | 002 | Vertical significance (surface observations) | Set to missing (cancel) |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 055 | Icing and ice |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 056 | Sea/water temperature |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 021 | Waves |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 024 | Wind and swell waves |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 063 |  |  |  | (Ship “period” data) |  |
|  |  |  | 3 | 02 | 038 | Present and past weather |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 040 | Precipitation measurement |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 034 | Precipitation past 24 hours |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 058 | Ship extreme temperature data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 064 | Ship / or other marine platform wind data |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 064 |  |  |  | (Ship / or other marine platform wind data) |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 0 | 02 | 002 | Type of instrumentation for wind measurement |  |
|  |  |  | 0 | 08 | 021 | Time significance | = 2 Time averaged |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 001 | Wind direction |  |
|  |  |  | 0 | 11 | 002 | Wind speed |  |
|  |  |  | 0 | 08 | 021 | Time significance | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |  |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 043 | Maximum wind gust direction |  |
|  |  |  | 0 | 11 | 041 | Maximum wind gust speed |  |

Note: this sequence has been validated and is awaiting approval of its validated status (see document IPET-DRMM-III / Doc 4.2.2 (2).

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 092 |  |  |  | (VOSClim data elements) |  |
|  |  |  | 0 | 11 | 104 | Aircraft true heading / true heading of ship or other mobile observing platform | Ship’s true heading |
|  |  |  | 0 | 01 | 012 | Direction of motion of moving observing platform | Ship’s course over ground |
|  |  |  | 0 | 01 | 013 | Speed of motion of moving observing platform | Ship’s speed over ground |
|  |  |  | 0 | 10 | 038 | Maximum height of deck cargo above summer load line |  |
|  |  |  | 0 | 10 | 039 | Departure of reference level (summer maximum load line) from actual sea level |  |
|  |  |  | 0 | 11 | 007 | Relative wind direction (in degrees off bow) |  |
|  |  |  | 0 | 11 | 008 | Relative wind speed |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | X | YYY |  |  |
| 3 | 02 | 093 |  |  |  | (Extended ship temperature and humidity data) |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 3 | 03 | 099 | Metadata common to temperature / humidity sensors |  |
|  |  |  | 0 | 12 | 101 | Temperature / air temperature |  |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor | set to 0 if no change from previous values, 1 if changes |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 3 | 03 | 099 | Metadata common to temperature / humidity sensors |  |
|  |  |  | 0 | 02 | 039 | Method of wet-bulb temperature measurement |  |
|  |  |  | 0 | 03 | 002 | Type of humidity sensor |  |
|  |  |  | 0 | 03 | 020 | Psychrometer coefficient | Set to missing if type of humidity sensor is not psychrometer |
|  |  |  | 0 | 03 | 017 | Hygrometer heating |  |
|  |  |  | 0 | 12 | 102 | Wet-bulb temperature |  |
|  |  |  | 0 | 12 | 103 | Dewpoint temperature |  |
|  |  |  | 0 | 13 | 003 | Relative humidity |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | Cancel (set to missing) |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface | Cancel (set to missing) |
|  |  |  | 3 | 03 | 099 | Metadata common to temperature / humidity sensors | Cancel (set all elements in sequence to missing) |
|  |  |  | 0 | 02 | 039 | Method of wet-bulb temperature measurement | Cancel (set to missing) |
|  |  |  | 0 | 03 | 002 | Type of humidity sensor | Cancel (set to missing) |
|  |  |  | 0 | 03 | 017 | Hygrometer heating | Cancel (set to missing) |
|  |  |  | 0 | 03 | 020 | Psychrometer coefficient | Cancel (set to missing) |

Note: Significant changes to previously proposed version taking into account need for consistency between land and marine metadata.

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 03 | 099 |  |  |  | Metadata common to temperature / humidity sensors |  |
|  |  |  | 0 | 03 | 005 | Horizontal width of screen or shield (x) |  |
|  |  |  | 0 | 03 | 006 | Horizontal depth of screen or shield (y) |  |
|  |  |  | 0 | 03 | 007 | Vertical height of screen or shield (z) |  |
|  |  |  | 0 | 03 | 013 | Type of thermometer |  |
|  |  |  | 0 | 03 | 018 | Instrument owner |  |
|  |  |  | 0 | 03 | 003 | Thermometer / hygrometer housing |  |
|  |  |  | 0 | 03 | 016 | Material for thermometer / hygrometer housing |  |
|  |  |  | 0 | 03 | 004 | Type of screen / shelter / radiation shield |  |
|  |  |  | 0 | 03 | 019 | Configuration of louvers for thermometer / hygrometer screen |  |
|  |  |  | 0 | 03 | 008 | Artificially ventilated screen or shield |  |
|  |  |  | 0 | 03 | 009 | Amount of forced ventilation at time of reading |  |

Category 06 – BUFR/CREX Meteorological or oceanographic sequences common to oceanographic observations

Add

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 06 | 043 |  |  |  | Ship basic bio-geochemical data |  |
|  |  |  | 0 | 41 | 001 | pCO2 |  |
|  |  |  | 0 | 41 | 004 | Atmospheric CO2 |  |
|  |  |  | 0 | 13 | 080 | pH |  |
|  |  |  | 0 | 41 | 005 | Turbidity |  |
|  |  |  | 0 | 41 | 003 | Dissolved nitrates |  |
|  |  |  | 0 | 22 | 188 | Dissolved oxygen |  |
|  |  |  | 0 | 41 | 002 | Fluorescence |  |

Category 08 – BUFR/CREX Surface report sequences (sea)

Add

| Table reference | Table References | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 08 | 014 |  |  |  | (Synoptic reports from sea stations suitable for VOS observation data) |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 01 | 018 | Encrypted ship’s call sign and encryption method |  |
|  |  |  | 3 | 01 | 093 | Ship identification, movement, date/time, horizontal and vertical coordinates |  |
|  |  |  | 2 | 08 | 032 | Change width of CCITT IA5 to 32 characters |  |
|  |  |  | 0 | 01 | 079 | Unique identifier for profile | Unique ID for report. |
|  |  |  | 2 | 08 | 000 | Change width of CCITT IA5 | Cancel |
|  |  |  | 3 | 02 | 062 | Ship “instantaneous” data |  |
|  |  |  | 3 | 02 | 063 | Ship “period” data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 092 | VOSClim data elements |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 06 | 033 | Surface salinity |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 06 | 034 | Surface current |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 06 | 043 | Ship basic bio-geochemical data |  |

Note: last 3 descriptors (1 01 000 to 3 06 043) to be moved outside 3 08 014 if 3 06 043 not ready for validation.

BUFR/CREX Code tables

Code/flag Tables 03

Add

0 03 001

Surface Station Type

| Code figure | Meaning |
| --- | --- |
| 0 | Land station (synoptic network) |
| 1 | Shallow water station (fixed to sea/lake floor) |
| 2 | Ship |
| 3 | Rig/platform |
| 4 | Moored buoy |
| 5 | Drifting buoy (or drifter) |
| 6 | Ice buoy |
| 7 | Land station (local network) |
| 8 | Land vehicle |
| 9 | Autonomous marine vehicle |
| 10-30 | Reserved (for future use) |
| 31 | Missing value |

0 03 002

Type of humidity sensor

| Code figure | Meaning |
| --- | --- |
| 0 | Psychrometer |
| 1 | Capacitive (Generic) |
| 2 | Capacitive (polymer) |
| 3 | Capacitive (Ceramic inc.Metal-oxide) |
| 4 | Resistive (Generic) |
| 5 | Resistive (Salt polymer) |
| 6 | Resistive (Conductive polymer) |
| 7 | Thermal conductivity |
| 8 | Gravimetric |
| 9 | Paper-metal coil |
| 10 | Ordinary human hair |
| 11 | Rolled hair (A.K.A Torsion) |
| 12 | Goldbeater's skin |
| 13 | Chilled mirror hygrometer |
| 14 | Dew cell |
| 15 | Optical absorption sensor |
| 16 - 30 | Reserved for future use |
| 31 | Missing value |

0 03 003

Thermometer / hygrometer housing

| Code figure | Meaning |
| --- | --- |
| 0 | Screen |
| 1 | Sling / Whirling |
| 2 | Unscreened |
| 3 | Radiation shield |
| 4 | Aspirated (e.g. Assmann) |
| 5 | Other Shelter |
| 6 | Handheld |
| 7-14 | Reserved for future use |
| 15 | Missing value |

0 03 004

Type of screen / shelter / radiation shield

| Code figure | Meaning |
| --- | --- |
| 0 | Stevenson screen |
| 1 | Marine Stevenson screen |
| 2 | Cylindrical section plate shield |
| 3 | Concentric tube |
| 4 | Rectangular section shield |
| 5 | Square section shield |
| 6 | Triangular section shield |
| 7 | Open covered lean to |
| 8 | Open covered inverted V roof |
| 9 | Integrated (e.g. Chilled Mirror) |
| 10-14 | Reserved for future use |
| 15 | Missing value |

0 03 008

Artificially ventilated screen or shield

| Code figure | Meaning |
| --- | --- |
| 0 | Natural ventilation in use |
| 1 | Artifical aspiration in use: constant flow at time of reading |
| 2 | Artifical aspiration in use: variable flow at time of reading |
| 3-6 | Reserved |
| 7 | Missing value |

0 03 013

Type of thermometer

| Code figure | Meaning |
| --- | --- |
| 0 | Electrical (resistance) |
| 1 | Mercury |
| 2 | Alcohol / glycol |
| 3-6 | Reserved for future use |
| 7 | Missing value |

0 03 016

Material for thermometer / hygrometer housing

| Code figure | Meaning |
| --- | --- |
| 0 | Wood |
| 1 | Metal alloy |
| 2 | Plastic / GRP |
| 3 | Reed / grass / leaf |
| 4-6 | Reserved for future use |
| 7 | Missing value |

0 03 017

Hygrometer heating

| Code figure | Meaning |
| --- | --- |
| 0 | Unheated |
| 1 | Heated |
| 2 | Not applicable |
| 3 | Missing value |

0 03 018

Instrument owner

| Code figure | Meaning |
| --- | --- |
| 0 | National hydro meteorological / weather service |
| 1 | Other |
| 2 | Standards institute |
| 3-6 | Reserved for future use |
| 7 | Missing value |

0 03 019

Configuration of louvers for thermometer / hygrometer screen

| Code figure | Meaning |
| --- | --- |
| 0 | Single v section louvers |
| 1 | Overlapping louvers |
| 2 | Double v section louvers |
| 3 | Non-overlapping louvers |
| 4 | Vented, non-louvered |
| 5 | Not applicable |
| 6 | Reserved for future use |
| 7 | Missing value |

Code/flag Tables 25

Add

0 25 185

Encryption method

| Code Figure | Meaning |
| --- | --- |
| 0 | AES 256 |
| 1 – 254 | Reserved |
| 255 | Missing value |

0 25 187

Method for reducing pressure report to sea level

| Code Figure | Meaning |
| --- | --- |
| 0 | Pressure adjusted to mean sea level following WMO 8 |
| 1 | Pressure adjusted to mean sea level following national practice |
| 2 | Pressure adjusted to local water level following WMO 8 |
| 3 | Pressure adjusted to local water level following national practice |
| 4 | Pressure not corrected for height |
| 5 – 14 | Reserved |
| 15 | Missing |

Common Code Table C6

Add

| Code figure |  | Conventional abbreviation | Abbreviation in IA5/ASCII | Abbreviation in IA2 | Definition in base units |
| --- | --- | --- | --- | --- | --- |
| 843 | Nephelometric Turbidity Units | NTU | NTU |  |  |

# Footnotes

Available from https://www.wmo.int/pages/prog/www/ISS/Meetings/IPET-DRMM_CollegePark2014/IPET-DRMM_DocPlan.html

Available from http://esurfmar.meteo.fr/doc/o/vos/E-SURFMAR_VOS_formats.pdf