| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING BEIJING, CHINA, 20 - 24 JULY 2015 |  | IPET-DRMM-III / Doc. 3.2 (2) rev.3 (14. 7. 2015) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR and CREX

New BUFR sequence and elements for GPM Microwave Imager (GMI)

Submitted by Enrico Fucile

_______________________________________________________________________

Summary and Purpose of Document

New BUFR sequence and elements are proposed to encode GPM Microwave Imager (GMI) data. The criteria of re-usability of the elements have been adopted as much as possible with the use of new elements in class 8 “significance qualifiers”.

_______________________________________________________________________

ACTION PROPOSED

The team is requested to review the proposal and approve the new sequence and elements for validation.

REFERENCES:

- IPET-DRMM-II / Doc. 3.2 (6) (10. 4. 2014)

DISCUSSIONS

During the IPET-DRMM II meeting in 2014 ECMWF submitted a proposal for new entries in BUFR table B for elements related to the position of a satellite platform required for the development of a BUFR sequence for GPM Microwave Imager (GMI) data. Taking into account the suggestions from the Team to define new elements in class 8 (significance qualifiers) rather than using specifications of existing coordinates elements we have modified that proposal and we are requesting the definition of a “coordinate significance” element with the role of specifying the significance of the subsequent elements from classes 4, 5, 6 and 7. This new element would be used in the GMI BUFR template and in the Aeolus L2B template which is under development and subject of a different proposal.

PROPOSAL

The following new BUFR table B entries and corresponding code tables are proposed:

Class 08 – BUFR/CREX Significance qualifiers

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 08 091 | Coordinates significance | Code table | 0 | 0 | 4 | Code table | 0 | 1 |

Code table 0 08 091 – Coordinates significance

| Code figure |  |
| --- | --- |
| 0 | Satellite coordinates |
| 1 | Observations coordinates |
| 2 | Start of observation |
| 3 | End of observation |
| 4 | Horizontal centre of gravity of the observation |
| 5 | Top of the observation |
| 6 | Bottom of the observation |
| 7 | Vertical centre of gravity of the observation |
| 8-14 | Reserved |
| 15 | Missing value |

Class 05 - BUFR/CREX Location (horizontal)

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 05 063 | Spacecraft Roll | DEG | 2 | 0 | 16 | DEG | 2 | 5 |
| 0 05 064 | Spacecraft Pitch | DEG | 2 | 0 | 16 | DEG | 2 | 5 |
| 0 05 066 | Spacecraft Yaw | DEG | 2 | 0 | 16 | DEG | 2 | 5 |
| 0 05 067 | Number of scan lines | Numeric | 0 | 0 | 8 | Numeric | 0 | 3 |

Class 40 – BUFR/CREX Satellite data

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 40 027 | Sun glint angle | Deg | 2 | -18000 | 16 | Deg | 2 | 5 |
| 0 40 028 | GMI quality flag | Flag table | 0 | 0 | 4 | Flag table | 0 | 5 |

Code table 0 40 028 – GMI quality flag

| Code figure |  |
| --- | --- |
| 0 | Good data |
| 1 | Possible sun glint |
| 2 | Possible radio frequency interference |
| 3 | Degraded geolocation data |
| 4 | Data corrected for warm load intrusion |
| 5 | Scan blanking on |
| 6 | Data is missing from file or unreadable |
| 7 | Unphysical brightness temperature (tb lt 50k or 350k gt tb) |
| 8 | Error in geolocation data |
| 9 | Data missing in one channel |
| 10 | Data missing in multiple channels |
| 11 | Lat/lon values are out of range |
| 12 | Non-normal status modes |
| 13 | Distance to corresponding lf pixel > 7 km |
| 14 | Reserved |
| 15 | Missing value (no quality information available) |

The following new entries are proposed in BUFR table D

| TABLE REFERENCE | TABLE REFERENCES | Element name | Element description |
| --- | --- | --- | --- |
| 3 40 012 | GPM Microwave Imager (GMI) |
|  | 0 01 007 | Satellite identifier |  |
|  | 0 02 019 | Satellite instruments |  |
|  | 0 08 091 | Coordinates significance | 0 -> Satellite coordinates |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 0 07 002 | Height or altitude |  |
|  | 0 05 063 | Spacecraft Roll |  |
|  | 0 05 064 | Spacecraft Pitch |  |
|  | 0 05 066 | Spacecraft Yaw |  |
|  | 0 05 041 | Scan line number |  |
|  | 0 05 067 | Number of scan lines |  |
|  | 3 01 011 | Year, moth, day |  |
|  | 3 01 012 | Hour, minute |  |
|  | 0 04 007 | Seconds within a minute (microsecond accuracy) |  |
|  | 0 08 091 | Coordinates significance | 1 -> Observation coordinates |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 1 07 000 | Delayed replication of 6 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 05 042 | Channel number |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 02 104 | Antenna polarization |  |
|  | 0 40 028 | GMI quality flag |  |
|  | 0 07 024 | Satellite zenith angle |  |
|  | 0 40 027 | Sun glint angle |  |
|  | 0 12 063 | Brightness temperature |  |