| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING BEIJING, CHINA, 20 - 24 JULY 2015 |  | IPET-DRMM-III / Doc. 3.2 (4) rev. 2 (15. 7. 2015) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR and CREX

New BUFR sequence and elements for Atmospheric Laser Doppler Instrument (ALADIN)

Submitted by Enrico Fucile, Michael Rennie (ECMWF), Joost de Kloe (KNMI)

_______________________________________________________________________

Summary and Purpose of Document

New BUFR sequence and elements are proposed to encode Atmospheric Laser Doppler Instrument (ALADIN) data from Atmospheric Dynamic Mission AEOLUS (AMD-AEOLUS).

_______________________________________________________________________

ACTION PROPOSED

The team is requested to review the proposal and accept the new sequence and elements for validation.

DISCUSSIONS

ECMWF is responsible for the operational implementation of the L2 meteorological processing facility for the Atmospheric Dynamics Mission Aeolus (ADM-Aeolus). This is the first space mission to acquire profiles of wind on a global scale with the Atmospheric Laser Doppler Instrument (ALADIN). In the context of this activity ECMWF has developed in collaboration with KNMI a new BUFR sequence for level 2B data which are of interest for the assimilation in NWP models.

In the sequence the use of a new significance qualifier for the coordinates is proposed to avoid the introduction of new specific location elements in the BUFR table B and to allow more flexibility and reusability of the new proposed elements. The proposed “coordinates significance” element (0-08-091) is used also in the proposed sequence for GMI data which is subject of document 3.2.2.

The observation geometry for this instrument is quite complex and in the figure below a schematic representation is reported with the aim to clarify the proposed entries in the “coordinates significance” table. One single observation in the L2B data set is characterised in the horizontal by start, end and horizontal centre of gravity, in the vertical by top, bottom and vertical centre of gravity. Those six points in space are enough to fully describe the observation volume.

PROPOSAL

The following new BUFR table B entries and corresponding code tables are proposed:

Class 08 – BUFR/CREX Significance qualifiers

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 08 091 | Coordinates significance | Code table | 0 | 0 | 4 | Code table | 0 | 1 |

Code table 0 08 091 – Coordinates significance

| Code figure |  |
| --- | --- |
| 0 | Satellite coordinates |
| 1 | Observations coordinates |
| 2 | Start of observation |
| 3 | End of observation |
| 4 | Horizontal centre of gravity of the observation |
| 5 | Top of the observation |
| 6 | Bottom of the observation |
| 7 | Vertical centre of gravity of the observation |
| 8-14 | Reserved |
| 15 | Missing value |

Class 05 - BUFR/CREX Location (horizontal)

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 05 068 | Profile number | Numeric | 0 | 0 | 32 | Numeric | 0 | 10 |
| 0 05 069 | Observation identifier | Numeric | 0 | 0 | 32 | Numeric | 0 | 10 |
| 0 05 070 | Receiver channel | Code table | 0 | 0 | 2 | Code table | 0 | 1 |

Code table 0 05 070 – Receiver channel

| Code figure |  |
| --- | --- |
| 0 | Mie |
| 1 | Rayleigh |
| 2 | Reserved |
| 3 | Missing |

Class 07 - BUFR/CREX Location (vertical)

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 07 071 | Height (high resolution) | m | 3 | -10000000 | 26 | m | 3 | 8 |

Class 25 - BUFR/CREX Processing information

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 25 187 | Confidence flag | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Code table 0 25 187 – Confidence flag

| Code figure |  |
| --- | --- |
| 0 | Valid |
| 1 | Invalid |
| 2-14 | Reserved |
| 15 | Missing |

Class 40 – BUFR/CREX Satellite data

| TABLE REFERENCE | ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| 0 40 029 | Horizontal observation integration length | m | 0 | 0 | 26 | m | 0 | 8 |
| 0 40 030 | Horizontal line of sight wind | m s-1 | 2 | -32767 | 16 | m s-1 | 2 | 5 |
| 0 40 031 | Error estimate of horizontal line of sight wind | m s-1 | 2 | 0 | 15 | m s-1 | 2 | 5 |
| 0 40 032 | Derivative wind to pressure | m s-1 Pa-1 | 3 | -100000 | 18 | m s-1 Pa-1 | 3 | 6 |
| 0 40 033 | Derivative wind to temperature | m s-1 K-1 | 3 | -100000 | 18 | m s-1 K-1 | 3 | 6 |
| 0 40 034 | Derivative wind to backscatter ratio | m s-1 | 3 | -200000 | 19 | m s-1 | 3 | 6 |
| 0 40 035 | Satellite range | m | 0 | 380000 | 18 | m | 0 | 6 |
| 0 40 036 | Lidar l2b classification type | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 40 037 | Backscatter ratio | Numeric | 3 | 500 | 20 | Numeric | 3 | 7 |

Code table 0 40 036 – Lidar l2b classification type

| Code figure |  |
| --- | --- |
| 0 | Clear |
| 1 | Cloud |
| 2-14 | Reserved |
| 15 | Missing |

The following new entries are proposed in BUFR table D

| TABLE REFERENCE | TABLE REFERENCES | Element name |  |
| --- | --- | --- | --- |
| 3 40 013 |  |
|  | 0 01 007 | Satellite identifier |  |
|  | 0 02 019 | Satellite instruments |  |
|  | 0 01 033 | Identification of originating/generating centre |  |
|  | 0 01 034 | Identification of originating/generating sub-centre |  |
|  | 0 04 001 | Year |  |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour |  |
|  | 0 04 005 | Minute |  |
|  | 0 04 007 | Seconds within a minute (microsecond accuracy) |  |
|  | 0 05 068 | Profile number |  |
|  | 0 05 069 | Observation identifier |  |
|  | 0 05 070 | Receiver channel |  |
|  | 0 40 036 | Lidar l2b classification type |  |
|  | 0 08 091 | Coordinates significance | 2 -> Start of observation |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 0 04 016 | Time increment |  |
|  | 0 08 091 | Coordinates significance | 3 -> End of observation |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 0 04 016 | Time increment |  |
|  | 0 08 091 | Coordinates significance | 4 -> Centre of gravity of observation |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 0 04 016 | Time increment |  |
|  | 0 08 091 | Coordinates significance | 5 -> Top of observation |
|  | 0 07 070 | Height (high resolution) |  |
|  | 0 05 021 | Bearing or azimuth |  |
|  | 0 07 021 | Elevation |  |
|  | 0 40 035 | Satellite range |  |
|  | 0 08 091 | Coordinates significance | 6 -> Bottom of observation |
|  | 0 07 070 | Height (high resolution) |  |
|  | 0 05 021 | Bearing or azimuth |  |
|  | 0 07 021 | Elevation |  |
|  | 0 40 035 | Satellite range |  |
|  | 0 08 091 | Coordinates significance | 7 -> Vertical centre of Gravity of the observation |
|  | 0 07 070 | Height (high resolution) |  |
|  | 0 05 021 | Bearing or azimuth |  |
|  | 0 07 021 | Elevation |  |
|  | 0 40 035 | Satellite range |  |
|  | 0 40 029 | Horizontal observation integration length |  |
|  | 0 40 030 | Horizontal line of sight wind |  |
|  | 0 40 031 | Error estimate of horizontal line of sight wind |  |
|  | 0 25 187 | Confidence flag |  |
|  | 0 10 004 | Pressure |  |
|  | 0 12 001 | Temperature/air temperature |  |
|  | 0 40 037 | Backscatter ratio |  |
|  | 0 40 032 | Derivative wind to pressure |  |
|  | 0 40 033 | Derivative wind to temperature |  |
|  | 0 40 034 | Derivative wind to backscatter ratio |  |