| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- THIRD MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING BEIJING, CHINA, 20 - 24 JULY 2015 |  | IPET-DRMM-III / Doc. 3.2 (8) rev. (15. 7. 2015) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

New Descriptor for radar data products

Submitted by Michael Mott, Sibylle Krebber (DWD)

_______________________________________________________________________

Summary and Purpose of Document

This document contains proposals for new BUFR descriptors for radar composite products.

_______________________________________________________________________

ACTION PROPOSED

The meeting in invited to review the document and approve the contents for validation.

DISCUSSIONS

DWD changed the radar composite routines to a new system. In this context the BUFR-format was updated. Especially more meta information is given. Currently the used descriptors are in the local table version 8 from originating centre 247 sub-centre 0. Such products are already exchanged within OPERA.

To create the composite within centre 78 sub-centre 10 the DWD would like to propose these descriptors as new descriptors for the BUFR master table. This would make the exchange of these products more international.

PROPOSAL

New BUFR Table B descriptors are proposed:

Class 29 – BUFR/CREX Map data

| TABLE REFERENCE |  | BUFR | CREX |
| --- | --- | --- | --- |
| F | X | Y | ELEMENT NAME | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Char) |
| 0 | 29 | 10 | Semi-major axis of rotation ellipsoid | m | 2 | 0 | 33 | m | 0 | 11 |
| 0 | 29 | 11 | Semi-minor axis of rotation ellipsoid | m | 2 | 0 | 33 | m | 0 | 11 |
| 0 | 29 | 12 | Longitude origin | Degree | 5 | -18000000 | 26 | Degree | 5 | 10 |
| 0 | 29 | 13 | Latitude origin | Degree | 5 | -9000000 | 25 | Degree | 5 | 9 |
| 0 | 29 | 14 | Latitude of true scale | Degree | 5 | -9000000 | 25 | Degree | 5 | 9 |
| 0 | 29 | 15 | X-offset (see Note 1) | m | 2 | -3355443200 | 33 | m | 0 | 12 |
| 0 | 29 | 16 | Y-offset (see Note 1) | m | 2 | -3355443200 | 33 | m | 0 | 12 |
| 0 | 29 | 17 | Geographic projection as projection initialisation string | CCITT_IA5 | 0 | 0 | 800 | Character | 0 | 100 |

Add Notes under Class 29 – BUFR/CREX Map data:

- X-Offset and Y-Offset are distances between the projection origin and the upper left corner of the upper left pixel in the map as explained in the following drawing:

# Endnotes

http://www.eumetnet.eu/sites/default/files/bufr_sw_desc.pdf