# Validation of sequence 3 02 064 (Ship / or other marine platform wind data)

# 1.	Responsible Organization

# National Oceanography Centre (UK)

# Met Office (UK)

# 2.	Requirements and Purposes

Table D sequence for the reporting of wind speed data from ship or other marine data.

# 3.	Description of Proposal

# BUFR sequence 3 02 064 – ship / or other marine platform wind data

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 064 | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 0 | 02 | 002 | Type of instrumentation for wind measurement |  |
|  |  |  | 0 | 08 | 021 | Time significance | Set to 2, time averaged |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 001 | Wind direction |  |
|  |  |  | 0 | 11 | 002 | Wind speed |  |
|  |  |  | 0 | 08 | 021 | Time significance | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 001 | Delayed replication factor |  |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 043 | Maximum wind gust direction |  |
|  |  |  | 0 | 11 | 041 | Maximum wind gust speed |  |

Note change from short delayed replication factor to delayed replication factor above (in red).

# 4.	Declaration of validation complete

The above proposal has been validated by the UK Met Office (UKMO) and UK National Oceanography Centre (NOC).

(1)	Centres participated in the validation

UKMO (Jon Turton)

NOC (Dr David Berry)

(2)	Date of validation

December 2014 to March 2015

(3)	Proof documents

Test messages (BUFR)

UKMO Encoded message: AMOSBUFRw3-02-064.dat

JCOMM (NOC) Encoded message: nocsbufr064_v2.dat

Decoded messages (Plain text)

UKMO:

AMOSBUFRw3-02-064_noc_decode.txt (decoded by NOC)

AMOS_BUFR_UKMO_decoded.txt (decoded by UKMO)

NOC:

nocsbufr064_v2_noc_decode.txt (decoded by NOC)

NOCS_BUFR_v2_UKMO_decoded.txt (decoded by UKMO)

(4)	Software used

UKMO: 	Custom UKMO encoder / decoder

NOC:		Encoder / decoder based on ECMWF libraries

# 5.	Result of Discussions

Sequence originally proposed as part of the template for the reporting of Synoptic reports from sea stations suitable for VOS observation data. The sequence has subsequently been validated independently of the original proposal due to the requirement to use the sequence in the reporting of ship AWS data by the UKMO.

# 6.	Proposed Implementation Date and Procedure for Formality

# If agreed, November 2015.

# 7.	Summary of Discussions